## Slide 1: Simplification of Configuration Profile Structure
8 March 2016
CSSMWG Telecon
John Pietras
Global Science and Technology, Inc.

## Slide 2: Agenda
Issues with Fall 2015 approach
Overview of new (and hopefully improved) approach
  Issue mitigation
  Class diagrams, etc.

## Slide 3: Issues with Fall 2015 Approach
Too many pieces needed to create a configuration profile
  Each Service Component Profile could be separately established
    Intended to support re-use of Service Component Profiles
  Service Component Connections object needed to link together Service Component Profiles to form a Configuration Profile
    Magnitude of linkages counter-weighs benefits of Service Component Profile re-usability
All linkages among Service Component Profiles are via cross-referencing SAP and Accessor ports
  Accessor port instance references the peer SAP port instance
  Cross-referencing information adds bulk to configuration profiles
  Keeping cross references straight is completely outside the purview of XML validation

## Slide 4: Issues Mitigation (1 of 2)
Every Configuration Profile contains all of the Service Component Profiles that it uses
  Service Combination Profile object has been eliminated
Containment replaces SAP/Accessor port pairs for primary linkages between Service Component Profiles
  Eliminates cross-referencing information from these linkages, which constitute the majority of linkages among Service Component Profile
  Use of subtype substitution enforces proper linkages
    A SAP of type XYZ contains an Accessor of type XYZ (or a subtype thereof)
    Example
      The RF Aperture SC Profile contains a Forward Modulated Waveform SAP, which contains a Forward Modulated Waveform Accessor
      The CCSDS 401 Forward Physical Channel Transmission SC Profile is cast as a subtype of the Forward Modulated Waveform Accessor
      Ergo, CCSDS 401 Forward Physical Channel Transmission SC Profile can be contained by the Forward Modulated Waveform SAP of the RF Aperture SC Profile

## Slide 5: Issues Mitigation (2 of 2)
Some Service Component Profiles have relationships with multiple other Service Component Profiles, but containment can be used to express at most one of these relationships
Ancillary relationships with other SC Profiles are implemented using a cross-referencing mechanism
  The UML provided/required interface terminology has been adapted for these ancillary relationships
  An object that possesses ancillary information that is needed by other objects has a provided interface by which that information is made available
  An object that needs ancillary information that is available from another object has a required interface that links to a peer provided interface

## Slide 6: ConfigurationProfileInfoEntity Class Diagram

## Slide 7: ConfigurationProfileContents Class Diagram - Fall 2015

## Slide 8: Current ConfigurationProfileContents Class Diagram

## Slide 9: RF Aperture Service Component Profile

## Slide 10: CCSDS 401 Forward Physical Channel Transmission Service Component Profile

## Slide 11: Bakeoff Service Combination Profile Diagram (Graphical Notation) – Fall 2015

## Slide 12: Bakeoff Service Combination Profile Diagram (Graphical Notation) – Current Version

## Slide 13: Example Service Combination Profile Notional Data Structures (partial) – Fall 2015
- Instance 1
RF Aperture SC Profile
Fwd Mod Waveform
SAP Port 1
CCSDS 401 Fwd Phys
Channel SC Profile
Fwd Phys Chnl Symbols
SAP Port 1
Service Combination Profile
Service
Component
Connections
Fwd Mod Waveform
Accessor Port 1
- Instance 1
Rtn Mod Waveform
SAP Port 2
Pointing Angles
SAP Port 3
Transmit Frequency
SAP Port 2
Ranging Signal Timing
SAP Port 3
TC Sync & Channel Encoding
SC Profile
Fwd All Transfer Frames
SAP Port 1
- Instance 1
Fwd Phys Chnl Symbols
Accessor Port 1
PortAssociatonSet
SAP port: [{RfApertureSc}:1]: [{FwdModWaveform SAP}:1]
PairedAccessorPort
Accessor port: [{Ccsds401FwdPhysChnlXmitSc}:1]: {FwdModWaveform Accessor}:1]
PortAssociatonSet
SAP port: [{TcSyncChnlEncodeSc}:1]: [{FwdPhsyChnlSymbols SAP}:1]
PairedAccessorPort
Accessor port: [{Ccsds401FwdPhysChnlXmitSc}:1]: {FwdPhsyChnlSymbols Accessor}:1]

## Slide 14: Example Service Combination Profile Notional Data Structures (partial) – Current Version
- Instance 1
RF Aperture SC Profile
Fwd Mod
Waveform
SAP
CCSDS 401 Fwd Phys
Channel SC Profile
Fwd Phys Chnl
Symbols
SAP
Fwd Mod
Waveform
Accessor
- Instance 1
Rtn Mod
Waveform
SAP
Pointing Angles
Provided IF
Transmit Frequency
SAP Provided IF
Ranging Signal Timing
SAP Provided IF
TC Sync & Channel
Encoding SC Profile
Fwd All Transfer
Frames SAP
- Instance 1
Fwd Phys Chnl
Symbols
Accessor
Aperture

## Slide 15: Bakeoff XML Instance Document – XMLspy Grid View