Draft Recommendation for
Space Data System Practices

Mission Operations Message Abstraction Layer—JAVA API

Draft Recommended Practice

CCSDS 523.1-R-1

Red Book

May 2012

AUTHORITY

|  | Issue: | Red Book, Issue 1 |  |
| --- | --- | --- | --- |
|  | Date: | May 2012 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED PRACTICE IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in the Procedures Manual for the Consultative Committee for Space Data Systems, and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This document is published and maintained by:

CCSDS Secretariat

Space Communications and Navigation Office, 7L70

Space Operations Mission Directorate

NASA Headquarters

Washington, DC 20546-0001, USA

STATEMENT OF INTENT

(WHEN THIS RECOMMENDED PRACTICE IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF INTENT:)

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommendations and are not considered binding on any Agency.

This Recommended Practice is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommended Practice is entirely voluntary. Endorsement, however, indicates the following understandings:

o    Whenever a member establishes a CCSDS-related practice, this practice should be in accord with the relevant Recommended Practice. Establishing such a practice does not preclude other provisions which a member may develop.

o    Whenever a member establishes a CCSDS-related practice, that member will provide other CCSDS members with the following information:

--    The practice itself.

--    The anticipated date of initial operational capability.

--    The anticipated duration of operational service.

o    Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Practice nor any ensuing practice is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommended Practice will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Practice is issued, existing CCSDS-related member Practices and implementations are not negated or deemed to be non-CCSDS compatible. It is the responsibility of each member to determine when such Practices or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new Practices and implementations towards the later version of the Recommended Practice.

FOREWORD

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommended Practice is therefore subject to CCSDS document management and change control procedures, which are defined in the Procedures Manual for the Consultative Committee for Space Data Systems.  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt e.V. (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- Federal Space Agency (FSA)/Russian Federation.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- CSIR Satellite Applications Centre (CSIR)/Republic of South Africa.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Practice.  Its ‘Red Book’ status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations.  As such, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

# DOCUMENT CONTROL

| Document | Title and Issue | Date | Status |
| --- | --- | --- | --- |
| CCSDS 523.1-R-1 | Mission Operations Message Abstraction Layer—JAVA API, Draft Recommended Practice, Issue 1 | May 2012 | Current draft |

# CONTENTS

Section	Page

1	Introduction	1-1

1.1	Purpose of this Recommended Practice	1-1

1.2	Scope	1-1

1.3	Applicability	1-1

1.4	Rationale	1-1

1.5	Document Structure	1-1

1.6	Definitions	1-1

1.7	Conventions	1-1

1.8	References	1-1

2	Overview	2-1

2.1	General	2-1

2.2	MO service Framework Java mapping	2-1

2.3	Mapping from MAL document	2-1

3	MAL API	3-1

3.1	Overview	3-1

3.2	MAL package	3-1

3.3	Data structures package	3-1

3.4	Consumer package	3-1

3.5	Provider package	3-1

3.6	Broker package	3-1

4	Service mapping	4-1

4.1	Overview	4-1

4.2	Definition	4-1

4.3	Consumer	4-1

4.4	Provider	4-1

4.5	Data structures	4-1

4.6	Element Factory Classes	4-1

4.7	Multiple Element Body classes	4-1

4.8	Helper and Element Factory Classes	4-1

5	Transport API	5-1

5.1	General	5-1

5.2	Classes and interfaces	5-1

6	Access Control API	6-1

6.1	General	6-1

6.2	Classes and Interfaces	6-1

7	Encoding API	7-1

7.1	Overview	7-1

7.2	Classes and interfaces	7-1

8	COM Service Mapping	8-1

8.1	Overview	8-1

8.2	Definition	8-1

8.3	COM Operations	8-1

8.4	Generic COM Service	8-1

ANNEX A	Definition of ACRONYMS  (Informative)	A-1

ANNEX B	Informative References  (Informative)	B-1

ANNEX C	Code Example  (Informative)	C-1

Figure

2-1	Mission Operations Services Concept Document Set	2-1

2-2	Relationship of MO Books	2-1

2-3	Overview of the Mission Operations Service Framework	2-1

2-4	MO Framework Java Mapping	2-1

3-1	Relationships between the API Main Interfaces	3-1

4-1	Relationships between the Stub Classes and Interfaces	4-1

4-2	Relationships between the Skeleton Classes and Interfaces (Delegation Pattern)	4-1

4-3	Relationships between the Skeleton Classes and Interfaces (Inheritance Pattern)	4-1

4-4	Multi-Binding Service Provider	4-1

Table

2-1	Variable Letter Case Rules	1-1

3-1	API Main Interfaces	3-1

3-2	MALContextFactory ‘registerFactoryClass’ Parameter	3-1

3-3	MALContextFactory ‘deregisterFactoryClass’ Parameter	3-1

3-4	MALContextFactory ‘createMALContext’ Parameter	3-1

3-5	MALContextFactory ‘registerElementClass’ Parameters	Erreur ! Signet non défini.

3-6	MALContextFactory ‘lookupElementClass’ Parameter	Erreur ! Signet non défini.

3-7	MALContextFactory ‘registerArea’ Parameter	3-1

3-8	MALContextFactory ‘lookupArea’ Parameter	3-1

3-9	MALContextFactory ‘lookupArea’ Parameter	Erreur ! Signet non défini.

3-10	MALContextFactory ‘lookupOperation’ Parameters	Erreur ! Signet non défini.

# CONTENTS (continued)

Table	Page

3-11	MALContext ‘getTransport’ Parameters	3-1

3-12	MALService Attributes	3-1

3-13	MALService Constructor Parameters	3-1

3-14	MALService ‘setArea’ Parameter	3-1

3-15	MALService ‘addOperation’ Parameter	3-1

3-16	MALOperation Attributes	3-1

3-17	MALOperation Constructor Parameters	3-1

3-18	MALOperation ‘getBodyShortName’ Parameter	Erreur ! Signet non défini.

3-19	MALOperation ‘setService’ Parameter	3-1

3-20	Interaction Stages Constants	3-1

3-21	Operation Short Names	3-1

3-22	MAL<Ip>Operation Constructor Parameters	3-1

3-23	MALService Attributes	3-1

3-24	MALArea Constructor Parameters	3-1

3-25	MALArea ‘addService’ Parameter	3-1

3-26	MALException Constructor Parameter	3-1

3-27	MALComposite ‘encode’ Parameter	Erreur ! Signet non défini.

3-28	MALComposite ‘decode’ Parameter	Erreur ! Signet non défini.

3-29	MAL::Attribute Variables	Erreur ! Signet non défini.

3-30	MALEncoder ‘encode<Attribute>’ Parameter	3-1

3-31	MALEncoder ‘encodeEnumeration’ Parameter	Erreur ! Signet non défini.

3-32	MALDecoder ‘decodeEnumeration’ Parameter	Erreur ! Signet non défini.

3-33	MALListEncoder ‘createListEncoder’ Parameter	Erreur ! Signet non défini.

3-34	MALListEncoder ‘createListDecoder’ Parameter	Erreur ! Signet non défini.

3-35	MALEncoder ‘encodeElement’ Parameter	3-1

3-36	MALEncoder ‘encodeComposite’ Parameter	Erreur ! Signet non défini.

3-37	MALDecoder ‘decodeComposite’ Parameter	Erreur ! Signet non défini.

3-38	Enumeration Constructor Parameter	3-1

3-39	List ‘setSize’ Parameter	Erreur ! Signet non défini.

3-40	List ‘addList’ Parameter	Erreur ! Signet non défini.

3-41	List ‘addList’ Parameter	Erreur ! Signet non défini.

3-42	List ‘add’ Parameter	Erreur ! Signet non défini.

3-43	List ‘add(index)’ Parameters	Erreur ! Signet non défini.

3-44	List ‘contains’ Parameter	Erreur ! Signet non défini.

3-45	List ‘containsAll’ Parameter	Erreur ! Signet non défini.

3-46	List ‘remove’ Parameter	Erreur ! Signet non défini.

3-47	List ‘remove(index)’ Parameter	Erreur ! Signet non défini.

3-48	List ‘get’ Parameter	Erreur ! Signet non défini.

3-49	List ‘set’ Parameters	Erreur ! Signet non défini.

3-50	List ‘indexOf’ Parameter	Erreur ! Signet non défini.

3-51	List ‘lastIndexOf’ Parameter	Erreur ! Signet non défini.

# CONTENTS (continued)

Table	Page

3-52	List ‘toArray’ Parameter	Erreur ! Signet non défini.

3-53	MAL::Attributes Mapped to a Java Type	3-1

3-54	Union Variables	3-1

3-55	Union Constructor Parameter	3-1

3-56	Blob Byte Array Constructor Parameter	3-1

3-57	Blob URL Constructor Parameter	3-1

3-58	Blob Byte Array ‘setValue’ Parameter	Erreur ! Signet non défini.

3-59	Blob ‘setURL’ Parameter	Erreur ! Signet non défini.

3-60	MAL::Attributes Represented by a Specific Class	3-1

3-61	Initial Value Assigned by the <Attribute> Empty Constructor	3-1

3-62	MALConsumerManager ‘createConsumer’ Parameters	3-1

3-63	QoS Properties	3-1

3-64	MALConsumer ‘send’ Parameters	3-1

3-65	MALConsumer ‘submit’ Parameters	3-1

3-66	MALConsumer ‘request’ Parameters	3-1

3-67	MALConsumer ‘invoke’ Parameters	3-1

3-68	MALConsumer ‘progress’ Parameters	3-1

3-69	MALConsumer ‘register’ Parameters	3-1

3-70	MALConsumer ‘deregister’ Parameters	3-1

3-71	MALConsumer ‘asyncSubmit’ Parameters	3-1

3-72	MALConsumer ‘asyncRequest’ Parameters	3-1

3-73	MALConsumer ‘asyncInvoke’ Parameters	3-1

3-74	MALConsumer ‘asyncProgress’ Parameters	3-1

3-75	MALConsumer ‘asyncRegister’ Parameters	3-1

3-76	MALConsumer ‘asyncDeregister’ Parameters	3-1

3-77	MALInteractionListener ‘acknowledgementReceived’ Parameters	3-1

3-78	MALInteractionListener ‘responseReceived’ Parameters	3-1

3-79	MALInteractionListener ‘updateReceived’ Parameters	3-1

3-80	MALInteractionListener ‘notifyReceived’ Parameters	3-1

3-81	MALInteractionListener ‘errorReceived’ Parameters	Erreur ! Signet non défini.

3-82	MALProviderManager ‘createProvider’ Parameters	3-1

3-83	MALProvider ‘getPublisher’ Parameter	3-1

3-84	MALInteractionHandler ‘malInitialize’ Parameter	3-1

3-85	MALInteractionHandler ‘handleSend’ Parameters	3-1

3-86	MALInteractionHandler ‘handleSubmit’ Parameters	3-1

3-87	MALInteractionHandler ‘handleRequest’ Parameters	3-1

3-88	MALInteractionHandler ‘handleInvoke’ Parameters	3-1

3-89	MALInteractionHandler ‘handleProgress’ Parameters	3-1

3-90	MALInteractionHandler ‘malFinalize’ Parameter	3-1

3-91	MALSubmit ‘sendError’ Parameters	3-1

3-92	MALResponse ‘sendResponse’ Parameters	3-1

# CONTENTS (continued)

Table	Page

3-93	MALResponse ‘sendError’ Parameters	3-1

3-94	MALInvoke ‘sendAcknowledgement’ Parameters	3-1

3-95	MALProgress ‘sendUpdate’ Parameter	3-1

3-96	MALProgress ‘sendUpdateError’ Parameter	3-1

3-97	MALPublisher ‘publish’ Parameters	3-1

3-98	MALPublisher ‘register’ Parameters	3-1

3-99	MALPublisher ‘deregister’ Parameters	Erreur ! Signet non défini.

3-100	MALPublisher ‘asyncRegister’ Parameters	3-1

3-101	MALPublisher ‘asyncDeregister’ Parameters	3-1

3-102	MALPublishInteractionListener ‘acknowledgementReceived’ Parameter	3-1

3-103	MALPublishInteractionListener ‘errorReceived’ Parameters	3-1

3-104	MALBrokerBinding ‘createBrokerBinding’ Parameters	3-1

4-1	Service Mapping Variables	Erreur ! Signet non défini.

4-2	Area Classes	4-1

4-3	Service Classes	4-1

4-4	Stub Interface Methods Mapping	Erreur ! Signet non défini.

4-5	<Service>Stub Attribute	4-1

4-6	Skeleton Handler Interface Methods Mapping	Erreur ! Signet non défini.

4-7	<Notify> Publisher Attributes	4-1

4-8	<Notify>Publisher constructor Parameters	4-1

4-9	Invoke <Op>Interaction Attribute	4-1

4-10	Progress <Op>Interaction Attribute	4-1

4-11	<Service>InheritanceSkeleton Attributes	4-1

4-12	<Service>DelegationSkeleton Attributes	4-1

4-13	Enumeration Template Variables	Erreur ! Signet non défini.

4-14	List Template Variables	Erreur ! Signet non défini.

4-15	Composite Template Variables	Erreur ! Signet non défini.

4-16	Service Helper Template Variables	Erreur ! Signet non défini.

4-17	Area Helper Template Variables	Erreur ! Signet non défini.

5-1	MALTransportFactory Attributes	5-1

5-2	MALTransportFactory ‘registerFactoryClass’ Parameters	5-1

5-3	MALTransportFactory ‘deregisterFactoryClass’ Parameter	5-1

5-4	MALTransportFactory Constructor Parameter	5-1

5-5	MALTransportFactory Creation Parameter	5-1

5-6	MALTransportFactory ‘createTransport’ Parameter	5-1

5-7	MALTransport ‘createEndPoint’ Parameters	5-1

5-8	MALTransport ‘deleteEndPoint’ Parameter	5-1

5-9	MALTransport ‘isSupportedQoSLevel’ Parameter	5-1

5-10	MALTransport ‘isSupportedInteractionType’ Parameter	5-1

5-11	MALTransport ‘createBroker’ Parameters	5-1

5-12	MALEndPoint ‘createMessage’ Parameters	5-1

# CONTENTS (continued)

Table	Page

5-13	MALEndPoint ‘sendMessage’ Parameters	5-1

5-14	MALEndPoint ‘sendMessages’ Parameters	5-1

5-15	MALEndPoint ‘setMessageListener’ Parameter	5-1

5-16	MALMessageListener ‘onMessage’ Parameters	5-1

5-17	MALMessageListener ‘onMessages’ Parameters	5-1

5-18	MALMessageListener ‘onInternalError’ Parameters	5-1

5-19	MALTransmitErrorException Constructor Parameters	5-1

5-20	MALTransmitMultipleErrorException Constructor Parameters	5-1

6-1	MALAccessControlFactory ‘registerFactoryClass’ Parameters	6-1

6-2	MALAccessControlFactory ‘createAccessControl’ Parameter	6-1

6-3	MALAccessControl ‘check’ Parameter	6-1

7-1	MALElementStreamFactory ‘registerFactoryClass’ Parameters	7-1

7-2	MALElementStreamFactory ‘deregisterFactoryClass’ Parameters	7-1

7-3	MALElementStreamFactory Creation Parameters	7-1

7-4	MALElementStreamFactory ‘init’ Parameters	7-1

7-5	MALElementStreamFactory ‘createInputStream’ Parameter	7-1

7-6	MALElementStreamFactory ‘createOutputStream’ Parameter	7-1

7-7	MALElementInputStream ‘readElement’ Parameter	7-1

7-8	MALElementOutputStream ‘writeElement’ Parameter	7-1

7-9	MALEncodingContext Attributes	7-1

# Introduction

## Purpose of this Recommended Practice

This Recommended Practice defines a Java API for the Mission Operations (MO) Message Abstraction Layer (MAL) specified in reference [1].

## Scope

The scope of this Recommended Practice is the definition of all concepts and terms that establish a Java API for consuming and providing MO services on top of the MAL.  The Java MAL API is intended to maximize the portability of the MO components across various underlying MAL implementations and transport protocols.

## Applicability

This Recommended Practice serves as a specification of a Java API providing all the concepts defined by the MAL, in particular the interaction patterns, the access control and transport interfaces.

The API supports version 1 of the MAL as specified in reference [1].

The API depends on Java 5.

## Rationale

The goal of this Recommended Practice is to document how to develop and utilize MAL-based services using Java (reference [2]).

Another objective is to create a guide for promoting portability between various software packages implementing the Java MAL API and applications using the Java MAL API.

## Document Structure

This Recommended Practice is organized as follows:

- section 1 provides purpose and scope, and lists definitions, conventions, and references used throughout the Recommended Practice;

- section 2 gives an overview of the API;

- section 3 defines the MAL API that represents the MAL service interface;

- section 4 defines how a MAL service specification is mapped to Java;

- section 5 defines the transport API that represents the MAL transport interface;

- section 6 defines the access control API that represents the MAL access control interface;

- section 7 defines the encoding API, an optional set of interfaces that can be used by the transport layer in order to externalize the encoding behavior;

- section 8 defines how a service using the COM service template is mapped to Java.

NOTE	–	Some application code examples are given in annex C.

## Definitions

Attribute: Either

- a field of a Java class called ‘attribute’,

- the data type MAL::Attribute, or

- the interface Attribute defined in the Java MAL API.

## Conventions

### NOMENCLATURE

The following conventions apply for the normative specifications in this Recommended Practice:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification;

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

NOTE	–	These conventions do not imply constraints on diction in text that is clearly informative in nature.

### Informative Text

In the normative sections of this document (sections 3-8), informative text is set off from the normative specifications either in notes or under one of the following subsection headings:

- Overview;

- Background;

- Rationale;

- Discussion.

### Use of Capital Letters

Names of interfaces and classes of the Java MAL API are shown with the first letter of each word capitalized.

### Code template variables

Some code templates are given throughout this document. Those templates are parameterized with variables. A variable is used by placing its name between the enclosing characters “<<” and “>>”. For example, the variable ‘method name’ is used in the following code line:

public void <<method name>>()

If a variable contains a list of values then the values are iterated with the following syntax:

<<variable name [i]>> … <<variable name [N]>>

The variable ‘i’ is the iteration index starting from 1.

The variable ‘N’ is the size of the list.

If the list size is zero then nothing is written in the code template.

If the list size (N) is greater than zero then the <<variable name [i]>> part is iterated N-1 times and the <<variable name [N]>> part is finally written in the code template.

For example, the variable ‘type’ contains a list of type. A method ‘m’ taking those types as parameters is declared as follows:

public void m(<<type [i]>> p<<i>>, … <<type [N]>> p<<N>>)

If the list is empty then the result is:

public void m()

If the list contains one element ‘A’ then the result is:

public void m(A p1)

The names of variables are not case-sensitive: ‘field name’ and ‘FIELD NAME’ designate the same variable.

However the value of the variable is case sensitive following the rules explained in the table 2-1:

Table 1-1:  Variable Value Case Rules

| Variable name case | Variable value case |
| --- | --- |
| All the letters in lower case. Example: <<variable name>> | No change |
| First letter in upper case and the other in lower case. Example: <<Variable name>> | No change except the first letter in upper case |
| All the letters in upper case. Example: <<VARIABLE NAME>> | Upper case |
| All the letters in lower case and between an initial and final character ‘!’. Example: <<!variable name!>> | Lower case |

### Java class packages

In the code templates, the package of classes is not indicated if there is no ambiguity. However the real Java code needs either to prefix the package name to the class name or to declare the package in an ‘import’ clause at the beginning of the class definition.

## References

The following documents contain provisions which, through reference in this text, constitute provisions of this Recommended Practice.  At the time of publication, the editions indicated were valid.  All documents are subject to revision, and users of this Recommended Practice are encouraged to investigate the possibility of applying the most recent editions of the documents indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS documents.

[1]	Mission Operations Message Abstraction Layer.  Recommendation for Space Data System Standards, CCSDS 521.0-B-1.  Blue Book.  Issue 1.  Washington, D.C.: CCSDS, October 2010.

[2]	James Gosling, et al.  The Java™ Language Specification.  3rd Ed.  Boston: Addison-Wesley, 2005.

[3]	T. Berners-Lee, R. Fielding, U.C. Irvine, and L. Masinter.  Uniform Resource Identifiers (URI): Generic Syntax.  RFC 2396.  Reston, Virginia: ISOC, August 1998.

[4]	R. Hinden, B. Carpenter, and L. Masinter.  Format for Literal IPv6 Addresses in URL’s.  RFC 2732.  Reston, Virginia: ISOC, December 1999.

[5]	Mission Operations Common Object Model.  Draft Recommendation for Space Data System Standards, CCSDS 521.1-R-3.  White Book.  Issue 3.  : CCSDS, April 2012.

NOTE	–	Informative references are listed in annex B.

# Overview

## General

This Recommended Practice provides an interface specification that translates the abstract service definitions of the MAL and MO Services into a Java-specific interface that can be used by programmers. The API must be faithful to the abstract services defined in the specifications and it must, by some means, provide access to the features of the services and all of their options. It plays a useful role in application portability, but plays no role in interoperability.

The following diagram presents the set of standards documentation in support of the Mission Operations Services Concept. The MO Java MAL API belongs to the language mappings documentation.

Figure 2-1:  Mission Operations Services Concept Document Set

For each programming language there is only required a single mapping of the MAL to that language as the abstract services are defined in terms of the MAL and therefore their language-specific API is derived from the mapping:

Figure 2-2:  Relationship of MO Books

This Recommended Practice defines a mapping from the abstract notation of the MAL to an unambiguous Java API, more specifically:

- how the specific MAL abstract services are mapped to Java;

- how any service errors or issues shall be communicated to higher layers;

- the physical representation of the abstract MAL messages at the interface necessary to constitute the operation templates;

- the mapping of the message structure rules for Java;

- the physical representation of the abstract MAL data types in Java.

It does not specify:

- individual application services, implementations or products;

- the implementation of entities or interfaces within real systems;

- the methods or technologies required to acquire data;

- the management activities required to schedule a service;

- the representation of any service specific Protocol Data Units (PDUs) or operations (this is derived from the Java transform defined in this document).

## MO service Framework Java mapping

The CCSDS Spacecraft Monitoring & Control (SM&C) working group has developed a concept for a Mission Operations (MO) Service Framework, which follows the principles of Service Oriented Architectures. It defines two important aspects, the first is a protocol for interaction between two separate entities, and the second is a framework of common services providing functionality common to most uses of the service framework.

Figure 2-3:  Overview of the Mission Operations Service Framework

This Recommended Practice defines the following Java mapping of the MO Service Framework:

- the application layer is mapped to Java application modules consuming and providing MO services;

- the MO services layer is mapped to service stubs and skeletons enabling the application to consume and provide MO services on top of the MAL;

- the MAL Interaction Patterns and Quality of Service features are mapped to a MAL module;

- the MAL access control feature is mapped to an access control module used by the MAL module;

- the transport layer is mapped to a transport module in charge of using a messaging technology;

- the transport module can manage the MAL message encoding internally or delegate this function to an encoding module.

The layer diagram displayed in figure 2-4 presents the Java modules resulting from the MO Service Framework mapping. It also gives the name of the programming interfaces used and implemented by the modules.

Figure 2-4:  MO Framework Java Mapping

The programming interfaces are:

- Java MAL API;

- MO Services API generated from the Service Mapping;

- Transport API;

- Access Control API;

- Encoding API.

The MO Services API is derived from the services specifications and the Java Service Mapping rules.

The messaging technology API is chosen by the transport module. As a consequence it cannot be defined in this document.

## Mapping from MAL document

This Recommended Practice defines a mapping from the abstract notation of the MAL to an unambiguous Java API. The structure of the MAL document (reference [1]) is mapped to this document as follows:

- the sections “Transaction Handling”, “State Transitions”, “Message Composition”, “MAL Service Interface” are mapped to the interaction pattern handling methods of the service consumer, provider and broker defined in the section “MAL API”;

- the sections “MAL Data Types” and “MAL Errors” are mapped to the section “MAL API” and “Service Mapping”;

- the Java representation of the MAL fundamental and attribute data types is defined in the section “MAL API”;

- the Java representation of the MAL data structures is generated according to the section “Service Mapping” except for the structures that need a specific mapping which is defined in the section “MAL API”;

- the Java representation of the MAL errors is generated according to the “Service Mapping”;

- the section “Service Specification XML” is mapped to the section “Service Mapping”;

- the section “Transport Interface” is mapped to the section “Transport API”;

- the section “Access Control Interface” is mapped to the section “Access Control API”.

There is no MAL document section that can be mapped to the section “Encoding API” because it is an optional feature provided by the Java MAL API.

# MAL API

## Overview

The MAL API defines the interfaces and classes required by the MAL service interface defined in reference [1].

The MAL API comprises the following levels:

- the generic API used by every MAL clients;

- the data structures and related interfaces;

- the service consumer API;

- the service provider API;

- the broker API.

The main interfaces provided by the API are those listed in table 3-1.

Table 3-1:  API Main Interfaces

| API level | Interface name | Description |
| --- | --- | --- |
| Generic | MALContextFactory | MALContext factory |
|  | MALContext | Context enabling a client to use the communication functions provided by the MAL layer |
| Consumer | MALConsumerManager | MALConsumer factory and activator |
|  | MALConsumer | Communication context enabling a client to initiate interaction patterns |
| Provider | MALProviderManager | MALProvider factory and activator. |
|  | MALProvider | Execution context of a service provider handling all the interaction patterns and initiating the Publish/Subscribe interaction pattern as a publisher |
| Broker | MALBrokerManager | MALBroker factory and activator |
|  | MALBroker | Execution context of a shared broker |

NOTE	–	Figure 3-1 gives an overview of the relationships between the main interfaces.

Figure 3-1:  Relationships between the API Main Interfaces

The packages provided by the API are:

- the MAL package: org.ccsds.moims.mo.mal;

- the data structures package: org.ccsds.moims.mo.mal.structures;

- the consumer package: org.ccsds.moims.mo.mal.consumer;

- the provider package: org.ccsds.moims.mo.mal.provider;

- the broker package: org.ccsds.moims.mo.mal.broker.

NOTE	–	The following subsections define the content of every package.

## MAL package

### Overview

This subsection defines the content of the generic MAL package:

org.ccsds.moims.mo.mal

### MALContextFactory

#### Definition

A MALContextFactory class shall be defined in order to enable a MAL client to instantiate and configure a MALContext.

The MALContextFactory class shall provide static repositories:

- the MALContext factory class repository shall map the MALContextFactory implementation classes to their class names;

- the MALArea repository shall map the area names to the MALArea descriptions;

- the error repository shall map the error codes to the error names.

The MALContextFactory class shall provide a default MALElementFactoryRegistry.

#### Class Initialization

The MALContextFactory class initialization shall:

- create the static repositories;

- instantiate the default MALElementFactoryRegistry;

- call the static method ‘init’ provided by the MALHelper by passing the default MALElementFactoryRegistry.

#### Factory Class Registration

The MALContextFactory class shall provide a static method ‘registerFactoryClass’ in order to register the class of a specific MALContextFactory.

NOTE	–	This method may be useful in environments where several class loaders are involved, e.g. OSGi platforms.

The method signature shall be:

public static void registerFactoryClass(Class factoryClass)

throws java.lang.IllegalArgumentException

The ‘registerFactoryClass’ parameter shall be assigned as described in table 3-2.

Table 3-2:  MALContextFactory ‘registerFactoryClass’ Parameter

| Parameter | Description |
| --- | --- |
| factoryClass | Class extending MALContextFactory |

The method shall store the class in the factory class repository.

The method shall throw an IllegalArgumentException if the parameter ‘factoryClass’ is NULL or does not extend MALContextFactory.

#### Factory Class Deregistration

The MALContextFactory class shall provide a static method ‘deregisterFactoryClass’ in order to deregister the class of a specific MALContextFactory.

The method signature shall be:

public static void deregisterFactoryClass(Class factoryClass)

throws java.lang.IllegalArgumentException

The ‘deregisterFactoryClass’ parameter shall be assigned as described in table 3-3.

Table 3-3:  MALContextFactory ‘deregisterFactoryClass’ Parameter

| Parameter | Description |
| --- | --- |
| factoryClass | Class extending MALContextFactory |

The method shall remove the class from the factory class repository.

The method shall throw an IllegalArgumentException if the parameter ‘factoryClass’ is NULL or does not extend MALContextFactory.

The method shall do nothing if the class is not found in the factory class repository.

#### MALContextFactory Creation

A static method ‘newFactory’ shall be provided in order to return a MALContextFactory instance.

The method signature shall be:

public static MALContextFactory newFactory() throws MALException

The method shall use the system property ‘org.ccsds.moims.mo.mal.factory.class’ to determine the name of the MALContextFactory implementation class to load and instantiate.

The method shall lookup the MALContextFactory implementation class from the factory class repository.

If the MALContextFactory implementation class is not found in the factory class repository then it shall be loaded from the current class loader.

If the MALContextFactory implementation class is not found in the current class loader then a MALException shall be raised with the ClassNotFoundException as the cause.

The method ‘newFactory’ shall not return the value NULL.

If no MALContextFactory can be returned then a MALException shall be raised.

#### MALContext Instantiation

The MALContextFactory class shall provide an abstract public method ‘createMALContext’ in order to instantiate a MALContext.

The method signature shall be:

public abstract MALContext createMALContext(java.util.Map properties)

throws MALException

The ‘createMALContext’ parameter shall be assigned as described in table 3-4.

Table 3-4:  MALContextFactory ‘createMALContext’ Parameter

| Parameter | Description |
| --- | --- |
| properties | Properties required by the specific MALContext implementation |

The parameter ‘properties’ may be NULL.

The method ‘createMALContext’ shall not return the value NULL.

If no MALContext can be returned then a MALException shall be raised.

The ‘createMALContext’ method shall be implemented by the specific factory class.

#### MALArea Registration

The MALContextFactory class shall provide a static method ‘registerArea’ in order to register MALAreas.

The method signature shall be:

public static void registerArea(MALArea area)

throws java.lang.IllegalArgumentException, MALException

The ‘registerArea’ parameter shall be assigned as described in table 3-5.

Table 3-5:  MALContextFactory ‘registerArea’ Parameter

| Parameter | Description |
| --- | --- |
| Area | MALArea to register |

If the parameter ‘area’ is NULL then an IllegalArgumentException shall be raised.

If a MALArea having the same name has already been registered and if the registered MALArea is not the same object as the MALArea to register then a MALException shall be raised.

#### MALArea Query

The MALContextFactory class shall provide two static methods ‘lookupArea’ in order to look up a MALArea from:

- an area name;

- an area number.

The method signatures shall be:

public static MALArea lookupArea(Identifier areaName)

throws java.lang.IllegalArgumentException

public static MALArea lookupArea(UShort areaNumber)

throws java.lang.IllegalArgumentException

The ‘lookupArea’ parameters shall be assigned as described in table 3-6.

Table 3-6:  MALContextFactory ‘lookupArea’ Parameters

| Parameter | Description |
| --- | --- |
| areaName | Name of the area to look up |
| areaNumber | Number of the area to look up |

If the parameters ‘areaName’ or ‘areaNumber’ are NULL then an IllegalArgumentException shall be raised.

The method shall return NULL if the MALArea is not found.

#### Error Registration

The MALContextFactory class shall provide a static method ‘registerError’ in order to register errors.

The method signature shall be:

public static void registerError(UInteger errorNumber,

Identifier errorName)

throws java.lang.IllegalArgumentException, MALException

The ‘registerError’ parameters shall be assigned as described in table 3-5.

Table 3-7:  MALContextFactory ‘registerError’ Parameters

| Parameter | Description |
| --- | --- |
| errorNumber | Error code |
| errorName | Name of the error |

If the parameters ‘errorNumber’ or ‘errorName’ are NULL then an IllegalArgumentException shall be raised.

If an error having the same code is already registered then a MALException shall be raised.

#### Error Query

The MALContextFactory class shall provide a static method ‘lookupError’ in order to look up an error name from an error code.

The method signature shall be:

public static Identifier lookupError(UInteger errorNumber)

The ‘lookupError’ parameter shall be assigned as described in table 3-6.

Table 3-8:  MALContextFactory ‘lookupError’ Parameter

| Parameter | Description |
| --- | --- |
| errorNumber | Code of the error to look up |

The parameter ‘errorNumber’ may be NULL.

The method shall return NULL if the error is not found.

#### MALElementFactoryRegistry Getter

The MALContextFactory class shall provide a static method in order to get the default MALElementFactoryRegistry.

The method signature shall be:

public static MALElementFactoryRegistry getDefaultElementFactoryRegistry()

The method shall return the default MALElementFactoryRegistry that has been instantiated during the MALContextFactory class initialization.

### MALContext

#### Definition

A MALContext interface shall be defined in order to enable a client to consume and/or provide services.

A MALContext shall be a factory of:

- MALConsumerManager;

- MALProviderManager;

- MALBrokerManager.

#### MALContext Creation

A MALContext shall be created by calling the method ‘createMALContext’ provided by the MALContextFactory.

NOTE	–	Because of the infrastructure and communication setup done when a MALContext is created, a MALContext is a heavyweight object. Most clients will initiate and handle all their interaction patterns with a single MALContext. However, some applications may use several MALContext objects.

#### MALConsumerManager Creation

A method ‘createConsumerManager’ shall be defined in order to enable to create and activate multiple MALConsumerManagers.

The method signature shall be:

public MALConsumerManager createConsumerManager() throws MALException

The method ‘createConsumerManager’ shall not return the value NULL.

If no MALConsumerManager can be returned then a MALException shall be raised.

If the MALContext is closed then a MALException shall be raised.

#### MALProviderManager Creation

A method ‘createProviderManager’ shall be defined in order to enable to create and activate multiple MALProviderManagers.

The method signature shall be:

public MALProviderManager createProviderManager() throws MALException

The method ‘createProviderManager’ shall not return the value NULL.

If no MALProviderManager can be returned then a MALException shall be raised.

If the MALContext is closed then a MALException shall be raised.

#### MALBrokerManager Creation

A method ‘createBrokerManager’ shall be defined in order to enable to create and activate multiple MALBrokerManagers by calling a method called ‘createBrokerManager’.

The method signature shall be:

public MALBrokerManager createBrokerManager() throws MALException

The method ‘createBrokerManager’ shall not return the value NULL.

If no MALBrokerManager can be returned then a MALException shall be raised.

If the MALContext is closed then a MALException shall be raised.

#### Get a Transport

Two methods ‘getTransport’ shall be defined in order to get the reference of a MALTransport:

- the first one shall take as a parameter the name of the protocol to be supported by the MALTransport;

- the second one shall take as a parameter a URI which protocol is to be supported by the MALTransport.

The method signatures shall be:

public MALTransport getTransport(String protocol)

throws java.lang.IllegalArgumentException, MALException

public MALTransport getTransport(URI uri)

throws java.lang.IllegalArgumentException, MALException

The ‘getTransport’ parameters shall be assigned as described in table 3-9.

Table 3-9:  MALContext ‘getTransport’ Parameters

| Parameter | Description |
| --- | --- |
| protocol | Name of the protocol to be supported |
| uri | URI which protocol is to be supported |

If the parameters ‘protocol’ or ‘uri’ are NULL then an IllegalArgumentException shall be raised.

The method shall return a unique MALTransport instance for a given protocol.

If there is still no instance of the MALTransport for the specified protocol then such an instance shall be created.

If no MALTransport can be returned then a MALException shall be raised.

If the MALContext is closed then a MALException shall be raised.

#### Close the MALContext

A method ‘close’ shall be defined in order to synchronously close all the MALConsumerManager, MALProviderManager and MALBrokerManager instances that have been created by this MALContext.

NOTE	–	In order to release the resources allocated by a MALContext, clients should close it when it is no longer used. The MALContext should be explicitly closed because it may be referenced by internal threads, making the Java Virtual Machine (JVM) garbage collector unable to release the allocated resources.

The method signature shall be:

public void close() throws MALException

If an internal error occurs then a MALException shall be raised.

### MALService

#### Definition

A MALService class shall be defined in order to represent the specification of a service (reference [1]).

The class shall define the attributes specified in table 3-10.

Table 3-10:  MALService Attributes

| Attribute | Type |
| --- | --- |
| number | UShort |
| name | Identifier |
| version | UOctet |
| area | MALArea |
| elementFactoryRegistry | MALElementFactoryRegistry |

#### Null Service Number

The following constant shall be defined:

public static final UShort NULL_SERVICE_NUMBER = new UShort(0);

#### Creation

The MALService constructor signature shall be:

public MALService(

UShort number,

Identifier name,

UOctet version

) throws java.lang.IllegalArgumentException

The MALService constructor parameters shall be assigned as described in table 3-11.

Table 3-11:  MALService Constructor Parameters

| Parameter | Description |
| --- | --- |
| number | Number of the service |
| name | Name of the service |
| version | Version of the service |

If the parameters ‘number’ or ‘name’ or ‘version’ are NULL then an IllegalArgumentException shall be raised.

The attribute ‘number’ shall be assigned with the value of the parameter ‘number’.

The attribute ‘name’ shall be assigned with the value of the parameter ‘name’.

The attribute ‘version’ shall be assigned with the value of the parameter ‘version’.

#### Getters

The MALService class shall provide the following getters:

- Name getter:

public Identifier getName()

- Area getter:

public MALArea getArea()

- Number getter:

public UShort getNumber()

- Version getter:

public UOctet getVersion()

- Element factory registry getter:

public MALElementFactoryRegistry getElementFactoryRegistry()

- Operation getters:

- Getter from the operation number:

public MALOperation getOperationByNumber(int opNumber)

- Getter from the operation name:

public MALOperation getOperationByName(Identifier opName)

- Getter from the capability set:

public MALOperation[] getOperationsByCapabilitySet(int capabilitySet)

- Send IP operation getter:

public MALSendOperation[] getSendOperations()

- Submit IP operation getter:

public MALSubmitOperation[] getSubmitOperations()

- Request IP operation getter:

public MALRequestOperation[] getRequestOperations()

- Invoke IP operation getter:

public MALInvokeOperation[] getInvokeOperations()

- Progress IP operation getter:

public MALProgressOperation[] getProgressOperations()

- Publish-Subscribe IP operation getter:

public MALPubSubOperation[] getPubSubOperations()

#### Set the Area

A method ‘setArea’ shall be defined in order to set the value of the attribute ‘area’.

The method shall be called only by the MALArea method ‘addService’. The control access level shall be ‘package’.

The method signature shall be:

void setArea(MALArea area) throws java.lang.IllegalArgumentException

The setArea parameter shall be assigned as described in table 3-12.

Table 3-12:  MALService ‘setArea’ Parameter

| Parameter | Description |
| --- | --- |
| area | MALArea that owns this MALService |

If the parameter ‘area’ is NULL then an IllegalArgumentException shall be raised.

The attribute ‘area’ shall be assigned with the value of the parameter ‘area’.

#### Set the Element Factory Registry

A method ‘setElementFactoryRegistry’ shall be defined in order to set the value of the attribute ‘elementFactoryRegistry’.

The method signature shall be:

public void setElementFactoryRegistry(MALElementFactoryRegistry

elementFactoryRegistry) throws java.lang.IllegalArgumentException

The ‘setElementFactoryRegistry’ parameter shall be assigned as described in table 3-12.

Table 3-13:  MALService ‘setElementFactoryRegistry’ Parameter

| Parameter | Description |
| --- | --- |
| elementFactoryRegistry | MALElementFactoryRegistry to be used for this MALService |

If the parameter ‘elementFactoryRegistry’ is NULL then an IllegalArgumentException shall be raised.

The attribute ‘elementFactoryRegistry’ shall be assigned with the value of the parameter ‘elementFactoryRegistry’.

#### Add an Operation

A method ‘addOperation’ shall be defined in order to enable to populate the list of operations provided by a service.

The method signature shall be:

public void addOperation(MALOperation operation)

throws java.lang.IllegalArgumentException

The ‘addOperation’ parameter shall be assigned as described in table 3-14.

Table 3-14:  MALService ‘addOperation’ Parameter

| Parameter | Description |
| --- | --- |
| operation | MALOperation to be added into this MALService |

If the parameter ‘operation’ is NULL then an IllegalArgumentException shall be raised.

The method ‘setService’ provided by the MALOperation shall be called with the reference of this MALService as a parameter.

### MALOperation

#### Definition

A MALOperation class shall be defined in order to represent the specification of an operation provided by a service (reference [1]).

The class shall be abstract.

The class shall be extended by one class defined for each Interaction Pattern

The class shall define the attributes specified in table 3-15.

Table 3-15:  MALOperation Attributes

| Attribute | Type |
| --- | --- |
| number | UShort |
| name | Identifier |
| replayable | Boolean |
| interactionType | InteractionType |
| capabilitySet | UShort |
| service | MALService |

#### Creation

The constructor signature of the MALOperation shall be:

public MALOperation(

UShort number,

Identifier name,

Boolean replayable,

InteractionType interactionType,

UShort capabilitySet)

throws java.lang.IllegalArgumentException

The MALOperation constructor parameters shall be assigned as described in table 3-16.

Table 3-16:  MALOperation Constructor Parameters

| Parameter | Description |
| --- | --- |
| number | Number of the operation |
| name | Name of the operation |
| replayable | Boolean that indicates whether the operation is replayable or not |
| interactionType | Interaction type of the operation |
| capabilitySet | Capability set number of the operation |

If the parameters ‘number’ or ‘name’ or ‘replayable’ or ‘interactionType’ or ‘capabilitySet’ are NULL then an IllegalArgumentException shall be raised.

The attribute ‘number’ shall be assigned with the value of the parameter ‘number’.

The attribute ‘name’ shall be assigned with the value of the parameter ‘name’.

The attribute ‘replayable’ shall be assigned with the value of the parameter ‘replayable’.

The attribute ‘interactionType’ shall be assigned according to the parameter ‘interactionType’.

The attribute ‘capabilitySet’ shall be assigned with the value of the parameter ‘capabilitySet’.

#### Getters

The MALOperation class shall provide the following getters:

- Name getter:

public Identifier getName()

- Number getter:

public UShort getNumber()

- InteractionType getter:

public InteractionType getInteractionType()

- Replayable getter:

public Boolean isReplayable()

- Service getter:

public MALService getService()

- CapabilitySet getter:

public UShort getCapabilitySet()

#### Get a MALOperationStage

An abstract method ‘getOperationStage’ shall be defined in order to return a MALOperationStage from its number.

The method signature shall be:

public abstract MALOperationStage getOperationStage(UOctet stageNumber)

throws java.lang.IllegalArgumentException

The ‘getOperationStage’ parameter shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 3-17:  MALOperation ‘getOperationStage’ Parameter

| Parameter | Description |
| --- | --- |
| stageNumber | Number of the MALOperationStage |

If the parameter ‘stageNumber’ is NULL then an IllegalArgumentException shall be raised.

The method shall return NULL only if the stage does not exist for that operation IP.

The method shall be implemented by the specific MAL<<Ip>>Operation classes.

#### Set the Service

A method ‘setService’ shall be defined in order to set the value of the attribute ‘service’.

The method shall be called by the MALService constructor.

The control access level shall be ‘package’.

The method signature shall be:

void setService(MALService service)

throws java.lang.IllegalArgumentException

The ‘setService’ parameter shall be assigned as described in table 3-18.

Table 3-18:  MALOperation ‘setService’ Parameter

| Parameter | Description |
| --- | --- |
| service | Service that owns this operation |

If the parameter ‘service’ is NULL then an IllegalArgumentException shall be raised.

The attribute ‘service’ shall be assigned with the value of the parameter ‘service’.

### MAL<<Ip>>Operation

#### Definition

A MAL<<Ip>>Operation class shall be defined for each interaction pattern. Their class names shall be:

- MALSendOperation;

- MALSubmitOperation;

- MALRequestOperation;

- MALInvokeOperation;

- MALProgressOperation;

- MALPubSubOperation.

#### Interaction Stages Constants

The MAL<<Ip>>Operation shall define constants giving the interaction stage values for the stages listed in table 3-19.

Table 3-19:  Interaction Stages Constants

| IP | stage name | stage value (HEX) |
| --- | --- | --- |
| Send | - | - |
| Submit | SUBMIT | 0x1 |
|  | SUBMIT_ACK | 0x2 |
| Request | REQUEST | 0x1 |
|  | REQUEST_RESPONSE | 0x2 |
| Invoke | INVOKE | 0x1 |
|  | INVOKE_ACK | 0x2 |
|  | INVOKE_RESPONSE | 0x3 |
| Progress | PROGRESS | 0x1 |
|  | PROGRESS_ACK | 0x2 |
|  | PROGRESS_UPDATE | 0x3 |
|  | PROGRESS_RESPONSE | 0x4 |
| PubSub | REGISTER | 0x1 |
|  | REGISTER_ACK | 0x2 |
|  | PUBLISH_REGISTER | 0x3 |
|  | PUBLISH_REGISTER_ACK | 0x4 |
|  | PUBLISH | 0x5 |
|  | NOTIFY | 0x6 |
|  | DEREGISTER | 0x7 |
|  | DEREGISTER_ACK | 0x8 |
|  | PUBLISH_DEREGISTER | 0x9 |
|  | PUBLISH_DEREGISTER_ACK | 0xA |

The constants shall be declared as specified below:

public static final byte _<<STAGE NAME>>_STAGE = 0x<<stage value>>

public static final UOctet <<STAGE NAME>>_STAGE = new UOctet(_<<STAGE NAME>>_STAGE)

#### Creation

For every interaction type except PUBLISH-SUBSCRIBE the constructor signature of the MAL<<Ip>>Operation shall be:

public MAL<<Ip>>Operation(

UShort number,

Identifier name,

Boolean replayable,

UShort capabilitySet,

<<stages>>)

throws java.lang.IllegalArgumentException

The ‘stages’ variable value shall enable to pass a MALOperationStage parameter for each interaction stage.

The ‘stages’ parameters shall be declared according to the IP variable as described in table 3-20.

Table 3-20:  Operation Stages

| IP | Stages |
| --- | --- |
| Send | MALOperationStage sendStage |
| Submit | MALOperationStage submitStage |
| Request | MALOperationStage requestStage, MALOperationStage responseStage |
| Invoke | MALOperationStage invokeStage, MALOperationStage invokeAckStage, MALOperationStage invokeResponseStage |
| Progress | MALOperationStage progressStage, MALOperationStage progressAckStage, MALOperationStage progressUpdateStage, MALOperationStage progressResponseStage |

The constructor signature of the MALPubSubOperation shall be:

public MALPubSubOperation(

UShort number,

Identifier name,

Boolean replayable,

UShort capabilitySet,

Object[] updateListShortForms,

Object[] lastUpdateListShortForms)

throws java.lang.IllegalArgumentException

The MAL<<Ip>>Operation constructor parameters shall be assigned as described in table 3-21.

Table 3-21:  MAL<<Ip>>Operation Constructor Parameters

| Parameter | Description |
| --- | --- |
| number | Number of the operation |
| name | Name of the operation |
| replayable | Boolean that indicates whether the operation is replayable or not |
| capabilitySet | Capability set number of the operation |
| sendStage | MALOperationStage representing the first stage of a SEND operation |
| submitStage | MALOperationStage representing the first stage of a SUBMIT operation |
| requestStage | MALOperationStage representing the first stage of a REQUEST operation |
| responseStage | MALOperationStage representing the first stage of a REQUEST operation |
| invokeStage | MALOperationStage representing the first stage of an INVOKE operation |
| invokeAckStage | MALOperationStage representing the ACK stage of an INVOKE operation |
| invokeResponseStage | MALOperationStage representing the RESPONSE stage of an INVOKE operation |
| progressStage | MALOperationStage representing the first stage of a PROGRESS operation |
| progressAckStage | MALOperationStage representing the ACK stage of a PROGRESS operation |
| progressUpdateStage | MALOperationStage representing the UPDATE stage of a PROGRESS operation |
| progressResponseStage | MALOperationStage representing the RESPONSE stage of a PROGRESS operation |
| updateListShortForms | Absolute short forms of the update lists transmitted by the PUBLISH/NOTIFY message of a PUBLISH-SUBSCRIBE operation |
| lastUpdateListShortForms | Absolute short forms of the update lists that can be assigned to the last element of the PUBLISH/NOTIFY message body |

If the parameters ‘number’ or ‘name’ or ‘replayable’ or ‘interactionType’ or ‘capabilitySet’ are NULL then an IllegalArgumentException shall be raised.

If the PUBLISH/NOTIFY message body is empty then the ‘updateListShortForms’ and the ‘lastUpdateListShortForms’ shall be empty arrays.

The ‘updateListShortForms’ shall not contain the value NULL except in the last item of the array if the declared type of the last element is abstract;

#### Get a MALOperationStage

The method ‘getOperationStage’ inherited from MALOperation shall be implemented by returning the MALOperationStage representing the specified stage.

MALSendOperation shall return the MALOperationStage representing the Send stage whatever the specified stage is.

### MALOperationStage

#### Definition

A MALOperationStage class shall be defined in order to represent the element types used by an operation during a stage as specified by the reference [1].

The class shall define the attributes specified in table 3-15.

Table 3-22:  MALOperationStage Attributes

| Attribute | Type |
| --- | --- |
| number | UOctet |
| operation | MALOperation |
| elementShortForms | Object[] |
| lastElementShortForms | Object[] |

#### Creation

The MALOperationStage constructor signature shall be:

public MALOperationStage(

UOctet number,

Object[] elementShortForms,

Object[] lastElementShortForms

) throws java.lang.IllegalArgumentException

The MALOperationStage constructor parameters shall be assigned as described in table 3-11.

Table 3-23:  MALOperationStage Constructor Parameters

| Parameter | Description |
| --- | --- |
| number | Number of the interaction stage |
| elementShortForms | Short forms of the body element types |
| lastElementShortForms | Short forms of the types that can be used for the last element in case of polymorphism |

If the parameters ‘number’ or ‘elementShortForms’ or ‘lastElementShortForms’ are NULL then an IllegalArgumentException shall be raised.

If the message body is empty then the ‘elementShortForms’ and the ‘lastElementShortForms’ shall be empty arrays.

The ‘elementShortForms’ shall not contain the value NULL except in the last item of the array if the declared type of the last element is abstract;

The attribute ‘number’ shall be assigned with the value of the parameter ‘number’.

The attribute ‘elementShortForms’ shall be assigned with the value of the parameter ‘elementShortForms’.

The attribute ‘lastElementShortForms’ shall be assigned with the value of the parameter ‘lastElementShortForms’.

#### Getters and setters

The MALOperation class shall provide the following getters and setters:

- Number getter:

public UOctet getNumber()

- Body short forms getter:

public Object[] getElementShortForms()

- Last element short forms getter and setter:

public Object[] getLastElementShortForms()

public void setLastElementShortForms(Object[] shortForms)

- Operation getter:

public MALOperation getOperation()

#### Set the Operation

A method ‘setOperation’ shall be defined in order to set the value of the attribute ‘operation’.

The method shall be called by the MALOperation constructor.

The control access level shall be ‘package’.

The method signature shall be:

void setOperation(MALOperation operation)

throws java.lang.IllegalArgumentException

The ‘setOperation’ parameter shall be assigned as described in table 3-18.

Table 3-24:  MALOperation ‘setOperation’ Parameter

| Parameter | Description |
| --- | --- |
| operation | Operation that owns this MALOperationStage |

If the parameter ‘operation’ is NULL then an IllegalArgumentException shall be raised.

The attribute ‘operation’ shall be assigned with the value of the parameter ‘operation’.

### MALArea

#### Definition

A MALArea class shall be defined in order to represent the specification of an area of services (reference [1]).

The class shall define the attributes specified in table 3-25.

Table 3-25:  MALService Attributes

| Attribute | Type |
| --- | --- |
| number | UShort |
| name | Identifier |

#### Creation

The constructor signature shall be:

public MALArea(UShort number, Identifier name)

throws java.lang.IllegalArgumentException

The MALArea constructor parameters shall be assigned as described in table 3-26.

Table 3-26:  MALArea Constructor Parameters

| Parameter | Description |
| --- | --- |
| number | Number of the area |
| name | Name of the area |

If the parameters ‘number’ or ‘name’ are NULL then an IllegalArgumentException shall be raised.

The attribute ‘number’ shall be assigned with the value of the parameter ‘number’.

The attribute ‘name’ shall be assigned with the value of the parameter ‘name’.

#### Getters

The following getters shall be provided:

- Number getter:

public UShort getNumber()

- Name getter:

public Identifier getName()

- Services getter:

public MALService[] getServices()

- Service getter by name and version:

public MALService getServiceByNameAndVersion(

Identifier serviceName, UOctet version)

- Service getter by number and version:

public MALService getServiceByNumberAndVersion(

UShort serviceNumber, UOctet version)

#### Add a Service

A method ‘addService’ shall be defined in order to add a MALService to this MALArea.

The method signature shall be:

public void addService(MALService service)

throws java.lang.IllegalArgumentException, MALException

The ‘addService’ parameter shall be assigned as described in table 3-27.

Table 3-27:  MALArea ‘addService’ Parameter

| Parameter | Description |
| --- | --- |
| service | Service to add to the area |

If the parameter ‘service’ is NULL then an IllegalArgumentException shall be raised.

It shall be allowed to add several MALServices representing different versions of the same service into the same MALArea.

If a service with the same name or number and the same version is already owned by the area then a MALException shall be raised.

The method ‘setArea’ provided by the MALService shall be called with the reference of this MALArea as a parameter.

### MALHelper

The MALHelper class shall be generated from the class template defined in section 4.8.3 for the area “MAL”.

### MALStandardError

#### Definition

A MALStandardError class shall be defined in order to represent a MAL error.

#### Creation

The MALStandardError constructor signature shall be:

public MALStandardError(

UInteger errorNumber,

Object extraInformation)

throws java.lang.IllegalArgumentException

The MALStandardError constructor parameters shall be assigned as described in table 3-11.

Table 3-28:  MALService Constructor Parameters

| Parameter | Description |
| --- | --- |
| errorNumber | Number of the MAL standard error |
| extraInformation | Extra information associated with the error |

If the parameter ‘errorNumber’ is NULL then an IllegalArgumentException shall be raised.

The parameter ‘extraInformation’ may be NULL.

#### Getters

The following getters shall be provided:

- Error number getter:

public UInteger getErrorNumber()

- Extra information getter:

public Object getExtraInformation()

#### Get the Error Name

A method ‘getErrorName’ shall be defined in order to return the name of the error which number is specified by the ERROR message.

The signature of ‘getErrorName’ shall be:

public Identifier getErrorName()

The method ‘getErrorName’ shall resolve the name of the error from the MALContextFactory error repository.

#### ToString

The method ‘toString’ shall be redefined by returning a String formatted as follows:

- the first character shall be ‘(’;

- the string “errorNumber=” shall be appended;

- the toString representation of the field ‘errorNumber’ shall be appended;

- the character ‘,’ shall be appended;

- the string “errorName=” shall be appended;

- the name of the error shall be resolved from the MALContextFactory error repository and appended;

- the character ‘,’ shall be appended;

- the string “extraInformation=” shall be appended;

- if ‘extraInformation’ is NULL then nothing shall be appended otherwise the toString representation of the field ‘extraInformation’ shall be appended;

- the last character shall be ‘)’.

### MALException

#### Definition

A MALException class shall be defined in order to enable the MAL API to raise an error as an exception.

The class shall extend the class java.lang.Exception.

#### Creation

Three constructors shall be defined in order to create a MALException:

- with an empty constructor;

- from a String message;

- from a String message and a java.lang.Throwable cause.

The constructor signatures shall be:

public MALException()

public MALException(String message)

public MALException(String message, Throwable cause)

The constructor parameters shall be assigned as described in table 3-30.

Table 3-29:  MALException Constructor Parameters

| Parameter | Description |
| --- | --- |
| message | Error message |
| cause | The error that caused this MALException to be raised |

The parameter ‘message’ shall be assigned with a message explaining why this MALException is raised.

If this MALException is causally linked to an exception then the parameter ‘cause’ shall be assigned with the linked exception.

If this MALException is not causally linked to an exception then the parameter ‘cause’ shall be NULL.

The MALException constructor shall call the java.lang.Exception constructor having the same signature and pass the parameters.

### MALInteractionException

#### Definition

A MALInteractionException class shall be defined in order to raise a MAL standard error (defined in reference [1]) as a java.lang.Exception.

The class shall extend the class java.lang.Exception.

#### Creation

A public constructor shall be defined with a MALStandardError parameter.

The constructor signature shall be:

public MALInteractionException(MALStandardError standardError)

The constructor parameter shall be assigned as described in table 3-30.

Table 3-30:  MALInteractionException Constructor Parameter

| Parameter | Description |
| --- | --- |
| standardError | Error to be raised |

The constructor shall call the java.lang.Exception constructor with the String representation of the MALStandardError ‘extraInformation’ field or NULL if the ‘extraInformation’ is NULL.

#### Getter

A getter method shall be defined in order to return the MALStandardError:

public MALStandardError getStandardError()

### MALElementFactory

#### Definition

A MALElementFactory interface shall be defined in order to allow the creation of an element in a generic way, i.e., using the MAL::Element polymorphism.

#### Create an Element

A method ‘createElement’ shall be provided in order to instantiate an element.

The method signature shall be:

public Object createElement()

### MALElementFactoryRegistry

#### Definition

A MALElementFactoryRegistry class shall be defined in order to map the MALElementFactory instances to the absolute short form of the created element.

The class and its methods shall not be final in order that an extension class can be defined.

#### Register a MALElementFactory

A method ‘registerElementFactory’ shall be provided in order to map a MALElementFactory to the absolute short form of the created element.

The method signature shall be:

public void registerElementFactory(Object shortForm,

MALElementFactory elementFactory)

throws java.lang.IllegalArgumentException, MALException

The ‘registerElementFactory’ parameters shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 3-31:  MALElementFactoryRegistry ‘registerElementFactory’ Parameters

| Parameter | Description |
| --- | --- |
| shortForm | Absolute short form of the element created by the registered MALElementFactory |
| elementFactory | The registered MALElementFactory |

If the parameter ‘shortForm’ or ‘elementFactory’ are NULL then an IllegalArgumentException shall be raised.

#### Lookup a MALElementFactory

A method ‘lookupElementFactory’ shall be provided in order to get a MALElementFactory from the absolute short form of an element.

The method signature shall be:

public MALElementFactory lookupElementFactory(Object shortForm)

throws java.lang.IllegalArgumentException

The ‘lookupElementFactory’ parameter shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 3-32:  MALElementFactoryRegistry ‘lookupElementFactory’ Parameter

| Parameter | Description |
| --- | --- |
| shortForm | Absolute short form of an element |

If the parameter ‘shortForm’ is NULL then an IllegalArgumentException shall be raised.

#### Deregister a MALElementFactory

A method ‘deregisterElementFactory’ shall be provided in order to remove a registered MALElementFactory from this MALElementFactoryRegistry.

The method signature shall be:

public boolean deregisterElementFactory(Object shortForm)

throws java.lang.IllegalArgumentException

The ‘deregisterElementFactory’ parameter shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 3-33:  MALElementFactoryRegistry ‘deregisterElementFactory’ Parameter

| Parameter | Description |
| --- | --- |
| shortForm | Absolute short form of the registered MALElementFactory to remove |

If the parameter ‘shortForm’ is NULL then an IllegalArgumentException shall be raised.

The method shall return TRUE if the MALElementFactory is found and removed.

The method shall return FALSE if the MALElementFactory is not found.

## Data structures package

### Overview

This subsection defines the classes and interfaces that are related to the MAL data types as defined in reference [1]. They belong to the Java package:

org.ccsds.moims.mo.mal.structures

### Element

#### Definition

An Element interface shall be defined in order to represent the MAL::Element type.

The interface shall define a pair of methods for encoding and decoding the element.

#### Short Form Query

A method ‘getShortForm’ shall be defined in order to return the absolute short form of the element type.

The method signature shall be:

public Long getShortForm()

#### Area Number Query

A method ‘getAreaNumber’ shall be defined in order to return the number of the area this element type belongs to.

The method signature shall be:

public UShort getAreaNumber()

#### Service Number Query

A method ‘getServiceNumber’ shall be defined in order to return the number of the service this element type belongs to.

The method signature shall be:

public UShort getServiceNumber()

#### Type Short Form Query

A method ‘getTypeShortForm’ shall be defined in order to return the relative short form of the element type.

The method signature shall be:

public Integer getTypeShortForm()

#### Create an Element

A method ‘createElement’ shall be defined in order to allow the creation of an element in a generic way, i.e., using the MAL::Element polymorphism.

The method signature shall be:

public Element createElement()

#### Encoding

A method ‘encode’ shall be defined in order to encode this Element.

The method signature shall be:

public void encode(MALEncoder encoder) throws MALException

The ‘encode’ parameter shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 3-34:  Element ‘encode’ Parameter

| Parameter | Description |
| --- | --- |
| encoder | MALEncoder to be used in order to encode this Element |

If an error occurs then a MALException shall be raised.

#### Decoding

A method ‘decode’ shall be defined in order to decode an Element.

The method signature shall be:

public Element decode(MALDecoder decoder) throws MALException

The ‘decode’ parameter shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 3-35:  Element ‘decode’ Parameter

| Parameter | Description |
| --- | --- |
| decoder | MALDecoder to be used in order to decode an Element |

If an error occurs then a MALException shall be raised.

The method shall not return the value NULL.

The returned Element may be not the same instance as this Element.

### Attribute

#### Definition

An Attribute interface shall be defined in order to represent the MAL::Attribute type.

NOTE	–	The mapping of the MAL::Attribute types is defined in section 3.3.8.

The Attribute interface shall extend the Element interface.

NOTE	–	This interface defines no method; it is a marker interface.

#### Area Service Number

The following constant shall be declared:

public static final long ABSOLUTE_AREA_SERVICE_NUMBER = 0x1000000000000L

#### Short Form Declaration

For each attribute type, the following constants shall be declared:

public static final int _<<ATTRIBUTE>>_TYPE_SHORT_FORM =

<<attribute short form>>

public static final Integer <<ATTRIBUTE>>_TYPE_SHORT_FORM =

_<<ATTRIBUTE>>_TYPE_SHORT_FORM

public static final Long <<ATTRIBUTE>>_SHORT_FORM =

ABSOLUTE_AREA_SERVICE_NUMBER + _<<ATTRIBUTE>>_TYPE_SHORT_FORM

### Composite

A Composite interface shall be defined in order to represent the MAL::Composite type.

The Composite interface shall be implemented by the classes representing the MAL::Composite data types.

The Composite interface shall extend the Element interface.

NOTE	–	This interface defines no method; it is a marker interface.

### MALEncoder and MALDecoder

#### Definition

The MALEncoder and MALDecoder interfaces shall be defined in order to provide encoding and decoding methods for the following data:

- an <<Attribute>>;

- a MAL::Element which type is statically defined by the service;

- a MAL::Attribute which type is not statically defined by the service (Attribute polymorphism).

The MALEncoder and MALDecoder interfaces shall also provide methods for creating MALListEncoder and MALListDecoder.

The encoding methods shall be defined in the interface MALEncoder.

The decoding methods shall be defined in the interface MALDecoder.

Two methods shall be provided in order to encode elements that may be NULL or not.

Two methods shall be provided in order to decode elements that may be NULL or not.

The variables defined in table [MALEncoder and MALDecoder Variables]Erreur ! Source du renvoi introuvable. shall be applied to the following code templates.

Table 3-36:  MALEncoder and MALDecoder Variables

| Variable name | Content |
| --- | --- |
| Attribute | Type name of the MAL attribute |
| Java mapping type | Java type used to represent the MAL attribute |

#### Encode an <<Attribute>>

Two encoding methods shall be defined for each MAL attribute type.

The encoding methods signature shall be:

public void encode<<Attribute>>(<<Java mapping type>> attribute)

throws java.lang.IllegalArgumentException, MALException

public void encodeNullable<<Attribute>>(<<Java mapping type>> attribute)

throws MALException

The ‘encode[Nullable]<<Attribute>>’ parameter shall be assigned as described in table 3-37.

Table 3-37:  MALEncoder ‘encode[Nullable]<<Attribute>>’ Parameter

| Parameter | Description |
| --- | --- |
| attribute | Attribute to encode |

If the method is ‘encodeNullable<<Attribute>>’ then the parameter ‘attribute’ may be NULL.

If the method is ‘encode<<Attribute>>’ and if the parameter ‘attribute’ is NULL then an IllegalArgumentException shall be raised.

If an error occurs then a MALException shall be raised.

#### Decode an <<Attribute>>

Two decoding methods shall be defined for each MAL attribute type.

The decoding methods signature shall be:

public <<Java mapping type>> decode<<Attribute>>() throws MALException

public <<Java mapping type>> decodeNullable<<Attribute>>()

throws MALException

If an error occurs then a MALException shall be raised.

#### Encoding an Element from a List

The elements from a list shall be indirectly encoded using a MALListEncoder.

A method ‘createListEncoder’ shall be defined for creating a MALListEncoder.

The List shall be passed as a parameter of the ‘createListEncoder’ method in order to enable the MALListEncoder to prepare the list encoding.

The ‘createListEncoder’ method signature shall be:

public MALListEncoder createListEncoder(List list)

throws java.lang.IllegalArgumentException

The ‘createListEncoder’ parameter shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 3-38:  MALListEncoder ‘createListEncoder’ Parameter

| Parameter | Description |
| --- | --- |
| list | List to be encoded |

If the parameter ‘list’ is NULL then an IllegalArgumentException shall be raised.

#### Decoding an Element from a List

The elements from a list shall be indirectly decoded using a MALListDecoder.

A method ‘createListDecoder’ shall be defined for creating a MALListDecoder.

The List shall be passed as a parameter of the ‘createListDecoder’ method in order to enable the MALListDecoder to handle the list decoding.

The ‘createListDecoder’ method signature shall be:

public MALListDecoder createListDecoder(List list)

throws java.lang.IllegalArgumentException

The ‘createListDecoder’ parameter shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 3-39:  MALListDecoder ‘createListDecoder’ Parameter

| Parameter | Description |
| --- | --- |
| list | List to be decoded |

If the parameter ‘list’ is NULL then an IllegalArgumentException shall be raised.

#### Encode an Element

Two encoding methods shall be defined for the Element type.

The encoding methods signature shall be:

public void encodeElement(Element element)

throws java.lang.IllegalArgumentException, MALException

public void encodeNullableElement(Element element) throws MALException

The ‘encode[Nullable]Element’ parameter shall be assigned as described in table 3-40.

Table 3-40:  MALEncoder ‘encode[Nullable]Element’ Parameter

| Parameter | Description |
| --- | --- |
| element | Element to encode |

If the method is ‘encodeNullableElement’ then the parameter ‘element’ may be NULL.

If the method is ‘encodeElement’ and if the parameter ‘element’ is NULL then an IllegalArgumentException shall be raised.

If an error occurs then a MALException shall be raised.

#### Decode an Element

Two decoding methods shall be defined for the Element type.

The decoding methods signature shall be:

public Element decodeElement(Element element)

throws java.lang.IllegalArgumentException, MALException

public Element decodeNullableElement(Element element)

throws java.lang.IllegalArgumentException, MALException

The ‘decode[Nullable]Element’ parameter shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 3-41:  MALDecoder ‘decode[Nullable]Element’ Parameter

| Parameter | Description |
| --- | --- |
| element | Element to decode |

If the parameter ‘element’ is NULL then an IllegalArgumentException shall be raised.

The returned element may be not the same instance as the parameter ‘element’.

If an error occurs then a MALException shall be raised.

#### Encode an Attribute

Two encoding methods shall be defined for the Attribute type.

The encoding methods signatures shall be:

public void encodeAttribute(Attribute attribute)

throws java.lang.IllegalArgumentException, MALException

public void encodeNullableAttribute(Attribute attribute)

throws MALException

The ‘encode[Nullable]Attribute’ parameter shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 3-42:  MALEncoder ‘encode[Nullable]Attribute’ Parameter

| Parameter | Description |
| --- | --- |
| attribute | Attribute to encode |

If the method is ‘encodeNullableAttribute’ then the parameter ‘attribute’ may be NULL.

If the method is ‘encodeAttribute’ and if the parameter ‘attribute’ is NULL then an IllegalArgumentException shall be raised.

If an error occurs then a MALException shall be raised.

#### Decode an Attribute

Two decoding methods shall be defined for the Attribute type.

The decoding methods signatures shall be:

public Attribute decodeAttribute() throws MALException

public Attribute decodeNullableAttribute() throws MALException

If an error occurs then a MALException shall be raised.

### MALListDecoder and MALListEncoder

#### Definition

The MALListDecoder and MALListEncoder interfaces shall be defined in order to provide methods for encoding and decoding the elements of a list.

#### Encoding

The MALListEncoder interface shall extend the interface MALEncoder in order to provide the methods required for encoding the elements that belong to the list.

A method ‘close’ shall be defined in order to notify the MALListEncoder that the list is over.

The method signature shall be:

public void close();

#### Decoding

The MALListDecoder interface shall extend the interface MALDecoder in order to provide the methods required for decoding the elements that belong to the list.

A method ‘hasNext’ shall be provided in order to check if the list has been entirely decoded:

- this method shall return TRUE if there is still at least one element to decode;

- otherwise it shall return FALSE: all the elements of the list have been decoded.

The method signature shall be:

public boolean hasNext();

NOTE	–	A stream-based implementation of the method ‘hasNext’ may check that the number of elements in the list is less than the expected size, implying that the list size has been encoded in the stream ahead of the elements. As the List is passed as a parameter when calling the method ‘createListDecoder’ the MALListDecoder can compare the current size of the List and the size it should reach once all the elements have been decoded.

### Enumeration

#### Definition

An abstract class ‘Enumeration’ shall be defined in order to represent the MAL::Enumeration type.

The class shall be extended by the classes representing a MAL enumeration type.

NOTE	–	The way to extend the Enumeration class is described in section 4.5.6.

The Enumeration class shall implement the Element interface.

#### Creation

A protected constructor shall be defined.

The constructor shall take as a parameter the ordinal, i.e., the value of the enumeration.

The constructor signature shall be:

protected Enumeration(int ordinal)

The constructor parameter shall be assigned as described in table 3-43.

Table 3-43:  Enumeration Constructor Parameter

| Parameter | Description |
| --- | --- |
| ordinal | The value of the enumeration |

#### Get the Ordinal

A getter shall be defined in order to return the value of the ordinal.

The method signature shall be:

public final int getOrdinal()

#### HashCode

The java.lang.Object method ‘hashCode’ shall be redefined by returning the ordinal value.

#### Equals

The java.lang.Object method ‘equals’ shall be redefined as follows:

- it shall return TRUE if the parameter has the same final type as this Enumeration and has the same ordinal value;

- otherwise it shall return FALSE.

### Attributes mapping

The MAL::Attribute types that are listed in table 3-44 shall be mapped to a Java type.

Table 3-44:  MAL::Attribute Types Mapped to a Java Type

| MAL::Attribute | Java type |
| --- | --- |
| Boolean | java.lang.Boolean |
| Float | java.lang.Float |
| Double | java.lang.Double |
| Octet | java.lang.Byte |
| Short | java.lang.Short |
| Integer | java.lang.Integer |
| Long | java.lang.Long |
| String | java.lang.String |

NOTE	–	Java primitive types (e.g. boolean, float, int) are not used because they cannot represent the value NULL.

NOTE 2–	As the Java types listed above do not implement the interface Element, a class Union is provided in order to enable the assignment of one of the mapped MAL::Attribute to an Element variable.

The other MAL::Attribute types shall be mapped to an Attribute class:

- Blob

- Duration

- Identifier

- Time

- FineTime

- UInteger

- ULong

- UOctet

- UShort

- URI

### Union

#### Definition

A Union class shall be defined in order to assign a MAL::Attribute mapped to a non-Element Java type (e.g. Boolean, String) to an Element variable.

The Union class shall implement the Attribute interface.

The variables defined in table 3-45 shall be applied to the Union code templates.

Table 3-45:  Union Variables

| Variable name | Content |
| --- | --- |
| Attribute type | Type name of a MAL::Attribute mapped to a Java type without the “MAL::” prefix |
| Attribute class | Class name of the Java type used to map the MAL::Attribute |
| Short form | Absolute short form of the MAL::Attribute |

#### Creation

The Union class shall provide a separate constructor for each MAL::Attribute type.

The method signature shall be:

public Union(<<Attribute class>> value)

throws java.lang.IllegalArgumentException

The constructor parameter shall be assigned as described in table 3-46.

Table 3-46:  Union Constructor Parameter

| Parameter | Description |
| --- | --- |
| value | Attribute value |

If the parameter ‘value’ is NULL then an IllegalArgumentException shall be raised.

#### Getters

The Union class shall provide a getter for each MAL::Attribute type.

The method signature shall be:

public <<Attribute class>> get<<Attribute type>>Value()

#### Get the Short Form

The Union class shall implement the method ‘getShortForm’ inherited from the Element interface.

The method shall return the absolute short form of the MAL::Attribute represented by this Union.

#### Get the Area Number

The Union class shall implement the method ‘getAreaNumber’ inherited from the Element interface.

The method shall return the MALHelper constant MAL_AREA_NUMBER.

#### Get the Service Number

The Union class shall implement the method ‘getServiceNumber’ inherited from the Element interface.

The method shall return the MALService constant NULL_SERVICE_NUMBER.

#### Get the Type Short Form

The Union class shall implement the method ‘getTypeShortForm’ inherited from the Element interface.

The method shall return the relative short form of the MAL::Attribute represented by this Union.

#### HashCode

The java.lang.Object method ‘hashCode’ shall be redefined by returning the ‘hashCode’ of the Union ‘value’.

#### Equals

The java.lang.Object method ‘equals’ shall be redefined as follows:

- it shall return TRUE if the type of the parameter is Union and if its value is equal to the value of this Union;

- otherwise it shall return FALSE.

#### ToString

The java.lang.Object method ‘toString’ shall be redefined by returning the String representation of the Union ‘value’.

#### Create an Element

The method ‘createElement’ defined by the interface Element shall be implemented by calling the Union constructor declaring the attribute type, passing any value and returning the result.

#### Encode

The method ‘encode’ defined by the interface Element shall be implemented by encoding the Union value with the method ‘encode<<Attribute>>’ provided by the MALEncoder.

#### Decode

The method ‘decode’ defined by the interface Element shall be implemented by decoding the Union value with the method ‘decode<<Attribute>>’ provided by the MALDecoder and returning a new Union.

### Blob

#### Definition

A Blob class shall be defined in order to represent a MAL Blob.

The class shall implement the Attribute interface.

#### Short Form

The class Blob shall declare the constants and implement the methods as specified in section 4.5.5.

#### Empty Constructor

An empty constructor shall be provided.

The constructor signature shall be:

public Blob()

#### Byte Array Constructor

A constructor taking a byte array as a parameter shall be provided:

public Blob(byte[] blobValue)

throws java.lang.IllegalArgumentException

The byte array constructor parameter shall be assigned as described in table 3-47.

Table 3-47:  Blob Byte Array Constructor Parameter

| Parameter | Description |
| --- | --- |
| blobValue | Byte array to be wrapped in a MAL::Blob |

If the parameter ‘blobValue’ is NULL then an IllegalArgumentException shall be raised.

The byte array should not be modified after the constructor has been called.

NOTE	–	If the byte array is modified after the constructor has been called then the Blob behavior is unspecified.

#### URL Constructor

A constructor taking a URL typed String as a parameter shall be provided.

The constructor signature shall be:

public Blob(String url) throws java.lang.IllegalArgumentException

The URL constructor parameter shall be assigned as described in table 3-48.

Table 3-48:  Blob URL Constructor Parameter

| Parameter | Description |
| --- | --- |
| url | URL which designated content shall be loaded in this MAL::Blob |

If the parameter ‘url’ is NULL then an IllegalArgumentException shall be raised.

If the parameter ‘url’ syntax  is not compliant with references [3] and [4] then an IllegalArgumentException shall be raised.

The resource identified by the URL should not be modified until the method ‘detach’ is called.

NOTE	–	If the resource identified by the URL is modified after the constructor has been called then the Blob behavior is unspecified.

#### Check if URL Based

A method ‘isURLBased’ shall be defined in order to indicate whether the Blob contains a URL or not.

The method signature shall be:

public boolean isURLBased()

The method shall return TRUE if the Blob contains a URL; otherwise it shall return FALSE.

#### Get the Byte Array Value

A method ‘getValue’ shall be defined in order to return the value of this Blob as a byte array.

The method signature shall be:

public byte[] getValue() throws MALException

If the Blob contains a URL then the designated content shall be loaded and copied in the returned byte array.

A MALException shall be thrown if an internal error occurs.

The returned byte array should not be modified.

NOTE	–	If the returned byte array is modified then the Blob behavior is unspecified.

#### Get the URL

A method ‘getURL’ shall be defined in order to return the URL of this Blob.

The method signature shall be:

public String getURL()

If the Blob does not contain a URL then the method shall return NULL.

The resource identified by the URL should not be modified until the method ‘detach’ is called.

NOTE	–	If the resource identified by the URL is modified then the Blob behavior is unspecified.

#### Detach

A method ‘detach’ shall be defined in order not to delete the resource designated by the URL when this Blob is garbaged.

The method signature shall be:

public void detach()

#### HashCode

The java.lang.Object method ‘hashCode’ shall be redefined by returning the byte array length if the Blob owns a byte array as a value; otherwise, the URL hash code shall be returned.

#### Equals

The java.lang.Object method ‘equals’ shall be redefined as follows:

- it shall return TRUE if the following conditions are true:

- the type of the parameter is Blob;

- the Blob parameter has the same byte array as this Blob;

- otherwise it shall return FALSE.

If a Blob is based on a URL then the binary content shall be loaded in order to make a deep comparison, i.e., the method shall check that the binary contents are the same.

#### Finalize

The java.lang.Object method ‘finalize’ shall be redefined.

If the Blob is attached and if the URL protocol is ‘file’ then the resource designated by the URL shall be deleted.

#### Create an Element

The method ‘createElement’ defined by the interface Element shall be implemented by calling the Blob empty constructor and returning the result.

#### Encode

The method ‘encode’ defined by the interface Element shall be implemented by encoding this Blob with the method ‘encodeBlob’ provided by the MALEncoder.

#### Decode

The method ‘decode’ defined by the interface Element shall be implemented by decoding a Blob with the method ‘decodeBlob’ provided by the MALDecoder and returning the result.

### Attribute classes

#### Overview

The MAL::Attribute types listed in table 3-49 shall be represented by an Attribute class wrapping a Java type.

Table 3-49:  MAL::Attribute Types Represented by a Specific Class

| MAL::Attribute | Wrapped Java type |
| --- | --- |
| Duration | int |
| Identifier | java.lang.String |
| Time | long |
| URI | java.lang.String |
| FineTime | long |
| UOctet | short |
| UShort | int |
| UInteger | long |
| ULong | java.math.BigInteger |

#### Class Definition

The class <<Attribute>> shall implement the interfaces:

- Attribute

- Comparable< <<Attribute>> >

#### Short Form

The class <<Attribute>> shall declare the constants and implement the methods as specified in section 4.5.5.

#### Empty Constructor

An empty constructor shall be provided.

The constructor signature shall be:

public <<Attribute>>()

The initial value of the MAL::Attribute shall be assigned as specified by table 3-50.

Table 3-50:  Initial Value Assigned by the <<Attribute>> Empty Constructor

| Java type | Default value |
| --- | --- |
| int | 0 |
| java.lang.String | NULL |
| long | 0 |
| short | 0 |
| BigInteger | NULL |

#### Constructor

A constructor taking the Java type as a parameter shall be defined.

The constructor signature shall be:

public <<Attribute>>(<<Java type>> value)

throws java.lang.IllegalArgumentException

If the parameter ‘value’ is NULL then an IllegalArgumentException shall be raised.

#### Get the Value

The method ‘getValue’ shall return the <<Attribute>> value.

The method signature shall be:

public <<Java type>> getValue()

#### HashCode

The java.lang.Object method ‘hashCode’ shall be redefined as follows:

- if the Java type is ‘int’, the value of the <<Attribute>> shall be returned;

- if the Java type is ‘long’, the value of the <<Attribute>> cast as an ‘int’ shall be returned;

- if the Java type is ‘java.lang.String’, the ‘hashCode’ of the String shall be returned.

#### Equals

The java.lang.Object method ‘equals’ shall be redefined as follows:

- it shall return TRUE if the type of the parameter is <<Attribute>> and if its value is equal to the value of this <<Attribute>>;

- otherwise it shall return FALSE.

#### ToString

The java.lang.Object method ‘toString’ shall be redefined by returning the ‘toString’ of the Attribute ‘value’.

#### Create an Element

The method ‘createElement’ defined by the interface Element shall be implemented by calling the empty constructor and returning the result.

#### Encode

The method ‘encode’ defined by the interface Element shall be implemented by calling the method ‘encode<<Attribute>>’ provided by the MALEncoder.

#### Decode

The method ‘decode’ defined by the interface Element shall be implemented by calling the method ‘decode<<Attribute>>’ provided by the MALDecoder and returning the result.

#### Compare

The method ‘compare’ defined by the interface Comparable shall be implemented by calling the method ‘compare’ provided by the Attribute ‘value’. If the ‘value’ type is primitive then the method ‘compare’ provided by the Java wrapper class shall be called.

### ElementList

An ElementList interface shall be defined in order to represent a list of MAL::Element.

The ElementList shall declare a generic type variable ‘T’.

NOTE	–	No type constraint can be defined because of MAL::Attribute types mapped to non-Element Java classes.

The ElementList interface shall extend the following interfaces:

- Composite;

- java.util.List<T>.

NOTE	–	This interface defines no method; it is a marker interface.

### AttributeList

An AttributeList interface shall be defined in order to represent a list of MAL::Attribute.

The AttributeList shall declare a generic type variable ‘T’.

NOTE	–	No type constraint can be defined because of MAL::Attribute types mapped to non-Element Java classes.

The AttributeList interface shall extend the ElementList<T> interface.

NOTE	–	This interface defines no method; it is a marker interface.

### CompositeList

A CompositeList interface shall be defined in order to represent a list of MAL::Composite.

The CompositeList shall declare a generic type variable ‘T’ with the constraint ‘T extends Composite’.

The CompositeList interface shall extend the ElementList<T> interface.

NOTE	–	This interface defines no method; it is a marker interface.

## Consumer package

### Overview

This part of the API is dedicated to the MAL clients initiating interactions as service consumers. The consumer state diagrams are specified in reference [1].

The classes and interfaces belong to the Java package:

org.ccsds.moims.mo.mal.consumer

### MALConsumerManager

#### Definition

A MALConsumerManager interface shall be defined in order to encapsulate the resources used to enable a MAL consumer to initiate interactions.

A MALConsumerManager shall be a MALConsumer factory.

#### MALConsumerManager Creation

A MALConsumerManager shall be created by calling the method ‘createConsumerManager’ provided by a MALContext.

Several consumers should be created in order to separate the resources used by the clients.

#### Create a Consumer

Two methods ‘createConsumer’ shall be defined in order to create a MALConsumer:

- using a private MALEndpoint;

- using a shared MALEndpoint.

The method signatures shall be:

public MALConsumer createConsumer(

String localName,

URI uriTo,

URI brokerUri,

MALService service,

Blob authenticationId,

IdentifierList domain,

Identifier networkZone,

SessionType sessionType,

Identifier sessionName,

QoSLevel qosLevel,

java.util.Map qosProps,

UInteger priority)

throws java.lang.IllegalArgumentException, MALException;

public MALConsumer createConsumer(

MALEndpoint endpoint,

URI uriTo,

URI brokerUri,

MALService service,

Blob authenticationId,

IdentifierList domain,

Identifier networkZone,

SessionType sessionType,

Identifier sessionName,

QoSLevel qosLevel,

java.util.Map qosProps,

UInteger priority)

throws java.lang.IllegalArgumentException, MALException;

The ‘createConsumer’ parameters shall be assigned as described in table 3-51.

Table 3-51:  MALConsumerManager ‘createConsumer’ Parameters

| Parameter | Description |
| --- | --- |
| localName | Name of the private MALEndpoint to be created and used by the consumer |
| endpoint | Shared MALEndpoint to be used by the consumer |
| uriTo | URI of the service provider the consumer will interact with |
| brokerUri | URI of the broker used by the service provider to publish updates |
| service | Definition of the consumed service |
| authenticationId | Authentication identifier used by the consumer during all the interactions with the service provider |
| domain | Domain the service provider belongs to |
| networkZone | Network zone the provider belongs to |
| sessionType | Session type of the service |
| sessionName | Name of the session |
| qosLevel | QoS level required by the consumer for all the interactions with the provider |
| qosProps | QoS properties that are needed to configure the QoS level |
| priority | Message priority required by the consumer for all the interactions with the provider |

The parameter ‘localName’ may be NULL.

If the parameter ‘localName’ is not NULL then its value shall be unique for the MALContext instance and the protocol specified by the URI ‘uriTo’.

The protocol of the URI ‘brokerUri’ shall be the same as the protocol of the URI ‘uriTo’.

The parameter ‘qosProps’ may be NULL.

If the parameters ‘endpoint’ or ‘uriTo’ or ‘brokerUri’ or ‘service’ or ‘authenticationId’ or ‘domain’ or ‘networkZone’ or ‘sessionType’ or ‘sessionName’ or ‘qosLevel’ or ‘priority’ are NULL then an IllegalArgumentException shall be raised.

The method ‘createConsumer’ shall not return the value NULL.

The creation of a MALConsumer, whatever the QoS level is, shall not raise a MALException if the service provider is not active.

If the MALConsumerManager is closed then a MALException shall be raised.

If the consumer local name is not NULL and if the consumer process starts again after a stop and creates the MALConsumer with the same local name (directly or through a shared MALEndpoint) then the MALConsumer shall recover the same URI as before the stop.

#### QoS Properties

The QoS properties given in table 3-52 shall be available.

Table 3-52:  QoS Properties

| Property name | Type | Description |
| --- | --- | --- |
| timeToLive | Integer | This is the time in milliseconds allowed by the consumer for delivering the messages to the provider. If the message cannot be delivered before then it is dropped and the MAL standard error DELIVERY_TIMEDOUT is returned to the MALConsumer if the interaction pattern allows it. |

#### Close

A method ‘close’ shall be defined in order to release the resources owned by a MALConsumerManager.

The method signature shall be:

public void close() throws MALException

The method ‘close’ shall close all the MALConsumer instances that are owned by this MALConsumerManager.

The method ‘close’ shall return after all the MALConsumer instances have been closed.

If an internal error occurs then a MALException shall be raised.

### MALConsumer

#### Definition

A MALConsumer interface shall be defined in order to provide a communication context that initiates interaction patterns either in a synchronous or asynchronous way.

The resources used by each MALConsumer should be shared as long as it is possible for the implementation to do it.

The MAL message body elements shall be represented using the type ‘java.lang.Object’.

The allowed body element types shall be:

- MAL element types;

- MALEncodedElement;

- Java types defined by a specific Java mapping extension.

#### MALConsumer Creation

A MALConsumer shall be created by calling the method ‘createConsumer’ provided by a MALConsumerManager.

NOTE	–	A correct usage of the MALConsumer is to create one for each service provider a MAL consumer wants to interact with. Typically a MALConsumer is created for each service stub.

#### Get the URI

A getter method shall be defined in order to return the consumer URI.

The method signature shall be:

public URI getURI()

#### Synchronous SEND IP Initiation

A method ‘send’ shall be defined in order to initiate a synchronous SEND interaction.

The method ‘send’ signature shall be:

public MALMessage send(MALSendOperation op, Object... body)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

The method ‘send’ parameters shall be assigned as described in table 3-53.

Table 3-53:  MALConsumer ‘send’ Parameters

| Parameter | Description |
| --- | --- |
| op | SEND operation to initiate |
| body | Body elements to transmit in the initiation message |

If the parameter ‘op’ is NULL then an IllegalArgumentException shall be raised.

The parameter ‘body’ may be empty.

The method ‘send’ shall return as soon as the initiation message has been sent.

The method shall return the MALMessage that has been sent.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if a non-MAL error occurs during the initiation message sending.

If the MALConsumer is closed then a MALException shall be raised.

#### Synchronous SUBMIT IP Initiation

A method ‘submit’ shall be defined in order to initiate a synchronous SUBMIT interaction.

The method ‘submit’ signature shall be:

public void submit(MALSubmitOperation op, Object... body)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

The method ‘submit’ parameters shall be assigned as described in table 3-54.

Table 3-54:  MALConsumer ‘submit’ Parameters

| Parameter | Description |
| --- | --- |
| op | SUBMIT operation to initiate |
| body | Body elements to transmit in the initiation message |

If the parameter ‘op’ is NULL then an IllegalArgumentException shall be raised.

The parameter ‘body’ may be empty.

The method ‘submit’ shall return as soon as the ACK message has been received.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if a non-MAL error occurs during the initiation message sending.

A MALInteractionException shall be thrown if an ACK ERROR occurs. The ACK ERROR message body shall be passed as the parameter ‘standardError’ of the MALException constructor.

If the MALConsumer is closed then a MALException shall be raised.

#### Synchronous REQUEST IP Initiation

A method ‘request’ shall be defined in order to initiate a synchronous REQUEST interaction.

The method ‘request’ signature shall be:

public MALMessageBody request(MALRequestOperation op, Object... body)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

The method ‘request’ parameters shall be assigned as described in table 3-55.

Table 3-55:  MALConsumer ‘request’ Parameters

| Parameter | Description |
| --- | --- |
| op | REQUEST operation to initiate |
| body | Body elements to transmit in the initiation message |

If the parameter ‘op’ is NULL then an IllegalArgumentException shall be raised.

The parameter ‘body’ may be empty.

The method ‘request’ shall return as soon as the RESPONSE message has been received.

The RESPONSE message body shall be returned as the method result.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if a non-MAL error occurs during the initiation message sending.

A MALInteractionException shall be thrown if a RESPONSE ERROR occurs. The RESPONSE ERROR message body shall be passed as the parameter ‘standardError’ of the MALInteractionException constructor.

If the MALConsumer is closed then a MALException shall be raised.

#### Synchronous INVOKE IP Initiation

A method ‘invoke’ shall be defined in order to initiate an INVOKE interaction.

The method ‘invoke’ signature shall be:

public MALMessageBody invoke(MALInvokeOperation op,

MALInteractionListener listener, Object... body)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

The method ‘invoke’ parameters shall be assigned as described in table 3-56.

Table 3-56:  MALConsumer ‘invoke’ Parameters

| Parameter | Description |
| --- | --- |
| op | INVOKE operation to initiate |
| listener | Listener in charge of receiving the messages RESPONSE and RESPONSE ERROR |
| body | Body elements to transmit in the initiation message |

If the parameter ‘op’ is NULL then an IllegalArgumentException shall be raised.

The parameter ‘body’ may be empty.

The method ‘invoke’ shall return as soon as the ACK message has been received.

The ACK message body shall be returned as the method result.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if an error occurs during the initiation message sending.

A MALInteractionException shall be thrown if an ACK ERROR occurs. The ACK ERROR message body shall be passed as the parameter ‘standardError’ of the MALInteractionException constructor.

If the MALConsumer is closed then a MALException shall be raised.

The method ‘invokeResponseReceived’ provided by the parameter ‘listener’ shall be called as soon as the RESPONSE message has been delivered.

The method ‘invokeResponseErrorReceived’ provided by the parameter ‘listener’ shall be called if a RESPONSE ERROR occurs.

#### Synchronous PROGRESS IP Initiation

A method ‘progress’ shall be defined in order to initiate a PROGRESS interaction.

The method ‘progress’ signature shall be:

public MALMessageBody progress(MALProgressOperation op,

MALInteractionListener listener, Object... body)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

The method ‘progress’ parameters shall be assigned as described in table 3-57.

Table 3-57:  MALConsumer ‘progress’ Parameters

| Parameter | Description |
| --- | --- |
| op | PROGRESS operation to initiate |
| listener | Listener in charge of receiving the messages UPDATE, UPDATE ERROR, RESPONSE and RESPONSE ERROR |
| body | Body elements to transmit in the initiation message |

If the parameter ‘op’ is NULL then an IllegalArgumentException shall be raised.

The parameter ‘body’ may be empty.

The method ‘progress’ shall return as soon as the ACK message has been received.

The ACK message body shall be returned as the method result.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if an error occurs during the initiation message sending.

A MALInteractionException shall be thrown if an ACK ERROR occurs. The ACK ERROR message body shall be passed as the parameter ‘standardError’ of the MALInteractionException constructor.

If the MALConsumer is closed then a MALException shall be raised.

The method ‘progressUpdateReceived’ provided by the parameter ‘listener’ shall be called as soon as an UPDATE message has been delivered.

The method ‘progressUpdateErrorReceived’ provided by the parameter ‘listener’ shall be called if an UPDATE ERROR occurs.

The method ‘progressResponseReceived’ provided by the parameter ‘listener’ shall be called as soon as the RESPONSE message has been delivered.

The method ‘progressErrorReceived’ provided by the parameter ‘listener’ shall be called if a RESPONSE ERROR occurs.

#### Synchronous PUBLISH-SUBSCRIBE IP REGISTER Initiation

A method ‘register’ shall be defined in order to initiate a synchronous PUBLISH-SUBSCRIBE REGISTER interaction.

The method ‘register’ signature shall be:

public void register(MALPubSubOperation op, Subscription subscription,

MALInteractionListener listener)

throws java.lang.IllegalArgumentException,

MALException, MALInteractionException

The method ‘register’ parameters shall be assigned as described in table 3-58.

Table 3-58:  MALConsumer ‘register’ Parameters

| Parameter | Description |
| --- | --- |
| op | PUBLISH-SUBSCRIBE operation which REGISTER stage is to initiate |
| subscription | Subscription to be registered |
| listener | Listener in charge of receiving the messages NOTIFY and NOTIFY ERROR. |

If the parameters ‘op’ or ‘subscription’ or ‘listener’ are NULL then an IllegalArgumentException shall be raised.

The method ‘register’ shall return as soon as the REGISTER ACK message has been received.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if an error occurs during the initiation message sending.

A MALInteractionException shall be thrown if a REGISTER ERROR occurs. The REGISTER ERROR message body shall be passed as the parameter ‘standardError’ of the MALInteractionException constructor.

If the MALConsumer is closed then a MALException shall be raised.

The method ‘notifyReceived’ provided by the parameter ‘listener’ shall be called as soon as a NOTIFY message has been delivered.

The method ‘notifyErrorReceived’ provided by the parameter ‘listener’ shall be called as soon as a NOTIFY ERROR message has been delivered.

If a call to ‘register’ is initiated while the consumer is already registered but with a different parameter ‘listener’ then only the second registered ‘listener’ shall receive the NOTIFY and NOTIFY ERROR messages.

#### Synchronous PUBLISH-SUBSCRIBE IP DEREGISTER Initiation

A method ‘deregister’ shall be defined in order to initiate a synchronous PUBLISH-SUBSCRIBE DEREGISTER interaction.

The method ‘deregister’ signature shall be:

public void deregister(MALPubSubOperation op,

IdentifierList subscriptionIdList)

throws java.lang.IllegalArgumentException,

MALException, MALInteractionException

The method ‘deregister’ parameters shall be assigned as described in table 3-59.

Table 3-59:  MALConsumer ‘deregister’ Parameters

| Parameter | Description |
| --- | --- |
| op | PUBLISH-SUBSCRIBE operation which DEREGISTER stage is to initiate |
| subscriptionIdList | List of the subscription identifiers to deregister |

If the parameters ‘op’ or ‘subscriptionIdList’ are NULL then an IllegalArgumentException shall be raised.

The method ‘deregister’ shall return as soon as the DEREGISTER ACK message has been received.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if an error occurs during the initiation message sending.

If the MALConsumer is closed then a MALException shall be raised.

#### Asynchronous SUBMIT IP Initiation

A method ‘asyncSubmit’ shall be defined in order to initiate an asynchronous SUBMIT interaction.

The method ‘asyncSubmit’ signature shall be:

public MALMessage asyncSubmit(MALSubmitOperation op,

MALInteractionListener listener, Object... body)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

The method ‘asyncSubmit’ parameters shall be assigned as described in table 3-60.

Table 3-60:  MALConsumer ‘asyncSubmit’ Parameters

| Parameter | Description |
| --- | --- |
| op | SUBMIT operation to initiate |
| listener | Listener in charge of receiving the messages ACK and ACK ERROR |
| body | Body elements to transmit in the initiation message |

If the parameters ‘op’ or ‘listener’ are NULL then an IllegalArgumentException shall be raised.

The parameter ‘body’ may be empty.

The method ‘asyncSubmit’ shall return as soon as the initiation message has been sent.

The method shall return the MALMessage that has been sent.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if an error occurs during the initiation message sending.

If the MALConsumer is closed then a MALException shall be raised.

The method ‘submitAckReceived’ provided by the parameter ‘listener’ shall be called as soon as the ACK message has been delivered.

The method ‘submitErrorReceived’ provided by the parameter ‘listener’ shall be called if an ACK ERROR occurs.

#### Asynchronous REQUEST IP Initiation

A method ‘asyncRequest’ shall be defined in order to initiate an asynchronous REQUEST interaction.

The method ‘asyncRequest’ signature shall be:

public MALMessage asyncRequest(MALRequestOperation op,

MALInteractionListener listener, Object... body)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

The method ‘asyncRequest’ parameters shall be assigned as described in table 3-61.

Table 3-61:  MALConsumer ‘asyncRequest’ Parameters

| Parameter | Description |
| --- | --- |
| op | REQUEST operation to initiate |
| listener | Listener in charge of receiving the messages RESPONSE and RESPONSE ERROR |
| body | Body elements to transmit in the initiation message |

If the parameters ‘op’ or ‘listener’ are NULL then an IllegalArgumentException shall be raised.

The parameter ‘body’ may be empty.

The method ‘asyncRequest’ shall return as soon as the initiation message has been sent.

The method shall return the MALMessage that has been sent.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if an error occurs during the initiation message sending.

If the MALConsumer is closed then a MALException shall be raised.

The method ‘requestResponseReceived’ provided by the parameter ‘listener’ shall be called as soon as the RESPONSE message has been delivered.

The method ‘requestErrorReceived’ provided by the parameter ‘listener’ shall be called if an RESPONSE ERROR occurs.

#### Asynchronous INVOKE IP Initiation

A method ‘asyncInvoke’ shall be defined in order to initiate an asynchronous INVOKE interaction.

The method ‘asyncInvoke’ signature shall be:

public MALMessage asyncInvoke(MALInvokeOperation op,

MALInteractionListener listener, Object... body)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

The method ‘asyncInvoke’ parameters shall be assigned as described in table 3-62.

Table 3-62:  MALConsumer ‘asyncInvoke’ Parameters

| Parameter | Description |
| --- | --- |
| op | INVOKE operation to initiate |
| listener | Listener in charge of receiving the messages ACK, ACK ERROR, RESPONSE and RESPONSE ERROR |
| body | Body elements to transmit in the initiation message |

If the parameters ‘op’ or ‘listener’ are NULL then an IllegalArgumentException shall be raised.

The parameter ‘body’ may be empty.

The method ‘asyncInvoke’ shall return as soon as the initiation message has been sent.

The method shall return the MALMessage that has been sent.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if an error occurs during the initiation message sending.

If the MALConsumer is closed then a MALException shall be raised.

The method ‘invokeAckReceived’ provided by the parameter ‘listener’ shall be called as soon as the ACK message has been delivered.

The method ‘invokeAckErrorReceived’ provided by the parameter ‘listener’ shall be called if an ACK ERROR occurs.

The method ‘invokeResponseReceived’ provided by the parameter ‘listener’ shall be called as soon as the RESPONSE message has been delivered.

The method ‘invokeResponseErrorReceived’ provided by the parameter ‘listener’ shall be called if a RESPONSE ERROR occurs.

#### Asynchronous PROGRESS IP Initiation

A method ‘asyncProgress’ shall be defined in order to initiate an asynchronous PROGRESS interaction.

The method ‘asyncProgress’ signature shall be:

public MALMessage asyncProgress(MALProgressOperation op,

MALInteractionListener listener, Object... body)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

The method ‘asyncProgress’ parameters shall be assigned as described in table 3-63.

Table 3-63:  MALConsumer ‘asyncProgress’ Parameters

| Parameter | Description |
| --- | --- |
| op | PROGRESS operation to initiate |
| listener | Listener in charge of receiving the messages ACK, ACK ERROR, UPDATE, UPDATE ERROR, RESPONSE and RESPONSE ERROR |
| body | Body elements to transmit in the initiation message |

If the parameters ‘op’ or ‘listener’ are NULL then an IllegalArgumentException shall be raised.

The parameter ‘body’ may be empty.

The method ‘asyncProgress’ shall return as soon as the initiation message has been sent.

The method shall return the MALMessage that has been sent.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if an error occurs during the initiation message sending.

If the MALConsumer is closed then a MALException shall be raised.

The method ‘progressAckReceived’ provided by the parameter ‘listener’ shall be called as soon as the ACK message has been delivered.

The method ‘progressAckErrorReceived’ provided by the parameter ‘listener’ shall be called if an ACK ERROR occurs.

The method ‘progressUpdateReceived’ provided by the parameter ‘listener’ shall be called as soon as an UPDATE message has been delivered.

The method ‘progressUpdateErrorReceived’ provided by the parameter ‘listener’ shall be called if an UPDATE ERROR occurs.

The method ‘progressResponseReceived’ provided by the parameter ‘listener’ shall be called as soon as the RESPONSE message has been delivered.

The method ‘progressResponseErrorReceived’ provided by the parameter ‘listener’ shall be called if a RESPONSE ERROR occurs.

#### Asynchronous PUBLISH-SUBSCRIBE IP REGISTER Initiation

A method ‘asyncRegister’ shall be defined in order to initiate an asynchronous PUBLISH-SUBSCRIBE REGISTER interaction.

The method ‘asyncRegister’ signature shall be:

public MALMessage asyncRegister(MALPubSubOperation op,

Subscription subscription, MALInteractionListener listener)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

The method ‘asyncRegister’ parameters shall be assigned as described in table 3-64.

Table 3-64:  MALConsumer ‘asyncRegister’ Parameters

| Parameter | Description |
| --- | --- |
| op | PUBLISH-SUBSCRIBE operation which REGISTER stage is to initiate |
| subscription | Subscription to be registered |
| listener | Listener in charge of receiving the messages REGISTER ACK, REGISTER ERROR, NOTIFY and NOTIFY ERROR |

If the parameters ‘op’ or ‘subscriptionIdList’ or ‘listener’ are NULL then an IllegalArgumentException shall be raised.

The method ‘asyncRegister’ shall return as soon as the initiation message has been sent.

The method shall return the MALMessage that has been sent.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if an error occurs during the initiation message sending.

If the MALConsumer is closed then a MALException shall be raised.

The method ‘registerAckReceived’ provided by the parameter ‘listener’ shall be called as soon as the REGISTER ACK message has been delivered.

The method ‘registerAckErrorReceived’ provided by the parameter ‘listener’ shall be called if an REGISTER ERROR occurs.

The method ‘notifyReceived’ provided by the parameter ‘listener’ shall be called as soon as a NOTIFY message has been delivered.

The method ‘notifyErrorReceived’ provided by the parameter ‘listener’ shall be called as soon as a NOTIFY ERROR message has been delivered.

If a call to ‘asyncRegister’ is initiated while the consumer is already registered but with a different parameter ‘listener’ then only the second registered ‘listener’ shall receive the NOTIFY and NOTIFY ERROR messages.

#### Asynchronous PUBLISH-SUBSCRIBE IP DEREGISTER Initiation

A method ‘asyncDeregister’ shall be defined in order to initiate an asynchronous PUBLISH-SUBSCRIBE DEREGISTER interaction.

The method ‘asyncDeregister’ signature shall be:

public MALMessage asyncDeregister(MALPubSubOperation op,

IdentifierList subscriptionIdList, MALInteractionListener listener)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

The method ‘asyncDeregister’ parameters shall be assigned as described in table 3-65.

Table 3-65:  MALConsumer ‘asyncDeregister’ Parameters

| Parameter | Description |
| --- | --- |
| op | PUBLISH-SUBSCRIBE operation which DEREGISTER stage is to initiate |
| subscriptionIdList | List of the subscription identifiers to deregister |
| listener | Listener in charge of receiving the messages DEREGISTER ACK, DEREGISTER ERROR |

If the parameters ‘op’ or ‘subscriptionIdList’ or ‘listener’ are NULL then an IllegalArgumentException shall be raised.

The method ‘asyncDeregister’ shall return as soon as the initiation message has been sent.

The method shall return the MALMessage that has been sent.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if an error occurs during the initiation message sending.

If the MALConsumer is closed then a MALException shall be raised.

The method ‘deregisterAckReceived’ provided by the parameter ‘listener’ shall be called as soon as the DEREGISTER ACK message has been delivered.

#### Continue an Interaction

A method ‘continueInteraction’ shall be defined in order to continue an interaction that has been interrupted.

The method signature shall be:

public void continueInteraction(

MALOperation op,

UOctet lastInteractionStage,

Time initiationTimestamp,

Long transactionId,

MALInteractionListener listener)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

The method ‘continueInteraction’ parameters shall be assigned as described in table 3-65.

Table 3-66:  MALConsumer ‘continueInteraction’ Parameters

| Parameter | Description |
| --- | --- |
| op | The operation to continue |
| lastInteractionStage | The last stage of the interaction to continue |
| initiationTimestamp | Timestamp of the interaction initiation message |
| transactionId | Transaction identifier of the interaction to continue |
| listener | Listener in charge of receiving the messages from the service provider |

If the parameters ‘operationNumber’ or ‘lastInteractionStage’ or ‘initiationTimestamp’ or ‘transactionId ‘ or ‘listener’ are NULL then an IllegalArgumentException shall be raised.

A MALInteractionException shall be thrown if a MAL standard error occurs.

A MALException shall be thrown if a non-MAL error occurs.

If the MALConsumer is closed then a MALException shall be raised.

#### Close

A method ‘close’ shall be defined in order to terminate all pending interaction patterns initiated by the MALConsumer.

The method signature shall be:

public void close() throws MALException

The synchronous IP initiation methods shall return with a response or a raised MALException depending on whether or not there was a message available at the time of the close.

All the MALInteractionListeners that were running at the time of the close shall have returned before the method ‘close’ returns.

If the consumer owns a private MALEndpoint then the method ‘close’ provided by the MALEndpoint shall be called.

If an internal error occurs then a MALException shall be raised.

If a provider or a broker try to interact with a closed consumer and if the QoS level is QUEUED then the message shall be queued and delivered as soon as the consumer message delivery is started again.

### MALInteractionListener

#### Definition

A MALInteractionListener interface shall be defined in order to enable a consumer to asynchronously receive a message.

#### Receive a SUBMIT ACK Message

A method ‘submitAckReceived’ shall be defined in order to receive the ACK message defined by the IP SUBMIT.

The method ‘submitAckReceived’ signature shall be:

public void submitAckReceived(MALMessageHeader header,

Map qosProperties) throws MALException

The method ‘submitAckReceived’ parameters shall be assigned as described in table 3-67.

Table 3-67:  MALInteractionListener ‘submitAckReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the ACK message |
| qosProperties | QoS properties of the ACK message |

The parameter ‘header’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

#### Receive a SUBMIT ERROR Message

A method ‘submitErrorReceived’ shall be defined in order to receive the ERROR message defined by the IP SUBMIT.

The method ‘submitErrorReceived’ signature shall be:

public void submitErrorReceived(MALMessageHeader header,

MALErrorBody body, Map qosProperties)

throws MALException

The method ‘submitErrorReceived’ parameters shall be assigned as described in table 3-67.

Table 3-68:  MALInteractionListener ‘submitErrorReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the ERROR message |
| body | Body of the ERROR message |
| qosProperties | QoS properties of the ERROR message |

The parameters ‘header’ and ‘body’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

#### Receive a REQUEST RESPONSE Message

A method ‘requestResponseReceived’ shall be defined in order to receive the RESPONSE message defined by the IP REQUEST.

The method ‘requestResponseReceived’ signature shall be:

public void requestResponseReceived(MALMessageHeader header,

MALMessageBody body, Map qosProperties) throws MALException

The method ‘requestResponseReceived’ parameters shall be assigned as described in table 3-69.

Table 3-69:  MALInteractionListener ‘requestResponseReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the RESPONSE message |
| body | Body of the RESPONSE message |
| qosProperties | QoS properties of the RESPONSE message |

The parameter ‘header’ shall not be NULL.

The parameters ‘body’ and ‘qosProperties’ may be NULL.

If the RESPONSE message is empty then the parameter ‘body’ shall be NULL.

#### Receive a REQUEST ERROR Message

A method ‘requestErrorReceived’ shall be defined in order to receive the ERROR message defined by the IP REQUEST.

The method ‘requestErrorReceived’ signature shall be:

public void requestErrorReceived(MALMessageHeader header,

MALErrorBody body, Map qosProperties)

throws MALException

The method ‘requestErrorReceived’ parameters shall be assigned as described in table 3-67.

Table 3-70:  MALInteractionListener ‘requestErrorReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the ERROR message |
| body | Body of the ERROR message |
| qosProperties | QoS properties of the ERROR message |

The parameters ‘header’ and ‘body’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

#### Receive an INVOKE ACK Message

A method ‘invokeAckReceived’ shall be defined in order to receive the ACK message defined by the IP INVOKE.

The method ‘invokeAckReceived’ signature shall be:

public void invokeAckReceived(MALMessageHeader header,

MALMessageBody body, Map qosProperties)

throws MALException

The method ‘invokeAckReceived’ parameters shall be assigned as described in table 3-67.

Table 3-71:  MALInteractionListener ‘invokeAckReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the ACK message |
| body | Body of the ACK message |
| qosProperties | QoS properties of the ACK message |

The parameter ‘header’ shall not be NULL.

The parameters ‘body’ and ‘qosProperties’ may be NULL.

If the ACK message is empty then the parameter ‘body’ shall be NULL.

If an error occurs then a MALException may be raised.

#### Receive an INVOKE ACK ERROR Message

A method ‘invokeAckErrorReceived’ shall be defined in order to receive the ACK ERROR message defined by the IP INVOKE.

The method ‘invokeAckErrorReceived’ signature shall be:

public void invokeAckErrorReceived(MALMessageHeader header,

MALErrorBody body, Map qosProperties)

throws MALException

The method ‘invokeAckErrorReceived’ parameters shall be assigned as described in table 3-67.

Table 3-72:  MALInteractionListener ‘invokeAckErrorReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the ACK ERROR message |
| body | Body of the ACK ERROR message |
| qosProperties | QoS properties of the ACK ERROR message |

The parameters ‘header’ and ‘body’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

#### Receive an INVOKE RESPONSE Message

A method ‘invokeResponseReceived’ shall be defined in order to receive the RESPONSE message defined by the IP INVOKE.

The method ‘invokeResponseReceived’ signature shall be:

public void invokeResponseReceived(MALMessageHeader header,

MALMessageBody body, Map qosProperties) throws MALException

The method ‘invokeResponseReceived’ parameters shall be assigned as described in table 3-69.

Table 3-73:  MALInteractionListener ‘invokeResponseReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the RESPONSE message |
| body | Body of the RESPONSE message |
| qosProperties | QoS properties of the RESPONSE message |

The parameter ‘header’ shall not be NULL.

The parameters ‘body’ and ‘qosProperties’ may be NULL.

If the RESPONSE message is empty then the parameter ‘body’ shall be NULL.

If an error occurs then a MALException may be raised.

#### Receive an INVOKE RESPONSE ERROR Message

A method ‘invokeResponseErrorReceived’ shall be defined in order to receive the RESPONSE ERROR message defined by the IP INVOKE.

The method ‘invokeResponseErrorReceived’ signature shall be:

public void invokeResponseErrorReceived(MALMessageHeader header,

MALErrorBody body, Map qosProperties)

throws MALException

The method ‘invokeResponseErrorReceived’ parameters shall be assigned as described in table 3-67.

Table 3-74:  MALInteractionListener ‘invokeResponseErrorReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the RESPONSE ERROR message |
| body | Body of the RESPONSE ERROR message |
| qosProperties | QoS properties of the RESPONSE ERROR message |

The parameters ‘header’ and ‘body’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

#### Receive a PROGRESS ACK Message

A method ‘progressAckReceived’ shall be defined in order to receive the ACK message defined by the IP PROGRESS.

The method ‘progressAckReceived’ signature shall be:

public void progressAckReceived(MALMessageHeader header,

MALMessageBody body, Map qosProperties)

throws MALException

The method ‘progressAckReceived’ parameters shall be assigned as described in table 3-67.

Table 3-75:  MALInteractionListener ‘progressAckReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the ACK message |
| body | Body of the ACK message |
| qosProperties | QoS properties of the ACK message |

The parameter ‘header’ shall not be NULL.

The parameters ‘body’ and ‘qosProperties’ may be NULL.

If the ACK message is empty then the parameter ‘body’ shall be NULL.

If an error occurs then a MALException may be raised.

#### Receive a PROGRESS ACK ERROR Message

A method ‘progressAckErrorReceived’ shall be defined in order to receive the ACK ERROR message defined by the IP PROGRESS.

The method ‘progressAckErrorReceived’ signature shall be:

public void progressAckErrorReceived(MALMessageHeader header,

MALErrorBody body, Map qosProperties)

throws MALException

The method ‘progressAckErrorReceived’ parameters shall be assigned as described in table 3-67.

Table 3-76:  MALInteractionListener ‘progressAckErrorReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the ACK ERROR message |
| body | Body of the ACK ERROR message |
| qosProperties | QoS properties of the ACK ERROR message |

The parameters ‘header’ and ‘body’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

#### Receive a PROGRESS UPDATE Message

A method ‘updateReceived’ shall be defined in order to receive the UPDATE message defined by the IP PROGRESS.

The method ‘progressUpdateReceived’ signature shall be:

public void progressUpdateReceived(MALMessageHeader header,

MALMessageBody body, Map qosProperties) throws MALException

The method ‘progressUpdateReceived’ parameters shall be assigned as described in table 3-77.

Table 3-77:  MALInteractionListener ‘progressUpdateReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the UPDATE message |
| body | Body of the UPDATE message |
| qosProperties | QoS properties of the UPDATE message |

The parameter ‘header’ shall not be NULL.

The parameters ‘body’ and ‘qosProperties’ may be NULL.

If the UDPATE message is empty then the parameter ‘body’ shall be NULL.

If an error occurs then a MALException may be raised.

#### Receive a PROGRESS UPDATE ERROR Message

A method ‘progressUpdateErrorReceived’ shall be defined in order to receive the UPDATE ERROR message defined by the IP PROGRESS.

The method ‘progressUpdateErrorReceived’ signature shall be:

public void progressUpdateErrorReceived(MALMessageHeader header,

MALErrorBody body, Map qosProperties)

throws MALException

The method ‘progressUpdateErrorReceived’ parameters shall be assigned as described in table 3-67.

Table 3-78:  MALInteractionListener ‘progressUpdateErrorReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the UPDATE ERROR message |
| body | Body of the UPDATE ERROR message |
| qosProperties | QoS properties of the UPDATE ERROR message |

The parameters ‘header’ and ‘body’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

#### Receive a PROGRESS RESPONSE Message

A method ‘progressResponseReceived’ shall be defined in order to receive the RESPONSE message defined by the IP PROGRESS.

The method ‘progressResponseReceived’ signature shall be:

public void progressResponseReceived(MALMessageHeader header,

MALMessageBody body, Map qosProperties) throws MALException

The method ‘progressResponseReceived’ parameters shall be assigned as described in table 3-69.

Table 3-79:  MALInteractionListener ‘progressResponseReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the RESPONSE message |
| body | Body of the RESPONSE message |
| qosProperties | QoS properties of the RESPONSE message |

The parameter ‘header’ shall not be NULL.

The parameters ‘body’ and ‘qosProperties’ may be NULL.

If the RESPONSE message is empty then the parameter ‘body’ shall be NULL.

If an error occurs then a MALException may be raised.

#### Receive a PROGRESS RESPONSE ERROR Message

A method ‘progressResponseErrorReceived’ shall be defined in order to receive the RESPONSE ERROR message defined by the IP PROGRESS.

The method ‘progressResponseErrorReceived’ signature shall be:

public void progressResponseErrorReceived(MALMessageHeader header,

MALErrorBody body, Map qosProperties)

throws MALException

The method ‘progressResponseErrorReceived’ parameters shall be assigned as described in table 3-67.

Table 3-80:  MALInteractionListener ‘progressResponseErrorReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the RESPONSE ERROR message |
| body | Body of the RESPONSE ERROR message |
| qosProperties | QoS properties of the RESPONSE ERROR message |

The parameters ‘header’ and ‘body’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

#### Receive a REGISTER ACK Message

A method ‘registerAckReceived’ shall be defined in order to receive the REGISTER ACK message defined by the IP PUBLISH-SUBSCRIBE.

The method ‘registerAckReceived’ signature shall be:

public void registerAckReceived(MALMessageHeader header,

Map qosProperties)

throws MALException

The method ‘registerAckReceived’ parameters shall be assigned as described in table 3-67.

Table 3-81:  MALInteractionListener ‘registerAckReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the REGISTER ACK message |
| qosProperties | QoS properties of the REGISTER ACK message |

The parameter ‘header’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

#### Receive a REGISTER ERROR Message

A method ‘registerErrorReceived’ shall be defined in order to receive the REGISTER ERROR message defined by the IP PUBLISH-SUBSCRIBE.

The method ‘registerErrorReceived’ signature shall be:

public void registerErrorReceived(MALMessageHeader header,

MALErrorBody body, Map qosProperties)

throws MALException

The method ‘registerErrorReceived’ parameters shall be assigned as described in table 3-67.

Table 3-82:  MALInteractionListener ‘registerErrorReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the REGISTER ERROR message |
| body | Body of the REGISTER ERROR message |
| qosProperties | QoS properties of the REGISTER ERROR message |

The parameters ‘header’ and ‘body’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

#### Receive a NOTIFY Message

A method ‘notifyReceived’ shall be defined in order to receive the NOTIFY message defined by the IP PUBLISH-SUBSCRIBE.

The method ‘notifyReceived’ signature shall be:

public void notifyReceived(MALMessageHeader header,

MALNotifyBody body, Map qosProperties)

throws MALException

The method ‘notifyReceived’ parameters shall be assigned as described in table 3-83.

Table 3-83:  MALInteractionListener ‘notifyReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the NOTIFY message |
| body | Body of the NOTIFY message |
| qosProperties | QoS properties of the REGISTER ERROR message |

The parameters ‘header’ and ‘body’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

#### Receive a NOTIFY ERROR message

A method ‘notifyErrorReceived’ shall be defined in order to receive the NOTIFY ERROR message defined by the IP PUBLISH-SUBSCRIBE.

The method ‘notifyErrorReceived’ signature shall be:

public void notifyErrorReceived(MALMessageHeader header,

MALErrorBody body, Map qosProperties)

throws MALException

The method ‘notifyErrorReceived’ parameters shall be assigned as described in table 3-67.

Table 3-84:  MALInteractionListener ‘notifyErrorReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the UPDATE ERROR message |
| body | Body of the REGISTER ERROR message |
| qosProperties | QoS properties of the UPDATE ERROR message |

The parameters ‘header’ and ‘body’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

#### Receive a DEREGISTER ACK message

A method ‘deregisterAckReceived’ shall be defined in order to receive the DEREGISTER ACK message defined by the IP PUBLISH-SUBSCRIBE.

The method ‘deregisterAckReceived’ signature shall be:

public void deregisterAckReceived(MALMessageHeader header,

Map qosProperties)

throws MALException

The method ‘deregisterAckReceived’ parameters shall be assigned as described in table 3-67.

Table 3-85:  MALInteractionListener ‘deregisterAckReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the DEREGISTER ACK message |
| qosProperties | QoS properties of the DEREGISTER ACK message |

The parameter ‘header’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

### MALInteractionAdapter

A MALInteractionAdapter abstract class shall be defined in order to enable a MAL client not to implement all the methods provided by the interface MALInteractionListener.

The class shall implement the interface MALInteractionListener.

The class shall implement all the methods provided by the interface MALInteractionListener with an empty implementation.

## Provider package

### Overview

This part of the API is dedicated to the MAL clients handling interactions as service providers. The provider state diagrams are specified in reference [1].

The classes and interfaces belong to the Java package:

org.ccsds.moims.mo.mal.provider

### MALProviderManager

#### Definition

A MALProviderManager interface shall be defined in order to encapsulate the resources used to enable MAL providers to handle interactions.

A MALProviderManager shall be a MALProvider factory.

#### MALProviderManager Creation

A MALProviderManager shall be created by calling the method ‘createProviderManager’ provided by a MALContext.

Several MALProviderManager instances should be created in order to separate the resources used by the providers.

#### Create a Provider

Two methods ‘createProvider’ shall be defined in order to create a MALProvider:

- using a private MALEndpoint;

- using a shared MALEndpoint.

The methods signatures shall be:

public MALProvider createProvider(

String localName,

String protocol,

MALService service,

Blob authenticationId,

MALInteractionHandler handler,

QoSLevel[] expectedQos,

UInteger priorityLevelNumber,

Map defaultQoSProperties,

Boolean isPublisher,

URI sharedBrokerUri)

throws java.lang.IllegalArgumentException, MALException

public MALProvider createProvider(

MALEndpoint endpoint,

MALService service,

Blob authenticationId,

MALInteractionHandler handler,

QoSLevel[] expectedQos,

UInteger priorityLevelNumber,

Map defaultQoSProperties,

Boolean isPublisher,

URI sharedBrokerUri)

throws java.lang.IllegalArgumentException, MALException

The ‘createProvider’ parameters shall be assigned as described in table 3-86.

Table 3-86:  MALProviderManager ‘createProvider’ Parameters

| Parameter | Description |
| --- | --- |
| localName | Name of the private MALEndpoint to be created and used by the provider |
| protocol | Name of the protocol used to bind the provider |
| endpoint | Shared MALEndpoint to be used by the provider |
| service | Description of the provided service |
| authenticationId | Authentication identifier used by the provider |
| handler | Interaction handler |
| expectedQoS | QoS levels the provider can rely on |
| priorityLevelNumber | Number of priorities the provider uses |
| defaultQoSProperties | Default QoS properties used by the provider to send messages back to the consumer and to publish updates to a shared broker |
| isPublisher | Specifies whether the provider is a PUBLISH-SUBSCRIBE publisher or not |
| sharedBrokerUri | URI of the shared broker to be used |

The parameter ‘localName’ may be NULL.

If the parameter ‘localName’ is not NULL then its value shall be unique for the MALContext instance and the protocol specified by the parameter ‘protocol’.

The parameter ‘defaultQoSProperties’ may be NULL.

If the parameters ‘protocol’ or ‘endpoint’ or ‘service’ or ‘authenticationId’ or ‘handler’ or ‘expectedQoS’ or ‘isPublisher’ are NULL then an IllegalArgumentException shall be raised.

The method ‘createProvider’ shall not return the value NULL.

If the parameter ‘isPublisher’ is TRUE then:

- if the parameter ‘sharedBrokerUri’ is NULL then a private broker shall be created;

- else the URI specified by the parameter ‘sharedBrokerUri’ shall be used as the destination URI by the provider when sending PUBLISH-SUBSCRIBE messages.

The URI specified by the parameter ‘sharedBrokerUri’ shall have the same protocol as specified by the parameter ‘protocol’.

The private broker shall be aggregated into the MALProvider, i.e., it shall be created and deleted at the same time as the provider it belongs to.

The private broker shall be separately identified by its own URI.

The URI of the private broker may be the same as the URI of the provider it belongs to.

A shared broker shall be created by using the broker part of this API.

If a private MALEndpoint is created then the message delivery shall be started. As a consequence the provider shall be able to handle interactions through the interface MALInteractionHandler as soon as the method ‘createProvider’ returns.

If the MALProviderManager is closed then a MALException shall be raised.

If the provider local name is not NULL and if the provider process starts again after a stop and creates the MALProvider with the same local name (directly or through a shared MALEndpoint) then the MALProvider shall recover the same URI as before the stop.

It shall be allowed to create several MALProviders using private brokers and sharing the same MALEndpoint.

The method ‘handleSend’ provided by the parameter ‘handler’ shall be called as soon as a SEND message has been delivered.

The method ‘handleSubmit’ provided by the parameter ‘handler’ shall be called as soon as a SUBMIT message has been delivered.

The method ‘handleRequest’ provided by the parameter ‘handler’ shall be called as soon as a REQUEST message has been delivered.

The method ‘handleInvoke’ provided by the parameter ‘handler’ shall be called as soon as an INVOKE message has been delivered.

The method ‘handleProgress’ provided by the parameter ‘handler’ shall be called as soon as a PROGRESS message has been delivered.

NOTE	–	The same instance of MALInteractionHandler can be passed several times as a parameter of the method ‘createProvider’. In this way the MALInteractionHandler will be activated by several MALProviders.

#### Close

A method ‘close’ shall be defined in order to release the resources owned by a MALProviderManager.

The method signature shall be:

public void close() throws MALException

The method ‘close’ shall close all the MALProviders owned by this MALProviderManager.

The method ‘close’ shall return after all the MALProviders have been closed.

If an internal error occurs then a MALException shall be raised.

### MALProvider

#### Definition

A MALProvider interface shall be defined in order to represent the execution context of a service provider for a given URI.

If a service provider is to be bound to several transport layers then several MALProviders shall be created, each one representing a binding between the service provider and a transport layer.

NOTE	–	Those MALProviders should own the same MALInteractionHandler instance. However, it is not mandatory, as several MALInteractionHandlers can share the same state, for example, a common data base.

#### MALProvider Creation

A MALProvider shall be created by calling the method ‘createProvider’ provided by a MALProviderManager.

A MALProvider shall be active as soon as it has been instantiated.

#### Get the URI of the Provider

The MALProvider interface shall provide a getter method that returns the URI of the provider.

The method signature shall be:

public URI getURI()

#### Publishing Enabled

A method ‘isPublisher’ shall be defined in order to indicate whether the provider can publish updates or not.

The method signature shall be:

public boolean isPublisher()

#### Get the URI of the Broker

The MALProvider interface shall provide a getter method that returns the URI of the private broker.

The method signature shall be:

public URI getBrokerURI()

The method shall return:

- NULL if the provider is not linked to a broker, i.e., the method ‘isPublisher’ returns false;

- the URI of the broker used by this provider.

#### Get the Authentication Identifier of the Private Broker

The MALProvider interface shall provide a getter method that returns the authentication identifier of the private broker.

The method signature shall be:

public Blob getBrokerAuthenticationId()

The method shall return:

- NULL if the provider does not own a private broker;

- the authentication identifier of the private broker.

#### Get the service

A getter method shall be defined in order to return the MALService provided by this MALProvider

The method signature shall be:

public MALService getService()

#### Create a Publisher

A method ‘createPublisher’ shall be defined in order to create a MALPublisher.

The method signature shall be:

public MALPublisher createPublisher(MALPubSubOperation op,

IdentifierList domain,

Identifier networkZone,

SessionType sessionType,

Identifier sessionName,

QoSLevel remotePublisherQos,

Map remotePublisherQosProps,

UInteger remotePublisherPriority)

throws java.lang.IllegalArgumentException, MALException

The ‘createPublisher’ parameters shall be assigned as described in table 3-87.

Table 3-87:  MALProvider ‘createPublisher’ Parameters

| Parameter | Description |
| --- | --- |
| op | PUBLISH-SUBSCRIBE operation |
| domain | Domain of the PUBLISH messages |
| networkZone | Network zone of the PUBLISH messages |
| sessionType | Session type of the PUBLISH messages |
| sessionName | Session name of the PUBLISH messages |
| remotePublisherQos | QoS level of the PUBLISH messages |
| remotePublisherQosProps | QoS properties of the PUBLISH messages |
| remotePublisherPriority | Priority of the PUBLISH messages |

If the parameters ‘domain’ or ‘networkZone’ or ‘sessionType’ or ‘sessionName’ are NULL then an IllegalArgumentException shall be raised.

If the broker is remote and if the parameters ‘remotePublisherQos’ or ‘remotePublisherQosProps’ or ‘remotePublisherPriority’ are NULL then an IllegalArgumentException shall be raised.

The parameters ‘remotePublisherQos’, ‘remotePublisherQosProps’ and ‘remotePublisherPriority’ shall be ignored if the broker is local.

If the MALProvider is not a publisher then a MALException shall be raised.

If the MALProvider is closed then a MALException shall be raised.

#### Close

A method ‘close’ shall be defined in order to deactivate the MALInteractionHandler so that no interaction pattern is handled any longer.

The method signature shall be:

public void close() throws MALException

A close should be called by a MAL client before the provider process is stopped for any operational reason.

The method ‘close’ shall deactivate this MALProvider.

If the MALInteractionHandler is being activated at the time of the close then the closing process shall wait for the end of the handler’s execution.

Once a MALProvider has been closed, the message delivery shall be stopped in order that the MALInteractionHandler does not receive any message through this MALProvider any more.

If an internal error occurs then a MALException shall be raised.

If the provider owns a private MALEndpoint then the MALEndpoint shall be closed.

Pending interactions shall be finalized by returning the error DESTINATION_LOST_OR_DIED to the consumers.

If the provider owns a private broker,

- this broker shall be deleted;

- the subscribers list shall be cleared;

- an error DESTINATION_LOST_OR_DIED shall be sent to the subscribers in order to inform them that they are no longer subscribed to the private broker.

If a consumer tries to interact with a closed provider and if the QoS level is not QUEUED, a DELIVERY_FAILED shall be returned to the consumer.

If a consumer tries to interact with a closed provider and if the QoS level is QUEUED, then the consumer’s request shall be queued and delivered as soon as the provider message delivery is started again.

### MALInteractionHandler

#### Definition

A MALInteractionHandler interface shall be defined in order to handle the interactions on the provider side.

The MALInteractionHandler interface shall not handle the PUBLISH-SUBSCRIBE REGISTER, PUBLISH REGISTER, PUBLISH, DEREGISTER and PUBLISH DEREGISTER messages.

NOTE	–	The messages REGISTER, PUBLISH REGISTER, PUBLISH, DEREGISTER and PUBLISH DEREGISTER are handled by a broker.

A MALInteractionHandler shall be passed as a parameter of the method ‘createProvider’ when creating a MALProvider.

NOTE	–	Several MALProviders may use the same instance of MALInteractionHandler.

#### Initialize

A method ‘malInitialize’ shall be defined in order to enable a MALInteractionHandler to be initialized when the provider is activated.

The method signature shall be:

public void malInitialize(MALProvider provider) throws MALException

The ‘malInitialize’ parameter shall be assigned as described in table 3-88.

Table 3-88:  MALInteractionHandler ‘malInitialize’ Parameter

| Parameter | Description |
| --- | --- |
| provider | Created MALProvider |

The method ‘malInitialize’ shall be called when the MALProvider is created.

NOTE	–	The method ‘malInitialize’ enables the handler to get the reference of the MALProvider and use it if necessary.

If an instance of MALInteractionHandler is used by several MALProviders then the method ‘malInitialize’ shall be called once for each MALProvider.

A MALException may be raised if an error occurs.

#### Handle a SEND IP

A method ‘handleSend’ shall be defined in order to handle a SEND interaction.

The method ‘handleSend’ signature shall be:

public void handleSend(MALInteraction interaction, MALMessageBody body)

throws MALInteractionException, MALException

The method ‘handleSend’ parameters shall be assigned as described in table 3-89.

Table 3-89:  MALInteractionHandler ‘handleSend’ Parameters

| Parameter | Description |
| --- | --- |
| interaction | SEND interaction context |
| body | Message body |

The parameter ‘interaction’ shall not be NULL.

The parameter ‘body’ may be NULL.

If an error occurs then a MALException may be raised.

A MALInteractionException may be raised.

#### Handle a SUBMIT IP

A method ‘handleSubmit’ shall be defined in order to handle a SUBMIT interaction.

The method ‘handleSubmit’ signature shall be:

public void handleSubmit(MALSubmit interaction, MALMessageBody body)

throws MALInteractionException, MALException

The method ‘handleSubmit’ parameters shall be assigned as described in table 3-90.

Table 3-90:  MALInteractionHandler ‘handleSubmit’ Parameters

| Parameter | Description |
| --- | --- |
| interaction | SUBMIT interaction context |
| body | Message body |

The parameter ‘interaction’ shall not be NULL.

The parameter ‘body’ may be NULL.

The ACK and ACK ERROR message body shall be returned through the MALSubmit context.

If a MAL standard error occurs it shall be returned through the MALSubmit context.

If a non-MAL error occurs then a MALException may be raised.

A MALInteractionException may be raised.

#### Handle a REQUEST IP

A method ‘handleRequest’ shall be defined in order to handle a REQUEST interaction.

The method ‘handleRequest’ signature shall be:

public void handleRequest(MALRequest interaction, MALMessageBody body)

throws MALInteractionException, MALException

The method ‘handleRequest’ parameters shall be assigned as described in table 3-91.

Table 3-91:  MALInteractionHandler ‘handleRequest’ Parameters

| Parameter | Description |
| --- | --- |
| interaction | REQUEST interaction context |
| body | Message body |

The parameter ‘interaction’ shall not be NULL.

The parameter ‘body’ may be NULL.

The RESPONSE and RESPONSE ERROR message body shall be returned through the MALRequest context.

If a MAL standard error occurs it shall be returned through the MALRequest context.

If a non-MAL error occurs then a MALException may be raised.

A MALInteractionException may be raised.

#### Handle an INVOKE IP

A method ‘handleInvoke’ shall be defined in order to handle a REQUEST interaction.

The method ‘handleInvoke’ signature shall be:

public void handleInvoke(MALInvoke interaction, MALMessageBody body)

throws MALInteractionException, MALException

The method ‘handleInvoke’ parameters shall be assigned as described in table 3-92.

Table 3-92:  MALInteractionHandler ‘handleInvoke’ Parameters

| Parameter | Description |
| --- | --- |
| interaction | INVOKE interaction context |
| body | Message body |

The parameter ‘interaction’ shall not be NULL.

The parameter ‘body’ may be NULL.

The ACK, ACK ERROR, RESPONSE and RESPONSE ERROR message body shall be returned through the MALInvoke context.

If a MAL standard error occurs it shall be returned through the MALInvoke context.

If a non-MAL error occurs then a MALException may be raised.

A MALInteractionException may be raised.

#### Handle a PROGRESS IP

A method ‘handleProgress’ shall be defined in order to handle a PROGRESS interaction.

The method ‘handleProgress’ signature shall be:

public void handleProgress(MALProgress interaction, MALMessageBody body)

throws MALInteractionException, MALException

The method ‘handleProgress’ parameters shall be assigned as described in table 3-93.

Table 3-93:  MALInteractionHandler ‘handleProgress’ Parameters

| Parameter | Description |
| --- | --- |
| interaction | PROGRESS interaction context |
| body | Message body |

The parameter ‘interaction’ shall not be NULL.

The parameter ‘body’ may be NULL.

The ACK, ACK ERROR, RESPONSE and RESPONSE ERROR message body shall be returned through the MALProgress context.

If a MAL standard error occurs it shall be returned through the MALProgress context.

If a non-MAL error occurs then a MALException may be raised.

A MALInteractionException may be raised.

#### Finalize

A method ‘malFinalize’ shall be defined in order to enable a MALInteractionHandler to be notified when a MALProvider is closed.

The method signature shall be:

public void malFinalize(MALProvider provider) throws MALException

The ‘malFinalize’ parameter shall be assigned as described in table 3-94.

Table 3-94:  MALInteractionHandler ‘malFinalize’ Parameter

| Parameter | Description |
| --- | --- |
| provider | Closed MALProvider |

The method ‘malFinalize’ shall be called when the MALProvider is closed.

A MALException may be raised if an error occurs.

### MALInteraction

#### Definition

A MALInteraction interface shall be defined in order to represent a generic IP handling context.

The MALInteraction interface shall be extended by a specific interaction interface for each IP except SEND and PUBLISH-SUBSCRIBE:

- SEND shall be handled by passing a MALInteraction;

- PUBLISH-SUBSCRIBE shall not be handled by a MALInteractionHandler.

#### Get the Message Header

A method ‘getMessageHeader’ shall be defined in order to return the header of the message that initiated the interaction.

The method signature shall be:

public MALMessageHeader getMessageHeader()

#### Get the Operation

A method ‘getOperation’ shall be defined in order to return the operation called through this interaction.

The method signature shall be:

public MALOperation getOperation()

#### Get/Set a QoS Property

The setQoSProperty and getQoSProperty methods shall be defined in order to enable to get and set the value of a QoS property.

The methods signatures shall be:

public void setQoSProperty(String name, Element value)

throws java.lang.IllegalArgumentException

public Element getQoSProperty(String name)

throws java.lang.IllegalArgumentException

The ‘get/setProperty’ parameters shall be assigned as described in table 3-94.

Table 3-95:  MALInteractionHandler ‘get/setQoSProperty’ Parameters

| Parameter | Description |
| --- | --- |
| name | Name of the property |
| value | Value of the property |

If the parameter ‘name’ is NULL then a java.lang.IllegalArgumentException shall be raised.

### MALSubmit

#### Definition

A MALSubmit interface shall be defined in order to represent a SUBMIT interaction handling context.

The MALSubmit interface shall inherit from the interface MALInteraction.

#### Send an ACK

A method ‘sendAcknowledgement’ shall be defined in order to send an ACK message.

The method signature shall be:

public MALMessage sendAcknowledgement()

throws MALException, MALInteractionException

NOTE	–	The SUBMIT ACK message body is empty.

The method shall check the interaction state as follows:

- if the state is INITIATED an ACK message shall be sent;

- otherwise a MALInteractionException containing a MAL::INCORRECT_STATE error shall be raised.

The method shall return as soon as the ACK message has been sent.

The method shall return the MALMessage that has been sent.

If an error occurs then a MALException shall be raised.

#### Send an ACK ERROR

A method ‘sendError’ shall be defined in order to send an ACK ERROR message.

The method signature shall be:

public MALMessage sendError(MALStandardError error)

throws java.lang.IllegalArgumentException,

MALException, MALInteractionException

The method ‘sendError’ parameter shall be assigned as described in table 3-96.

Table 3-96:  MALSubmit ‘sendError’ Parameter

| Parameter | Description |
| --- | --- |
| error | Error to be transmitted to the consumer |

If the parameter ‘error’ is NULL then an IllegalArgumentException shall be raised.

The method shall check the interaction state as follows:

- if the state is INITIATED an ACK ERROR message shall be sent;

- otherwise a MALInteractionException containing a MAL::INCORRECT_STATE error shall be raised.

The method shall return as soon as the ACK ERROR message has been sent.

The method shall return the MALMessage that has been sent.

If an error occurs then a MALException shall be raised.

### MALRequest

#### Definition

A MALRequest interface shall be defined in order to represent a REQUEST interaction handling context.

The MALRequest interface shall inherit from the interface MALInteraction.

#### Send a RESPONSE

A method ‘sendResponse’ shall be defined in order to send a RESPONSE message.

The method signature shall be:

public MALMessage sendResponse(Object... body)

throws MALException, MALInteractionException

The method ‘sendResponse’ parameter shall be assigned as described in table 3-97.

Table 3-97:  MALResponse ‘sendResponse’ Parameter

| Parameter | Description |
| --- | --- |
| body | Message body to be transmitted to the consumer |

The method shall check the interaction state as follows:

- if the state is INITIATED a RESPONSE message shall be sent;

- otherwise a MALInteractionException containing a MAL::INCORRECT_STATE error shall be raised.

The method shall return as soon as the RESPONSE message has been sent.

The method shall return the MALMessage that has been sent.

If an error occurs then a MALException shall be raised.

The allowed body element types shall be:

- MAL element types;

- MALEncodedElement;

- Java types defined by a specific Java mapping extension.

#### Send a RESPONSE ERROR

A method ‘sendError’ shall be defined in order to send a RESPONSE message.

The method signature shall be:

public MALMessage sendError(MALStandardError error)

throws java.lang.IllegalArgumentException,

MALException, MALInteractionException

The method ‘sendError’ parameter shall be assigned as described in table 3-98.

Table 3-98:  MALResponse ‘sendError’ Parameter

| Parameter | Description |
| --- | --- |
| error | Error to be transmitted to the consumer |

If the parameter ‘error’ is NULL then an IllegalArgumentException shall be raised.

The method shall check the interaction state as follows:

- if the state is INITIATED a RESPONSE ERROR message shall be sent;

- otherwise a MALInteractionException containing a MAL::INCORRECT_STATE error shall be raised.

The method shall return as soon as the RESPONSE ERROR message has been sent.

The method shall return the MALMessage that has been sent.

If an error occurs then a MALException shall be raised.

### MALInvoke

#### Definition

A MALInvoke interface shall be defined in order to represent an INVOKE interaction handling context.

The MALInvoke interface shall inherit from the interface MALRequest.

#### Send an ACK

A method ‘sendAcknowledgement’ shall be defined in order to send an ACK message.

The method signature shall be:

public MALMessage sendAcknowledgement(Object... body)

throws MALException, MALInteractionException

The method ‘sendAcknowledgement’ parameter shall be assigned as described in table 3-99.

Table 3-99:  MALInvoke ‘sendAcknowledgement’ Parameters

| Parameter | Description |
| --- | --- |
| body | Message body to be transmitted to the consumer |

The method shall check the interaction state as follows:

- if the state is INITIATED an ACK message shall be sent;

- otherwise a MALInteractionException containing a MAL::INCORRECT_STATE error shall be raised.

The method shall return as soon as the ACK message has been sent.

The method shall return the MALMessage that has been sent.

If an error occurs then a MALException shall be raised.

The allowed body element types shall be:

- MAL element types;

- MALEncodedElement;

- Java types defined by a specific Java mapping extension.

#### Send a RESPONSE

The method ‘sendResponse’ inherited from MALRequest shall check the interaction state as follows:

- if the state is ACKNOWLEDGED a RESPONSE message shall be sent;

- otherwise a MALInteractionException containing a MAL::INCORRECT_STATE error shall be raised.

If an error occurs then a MALException shall be raised.

#### Send an ACK or a RESPONSE ERROR

The method ‘sendError’ inherited from MALRequest shall check the interaction state as follows:

- if the state is INITIATED an ACK ERROR message shall be sent;

- else if the state is ACKNOWLEDGED a RESPONSE ERROR message shall be sent;

- otherwise a MALInteractionException containing a MAL::INCORRECT_STATE error shall be raised.

If an error occurs then a MALException shall be raised.

### MALProgress

#### Definition

A MALProgress interface shall be defined in order to represent a PROGRESS interaction handling context.

The MALProgress interface inherits from the interface MALInvoke.

#### Send an ACK

The method ‘sendAcknowledgement’ inherited from MALInvoke shall check the interaction state as follows:

- if the state is INITIATED an ACK message shall be sent;

- otherwise a MALInteractionException containing a MAL::INCORRECT_STATE error shall be raised.

If an error occurs then a MALException shall be raised.

#### Send an UPDATE

A method ‘sendUpdate’ shall be defined in order to send an UPDATE message.

The method signature shall be:

public MALMessage sendUpdate(Object... body) throws MALException

The method ‘sendUpdate’ parameter shall be assigned as described in table 3-100.

Table 3-100:  MALProgress ‘sendUpdate’ Parameter

| Parameter | Description |
| --- | --- |
| body | Message body to be transmitted to the consumer |

The method shall check the interaction state as follows:

- if the state is either ACKNOWLEDGED or PROGRESSING an UPDATE message shall be sent;

- otherwise a MALInteractionException containing a MAL::INCORRECT_STATE error shall be raised.

The method shall return as soon as the UPDATE message has been sent.

The method shall return the MALMessage that has been sent.

If an error occurs then a MALException shall be raised.

The allowed body element types shall be:

- MAL element types;

- MALEncodedElement;

- Java types defined by a specific Java mapping extension.

#### Send a RESPONSE

The method ‘sendResponse’ inherited from MALRequest shall check the interaction state as follows:

- if the state is either ACKNOWLEDGED or PROGRESSING a RESPONSE message shall be sent;

- otherwise a MALInteractionException containing a MAL::INCORRECT_STATE error shall be raised.

If an error occurs then a MALException shall be raised.

#### Send an ACK or a RESPONSE ERROR

The method ‘sendError’ inherited from MALRequest shall check the interaction state as follows:

- if the state is INITIATED an ACK ERROR message shall be sent;

- if the state is either ACKNOWLEDGED or PROGRESSING a RESPONSE ERROR message shall be sent;

- otherwise a MALInteractionException containing a MAL::INCORRECT_STATE error shall be raised.

If an error occurs then a MALException shall be raised.

#### Send an UPDATE ERROR

A method ‘sendUpdateError’ shall be defined in order to send an UPDATE ERROR message.

The method signature shall be:

public MALMessage sendUpdateError(MALStandardError error)

throws MALInteractionException, MALException

The method ‘sendUpdateError’ parameter shall be assigned as described in table 3-101.

Table 3-101:  MALProgress ‘sendUpdateError’ Parameter

| Parameter | Description |
| --- | --- |
| error | Error to be transmitted to the consumer |

The method shall check the interaction state as follows:

- if the state is either ACKNOWLEDGED or PROGRESSING an UPDATE ERROR message shall be sent;

- otherwise a MALInteractionException containing a MAL::INCORRECT_STATE error shall be raised.

The method shall return as soon as the UPDATE ERROR message has been sent.

The method shall return the MALMessage that has been sent.

If an error occurs then a MALException shall be raised.

### MALPublisher

#### Definition

A MALPublisher interface shall be defined in order to enable a provider to publish updates and errors to registered consumers.

#### Publish Updates

A method ‘publish’ shall be defined in order to publish a list of updates.

The method signature shall be:

public MALMessage publish(

UpdateHeaderList updateHeaderList,

java.util.List… updateLists)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

The ‘publish’ parameters shall be assigned as described in table 3-102.

Table 3-102:  MALPublisher ‘publish’ Parameters

| Parameter | Description |
| --- | --- |
| updateHeaderList | Published UpdateHeaders |
| updateLists | Lists of updates to be published |

If the parameter ‘updateLists’ is NULL then an IllegalArgumentException shall be raised.

The method ‘publish’ shall return as soon as the PUBLISH message has been sent.

The method shall return the MALMessage that has been sent.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if a non-MAL error occurs during the initiation message sending.

If the MALPublisher is closed then a MALException shall be raised.

The allowed update list types shall be:

- a MAL element list;

- a List<MALEncodedElement> containing the encoded updates;

- a List defined by a specific Java mapping extension.

#### Register

A method ‘register’ shall be defined in order to enable a provider to synchronously register to its broker.

The method signature shall be:

public void register(EntityKeyList entityKeys,

MALPublishInteractionListener listener)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

NOTE	–	The ‘register’ parameters shall be assigned as described in table 3-103.

Table 3-103:  MALPublisher ‘register’ Parameters

| Parameter | Description |
| --- | --- |
| entityKeyList | Keys of the entities that are to be published |
| listener | Listener in charge of receiving the messages PUBLISH ERROR |

If the parameters ‘entityKeyList’ or ‘listener’ are NULL then an IllegalArgumentException shall be raised.

The method ‘register’ shall return as soon as the PUBLISH REGISTER ACK message has been received.

A MALException shall be thrown if a non-MAL error occurs during the initiation message sending.

A MALInteractionException shall be thrown if a PUBLISH REGISTER ERROR occurs. The PUBLISH REGISTER ERROR message body shall be passed as the parameter ‘standardError’ of the MALInteractionException constructor.

The method ‘errorReceived’ provided by the parameter ‘listener’ shall be called if a PUBLISH ERROR occurs. The call to ‘errorReceived’ shall have the following parameters:

- the PUBLISH ERROR message header passed as the parameter ‘header’;

- the PUBLISH ERROR message body passed as the parameter ‘error’.

If a call to ‘register’ is initiated while the publisher is already registered but with a different parameter ‘listener’ then only the second registered ‘listener’ shall receive the PUBLISH ERROR messages.

If the MALPublisher is closed then a MALException shall be raised.

#### Deregister

A method ‘deregister’ shall be defined in order to enable a provider to synchronously deregister from its broker.

The method signature shall be:

public void deregister() throws MALInteractionException, MALException

The method ‘deregister’ shall return as soon as the PUBLISH DEREGISTER ACK message has been received.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if a non-MAL error occurs during the initiation message sending.

#### Asynchronous Register

A method ‘asyncRegister’ shall be defined in order to enable a provider to asynchronously register to its broker.

The method signature shall be:

public MALMessage asyncRegister(EntityKeyList entityKeys,

MALPublishInteractionListener listener)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

NOTE	–	The ‘asyncRegister’ parameters shall be assigned as described in table 3-104.

Table 3-104:  MALPublisher ‘asyncRegister’ Parameters

| Parameter | Description |
| --- | --- |
| entityKeyList | Keys of the entities that are to be published |
| listener | Listener in charge of receiving the messages PUBLISH REGISTER ACK, PUBLISH REGISTER ERROR and PUBLISH ERROR |

If the parameter ‘entityKeyList’ or ‘listener’ are NULL then an IllegalArgumentException shall be raised.

The method ‘asyncRegister’ shall return as soon as the PUBLISH REGISTER message has been sent.

The method shall return the MALMessage that has been sent.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if a non-MAL error occurs during the initiation message sending.

The method ‘publishAckReceived’ provided by the parameter ‘listener’ shall be called as soon as the PUBLISH REGISTER ACK message has been delivered. The call to ‘acknowledgementReceived’ shall assign the PUBLISH REGISTER ACK message header to the parameter ‘header’.

The method ‘errorReceived’ provided by the parameter ‘listener’ shall be called if a PUBLISH REGISTER ERROR or a PUBLISH ERROR occurs. The call to ‘errorReceived’ shall have the following parameters:

- the ERROR message header passed as the parameter ‘header’;

- the ERROR message body passed as the parameter ‘error’.

If a call to ‘register’ is initiated while the publisher is already registered but with a different parameter ‘listener’ then only the second registered ‘listener’ shall receive the PUBLISH ERROR messages.

If the MALPublisher is closed then a MALException shall be raised.

#### Asynchronous Deregister

A method ‘asyncDeregister’ shall be defined in order to enable a provider to asynchronously deregister from its broker.

The method signature shall be:

public MALMessage asyncDeregister(

MALPublishInteractionListener listener)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

NOTE	–	The asyncDeregister parameter shall be assigned as described in table 3-105.

Table 3-105:  MALPublisher ‘asyncDeregister’ Parameter

| Parameter | Description |
| --- | --- |
| listener | Listener in charge of receiving the messages PUBLISH DEREGISTER ACK |

If the parameter ‘listener’ is NULL then an IllegalArgumentException shall be raised.

The method ‘asyncDeregister’ shall return as soon as the PUBLISH DEREGISTER message has been sent.

The method shall return the MALMessage that has been sent.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if a non-MAL error occurs during the initiation message sending.

The method ‘acknowledgementReceived’ provided by the parameter ‘listener’ shall be called as soon as the PUBLISH DEREGISTER ACK message has been delivered. The call to ‘acknowledgementReceived’ shall assign the PUBLISH DEREGISTER ACK message header to the parameter ‘header’.

If the MALPublisher is closed then a MALException shall be raised.

#### Get the MALProvider

A getter method shall be defined in order to return the MALProvider that created this MALPublisher

The method signature shall be:

public MALProvider getProvider()

#### Close

A method ‘close’ shall be defined in order to release the resources owned by this MALPublisher.

The method signature shall be:

public void close() throws MALException

A closed MALPublisher may still be registered.

A closed MALPublisher shall not deliver any asynchronous messages any more, i.e., PUBLISH ERROR, PUBLISH REGISTER ACK and PUBLISH DEREGISTER ACK.

### MALPublishInteractionListener

#### Definition

A MALPublishInteractionListener interface shall be defined in order to allow the reception of the publish interaction results.

#### Receive a PUBLISH REGISTER ACK

A method ‘publishRegisterAckReceived’ shall be defined in order to receive the PUBLISH REGISTER ACK message defined by the IP PUBLISH-SUBSCRIBE.

The method signature shall be:

public void publishRegisterAckReceived(MALMessageHeader header,

Map qosProperties) throws MALException;

The method ‘publishRegisterAckReceived’ parameters shall be assigned as described in table 3-106.

Table 3-106:  MALPublishInteractionListener ‘publishRegisterAckReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the message |
| qosProperties | QoS properties of the message |

The parameter ‘header’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

#### Receive a PUBLISH REGISTER ERROR

A method ‘errorReceived’ shall be defined in order to receive the PUBLISH REGISTER ERROR message defined by the IP PUBLISH-SUBSCRIBE.

The method signature shall be:

public void publishRegisterErrorReceived(MALMessageHeader header,

MALErrorBody body, Map qosProperties) throws MALException;

The method ‘publishRegisterErrorReceived’ parameters shall be assigned as described in table 3-107.

Table 3-107:  MALPublishInteractionListener ‘publishRegisterErrorReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the message |
| body | Body of the message |
| qosProperties | QoS properties of the message |

The parameters ‘header’ and ‘body’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

#### Receive a PUBLISH ERROR

A method ‘publishErrorReceived’ shall be defined in order to receive the PUBLISH ERROR message defined by the IP PUBLISH-SUBSCRIBE.

The method signature shall be:

public void publishErrorReceived(MALMessageHeader header,

MALErrorBody body, Map qosProperties) throws MALException;

The method ‘publishErrorReceived’ parameters shall be assigned as described in table 3-107.

Table 3-108:  MALPublishInteractionListener ‘publishErrorReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the message |
| body | Body of the message |
| qosProperties | QoS properties of the message |

The parameters ‘header’ and ‘body’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

#### Receive a PUBLISH DEREGISTER ACK

A method ‘publishDeregisterAckReceived’ shall be defined in order to receive the PUBLISH DEREGISTER ACK message defined by the IP PUBLISH-SUBSCRIBE.

The method signature shall be:

public void publishDeregisterAckReceived(MALMessageHeader header,

Map qosProperties) throws MALException;

The method ‘publishDeregisterAckReceived’ parameters shall be assigned as described in table 3-106.

Table 3-109:  MALPublishInteractionListener ‘publishDeregisterAckReceived’ Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the message |
| qosProperties | QoS properties of the message |

The parameter ‘header’ shall not be NULL.

The parameter ‘qosProperties’ may be NULL.

If an error occurs then a MALException may be raised.

### MALProviderSet

#### Definition

A MALProviderSet class shall be defined in order to:

- manage a list of MALProvider providing the same service through different protocols;

- create instances of MALPublisherSet, register their references and update them when a MALProvider is either added or removed.

#### Creation

A public constructor shall be defined.

The constructor signature shall be:

public MALProviderSet(MALService service)

throws java.lang.IllegalArgumentException

The constructor parameter shall be assigned as described in table 3-46.

Table 3-110:  MALProviderSet Constructor Parameter

| Parameter | Description |
| --- | --- |
| service | The service to be provided by the MALProviders added in this MALProviderSet |

If the parameter ‘service’ is NULL then an IllegalArgumentException shall be raised.

#### Create a MALPublisherSet

A method ‘createPublisherSet’ shall be defined in order to create a MALPublisherSet and register its reference.

The method signature shall be:

public MALPublisherSet createPublisherSet(

MALPubSubOperation op,

IdentifierList domain,

Identifier networkZone,

SessionType sessionType,

Identifier sessionName,

QoSLevel remotePublisherQos,

Map remotePublisherQosProps,

UInteger remotePublisherPriority)

throws java.lang.IllegalArgumentException, MALException

The method ‘createPublisherSet’ parameters shall be assigned as described in table 3-100.

Table 3-111:  MALProviderSet ‘createPublisherSet’ Parameters

| Parameter | Description |
| --- | --- |
| op | PUBLISH-SUBSCRIBE operation |
| domain | Domain of the PUBLISH messages |
| networkZone | Network zone of the PUBLISH messages |
| sessionType | Session type of the PUBLISH messages |
| sessionName | Session name of the PUBLISH messages |
| remotePublisherQos | QoS level of the PUBLISH messages |
| remotePublisherQosProps | QoS properties of the PUBLISH messages |
| remotePublisherPriority | Priority of the PUBLISH messages |

If the parameters ‘domain’ or ‘networkZone’ or ‘sessionType’ or ‘sessionName’ are NULL then an IllegalArgumentException shall be raised.

If the broker is remote and if the parameters ‘remotePublisherQos’ or ‘remotePublisherQosProps’ or ‘remotePublisherPriority’ are NULL then an IllegalArgumentException shall be raised.

The parameters ‘remotePublisherQos’, ‘remotePublisherQosProps’ and ‘remotePublisherPriority’ shall be ignored if the broker is local.

The reference of the returned MALPublisherSet shall be registered in this MALProviderSet.

#### Add a provider

A method ‘addProvider’ shall be defined in order to add a MALProvider to this MALProviderSet.

The method signature shall be:

public void addProvider(MALProvider provider)

throws java.lang.IllegalArgumentException, MALException

The method ‘addProvider’ parameter shall be assigned as described in table 3-100.

Table 3-112:  MALProviderSet ‘addProvider’ Parameter

| Parameter | Description |
| --- | --- |
| provider | MALProvider to be added |

If the parameter ‘provider’ is NULL then an IllegalArgumentException shall be raised.

If the added MALProvider provides a MALService which is not the same as the MALService of this MALProviderSet then a MALException shall be raised.

For every registered MALPublisherSet, one MALPublisher shall be created by calling the method ‘createPublisher’ provided by the MALPublisherSet.

#### Remove a provider

A method ‘removeProvider’ shall be defined in order to remove a MALProvider from this MALProviderSet.

The method signature shall be:

public boolean removeProvider(MALProvider provider)

throws java.lang.IllegalArgumentException

The method ‘removeProvider’ parameter shall be assigned as described in table 3-100.

Table 3-113:  MALProviderSet ‘removeProvider’ Parameter

| Parameter | Description |
| --- | --- |
| provider | MALProvider to be removed |

If the parameter ‘provider’ is NULL then an IllegalArgumentException shall be raised.

If this MALProviderSet contains the specified provider then the method shall return ‘true’. Otherwise it shall return ‘false’.

For every registered MALPublisherSet, the MALPublisher created through the removed MALProvider shall be deleted by calling the method ‘deletePublisher’ provided by the MALPublisherSet.

### MALPublisherSet

#### Definition

A MALPublisherSet class shall be defined in order to manage a set of MALPublishers that publish updates:

- through the same PUBLISH-SUBSCRIBE operation;

- in the same domain, network zone and session;

- with the same QoS level and priority.

#### Creation

A constructor shall be defined.

The constructor signature shall be:

MALPublisherSet(

MALProviderSet providerSet,

MALPubSubOperation op,

IdentifierList domain,

Identifier networkZone,

SessionType sessionType,

Identifier sessionName,

QoSLevel remotePublisherQos,

Map remotePublisherQosProps,

UInteger remotePublisherPriority)

throws java.lang.IllegalArgumentException, MALException

The constructor parameters shall be assigned as described in table 3-46.

Table 3-114:  MALPublisherSet Constructor Parameters

| Parameter | Description |
| --- | --- |
| providerSet | MALProviderSet that created this MALPublisherSet |
| op | PUBLISH-SUBSCRIBE operation |
| domain | Domain of the PUBLISH messages |
| networkZone | Network zone of the PUBLISH messages |
| sessionType | Session type of the PUBLISH messages |
| sessionName | Session name of the PUBLISH messages |
| remotePublisherQos | QoS level of the PUBLISH messages |
| remotePublisherQosProps | QoS properties of the PUBLISH messages |
| remotePublisherPriority | Priority of the PUBLISH messages |

If the parameters ‘providerSet’ or ‘domain’ or ‘networkZone’ or ‘sessionType’ or ‘sessionName’ are NULL then an IllegalArgumentException shall be raised.

The parameters ‘remotePublisherQos’, ‘remotePublisherQosProps’ and ‘remotePublisherPriority’ may be NULL.

#### Create a MALPublisher

A method ‘createPublisher’ shall be defined in order to create a MALPublisher and add it to this MALPublisherSet.

The method signature shall be:

void createPublisher(MALProvider provider)

throws java.lang.IllegalArgumentException, MALException

The method ‘createPublisher’ parameter shall be assigned as described in table 3-100.

Table 3-115:  MALPublisherSet ‘createPublisher’ Parameter

| Parameter | Description |
| --- | --- |
| provider | MALProvider to be used in order to create the MALPublisher |

If the parameter ‘provider’ is NULL then an IllegalArgumentException shall be raised.

If a MALException occurs then it shall be raised again.

#### Delete a MALPublisher

A method ‘deletePublisher’ shall be defined in order to close a MALPublisher and remove it from this MALPublisherSet.

The method signature shall be:

void deletePublisher(MALProvider provider)

throws java.lang.IllegalArgumentException, MALException

The method ‘deletePublisher’ parameter shall be assigned as described in table 3-100.

Table 3-116:  MALPublisherSet ‘deletePublisher’ Parameter

| Parameter | Description |
| --- | --- |
| provider | MALProvider used to create the MALPublisher to remove |

If the parameter ‘provider’ is NULL then an IllegalArgumentException shall be raised.

If no MALPublisher has been created with the specified MALProvider then the method shall return void, i.e., no MALException shall be raised.

If a MALPublisher has been created with the specified MALProvider then the MALPublisher shall be closed and removed from this MALPublisherSet.

If a MALException occurs then it shall be raised again.

#### Publish Updates

A method ‘publish’ shall be defined in order to publish updates through all the MALPublishers of this MALPublisherSet.

The method signature shall be:

public MALMessage publish(UpdateHeaderList updateHeaderList,

java.util.List… updateLists)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

The ‘publish’ parameters shall be assigned as described in table 3-102.

Table 3-117:  MALPublisherSet ‘publish’ Parameters

| Parameter | Description |
| --- | --- |
| updateHeaderList | Published UpdateHeaders |
| updateLists | Lists of updates to be published |

Each MALPublisher shall be sequentially invoked through the method ‘publish’.

If a MALException or MALInteractionException occurs then it shall be immediately raised again by this method.

#### Register

A method ‘register’ shall be defined in order to synchronously register through all the MALPublishers of this MALPublisherSet.

The method signature shall be:

public void register(EntityKeyList entityKeys,

MALPublishInteractionListener listener)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

NOTE	–	The ‘register’ parameters shall be assigned as described in table 3-103.

Table 3-118:  MALPublisherSet ‘register’ Parameters

| Parameter | Description |
| --- | --- |
| entityKeyList | Keys of the entities that are to be published |
| listener | Listener in charge of receiving the messages PUBLISH ERROR |

Each MALPublisher shall be sequentially invoked through the method ‘register’.

If a MALException or MALInteractionException occurs then it shall be immediately raised again by this method.

#### Deregister

A method ‘deregister’ shall be defined in order to synchronously deregister through all the MALPublishers of this MALPublisherSet.

The method signature shall be:

public void deregister() throws MALInteractionException, MALException

Each MALPublisher shall be sequentially invoked through the method ‘deregister’.

If a MALException or MALInteractionException occurs then it shall be immediately raised again by this method.

#### Asynchronous Register

A method ‘asyncRegister’ shall be defined in order to asynchronously register through all the MALPublishers of this MALPublisherSet.

The method signature shall be:

public MALMessage asyncRegister(EntityKeyList entityKeys,

MALPublishInteractionListener listener)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

NOTE	–	The ‘asyncRegister’ parameters shall be assigned as described in table 3-104.

Table 3-119:  MALPublisherSet ‘asyncRegister’ Parameters

| Parameter | Description |
| --- | --- |
| entityKeyList | Keys of the entities that are to be published |
| listener | Listener in charge of receiving the messages PUBLISH REGISTER ACK, PUBLISH REGISTER ERROR and PUBLISH ERROR |

Each MALPublisher shall be sequentially invoked through the method ‘asyncRegister’.

If a MALException or MALInteractionException occurs then it shall be immediately raised again by this method.

#### Asynchronous Deregister

A method ‘asyncDeregister’ shall be defined in order to asynchronously deregister through all the MALPublishers of this MALPublisherSet.

The method signature shall be:

public MALMessage asyncDeregister(

MALPublishInteractionListener listener)

throws java.lang.IllegalArgumentException, MALInteractionException,

MALException

NOTE	–	The asyncDeregister parameter shall be assigned as described in table 3-105.

Table 3-120:  MALPublisherSet ‘asyncDeregister’ Parameter

| Parameter | Description |
| --- | --- |
| listener | Listener in charge of receiving the messages PUBLISH DEREGISTER ACK |

Each MALPublisher shall be sequentially invoked through the method ‘asyncDeregister’.

If a MALException or MALInteractionException occurs then it shall be immediately raised again by this method.

#### Close

A method ‘close’ shall be defined in order to close all the MALPublishers of this MALPublisherSet.

The method signature shall be:

public void close() throws MALException

Each MALPublisher shall be sequentially invoked through the method ‘close’.

If a MALException occurs then it shall be immediately raised again by this method.

## Broker package

### Overview

This part of the API is dedicated to the MAL clients handling PUBLISH-SUBSCRIBE interactions as brokers. The broker state diagrams are specified in reference [1].

The classes and interfaces belong to the Java package:

org.ccsds.moims.mo.mal.broker

### MALBrokerManager

#### Definition

A MALBrokerManager interface shall be defined in order to encapsulate the resources used to enable MAL brokers to handle PUBLISH-SUBSCRIBE interactions.

A MALBrokerManager shall be a MALBroker factory.

#### MALBrokerManager Creation

A MALBrokerManager shall be created by calling the method ‘createBrokerManager’ provided by MALContext.

Several MALBrokerManager instances should be created in order to separate the resources used by some brokers.

#### Create a MALBroker

Two methods ‘createBroker’ shall be defined in order to create a shared MAL level broker:

- using no parameter;

- using a MALBrokerHandler parameter.

The methods signatures shall be:

public MALBroker createBroker() throws MALException

public MALBroker createBroker(MALBrokerHandler handler)

throws java.lang.IllegalArgumentException, MALException

The ‘createBroker’ parameter shall be assigned as described in table 3-86.

Table 3-121:  MALBrokerManager ‘createBroker’ Parameter

| Parameter | Description |
| --- | --- |
| handler | Broker interaction handler |

If the parameter ‘handler’ is NULL then an IllegalArgumentException shall be raised.

The method ‘createBroker’ shall not return the value NULL.

If an error occurs then a MALException shall be raised.

If the MALBrokerManager is closed then a MALException shall be raised.

#### Create a MALBrokerBinding

Two methods ‘createBrokerBinding’ shall be defined in order to bind a shared MAL level broker to a particular transport:

- using a private MALEndpoint;

- using a shared MALEndpoint.

The methods signatures shall be:

public MALBrokerBinding createBrokerBinding(

MALBroker optionalMALBroker,

String localName,

String protocol,

Blob authenticationId,

QoSLevel[] expectedQos,

UInteger priorityLevelNumber,

Map qosProperties)

throws java.lang.IllegalArgumentException, MALException

public MALBrokerBinding createBrokerBinding(

MALBroker optionalMALBroker,

MALEndpoint endpoint,

Blob authenticationId,

QoSLevel[] expectedQos,

UInteger priorityLevelNumber,

Map qosProperties)

throws java.lang.IllegalArgumentException, MALException

The ‘createBrokerBinding’ parameters shall be assigned as described in table 3-122.

Table 3-122:  MALBrokerBinding ‘createBrokerBinding’ Parameters

| Parameter | Description |
| --- | --- |
| optionalMALBroker | MAL level broker to be bound |
| localName | Name of the private MALEndpoint to be created and used by the broker binding |
| protocol | Name of the protocol used to bind the broker |
| endpoint | Shared MALEndpoint to be used by the broker |
| authenticationId | Authentication identifier that should be used by the broker |
| expectedQos | QoS levels the broker assumes it can rely on |
| priorityLevelNumber | Number of priorities the broker uses |
| qosProperties | Default QoS properties used by the broker to send messages |

If the parameter ‘optionalMALBroker’ is NULL then a transport level broker shall be created.

The parameter ‘localName’ may be NULL.

If the parameter ‘localName’ is not NULL then its value shall be unique for the MALContext instance and the protocol specified by the parameter ‘protocol’.

The parameter ‘authenticationId’ shall only give a hint: some transports may not use this authentication identifier and assign another authentication identifier to the broker.

The parameter ‘qosProperties’ may be NULL.

If the parameters ‘protocol’ or ‘endpoint’ or ‘authenticationId’ or ‘expectedQos’ are NULL then an IllegalArgumentException shall be raised.

If the MALBrokerManager is closed then a MALException shall be raised.

If the broker binding local name is not NULL and if the broker process starts again after a stop and creates the MALBrokerBinding with the same local name (directly or through a shared MALEndpoint) then the MALBrokerBinding shall recover the same URI as before the stop.

#### Close

A method ‘close’ shall be defined in order to release the resources owned by this MALBrokerManager.

The method signature shall be:

public void close() throws MALException

The method ‘close’ shall close all the MALBrokerBindings owned by this MALBrokerManager.

The method ‘close’ shall return after all the MALBrokerBindings have been closed.

If an internal error occurs then a MALException shall be raised.

### MALBroker

#### Definition

A MALBroker interface shall be defined in order to represent a shared MAL level broker, i.e., a shared broker implemented at the MAL level.

NOTE	–	A single MALBroker instance can be bound to one or several transport layers. In this way, the MALBroker can act as a bridge between several transport layers. For instance, a MALBroker can bridge two transport layers by receiving updates from publishers through the first transport layer and notifying those updates to subscribers through the second transport layer.

#### Get Bindings

A method ‘getBindings’ shall be defined in order to return the MALBrokerBindings owned by this MALBroker.

The method signature shall be:

public MALBrokerBinding[] getBindings()

#### Close

A method ‘close’ shall be defined in order to terminate all pending interactions.

The signature shall be:

public void close() throws MALException

The method ‘close’ shall call the method ‘close’ provided by all the MALBrokerBinding owned by this MALBroker.

If an internal error occurs then a MALException shall be raised.

### MALBrokerBinding

#### Definition

A MALBrokerBinding interface shall be defined in order to represent:

- a binding of a shared MAL level broker to a transport layer;

- a transport level broker.

#### Get the URI

A method ‘getURI’ shall be defined in order to return the URI of the broker binding.

The method signature shall be:

public URI getURI()

#### Get the Authentication Identifier

A method ‘getAuthenticationId’ shall be defined in order to return the authentication identifier of the broker.

The method signature shall be:

public Blob getAuthenticationId()

The method shall return the actual authentication identifier.

NOTE	–	The method may not return the same value as the one assigned when creating the broker, that assignment being just a hint.

#### Send a NOTIFY

A method ‘sendNotify’ shall be defined in order to enable a MALBrokerHandler to send a NOTIFY message to a subscriber.

The method signature shall be:

public MALMessage sendNotify(

MALOperation operation,

URI subscriber,

Long transactionId,

IdentifierList domainId,

Identifier networkZone,

SessionType sessionType,

Identifier sessionName,

QoSLevel notifyQos,

Map notifyQosProps,

UInteger notifyPriority,

Identifier subscriptionId,

UpdateHeaderList updateHeaderList,

java.util.List... updateLists)

throws java.lang.IllegalArgumentException,

MALInteractionException, MALException

The ‘sendNotify’ parameters shall be assigned as described in table 3-122.

Table 3-123:  MALBrokerBinding ‘sendNotify’ Parameters

| Parameter | Description |
| --- | --- |
| operation | Operation of the NOTIFY message |
| subscriber | Subscriber’s URI |
| transactionId | Transaction identifier of the NOTIFY message |
| domainId | Domain of the NOTIFY message |
| networkZone | Network zone of the NOTIFY message |
| sessionType | Session type of the NOTIFY message |
| sessionName | Session name of the NOTIFY message |
| notifyQos | QoS level of the NOTIFY message |
| notifyQosProps | QoS properties of the NOTIFY message |
| notifyPriority | Priority of the NOTIFY message |
| subscriptionId | Subscription identifier |
| updateHeaderList | List of update headers |
| updateLists | Lists of updates |

If at least one of the parameters, except ‘notifyQoSProps’, is NULL then an IllegalArgumentException shall be raised.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if a non-MAL error occurs during the message sending.

If this MALBrokerBinding represents a transport level broker or is linked to a MAL level broker without MALBrokerHandler then a MALException shall be raised.

If the MALBrokerBinding is closed then a MALException shall be raised.

The method shall return the MALMessage that has been sent.

The allowed update list types shall be:

- a MAL element list;

- a List<MALEncodedElement> containing the encoded updates;

- a List defined by a specific Java mapping extension.

#### Send a NOTIFY ERROR

A method ‘sendNotifyError’ shall be defined in order to enable a MALBrokerHandler to send a NOTIFY ERROR message to a subscriber.

The method signature shall be:

public MALMessage sendNotifyError(

MALOperation operation,

URI subscriber,

Long transactionId,

IdentifierList domainId,

Identifier networkZone,

SessionType sessionType,

Identifier sessionName,

QoSLevel notifyQos,

Map notifyQosProps,

UInteger notifyPriority,

MALStandardError error)

throws java.lang.IllegalArgumentException,

MALInteractionException, MALException

The ‘sendNotifyError’ parameters shall be assigned as described in table 3-122.

Table 3-124:  MALBrokerBinding ‘sendNotifyError’ Parameters

| Parameter | Description |
| --- | --- |
| operation | Operation of the NOTIFY ERROR message |
| subscriber | Subscriber’s URI |
| transactionId | Transaction identifier of the NOTIFY ERROR message |
| domainId | Domain of the NOTIFY ERROR message |
| networkZone | Network zone of the NOTIFY ERROR message |
| sessionType | Session type of the NOTIFY ERROR message |
| sessionName | Session name of the NOTIFY ERROR message |
| notifyQos | QoS level of the NOTIFY ERROR message |
| notifyQosProps | QoS properties of the NOTIFY ERROR message |
| notifyPriority | Priority of the NOTIFY ERROR message |
| error | Body of the NOTIFY ERROR Error message |

If at least one of the parameters, except ‘notifyQoSProps’, is NULL then an IllegalArgumentException shall be raised.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if a  non-MAL error occurs during the message sending.

If this MALBrokerBinding represents a transport level broker or is linked to a MAL level broker without MALBrokerHandler then a MALException shall be raised.

If the MALBrokerBinding is closed then a MALException shall be raised.

The method shall return the MALMessage that has been sent.

#### Send a PUBLISH ERROR

A method ‘sendPublishError’ shall be defined in order to enable a MALBrokerHandler to send a PUBLISH ERROR message to a publisher.

The method signature shall be:

public MALMessage sendPublishError(

MALOperation operation,

URI publisher,

Long transactionId,

IdentifierList domainId,

Identifier networkZone,

SessionType sessionType,

Identifier sessionName,

QoSLevel qos,

Map qosProps,

UInteger priority,

MALStandardError error)

throws java.lang.IllegalArgumentException,

MALInteractionException, MALException

The ‘sendPublishError’ parameters shall be assigned as described in table 3-122.

Table 3-125:  MALBrokerBinding ‘sendPublishError’ Parameters

| Parameter | Description |
| --- | --- |
| operation | Operation of the PUBLISH ERROR message |
| publisher | Publisher’s URI |
| transactionId | Transaction identifier of the PUBLISH ERROR message |
| domainId | Domain of the PUBLISH ERROR message |
| networkZone | Network zone of the PUBLISH ERROR message |
| sessionType | Session type of the PUBLISH ERROR message |
| sessionName | Session name of the PUBLISH ERROR message |
| qos | QoS level of the PUBLISH ERROR message |
| notifyQoSProps | QoS properties of the PUBLISH ERROR message |
| notifyPriority | Priority of the PUBLISH ERROR message |
| error | Body of the PUBLISH ERROR message |

If at least one of the parameters, except ‘qosProps’, is NULL then an IllegalArgumentException shall be raised.

A MALInteractionException shall be thrown if a MAL standard error occurs during the initiation message sending.

A MALException shall be thrown if a non-MAL error occurs during the message sending.

If this MALBrokerBinding represents a transport level broker or a MAL level broker without MALBrokerHandler then a MALException shall be raised.

If the MALBrokerBinding is closed then a MALException shall be raised.

The method shall return the MALMessage that has been sent.

#### Close

A method ‘close’ shall be defined in order to terminate all pending interactions and deactivate the broker binding.

The method signature shall be:

public void close() throws MALException

A close should be called by a MAL client before the broker process is stopped for any operational reason.

The method ‘close’ shall deactivate this MALBrokerBinding.

If the MALBroker is being activated at the time of the close then the closing process shall wait for the end of the broker’s execution.

Once a MALBrokerBinding has been closed, the message delivery shall be stopped in order that the broker will not receive any message through this MALBrokerBinding.

If an internal error occurs then a MALException shall be raised.

Pending interactions shall be finalized by returning the error DESTINATION_LOST_OR_DIED to the subscribers or publishers.

If a subscriber or a publisher tries to interact with a closed broker binding and if the QoS level is not QUEUED, a DELIVERY_FAILED shall be returned to the subscriber or publisher.

If a subscriber or a publisher tries to interact with a closed broker binding and if the QoS level is QUEUED, then the request shall be queued and delivered as soon as the broker binding message delivery is started again.

If the broker binding owns a private MALEndpoint then the MALEndpoint shall be closed.

### MALBrokerHandler

#### Definition

A MALBrokerHandler interface shall be defined in order to enable to handle the interactions on the broker side.

The MALBrokerHandler interface shall handle the following PUBLISH-SUBSCRIBE interaction stages: REGISTER, PUBLISH REGISTER, PUBLISH, DEREGISTER and PUBLISH DEREGISTER.

#### Initialize

A method ‘malInitialize’ shall be defined in order to enable a MALBrokerHandler to be initialized when the broker is activated.

The method signature shall be:

public void malInitialize(MALBrokerBinding brokerBinding)

The method ‘malInitialize’ parameter shall be assigned as described in table 3-88.

Table 3-126:  MALBrokerHandler ‘malInitialize’ Parameter

| Parameter | Description |
| --- | --- |
| brokerBinding | Created MALBrokerBinding |

The method ‘malInitialize’ shall be called when the method ‘createBrokerBinding’ provided by the interface MALBrokerManager is called.

NOTE	–	The method ‘malInitialize’ enables the handler to store the reference of the MALBrokerBinding in order to send NOTIFY, NOTIFY ERROR and PUBLISH ERROR messages.

If an instance of MALBrokerHandler is used by several MALBrokerBinding then the method ‘malInitialize’ shall be called once for each MALBrokerBinding.

#### Handle the REGISTER stage

A method ‘handleRegister’ shall be defined in order to handle the REGISTER stage of a PUBLISH-SUBSCRIBE interaction.

The method ‘handleRegister’ signature shall be:

public void handleRegister(MALInteraction interaction,

MALRegisterBody body)

throws MALInteractionException, MALException

The method ‘handleRegister’ parameters shall be assigned as described in table 3-89.

Table 3-127:  MALBrokerHandler ‘handleRegister’ Parameters

| Parameter | Description |
| --- | --- |
| interaction | Interaction context |
| body | Body of the REGISTER message to handle |

The parameters ‘interaction’ and ‘body’ shall not be NULL.

A REGISTER ACK message shall be sent to the subscriber when the method returns.

If a MAL standard error occurs then a MALInteractionException shall be raised.

If a non-MAL error occurs then a MALException shall be raised.

If a MALInteractionException is raised then a REGISTER ERROR message shall be sent to the subscriber.

#### Handle the PUBLISH REGISTER stage

A method ‘handlePublishRegister’ shall be defined in order to handle the PUBLISH REGISTER stage of a PUBLISH-SUBSCRIBE interaction.

The method ‘handlePublishRegister’ signature shall be:

public void handlePublishRegister(MALInteraction interaction,

MALPublishRegisterBody body)

throws MALInteractionException, MALException

The method ‘handlePublishRegister’ parameters shall be assigned as described in table 3-89.

Table 3-128:  MALBrokerHandler ‘handlePublishRegister’ Parameters

| Parameter | Description |
| --- | --- |
| interaction | Interaction context |
| body | Body of the PUBLISH REGISTER message to handle |

The parameters ‘interaction’ and ‘body’ shall not be NULL.

A PUBLISH REGISTER ACK message shall be sent to the subscriber when the method returns.

If a MAL standard error occurs then a MALInteractionException shall be raised.

If a non-MAL error occurs then a MALException shall be raised.

If a MALInteractionException is raised then a PUBLISH REGISTER ERROR message shall be sent to the subscriber.

#### Handle the PUBLISH stage

A method ‘handlePublish’ shall be defined in order to handle the PUBLISH stage of a PUBLISH-SUBSCRIBE interaction.

The method ‘handlePublish’ signature shall be:

public void handlePublish(MALInteraction interaction,

MALPublishBody body)

throws MALInteractionException, MALException

The method ‘handlePublish’ parameters shall be assigned as described in table 3-89.

Table 3-129:  MALBrokerHandler ‘handlePublish’ Parameters

| Parameter | Description |
| --- | --- |
| interaction | Interaction context |
| body | Body of the PUBLISH message to handle |

The parameters ‘interaction’ and ‘body’ shall not be NULL.

If a MAL standard error occurs then a message PUBLISH ERROR shall be sent through the MALBrokerBinding which URI is equal to the field ‘URI to’ of the PUBLISH message.

If a non-MAL error occurs then a MALException shall be raised.

#### Handle the DEREGISTER stage

A method ‘handleDeregister’ shall be defined in order to handle the DEREGISTER stage of a PUBLISH-SUBSCRIBE interaction.

The method ‘handleDeregister’ signature shall be:

public void handleDeregister(MALInteraction interaction,

MALDeregisterBody body)

throws MALInteractionException, MALException

The method ‘handleDeregister’ parameters shall be assigned as described in table 3-89.

Table 3-130:  MALBrokerHandler ‘handleDeregister’ Parameters

| Parameter | Description |
| --- | --- |
| interaction | Interaction context |
| body | Body of the DEREGISTER message to handle |

The parameters ‘interaction’ and ‘body’ shall not be NULL.

A DEREGISTER ACK message shall be sent to the subscriber when the method returns.

If a non-MAL error occurs then a MALException shall be raised.

#### Handle the PUBLISH DEREGISTER stage

A method ‘handlePublishDeregister’ shall be defined in order to handle the PUBLISH DEREGISTER stage of a PUBLISH-SUBSCRIBE interaction.

The method ‘handlePublishDeregister’ signature shall be:

public void handlePublishDeregister(MALInteraction interaction)

throws MALInteractionException, MALException

The method ‘handlePublishDeregister’ parameters shall be assigned as described in table 3-89.

Table 3-131:  MALBrokerHandler ‘handlePublishDeregister’ Parameters

| Parameter | Description |
| --- | --- |
| interaction | Interaction context |

The parameter ‘interaction’ shall not be NULL.

A PUBLISH DEREGISTER ACK message shall be sent to the subscriber when the method returns.

If a non-MAL error occurs then a MALException shall be raised.

#### Finalize

A method ‘malFinalize’ shall be defined in order to enable a MALBrokerHandler to be notified when a MALBrokerBinding is closed.

The method signature shall be:

public void malFinalize(MALBrokerBinding brokerBinding)

The method ‘malFinalize’ parameter shall be assigned as described in table 3-94.

Table 3-132:  MALBrokerHandler ‘malFinalize’ Parameter

| Parameter | Description |
| --- | --- |
| brokerBinding | Closed MALBrokerBinding |

The method ‘malFinalize’ shall be called when the method ‘close’ provided by the interface MALBrokerBinding is called.

# Service Mapping

## Overview

This section explains how to map a service specification (reference [1]) to Java. Two aspects are handled here:

- the definition of the interfaces used by a consumer/provider to use/provide a service;

- the way of implementing those interfaces.

This section uses Java code templates. The template variables are related to the MAL XML Schema, i.e., each variable is linked to an XPath enabling to unambiguously resolve the values to be assigned to this variable when applying the template.

## Definition

The values of the variables used in the Java code templates shall be resolved according to the table Erreur ! Source du renvoi introuvable.and the following rules:

- the default namespace shall be http://www.ccsds.org/schema/ServiceSchema;

- the default current XPath context shall be the element “specification”;

- each variable shall be assigned with the value specified by the XPath;

- in the context of the parent of the element specified by the XPath, several values may be assigned to a variable;

- if the last column mentions “Attribute value” then the value of the specified XML attribute shall be assigned;

- if the last column contains a value in inverted commas then this value shall be assigned;

- if the last column mentions “Java class mapped from type” then the name of the Java class mapped from the specified XML element ‘type’ shall be assigned;

- if the last column mentions “Type absolute short form” then the value shall depend on the type specified by the XML element ‘type’ as follows:

- if the type is concrete then the absolute short form shall be assigned;

- if the type is abstract then the value NULL shall be assigned.

- if the last column mentions “Mapping extension” then the class name “Object” shall be assigned unless a specific Java mapping extension is defined for the specified namespace <<extension>>.

Table 4-1:  Service Mapping Variables

| Variable name | Current context | Element or attribute | Value |
| --- | --- | --- | --- |
| ack | area/service/ capabilitySet | invokeIP/ acknowledgement/ type | Java class mapped from type |
|  |  | progressIP/ acknowledgement/ type | Java class mapped from type |
|  |  | invokeIP/ acknowledgement/ <<extension>>:* | Mapping extension |
|  |  | progressIP/ acknowledgement/ <<extension>>:* | Mapping extension |
| ack short form | area/service/ capabilitySet | invokeIP/ acknowledgement/ type | Type absolute short form |
|  |  | progressIP/ acknowledgement/ type | Type absolute short form |
| area | . | area/@name | Attribute value |
| area number | . | area/@number | Attribute value |
| composite | .//dataType | composite/@name | Attribute value |
| composite parent class | .//dataType/ composite/extends | type | Java class mapped from type |
| composite field name | .//dataType/ composite | field/@name | Attribute value |
| composite field class | .//dataType/ composite/field | type | Java class mapped from type |
| enumeration | .//dataType | enumeration@name | Attribute value |
| enum item | .//dataType/ enumeration | item/@value | Attribute value |
| enum item ordinal | .//dataType/ enumeration | item/@shortForm | Attribute value |
| error | .//errors | error/@name | Attribute value |
| error number | .//errors | error/@number | Attribute value |
| in | area/service/ capabilitySet | sendIP/send/type | Java class mapped from type |
|  |  | submitIP/submit/type | Java class mapped from type |
|  |  | requestIP/request/type | Java class mapped from type |
|  |  | invokeIP/invoke/type | Java class mapped from type |
|  |  | progressIP/progress/type | Java class mapped from type |
|  |  | sendIP/send/ <<extension>>:* | Mapping extension |
|  |  | submitIP/submit/ <<extension>>:* | Mapping extension |
|  |  | requestIP/request/ <<extension>>:* | Mapping extension |
|  |  | invokeIP/invoke/ <<extension>>:* | Mapping extension |
|  |  | progressIP/progress/ <<extension>>:* | Mapping extension |
| in short form | area/service/ capabilitySet | sendIP/send/type | Type absolute short form |
|  |  | submitIP/submit/type | Type absolute short form |
|  |  | requestIP/request/type | Type absolute short form |
|  |  | invokeIP/invoke/type | Type absolute short form |
|  |  | progressIP/progress/type | Type absolute short form |
| list | .//dataType | list/@name | Attribute value |
| list element class | .//dataType/list | type | Java class mapped from type |
| notify | area/service/ capabilitySet | pubsubIP/publishNotify/ type | Java class mapped from type |
| notify short form | area/service/ capabilitySet | pubsubIP/publishNotify/ type | Type absolute short form |
| op | area/service/ capabilitySet | sendIP/@name | Attribute value |
|  |  | submitIP/@name | Attribute value |
|  |  | requestIP/@name | Attribute value |
|  |  | invokeIP/@name | Attribute value |
|  |  | progressIP/@name | Attribute value |
|  |  | pubsubIP/@name | Attribute value |
| op ip | area/service/ capabilitySet | sendIP | “SEND” |
|  |  | submitIP | “SUBMIT” |
|  |  | requestIP | “REQUEST” |
|  |  | invokeIP | “INVOKE” |
|  |  | progressIP | “PROGRESS” |
|  |  | pubsubIP | “PUBLISH-SUBSCRIBE” |
| op number | area/service/ capabilitySet | sendIP/@number | Attribute value |
|  |  | submitIP/@number | Attribute value |
|  |  | requestIP/@number | Attribute value |
|  |  | invokeIP/@number | Attribute value |
|  |  | progressIP/@number | Attribute value |
|  |  | pubsubIP/@number | Attribute value |
| op replayable | area/service/ capabilitySet | sendIP/@supportInReplay | Attribute value |
|  |  | submitIP/@supportInReplay | Attribute value |
|  |  | requestIP/@supportInReplay | Attribute value |
|  |  | invokeIP/@supportInReplay | Attribute value |
|  |  | progressIP/@supportInReplay | Attribute value |
|  |  | pubsubIP/@supportInReplay | Attribute value |
| res | area/service/ capabilitySet | requestIP/response/type | Java class mapped from type |
|  |  | invokeIP/response/type | Java class mapped from type |
|  |  | progressIP/response/type | Java class mapped from type |
|  |  | requestIP/response/ <<extension>>:* | Mapping extension |
|  |  | invokeIP/response/ <<extension>>:* | Mapping extension |
|  |  | progressIP/response/ <<extension>>:* | Mapping extension |
| res | area/service/ capabilitySet | requestIP/response/type | Type absolute short form |
|  |  | invokeIP/response/type | Type absolute short form |
|  |  | progressIP/response/type | Type absolute short form |
| service | area | service/@name | Attribute value |
| service number | area | service/@number | Attribute value |
| short form | .//dataType | composite/@shortForm | Attribute value |
|  |  | enumeration/@shortForm | Attribute value |
|  |  | list/@shortForm | Attribute value |
| update | area/service/ capabilitySet | progressIP/update/type | Java class mapped from type |
|  |  | progressIP/update/ <<extension>>:* | Mapping extension |
| update short form | area/service/ capabilitySet | progressIP/update/type | Type absolute short form |

A Java package root name shall be defined for each service area.

NOTE	–	For example the package root name can be:

org.ccsds.moims.mo

The Java package root name shall be unique in the Java package namespace.

The Java package root name may contain a service version number in order to enable to launch several versions of the same service in a process.

The package root name shall be assigned to the code template variable “root name”.

The following packages shall be defined:

<<root name>>.<<!area!>>

<<root name>>.<<!area!>>.structures

<<root name>>.<<!area!>>.structures.factory

<<root name>>.<<!area!>>.<<!service!>>

<<root name>>.<<!area!>>.<<!service!>>.body

<<root name>>.<<!area!>>.<<!service!>>.consumer

<<root name>>.<<!area!>>.<<!service!>>.provider

<<root name>>.<<!area!>>.<<!service!>>.structures

<<root name>>.<<!area!>>.<<!service!>>.structures.factory

For each area, the classes indicated in table 4-2 shall be created.

Table 4-2:  Area Classes

| Package name | Content |
| --- | --- |
| <<root name>>.<<!area!>> | Area helper class |
| <<root name>>.<<!area!>>.structures | Data structures classes: enumerations, lists and other composites |
| <<root name>>.<<!area!>>.structures.factory | MALElementFactory classes |

For each service, the classes and interfaces indicated in table 4-3 shall be created.

Table 4-3:  Service Classes

| Package name | Content |
| --- | --- |
| <<root name>>.<<!area!>>.<<!service!>> | Service helper class |
| <<root name>>.<<!area!>>.<<!service!>>.consumer | Stub interface Adapter class Stub implementation class |
| <<root name>>.<<!area!>>.<<!service!>>.provider | Handler interface Skeleton interface Publisher classes Interaction classes Skeleton implementation classes (inheritance and delegation models) |
| <<root name>>.<<!area!>>.<<!service!>>.structures | Data structures classes: enumerations, lists and other composite types |
| <<root name>>.<<!area!>>.<<!service!>>.structures.factory | MALElementFactory classes |
| <<root name>>.<<!area!>>.<<!service!>>.body | Multiple element body classes |

## Consumer

### General

Figure 4-1 is a class diagram that describes the relationships between the stub classes and interfaces at the consumer side. The following classes or interfaces are defined:

- <<Service>> is the stub interface;

- <<Service>>Stub is the stub implementation;

- <<Service>>Adapter is the specific adapter class.

Figure 4-1:  Relationships between the Stub Classes and Interfaces

### Stub Interface

#### Definition

A Stub interface shall be defined in order to initiate interaction patterns through service specific methods.

The name of the interface shall be: <<Service>>.

#### Consumer Getter

A method shall be defined in order to get the reference of the MALConsumer.

The method signature shall be:

public MALConsumer getConsumer()

#### SEND Operation Invocation

A method <<op>> shall be defined for each SEND operation provided by the service.

The signature of the method <<op>> shall be:

public MALMessage <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>)

throws MALInteractionException, MALException

#### SUBMIT Operation Synchronous Invocation

A method <<op>> shall be defined for each SUBMIT operation provided by the service.

The signature of the method <<op>> shall be:

public void <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>)

throws MALInteractionException, MALException

#### REQUEST Operation Synchronous Invocation

A method <<op>> shall be defined for each REQUEST operation provided by the service.

If the RESPONSE message body is empty then the signature of the method <<op>> shall be:

public void <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>)

throws MALInteractionException, MALException

If the RESPONSE message body contains one element then the signature of the method <<op>> shall be:

public <<Res [1]>> <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>)

throws MALInteractionException, MALException

If the RESPONSE message body contains more than one element then the signature of the method <<op>> shall be:

public <<Op>>Response <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>)

throws MALInteractionException, MALException

#### INVOKE Operation Synchronous Invocation

A method <<op>> shall be defined for each INVOKE operation provided by the service.

If the ACK message body is empty then the signature of the method <<op>> shall be:

public void <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

<<Service>>Adapter adapter) throws MALInteractionException, MALException

If the ACK message body contains one element then the signature of the method <<op>> shall be:

public <<Ack [1]>> <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

<<Service>>Adapter adapter) throws MALInteractionException, MALException

If the ACK message body contains more than one element then the signature of the method <<op>> shall be:

public <<Op>>Ack <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

<<Service>>Adapter adapter) throws MALInteractionException, MALException

#### PROGRESS Operation Synchronous Invocation

A method <<op>> shall be defined for each PROGRESS operation provided by the service.

If the ACK message body is empty then the signature of the method <<op>> shall be:

public void <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

<<Service>>Adapter adapter) throws MALInteractionException, MALException

If the ACK message body contains one element then the signature of the method <<op>> shall be:

public <<Ack [1]>> <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

<<Service>>Adapter adapter) throws MALInteractionException, MALException

If the ACK message body contains more than one element then the signature of the method <<op>> shall be:

public <<Op>>Ack <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

<<Service>>Adapter adapter) throws MALInteractionException, MALException

#### PUBLISH-SUBSCRIBE Operation REGISTER Synchronous Invocation

A method <<op>>Register shall be defined for each PUBLISH-SUBSCRIBE operation provided by the service.

The signature of the method <<op>>Register shall be:

public void <<op>>Register(Subscription subscription,

<<Service>>Adapter adapter) throws MALInteractionException, MALException

#### PUBLISH-SUBSCRIBE Operation DEREGISTER Synchronous Invocation

A method <<op>>Deregister shall be defined for each PUBLISH-SUBSCRIBE operation provided by the service.

The signature of the method <<op>>Deregister shall be:

public void <<op>>Deregister(IdentifierList subscriptionIdList)

throws MALInteractionException, MALException

#### SUBMIT Operation Asynchronous Invocation

A method async<<Op>> shall be defined for each SUBMIT operation provided by the service.

The signature of the method async<<Op>> shall be:

public MALMessage async<<Op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

<<Service>>Adapter adapter) throws MALInteractionException, MALException

#### REQUEST Operation Asynchronous Invocation

A method async<<Op>> shall be defined for each REQUEST operation provided by the service.

The signature of the method async<<Op>> shall be:

public MALMessage async<<Op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

<<Service>>Adapter adapter) throws MALInteractionException, MALException

#### INVOKE Operation Asynchronous Invocation

A method async<<Op>> shall be defined for each INVOKE operation provided by the service.

The signature of the method async<<Op>> shall be:

public MALMessage async<<Op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

<<Service>>Adapter adapter) throws MALInteractionException, MALException

#### PROGRESS Operation Asynchronous Invocation

A method async<<Op>> shall be defined for each PROGRESS operation provided by the service.

The signature of the method async<<Op>> shall be:

public MALMessage async<<Op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

<<Service>>Adapter adapter) throws MALInteractionException, MALException

#### PUBLISH-SUBSCRIBE Operation REGISTER Asynchronous Invocation

A method async<<Op>>Register shall be defined for each PUBLISH-SUBSCRIBE operation provided by the service.

The signature of the method async<<Op>>Register shall be:

public MALMessage async<<Op>>Register(Subscription subscription,

<<Service>>Adapter adapter) throws MALInteractionException, MALException

#### PUBLISH-SUBSCRIBE Operation DEREGISTER Asynchronous Invocation

A method async<<Op>>Deregister shall be defined for each PUBLISH-SUBSCRIBE operation provided by the service.

The signature of the method async<<Op>>Deregister shall be:

public MALMessage async<<Op>>Deregister(IdentifierList subscriptionIdList,

<<Service>>Adapter adapter) throws MALInteractionException, MALException

#### Continue an Interaction

A method ‘continue<<Op>>’ shall be defined for each SUBMIT, REQUEST, INVOKE and PROGRESS operation provided by the service.

The method signature shall be:

public void continue<<Op>>(UOctet lastInteractionStage,

Time initiationTimestamp, Long transactionId, <<Service>>Adapter adapter)

throws MALInteractionException, MALException

### Stub adapter class

#### Definition

A Stub adapter class shall be defined in order to specialize the MALInteractionAdapter methods according to the specific operations provided by the service.

The name of the class shall be: <<Service>>Adapter.

The Stub adapter class shall be abstract.

The Stub adapter class shall extend the class MALInteractionAdapter and define one specific adapter method for each operation and message type.

The Stub adapter class shall redefine each method provided by MALInteractionAdapter in order to call the specific adapter method according to the operation.

When the parameter 'body' is typed MALMessageBody, the body elements shall be extracted by calling the method 'getBodyElement'.

When the parameter 'body' is typed MALErrorBody, the body element shall be the MALStandardError extracted by calling the method 'getError'.

When getting a body element from a MALMessageBody, the Stub adapter class shall pass an instance of the element if the type is concrete, i.e., if there is no polymorphism; otherwise the Stub adapter class shall pass the value NULL.

The Stub adapter class shall convert the body elements typed Union into their Java type when calling the specific adapter method.

If the operation specified by the header is not defined by the service then a MALException shall be raised except if the IP is PUBLISH-SUBSCRIBE and the stage is NOTIFY.

#### SUBMIT ACK Adapter Method

The method ‘submitAckReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>AckReceived’ with the parameters ‘header’ and ‘qosProperties’.

#### SUBMIT ERROR Adapter Method

The method ‘submitErrorReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>ErrorReceived’ with the parameters ‘header’, the MALStandardError and ‘qosProperties’.

#### REQUEST RESPONSE Adapter Method

The method ‘requestResponseReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>ResponseReceived’ with the parameters ‘header’, the body elements and ‘qosProperties’.

#### REQUEST ERROR Adapter Method

The method ‘requestErrorReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>ErrorReceived’ with the parameters ‘header’, the MALStandardError and ‘qosProperties’.

#### INVOKE ACK Adapter Method

The method ‘invokeAckReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>AckReceived’ with the parameters ‘header’, the body elements and ‘qosProperties’.

#### INVOKE ACK ERROR Adapter Method

The method ‘invokeAckErrorReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>AckErrorReceived’ with the parameters ‘header’, the MALStandardError and ‘qosProperties’.

#### INVOKE RESPONSE Adapter Method

The method ‘invokeResponseReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>ResponseReceived’ with the parameters ‘header’, the body elements and ‘qosProperties’.

#### INVOKE RESPONSE ERROR Adapter Method

The method ‘invokeResponseErrorReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>ResponseErrorReceived’ with the parameters ‘header’, the MALStandardError and ‘qosProperties’.

#### PROGRESS ACK Adapter Method

The method ‘progressAckReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>AckReceived’ with the parameters ‘header’, the body elements and ‘qosProperties’.

#### PROGRESS ACK ERROR Adapter Method

The method ‘progressAckErrorReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>AckErrorReceived’ with the parameters ‘header’, the MALStandardError and ‘qosProperties’.

#### PROGRESS UPDATE Adapter Method

The method ‘progressUpdateReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>UpdateReceived’ with the parameters ‘header’, the body elements and ‘qosProperties’.

#### PROGRESS UPDATE ERROR Adapter Method

The method ‘progressUpdateErrorReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>UpdateErrorReceived’ with the parameters ‘header’, the MALStandardError and ‘qosProperties’.

#### PROGRESS RESPONSE Adapter Method

The method ‘progressResponseReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>ResponseReceived’ with the parameters ‘header’, the body elements and ‘qosProperties’.

#### PROGRESS RESPONSE ERROR Adapter Method

The method ‘progressResponseErrorReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>ResponseErrorReceived’ with the parameters ‘header’, the MALStandardError and ‘qosProperties’.

#### REGISTER ACK Adapter Method

The method ‘registerAckReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>RegisterAckReceived’ with the parameter ‘header’ and ‘qosProperties’.

#### REGISTER ERROR Adapter Method

The method ‘registerErrorReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>RegisterErrorReceived’ with the parameters ‘header’, the MALStandardError and ‘qosProperties’.

#### NOTIFY Adapter Method

The method ‘notifyReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>NotifyReceived’ with the parameters ‘header’, ‘subscriptionId’, ‘updateHeaderList’, the multiple update lists (<<Notify [i]>>List, ... <<Notify [N]>>List) and ‘qosProperties’.

If the area and service specified by the header are not the same as the area and service this adapter belongs to then the method ‘notifyReceivedFromOtherService’ shall be called with parameters ‘header’, ‘body’ and ‘qosProperties’.

#### NOTIFY ERROR Adapter Method

The method ‘notifyErrorReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>NotifyErrorReceived’ with the parameters ‘header’, the MALStandardError and ‘qosProperties’.

#### DEREGISTER ACK Adapter Method

The method ‘deregisterAckReceived’ inherited from MALInteractionAdapter shall be redefined by calling the specific adapter method ‘<<op>>DeregisterAckReceived’ with the parameter ‘header’ and ‘qosProperties’.

#### Specific SUBMIT Adapter Methods

For each SUBMIT operation two specific adapter methods shall be defined:

- <<op>>AckReceived;

- <<op>>ErrorReceived.

The ‘<<op>>AcknowledgementReceived’ signature shall be:

public void <<op>>AckReceived(MALMessageHeader header,

java.util.Map qosProperties)

The ‘<<op>>ErrorReceived’ signature shall be:

public void <<op>>ErrorReceived(MALMessageHeader header,

MALStandardError error, java.util.Map qosProperties)

#### Specific REQUEST Adapter Methods

For each REQUEST operation two specific adapter methods shall be defined:

- <<op>>ResponseReceived;

- <<op>>ErrorReceived.

The ‘<<op>>ResponseReceived’ signature shall be defined according to the RESPONSE message body:

- If it is empty the signature shall be:

public void <<op>>ResponseReceived(MALMessageHeader header,

java.util.Map qosProperties)

- Else the signature shall be:

public void <<op>>ResponseReceived(MALMessageHeader header,

<<Res [i]>> res<<i>>, ... <<Res [N]>> res<<N>>,

java.util.Map qosProperties)

The ‘<<op>>ErrorReceived signature shall be:

public void <<op>>ErrorReceived(MALMessageHeader header,

MALStandardError error, java.util.Map qosProperties)

#### Specific INVOKE Adapter Methods

For each INVOKE operation three specific adapter methods shall be defined:

- <<op>>AckReceived;

- <<op>>AckErrorReceived;

- <<op>>ResponseReceived;

- <<op>>ReponseErrorReceived.

The ‘<<op>>AckReceived’ signature shall be defined according to the ACK message body:

- if it is empty the signature shall be:

public void <<op>>AckReceived(MALMessageHeader header,

java.util.Map qosProperties)

- else the signature shall be:

public void <<op>>AckReceived(MALMessageHeader header,

<<Ack [i]>> ack<<i>>, ... <<Ack [N]>> ack<<N>>,

java.util.Map qosProperties )

The ‘<<op>>AckErrorReceived’ signature shall be:

public void <<op>>AckErrorReceived(MALMessageHeader header,

MALStandardError error, java.util.Map qosProperties)

The ‘<<op>>ResponseReceived’ signature shall be defined according to the RESPONSE message body:

- if it is empty the signature shall be:

public void <<op>>ResponseReceived(MALMessageHeader header,

java.util.Map qosProperties)

- else the signature shall be:

public void <<op>>ResponseReceived(MALMessageHeader header,

<<Res [i]>> res<<i>>, ... <<Res [N]>> res<<N>>,

java.util.Map qosProperties)

The ‘<<op>>ResponseErrorReceived’ signature shall be:

public void <<op>>ResponseErrorReceived(MALMessageHeader header,

MALStandardError error, java.util.Map qosProperties)

#### Specific PROGRESS Adapter Methods

For each PROGRESS operation four specific adapter methods shall be defined:

- <<op>>AckReceived;

- <<op>>AckErrorReceived;

- <<op>>UpdateReceived;

- <<op>>UpdateErrorReceived;

- <<op>>ResponseReceived;

- <<op>>ResponseErrorReceived.

The ‘<<op>>AckReceived’ signature shall be defined according to the ACK message body:

- if it is empty the signature shall be:

public void <<op>>AckReceived(MALMessageHeader header,

java.util.Map qosProperties)

- else the signature shall be:

public void <<op>>AckReceived (MALMessageHeader header,

Ack [i]>> ack<<i>>, ... <<Ack [N]>> ack<<N>>,

java.util.Map qosProperties)

The ‘<<op>>AckErrorReceived’ signature shall be:

public void <<op>>AckErrorReceived(MALMessageHeader header,

MALStandardError error)

The ‘<<op>>UpdateReceived’ signature shall be defined according to the UPDATE message body:

- if it is empty the signature shall be:

public void <<op>>UpdateReceived(MALMessageHeader header,

java.util.Map qosProperties)

- else the signature shall be:

public void <<op>>UpdateReceived(MALMessageHeader header,

<<Update [i]>> update<<i>>, ... <<Update [N]>> update<<N>>,

java.util.Map qosProperties)

The ‘<<op>>UpdateErrorReceived’ signature shall be:

public void <<op>>UpdateErrorReceived(MALMessageHeader header,

MALStandardError error, java.util.Map qosProperties)

The ‘<<op>>ResponseReceived’ signature shall be defined according to the RESPONSE message body:

- if it is empty the signature shall be:

public void <<op>>ResponseReceived(MALMessageHeader header,

java.util.Map qosProperties)

- else the signature shall be:

public void <<op>>ResponseReceived(MALMessageHeader header,

<<Res [i]>> res<<i>>, ... <<Res [N]>> res<<N>>,

java.util.Map qosProperties)

The ‘<<op>>ResponseErrorReceived’ signature shall be:

public void <<op>>ResponseErrorReceived(MALMessageHeader header,

MALStandardError error, java.util.Map qosProperties)

#### Specific PUBLISH-SUBSCRIBE Adapter Methods

For each PUBLISH-SUBSCRIBE operation six specific adapter methods shall be defined:

- <<op>>RegisterAckReceived;

- <<op>>RegisterErrorReceived;

- <<op>>DeregisterAckReceived;

- <<op>>NotifyReceived;

- <<op>>NotifyErrorReceived.

The ‘<<op>>RegisterAckReceived’ signature shall be:

public void <<op>>RegisterAckReceived(MALMessageHeader header,

<<Ack>> ack, java.util.Map qosProperties)

The ‘<<op>>RegisterErrorReceived’ signature shall be:

public void <<op>>RegisterErrorReceived(MALMessageHeader header,

MALStandardError error, java.util.Map qosProperties )

The ‘<<op>>DeregisterAckReceived’ signature shall be:

public void <<op>>DeregisterAckReceived(MALMessageHeader header,

<<Ack>> ack, java.util.Map qosProperties)

The ‘<<op>>NotifyReceived’ signature shall be defined according to the <<Notify [N]>> type:

public void <<op>>NotifyReceived(MALMessageHeader header,

Identifier subscriptionId,

UpdateHeaderList updateHeaderList,

<<Notify [i]>>List updateList<<i>>, ...

<<Notify [N]>>List updateList<<N>>,

java.util.Map qosProperties)

The ‘<<op>>NotifyErrorReceived’ signature shall be:

public void <<op>>NotifyErrorReceived(MALMessageHeader header,

MALStandardError error, java.util.Map qosProperties)

#### Notify from Other Service Adapter Method

A method ‘notifyReceivedFromOtherService’ shall be defined in order to enable a consumer to receive Notify messages from any services, i.e., not only from the consumed service.

The method signature shall be:

public void notifyReceivedFromOtherService(

MALMessageHeader msgHeader,

MALNotifyBody body,

Map qosProperties) throws MALException

### Stub implementation class

#### Definition

A Stub class shall be defined in order to implement the Stub interface.

The name of the class shall be the identifier of the service suffixed with ‘Stub’: <<Service>>Stub.

The stub class shall implement the interface <<Service>>.

The class shall define the attribute specified in table 4-4.

Table 4-4:  <<Service>>Stub Attribute

| Attribute | Type |
| --- | --- |
| consumer | MALConsumer |

The stub class shall provide a public constructor.

The constructor signature shall be:

public <<Service>>Stub(MALConsumer consumer)

The constructor shall assign the attribute ‘consumer’ with the value of the parameter ‘consumer’.

When calling the MALConsumer, the Stub shall convert each body element which type is mapped to a Union by creating a new Union from the body element.

When getting a body element from a MALMessageBody, the Stub class shall pass an instance of the element if the type is concrete, i.e., if there is no polymorphism; otherwise the Stub class shall pass the value NULL.

When returning a result from the MALConsumer, the Stub shall convert each body element which type is Union to its Java type value.

#### SEND Operation Invocation

For each SEND operation, the method ‘<<op>>’ inherited from the interface <<Service>> shall be implemented by calling the method ‘send’ provided by the attribute ‘consumer’ with the following parameters:

- the MALSendOperation description resolved from the <<Service>>Helper;

- the body elements.

#### SUBMIT Operation Synchronous Invocation

For each SUBMIT operation, the method ‘<<op>>’ inherited from the interface <<Service>> shall be implemented by calling the method ‘submit’ provided by the attribute ‘consumer’ with the following parameters:

- the MALSubmitOperation description resolved from the <<Service>>Helper;

- the body elements.

#### REQUEST Operation Synchronous Invocation

For each REQUEST operation, the method ‘<<op>>’ inherited from the interface <<Service>> shall be implemented by calling the method ‘request’ provided by the attribute ‘consumer’ with the following parameters:

- the MALRequestOperation description resolved from the <<Service>>Helper;

- the body elements.

If the RESPONSE is not empty, the body elements returned by the call to the method ‘request’ shall be returned as the result of the method ‘<<op>>’ in the following way:

- if there is only one body element then it shall be returned;

- if there is more than one body element then an <<Op>>Response shall be created from the body elements and returned.

#### INVOKE Operation Synchronous Invocation

For each INVOKE operation, the method ‘<<op>>’ inherited from the interface <<Service>> shall be implemented by calling the method ‘invoke’ provided by the attribute ‘consumer’ with the following parameters:

- the MALInvokeOperation description resolved from the <<Service>>Helper;

- the <<Service>>Adapter;

- the body elements.

If the ACK is not empty, the body elements returned by the call to the method ‘invoke’ shall be returned as the result of the method ‘<<op>>’ in the following way:

- if there is only one body element then it shall be returned;

- if there is more than one body element then a <<Op>>Ack shall be created from the body elements and returned.

#### PROGRESS Operation Synchronous Invocation

For each PROGRESS operation, the method ‘<<op>>’ inherited from the interface <<Service>> shall be implemented by calling the method ‘progress’ provided by the attribute ‘consumer’ with the following parameters:

- the MALProgressOperation description resolved from the <<Service>>Helper;

- the <<Service>>Adapter;

- the body elements.

If the ACK is not empty, the Element returned by the call to the method ‘progress’ shall be returned as the result of the method ‘<<op>>’ in the following way:

- if there is only one body element then it shall be returned;

- if there is more than one body element then a <<Op>>Ack shall be created from the body elements and returned..

#### PUBLISH-SUBSCRIBE Operation Synchronous Invocation

For each PUBLISH-SUBSCRIBE operation, the method ‘registerFor<<op>>’ inherited from the interface <<Service>> shall be implemented by calling the method ‘register’ provided by the attribute ‘consumer’ with the following parameters:

- the MALPubSubOperation description resolved from the <<Service>>Helper;

- the Subscription;

- the <<Service>>Adapter.

For each PUBLISH-SUBSCRIBE operation, the method ‘deregisterFor<<op>>’ inherited from the interface <<Service>> shall be implemented by calling the method ‘deregister’ provided by the attribute ‘consumer’ with the following parameters:

- the MALPubSubOperation description resolved from the <<Service>>Helper;

- the IdentifierList.

#### SUBMIT Operation Asynchronous Invocation

For each SUBMIT operation, the method ‘async<<Op>>’ inherited from the interface <<Service>> shall be implemented by calling the method ‘asyncSubmit’ provided by the attribute ‘consumer’ with the following parameters:

- the MALSubmitOperation description resolved from the <<Service>>Helper;

- the <<Service>>Adapter;

- the body elements.

#### REQUEST Operation Asynchronous Invocation

For each REQUEST operation, the method ‘async<<Op>>’ inherited from the interface <<Service>> shall be implemented by calling the method ‘asyncRequest’ provided by the attribute ‘consumer’ with the following parameters:

- the MALRequestOperation description resolved from the <<Service>>Helper;

- the <<Service>>Adapter;

- the body elements.

#### INVOKE Operation Asynchronous Invocation

For each INVOKE operation, the method ‘async<<Op>>’ inherited from the interface <<Service>> shall be implemented by calling the method ‘asyncInvoke’ provided by the attribute ‘consumer’ with the following parameters:

- the MALInvokeOperation description resolved from the <<Service>>Helper;

- the <<Service>>Adapter;

- the body elements.

#### PROGRESS Operation Asynchronous Invocation

For each PROGRESS operation, the method ‘async<<Op>>’ inherited from the interface <<Service>> shall be implemented by calling the method ‘asyncProgress’ provided by the attribute ‘consumer’ with the following parameters:

- the MALProgressOperation description resolved from the <<Service>>Helper;

- the <<Service>>Adapter;

- the body elements.

#### PUBLISH-SUBSCRIBE Operation Asynchronous Invocation

For each PUBLISH-SUBSCRIBE operation, the method ‘async<<Op>>Register’ inherited from the interface <<Service>> shall be implemented by calling the method ‘asyncRegister’ provided by the attribute ‘consumer’ with the following parameters:

- the MALPubSubOperation description resolved from the <<Service>>Helper;

- the Subscription;

- the <<Service>>Adapter.

For each PUBLISH-SUBSCRIBE operation, the method ‘async<<Op>>Deregister’ inherited from the interface <<Service>> shall be implemented by calling the method ‘asyncDeregister’ provided by the attribute ‘consumer’ with the following parameters:

- the MALPubSubOperation description resolved from the <<Service>>Helper;

- the IdentifierList;

- the <<Service>>Adapter.

#### Continue an Interaction

For each SUBMIT, REQUEST, INVOKE and PROGRESS operation, the method ‘continue<<Op>>’ inherited from the interface <<Service>> shall be implemented by calling the method ‘continueInteraction’ provided by the attribute ‘consumer’ with the following parameters:

- the MALOperation description resolved from the <<Service>>Helper;

- the parameters ‘lastInteractionStage’, ‘initiationTimestamp’ and ‘transactionId’;

- the <<Service>>Adapter.

## Provider

### General

Figure 4-2 is a class diagram that describes the relationships between the skeleton classes and interfaces at the provider side with the delegation pattern. The following classes or interfaces are defined:

- <<Service>>Skeleton is the skeleton interface;

- <<Service>>DelegationSkeleton is the skeleton implementation class according to the delegation pattern;

- <<Service>>Handler is the service specific handler interface;

- <<Service>>HandlerImpl is the service implementation class;

- <<Op>>Publisher is a specific publishing interface;

- <<Operation>>Interaction is a specific interaction interface.

Figure 4-2:	Relationships between the Skeleton Classes and Interfaces (Delegation Pattern)

With the inheritance pattern, the class <<Service>>DelegationSkeleton is replaced by the class <<Service>>InheritanceSkeleton, which is the skeleton implementation class according to the inheritance pattern. The class diagram becomes that shown in figure 4-3.

Figure 4-3:	Relationships between the Skeleton Classes and Interfaces (Inheritance Pattern)

A service provider can be bound several times to one or several transport layers. Such a service provider is called a ‘multi-binding service provider’. It is represented by a single skeleton instance bound to several MALProviders as shown by figure 4-4.

Figure 4-4:  Multi-Binding Service Provider

### Handler interface

#### Definition

A handler interface shall be defined in order to handle interaction patterns through service specific methods.

The name of the interface is the identifier of the service suffixed with ‘Handler’: <<Service>>Handler.

#### SEND Operation Invocation

A method <<op>> shall be defined for each SEND operation provided by the service.

The signature of the method <<op>> shall be:

public void <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

MALInteraction interaction)

throws MALInteractionException, MALException

#### SUBMIT Operation Invocation

A method <<op>> shall be defined for each SUBMIT operation provided by the service.

The signature of the method <<op>> shall be:

public void <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

MALInteraction interaction)

throws MALInteractionException, MALException

#### REQUEST Operation Invocation

A method <<op>> shall be defined for each REQUEST operation provided by the service.

If the RESPONSE message body is empty then the signature of the method <<op>> shall be:

public void <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

MALInteraction interaction)

throws MALInteractionException, MALException

If the RESPONSE message body contains one element then the signature of the method <<op>> shall be:

public <<Res [1]>> <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

MALInteraction interaction)

throws MALInteractionException, MALException

If the RESPONSE message body contains more than one element then the signature of the method <<op>> shall be:

public <<Op>>Response <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

MALInteraction interaction)

throws MALInteractionException, MALException

#### INVOKE Operation Invocation

A method <<op>> shall be defined for each INVOKE operation provided by the service.

The signature of the method <<op>> shall be:

public void <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

MALInvoke interaction)

throws MALInteractionException, MALException

#### PROGRESS Operation Invocation

A method <<op>> shall be defined for each PROGRESS operation provided by the service.

The signature of the method <<op>> shall be:

public void <<op>>(<<In [i]>> p<<i>>, ... <<In [N]>> p<<N>>,

MALProgress interaction)

throws MALInteractionException, MALException

#### Skeleton setter

A method ‘setSkeleton’ shall be defined in order to set the reference of the skeleton object.

The method signature shall be:

public void setSkeleton(<<Service>>Skeleton skeleton)

### Skeleton interface

#### Definition

A skeleton interface shall be defined in order to enable the creation of publishers.

The name of the interface is the identifier of the service suffixed with ‘Skeleton’: <<Service>>Skeleton.

#### Create a Publisher

One method shall be defined for each PUBLISH-SUBSCRIBE operation in order to create a specific publisher.

The method signature shall be:

public <<Op>>Publisher create<<Op>>Publisher(

IdentifierList domain,

Identifier networkZone,

SessionType sessionType,

Identifier sessionName,

QoSLevel publishQos,

java.util.Map publishProperties,

UInteger publishPriority) throws MALException

### Publisher

#### Definition

A publisher class shall be defined in order to enable the handler to publish updates to the brokers owned by the activating providers, i.e., the MALProviders that activate the handler.

One publisher class shall be defined for each PUBLISH-SUBSCRIBE operation.

A publisher class shall belong to the ‘provider’ package of the service that owns the PUBLISH-SUBSCRIBE operation.

The name of the class shall be the identifier of the PUBLISH-SUBSCRIBE operation suffixed with ‘Publisher’: <<Op>>Publisher.

The class shall define the attribute specified in table 4-5.

Table 4-5:  <<Op>> Publisher Attribute

| Attribute | Type |
| --- | --- |
| publisherSet | MALPublisherSet |

The publisher class shall provide a public constructor.

The constructor signature shall be:

public <<Op>>Publisher(MALPublisherSet publisherSet)

The constructor parameter shall be assigned as described in table 4-6.

Table 4-6:  <<Op>>Publisher constructor Parameter

| Parameter | Description |
| --- | --- |
| publisherSet | MALPublisherSet created through the MALProviderSet owned by the skeleton |

#### Synchronous REGISTER Invocation

A method ‘register’ shall be defined in order to call the MALPublisherSet method ‘register’.

The method signature shall be the same as the MALPublisherSet method ‘register’.

#### Synchronous DEREGISTER Invocation

A method ‘deregister’ shall be defined in order to call the MALPublisherSet method ‘deregister’.

The method signature shall be the same as the MALPublisherSet method ‘deregister’.

#### Asynchronous REGISTER Invocation

A method ‘asyncRegister’ shall be defined in order to call the MALPublisherSet method ‘asyncRegister’.

The method signature shall be the same as the MALPublisherSet method ‘asyncRegister’.

#### Asynchronous DEREGISTER Invocation

A method ‘asyncDeregister’ shall be defined in order to call the MALPublisherSet method ‘asyncDeregister’.

The method signature shall be the same as the MALPublisherSet method ‘asyncDeregister’.

#### PUBLISH Invocation

A method ‘publish’ shall be defined in order to call the MALPublisherSet method ‘publish’.

The method signature shall be:

public void publish(

UpdateHeaderList updateHeaderList,

<<Notify [i]>> updateList<<i>>, ... <<Notify [N]>> updateList<<N>>)

throws java.lang.IllegalArgumentException,

MALInteractionException, MALException

The ‘publish’ parameters shall be assigned as described in table 3-102.

Table 4-7:  <<Op>>Publisher ‘publish’ Parameters

| Parameter | Description |
| --- | --- |
| updateHeaderList | Headers of the updates to be published |
| updateList<<i>> | List of updates to be published |

#### Close

A method ‘close’ shall be defined in order to call the MALPublisherSet method ‘close’.

The method signature shall be the same as the MALPublisherSet method ‘close’.

### INVOKE Interaction

#### Definition

For each INVOKE operation a class ‘<<Op>>Interaction’ shall be defined.

The <<Op>>Interaction class shall define the attribute specified in table 4-8.

Table 4-8:  Invoke <<Op>>Interaction Attribute

| Attribute | Type |
| --- | --- |
| interaction | MALInvoke |

The class shall provide a public constructor.

The constructor signature shall be:

<<Op>>Interaction(MALInvoke interaction)

When calling the MALInvoke, the <<Op>>Interaction class shall convert each body element which type is mapped to a Union by creating a new Union from the body element.

If the message body is empty then the value NULL shall be passed to the MALInvoke interaction.

#### Interaction Getter

A method shall be defined in order to get the MALInvoke interaction.

The method signature shall be:

public MALInvoke getInteraction()

#### Specific ACK Sending

A method ‘sendAcknowledgement’ shall be defined in order to send a specific ACK.

The ‘sendAcknowledgement’ signature shall be:

public MALMessage sendAcknowledgement(

<<Ack [i]>> ack<<i>>, ... <<Ack [N]>> ack<<N>>)

throws MALInteractionException, MALException

The method shall be implemented in order to call the method ‘sendAcknowledgement’ provided by the MALInvoke interaction.

#### Specific RESPONSE Sending

A method ‘sendResponse’ shall be defined in order to send a specific RESPONSE.

The ‘sendResponse’ signature shall be:

public MALMessage sendResponse(

<<Res [i]>> res<<i>>, ... <<Res [N]>> res<<N>>)

throws MALInteractionException, MALException

The method shall be implemented in order to call the method ‘sendResponse’ provided by the MALInvoke interaction.

#### Generic ERROR Sending

A method ‘sendError’ shall be defined in order to send an ERROR.

The ‘sendError’ signature shall be:

public MALMessage sendError(MALStandardError error)

throws MALInteractionException, MALException

The method shall be implemented in order to call the method ‘sendError’ provided by the MALInvoke interaction.

### PROGRESS Interaction

#### Definition

For each PROGRESS operation a class ‘<<Op>>Interaction’ shall be defined.

The <<Op>>Interaction class shall define the attribute specified in table 4-9.

Table 4-9:  Progress <<Op>>Interaction Attribute

| Attribute | Type |
| --- | --- |
| interaction | MALProgress |

The class shall provide a public constructor.

The constructor signature shall be:

<<Op>>Interaction(MALProgress interaction)

When calling the MALProgress, the <<Op>>Interaction class shall convert each body element which type is mapped to a Union by creating a new Union from the body element.

If the message body is empty then the value NULL shall be passed to the MALProgress interaction.

#### Interaction Getter

A method shall be defined in order to get the MALProgress interaction.

The method signature shall be:

public MALProgress getInteraction()

#### Specific ACK Sending

A method ‘sendAcknowledgement’ shall be defined in order to send a specific ACK.

The ‘sendAcknowledgement’ signature shall be defined according to the ACK message body:

public MALMessage sendAcknowledgement(

<<Ack [i]>> ack<<i>>, ... <<Ack [N]>> ack<<N>>)

throws MALInteractionException, MALException

The method shall be implemented in order to call the method ‘sendAcknowledgement’ provided by the MALProgress.

#### Specific UPDATE Sending

A method ‘sendUpdate’ shall be defined in order to send a specific UPDATE.

The ‘sendUpdate’ signature shall be:

public MALMessage sendUpdate(<<Update>> update)

throws MALInteractionException, MALException

The method shall be implemented in order to call the method ‘sendUpdate’ provided by the MALProgress interaction.

#### Specific RESPONSE Sending

A method ‘sendResponse’ shall be defined in order to send a specific RESPONSE.

The ‘sendResponse’ signature shall be:

public MALMessage sendResponse(

<<Res [i]>> res<<i>>, ... <<Res [N]>> res<<N>>)

throws MALInteractionException, MALException

The method shall be implemented in order to call the method ‘sendResponse’ provided by the MALProgress interaction.

#### Generic ERROR Sending

A method ‘sendError’ shall be defined in order to send an ERROR.

The ‘sendError’ signature shall be:

public MALMessage sendError(MALStandardError error)

throws MALInteractionException, MALException

The method shall be implemented in order to call the method ‘sendError’ provided by the MALProgress interaction.

### Inheritance skeleton implementation class

#### Definition

A skeleton class shall be defined in order to enable to implement a handler by inheriting from this skeleton.

The name of the class shall be the identifier of the service suffixed with ‘InheritanceSkeleton’: <<Service>>InheritanceSkeleton.

The skeleton class shall be abstract.

The skeleton class shall implement three interfaces:

- MALInteractionHandler

- <<Service>>Skeleton

- <<Service>>Handler

The skeleton class shall define the attributes specified in table 4-10.

Table 4-10:  <<Service>>InheritanceSkeleton Attributes

| Attribute | Type |
| --- | --- |
| providerSet | MALProviderSet |

The skeleton class shall provide a public empty constructor.

The constructor signature shall be:

public <<Service>>InheritanceSkeleton()

The constructor shall assign the attribute ‘providerSet’ with a new ProviderSet taking as a parameter the MALService statically declared by the <<Service>>Helper.

When getting a body element from a MALMessageBody, the Skeleton class shall pass an instance of the element if the type is concrete, i.e., if there is no polymorphism; otherwise the Skeleton class shall pass the value NULL.

When calling the <<Service>>Handler, the Skeleton class shall convert each body element which type is Union to its Java type value.

When returning a result from the <<Service>>Handler, the Skeleton class shall convert each body element which type is mapped to a Union by creating a new Union from the body element.

#### MAL Initialization

The method ‘malInitialize’ shall be implemented by adding the MALProvider to the MALProviderSet.

#### MAL Finalization

The method ‘malFinalize’ shall be implemented by removing the MALProvider from the MALProviderSet.

#### Creating Publishers

The skeleton class shall implement the methods ‘create<<Op>>Publisher’ inherited from the <<Service>>Skeleton interface.

The implementation shall create a new MALPublisherSet from the MALProviderSet, call the <<Op>>Publisher constructor with the created MALPublisherSet as a parameter and return the result.

#### Handle SEND Interactions

The method ‘handleSend’ inherited from the <<Service>>Handler interface shall be implemented by calling the specific handler method according to the operation.

If the operation is not defined by the service then a MAL standard error MAL::UNSUPPORTED_OPERATION shall be raised as a MALInteractionException.

#### Handle SUBMIT Interactions

The method ‘handleSubmit’ inherited from the <<Service>>Handler interface shall be implemented by calling the specific handler method according to the operation.

Once the specific handler method ‘<<op>>’ has been called the method ‘sendAcknowledgement’ provided by the MALSubmit parameter shall be called.

If the operation is not defined by the service then a MAL standard error MAL::UNSUPPORTED_OPERATION shall be raised as an ACK ERROR through the MALSubmit interaction context.

#### Handle REQUEST Interactions

The method ‘handleRequest’ inherited from the <<Service>>Handler interface shall be implemented by calling the specific handler method according to the operation.

Once the specific handler method ‘<<op>>’ has been called the method ‘sendResponse’ provided by the MALRequest parameter shall be called.

If the returned message body is empty then no value shall be passed to the interaction.

If the operation is not defined by the service then a MAL standard error MAL::UNSUPPORTED_OPERATION shall be raised as a RESPONSE ERROR through the MALRequest interaction context.

#### Handle INVOKE Interactions

The method ‘handleInvoke’ inherited from the <<Service>>Handler interface shall be implemented by calling the specific handler method according to the operation.

a new <<Op>>Interaction shall be instantiated with the MALInvoke parameter of the method ‘handleInvoke’ and passed as the <<Op>>Interaction parameter of the method ‘<<op>>’.

If the operation is not defined by the service then a MAL standard error MAL::UNSUPPORTED_OPERATION shall be raised as an ACK ERROR through the MALInvoke interaction context.

#### Handle PROGRESS Interactions

The method ‘handleProgress’ inherited from the <<Service>>Handler interface shall be implemented by calling the specific handler method according to the operation.

a new <<Op>>Interaction shall be instantiated with the MALProgress parameter of the method ‘handleProgress’ and passed as the <<Op>>Interaction parameter of the method ‘<<op>>’.

If the operation is not defined by the service then a MAL standard error MAL::UNSUPPORTED_OPERATION shall be raised as an ACK ERROR through the MALProgress interaction context.

### Delegation skeleton implementation class

#### Definition

A skeleton class shall be defined in order to enable to implement a handler by implementing the <<Service>>Handler interface.

The name of the class shall be the identifier of the service suffixed with ‘DelegationSkeleton’ : <<Service>>DelegationSkeleton.

The skeleton class shall not be abstract.

The skeleton class shall implement two interfaces:

- MALInteractionHandler;

- <<Service>>Skeleton.

The skeleton class shall define the attributes specified in table 4-11.

Table 4-11:  <<Service>>DelegationSkeleton Attributes

| Attribute | Type |
| --- | --- |
| delegate | <<Service>>Handler |
| providerSet | MALProviderSet |

The skeleton class shall provide a public constructor.

The constructor signature shall be:

public <<Service>>DelegationSkeleton(<<Service>>Handler delegate)

The constructor shall assign the attribute ‘delegate’ with the value of the parameter ‘delegate’.

#### MAL Initialization

The delegation skeleton class shall implement the methods ‘malInitialize’ in the same way as the inheritance skeleton.

#### MAL Finalization

The delegation skeleton class shall implement the methods ‘malFinalize’ in the same way as the inheritance skeleton.

#### Creating Publishers

The delegation skeleton class shall implement the methods ‘create<<Op>>Publisher’ in the same way as the inheritance skeleton.

#### Handle Interactions

The delegation skeleton class shall implement the method ‘handle<<Ip>>’ in the same way as the inheritance skeleton except that the specific handler method is provided by the attribute ‘delegate’.

## Data structures

### Overview

This subsection specifies how enumeration, list and composite data structures are mapped to classes used on both consumer and provider sides.

### Package

If the data structure belongs to an area then the package shall be:

<<root name>>.<<!area!>>.structures

If the data structure belongs to a service then the package shall be:

<<root name>>.<<!area!>>.<<!service!>>.structures

### Class Definition

A class shall be defined for each data type.

The class name shall be the name of the data type: <<Type name>>.

A list class shall be defined for every concrete data type.

The list class name shall be: <<List element type name>>List.

The class shall be public.

If the data type is concrete then the class shall be final.

If the data type is abstract then the class shall be abstract.

### Interface definition

A list marker interface shall be defined for every abstract data type.

The list marker interface name shall be: <<List element type name>>List.

### Short Form

#### Constants declaration

If the data type is concrete then its absolute short form shall be computed as follows:

- the absolute short form shall be a long integer;

- the area number shall be shifted to the left most position of the absolute short form: bits 48 to 63;

- the service number shall be shifted to the left of the absolute short form after the area number: bits 32 to 47;

- the relative type shall be assigned to the right most position of the absolute short form: bits 0 to 31.

If the data type is concrete then the following constants shall be declared:

public static final Long SHORT_FORM = new Long(<<absolute short form>>)

public static final Integer TYPE_SHORT_FORM =

new Integer(<<type short form>>)

#### Get the Short Form

If the data type is concrete then the method ‘getShortForm’ inherited from the Element interface shall be implemented by returning the constant SHORT_FORM declared by the class.

#### Get the Area Number

If the data type is concrete then the method ‘getAreaNumber’ inherited from the Element interface shall be implemented by returning the number of the area where the data type is defined.

#### Get the Service Number

If the data type is concrete then the method ‘getServiceNumber’ inherited from the Element interface shall be implemented as follows:

- if the data type belongs to a service then the number of the service shall be returned;

- if the data type does not belong to a service then the MALService constant NULL_SERVICE_NUMBER shall be returned.

#### Get the Type Short Form

If the data type is concrete then the method ‘getShortForm’ inherited from the Element interface shall be implemented by returning the constant TYPE_SHORT_FORM declared by the class.

### Enumeration

#### Limitation

The Java MAL API shall only support MAL enumeration which values are contiguous, start from 1 and be smaller or equal to the biggest 32 bits signed integer.

#### Class Definition

The class shall extend the class Enumeration.

The class shall be final.

#### Enumeration Items

Two static constants shall be defined for each item of the enumeration:

- the integer value typed ‘int’:

public final static int _<<ENUM ITEM>>_INDEX =

<<enum item ordinal>>;

- the typed value which is an instance of the enumeration class:

public final static <<Enumeration>> <<ENUM ITEM>> =

new <<Enumeration>>(new Integer(_<<ENUM ITEM>>_INDEX));

#### Get the Enumeration from the Ordinal Value

A method ‘fromInt’ shall be defined in order to return the Enumeration item from its ordinal value.

The method signature shall be:

public static <<Enumeration>> fromInt(int ordinal)

#### Get the Enumeration from the Item Name

A method ‘fromString’ shall be defined in order to return the Enumeration item from its name.

The method signature shall be:

public static <<Enumeration>> fromString(String itemName)

#### ToString

The method ‘toString’ shall be redefined by returning the name of the enumerated value: <<ENUM ITEM>>.

#### Create an Element

The method ‘createElement’ defined by the interface Element shall be implemented by returning the first item of the enumeration.

#### Encode

The method ‘encode’ defined by the interface Element shall be implemented by encoding the ‘ordinal’ through the MALEncoder as follows:

- if the enumeration size is smaller or equal to 255 then the method ‘encodeUOctet’ shall be called;

- if the enumeration size is greater than 255 and smaller or equal to 65535 then the method ‘encodeUShort’ shall be called;

- if the enumeration size is greater than 65535 then the method ‘encodeUInteger’ shall be called.

#### Decode

The method ‘decode’ defined by the interface Element shall be implemented by decoding the ‘ordinal’ and returning the result of the method ‘fromInt’.

The ‘ordinal’ shall be decoded through the MALDecoder as follows:

- if the enumeration size is smaller or equal to 255 then the method ‘decodeUOctet’ shall be called;

- if the enumeration size is greater than 255 and smaller or equal to 65535 then the method ‘decodeUShort’ shall be called;

- if the enumeration size is greater than 65535 then the method ‘decodeUInteger’ shall be called.

### List Class

#### Class Definition

The class shall extend a class that implements java.util.List and assign the Java Generic type variable with the list element mapping class.

If the list element type is a MAL::Attribute then the class shall implement the interface AttributeList and assign the Java Generic type variable with the list element mapping class.

If the list element type is an enumeration then the class shall implement the interface ElementList and assign the Java Generic type variable with the list element mapping class.

If the list element type is a composite then:

- if the element type extends MAL::Composite then the list class shall implement the interface CompositeList and assign the Java Generic type variable with the list element mapping class;

- if the element type extends a type <<parent composite>> then the list class shall implement the interface <<Parent composite>>List and assign the Java Generic type variable with the list element mapping class;

#### Empty Constructor

An empty public constructor shall be defined.

The constructor signature shall be:

public <<List class name>>()

#### Constructor with an initial size

A public constructor shall be defined in order to create a list with an initial size.

The specified initial size may not be taken into account depending on the implementation.

The constructor signature shall be:

public <<List class name>>(int initialSize)

#### Encode

The method ‘encode’ inherited from the Element interface shall be implemented.

A MALListEncoder shall be created by calling the method 'createListEncoder' provided by the MALEncoder;

Each element of the list shall be encoded through the MALListEncoder as follows:

- if the declared list element type is a MAL::Attribute then the method ‘encodeNullable<<Attribute>>’ provided by the MALEncoder shall be called;

- else the method ‘encodeNullableElement’ provided by the MALEncoder shall be called.

#### Decode

The method ‘decode’ inherited from the Element interface shall be implemented.

A MALListDecoder shall be created by calling the method 'createListDecoder' provided by the MALDecoder;

As long as the method 'hasNext' of the MALListDecoder returns TRUE, an element of the list shall be decoded through the MALListDecoder as follows:

- if the declared List element type is a MAL::Attribute then the method ‘decodeNullable<<Attribute>>’ provided by the MALDecoder shall be called;

- else the method ‘decodeNullableElement’ provided by the MALDecoder shall be called with a new instance of the element as a parameter.

NOTE	–	The declared list element type cannot be an abstract MAL::Composite.

The decoded element shall be added to this list;

This list shall be returned as a result.

#### Create an Element

The method ‘createElement’ defined by the interface Element shall be implemented by calling the empty constructor and returning the result.

### Composite

#### Class Definition

If the parent type is not MAL::Composite then the class shall extend the class that represents the parent type: <<Composite parent class>>.

If the parent type is MAL::Composite then the class shall implement the interface Composite.

#### Attributes Declaration

A private Java attribute <<field name>> typed <<Field class>> shall be declared for each field of the Composite.

#### Empty Constructor

An empty public constructor shall be defined.

The constructor signature shall be:

public <<Composite>>()

#### Constructor

A public constructor shall be defined with all the fields owned by this Composite and its parents.

The fields shall be declared in the same order as in the Composite type definition and descending the parent hierarchy.

The constructor shall declare the following clause:

throws java.lang.IllegalArgumentException

If a field cannot be null and if it is assigned with the value NULL then an IllegalArgumentException shall be raised.

#### Getters

A getter shall be defined for each field.

The method signature shall be:

public <<Composite field class>> get<<Composite field name>>()

#### Setters

A setter shall be defined for each field.

The method signature shall be:

public void set<<Composite field name>>(

<<Composite field class>> <<field name>>)

throws java.lang.IllegalArgumentException

If the field cannot be null and if it is assigned with the value NULL then an IllegalArgumentException shall be raised.

#### HashCode

The java.lang.Object method ‘hashCode’ shall be redefined as follows:

- if the parent type is MAL::Composite, the hashCode shall be equal to one.

- if the parent type is not MAL::Composite, the hashCode shall be equal to the result returned by ‘the super ‘hashCode’ method;

- for each field the hashCode shall be assigned with the sum of:

- the current hashCode value multiplied by a factor which value is 31;

- the hashCode returned by the field or zero if the field is NULL.

#### Equals

The java.lang.Object method ‘equals’ shall be redefined as follows. The method shall return:

- TRUE if the parameter is the same as ‘this’;

- FALSE if the parameter is NULL;

- FALSE if the parameter class is not compliant with the class <<Composite>>;

- if the parent type is not MAL::Composite, it shall return FALSE if the call to the super ‘equals’ method returns FALSE;

- FALSE if the value of a field from the Composite parameter is not equal to the value of the same field from this Composite;

- TRUE in the other cases.

#### ToString

The method ‘toString’ shall be redefined by returning a String formatted as follows:

- the first character shall be ‘(’;

- the inherited toString method shall be called;

- the character ‘,’ shall be appended;

- for each field:

- the name of the field shall be appended;

- the character ‘=’ shall be appended;

- the toString representation of the field shall be appended;

- if the field is not the last one, the character ‘,’ shall be appended;

- the last character shall be ‘)’.

#### Encode

The method ‘encode’ shall be implemented as follows:

- if the parent type is not MALComposite then the super ‘encode’ shall be called;

- every field shall be encoded in the same order as its declaration;

- if the field can be null then the “Nullable” encoding method shall be called;

- the encoding shall be done according to the declared field type:

- if the declared field type is a MAL attribute then the method ‘encode[Nullable]<<Attribute>>’ provided by the MALEncoder shall be called;

- if the declared field type is MAL::Attribute then the method ‘encode[Nullable]Attribute’ provided by the MALEncoder shall be called;

- if the declared field type is a MAL enumeration then the method ‘encode[Nullable]Element’ provided by the MALEncoder shall be called;

- otherwise the declared field shall be a concrete MAL composite and the method ‘encode[Nullable]Element’ provided by the MALEncoder shall be called.

#### Decode

The method ‘decode’ shall be implemented as follows:

- if the parent type is not MALComposite then the super ‘decode’ shall be called;

- the result of the super ‘decode’ shall not be used as it returns ‘this’;

- every field shall be decoded in the same order as its declaration;

- if the field can be null then the “nullable” decoding method shall be called;

- the decoding shall be done according to the declared field type:

- if the declared field type is a MAL attribute then the method ‘decode[Nullable]<<Attribute>>’ provided by the MALDecoder shall be called;

- if the declared field type is MAL::Attribute then the method ‘decode[Nullable]Attribute’ provided by the MALDecoder shall be called;

- if the declared field type is a MAL enumeration then the method ‘decode[Nullable]Element’ provided by the MALDecoder shall be called with the first item of the enumeration as a parameter;

- otherwise the declared field shall be a concrete MAL composite and the method ‘decode[Nullable]Element’ provided by the MALDecoder shall be called with a new instance of the composite as a parameter.

- the method shall return ‘this’.

#### Create an Element

The method ‘createElement’ defined by the interface Element shall be implemented by calling the empty constructor and returning the result.

### List Marker Interface

#### Interface Definition

The list marker interface shall declare a generic type variable ‘T’ with the constraint ‘T extends <<Composite>>’.

If the list element type extends MAL::Composite then the list interface shall extend the interface CompositeList<T>.

If the list element type extends a type <<parent composite>> then the list interface shall extend the interface <<Parent composite>>List<T>.

## Element Factory Classes

### Overview

This subsection specifies how MALElementFactory classes are generated.

### Package

If the data structure belongs to an area then the package shall be:

<<root name>>.<<!area!>>.structures.factory

If the data structure belongs to a service then the package shall be:

<<root name>>.<<!area!>>.<<!service!>>.structures.factory

### Class Definition

A class shall be defined for each concrete data type and list type.

The class name shall be the name of the data type followed by the suffix “Factory”: <<Type name>>Factory.

The class shall be public and final.

The class shall implement the interface MALElementFactory by implementing the method ‘createElement’ in the following way:

- if the element is a Composite then the empty constructor shall be called;

- if the element is an Enumeration then the first enumeration item shall be returned;

- if the element is an Attribute and is not mapped to a Union then the empty constructor shall be called;

- if the element is an Attribute and is mapped to a Union then the Union constructor declaring the attribute type shall be called by passing any value.

## Multiple Element Body classes

### Overview

This subsection describes the multiple element body classes used on both consumer and provider sides.

### Package

The package shall be:

<<root name>>.<<!area!>>.<<!service!>>.body

### RESPONSE Body

#### Definition

A class shall be defined in order to gather the body elements from the RESPONSE message.

The class name shall be: <<Op>>Response.

An <<Op>>Response shall be defined for every REQUEST operation with a RESPONSE message that takes more than one argument.

#### Attributes Declaration

A private Java attribute shall be declared for each body element:

private <<Res [i]>> bodyElement<<i>>;

...

private <<Res [N]>> bodyElement<<N>>;

#### Empty Constructor

An empty public constructor shall be defined.

The constructor signature shall be:

public <<Op>>Response()

#### Constructor

A public constructor shall be defined with all the fields owned by this class.

The constructor signature shall be:

public <<Op>>Response(<<Res [i]>> bodyElement<<i>>, …

<<Res [N]>> bodyElement<<N>>)

#### Getters

A getter shall be defined for each field.

The method signature shall be:

public <<Res [i]>> getBodyElement<<i>>()

#### Setters

A setter shall be defined for each field.

The method signature shall be:

public void setBodyElement<<i>>(<<Res [i]>> bodyElement)

### ACK Body

#### Definition

A class shall be defined in order to gather the body elements from the ACK message.

The class name shall be: <<Op>>Ack.

An <<Op>>Ack shall be defined for every INVOKE or PROGRESS operation with an ACK message that takes more than one argument.

#### Attributes Declaration

A private Java attribute shall be declared for each body element:

private <<Ack [i]>> bodyElement<<i>>;

...

private <<Ack [N]>> bodyElement<<N>>;

#### Empty Constructor

An empty public constructor shall be defined.

The constructor signature shall be:

public <<Op>>Ack()

#### Constructor

A public constructor shall be defined with all the fields owned by this class.

The constructor signature shall be:

public <<Op>>Ack(<<Res [i]>> bodyElement<<i>>, …

<<Res [N]>> bodyElement<<N>>)

#### Getters

A getter shall be defined for each field.

The method signature shall be:

public <<Ack [i]>> getBodyElement<<i>>()

#### Setters

A setter shall be defined for each field.

The method signature shall be:

public void setBodyElement<<i>>(<<Ack [i]>> bodyElement)

## Helper and Element Factory Classes

### Overview

This subsection describes the helper and element factory classes used on both consumer and provider sides.

### Service Helper

#### Class Definition

The package shall be:

<<root name>>.<<!area!>>.<<!service!>>

The name of the class shall be the identifier of the service suffixed with ‘Helper’: <<Service>>Helper.

#### Service Declaration

The number of the service shall be declared as follows:

public static final int _<<SERVICE>>_SERVICE_NUMBER = <<service number>>;

public static final UShort <<SERVICE>>_SERVICE_NUMBER =

new UShort(_<<SERVICE>>_SERVICE_NUMBER);

The name of the service shall be declared as follows:

public static final Identifier <<SERVICE>>_SERVICE_NAME =

new Identifier("<<service>>");

The MALService shall be declared as follows:

public static final MALService <<SERVICE>>_SERVICE =

new <<mal package>>.MALService(

<<SERVICE>>_SERVICE_NUMBER,

<<SERVICE>>_SERVICE_NAME,

new UOctet((short) <<service version>>));

#### Service Level Errors Declaration

The service level errors shall be declared as follows:

public static final int _<<ERROR>>_ERROR_NUMBER = <<error number>>;

public static final UInteger _<<ERROR>>_ERROR_NUMBER =

new UInteger(_<<ERROR>>_ERROR_NUMBER);

#### Operations Declaration

The numbers of the operations provided by the service shall be declared as follows:

public static final int _<<OP>>_OP_NUMBER = <<op number>>;

public static final UShort <<OP>>_OP_NUMBER =

new UShort(_<<OP>>_OP_NUMBER);

A static MAL<<Ip>>Operation constant shall be created for each operation.

The last body element short forms array shall be empty.

The SEND operations shall be declared as follows:

public static final MALSendOperation <<OP>>_OP =

new MALSendOperation(

<<OP>>_OP_NUMBER,

new Identifier("<<op>>"),

new Boolean(<<op replayable>>),

new UShort(<<capability set>>),

new MALOperationStage(

new UShort((short) 1),

new Object[] {<<in short form [i]>>, ... <<in short form [N]>>},

new Object[] {}));

The SUBMIT operations shall be declared as follows:

public static final MALSubmitOperation <<OP>>_OP =

new MALSubmitOperation(

<<OP>>_OP_NUMBER,

new Identifier("<<op>>"),

new Boolean(<<op replayable>>),

new UShort(<<capability set>>),

new MALOperationStage(

new UShort((short) 1),

new Object[] {<<in short form [i]>>, ... <<in short form [N]>>},

new Object[] {}));

The REQUEST operations shall be declared as follows:

public static final MALRequestOperation <<OP>>_OP =

new MALRequestOperation (

<<OP>>_OP_NUMBER,

new Identifier("<<op>>"),

new Boolean(<<op replayable>>),

new UShort(<<capability set>>),

new MALOperationStage(

new UShort((short) 1),

new Object[] {<<in short form [i]>>, ... <<in short form [N]>>},

new Object[] {}),

new MALOperationStage(

new UShort((short) 2),

new Object[] {<<res short form [i]>>, ... <<res short form [N]>>},

new Object[] {}));

The INVOKE operations shall be declared as follows:

public static final MALInvokeOperation <<OP>>_OP =

new MALInvokeOperation(

<<OP>>_OP_NUMBER,

new Identifier("<<op>>"),

new Boolean(<<op replayable>>),

new UShort(<<capability set>>),

new MALOperationStage(

new UShort((short) 1),

new Object[] {<<in short form [i]>>, ... <<in short form [N]>>},

new Object[] {}),

new MALOperationStage(

new UShort((short) 2),

new Object[] {<<ack short form [i]>>, ... <<ack short form [N]>>},

new Object[] {}),

new MALOperationStage(

new UShort((short) 3),

new Object[] {<<res short form [i]>>, ... <<res short form [N]>>},

new Object[] {}));

The PROGRESS operations shall be declared as follows:

public static final MALProgressOperation <<OP>>_OP =

new MALProgressOperation (

<<OP>>_OP_NUMBER,

new Identifier("<<op>>"),

new Boolean(<<op replayable>>),

new UShort(<<capability set>>),

new MALOperationStage(

new UShort((short) 1),

new Object[] {<<in short form [i]>>, ... <<in short form [N]>>},

new Object[] {}),

new MALOperationStage(

new UShort((short) 2),

new Object[] {<<ack short form [i]>>, ... <<ack short form [N]>>},

new Object[] {}),

new MALOperationStage(

new UShort((short) 3),

new Object[] {

<<update short form [i]>>, ... << update short form [N]>>},

new Object[] {}),

new MALOperationStage(

new UShort((short) 4),

new Object[] {<<res short form [i]>>, ... <<res short form [N]>>},

new Object[] {}));

The PUBLISH-SUBSCRIBE operations shall be declared as follows:

public static final MALPubSubOperation <<OP>>_OP =

new MALPubSubOperation(

<<OP>>_OP_NUMBER,

new Identifier("<<op>>"),

new Boolean(<<op replayable>>),

new UShort(<<capability set>>),

new Object[] {

<<notify short form [i]>>, ... << notify short form [N]>>},

new Object[] {} );

#### Operation Level Errors Declaration

For all the operations of the service, a public static inner class called <<Op>>OperationHelper shall be declared.

All the errors defined at the level of this operation shall be declared as follows:

public static final int _<<ERROR>>_ERROR_NUMBER = <<error number>>;

public static final UInteger <<ERROR>>_ERROR_NUMBER =

new UInteger(_<<ERROR>>_ERROR_NUMBER);

#### Initialization

A method ‘init’ shall be defined in order to initialize the resources required by the usage of this service.

The method signature shall be:

public static void init(MALElementFactoryRegistry elementFactoryRegistry)

throws MALException

The method ‘init’ shall be idempotent.

The method ‘init’ shall be called by a MAL client before using the service.

All the MALOperation constants declared in the helper class shall be added to the MALService by calling the method ‘addOperation’.

The MALService shall be added to its MALArea by calling the method ‘addService’.

The MALElementFactoryRegistry shall be assigned to the MALService by calling the method ‘setElementFactoryRegistry’.

Every MALElementFactory defined in this service shall be registered into the MALElementFactoryRegistry passed as a parameter of the method ‘init’..

Every error defined in this service shall be registered into the MALContextFactory.

#### Deep Initialization

A method ‘deepInit’ shall be defined in order to initialize the resources required by the usage of this service and all the areas and services it depends on.

The method signature shall be:

public static void deepInit(MALElementFactoryRegistry elementFactoryRegistry)

throws MALException

The method ‘deepInit’ shall call the method ‘init’ provided by this helper.

The method ‘deepInit’ shall call the method ‘deepInit’ provided by the helper of every area and service this service depends on.

### Area helper

#### Class Definition

The package shall be:

<<root name>>.<<!area!>>

The name of the class shall be the identifier of the area suffixed with ‘Helper’: <<Area>>Helper.

#### Area Declaration

The number of the area shall be declared as follows:

public static final int _<<AREA>>_AREA_NUMBER = <<area number>>;

public static final UShort <<AREA>>_AREA_NUMBER =

new UShort(_<<AREA>>_AREA_NUMBER);

The name of the area shall be declared as follows:

public static final Identifier <<AREA>>_AREA_NAME =

new Identifier("<<area>>");

The MALArea shall be declared as follows:

public static <<mal package>>.MALArea <<AREA>>_AREA = new MALArea(

<<AREA>>_AREA_NUMBER, <<AREA>>_AREA_NAME);

#### Error Declaration

The area level errors shall be declared as follows:

public static final int _<<ERROR>>_ERROR_NUMBER = <<error number>>;

public static final UInteger _<<ERROR>>_ERROR_NUMBER =

new UInteger(_<<ERROR>>_ERROR_NUMBER);

#### Initialization

A method ‘init’ shall be defined in order to initialize the resources required by the usage of this area.

The method signature shall be:

public static void init(MALElementFactoryRegistry elementFactoryRegistry)

throws MALException

The method ‘init’ shall be idempotent.

The method ‘init’ shall be called by a MAL client before using the area.

The MALArea shall be registered in the MALContextFactory by calling the method ‘registerArea’.

Every MALElementFactory defined in this area shall be registered into the MALElementFactoryRegistry passed as a parameter of the method ‘init’.

Every error defined in this area shall be registered into the MALContextFactory.

#### Deep Initialization

A method ‘deepInit’ shall be defined in order to initialize the resources required by the usage of this area and all the areas and services it depends on.

The method signature shall be:

public static void deepInit(MALElementFactoryRegistry elementFactoryRegistry)

throws MALException

The method ‘deepInit’ shall call the method ‘init’ provided by this helper.

The method ‘deepInit’ shall call the method ‘deepInit’ provided by the helper of every area and service this area depends on.

# Transport API

## General

The transport API defines the interfaces and classes required by the MAL transport interface defined in reference [1].

The transport API shall be used by the MAL layer in order that any transport module that complies with this API can be plugged into the MAL layer.

## Classes and interfaces

### General

The classes and interfaces defined by this API are contained in the package:

org.ccsds.moims.mo.mal.transport

### MALTransportFactory

#### Definition

A MALTransportFactory class shall be defined in order to enable the MAL layer to instantiate and configure a MALTransport.

This class shall be abstract.

The class shall be extended by every specific factory class.

The class shall define the attributes specified in table 5-1.

Table 5-1:  MALTransportFactory Attributes

| Attribute | Type |
| --- | --- |
| protocol | String |

The MALTransportFactory class shall provide a static factory class repository that maps the MALTransportFactory implementation classes to their class names.

#### Factory Class Registration

The MALTransportFactory class shall provide a static method ‘registerFactoryClass’ in order to register the class of a specific MALTransportFactory.

NOTE	–	This method may be useful in environments where several class loaders are involved (e.g. OSGi platforms).

The method signature shall be:

public static void registerFactoryClass(Class factoryClass)

throws java.lang.IllegalArgumentException

The ‘registerFactoryClass’ parameter shall be assigned as described in table 5-2.

Table 5-2:  MALTransportFactory ‘registerFactoryClass’ Parameters

| Parameter | Description |
| --- | --- |
| factoryClass | Class extending MALTransportFactory |

The method shall store the class in the factory class repository.

The method shall throw an IllegalArgumentException if the parameter ‘factoryClass’ does not extend MALTransportFactory.

#### Factory Class Deregistration

The MALTransportFactory class shall provide a static method ‘deregisterFactoryClass’ in order to deregister the class of a specific MALTransportFactory.

The method signature shall be:

public static void deregisterFactoryClass(Class factoryClass)

throws java.lang.IllegalArgumentException

The ‘deregisterFactoryClass’ parameter shall be assigned as described in table 5-3.

Table 5-3:  MALTransportFactory ‘deregisterFactoryClass’ Parameter

| Parameter | Description |
| --- | --- |
| factoryClass | Class extending MALTransportFactory |

The method shall remove the class from the factory class repository.

The method shall throw an IllegalArgumentException if the parameter ‘factoryClass’ does not extend MALTransportFactory.

The method shall do nothing if the class is not found in the factory class repository.

#### Constructor

The MALTransportFactory constructor signature shall be:

public MALTransportFactory(String protocol)

java.lang.IllegalArgumentException

The MALTransportFactory constructor parameter shall be assigned as described in table 5-4.

Table 5-4:  MALTransportFactory Constructor Parameter

| Parameter | Description |
| --- | --- |
| protocol | Name of the protocol to be handled by the instantiated MALTransportFactory |

If the parameter ‘protocol’ is NULL then an IllegalArgumentException shall be raised.

The attribute ‘protocol’ shall be assigned with the value of the parameter ‘protocol’.

#### Protocol Getter

A getter shall be defined for the attribute ‘protocol’.

The method signature shall be:

public String getProtocol()

#### MALTransportFactory Creation

A static method ‘newFactory’ shall be defined in order to create a factory instance from a protocol name.

The method signature shall be:

public static MALTransportFactory newFactory(String protocol)

throws java.lang.IllegalArgumentException, MALException

The ‘newFactory’ parameter shall be assigned as described in table 5-5.

Table 5-5:  MALTransportFactory ‘newFactory’ Parameter

| Parameter | Description |
| --- | --- |
| protocol | Name of the protocol to be handled by the instantiated MALTransportFactory |

If the parameter ‘protocol’ is NULL then an IllegalArgumentException shall be raised.

The method shall resolve the specific MALTransportFactory class name through the system property:

org.ccsds.moims.mo.mal.transport.protocol.<<protocol name>>

NOTE	–	Each of those protocol properties is assigned with the class name of the transport factory. It should be noted that two different protocol properties can share the same transport factory class name. Below is an example of a configuration of protocol properties (the Java package is omitted in the class names):

# JMS transport with SOAP encoding

org.ccsds.moims.mo.mal.transport.protocol.jmssoap  JmsTransportFactory

# Web Service transport with SOAP encoding

org.ccsds.moims.mo.mal.transport.protocol.wssoap   WsTransportFactory

# RMI transport with Java serialization encoding

org.ccsds.moims.mo.mal.transport.protocol.rmiser   RmiTransportFactory

The method shall lookup the MALTransportFactory implementation class from the factory class repository.

If the class is not found in the factory class repository then it shall be loaded from the current class loader.

If the class is not found in the current class loader then a MALException shall be raised with the ClassNotFoundException as the cause.

The specific MALTransportFactory class shall be instantiated by calling its constructor that declares a String parameter and passing the protocol name.

The method ‘newFactory’ shall not return the value NULL.

If no MALTransportFactory can be returned then a MALException shall be raised.

#### MALTransport Instantiation

The factory class shall provide an abstract public method to instantiate a MALTransport.

The method signature shall be:

public abstract MALTransport createTransport(

java.util.Map properties) throws MALException

The ‘createTransport’ parameter shall be assigned as described in table 5-6.

Table 5-6:  MALTransportFactory ‘createTransport’ Parameter

| Parameter | Description |
| --- | --- |
| properties | Configuration properties |

The parameter ‘properties’ may be NULL.

The method ‘createTransport’ shall not return the value NULL.

If no MALTransport can be returned then a MALException shall be raised.

This method shall be implemented by every specific factory class.

### MALTransport

#### Definition

A MALTransport interface shall be defined in order to enable the MAL layer to send and receive MAL messages through a single protocol.

If several protocols are used by the MAL layer then one MALTransport instance shall be created for each of them.

Messages shall be sent and received through communication ports represented by the interface MALEndpoint.

A MALTransport shall be a factory of MALEndpoint.

One MALEndpoint shall be created for each MALConsumer and MALProvider.

NOTE	–	If a MALProvider owns a private broker, the MAL layer can create either two different MALEndpoints, one for the service provider and the other for the broker, or a single one for both. In the first case, the service provider and its broker have two different URIs whereas in the second case they share the same one.

#### Create an Endpoint

A method ‘createEndpoint’ shall be defined in order to instantiate a new MALEndpoint object from two parameters.

The method signature shall be:

public MALEndpoint createEndpoint(String localName,

Map qosProperties) throws MALException

The ‘createEndpoint’ parameters shall be assigned as described in table 5-7.

Table 5-7:  MALTransport ‘createEndpoint’ Parameters

| Parameter | Description |
| --- | --- |
| localName | Name of the endpoint |
| qosProperties | QoS properties to be used when creating the MALEndpoint |

The parameters ‘localName’ and ‘qosProperties’ may be NULL.

If the parameter ‘localName’ is not NULL then its value shall be unique for a given transport.

If the MALTransport is closed then a MALException shall be raised.

If the endpoint local name is not NULL and if the process starts again after a stop and creates the MALEndpoint with the same local name then the MALEndpoint shall recover the same URI as before the stop.

NOTE	–	If the name is NULL then the endpoint URI cannot be recovered.

#### Get an Endpoint

Two methods ‘getEndpoint’ shall be defined in order to get the reference of a MALEndpoint from:

- its local name;

- its URI.

The method signatures shall be:

public MALEndpoint getEndpoint(String localName)

throws java.lang.IllegalArgumentException, MALException

public MALEndpoint getEndpoint(URI uri)

throws java.lang.IllegalArgumentException, MALException

The ‘getEndpoint’ parameters shall be assigned as described in table 5-9.

Table 5-8:  MALTransport ‘getEndpoint’ Parameters

| Parameter | Description |
| --- | --- |
| localName | Name of the MALEndpoint to get |
| uri | URI of the MALEndpoint to get |

If the parameter ‘localName’ or ‘uri’ are NULL then an IllegalArgumentException shall be raised.

If the MALTransport is closed then a MALException shall be raised.

#### Delete an Endpoint

A method ‘deleteEndpoint’ shall be defined in order to delete an endpoint designated by its local name.

The method signature shall be:

public void deleteEndpoint(String localName)

throws java.lang.IllegalArgumentException, MALException

The deleteEndpoint parameter shall be assigned as described in table 5-9.

Table 5-9:  MALTransport ‘deleteEndpoint’ Parameter

| Parameter | Description |
| --- | --- |
| localName | Name of the MALEndpoint to delete |

If the parameter ‘localName’ is NULL then an IllegalArgumentException shall be raised.

If the MALTransport is closed then a MALException shall be raised.

After deletion, the endpoint’s URI shall be invalidated.

If a consumer initiates an interaction with a deleted endpoint, then the error MAL::DESTINATION_UNKNOWN shall be returned to the consumer if it is allowed by the IP.

#### Check QoS Support

A method ‘isSupportedQoSLevel’ shall be defined in order to indicate whether a QoS level is supported or not.

The method signature shall be:

public boolean isSupportedQoSLevel(QoSLevel qos)

The isSupportedQoSLevel parameter shall be assigned as described in table 5-10.

Table 5-10:  MALTransport ‘isSupportedQoSLevel’ Parameter

| Parameter | Description |
| --- | --- |
| qos | QoSLevel which support is to be tested |

The method shall return TRUE if the specified QoSLevel is supported by the MALTransport; otherwise it shall return FALSE.

The MAL layer shall use this method in order to test if a QoS level is supported or not by the MALTransport.

#### Check IP Support

A method ‘isSupportedInteractionType’ shall be defined in order to indicate whether an IP is supported or not.

The method signature shall be:

public boolean isSupportedInteractionType(InteractionType type)

The isSupportedInteractionType parameter shall be assigned as described in table 5-11.

Table 5-11:  MALTransport ‘isSupportedInteractionType’ Parameter

| Parameter | Description |
| --- | --- |
| type | The InteractionType which support is to be tested. |

The method shall return TRUE if the specified InteractionType is supported by the MALTransport; otherwise it shall return FALSE.

The MAL layer shall use this method in order to test if an IP is supported or not by the MALTransport.

#### Create a Transport Level Broker

Two methods ‘createBroker’ shall be defined in order to allow the creation of a transport level broker:

- using a private MALEndpoint;

- using a shared MALEndpoint.

Their signatures shall be:

public MALBrokerBinding createBroker(

String localName,

Blob authenticationId,

QoSLevel[] expectedQos,

UInteger priorityLevelNumber,

Map defaultQosProperties)

throws java.lang.IllegalArgumentException, MALException

public MALBrokerBinding createBroker(

MALEndpoint endpoint,

Blob authenticationId,

QoSLevel[] expectedQos,

UInteger priorityLevelNumber,

Map defaultQosProperties)

throws java.lang.IllegalArgumentException, MALException

The ‘createBroker’ parameters shall be assigned as described in table 5-12.

Table 5-12:  MALTransport ‘createBroker’ Parameters

| Parameter | Description |
| --- | --- |
| localName | Name of the private MALEndpoint to be created and used by the broker |
| endpoint | Shared MALEndpoint to be used by the broker |
| authenticationId | Authentication identifier that should be used by the broker |
| expectedQoS | QoS levels the broker assumes it can rely on |
| priorityLevelNumber | Number of priorities the broker uses |
| defaultQoSProperties | Default QoS properties used by the broker to send messages |

The parameters ‘localName’, ‘authenticationId’ and ‘defaultQoSProperties’ may be NULL.

If the parameters ‘endpoint’ or ‘expectedQoS’ are NULL then an IllegalArgumentException shall be raised.

If the parameter ‘localName’ is not NULL then its value shall be unique for a given transport.

If the parameter ‘service’ is NULL then the broker shall accept to interact through PUBLISH-SUBSCRIBE operations from any services.

The parameter ‘authenticationId’ may not be used. It is just a hint: some transports may not use this authentication identifier and assign another identifier to the broker.

The method shall return NULL if no broker can be created by this MALTransport.

A transport level broker shall be handled by the MALTransport. The PUBLISH-SUBSCRIBE interaction shall not be handled at the MAL level: no MALMessage shall be received by the MAL layer for such a broker.

The transport level broker shall be represented as a MALBrokerBinding.

If the MALTransport is closed then a MALException shall be raised.

If the local name is not NULL and if the process starts again after a stop and creates the MALBrokerBinding with the same local name then the MALBrokerBinding shall recover the same URI as before the stop.

If a private MALEndpoint is used then the message delivery to the broker shall be started as soon as the method returns.

#### Close

A method ‘close’ shall be defined in order to release all the resources allocated by the MALTransport.

The method signature shall be:

public void close() throws MALException

If an internal error occurs then a MALException shall be raised.

### MALEndpoint

#### Definition

A MALEndpoint interface shall be defined in order to send and receive MALMessages.

A new MALEndpoint shall be created when the MAL layer needs to allocate a new URI. This happens in the following cases:

- creation of a MALConsumer;

- creation of a MALProvider;

- creation of a MALBrokerBinding owned by a MALBroker.

In those cases, the URI of the MALConsumer, the MALProvider, or the MALBrokerBinding shall be the one owned by its MALEndpoint.

A MALEndpoint shall be a MALMessage factory.

The MALMessages sent by a MALConsumer, a MALProvider, or a MALBrokerBinding shall be sent through their MALEndpoint: the field ‘URIfrom’ belonging to the header of the MALMessages shall be assigned with the MALEndpoint URI.

A MALEndpoint shall be able to send messages as soon as it has been created.

A method ‘startMessageDelivery’ shall be defined in order to explicitly start the message delivery.

If a message is received by a MALEndpoint which message delivery is not started,

- and if the QoS level is QUEUED then the message shall be queued and delivered as soon as the delivery is started;

- else if the interaction allows to return an error message then a DELIVERY_FAILED error shall be returned to the sending endpoint.

#### Get the URI

A getter method shall be defined in order to return the URI of the MALEndpoint.

The method signature shall be:

public URI getURI()

#### Get the Local Name

A getter method shall be defined in order to return the local name of the MALEndpoint.

The method signature shall be:

public String getLocalName()

#### Create a Message

Two methods ‘createMessage’ shall be defined in order to instantiate a new MALMessage object:

- declaring parameters for the interaction type, the area, the service, the service version and the operation;

- declaring a MALOperation parameter.

The ‘createMessage’ methods signatures shall be:

public MALMessage createMessage(

Blob authenticationId,

URI uriTo,

Time timestamp,

QoSLevel qosLevel,

UInteger priority,

IdentifierList domain,

Identifier networkZone,

SessionType session,

Identifier sessionName,

InteractionType interactionType,

UOctet interactionStage,

Long transactionId,

UShort serviceAreaNumber,

UShort serviceNumber,

UShort operationNumber,

UOctet serviceVersion,

Boolean isErrorMessage,

Map qosProperties,

Object... body)

throws java.lang.IllegalArgumentException, MALException

public MALMessage createMessage(

Blob authenticationId,

URI uriTo,

Time timestamp,

QoSLevel qosLevel,

UInteger priority,

IdentifierList domain,

Identifier networkZone,

SessionType session,

Identifier sessionName,

Long transactionId,

Boolean isErrorMessage,

MALOperation operation,

UOctet interactionStage,

Map qosProperties,

Object... body)

throws java.lang.IllegalArgumentException, MALException

The ‘createMessage’ parameters shall be assigned as described in table 5-13.

Table 5-13:  MALEndpoint ‘createMessage’ Parameters

| Parameter | Description |
| --- | --- |
| authenticationId | Authentication identifier of the message |
| uriTo | URI of the message destination |
| timestamp | Timestamp of the message |
| qosLevel | QoS level of the message |
| priority | Priority of the message |
| domain | Domain of the service provider |
| networkZone | Network zone of the service provider |
| session | Session of the service provider |
| sessionName | Session name of the service provider |
| interactionType | Interaction type of the operation |
| interactionStage | Interaction stage of the interaction |
| transactionId | Transaction identifier of the interaction |
| serviceAreaNumber | Area number of the service |
| serviceNumber | Service number |
| operationNumber | Operation number |
| serviceVersion | Service version number |
| operation | Operation representated as a MALOperation |
| isErrorMessage | Flag indicating if the message conveys an error |
| qosProperties | QoS properties of the message |
| body | Message body elements |

If any of the parameters except ‘body’ or ‘qosProperties’ are NULL then an IllegalArgumentException shall be raised.

The parameters ‘body’ and ‘qosProperties’ may be NULL.

The body encoding shall be performed by the transport layer.

If the MALEndpoint is closed then a MALException shall be raised.

#### Send a Message

A method ‘sendMessage’ shall be provided in order to send a MALMessage.

The signature shall be:

public void sendMessage(MALMessage msg)

throws java.lang.IllegalArgumentException,

MALTransmitErrorException, MALException

The sendMessage parameter shall be assigned as described in table 5-14.

Table 5-14:  MALEndpoint ‘sendMessage’ Parameters

| Parameter | Description |
| --- | --- |
| msg | Message to be sent |

If the parameter ‘msg’ is NULL then an IllegalArgumentException shall be raised.

If a TRANSMIT ERROR occurs then a MALTransmitErrorException shall be raised.

If the MALEndpoint is closed then a MALException shall be raised.

#### Send Multiple Messages

A method ‘sendMessages’ shall be defined in order to send a list of MALMessages.

The method signature shall be:

public void sendMessages(MALMessage[] msgList)

throws java.lang.IllegalArgumentException,

MALTransmitMultipleErrorException, MALException

The ‘sendMessages’ parameter shall be assigned as described in table 5-15.

Table 5-15:  MALEndpoint ‘sendMessages’ Parameters

| Parameter | Description |
| --- | --- |
| msgList | List of messages to be sent |

If the parameter ‘msgList’ is NULL then an IllegalArgumentException shall be raised.

If a MULTIPLETRANSMIT ERROR occurs then a MALTransmitErrorException shall be raised.

If the MALEndpoint is closed then a MALException shall be raised.

#### Listen to Delivered Messages

A method ‘setMessageListener’ shall be defined in order to listen to delivered messages.

The method signature shall be:

public void setMessageListener(MALMessageListener listener)

throws MALException

The setMessageListener parameter shall be assigned as described in table 5-16.

Table 5-16:  MALEndpoint ‘setMessageListener’ Parameter

| Parameter | Description |
| --- | --- |
| listener | MALMessageListener in charge of receiving the MALMessages |

The parameter ‘listener’ shall not be NULL.

If the MALEndpoint is closed then a MALException shall be raised.

#### Start Message Delivery

A method ‘startMessageDelivery’ shall be defined in order to start the message delivery.

The method signature shall be:

public void startMessageDelivery() throws MALException

As soon as the method has returned the messages shall be delivered through the MALMessageListener.

If no MALMessageListener has been set then a DELIVERY_FAILED error shall be returned to the sending endpoint.

If the MALEndpoint is closed then a MALException shall be raised.

#### Stop Message Delivery

A method ‘stopMessageDelivery’ shall be defined in order to stop the message delivery.

The method signature shall be:

public void stopMessageDelivery() throws MALException

As soon as the method has returned no message shall be delivered through the MALMessageListener. The method shall synchronously stop the message delivery.

If the MALMessageListener is handling a message at the time of the deactivation then the method ‘stopMessageDelivery’ shall return after the end of the message handling.

If the MALEndpoint is closed then a MALException shall be raised.

#### Close

A method ‘close’ shall be defined in order to release the resources owned by a MALEndpoint.

The method signature shall be:

public void close() throws MALException

The method shall deactivate the MALEndpoint message delivery.

This method shall be called by the MAL layer when a MALConsumer or a MALProvider is closed.

A MALEndpoint which local name is NULL shall be deleted.

NOTE	–	If the MALEndpoint owns a non-null name, then it can be recovered after a close; i.e., it can be created again with the same name. The new MALEndpoint instance will be designated with the same URI.

If an internal error occurs then a MALException shall be raised.

### MALMessageHeader

#### Definition

A MALMessageHeader interface shall be defined in order to give a generic access to the MAL message header.

#### Field Getter and Setter

A getter and a setter shall be defined for each field of the MAL message header as defined in [1].

The name of each field shall be built from the name given in [1] by removing the spaces.

The getter of ‘Is Error Message’ shall be called ‘getIsErrorMessage’.

### MALMessageBody

#### Definition

A MALMessageBody interface shall be defined in order to give a generic access to the MAL message body.

#### Get the Number of Body Elements

A method ‘getElementCount’ shall be defined in order to return the number of elements contained in the MAL message body.

The method signature shall be:

public int getElementCount()

#### Get a Body Element

A method ‘getBodyElement’ shall be defined in order to get a body element.

The method signature shall be:

public Object getBodyElement(int index, Object element)

throws java.lang.IllegalArgumentException, MALException

The ‘getBodyElement’ parameters shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 5-17:  MALMessageBody ‘getBodyElement’ Parameters

| Parameter | Description |
| --- | --- |
| index | Index of the element in the body |
| element | Element to be decoded |

If an error occurs then a MALException shall be raised.

The index values shall start from 0 which designates the first element of the body.

The returned instance may not be the same as the parameter ‘element’.

#### Get an Encoded Body Element

A method ‘getEncodedBodyElement’ shall be defined in order to get an encoded body element.

The method signature shall be:

public MALEncodedElement getEncodedBodyElement(int index)

throws MALException

The ‘getEncodedBodyElement’ parameters shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 5-18:  MALMessageBody ‘getEncodedBodyElement’ Parameter

| Parameter | Description |
| --- | --- |
| index | Index of the element in the body |

### MALErrorBody

#### Definition

A MALErrorBody interface shall be defined in order to give access to the body of an ERROR message, i.e., a MAL message which header field ‘isError’ is TRUE.

The interface MALErrorBody shall extend MALMessageBody.

#### Get the Error

A method ‘getError’ shall be defined in order to return the error number from the ERROR message.

The method signature shall be:

public MALStandardError getError() throws MALException

If an error occurs then a MALException shall be raised.

### MALRegisterBody

#### Definition

A MALRegisterBody interface shall be defined in order to give access to the body of the REGISTER message defined by the IP PUBLISH-SUBSCRIBE.

The interface MALRegisterBody shall extend MALMessageBody.

#### Get the Subscription

A method ‘getSubscription’ shall be defined in order to return the Subscription from the REGISTER message.

The method signature shall be:

public Subscription getSubscription() throws MALException

If an error occurs then a MALException shall be raised.

### MALPublishRegisterBody

#### Definition

A MALPublishRegisterBody interface shall be defined in order to give access to the body of the PUBLISH REGISTER message defined by the IP PUBLISH-SUBSCRIBE.

The interface MALPublishRegisterBody shall extend MALMessageBody.

#### Get the EntityKeyList

A method ‘getEntityKeyList’ shall be defined in order to return the EntityKeyList from the PUBLISH REGISTER message.

The method signature shall be:

public EntityKeyList getEntityKeyList() throws MALException

If an error occurs then a MALException shall be raised.

### MALPublishBody

#### Definition

A MALPublishBody interface shall be defined in order to give access to the body of the PUBLISH message defined by the PUBLISH-SUBSCRIBE interaction.

The interface MALPublishBody shall extend MALMessageBody.

#### Get the List of UpdateHeader

A method ‘getUpdateHeaderList’ shall be defined in order to return the list of UpdateHeaders from the message.

The method signature shall be:

public UpdateHeaderList getUpdateHeaderList() throws MALException

If an error occurs then a MALException shall be raised.

#### Get the Update Lists

A method ‘getUpdateLists’ shall be defined in order to return the update lists from the message.

The method signature shall be:

public List[] getUpdateLists(List... updateLists) throws MALException;

The ‘getUpdateLists’ parameter shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 5-19:  MALPublishBody ‘getUpdateLists’ Parameter

| Parameter | Description |
| --- | --- |
| updateLists | Update lists to decode |

If an error occurs then a MALException shall be raised.

#### Get an Update List

A method ‘getUpdateList’ shall be defined in order to return an update list of from the message.

The method signature shall be:

public java.util.List getUpdateList(int listIndex,

java.util.List updateList) throws MALException

The ‘getUpdateList’ parameter shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 5-20:  MALPublishBody ‘getUpdateList’ Parameter

| Parameter | Description |
| --- | --- |
| listIndex | Index of the update list |
| updateList | Update list to decode |

The ‘listIndex’ values shall start from 0 which designates the first list of the body.

If an error occurs then a MALException shall be raised.

#### Get the Number of Updates

A method ‘getUpdateCount’ shall be defined in order to return the number of UpdateHeader elements from the message.

The method signature shall be:

public int getUpdateCount() throws MALException

If an error occurs then a MALException shall be raised.

#### Get an Update

A method ‘getUpdate’ shall be defined in order to return an <<Update>> from the message.

The method signature shall be:

public Object getUpdate(int listIndex, int updateIndex)

throws MALException

The ‘getUpdate’ parameter shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 5-21:  MALPublishBody ‘getUpdate’ Parameter

| Parameter | Description |
| --- | --- |
| listIndex | Index of the update list |
| updateIndex | Index of the update |

The ‘listIndex’ values shall start from 0 which designates the first list of the body.

The ‘updateIndex’ values shall start from 0 which designates the first update of the list.

If an error occurs then a MALException shall be raised.

#### Get an Encoded Update

A method ‘getEncodedUpdate’ shall be defined in order to return an encoded <<Update>> from the message.

The method signature shall be:

public MALEncodedElement getEncodedUpdate(int listIndex, int updateIndex)

throws MALException

The ‘getEncodedUpdate’ parameter shall be assigned as described in table Erreur ! Source du renvoi introuvable..

Table 5-22:  MALPublishBody ‘getEncodedUpdate’ Parameter

| Parameter | Description |
| --- | --- |
| listIndex | Index of the update list |
| updateIndex | Index of the update |

The ‘listIndex’ values shall start from 0 which designates the first list of the body.

The ‘updateIndex’ values shall start from 0 which designates the first update of the list.

If an error occurs then a MALException shall be raised.

This method may raise a MALException if the transport encoding format does not enable to separately decode the updates.

### MALNotifyBody

#### Definition

A MALNotifyBody interface shall be defined in order to give access to the body of the NOTIFY message defined by the PUBLISH-SUBSCRIBE interaction.

The interface MALNotifyBody shall extend MALPublishBody.

#### Get the Subscription Identifier

A method ‘getSubscriptionId’ shall be defined in order to return the identifier of the subscription from this NOTIFY message.

The method signature shall be:

public Identifier getSubscriptionId() throws MALException

If an error occurs then a MALException shall be raised.

### MALDeregisterBody

#### Definition

A MALDeregisterBody interface shall be defined in order to give access to the body of the DEREGISTER message defined by the IP PUBLISH-SUBSCRIBE.

The interface MALDeregisterBody shall extend MALMessageBody.

#### Get the IdentifierList

A method ‘getIdentifierList’ shall be defined in order to return the IdentifierList from the DEREGISTER message.

The method signature shall be:

public IdentifierList getIdentifierList() throws MALException

If an error occurs then a MALException shall be raised.

### MALEncodedElement

#### Definition

A MALEncodedElement class shall be defined in order to represent an encoded element.

The MALEncodedElement class shall only be used to represent:

- an encoded body element;

- an encoded element contained in a body element typed as a list.

The type List<MALEncodedElement> shall be used when representing a body element typed as a list and containing encoded elements.

#### Creation

A public constructor shall be defined with a Blob parameter.

The constructor signature shall be:

public MALEncodedElement(Blob encodedElement)

The constructor parameter shall be assigned as described in table 3-30.

Table 5-23:  MALEncodedElement Constructor Parameter

| Parameter | Description |
| --- | --- |
| encodedElement | Encoded element |

#### Getter

A method shall be defined in order to get the encoded element.

The method signature shall be:

public Blob getEncodedElement()

### MALMessage

#### Definition

A MALMessage interface shall be defined in order to give a generic acces to the transport specific messages.

#### Accessors

Getter methods shall be defined in order to give access to the header, the body and the QoS properties of the message.

Their signatures shall be:

public MALMessageHeader getHeader()

public MALMessageBody getBody()

public Map getQoSProperties()

If header field ‘isError’ is TRUE then the message ‘getBody’ shall return a MALErrorBody.

If the interaction type is PUBLISH-SUBSCRIBE and the stage is REGISTER then the message ‘getBody’ shall return a MALRegisterBody.

If the interaction type is PUBLISH-SUBSCRIBE and the stage is PUBLISH REGISTER then the message ‘getBody’ shall return a MALPublishRegisterBody.

If the interaction type is PUBLISH-SUBSCRIBE and the stage is PUBLISH then the message ‘getBody’ shall return a MALPublishBody.

If the interaction type is PUBLISH-SUBSCRIBE and the stage is NOTIFY then the message ‘getBody’ shall return a MALNotifyBody.

If the interaction type is PUBLISH-SUBSCRIBE and the stage is DEREGISTER then the message ‘getBody’ shall return a MALDeregisterBody.

#### Free

A method ‘free’ shall be defined in order to enable the transport to free resources owned by the MALMessage.

The method signature shall be:

public void free() throws MALException

The method shall be called by the MAL layer as soon as the MALMessage is no longer used.

If an internal error occurs then a MALException shall be raised.

### MALMessageListener

#### Definition

A MALMessageListener interface shall be defined in order to enable the MAL layer to be notified by the transport module when:

- a MALMessage has been received by a MALEndpoint;

- an asynchronous internal error has been raised by the transport layer as a consequence of a severe failure making the transport unable to work.

#### Receive a Message

A method ‘onMessage’ shall be defined in order to receive a message.

The method signature shall be:

public void onMessage(MALEndpoint callingEndpoint, MALMessage msg)

The ‘onMessage’ parameters shall be assigned as described in table 5-24.

Table 5-24:  MALMessageListener ‘onMessage’ Parameters

| Parameter | Description |
| --- | --- |
| callingEndpoint | MALEndpoint calling the MALMessageListener |
| msg | Message received by the listener |

#### Receive Multiple Messages

A method ‘onMessages’ shall be defined in order to receive multiple messages.

The method signature shall be:

public void onMessages(MALEndpoint callingEndpoint, MALMessage[] msgList)

The ‘onMessages’ parameters shall be assigned as described in table 5-25.

Table 5-25:  MALMessageListener ‘onMessages’ Parameters

| Parameter | Description |
| --- | --- |
| callingEndpoint | MALEndpoint calling the MALMessageListener |
| msgList | List of the messages received by the listener |

#### Severe Internal Error

A method ‘onInternalError’ shall be defined in order to receive an internal error.

The method signature shall be:

public void onInternalError(MALEndpoint callingEndpoint, java.lang.Throwable error)

The ‘onMessages’ parameters shall be assigned as described in table 5-26.

Table 5-26:  MALMessageListener ‘onInternalError’ Parameters

| Parameter | Description |
| --- | --- |
| callingEndpoint | MALEndpoint calling the MALMessageListener |
| error | Error to be received by the listener |

### MALTransmitErrorException

#### Definition

A MALTransmitErrorException class shall be defined in order to raise a TRANSMIT ERROR as an exception.

The class shall extend the class MALInteractionException.

#### Constructor

A constructor shall be defined.

The constructor signature shall be:

public MALTransmitErrorException(MALMessageHeader header,

MALStandardError standardError,

Map qosProperties)

The MALTransmitErrorException constructor parameters shall be assigned as described in table 5-27.

Table 5-27:  MALTransmitErrorException Constructor Parameters

| Parameter | Description |
| --- | --- |
| header | Header of the MALMessage which cannot be transmitted |
| standardError | Error preventing the message to be transmitted |
| qosProperties | QoS properties of the MALMessage which cannot be transmitted |

The constructor shall call the MALInteractionException constructor and pass the MALStandardError parameter.

#### Get the Header

A getter method ‘getHeader’ shall be defined in order to return the header of the MALMessage which cannot be transmitted.

The method signature shall be:

public MALMessageHeader getHeader()

#### Get the QoS Properties

A getter method ‘getQosProperties’ shall be defined in order to return the QoS properties of the MALMessage which cannot be transmitted.

The method signature shall be:

public Map getQosProperties()

### MALTransmitMultipleErrorException

#### Definition

A MALTransmitMultipleErrorException class shall be defined in order to raise a TRANSMITMULTIPLE ERROR as an exception.

The class shall extend the class MALException.

#### Constructor

A constructor shall be defined.

The method signature shall be:

public MALTransmitMultipleErrorException(

MALTransmitErrorException[] transmitExceptions)

The MALTransmitMultipleErrorException parameter shall be assigned as described in table 5-28.

Table 5-28:  MALTransmitMultipleErrorException Constructor Parameter

| Parameter | Description |
| --- | --- |
| transmitExceptions | Transmit errors preventing messages to be transmitted |

#### Get the Transmit Errors

A getter method ‘getTransmitExceptions’ shall be defined in order to return the Transmit errors raised by the MALMessages which Transmit failed.

The method signature shall be:

public MALTransmitErrorException[] getTransmitExceptions()

# Access Control API

## General

The access control API defines the interfaces and classes required by the MAL access control interface defined in reference [1].

The access control API shall be used by the MAL layer in order that any access control module that complies with this API can be plugged into the MAL layer.

## Classes and Interfaces

### General

The classes and interfaces of the access control API are contained in the package:

org.ccsds.moims.mo.mal.accesscontrol

### MALAccessControlFactory

#### Definition

A MALAccessControlFactory class shall be defined in order to enable the MAL layer to create and configure MALAccessControl instances.

This class shall be abstract.

The class shall be extended by every specific factory class.

The MALAccessControlFactory class shall provide a static factory class repository that maps the MALAccessControlFactory implementation classes to their class names.

#### Factory Class Registration

The MALAccessControlFactory class shall provide a static method ‘registerFactoryClass’ in order to register the class of a specific MALAccessControlFactory.

NOTE	–	This method may be useful in environments where several class loaders are involved (e.g., OSGi platforms).

The method signature shall be:

public static void registerFactoryClass(Class factoryClass)

throws java.lang.IllegalArgumentException

The ‘registerFactoryClass’ parameters shall be assigned as described in table 6-1.

Table 6-1:  MALAccessControlFactory ‘registerFactoryClass’ Parameters

| Parameter | Description |
| --- | --- |
| factoryClass | Class extending MALAccessControlFactory |

The method shall store the class in the factory class repository.

The method shall throw an IllegalArgumentException if the parameter ‘factoryClass’ does not extend MALAccessControlFactory.

#### Factory Class Deregistration

The MALAccessControlFactory class shall provide a static method ‘deregisterFactoryClass’ in order to deregister the class of a specific MALAccessControlFactory.

The method signature shall be:

public static void deregisterFactoryClass(Class factoryClass)

throws java.lang.IllegalArgumentException

The ‘deregisterFactoryClass’ parameters shall be assigned as described in table 5-3.

Table 6-2:  MALAccessControlFactory ‘deregisterFactoryClass’ Parameter

| Parameter | Description |
| --- | --- |
| factoryClass | Class extending MALAccessControlFactory |

The method shall remove the class from the factory class repository.

The method shall throw an IllegalArgumentException if the parameter ‘factoryClass’ does not extend MALAccessControlFactory.

The method shall do nothing if the class is not found in the factory class repository.

#### MALAccessControlFactory Creation

A static method ‘newFactory’ shall be defined in order to return a MALAccessControlFactory instance.

The method signature shall be:

public static MALAccessControlFactory newFactory() throws MALException

The method shall resolve the specific MALAccessControlFactory class name through the system property:

org.ccsds.moims.mo.mal.accesscontrol.factory.class

The method shall lookup the MALAccessControlFactory implementation class from the factory class repository.

If the class is not found in the factory class repository then it shall be loaded from the current class loader.

If the class is not found in the current class loader then a MALException shall be raised with the ClassNotFoundException as the cause.

The method ‘newFactory’ shall not return the value NULL.

If no MALAccessControlFactory can be returned then a MALException shall be raised.

#### MALAccessControl Instantiation

The factory class shall provide an abstract public method to instantiate a MALAccessControl.

The method’s signature shall be:

public abstract MALAccessControl createAccessControl(

java.util.Map properties) throws MALException

The createAccessControl parameter shall be assigned as described in table 6-3.

Table 6-3:  MALAccessControlFactory ‘createAccessControl’ Parameter

| Parameter | Description |
| --- | --- |
| properties | Configuration properties |

The parameter ‘properties’ may be NULL.

The method ‘createAccessControl’ shall not return the value NULL.

If no MALAccessControl can be returned then a MALException shall be raised.

This method shall be implemented by every specific factory class.

### MALAccessControl

#### Definition

A MALAccessControl interface shall be defined in order to implement the access control policy.

#### Check

A method ‘check’ shall be defined in order to intercept and check:

- outgoing messages before they are transmitted to the transport layer;

- incoming messages before they are delivered to the MAL client.

The method signature shall be:

public MALMessage check(MALMessage msg)

throws java.lang.IllegalArgumentException, MALCheckErrorException

The check parameter shall be assigned as described in table 6-4.

Table 6-4:  MALAccessControl ‘check’ Parameter

| Parameter | Description |
| --- | --- |
| msg | MALMessage to be checked |

If the parameter ‘msg’ is NULL then an IllegalArgumentException shall be raised.

The method shall be invoked by the MAL layer:

- before a MALMessage is sent through a MALEndpoint;

- after a MALMessage has been received by a MALMessageListener.

The method shall return the MALMessage to be handled by the MAL layer.

If a MALCheckErrorException is raised, the exception shall be transmitted to the MALMessage sender.

### MALCheckErrorException

#### Definition

A MALCheckErrorException class shall be defined in order to raise a CHECK ERROR as an exception.

The class shall extend the class MALInteractionException.

#### Constructor

A constructor shall be defined.

The method signature shall be:

public MALCheckErrorException(MALStandardError standardError,

Map qosProperties)

The MALCheckErrorException constructor parameters shall be assigned as described in table 5-27.

Table 6-5:  MALCheckErrorException Constructor Parameters

| Parameter | Description |
| --- | --- |
| standardError | Error preventing the message to be transmitted |
| qosProperties | QoS properties of the MALMessage which cannot be transmitted |

The constructor shall call the MALInteractionException constructor and pass the MALStandardError parameter.

#### Get the QoS Properties

A getter method ‘getQosProperties’ shall be defined in order to return the QoS properties of the MALMessage which cannot be transmitted.

The method signature shall be:

public Map getQosProperties()

# Encoding API

## Overview

The encoding API should be used by the transport modules that need to externalize the encoding behavior of a body element. The use of this encoding API is optional. The encoding API enables the transport layer to share and reuse any encoding module that complies with this API. However, a transport layer can implement the encoding behavior in an internal way without this API.

NOTE	–	Two types of encoding module can be implemented:

- A generic encoding module implements the MALEncoder and MALDecoder interfaces in order to encode and decode body elements in a generic way, i.e., by calling the generic methods ‘encode’ and ‘decode’ implemented by each specific structures.

- A specific encoding module does not implement the MALEncoder and MALDecoder interfaces. It encodes and decodes body elements in a specific way, e.g. by calling the getter and setter methods provided by the specific structures.

## Classes and interfaces

### General

The classes and interfaces of the encoding API are contained in the package:

org.ccsds.moims.mo.mal.encoding

### MALElementStreamFactory

#### Definition

A MALElementStreamFactory class shall be defined in order to create and configure:

- MALElementInputStream instances;

- MALElementOutputStream instances.

This class shall be abstract.

The class shall be extended by every specific factory class.

#### Factory Class Registration

The MALElementStreamFactory class shall provide a static method ‘registerFactoryClass’ in order to register the class of a specific MALElementStreamFactory.

NOTE	–	This method may be useful in environments where several class loaders are involved (e.g., OSGi platforms).

The method signature shall be:

public static void registerFactoryClass(Class factoryClass)

throws java.lang.IllegalArgumentException

The ‘registerFactoryClass’ parameters shall be assigned as described in table 7-1.

Table 7-1:  MALElementStreamFactory ‘registerFactoryClass’ Parameters

| Parameter | Description |
| --- | --- |
| factoryClass | Class extending MALElementStreamFactory |

The method shall store the class in the factory class repository.

The method shall throw an IllegalArgumentExceptionif the parameter ‘factoryClass’ does not extend MALElementStreamFactory.

#### Factory Class Deregistration

The MALElementStreamFactory class shall provide a static method ‘deregisterFactoryClass’ in order to deregister the class of a specific MALElementStreamFactory.

The method signature shall be:

public static void deregisterFactoryClass(Class factoryClass)

throws java.lang.IllegalArgumentException

The ‘deregisterFactoryClass’ parameters shall be assigned as described in table 7-2.

Table 7-2:  MALElementStreamFactory ‘deregisterFactoryClass’ Parameters

| Parameter | Description |
| --- | --- |
| factoryClass | Class extending MALElementStreamFactory |

The method shall remove the class from the factory class repository.

The method shall throw an IllegalArgumentException if the parameter ‘factoryClass’ does not extend MALElementStreamFactory.

The method shall do nothing if the class is not found in the factory class repository.

#### MALElementStreamFactory Creation

A static method ‘newFactory’ shall be defined in order to create a factory instance from a protocol name.

The method signature shall be:

public static MALElementStreamFactory newFactory(String protocol,

Map properties) throws MALException

The ‘newFactory’ parameters shall be assigned as described in table 7-3.

Table 7-3:  MALElementStreamFactory Creation Parameters

| Parameter | Description |
| --- | --- |
| protocol | Name of the protocol to be handled by the instantiated MALElementStreamFactory |
| properties | Configuration properties |

The parameter ‘protocol’ shall give the name of the protocol handled by the transport.

The parameter ‘properties’ shall give the properties of the MALTransport.

The method shall resolve the specific MALElementStreamFactory class name through the system property:

org.ccsds.moims.mo.mal.encoding.protocol.<<protocol name>>

NOTE	–	Each of those protocol properties is assigned with the class name of the MALElementStreamFactory. It should be noted that two different protocol properties can share the same MALElementStreamFactory class name. Below is an example of a configuration of protocol properties (the Java package is omitted in the class names):

# JMS transport with SOAP encoding

org.ccsds.moims.mo.mal.encoding.protocol.jmssoap  SoapElementStreamFactory

# Web Service transport with SOAP encoding

org.ccsds.moims.mo.mal.encoding.protocol.wssoap   SoapElementStreamFactory

# RMI transport with Java serialization encoding

org.ccsds.moims.mo.mal.encoding.protocol.rmiser   SerElementStreamFactory

The method shall lookup the MALElementStreamFactory implementation class from the factory class repository.

If the class is not found in the factory class repository then it shall be loaded from the current class loader.

If the class is not found in the current class loader then a MALException shall be raised with the ClassNotFoundException as the cause.

The method shall create an instance of MALElementStreamFactory by calling the empty constructor provided by the implementation class.

The method ‘newFactory’ shall not return the value NULL.

If no MALElementStreamFactory can be returned then a MALException shall be raised.

Once the instance is created, the method ‘init’ provided by MALElementStreamFactory shall be called.

#### MALElementStreamFactory Initialization

A method ‘init’ shall be defined in order to enable the specific implementation class to initialize the encoding module.

The method signature shall be:

protected abstract void init(String protocol, Map properties)

throws java.lang.IllegalArgumentException, MALException

The ‘init’ parameters shall be assigned as described in table 7-4.

Table 7-4:  MALElementStreamFactory ‘init’ Parameters

| Parameter | Description |
| --- | --- |
| protocol | Name of the protocol passed through the instantiation method |
| properties | Properties passed through the instantiation method |

If the parameter ‘protocol’ is NULL then an IllegalArgumentException shall be raised.

The parameter ‘properties’ may be NULL.

If an internal error occurs then a MALException shall be raised.

#### MALElementInputStream Instantiation

Two methods ‘createInputStream’ shall be defined in order to enable the transport layer to create a MALElementInputStream:

- the first one shall declare an input stream parameter;

- the second one shall declare a byte array parameter.

The method signature shall be:

public abstract MALElementInputStream createInputStream(

java.io.InputStream is)

throws java.lang.IllegalArgumentException, MALException

public abstract MALElementInputStream createInputStream(

byte[] bytes, int offset)

throws java.lang.IllegalArgumentException, MALException

The createInputStream parameter shall be assigned as described in table 7-5.

Table 7-5:  MALElementStreamFactory ‘createInputStream’ Parameter

| Parameter | Description |
| --- | --- |
| is | InputStream (java.io) used by the transport layer to decode Elements |
| bytes | the bytes to be decoded |
| offset | the index of the first byte to decode |

If the parameter ‘is’ or ‘bytes’ is NULL then an IllegalArgumentException shall be raised.

#### MALElementOutputStream Instantiation

A method ‘createOutputStream’ shall be defined in order to enable the transport layer to create a MALElementOutputStream.

The method signature shall be:

public abstract MALElementOutputStream createOutputStream(

java.io.OutputStream os)

throws java.lang.IllegalArgumentException, MALException

The createOutputStream parameter shall be assigned as described in table 7-6.

Table 7-6:  MALElementStreamFactory ‘createOutputStream’ Parameter

| Parameter | Description |
| --- | --- |
| os | OutputStream (java.io) used by the transport layer to encode Elements |

#### Encode Elements

A method ‘encode’ shall be defined in order to encode an element array and return the encoding result as a byte array.

The method signature shall be:

public abstract byte[] encode(Object[] elements, MALEncodingContext ctx)

throws MALException

The ‘encode’ parameters shall be assigned as described in table 7-9.

Table 7-7:  MALElementStreamFactory ‘encode’ Parameters

| Parameter | Description |
| --- | --- |
| elements | Elements to encode |
| ctx | MALEncodingContext to be used in order to encode the elements |

The parameters ‘elements’ or ‘ctx’ are NULL then an IllegalArgumentException shall be raised.

The allowed types for each encoded element shall be:

- MAL element types;

- MALEncodedElement;

- List<MALEncodedElement>;

- Java types defined by a specific Java mapping extension.

### MALElementInputStream

#### Definition

A MALElementInputStream interface shall be defined in order to decode Elements.

#### Read an Element

A method ‘readElement’ shall be defined in order to decode an Element.

The method signature shall be:

public Object readElement(Object element, MALEncodingContext ctx)

throws java.lang.IllegalArgumentException, MALException

The ‘readElement’ parameters shall be assigned as described in table 7-8.

Table 7-8:  MALElementInputStream ‘readElement’ Parameters

| Parameter | Description |
| --- | --- |
| element | Element to decode |
| ctx | MALEncodingContext to be used in order to decode an Element |

The parameter ‘element’ may be NULL.

The allowed types for the parameter ‘element’ shall be:

- MAL element types;

- Java types defined by a specific Java mapping extension.

If the parameters ‘ctx’ is NULL then an IllegalArgumentException shall be raised.

If the MALElementInputStream is closed then a MALException shall be raised.

The returned element may be not the same instance as the parameter ‘element’.

The allowed returned element types shall be:

- MAL element types;

- MALEncodedElement;

- List<MALEncodedElement>;

- Java types defined by a specific Java mapping extension.

#### Close

A method ‘close’ shall be defined in order to close the stream.

The method signature is:

public void close() throws MALException

The method shall call the method ‘close’ provided by the InputStream (java.io) owned by this MALElementInputStream.

If an internal error occurs then a MALException shall be raised.

### MALElementOutputStream

#### Definition

A MALElementOutputStream interface shall be defined in order to encode Elements.

#### Write an Element

A method ‘writeElement’ shall be defined in order to encode an Element.

The method signature shall be:

public void writeElement(Object element, MALEncodingContext ctx)

throws java.lang.IllegalArgumentException, MALException

The ‘writeElement’ parameters shall be assigned as described in table 7-9.

Table 7-9:  MALElementOutputStream ‘writeElement’ Parameters

| Parameter | Description |
| --- | --- |
| element | Element to encode |
| ctx | MALEncodingContext to be used in order to encode the Element |

The parameter ‘element’ may be NULL.

The allowed types for the parameter ‘element’ shall be:

- MAL element types;

- MALEncodedElement;

- List<MALEncodedElement>;

- Java types defined by a specific Java mapping extension.

If the parameter ‘ctx’ is NULL then an IllegalArgumentException shall be raised.

If the MALElementOutputStream is closed then a MALException shall be raised.

#### Flush the Stream

A method ‘flush’ shall be defined in order to flush the stream.

The method signature shall be:

public void flush() throws MALException

The method shall write all the buffered data owned by this MALElementOutputStream. Moreover it shall call the method ‘flush’ provided by the OutputStream (java.io) owned by this MALElementOutputStream.

If an internal error occurs then a MALException shall be raised.

If the MALElementOutputStream is closed then a MALException shall be raised.

#### Close

A method ‘close’ shall be defined in order to close the stream.

The method signature is:

public void close() throws MALException

The implementation shall call the method ‘close’ provided by the OutputStream (java.io) owned by this MALElementOutputStream.

If an internal error occurs then a MALException shall be raised.

### MALEncodingContext

#### Definition

A class MALEncodingContext shall be defined in order to give access to:

- the header of the MALMessage that contains the Element to encode or decode;

- the description of the operation that has been called;

- the index of the body element to encode or decode;

- the list of the QoS properties owned by the MALEndpoint that sends or receives the Element;

- the list of the QoS properties owned by the MALMessage that contains the Element to encode or decode.

#### Getters and Setters

Getter and setter methods shall be defined in order to give access to the attributes listed in table 7-10.

Table 7-10:  MALEncodingContext Attributes

| Attributes | Type |
| --- | --- |
| header | MALMessageHeader |
| operation | MALOperation |
| bodyElementIndex | int |
| endpointQosProperties | java.util.Map |
| messageQosProperties | Java.util.Map |

# COM Service Mapping

## Overview

This section explains how to map a service using the COM service template to Java. The COM service template is defined in the reference [1].

This section uses variables that are related to the COM XML Schema, i.e., each variable is linked to an XPath enabling to unambiguously resolve the values to be assigned to this variable.

## Definition

The COM service mapping shall be done in two steps:

- add the COM operations to the service using the COM template and assign the placeholder as defined by this section;

- apply the MAL service mapping defined in section 4.

This section uses variables which values shall be resolved as described in the table [COM Service Mapping Variables]; the following rules shall be applied:

- the default namespace shall be http://www.ccsds.org/schema/ServiceSchema;

- the “com” namespace shall be http://www.ccsds.org/schema/COMSchema;

- the “xsd” namespace shall be http://www.w3.org/2001/XMLSchema-instance;

- the default current XPath context shall be the element “specification”;

- each variable shall be assigned with the value specified by the XPath;

- in the context of the parent of the element specified by the XPath, several values may be assigned to a variable;

- if the last column mentions “Attribute value” then the value of the specified XML attribute shall be assigned;

- if the last column mentions “Type name” then the name of the MAL data type shall be assigned.

Table 8-1:  COM Service Mapping Variables

| Variable name | Current context | Element or attribute | Value |
| --- | --- | --- | --- |
| service schema type | area/ | service/@xsd:type | Attribute value |
| definition type | area/service/ | com::includesDefinition/ com:objectType | Type name |
| occurrence type | area/service/ | com::includesOccurrence/ com:objectType | Type name |
| status type | area/service/ | com::includesStatus/ com:objectType | Type name |
| event type | area/service/ | com::includesEvent/ com:objectType | Type name |
| definition update type | area/service/ | com::includesDefinition/ com:updateType | Type name |
| occurrence update type | area/service/ | com::includesOccurrence/ com:updateType | Type name |
| status update type | area/service/ | com::includesStatus/ com:updateType | Type name |

## COM Operations

A service which <<service schema type>> is “com:ExtendedServiceType” shall be modified by adding COM operations.

If the service defines a <<definition type>> then the COM operations from the capability sets 1, 2, 3, 4 and the definition retrieval operations shall be added and the placeholders shall be assigned as follows:

- the placeholder DEFINITION shall be assigned with <<definition type>>;

- if the service defines a <<definition update type>> then the placeholder DEFINITION_UPDATE shall be assigned with <<definition update type>> otherwise it shall be assigned with <<definition type>>.

If the service defines an <<occurrence type>> then the COM operations from the capability sets 5, 6, 7, 8 and the occurrence retrieval operations shall be added and the placeholders shall be assigned as follows:

- the placeholder OCCURRENCE shall be assigned with <<occurrence type>>;

- if the service defines an <<occurrence update type>> then the placeholder OCCURRENCE_UPDATE shall be assigned with <<occurrence update type>> otherwise it shall be assigned with <<occurrence type>>.

If the service defines a <<status type>> then the COM operations from the capability sets 9, 10 and the status retrieval operations shall be added and the placeholders shall be assigned as follows:

- the placeholder STATUS shall be assigned with <<status type>>;

- if the service defines a <<status update type>> then the placeholder STATUS_UPDATE shall be assigned with <<status update type>> otherwise it shall be assigned with <<status type>>.

If the service defines an <<event type>> then the COM operations from the capability sets 11, 12 and the event retrieval operations shall be added and the placeholder EVENT shall be assigned with <<status type>>.

## Generic COM Service

The COM service template shall be mapped to a generic COM service.

The COM operations from the capability sets 1, 2, 3, 4 and the definition retrieval operations shall be modified by assigning the placeholders DEFINITION and DEFINITION_UPDATE with the abstract type COM::Definition.

The COM operations from the capability sets 5, 6, 7, 8 and the occurrence retrieval operations shall be modified by assigning the placeholders OCCURRENCE and OCCURRENCE_UPDATE with the abstract type COM::Occurrence.

The COM operations from the capability sets 9, 10 and the status retrieval operations shall be modified by assigning the placeholders STATUS and STATUS_UPDATE with the abstract type COM::Status.

The COM operations from the capability sets 11, 12 and the event retrieval operations shall be modified by assigning the placeholder EVENT with the abstract type COM::Event.

Definition of ACRONYMS

(Informative)

API		Application Programming Interface

BLOB		Binary Large OBject

IP		Interaction Pattern

JVM		Java Virtual Machine

MAL		Message Abstract Layer

MO		Mission Operations

QoS		Quality of Service

SM&C	CCSDS Spacecraft Monitor & Control

URI		Uniform Resource Identifier

URL		Uniform Resource Locator

Informative References

(Informative)

[B1]	Mission Operations Services Concept.  Report Concerning Space Data System Standards, CCSDS 520.0-G-3.  Green Book.  Issue 3.  Washington, D.C.: CCSDS, [forthcoming].

[B2]	Mission Operations Reference Model.  Recommendation for Space Data System Standards, CCSDS 520.1-M-1.  Magenta Book.  Issue 1.  Washington, D.C.: CCSDS, July 2010.

NOTE	–	Normative references are listed in section 1.8.

Code Example

(Informative)

Overview

This annex contains a code example for launching a consumer and a provider of the service ExampleArea::ExampleService.

Handler implementation code

The following class is a code template for the handler implementation using the inheritance model:

public class ExampleServiceHandlerImpl

extends ExampleServiceInheritanceSkeleton {

public void exampleSubmitOperation(ExampleParameter parameter,

MALInteraction interaction) throws MALException {

// …

}

}

Provider launching code

This is the main method that launches an instance of ExampleService provider:

public static void main(String[] args) throws Exception {

MALContextFactory malContextFactory = MALContextFactory.newFactory();

MALContext malContext =

malContextFactory.createMALContext(new Properties());

ExampleAreaHelper.init(

MALContextFactory.getDefaultElementFactoryRegistry());

ExampleServiceHelper.init(

MALContextFactory.getDefaultElementFactoryRegistry());

MALProviderManager providerMgr = malContext.createProviderManager();

ExampleServiceHandlerImpl handler = new ExampleServiceHandlerImpl();

URI brokerURI = null; // the broker is private

MALProvider provider = providerMgr.createProvider(

"<<Provider name>>",

"<<Protocol name>>",

ExampleServiceHelper.EXAMPLESERVICE_SERVICE,

new Blob(),

handler,

new QoSLevel[] { QoSLevel.ASSURED },

1,

new Hashtable(),

new Boolean(true),

brokerURI);

System.out.println("ExampleService URI: " + provider.getURI());

System.out.println("ExampleService broker URI: "

+ provider.getBrokerURI());

}

Consumer launching code

This is the main method that launches an instance of ExampleService consumer:

public static void main(String[] args) throws Exception {

MALContextFactory malContextFactory = MALContextFactory.newFactory();

MALContext malContext =

malContextFactory.createMALContext(new Properties());

ExampleAreaHelper.init(

MALContextFactory.getDefaultElementFactoryRegistry());

ExampleServiceHelper.init(

MALContextFactory.getDefaultElementFactoryRegistry());

MALConsumerManager consumerMgr = malContext.createConsumerManager();

MALConsumer consumer = consumerMgr.createConsumer(

"<<consumer name>>",

new URI("<<provider URI>>"),

new URI("<<broker URI>>"),

ExampleServiceHelper.EXAMPLESERVICE_SERVICE,

new Blob(new byte[0]),

new IdentifierList(),

new Identifier("networkZone"),

SessionType.LIVE,

new Identifier("LIVE"),

QoSLevel.ASSURED,

new Hashtable(),

new UInteger(0));

ExampleServiceStub stub = new ExampleServiceStub(consumer);

}

Shared Broker launching code

If a shared broker is needed then the following main method should also be executed:

public static void main(String[] args) throws Exception {

MALContextFactory malContextFactory = MALContextFactory.newFactory();

MALContext malContext =

malContextFactory.createMALContext(new Properties());

ExampleAreaHelper.init(

MALContextFactory.getDefaultElementFactoryRegistry());

ExampleServiceHelper.init(

MALContextFactory.getDefaultElementFactoryRegistry());

MALBrokerManager brokerManager = malContext.createBrokerManager();

MALBroker sharedBroker = brokerManager.createBroker(

ExampleServiceHelper.EXAMPLESERVICE_SERVICE);

MALBrokerBinding sharedBrokerBinding =

brokerManager.createBrokerBinding(

sharedBroker,

"<<Broker name>>",

"<<Protocol name>>",

new Blob(new byte[0]),

new QoSLevel[] {QoSLevel.ASSURED},

1,

new Hashtable());

System.out.println("Shared broker URI: "

+ sharedBrokerBinding.getURI());

}

# Footnotes

The Java binding namespace is to be defined in a CCSDS-wide registry within the Space Assigned Numbers Authority (SANA).