Draft Recommendation for
Space Data System Standards

Mission Operations Common Services

Draft Recommended Standard

CCSDS 522.0-R-2 Draft 2

Red Book

October 2014

AUTHORITY

|  | Issue: | Red Book, Issue 2-Draft 2 |  |
| --- | --- | --- | --- |
|  | Date: | October 2014 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in the Procedures Manual for the Consultative Committee for Space Data Systems, and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This document is published and maintained by:

CCSDS Secretariat

Office of Space Communication (Code M-3)

National Aeronautics and Space Administration

Washington, DC  20546, USA

STATEMENT OF INTENT

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF INTENT:)

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

o	Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

o	Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

o	Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible.  It is the responsibility of each member to determine when such standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in the Procedures Manual for the Consultative Committee for Space Data Systems.  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- British National Space Centre (BNSC)/United Kingdom.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- Deutsches Zentrum für Luft- und Raumfahrt e.V. (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- Centro Tecnico Aeroespacial (CTA)/Brazil.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- MIKOMTEK: CSIR (CSIR)/Republic of South Africa.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Organization (NSPO)/Taiwan.

- Naval Center for Space Technology (NCST)/USA.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard.  Its ‘Red Book’ status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations.  As such, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

# DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS 522.0-R-2 Draft 2 | Mission Operations Common Services, Draft Recommended Standard, Issue 2-Draft 2 | October 2014 | Current draft |

# CONTENTS

Section	Page

1	Introduction	1-1

1.1	General	1-1

1.2	Purpose and Scope	1-1

1.3	Applicability	1-1

1.4	Rationale	1-1

1.5	Document structure	1-2

1.6	Definition of Terms	1-2

1.7	NOMENCLATURE	1-4

1.8	Conventions	1-4

1.9	References	1-5

2	Overview	2-6

2.1	General	2-6

2.2	Directory Service	2-7

2.3	Login Service	2-9

2.4	Interact Service	2-9

2.5	Replay service	2-10

2.6	Configuration Service	2-11

3	Specification: Common	3-1

3.1	General	3-1

3.2	Service: Directory	3-1

3.3	Service: Login	3-6

3.4	Service: Interact	3-15

3.5	Service: Replay	3-38

3.6	Service: Configuration	3-49

4	Data types	4-53

4.1	Service data types: Directory	4-53

4.2	Service data types: Login	4-57

4.3	Service data types: Interact	4-58

4.4	Service data types: Replay	4-60

5	Error codes	5-63

6	SERVICE SPECIFICATION XML	6-64

ANNEX A Protocol IMPLEMENTATION CONFORMANCE Statement Proforma  (Normative)	A-1

ANNEX B Security, SANA, and Patent Considerations  (Informative)	B-1

ANNEX C Definition of Acronyms  (Informative)	C-1

ANNEX D Informative References  (Informative)	D-1

ANNEX E Informative References  (Informative)	E-2

Figure

2-1	Mission Operations Services Concept Document Set	2-7

2-2	Directory Service Concept	2-8

Table

1-1	Example Operation Template	1-5

2-1	Message Header Fields	2-8

3-1Directory Service Operations	3-2

3-2Directory Service Object Types	3-2

3-1Directory Service COM object relationships	3-3

3-3Login Service Operations	3-7

3-4Login Service Object Types	3-8

3-5Login Service Events	3-8

3-2Login Service COM object and event relationships	3-9

3-6Interact Service Operations	3-16

3-7Interact Service Object Types	3-18

3-8Interact Service Events	3-19

3-3Interact Service COM object and event relationships	3-20

3-9Replay Service Operations	3-38

3-10Replay Service Object Types	3-39

3-11Replay Service Events	3-40

3-4Replay Service COM object and event relationships	3-40

3-12Configuration Service Operations	3-49

3-13Configuration Service Object Types	3-50

3-14Configuration Service Events	3-50

3-5Configuration Service COM object and event relationships	3-51

5-1Common Error Codes	5-63

# Introduction

## General

This Recommended Standard defines the Mission Operations (MO) Common Services in conformance with the service framework specified in reference [B1] of annex B, Mission Operations Services Concept.

The Common Services are a set of services that provide support facilities to the Mission Operation services.

These services are defined in terms of the Common Object Model (COM) R[3] and the Message Abstraction Layer (MAL) R[2].

## Purpose and Scope

This Recommended Standard defines, in an abstract manner, the Common services in terms of:

- the operations necessary to provide the service;

- the parameter data associated with each operation;

- the required behaviour of each operation;

- the use of the model.

It does not specify:

- individual implementations or products;

- the implementation of entities or interfaces within real systems;

- the methods or technologies required for communications.

## Applicability

This specification is applicable to any system component that utilises a common infrastructure for service discovery. Nominally, but not exclusively, this applies to ground control systems to external entities and between external entities.

## Rationale

The primary goal of CCSDS is to increase the level of interoperability among agencies. This Recommended Practice furthers that goal by providing a standard service specification for the discovery of services and also common infrastructure services.

## Document structure

This Recommended Standard is organised as follows:

- section 1 provides purpose and scope, applicability, and rationale of this Recommended Practice and lists the definitions, conventions, and references used throughout the document;

- section 2 presents an overview of the concepts;

- section 3 presents the Common Services specification;

- section 4 is a formal specification of the Common Services data structures;

- section 5 is a formal specification of the Common Services errors;

- section 6 specifies the internet location of the formal service specification eXtensible Markup Language (XML).

## Definition of Terms

software component (component): A software unit supporting the business function. Components offer their function as services, which can either be used internally or which can be made available for use outside the component through provided service interfaces. Components may also depend on services provided by other components through consumed service interfaces.

hardware component: A complex physical entity (such as a spacecraft, a tracking system, or a control system) or an individual physical entity of a system (such as an instrument, a computer, or a piece of communications equipment). A hardware component may be composed from other hardware components. Each hardware component may host one or more software components. Each hardware component has one or more ports where connections to other hardware components are made. Any given port on the hardware component may expose one or more service interfaces.

service: A set of capabilities that a component provides to another component via an interface. A service is defined in terms of the set of operations that can be invoked and performed through the service interface. Service specifications define the capabilities, behaviour, and external interfaces, but do not define the implementation.

service interface: A set of interactions provided by a component for participation with another component for some purpose, along with constraints on how they can occur. A service interface is an external interface of a service where the behaviour of the service provider component is exposed. Each service will have one defined ‘provided service interface’ and may have one or more ‘consumed service interface’ and one ‘management service interface’.

provided service interface: A service interface that exposes the service function contained in a component for use by service consumers. It receives the MAL messages from a consumed service interface and maps them into Application Program Interface (API) calls on the provider component.

consumed service interface: The API presented to the consumer component that maps from the Service operations to one or more Service Data Units (SDUs) contained in MAL messages that are transported to the provided service interface.

management service interface: A service interface that exposes management functions of a service function contained in a component for use by service consumers.

service provider (provider): A component that offers a service to another by means of one of its provided service interfaces.

service consumer (consumer): A component that consumes or uses a service provided by another component. A component may be a provider of some services and a consumer of others.

service data unit, SDU: A unit of data that is sent by a service interface and is transmitted, semantically unchanged, to a peer service interface.

service extension: Addition of capabilities to a base service. A service may extend the capabilities of another service with additional operations. An extended service is indistinguishable from the base service to consumers such that consumers of the base service can also be consumers of the extended service without modification.

service capability set: A grouping of service operations. The specification of services is based on the expectation that different deployments require different levels of complexity and functionality from a service. To this end a given service may be implementable at one of several distinct levels, corresponding to the inclusion of one or more capability sets. The capability sets define a grouping of the service operations that remains sensible and coherent; it also provides a service provider with an ability to communicate to a consumer its capability.

service directory: an entity that provides publish and lookup facilities to service providers and consumers.

NOTE	–	Strictly speaking, a directory is not required if a well-known service is to be used; however, in most circumstances a directory provides required flexibility in the location of services. Service location can be statically configured, dynamically discovered through a service directory, or a combination of the two; this is an implementation choice. The service directory is itself, by definition, a service.

## NOMENCLATURE

### Normative Text

The following conventions apply for the normative specifications in this Recommended Standard:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification;

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

NOTE	–	These conventions do not imply constraints on diction in text that is clearly informative in nature.

### Informative Text

In the normative sections of this document, informative text is set off from the normative specifications either in notes or under one of the following subsection headings:

- Overview;

- Background;

- Rationale;

- Discussion.

## Conventions

### Figures

In figures illustrating this document, Unified Modelling Language (UML) modelling diagrams are used. Reference [2] provides further information regarding diagrams types and their meaning.

### Tables

The table format information presented here is extracted from section 2 of reference [2]. It is repeated here to aid in understanding tables as they are presented in this document. A full description of the table formats presented in this document can be found in section 2 of reference [2] and in section 2 of reference [3].

Each interaction pattern definition contains a table that defines the template for operations that use that pattern.

Table 1-1:  Example Operation Template

| Operation Identifier | <<Operation name>> |
| --- | --- |
| Interaction Pattern | <<Interaction pattern name>> |
| Pattern Sequence | Message | Body Type |
| <<Message direction>> | <<Message name>> | <<Message type>> |
| … | … | … |

The message direction denotes the direction of the message relative to the provider of the pattern and is either IN or OUT. So all messages directed towards the provider are IN messages, and all messages directed away from the provider are OUT messages.

Blue cells (dark grey when printed on a monochrome printer) contain table headings, light grey cells contain fields that are fixed for a pattern, and white cells contain values that must be provided by the operation or structure.

## References

The following documents contain provisions which, through reference in this text, constitute provisions of this Recommended Standard.  At the time of publication, the editions indicated were valid.  All documents are subject to revision, and users of this Recommended Standard are encouraged to investigate the possibility of applying the most recent editions of the documents indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS Recommended Standards.

- Mission Operations Reference Model. Issue 1. Recommendation for Space Data System Practices (Magenta Book), CCSDS 520.1-M-1. Washington, D.C.: CCSDS, July 2010.

- Mission Operations Message Abstraction Layer. Issue 2. Recommendation for Space Data System Standards (Blue Book), CCSDS 521.0-B-2. Washington, D.C.: CCSDS, March 2013.

- Mission Operations Common Object Model. Issue 1. Recommendation for Space Data System Standards (Blue Book), CCSDS 521.1-B-1. Washington, D.C.: CCSDS, February 2014.

NOTE	–	Informative references are listed in ANNEX E.

# Overview

## General

The Common Services provide infrastructure services to support the mission operations services. These Common services cover the following aspect of a system:

- Directory

- Service publish and lookup

- Login

- Operator login

- Configuration

- Service configuration management

- Interaction

- Operator interaction

- Replay

- Replay session management and control

The Common services provide functions that exist in the vast majority of systems but have previously been proprietary.

The following diagram presents the set of standards documentation in support of the Mission Operations Services Concept. The Common services belong to the Specifications documentation.

Figure 2-1:  Mission Operations Services Concept Document Set

NOTE	–	References [D1] and [1] contain additional information about the MO Services Concept and the MO Reference Model, respectively.

The MO Common services build upon the layering concept outlined in reference [D1] and are defined in terms of the MO MAL outlined in reference [2], so it is possible to deploy them over any supported protocol and message transport. The Common services are also defined in terms of the COM, as defined in reference [3], and builds upon the COM event service and the COM archive.

NOTE	–	The services defined in this specification are not dependent on any of the other services, other than the COM services, and are complete in their own right. An implementation is free to opt out of any service and also any capability set of these services; however, it may not make sense to support certain services without others.

## Directory Service

The directory service provides publish and lookup facilities to service providers and consumers. It allows providers to publish their location in the form of a URI (Universal Resource Indicator) so that consumers can locate it without having to know in advance the location. Strictly speaking a directory is not required if a well-known service is to be used; however, in most circumstances a directory provides required flexibility in the location of services.

Figure 2-2:  Directory Service Concept

A service provider publishes to the directory service the set of services, and the capabilities of those services, that it supports for a specific Domain, Network Zone and Session.

Each entry for a service provider contains the associated service information such as capability sets, the QoS (Quality of Service) levels that it can provide, and the URIs required to locate it. Capability sets provide a quick way for service providers to inform consumers of which optional capabilities of a service they support.

The addressing information associated to a service provider, the QoS and URI aspects, are held as a list which allows a service provider to support more than one type of QoS and message transport technology in parallel.

The service directory does not contain any information about the relationships between services that are physically located in a single provider application, only that a provider supports several services. This is considered outside of the scope of the Directory service.

The Directory service cannot be used by clients to locate the Directory service itself, therefore another means of determining the address of it (usually configuration) is required.

### Service provider properties

Each entry in the Directory service for a particular service contains a list of named properties that can be defined by the implementing service provider for passing of relevant information to a service consumer. This list is open ended in so much that any values can be added, however Table 2-1 lists the standard properties and their meanings:

Table 2-1:  Standard Service Provider Properties

| Property identifier | Permitted values | Default value | Description |
| --- | --- | --- | --- |
| TIMEREF | UTC TAI GPS | UTC | Defines the epoch of the time values obtained from this service provider. It is possible an implementation specific time reference is used however this is outside the scope of this specification. |

## Login Service

The Login service allows an operator to provide authentication information to the system. It takes the operator’s credentials and uses a deployment-specific mechanism to authenticate the operator; the result of this is used by the MAL during access control.

The Login service and the access control provided by the MAL are fully dependent on a deployment-specific security architecture (for example the authentication protocol Kerberos). Both layers (Common and MAL) provide access to, and use of, this security service. Neither implement this themselves. See reference [1] for more information regarding access control.

## Interact Service

When a component of the system requires some input from an operator, for example confirmation of a critical operation, the interaction service allows a component to request that information from an appropriate operator.

Four types of operator interaction are supported:

- Acknowledge

Operator is required to acknowledge an operation (simple ‘Ok’ style interaction).

- Confirm

Operator is required to confirm or decline an operation (‘Yes/No’ style interaction).

- Choice

Operator is presented with a list of options to choose from (drop down list of choices).

- Get values

Operator is required to provide a set of values (value entry boxes).

It is also possible that a software component targets a role rather than a specific user;  it may be the case that the software component requires interaction from an operator, but one of several may provide the response. The username of the operator that responds to an interaction is returned to the consumer when the interaction is completed so that the operator in question can be referenced directly in future interactions if appropriate.

How a component or application determines which role or operator to interact with is an implementation-specific detail that is outside the scope of the Recommended Standard.

### Replay service

A historical replay is considered to be a session distinct from other active sessions such as the current live session or simulation sessions. Each replay session is created based on an existing live or simulation session; the replay session is a read-only copy of the base session that can be ‘browsed’ under consumer control.

The replay service allows a consumer to create, control, and delete replay sessions. Once a replay has been created, a consumer can:

- single step through history forwards and backwards;

- play the history forwards and backwards;

- adjust the replay rate of the replay session;

- delete the replay session.

The creation of the replay session returns a set of service details, similar to what is returned by the directory service, detailing all the services supported by the replay session. It is entirely possible for a replay session to be published under a directory service, as it uses the directory service structures for detailing its location information.

It should be noted that the replay session is effectively read-only as far as the data is concerned: any service or operation that would result in a modification to history is not permitted (for example the request for an interaction from the interaction service). However, operations that affect the delivery of history are still possible as they are just altering the state of the replay session service providers rather than the data itself.

The service specifications mark whether a specific operation is permitted during a replay session; if an operation is not supported during replay then any attempt to call it results in the standard error of NOT_IN_REPLAY being returned.

## Configuration Service

The configuration service provides the ability to transfer the configuration of a service to and from a service provider. It provides facilities for the management of configurations held by a provider if applicable to that implementation.

Implementations of the configuration service may support bespoke configuration upload mechanisms (such as file upload).  This is supported by the configuration specification where consumers would be notified of a new configuration; however, the details of these upload methods are outside of the scope of the Recommended Standard.

The specific configuration of a service is not covered in this Recommended Standard; however, it is fully expected that services may require some degree of configuration, for example, the list of telemetry parameters. Both the consumer and the provider must agree on the contents of this configuration, but it is outside of the scope of the specification to define how this configuration is defined. This Recommended Standard only defines how configurations are exchanged and managed.

# Specification: Common

## General

This section details the Common Services; the structures used by the services are detailed in section 4. The services and structures are defined in terms of the MO Message Abstraction Layer (MAL) which is defined in reference [2], so it is possible to deploy them over any supported protocol and message transport.

The services defined here are also specified in terms of the COM which is defined in reference [3].

To aid comprehension several tables are included for each service and operation definition. The table formats are the same as those used for the specification of the MO COM Services in reference [3]. The formats are fully described in reference [2] in section 2 and in reference [3] section 2, for COM usage.

All service specifications in this document are part of the Common Area. This has a short form number of '3'.

## Service: Directory

### General

The Directory service allows service providers to publish information about which services they provide and consumers to discover service provider address and capability information.

Service provider information is made available using the Directory service publishService operation and removed using the withdrawService operation.

The lookupService operation provides the ability for consumers to query the directory service based on a filter such as required service capability.

A service provider publishes, using the publishService operation, the set of services and the capabilities of those services that it offers. It also publishes with the capabilities one or more set of address information which defines one way to contact that service provider. It is possible for a provider to offer multiple service addresses as it allows the provider to support multiple message transports and encodings. Each service address lists the supported QoS levels and associated QoS properties available for that connection; a service consumer indicates the required QoS level and priority to a service provider by using these values in the initial message.

For services that have operations based on the publish and subscribe interaction pattern there may be required a separate URI for the broker component. To support this the directory service holds two URIs for each service, the URI of the primary interface and also a secondary one which, if present, is used for publish and subscribe-based operations. It is also possible that a publish and subscribe broker component is shared between more than one provider, known as a shared broker, and in this case the broker should be published as a directory service entry without a primary interface URI. The sharing providers should reference it by referencing it in the 'dataProviderObjInstId' field in their directory service entry.

Table 3-1:  Directory Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| Common | Directory | 3 | 1 | 1 |
| Interaction Pattern | Operation Identifier | Operation Number | Support in Replay | Capability Set |
| REQUEST | lookupService | 1 | Yes | 1 |
| REQUEST | publishService | 2 | No | 2 |
| SUBMIT | withdrawService | 3 | No |  |

### High Level Requirements

- The directory service shall provide:

  - the capability for requesting service provider details based on a filter;

  - the capability for publishing new service provider details;

  - the capability for withdrawing service provider details.

### COM usage

- Service providers shall be represented as ServiceProvider COM objects in the directory service.

- ServiceProvider objects shall be created by the publishService operation.

- The object instance identifier for a ServiceProvider object shall be populated by the provider of the directory service.

- The ServiceProvider object related link shall not be used and therefore set to NULL.

- The ServiceProvider object source link shall not be used and therefore set to NULL.

- For the ProviderAddressDetails of a particular ServiceProvider object, if the dataProviderObjInstId field contains a value and the dataURI field is NULL, then the dataURI value of the referenced provider shall be used.

Table 3-2:  Directory Service Object Types

| Object Name | Object Number | Object Body Type | Related points to |
| --- | --- | --- | --- |
| ServiceProvider | 1 | ProviderDetails | Not used |

### COM Object Relationships

The Figure below shows the COM object relationships for this service:

Figure 3-1:  Directory Service COM object relationships

### COM Archive Service usage

All directory objects should be stored in the COM archive by the provider of the service.

### OPERATION: lookupService

#### General

The lookup operation allows a service consumer to query the directory service to determine if a specific service is available. If no match is found, then an empty list is returned.

| Operation Identifier | lookupService |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | filter : (ServiceFilter) |
| OUT | RESPONSE | matchingProviders : (List<ProviderSummary>) |

#### Structures

- The lookup operation shall take a single ServiceFilter structure.

- If the final identifier of the domain field of the filter is the wildcard '*', then all sub-domains shall be searched for matches.

- If the wildcard is used is any other part of the domain other than the final one then an INVALID error shall be returned.

- If the domain field only contains the wildcard '*' then all domains shall be matched.

- If the network field is the wildcard '*' then all networks shall be matched.

- If the sessionType field is NULL then all session types shall be matched.

- If the sessionName field is the wildcard '*' then all session names shall be matched.

- If the area field is the wildcard '*' then all areas names shall be matched.

- If the service field is the wildcard '*' then all services shall be matched.

- If the version field is the wildcard '*' then all area versions shall be matched.

- If the requiredCapabilities field is an empty list then all service capability sets shall be matched.

- If the serviceProviderName field is the wildcard '*' then all service provider names shall be matched.

- The operation shall return a list of service providers that match the filter.

#### Errors

The operation may return the following error:

##### ERROR: INVALID

Invalid domain value.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

### OPERATION: publishService

#### General

The publishService operation adds new, or updates existing, entries in the list of services held in the directory service.

| Operation Identifier | publishService |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | newProviderDetails : (List<PublishDetails>) |
| OUT | RESPONSE | providerObjectKeys : (List<COM::ObjectKey>) |

#### Structures

- The operation shall take a list of PublishDetails structures.

- For each PublishDetails structure if any of the fields of the domain/session/network fields are either empty or contain the wildcard '*' an INVALID error shall be returned.

- For each contained ProviderDetails structure if the serviceProviderName field is empty or contains the wildcard '*' an INVALID error shall be returned.

- For each contained ProviderCapability structure if the area/service/version fields contains '0' or the supportedCapabilities list is empty or contains '0' then an INVALID error shall be returned.

- For each contained ProviderAddressDetails structure if the supportedLevels list is empty or the priorityLevels field is '0' then an INVALID error shall be returned.

- If an error is being returned then all updates shall be ignored.

- The operation shall create new ServiceProvider COM objects to represent the new service providers.

- The created objects should be stored in the COM archive by the service provider.

- The operation shall return a list of ObjectKeys that represent the ServiceProvider COM objects representing the providers.

- The returned keys may be used by the withdrawService operation to withdraw the providers from the directory service.

#### Errors

The operation may return the following error:

##### ERROR: INVALID

Submitted values are invalid.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

### OPERATION: withdrawService

#### General

The withdrawService operation removes existing entries from the list of services held in the directory service. If no match is found for the withdraw request, then nothing is changed.

| Operation Identifier | withdrawService |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | providerObjectKeys : (List<COM::ObjectKey>) |

#### Structures

- The operation shall take a list of ObjectKeys for the ServiceProvider COM objects to remove from the directory service.

- For each ObjectKey structure if the domain field is empty or contain the wildcard '*' or the supplied instId is '0' an INVALID error shall be returned.

- If the fields do not match an existing ServiceProvider COM object then an UNKNOWN error shall be returned.

- If an error is being returned then all updates shall be ignored.

- Each matched provider shall be removed from the directory service.

- The service provider should remove the matched objects from the COM archive.

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

Provider to withdraw was not found.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: INVALID

Submitted values are invalid.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

## Service: Login

### General

The Login service defines the primary mechanism for the submission of authentication details to a deployment specific security system. It supports operations to allow a user to login, logout, report available roles, and also handover the login to another user.

The service is closely tied to the Access Control aspect of the MAL where the returned authentication identifiers are used in the MAL message header to authenticate and authorise message via Access Control.

The login service supports the concept of roles, where users may log in with a specific role; the meaning of each role is mission-specific, however it is expected that a specific role allocates the user privileges to invoke operations on mission operation services.

The use of login roles is optional but if they are used then the role details are held in the COM archive and the COM archive operations are used to manage the role definitions.

The form in which the password is sent to the Login service provider must be agreed upon beforehand and is dependent on the security system deployed. For example, most security implementations do not recommend the use of plain text passwords but rather some encrypted version of the password. For this reason the contents of the messages sent between the login service consumer and provider during authentication handshaking are implementation-specific.

The authentication and authorisation concept of the MO services is covered in section 3.6 of the Reference Model (R2).

Table 3-3:  Login Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| Common | Login | 3 | 2 | 1 |
| Interaction Pattern | Operation Identifier | Operation Number | Support in Replay | Capability Set |
| REQUEST | login | 1 | No | 1 |
| SUBMIT | logout | 2 | No |  |
| REQUEST | reportRoles | 3 | No | 2 |
| REQUEST | handover | 4 | No | 3 |

### High Level Requirements

- The login service shall provide:

  - the capability for logging in;

  - the capability for logging out;

  - the capability for reporting the list of possible roles for a login profile;

  - the capability to hand over an existing login from one user to another.

### Functional Requirements

### COM usage

- Instances of a user login shall be represented as LoginInstance COM object.

- Instances of a user role shall be represented as LoginRole COM object.

- LoginInstance objects shall be created by the login and handover operations.

- The object instance identifier for a LoginInstance object shall be populated by the provider of the Login service.

- The LoginInstance object shall use the related link to indicate which LoginRole (if any) the login uses.

- The LoginInstance object shall use the source link to indicate which LoginInstance (if any) the login was handed over to.

- If a login has not been handed over to another login then the source link of the LoginInstance object shall be set to NULL.

Table 3-4:  Login Service Object Types

| Object Name | Object Number | Object Body Type | Related points to |
| --- | --- | --- | --- |
| LoginInstance | 1 | Profile | 2 |
| LoginRole | 2 | MAL::Identifier | Not used |

### COM Event Service usage

- When a user logs in a LoginEvent COM event shall be generated.

- When a user logs out a LogoutEvent COM event shall be generated.

- When the handover operation is successful a LogoutEvent COM event shall be generated for the previous login and a LoginEvent COM event shall be generated for the new login.

- The LoginEvent event shall use the related link to indicate which LoginInstance object is being logged in.

- The LogoutEvent event shall use the related link to indicate which LoginInstance object is being logged out.

- The events shall not use the COM object source link and shall set it to NULL.

- The events shall be published using the COM event service.

Table 3-5:  Login Service Events

| Event Name | Object Number | Object Body Type | Related points to | Source points to |
| --- | --- | --- | --- | --- |
| LoginEvent | 3 | Not used | 1 | Not specified |
| LogoutEvent | 4 | Not used | 1 | Not specified |

### COM Object Relationships

The Figure below shows the COM object and event relationships for this service:

Figure 3-2:  Login Service COM object and event relationships

### COM Archive Service usage

- LoginInstance objects should be stored in the COM archive.

- When a login service event is published, the event object should be stored in the COM archive by the publisher.

- LoginRole objects shall be stored in the COM archive.

- The login service shall use the COM archive operations for maintaining the login roles.

### OPERATION: login

#### General

The login operation allows a user to log in to the system. A user can log in more than once by using a different role; however, a specific deployment may place limits on the number of users that may use a specific role, and in that case will fail the login operation.

| Operation Identifier | login |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | userDetails : (Profile) password : (MAL::String) |
| OUT | RESPONSE | authId : (MAL::Blob) objInstId : (MAL::Long) |

#### Structures

- The userDetails field shall contain the details of the new user and role combination.

- If the username field of the supplied Profile structure is either the wildcard '*' or empty an INVALID error shall be returned.

- If the role field of the supplied Profile structure is either the wildcard '*' or empty an INVALID error shall be returned.

- If roles are required by the system and the role field of the supplied Profile structure is NULL then an INVALID error shall be returned.

- The role field of the supplied Profile structure may be NULL if roles are not used by the system.

- An UNKNOWN error shall be returned if the username, password and role combination are not correct for the system i.e. unknown user/role or incorrect password.

- A DUPLICATE error shall be returned if the username and role combination is currently in use.

- A TOO_MANY error shall be returned if the username or role are already used and exceed the permitted maximum usage value (deployment dependent).

- If the login is successful the provider should create a new LoginInstance COM object and store it in the COM archive.

- The related link of the new LoginInstance COM object shall be set to the requested LoginRole COM object.

- The returned authId field shall be used as the authenticationId field in future MAL messages by the consumer MAL for authentication. The token is specific to the user and role in use.

- The returned objInstId field shall contain the LoginInstance COM object instance identifier that was created by the login operation.

#### Errors

The operation may return one of the following errors:

##### ERROR: DUPLICATE

Username/role combination currently in use.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DUPLICATE | Defined in COM | Not Used |

##### ERROR: INVALID

Submitted profile contains invalid values.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

##### ERROR: TOO_MANY

Role concurrent session limit count exceeded.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TOO_MANY | Defined in MAL | Not Used |

##### ERROR: UNKNOWN

Unknown username/role/password combination.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

### OPERATION: logout

#### General

The logout operation allows a user to log out from the system. No information is passed in the message as the MAL authentication Id is enough to identify the login.

| Operation Identifier | logout |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT |  |

#### Structures

- Upon reception of the message the operation shall remove the matched user from the set of logged in users.

- No errors shall be returned by this operation.

#### Errors

The operation does not return any errors.

### OPERATION: reportRoles

#### General

The reportRoles operation returns the list of available roles for a specific user. This operation is expected to be called before a user logs in so that the software can provide a list of possible roles.

| Operation Identifier | reportRoles |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | username : (MAL::Identifier) password : (MAL::String) |
| OUT | RESPONSE | permittedRoles : (List<MAL::Identifier>) |

#### Structures

- The username field shall hold the details of the user.

- If the username field is either the wildcard '*', NULL or empty an INVALID error shall be returned.

- An UNKNOWN error shall be returned if the username and password combination are not correct for the system i.e. unknown user or incorrect password.

- The operation shall return a list of roles that are permitted for the user or NULL if roles are not used by the system.

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

Unknown username/password combination.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: INVALID

Submitted profile contains invalid values.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

### OPERATION: handover

#### General

The handover operation allows an existing login to be transferred to a new user. Two cases are expected here, the first is where the operation is used to change the user's current role, and the second is where an operations context is handed over to another user.

| Operation Identifier | handover |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | newUserDetails : (Profile) newUserPassword : (MAL::String) |
| OUT | RESPONSE | newAuthId : (MAL::Blob) newObjInstId : (MAL::Long) |

#### Structures

- The newUserDetails field shall contain the details of the new user and role combination.

- If the username field of the supplied Profile structure is either NULL, the wildcard '*', or empty an INVALID error shall be returned.

- If the role field of the supplied Profile structure is either the wildcard '*' or empty an INVALID error shall be returned.

- If roles are required by the system and the role field of the supplied Profile structure is NULL then an INVALID error shall be returned.

- The role field of the supplied Profile structure may be NULL if roles are not used by the system.

- An UNKNOWN error shall be returned if the username, password and role combination are not correct for the system i.e. unknown user/role or incorrect password.

- A DUPLICATE error shall be returned if the username and role combination is currently in use.

- A TOO_MANY error shall be returned if the username or role are already used and exceed the permitted maximum usage value (deployment dependent).

- The DUPLICATE and TOO_MANY checks shall take into account the fact that current operator/role combination will be logged out after the handover operation completes.

- If the handover is successful the provider should create a new LoginInstance COM object and store it in the COM archive.

- The related link of the new LoginInstance COM object shall be set to the requested LoginRole COM object.

- The source link of the new LoginInstance COM object shall be set to NULL.

- The provider should update in the COM archive the LoginInstance COM object that represents the previous login by setting its source link to the object instance identifier of the new LoginInstance COM object.

- The returned newAuthId field shall be used as the authenticationId field in future MAL messages by the consumer MAL for authentication. The token is specific to the new user and role in use.

- The returned newObjInstId field shall contain the LoginInstance COM object instance identifier that was created by the operation.

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

Unknown username/role/password combination.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: INVALID

Submitted profile contains invalid values.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

##### ERROR: TOO_MANY

Role concurrent session limit count exceeded.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TOO_MANY | Defined in MAL | Not Used |

##### ERROR: DUPLICATE

Username/role combination currently in use.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DUPLICATE | Defined in COM | Not Used |

## Service: Interact

### General

The interact service allows a consumer to raise interactions that can be completed by another consumer of the interact service in the system. The expected use is for software components of a system to request decision input or extra information from user of the system:

There are four basic types of interaction supported by the service, the first is a simple acknowledge where a user can simply acknowledge the interaction, the second is a confirm where a user can confirm or reject the interaction, the third is a choice selection where the user selects from a supplied set of options, and the final interaction is a request for values where the user supplies a set of data values to the request.

The basic sequence of interaction is below:

The interaction requests can contain a response timeout field that provides the interaction service provider with an upper time in which a response is required, if a response is not received in this time period, then the provider returns a TIMEDOUT error to the consumer that raised the interaction.

An interaction service provider implementation is responsible for determining which users may provide the interaction response and also for managing the situation where several users attempt to provide a response. For each interaction operation only one response will be returned to the consumer that initiated the interaction; it is the responsibility of the interaction service provider to ensure this is the case and also to inform the failed users that their interaction response was not used.

Table 3-6:  Interact Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| Common | Interact | 3 | 3 | 1 |
| Interaction Pattern | Operation Identifier | Operation Number | Support in Replay | Capability Set |
| INVOKE | raiseAcknowledge | 1 | No | 1 |
| SUBMIT | respondAcknowledge | 2 | No |  |
| INVOKE | raiseConfirm | 3 | No | 2 |
| SUBMIT | respondConfirm | 4 | No |  |
| INVOKE | raiseChoice | 5 | No | 3 |
| SUBMIT | respondChoice | 6 | No |  |
| INVOKE | getValues | 7 | No | 4 |
| SUBMIT | respondValues | 8 | No |  |
| REQUEST | listActiveInteractions | 9 | Yes | 5 |
| SUBMIT | cancelInteraction | 10 | No | 6 |

### High Level Requirements

- The interact service shall provide:

  - the capability for requesting an acknowledge interaction;

  - the capability for responding to an acknowledge interaction;

  - the capability for requesting a confirm interaction;

  - the capability for responding to a confirm interaction;

  - the capability for requesting a choice interaction;

  - the capability for responding to a choice interaction;

  - the capability for requesting a get values interaction;

  - the capability for responding to a get values interaction;

  - the capability for listing the currently active interactions;

  - the capability for cancelling an interaction.

- The interact service shall use the event service for notifying consumers of new interactions and also completion of existing interactions.

### COM usage

- Two COM objects shall be used to hold an interaction request details, the first is a InteractRequest COM object and the second a COM object that holds the actual interaction specific details of the interaction.

- The actual interaction request details shall be represented as one of the specific interaction COM objects (InteractAckRequest, InteractConfirmRequest, InteractChoiceRequest, InteractValueRequest).

- The InteractRequest object shall use the source link to indicate which actual interaction request details COM object (InteractAckRequest, InteractConfirmRequest, InteractChoiceRequest, InteractValueRequest) it uses.

- Two COM objects shall be used to hold an interaction response details, the first is a InteractResult COM object and the second a COM object that holds the actual interaction specific response of the interaction.

- The actual interaction response details shall be represented as one of the specific interaction COM objects (InteractTimedoutResult, InteractCancelResult, InteractAckResult, InteractConfirmResult, InteractChoiceResult, InteractValueResult).

- The InteractResult object shall use the related link to indicate which interaction request it is the response to.

- The InteractResult object shall use the source link to indicate which actual interaction response details COM object (InteractTimedoutResult, InteractCancelResult, InteractAckResult, InteractConfirmResult, InteractChoiceResult, InteractValueResult) it uses.

Table 3-7:  Interact Service Object Types

| Object Name | Object Number | Object Body Type | Related points to |
| --- | --- | --- | --- |
| InteractRequest | 1 | No body | Not used |
| InteractResult | 2 | No body | 1 |
| InteractAckRequest | 5 | InteractAcknowledgeDetails | Not used |
| InteractConfirmRequest | 6 | InteractConfirmDetails | Not used |
| InteractChoiceRequest | 7 | InteractChoiceDetails | Not used |
| InteractValueRequest | 8 | InteractValueDetails | Not used |
| InteractTimedoutResult | 9 | No body | Not used |
| InteractCancelResult | 10 | No body | Not used |
| InteractAckResult | 11 | No body | Not used |
| InteractConfirmResult | 12 | InteractConfirmResponse | Not used |
| InteractChoiceResult | 13 | InteractChoiceResponse | Not used |
| InteractValueResult | 14 | InteractValueResponse | Not used |

### COM Event Service usage

- When an interaction is raised it shall cause an InteractRaised COM event to be published using the COM event service.

- The related link of the InteractRaised event shall be the InteractRequest COM object that represents the interaction.

- The source link of the InteractRaised event shall be the COM object that raised the interaction, most likely a LoginInstance COM Object.

- The body of the InteractRaised event shall be the object identifier of the desired destination, either a specific LoginInstance or LoginRole COM object.

- When an interaction is responded to it shall cause an InteractComplete COM event to be published using the COM event service.

- The related link of the InteractComplete object shall be the InteractResult COM object that represents the interaction response.

- The source link of the InteractComplete object shall be the COM object that responded to the interaction, most likely a LoginInstance COM Object.

Table 3-8:  Interact Service Events

| Event Name | Object Number | Object Body Type | Related points to | Source points to |
| --- | --- | --- | --- | --- |
| InteractRaised | 3 | COM::ObjectId | 1 | The source shall link to the COM object that raised the interaction, most likely a LoginInstance COM Object |
| InteractComplete | 4 | Not used | 2 | The source shall link to the COM object that completed the interaction, most likely a LoginInstance COM Object. |

### COM Object Relationships

The Figure below shows the COM object and event relationships for this service:

Figure 3-3:  Interact Service COM object and event relationships

### COM Archive Service usage

- All interact objects should be stored in the COM archive by the provider of the service.

- When an interaction event is published, the event object should be stored in the COM archive by the publisher.

### OPERATION: raiseAcknowledge

#### General

The raiseAcknowledge operation allows a consumer to request an acknowledge from a user/role. The user can only acknowledge the interaction; it cannot be declined (confirm is used in this case). It is expected to be used to allow a user to acknowledge that a specific operation can proceed for example. If no user or role is specified, then the interaction is for any user or role.

The interaction can be responded to via the matching respond operation.

| Operation Identifier | raiseAcknowledge |
| --- | --- |
| Interaction Pattern | INVOKE |
| Pattern Sequence | Message | Body Type |
| IN | INVOKE | interactionDetails : (InteractAcknowledgeDetails) |
| OUT | ACK | objInstId : (MAL::Long) |
| OUT | RESPONSE |  |

#### Structures

- If the destination field of the interactionDetails field is either the wildcard '*' or empty then the operation is for any user and the destinationIsRole field shall be ignored.

- If the destination field of the interactionDetails field is not the wildcard '*' or empty and the destinationIsRole field is set to FALSE, the destination field shall contain a user name.

- If the destination field of the interactionDetails field is not the wildcard '*' or empty and the destinationIsRole field is set to TRUE, the destination field shall contain a role name.

- If an appropriate user or role cannot be identified then an UNKNOWN error shall be returned.

- The operation shall create new InteractRequest and InteractAckRequest COM objects to represent the interaction.

- The created objects should be stored in the COM archive by the service provider.

- An InteractRaised COM event shall be created and distributed by the service provider.

- The acknowledgement objInstId field shall hold the COM object instance identifier of the InteractRequest COM object.

- The returned COM object instance identifier shall be used by the matching respond operation to match this interaction.

- The returned COM object instance identifier may be used by the cancelInteraction operation to cancel this interaction.

- If responseTimeout field of the interactionDetails field contains a non-zero duration and no response has been received in that time then the interaction shall be considered timed out.

- If the interaction has timed out then the provider shall create new InteractResult and InteractTimedoutResult COM objects.

- If the interaction has timed out then the created timed out objects should be stored in the COM archive by the service provider.

- If the interaction has timed out then an InteractComplete COM event shall be created and distributed by the service provider.

- If the interaction has timed out then a TIMEDOUT error shall be returned.

- If this operation is cancelled, then a CANCELLED error shall be returned.

- The response shall be returned when the interaction has been completed.

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

User could not be found to satisfy interaction.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: TIMEDOUT

Interaction timed out.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TIMEDOUT | 70010 | Not Used |

##### ERROR: CANCELLED

Interaction was cancelled.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| CANCELLED | 70011 | Not Used |

### OPERATION: respondAcknowledge

#### General

The respondAcknowledge operation is used to supply a response to an already raised acknowledge interaction.

| Operation Identifier | respondAcknowledge |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | interactionId : (MAL::Long) |

#### Structures

- The interactionId field contains the object instance identifier of the InteractRequest COM object that represents the interaction being acknowledged.

- If the interactionId does not match any existing interaction then an UNKNOWN shall be returned.

- If the authentication identifier of the SUBMIT message does not correspond to the correct user or role for the interaction then an AUTHENTICATION_FAIL error shall be returned.

- If the interactionId matches an InteractRequest but it is not an Acknowledgement interaction then an INVALID error shall be returned.

- If the interactionId matches an InteractRequest but it has already had a response then a DUPLICATE error shall be returned.

- If the interactionId matches an InteractRequest but it has been cancelled with the cancelInteraction operation then a CANCELLED error shall be returned.

- If the interactionId matches an InteractRequest but it has timed out then a TIMEDOUT error shall be returned.

- The operation shall create new InteractResult and InteractAckResult COM objects to represent the interaction response.

- The created objects should be stored in the COM archive by the service provider.

- An InteractComplete COM event shall be created and distributed by the service provider.

- The matching raiseAcknowledge operation shall return the response at this point.

#### Errors

The operation may return one of the following errors:

##### ERROR: AUTHORISATION_FAIL

The respondee is not the correct user or role for the interaction.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| AUTHORISATION_FAIL | Defined in MAL | Not Used |

##### ERROR: UNKNOWN

Requested interaction is not known.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: DUPLICATE

The matched interaction has already had a response.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DUPLICATE | Defined in COM | Not Used |

##### ERROR: INVALID

The matched interaction is not of the correct interaction type.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

##### ERROR: TIMEDOUT

Matched interaction timed out.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TIMEDOUT | 70010 | Not Used |

##### ERROR: CANCELLED

Interaction was cancelled.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| CANCELLED | 70011 | Not Used |

### OPERATION: raiseConfirm

#### General

The raiseConfirm operation allows a consumer to request confirmation from a user/role. The user can confirm or decline the interaction; it is expected to be used to present a user with a 'Yes/No' confirmation choice. If no user or role is specified, then the interaction is for any user or role.

The interaction can be responded to via the matching respond operation.

| Operation Identifier | raiseConfirm |
| --- | --- |
| Interaction Pattern | INVOKE |
| Pattern Sequence | Message | Body Type |
| IN | INVOKE | interactionDetails : (InteractConfirmDetails) |
| OUT | ACK | objInstId : (MAL::Long) |
| OUT | RESPONSE | interactionResponse : (InteractConfirmResponse) |

#### Structures

- If the destination field of the interactionDetails field is either the wildcard '*' or empty then the operation is for any user and the destinationIsRole field shall be ignored.

- If the destination field of the interactionDetails field is not the wildcard '*' or empty and the destinationIsRole field is set to FALSE, the destination field shall contain a user name.

- If the destination field of the interactionDetails field is not the wildcard '*' or empty and the destinationIsRole field is set to TRUE, the destination field shall contain a role name.

- If an appropriate user or role cannot be identified then an UNKNOWN error shall be returned.

- The operation shall create new InteractRequest and InteractConfirmRequest COM objects to represent the interaction.

- The created objects should be stored in the COM archive by the service provider.

- An InteractRaised COM event shall be created and distributed by the service provider.

- The acknowledgement objInstId field shall hold the COM object instance identifier of the InteractRequest COM object.

- The returned COM object instance identifier shall be used by the matching respond operation to match this interaction.

- The returned COM object instance identifier may be used by the cancelInteraction operation to cancel this interaction.

- If responseTimeout field of the interactionDetails field contains a non-zero duration and no response has been received in that time then the interaction shall be considered timed out.

- If the interaction has timed out then the provider shall create new InteractResult and InteractTimedoutResult COM objects.

- If the interaction has timed out then the created timed out objects should be stored in the COM archive by the service provider.

- If the interaction has timed out then an InteractComplete COM event shall be created and distributed by the service provider.

- If the interaction has timed out then a TIMEDOUT error shall be returned.

- If this operation is cancelled, then a CANCELLED error shall be returned.

- The response shall be returned when the interaction has been completed.

#### Errors

The operation may return the following error:

##### ERROR: UNKNOWN

User could not be found to satisfy interaction.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

### OPERATION: respondConfirm

#### General

The respondConfirm operation is used to supply a response to an already raised confirm interaction.

| Operation Identifier | respondConfirm |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | interactionId : (MAL::Long) confirmation : (MAL::Boolean) |

#### Structures

- The interactionId field contains the object instance identifier of the InteractRequest COM object that represents the interaction being confirmed.

- If the interactionId does not match any existing interaction then an UNKNOWN shall be returned.

- If the authentication identifier of the SUBMIT message does not correspond to the correct user or role for the interaction then an AUTHENTICATION_FAIL error shall be returned.

- If the interactionId matches an InteractRequest but it is not a Confirm interaction then an INVALID error shall be returned.

- If the interactionId matches an InteractRequest but it has already had a response then a DUPLICATE error shall be returned.

- If the interactionId matches an InteractRequest but it has been cancelled with the cancelInteraction operation then a CANCELLED error shall be returned.

- If the interactionId matches an InteractRequest but it has timed out then a TIMEDOUT error shall be returned.

- The operation shall create new InteractResult and InteractConfirmResult COM objects to represent the interaction response.

- The created objects should be stored in the COM archive by the service provider.

- An InteractComplete COM event shall be created and distributed by the service provider.

- The matching raiseConfirm operation shall return the response at this point.

#### Errors

The operation may return one of the following errors:

##### ERROR: DUPLICATE

The matched interaction has already had a response.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DUPLICATE | Defined in COM | Not Used |

##### ERROR: UNKNOWN

Requested interaction is not known.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: INVALID

The matched interaction is not of the correct interaction type.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

##### ERROR: AUTHORISATION_FAIL

The respondee is not the correct user or role for the interaction.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| AUTHORISATION_FAIL | Defined in MAL | Not Used |

##### ERROR: TIMEDOUT

Matched interaction timed out.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TIMEDOUT | 70010 | Not Used |

##### ERROR: CANCELLED

Interaction was cancelled.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| CANCELLED | 70011 | Not Used |

### OPERATION: raiseChoice

#### General

The raiseChoice operation allows a consumer to request a user/role provide a choice from a set of predefined values. The user must pick one of the presented list of options; it is expected to be used to allow a user to select an option from the list of possible choices. If no user or role is specified, then the interaction is for any user or role.

The interaction can be responded to via the matching respond operation.

| Operation Identifier | raiseChoice |
| --- | --- |
| Interaction Pattern | INVOKE |
| Pattern Sequence | Message | Body Type |
| IN | INVOKE | interactionDetails : (InteractChoiceDetails) |
| OUT | ACK | objInstId : (MAL::Long) |
| OUT | RESPONSE | interactionResponse : (InteractChoiceResponse) |

#### Structures

- If the destination field of the interactionDetails field is either the wildcard '*' or empty then the operation is for any user and the destinationIsRole field shall be ignored.

- If the destination field of the interactionDetails field is not the wildcard '*' or empty and the destinationIsRole field is set to FALSE, the destination field shall contain a user name.

- If the destination field of the interactionDetails field is not the wildcard '*' or empty and the destinationIsRole field is set to TRUE, the destination field shall contain a role name.

- If an appropriate user or role cannot be identified then an UNKNOWN error shall be returned.

- The operation shall create new InteractRequest and InteractChoiceRequest COM objects to represent the interaction.

- The created objects should be stored in the COM archive by the service provider.

- An InteractRaised COM event shall be created and distributed by the service provider.

- The acknowledgement objInstId field shall hold the COM object instance identifier of the InteractRequest COM object.

- The returned COM object instance identifier shall be used by the matching respond operation to match this interaction.

- The returned COM object instance identifier may be used by the cancelInteraction operation to cancel this interaction.

- If responseTimeout field of the interactionDetails field contains a non-zero duration and no response has been received in that time then the interaction shall be considered timed out.

- If the interaction has timed out then the provider shall create new InteractResult and InteractTimedoutResult COM objects.

- If the interaction has timed out then the created timed out objects should be stored in the COM archive by the service provider.

- If the interaction has timed out then an InteractComplete COM event shall be created and distributed by the service provider.

- If the interaction has timed out then a TIMEDOUT error shall be returned.

- If this operation is cancelled, then a CANCELLED error shall be returned.

- The response shall be returned when the interaction has been completed.

#### Errors

The operation may return the following error:

##### ERROR: UNKNOWN

User could not be found to satisfy interaction.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

### OPERATION: respondChoice

#### General

The respondChoice operation is used to supply a response to an already raised choice interaction.

| Operation Identifier | respondChoice |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | interactionId : (MAL::Long) choiceIndex : (MAL::UInteger) |

#### Structures

- The interactionId field contains the object instance identifier of the InteractRequest COM object that represents the interaction being responded to.

- If the interactionId does not match any existing interaction then an UNKNOWN shall be returned.

- If the authentication identifier of the SUBMIT message does not correspond to the correct user or role for the interaction then an AUTHENTICATION_FAIL error shall be returned.

- If the interactionId matches an InteractRequest but it is not a Choice interaction then an INVALID error shall be returned.

- If the interactionId matches an InteractRequest but it has already had a response then a DUPLICATE error shall be returned.

- If the interactionId matches an InteractRequest but it has been cancelled with the cancelInteraction operation then a CANCELLED error shall be returned.

- If the interactionId matches an InteractRequest but it has timed out then a TIMEDOUT error shall be returned.

- The operation shall create new InteractResult and InteractChoiceResult COM objects to represent the interaction response.

- The created objects should be stored in the COM archive by the service provider.

- An InteractComplete COM event shall be created and distributed by the service provider.

- The matching raiseChoice operation shall return the response at this point.

#### Errors

The operation may return one of the following errors:

##### ERROR: AUTHORISATION_FAIL

The respondee is not the correct user or role for the interaction.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| AUTHORISATION_FAIL | Defined in MAL | Not Used |

##### ERROR: INVALID

The matched interaction is not of the correct interaction type.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

##### ERROR: UNKNOWN

Requested interaction is not known.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: DUPLICATE

The matched interaction has already had a response.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DUPLICATE | Defined in COM | Not Used |

##### ERROR: TIMEDOUT

Matched interaction timed out.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TIMEDOUT | 70010 | Not Used |

##### ERROR: CANCELLED

Interaction was cancelled.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| CANCELLED | 70011 | Not Used |

### OPERATION: getValues

#### General

The getValues operation allows a consumer to request a set of new values from a user/role. The user must supply the set of values; it is expected to be used to allow a user to provide input values for an operation. If no user or role is specified, then the interaction is for any user or role.

The interaction can be responded to via the matching respond operation.

| Operation Identifier | getValues |
| --- | --- |
| Interaction Pattern | INVOKE |
| Pattern Sequence | Message | Body Type |
| IN | INVOKE | interactionDetails : (InteractValueDetails) |
| OUT | ACK | objInstId : (MAL::Long) |
| OUT | RESPONSE | interactionResponse : (InteractValueResponse) |

#### Structures

- If the destination field of the interactionDetails field is either the wildcard '*' or empty then the operation is for any user and the destinationIsRole field shall be ignored.

- If the destination field of the interactionDetails field is not the wildcard '*' or empty and the destinationIsRole field is set to FALSE, the destination field shall contain a user name.

- If the destination field of the interactionDetails field is not the wildcard '*' or empty and the destinationIsRole field is set to TRUE, the destination field shall contain a role name.

- If an appropriate user or role cannot be identified then an UNKNOWN error shall be returned.

- For each entry in the defaultValues list field of the interactionDetails field, if the name field is either NULL or an empty string then an INVALID error shall be returned.

- For each entry in the defaultValues list, the value field must be provided, even if it is empty (not NULL), so that the software used to request the value from an operator can determine the type of value required (Integer, Boolean, etc.).

- For each entry in the defaultValues list, if the value field contains NULL then an INVALID error shall be returned as the receiving software will not be able to determine the desired value type.

- The operation shall create new InteractRequest and InteractValueRequest COM objects to represent the interaction.

- The created objects should be stored in the COM archive by the service provider.

- An InteractRaised COM event shall be created and distributed by the service provider.

- The acknowledgement objInstId field shall hold the COM object instance identifier of the InteractRequest COM object.

- The returned COM object instance identifier shall be used by the matching respond operation to match this interaction.

- The returned COM object instance identifier may be used by the cancelInteraction operation to cancel this interaction.

- If responseTimeout field of the interactionDetails field contains a non-zero duration and no response has been received in that time then the interaction shall be considered timed out.

- If the interaction has timed out then the provider shall create new InteractResult and InteractTimedoutResult COM objects.

- If the interaction has timed out then the created timed out objects should be stored in the COM archive by the service provider.

- If the interaction has timed out then an InteractComplete COM event shall be created and distributed by the service provider.

- If the interaction has timed out then a TIMEDOUT error shall be returned.

- If this operation is cancelled, then a CANCELLED error shall be returned.

- The response shall be returned when the interaction has been completed.

#### Errors

The operation may return one of the following errors:

##### ERROR: INVALID

Invalid values in the request.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

##### ERROR: UNKNOWN

User could not be found to satisfy interaction.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

### OPERATION: respondValues

#### General

The respondValues operation is used to supply a response to an already raised get values interaction.

| Operation Identifier | respondValues |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | interactionId : (MAL::Long) newValues : (List<MAL::NamedValue>) |

#### Structures

- The interactionId field contains the object instance identifier of the InteractRequest COM object that represents the interaction being responded to.

- If the interactionId does not match any existing interaction then an UNKNOWN shall be returned.

- If the authentication identifier of the SUBMIT message does not correspond to the correct user or role for the interaction then an AUTHENTICATION_FAIL error shall be returned.

- If the interactionId matches an InteractRequest but it is not a getValues interaction then an INVALID error shall be returned.

- If the interactionId matches an InteractRequest but it has already had a response then a DUPLICATE error shall be returned.

- If the interactionId matches an InteractRequest but it has been cancelled with the cancelInteraction operation then a CANCELLED error shall be returned.

- If the interactionId matches an InteractRequest but it has timed out then a TIMEDOUT error shall be returned.

- The operation shall create new InteractResult and InteractValueResult COM objects to represent the interaction response.

- The created objects should be stored in the COM archive by the service provider.

- An InteractComplete COM event shall be created and distributed by the service provider.

- The matching getValues operation shall return the response at this point.

#### Errors

The operation may return one of the following errors:

##### ERROR: INVALID

The matched interaction is not of the correct interaction type.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

##### ERROR: AUTHORISATION_FAIL

The respondee is not the correct user or role for the interaction.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| AUTHORISATION_FAIL | Defined in MAL | Not Used |

##### ERROR: UNKNOWN

Requested interaction is not known.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: DUPLICATE

The matched interaction has already had a response.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DUPLICATE | Defined in COM | Not Used |

##### ERROR: TIMEDOUT

Matched interaction timed out.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TIMEDOUT | 70010 | Not Used |

##### ERROR: CANCELLED

Interaction was cancelled.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| CANCELLED | 70011 | Not Used |

### OPERATION: listActiveInteractions

#### General

The listActiveInteractions operation returns the list of active interactions, i.e. those that have not been either had a responded, cancelled or timed out.

| Operation Identifier | listActiveInteractions |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST |  |
| OUT | RESPONSE | activeInteractionObjInstIds : (List<COM::ObjectDetails>) |

#### Structures

- The operation shall return a list of ObjectDetails.

- Each entry in the returned list represents a single active interaction.

- The related field of the returned ObjectDetails holds the object instance identifier of the InteractRequest COM object that represents the active interaction.

- The source field of the returned ObjectDetails holds the domain and object instance identifier of the interaction specific COM object for the active interaction.

- The COM archive should be used to obtain the interaction specific details.

#### Errors

The operation does not return any errors.

### OPERATION: cancelInteraction

#### General

The cancelInteraction operation allows a consumer of the service to cancel an active interaction.

| Operation Identifier | cancelInteraction |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | interactionId : (MAL::Long) |

#### Structures

- The interactionId field contains the object instance identifier of the InteractRequest COM object that represents the interaction being cancelled.

- If the interactionId does not match any existing interaction then an UNKNOWN shall be returned.

- If the interactionId matches an InteractRequest but it has already had a response then a DUPLICATE error shall be returned.

- If the interactionId matches an InteractRequest but it has been cancelled with the cancelInteraction operation then a CANCELLED error shall be returned.

- If the interactionId matches an InteractRequest but it has timed out then a TIMEDOUT error shall be returned.

- The operation shall create new InteractResult and InteractCancelResult COM objects to represent the interaction response.

- The created objects should be stored in the COM archive by the service provider.

- An InteractComplete COM event shall be created and distributed by the service provider.

- The matching raise operation shall return the CANCELLED error at this point.

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

Requested interaction is not known.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: DUPLICATE

The matched interaction has already had a response.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DUPLICATE | Defined in COM | Not Used |

##### ERROR: TIMEDOUT

Matched interaction timed out.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TIMEDOUT | 70010 | Not Used |

##### ERROR: CANCELLED

Interaction was already cancelled.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| CANCELLED | 70011 | Not Used |

## Service: Replay

### General

The Replay service allows a consumer to create, control and delete replay sessions. The replay session is a read-only duplicate of an existing live or simulation session that allows the consumer to control the current time. As well as specifying the initial replay time, the replay can be controlled in a similar way to a video player (play, pause, fast forward, rewind, single step, jump to specific time etc.).

Access control for a replay session is provided via standard MAL access control. The replay service provider can determine who created a specific replay and can therefore limit further replay operations internally. The specific replay access control policy is a deployment-dependent issue.

It should be noted that the 'Support in Replay' flag is set to 'No' for all replay operations. This is because these operations are used to control a replay session and cannot be issued inside a replay session.

Table 3-9:  Replay Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| Common | Replay | 3 | 4 | 1 |
| Interaction Pattern | Operation Identifier | Operation Number | Support in Replay | Capability Set |
| SUBMIT | pauseReplay | 1 | No | 1 |
| SUBMIT | resumeReplay | 2 | No |  |
| SUBMIT | forwardStep | 3 | No | 2 |
| SUBMIT | backwardStep | 4 | No |  |
| SUBMIT | updateReplay | 5 | No | 3 |
| REQUEST | listActiveReplays | 6 | No | 4 |
| INVOKE | addReplay | 7 | No | 5 |
| SUBMIT | removeReplay | 8 | No |  |

### High Level Requirements

- The replay service shall provide:

  - the capability for pausing a replay session;

  - the capability for resuming playback of a replay session;

  - the capability for single stepping a replay session;

  - the capability for updating the playback rates and current time of a replay session;

  - the capability for listing the active replay details;

  - the capability for creating a new replay session;

  - the capability for deleting an existing replay session.

### Functional Requirements

- Replay sessions shall be based on an existing LIVE or SIMULATION session.

- New replay session shall be created using the addReplay operation.

- The addReplay operation shall take the details of the existing LIVE or SIMULATION session to duplicate and a time to use as the current time for the replay session.

- The rate field of the PlaybackSettings structure shall control the current replay rate for the replay session. For example, setting the rate to 2.5 would play the items at two and a half times the normal rate.

- The interval field of the PlaybackSettings shall control the current replay step interval for the replay session.

- The replay service provider shall publish ReplayStatus events whenever the current time or replay state of the replay session changes.

- When the end of a replay session is reached, either before the first entry for backwards replay and after the last entry for forwards replay, the state of a replay shall be automatically switched to STOPPED.

### COM usage

- Instances of a replay session shall be represented as a Replay COM object.

- The Replay object does not use the related link and it shall be set to NULL.

- The source link of the Replay object should be the object that caused it to be created, most likely a COM OperationActivity object or an operator login in the case of off-line editors being used.

Table 3-10:  Replay Service Object Types

| Object Name | Object Number | Object Body Type | Related points to |
| --- | --- | --- | --- |
| Replay | 1 | ReplayDetails | Not used |

### COM Event Service usage

- When either the replay state or current time of a replay session changes a ReplayStatus COM event shall be generated and published.

- The event shall be published using the COM event service.

- The related link of the ReplayStatus event object shall link to the Replay object that represents the replay session.

- The source link of the ReplayStatus event object shall not be used and set to NULL.

Table 3-11:  Replay Service Events

| Event Name | Object Number | Object Body Type | Related points to | Source points to |
| --- | --- | --- | --- | --- |
| ReplayStatus | 2 | ReplayStatusDetails | 1 | Not specified |

### COM Object Relationships

The Figure below shows the COM object and event relationships for this service:

Figure 3-4:  Replay Service COM object and event relationships

### COM Archive Service usage

- Replay objects should be stored in the COM archive.

- When a replay status event is published, the ReplayStatus event object should not be stored in the COM archive by the publisher as these events are very frequent and only show the current status of the replay.

### OPERATION: pauseReplay

#### General

The pauseReplay operation allows a consumer to pause playback of the selected replay session. Effectively this sets the replay session state to STOPPED.

| Operation Identifier | pauseReplay |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | replayObjInstId : (MAL::Long) |

#### Structures

- The replayObjInstId field shall match an existing Replay COM object.

- If no matching Replay COM object can be found then an UNKNOWN error shall be returned.

- If the matched replay session is in the STOPPED state an INVALID error shall be returned.

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

Unknown replay session.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: INVALID

Session was already in the STOPPED state.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

### OPERATION: resumeReplay

#### General

The resumeReplay operation allows a consumer to resume playback of the selected replay session.

| Operation Identifier | resumeReplay |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | replayObjInstId : (MAL::Long) playForwards : (MAL::Boolean) |

#### Structures

- The replayObjInstId field shall match an existing Replay COM object.

- If no matching Replay COM object can be found then an UNKNOWN error shall be returned.

- If the matched replay session is not in the STOPPED state an INVALID error shall be returned.

- If the playForwards field it set to TRUE then resume playback in the forwards direction otherwise play backwards at the current rate.

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

Unknown replay session.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: INVALID

Session was not in the STOPPED state.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

### OPERATION: forwardStep

#### General

The forwardStep operation allows the service consumer to instruct the replay to advance from its current position to the time of either the next item or by the current step interval. The provider re-publishes the stored items to observing service consumers in accordance with their registered interests.

| Operation Identifier | forwardStep |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | replayObjInstId : (MAL::Long) byItem : (MAL::Boolean) |

#### Structures

- The replayObjInstId field shall match an existing Replay COM object.

- If no matching Replay COM object can be found then an UNKNOWN error shall be returned.

- If the matched replay session is not in the STOPPED state an INVALID error shall be returned.

- The supplied Boolean byItem field shall indicate whether to step to the next item (value True) or by the current step interval (value False).

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

Unknown replay session.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: INVALID

Session was not in the STOPPED state.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

### OPERATION: backwardStep

#### General

The backwardStep operation allows the service consumer to instruct the replay to step backwards from its current position to the time of either the previous item or by the current step interval. The provider re-publishes the stored items to observing service consumers in accordance with their registered interests.

| Operation Identifier | backwardStep |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | replayObjInstId : (MAL::Long) byItem : (MAL::Boolean) |

#### Structures

- The replayObjInstId field shall match an existing Replay COM object.

- If no matching Replay COM object can be found then an UNKNOWN error shall be returned.

- If the matched replay session is not in the STOPPED state an INVALID error shall be returned.

- The supplied Boolean byItem field shall indicate whether to step to the previous item (value True) or by the current step interval (value False).

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

Unknown replay session.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: INVALID

Session was not in the STOPPED state.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

### OPERATION: updateReplay

#### General

The updateReplay operation allows a consumer to modify the playback settings of an existing replay.

The operation cannot be used to change the name of an existing replay, removal of the existing replay and adding a new replay must be used in this case.

The updated replay details should be stored in the COM archive by the service provider.

| Operation Identifier | updateReplay |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | replayObjInstId : (MAL::Long) newPlaybackDetails : (PlaybackSettings) newCurrentTime : (MAL::Time) |

#### Structures

- The replayObjInstId field shall contain the object instance identifier of the Replay object to be updated.

- The supplied object instance identifier shall match an existing Replay COM object, an UNKNOWN error shall be raised if this is not the case.

- If an error is raised then the replay shall not be updated as a result of this operation call.

- The newPlaybackDetails field shall contain the replacement PlaybackSettings.

- The newCurrentTime field shall contain the new current time for the replay session.

- The newCurrentTime field may be NULL in which case the current time of the replay shall not be modified.

- The existing PlaybackSettings of the matched Replay COM object shall be replaced by the supplied values.

- The matched replay shall continue its replay based on the new playback settings.

- The updated replay details should be stored in the COM archive by the service provider.

- If the current time or the replay state of the matched replay is modified by this operation call then a new ReplayStatus event shall be published.

#### Errors

The operation may return the following error:

##### ERROR: UNKNOWN

Unknown replay session.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

### OPERATION: listActiveReplays

#### General

The listActiveReplays operation allows a consumer to request the object instance identifiers and playback details of the active replay sessions.

| Operation Identifier | listActiveReplays |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST |  |
| OUT | RESPONSE | replaySummary : (List<ReplaySummary>) |

#### Structures

The response shall contain a list of ReplaySummary structures that detail the active replay sessions.

#### Errors

The operation does not return any errors.

### OPERATION: addReplay

#### General

The addReplay operation allows a consumer to create a new replay session.

The new Replay COM object is expected to be stored in the COM archive by the provider of the replay service.

| Operation Identifier | addReplay |
| --- | --- |
| Interaction Pattern | INVOKE |
| Pattern Sequence | Message | Body Type |
| IN | INVOKE | replayDetails : (ReplayDetails) initialTime : (MAL::Time) returnProviderSummary : (MAL::Boolean) |
| OUT | ACK |  |
| OUT | RESPONSE | replayObjInstId : (MAL::Long) serviceDetails : (List<ProviderSummary>) |

#### Structures

- The replayDetails field shall hold the ReplayDetails of the new replay session to be added.

- The sessionName field of the supplied ReplayDetails structure must not be the wildcard '*', 'LIVE', or empty (an INVALID error shall be returned in this case).

- The supplied sessionName must be unique among all Replay objects for the provider otherwise a DUPLICATE error shall be raised.

- Replay sessions shall be based on an existing LIVE or SIMULATION session.

- If the sourceSessionType field is set to REPLAY then an INVALID error shall be returned.

- The sourceSessionType and sourceSessionName field shall be used to match an existing LIVE or SIMULATION session.

- If the source session cannot be found then an UNKNOWN error shall be returned.

- If an error is raised then a new replay shall not be added as a result of this operation call.

- The initialTime field shall contain the initial time of the replay session.

- The operation shall return the acknowledgement if the supplied values are valid but before the new replay session has been created.

- The response shall contain the object instance identifier of the new Replay object.

- If the returnProviderSummary field is set to TRUE then the operation shall populate the serviceDetails field with a list of service providers that provide the replay session.

- If the returnProviderSummary field is set to FALSE then the operation shall populate the serviceDetails field with a NULL.

#### Errors

The operation may return one of the following errors:

##### ERROR: INVALID

Supplied replay details are invalid.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

##### ERROR: DUPLICATE

Session name already exists.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DUPLICATE | Defined in COM | Not Used |

##### ERROR: UNKNOWN

Source replay session is unknown.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

### OPERATION: removeReplay

#### General

The removeReplay operation allows a consumer to remove a replay from the set of replays supported by the replay provider.

The operation does not remove the Replay object from the COM archive, merely removes the object from the provider. This permits existing ReplayStatus objects to continue to reference the correct Replay object in the COM archive.

| Operation Identifier | removeReplay |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | replayObjInstId : (MAL::Long) |

#### Structures

- The replayObjInstId field shall hold the object instance identifier of the Replay object to be removed from the provider.

- If a provided Replay object instance identifier does not match an existing replay session then this operation shall fail with an UNKNOWN error.

- Matched Replay objects shall not be removed from the COM archive only the list of active replay sessions in the provider.

- If an error is raised then no replays shall be removed as a result of this operation call.

- If the operation succeeds then the provider shall remove the replay session from the active replays.

#### Errors

The operation may return the following error:

##### ERROR: UNKNOWN

Unknown replay session.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

## Service: Configuration

### General

The Configuration service allows a service consumer to activate pre-defined configurations of a service provider.

The service uses a COM object to represent the different configurations allowed by a service provider; a service consumer selects one configuration to activate using the Configuration service activate operation.

If a file is to be used to represent a configuration then the configuration service defines an existing COM object, ConfigurationFile, to represent that specific configuration.

The contents of a configuration for a service provider is deployment specific however the management of these configurations, and the selection of a configuration for current use, is the purpose of this service.

Implementations of this service may also use bespoke methods for configuration representation (such as hardcoded configuration) which is outside the scope of this specification, however, the status and management of these configurations can still be managed with this service.

Table 3-12:  Configuration Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| Common | Configuration | 3 | 5 | 1 |
| Interaction Pattern | Operation Identifier | Operation Number | Support in Replay | Capability Set |
| INVOKE | activate | 1 | No | 1 |

### High Level Requirements

- The configuration service shall provide:

  - the capability for activating a configuration.

### COM usage

- Two COM objects shall be used to hold the configuration definition details, the first is a ConfigurationDefinition COM object that holds the activation state of the configuration and a second COM object that holds the actual configuration details.

- The ConfigurationDefinition object shall use the source link to indicate which COM object holds the actual configuration information.

- The ConfigurationDefinition object does not use the related link and it shall be set to NULL.

- the body of the ConfigurationDefinition object shall be a Boolean which indicates whether it is active or not.

- The COM object that holds the configuration details may be represented as a file in which case a ConfigurationFile COM object should be used to represent it.

Table 3-13:  Configuration Service Object Types

| Object Name | Object Number | Object Body Type | Related points to |
| --- | --- | --- | --- |
| ConfigurationDefinition | 1 | MAL::Boolean | Not used |
| ConfigurationFile | 3 | MAL::File | Not used |

### COM Event Service usage

- When a configuration is activated the change in active configuration shall be represented as ConfigurationActivation COM events.

- The ConfigurationActivation

- event shall be raised when a configuration is made active.

- The body of the ConfigurationActivation event shall be the object instance identifier of the previously active ConfigurationDefinition object.

- The body of the ConfigurationActivation event shall be NULL if no configuration was previously active.

Table 3-14:  Configuration Service Events

| Event Name | Object Number | Object Body Type | Related points to | Source points to |
| --- | --- | --- | --- | --- |
| ConfigurationActivation | 2 | MAL::Long | 1 | The source of the event is the object that triggered the activation, most likely the activate operation. |

### COM Object Relationships

The Figure below shows the COM object and event relationships for this service:

Figure 3-5:  Configuration Service COM object and event relationships

### COM Archive Service usage

- ConfigurationDefinition objects should be stored in the COM archive.

- The COM objects that hold the actual configuration definition details should be stored in the COM archive.

- When a configuration activation event is published, the ConfigurationActivation event object should be stored in the COM archive.

### OPERATION: activate

#### General

The activate operation instructs a service provider to make a specific configuration active. As it is possible that it may take an indeterminate amount of time to activate a specific configuration the INVOKE pattern is used.

| Operation Identifier | activate |
| --- | --- |
| Interaction Pattern | INVOKE |
| Pattern Sequence | Message | Body Type |
| IN | INVOKE | configObjInstId : (MAL::Long) |
| OUT | ACK |  |
| OUT | RESPONSE |  |

#### Structures

- The operation shall take a COM object instance identifier that identifies the configuration to activate.

- An UNKNOWN error shall be returned if the object instance identifier does not match an existing configuration.

- If the object instance identifier does not reference a valid configuration for the service provider an INVALID error shall be returned.

- The empty acknowledgement shall be returned if a matching configuration exists.

- The configuration shall be made active after the acknowledgement is sent and before the response is sent.

- The INVALID error may be returned as a result of a service specific data check.

- If the operation fails the previous configuration shall remain active.

- A ConfigurationActivation COM Event shall be published if the new configuration has been made active.

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

Requested configuration is unknown.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: INVALID

Requested configuration is invalid.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

# Data types

## Service data types: Directory

### Composite: ProviderDetails

The ProviderDetails structure holds information about a provider of a service and its capabilities. The structure contains a list of ProviderAddressDetails structures; a provider may support more than one transport technology and therefore can be reached using more than one address.

| Name | ProviderDetails |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 1 |
| Field | Type | Nullable | Comment |
| serviceProviderName | MAL::Identifier | No | The provider-defined name of the service; allows multiple service providers of the same service type to coexist in the directory service. This value is the unique service provider name. |
| serviceCapabilities | List<ProviderCapability> | No | The service capabilities supported by this service provider |
| providerAddresses | List<ProviderAddressDetails> | No | List of address for this service provider |

### Composite: ProviderCapability

The ProviderCapability structure holds information about a service and the capabilities offered by a provider.

| Name | ProviderCapability |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 2 |
| Field | Type | Nullable | Comment |
| area | MAL::UShort | No | The area of this service taken from the numeric Area identifier of the service specification. |
| service | MAL::UShort | No | The service taken from the numeric Service identifier of the service specification. |
| version | MAL::UOctet | No | The version of this service taken from the Area Version of the area specification. |
| supportedCapabilities | List<MAL::UShort> | No | The set of capabilities set numbers that this service provider supports. |
| serviceProperties | List<MAL::NamedValue> | No | Allows the passing of deployment specific service properties. |

### Composite: ProviderAddressDetails

The ProviderAddressDetails structure holds all information required by the Directory service about a providers URI and attributes relating to QoS.

| Name | ProviderAddressDetails |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 3 |
| Field | Type | Nullable | Comment |
| supportedLevels | List<MAL::QoSLevel> | No | The set of possible QoS levels this service can provide. |
| QoSproperties | List<MAL::NamedValue> | No | Any QoS properties relevant to this address URIs and the specified transport. |
| priorityLevels | MAL::UInteger | No | Number of QoS priority levels that this provider supports. |
| serviceURI | MAL::URI | Yes | The Service URI that identifies the physical location of this service. NULL if represents a shared data provider (Broker). |
| dataURI | MAL::URI | Yes | The data URI that identifies the physical location of the publish and subscribe interface. NULL if service does not use publish and subscribe operations or if a shared data provider is to be used. |
| dataProviderObjInstId | MAL::Long | Yes | The object instance identifier of a ServiceProvider COM object that is the shared broker used by this provider. |

### Composite: ProviderSummary

The ProviderSummary structure holds information about a provider of a service and its capabilities.

| Name | ProviderSummary |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 4 |
| Field | Type | Nullable | Comment |
| providerKey | COM::ObjectKey | No | The COM object key of this service provider |
| providerDetails | ProviderDetails | No | The service capabilities supported by this provider |

### Composite: PublishDetails

The PublishDetails structure holds all the required information to publish new service provider details.

| Name | PublishDetails |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 5 |
| Field | Type | Nullable | Comment |
| domain | List<MAL::Identifier> | No | The domain of the provider. |
| sessionType | MAL::SessionType | No | The type of session of the provider. |
| sourceSessionName | MAL::Identifier | Yes | If this is part of a replay session, this field holds the session name of the source session. NULL otherwise |
| network | MAL::Identifier | No | The network of the provider. |
| providerDetails | List<ProviderDetails> | No | The new service provider details. |

### Composite: ServiceFilter

The ServiceFilter structure holds all information required by the Directory service for service lookup operation. The field filters are AND'd together.

| Name | ServiceFilter |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 6 |
| Field | Type | Nullable | Comment |
| domain | List<MAL::Identifier> | No | The domain to query. Can be the wildcard value of '*' in which case matches all values. |
| network | MAL::Identifier | No | The network to match. Can be the wildcard value of '*' in which case matches all values. |
| sessionType | MAL::SessionType | Yes | The session type to match. Can be NULL in which case matches all values. |
| sessionName | MAL::Identifier | No | The session name to match. Can be the wildcard value of '*' in which case matches all values. |
| area | MAL::UShort | No | The area of this service taken from the Area Identifier of the service specification. Can be '0' which matches all values. |
| service | MAL::UShort | No | The service taken from the Service Identifier of the service specification. Can be '0' which matches all values. |
| version | MAL::UOctet | No | The version of this service taken from the Area Version of the service specification. Can be '0' which matches all values. |
| requiredCapabilities | List<MAL::UInteger> | No | List of required capabilities. If zero length list then matches any. |
| serviceProviderName | MAL::Identifier | No | The required service provider. Can be the wildcard value of '*' in which case matches all values. |

## Service data types: Login

### Composite: Profile

The Profile structure contains details of the user who is logging on to take a specified role.

| Name | Profile |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 1 |
| Field | Type | Nullable | Comment |
| username | MAL::Identifier | No | The name of the user. |
| role | MAL::Identifier | Yes | The optional role of the user. |

## Service data types: Interact

### Composite: InteractDetailsBase

The base Interact service request structure. Holds fields common to all Interact service requests.

| Name | InteractDetailsBase |
| --- | --- |
| Extends | Composite |
| Abstract |
| Field | Type | Nullable | Comment |
| destination | MAL::Identifier | No | Name of user or role to interact with, set to a wildcard or empty if for anyone. |
| destinationIsRole | MAL::Boolean | No | True if destination is a role name, value ignored if no destination supplied. |
| responseTimeout | MAL::Duration | No | Duration in which response must be received. '0' if no timeout required. |
| displayMessage | MAL::String | No | Message to present to user. |

### Composite: InteractAcknowledgeDetails

The InteractAcknowledgeDetails structure holds the fields required for an interaction acknowledgement.

| Name | InteractAcknowledgeDetails |
| --- | --- |
| Extends | InteractDetailsBase |
| Short Form Part | 1 |

### Composite: InteractConfirmDetails

The InteractConfirmDetails structure holds the fields required for an interaction confirmation.

| Name | InteractConfirmDetails |
| --- | --- |
| Extends | InteractDetailsBase |
| Short Form Part | 2 |

### Composite: InteractChoiceDetails

The InteractChoiceDetails structure holds the fields required for an interaction choice query.

| Name | InteractChoiceDetails |
| --- | --- |
| Extends | InteractDetailsBase |
| Short Form Part | 3 |
| Field | Type | Nullable | Comment |
| allowedChoices | List<MAL::String> | No | Set of choices for operator to select from. |

### Composite: InteractValueDetails

The InteractValueDetails structure holds the fields required for an interaction value query.

| Name | InteractValueDetails |
| --- | --- |
| Extends | InteractDetailsBase |
| Short Form Part | 4 |
| Field | Type | Nullable | Comment |
| defaultValues | List<MAL::NamedValue> | No | Default values to provide to operator. Both parts of the Element pairs structure must be populated as it provides the value type required. The first part of the pair shall always be a String that contains the name of the value required. |

### Composite: InteractConfirmResponse

The InteractConfirmResponse structure represents a response to an interaction confirm query.

| Name | InteractConfirmResponse |
| --- | --- |
| Extends | Composite |
| Short Form Part | 6 |
| Field | Type | Nullable | Comment |
| confirmation | MAL::Boolean | No | Response to interaction. |

### Composite: InteractChoiceResponse

The InteractChoiceResponse structure represents a response to a choice interaction query.

| Name | InteractChoiceResponse |
| --- | --- |
| Extends | Composite |
| Short Form Part | 7 |
| Field | Type | Nullable | Comment |
| choiceIndex | MAL::UInteger | No | Index of chosen value from provided list. |

### Composite: InteractValueResponse

The InteractValueResponse structure represents a response to a value interaction query.

| Name | InteractValueResponse |
| --- | --- |
| Extends | Composite |
| Short Form Part | 8 |
| Field | Type | Nullable | Comment |
| newValues | List<MAL::NamedValue> | No | New values provided by operator. Only changed values from those supplied in the request shall be returned. The type of the value returned must match that of the default value sent in the request. |

## Service data types: Replay

### ENUMERATION: ReplayState

The ReplayState enumeration represents the possible states of a replay.

| Name | ReplayState |
| --- | --- |
| Short Form Part | 4 |
| Enumeration Value | Numerical Value | Comment |
| STOPPED | 1 | Replay is stopped. |
| FORWARDS | 2 | Replay is playing forwards. |
| BACKWARDS | 3 | Replay is playing backwards. |

### Composite: ReplayDetails

The ReplayDetails structure contains the replay details.

| Name | ReplayDetails |
| --- | --- |
| Extends | Composite |
| Short Form Part | 1 |
| Field | Type | Nullable | Comment |
| sessionName | MAL::Identifier | No | The session name for this replay session. |
| sourceSessionType | MAL::SessionType | No | Type of the session used as a source for the replay session (cannot be REPLAY). |
| sourceSessionName | MAL::Identifier | No | Identifier of the session used as a source for the replay session. |
| playbackSettings | PlaybackSettings | No | The playback settings for this replay |

### Composite: PlaybackSettings

The PlaybackSettings structure holds the replay playback settings.

| Name | PlaybackSettings |
| --- | --- |
| Extends | Composite |
| Short Form Part | 2 |
| Field | Type | Nullable | Comment |
| rate | MAL::Float | No | Replay rate for the replay session. |
| interval | MAL::Duration | No | Replay step interval for the replay session. |

### Composite: ReplayStatusDetails

The ReplayStatusDetails holds the current state of a replay.

| Name | ReplayStatusDetails |
| --- | --- |
| Extends | Composite |
| Short Form Part | 3 |
| Field | Type | Nullable | Comment |
| state | ReplayState | No | The current state of the replay session. |
| currentTime | MAL::Time | No | The current time of the replay session. |

### Composite: ReplaySummary

The ReplaySummary structure holds the summary details of a replay session.

| Name | ReplaySummary |
| --- | --- |
| Extends | Composite |
| Short Form Part | 5 |
| Field | Type | Nullable | Comment |
| objInstId | MAL::Long | No | The object instance identifier of the replay. |
| details | ReplayDetails | No | The current replay details and playback settings. |
| currentState | ReplayStatusDetails | No | The current state and time of the replay. |

# Error codes

The following table lists the errors defined in this specification:

Table 5-1:  Common Error Codes

| Error | Error # | Comment |
| --- | --- | --- |
| TIMEDOUT | 70010 | Operation specific |
| CANCELLED | 70011 | Operation specific |

# SERVICE SPECIFICATION XML

The following section defines the service in the XML notation as specified in reference [2].

The use of XML for service specification provides a machine-readable format rather than the text-based document format. The published specifications and XML schemas are held in an online SANA registry, located at:

[SANA Registry location to be supplied]

The normative XML for this specification, validated against the XML schemas, is located:

[SANA Registry location to be supplied]

Protocol IMPLEMENTATION CONFORMANCE Statement Proforma

(Normative)

[The required PICS Proforma annex will be supplied prior to final publication.]

Security, SANA, and Patent Considerations

(Informative)

SECURITY CONSIDERATIONS

The security considerations of this specification are the same as those of reference [2]. Specifically authentication and authorisation of a participating consumer or provider is provided by the MAL access control concept and is covered in sections 3.6, 5.2 and 5.3 of the Reference Model (R[1]).

Security of a communications link is delegated to the transport layer.

SANA CONSIDERATIONS

The recommendations of this document request SANA populate the registry specified in reference [2] with the schema and XML detailed in section 5 of this document.

As stated in reference [2], the registration rule for change to this registry requires an engineering review by a designated expert. The expert shall be assigned by the WG Chair, or in absence, Area Director.

PATENT CONSIDERATIONS

The recommendations of this document have no patent issues.

Definition of Acronyms

(Informative)

API	Application Program Interface

AMS	CCSDS Asynchronous Messaging System

CCS	Central Checkout System

CCSDS	Consultative Committee for Space Data Systems

COM	Common Object Model

MAL	Message Abstract Layer

M&C	Monitor and Control

MCS	Mission Control System

MO	Mission Operations

SDU	Service Data Units

SPP	CCSDS Space Packet Protocol

UML	Unified Modeling Language

XML	eXtensible Markup Language

Informative References

(Informative)

[D1] 	Mission Operations Services Concept. Issue 3. Report Concerning Space Data System Standards (Green Book), CCSDS 520.0-G-3. Washington, D.C.: CCSDS, December 2010.

NOTE	–	Normative references are contained in 1.9.

Informative References

(Informative)

- Mission Operations Services Concept.  Report Concerning Space Data System Standards, CCSDS 520.0-G-3.  Green Book.  Issue 3.  Washington, D.C.: CCSDS, December 2010.

NOTE	–	Normative references are contained in 1.9.