Draft Recommendation for
Space Data System Standards

Mission Operations Common Services

Draft Recommended Standard

CCSDS 522.0-R-2 Draft 5

Red Book

February 2017

AUTHORITY

|  | Issue: | Red Book, Issue 2-Draft 5 |  |
| --- | --- | --- | --- |
|  | Date: | February 2017 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in the Procedures Manual for the Consultative Committee for Space Data Systems, and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This document is published and maintained by:

CCSDS Secretariat

Office of Space Communication (Code M-3)

National Aeronautics and Space Administration

Washington, DC  20546, USA

STATEMENT OF INTENT

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF INTENT:)

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

o	Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

o	Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

o	Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible.  It is the responsibility of each member to determine when such standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in the Procedures Manual for the Consultative Committee for Space Data Systems.  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- British National Space Centre (BNSC)/United Kingdom.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- Deutsches Zentrum für Luft- und Raumfahrt e.V. (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- Centro Tecnico Aeroespacial (CTA)/Brazil.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- MIKOMTEK: CSIR (CSIR)/Republic of South Africa.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Organization (NSPO)/Taiwan.

- Naval Center for Space Technology (NCST)/USA.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard.  Its ‘Red Book’ status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations.  As such, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

# DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS 522.0-R-2 Draft 5 | Mission Operations Common Services, Draft Recommended Standard, Issue 2-Draft 5 | February 2017 | Current draft |

# CONTENTS

Section	Page

1	Introduction	1-1

1.1	General	1-1

1.2	Purpose and Scope	1-1

1.3	Applicability	1-1

1.4	Rationale	1-1

1.5	Document structure	1-2

1.6	Definition of Terms	1-2

1.7	NOMENCLATURE	1-4

1.8	Conventions	1-4

1.9	References	1-5

2	Overview	2-7

2.1	General	2-7

2.2	Directory Service	2-8

2.3	Login Service	2-9

2.4	Configuration Service	2-10

2.5	Types of Configuration	2-10

2.6	COM standardised representation	2-11

2.7	Configuration service use cases	2-11

3	Specification: Common	3-14

3.1	General	3-14

3.2	Service: Directory	3-14

3.3	Service: Login	3-22

3.4	Service: Configuration	3-30

4	Data types	4-44

4.1	Area data types: Common	4-44

4.2	Service data types: Directory	4-44

4.3	Service data types: Login	4-49

4.4	Service data types: Configuration	4-49

5	Error codes	5-51

6	SERVICE SPECIFICATION XML	6-52

ANNEX A Protocol IMPLEMENTATION CONFORMANCE Statement Proforma  (Normative)	A-1

ANNEX B Security, SANA, and Patent Considerations  (Informative)	B-1

ANNEX C Definition of Acronyms  (Informative)	C-1

ANNEX D Informative References  (Informative)	D-1

ANNEX E Informative References  (Informative)	E-2

Figure

2-1	Mission Operations Services Concept Document Set	2-7

2-2	Directory Service Concept	2-8

Table

1-1	Example Operation Template	1-5

2-1	Message Header Fields	2-9

1-1Directory Service Operations	3-14

1-1Directory Service Object Types	3-16

1-1Directory Service COM object relationships	3-17

1-1Login Service Operations	3-22

1-1Login Service Object Types	3-23

1-1Login Service Events	3-24

1-1Login Service COM object and event relationships	3-25

1-1Configuration Service Operations	3-31

1-1Configuration Service Object Types	3-32

1-1Configuration Service Events	3-33

1-1Configuration Service COM object and event relationships	3-34

# Introduction

## General

This Recommended Standard defines the Mission Operations (MO) Common Services in conformance with the service framework specified in reference [B1] of annex B, Mission Operations Services Concept.

The Common Services are a set of services that provide support facilities to the Mission Operation services.

These services are defined in terms of the Common Object Model (COM) R[3] and the Message Abstraction Layer (MAL) R[2].

## Purpose and Scope

This Recommended Standard defines, in an abstract manner, the Common services in terms of:

- the operations necessary to provide the service;

- the parameter data associated with each operation;

- the required behaviour of each operation;

- the use of the model.

It does not specify:

- individual implementations or products;

- the implementation of entities or interfaces within real systems;

- the methods or technologies required for communications.

## Applicability

This specification is applicable to any system component that utilises a common infrastructure for service discovery. Nominally, but not exclusively, this applies to ground control systems to external entities and between external entities.

## Rationale

The primary goal of CCSDS is to increase the level of interoperability among agencies. This Recommended Practice furthers that goal by providing a standard service specification for the discovery of services and also common infrastructure services.

## Document structure

This Recommended Standard is organised as follows:

- section 1 provides purpose and scope, applicability, and rationale of this Recommended Practice and lists the definitions, conventions, and references used throughout the document;

- section 2 presents an overview of the concepts;

- section 3 presents the Common Services specification;

- section 4 is a formal specification of the Common Services data structures;

- section 5 is a formal specification of the Common Services errors;

- section 6 specifies the internet location of the formal service specification eXtensible Markup Language (XML).

## Definition of Terms

software component (component): A software unit supporting the business function. Components offer their function as services, which can either be used internally or which can be made available for use outside the component through provided service interfaces. Components may also depend on services provided by other components through consumed service interfaces.

hardware component: A complex physical entity (such as a spacecraft, a tracking system, or a control system) or an individual physical entity of a system (such as an instrument, a computer, or a piece of communications equipment). A hardware component may be composed from other hardware components. Each hardware component may host one or more software components. Each hardware component has one or more ports where connections to other hardware components are made. Any given port on the hardware component may expose one or more service interfaces.

service: A set of capabilities that a component provides to another component via an interface. A service is defined in terms of the set of operations that can be invoked and performed through the service interface. Service specifications define the capabilities, behaviour, and external interfaces, but do not define the implementation.

service interface: A set of interactions provided by a component for participation with another component for some purpose, along with constraints on how they can occur. A service interface is an external interface of a service where the behaviour of the service provider component is exposed. Each service will have one defined ‘provided service interface’ and may have one or more ‘consumed service interface’ and one ‘management service interface’.

provided service interface: A service interface that exposes the service function contained in a component for use by service consumers. It receives the MAL messages from a consumed service interface and maps them into Application Program Interface (API) calls on the provider component.

consumed service interface: The API presented to the consumer component that maps from the Service operations to one or more Service Data Units (SDUs) contained in MAL messages that are transported to the provided service interface.

management service interface: A service interface that exposes management functions of a service function contained in a component for use by service consumers.

service provider (provider): A component that offers a service to another by means of one of its provided service interfaces.

service consumer (consumer): A component that consumes or uses a service provided by another component. A component may be a provider of some services and a consumer of others.

service data unit, SDU: A unit of data that is sent by a service interface and is transmitted, semantically unchanged, to a peer service interface.

service extension: Addition of capabilities to a base service. A service may extend the capabilities of another service with additional operations. An extended service is indistinguishable from the base service to consumers such that consumers of the base service can also be consumers of the extended service without modification.

service capability set: A grouping of service operations. The specification of services is based on the expectation that different deployments require different levels of complexity and functionality from a service. To this end a given service may be implementable at one of several distinct levels, corresponding to the inclusion of one or more capability sets. The capability sets define a grouping of the service operations that remains sensible and coherent; it also provides a service provider with an ability to communicate to a consumer its capability.

service directory: an entity that provides publish and lookup facilities to service providers and consumers.

NOTE	–	Strictly speaking, a directory is not required if a well-known service is to be used; however, in most circumstances a directory provides required flexibility in the location of services. Service location can be statically configured, dynamically discovered through a service directory, or a combination of the two; this is an implementation choice. The service directory is itself, by definition, a service.

## NOMENCLATURE

### Normative Text

The following conventions apply for the normative specifications in this Recommended Standard:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification;

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

NOTE	–	These conventions do not imply constraints on diction in text that is clearly informative in nature.

### Informative Text

In the normative sections of this document, informative text is set off from the normative specifications either in notes or under one of the following subsection headings:

- Overview;

- Background;

- Rationale;

- Discussion.

## Conventions

### Figures

In figures illustrating this document, Unified Modelling Language (UML) modelling diagrams are used. Reference [2] provides further information regarding diagrams types and their meaning.

### Tables

The table format information presented here is extracted from section 2 of reference [2]. It is repeated here to aid in understanding tables as they are presented in this document. A full description of the table formats presented in this document can be found in section 2 of reference [2] and in section 2 of reference [3].

Each interaction pattern definition contains a table that defines the template for operations that use that pattern.

Table 1-1:  Example Operation Template

| Operation Identifier | <<Operation name>> |
| --- | --- |
| Interaction Pattern | <<Interaction pattern name>> |
| Pattern Sequence | Message | Body Type |
| <<Message direction>> | <<Message name>> | <<Message type>> |
| … | … | … |

The message direction denotes the direction of the message relative to the provider of the pattern and is either IN or OUT. So all messages directed towards the provider are IN messages, and all messages directed away from the provider are OUT messages.

Blue cells (dark grey when printed on a monochrome printer) contain table headings, light grey cells contain fields that are fixed for a pattern, and white cells contain values that must be provided by the operation or structure.

## References

The following documents contain provisions which, through reference in this text, constitute provisions of this Recommended Standard.  At the time of publication, the editions indicated were valid.  All documents are subject to revision, and users of this Recommended Standard are encouraged to investigate the possibility of applying the most recent editions of the documents indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS Recommended Standards.

- Mission Operations Reference Model. Issue 1. Recommendation for Space Data System Practices (Magenta Book), CCSDS 520.1-M-1. Washington, D.C.: CCSDS, July 2010.

- Mission Operations Message Abstraction Layer. Issue 2. Recommendation for Space Data System Standards (Blue Book), CCSDS 521.0-B-2. Washington, D.C.: CCSDS, March 2013.

- Mission Operations Common Object Model. Issue 1. Recommendation for Space Data System Standards (Blue Book), CCSDS 521.1-B-1. Washington, D.C.: CCSDS, February 2014.

- Mission Operations HTTP Transport and XML Encoding. Draft A. Recommendation for Space Data System Standards (White Book), CCSDS 000.0-W-0. Washington, D.C.: CCSDS, August 2016.

NOTE	–	Informative references are listed in ANNEX E.

# Overview

## General

The Common Services provide infrastructure services to support the mission operations services. These Common services cover the following aspect of a system:

- Directory

- Service publish and lookup

- Login

- Operator login

- Configuration

- Service configuration management

The Common services provide functions that exist in the vast majority of systems but have previously been proprietary.

The following diagram presents the set of standards documentation in support of the Mission Operations Services Concept. The Common services belong to the Specifications documentation.

Figure 2-1:  Mission Operations Services Concept Document Set

NOTE	–	References [D1] and [1] contain additional information about the MO Services Concept and the MO Reference Model, respectively.

The MO Common services build upon the layering concept outlined in reference [D1] and are defined in terms of the MO MAL outlined in reference [2], so it is possible to deploy them over any supported protocol and message transport. The Common services are also defined in terms of the COM, as defined in reference [3], and build upon the COM event service and the COM archive.

NOTE	–	The services defined in this specification are not dependent on any of the other services, other than the COM services, and are complete in their own right. An implementation is free to opt out of any service and also any capability set of these services; however, it may not make sense to support certain services without others.

## Directory Service

The directory service provides publish and lookup facilities to service providers and consumers. It allows providers to publish their location in the form of a URI (Universal Resource Indicator) so that consumers can locate it without having to know in advance the location. Strictly speaking a directory is not required if a well-known service is to be used; however, in most circumstances a directory provides required flexibility in the location of services.

Figure 2-2:  Directory Service Concept

A service provider publishes to the directory service the set of services, and the capabilities of those services, that it supports for a specific Domain, Network Zone and Session.

Each entry for a service provider contains the associated service information such as capability sets, the QoS (Quality of Service) levels that it can provide, and the URIs required to locate it. Capability sets provide a quick way for service providers to inform consumers of which optional capabilities of a service they support.

The addressing information associated to a service provider, the QoS and URI aspects, are held as a list which allows a service provider to support more than one type of QoS and message transport technology in parallel.

The service directory does not contain any information about the relationships between services that are physically located in a single provider application, only that a provider supports several services. This is considered outside of the scope of the Directory service.

The Directory service cannot be used by clients to locate the Directory service itself, therefore another means of determining the address of it (usually configuration) is required.

### Service provider properties

Each entry in the Directory service for a particular service contains a list of named properties that can be defined by the implementing service provider for passing of relevant information to a service consumer. This list is open ended in so much that any values can be added, however Table 2-1 lists the standard properties and their meanings:

Table 2-1:  Standard Service Provider Properties

| Property identifier | Permitted values | Default value | Description |
| --- | --- | --- | --- |
| TIMEREF | UTC TAI GPS | UTC | Defines the epoch of the time values obtained from this service provider. It is possible that an implementation specific time reference is used however this is outside the scope of this specification. |

## Login Service

The Login service allows an operator to provide authentication information to the system. It takes the operator’s credentials and uses a deployment-specific mechanism to authenticate the operator; the result of this is used by the MAL during access control.

The Login service and the access control provided by the MAL are fully dependent on a deployment-specific security architecture (for example the authentication protocol Kerberos). Both layers (Common and MAL) provide access to, and use of, this security service. Neither implement this themselves. See reference [1] for more information regarding access control.

## Configuration Service

The configuration service provides the ability to transfer the configuration of a service to and from a service provider. It provides facilities for the management of configurations held by a provider if applicable to that implementation.

Implementations of the configuration service may support bespoke configuration upload mechanisms (such as file upload).  This is supported by the configuration specification where consumers would be notified of a new configuration; however, the details of these upload methods are outside of the scope of the Recommended Standard.

The specific configuration of a service is not covered in this Recommended Standard; however, it is fully expected that services may require some degree of configuration, for example, the list of telemetry parameters.

It should be noted that the configuration service uses the COM Event service to activate and store configurations. Therefore the event system used must be reliable for the configuration service to work.

## Types of Configuration

The configuration service defines three supported types of Configuration:

- Hard-coded configurations

  - These configurations have identification but have no visible definition i.e. their definition is represented by code rather than a configuration file.

  - An example is a camera preset mode.

- Non-COM compliant configurations

  - These configurations do not use the COM object model for holding the configuration information and are therefore service/deployment/implementation specific.

  - An example is a non-MO application configuration file.

- COM compliant configurations

  - These configurations use the COM object model for representing configuration information.

  - An example is the set of available Parameters in a M&C Parameter service provider.

It also defines two levels of Configuration:

- Service Configuration

  - is the configuration of a single service in a provider including all the attribute values of its definition objects.

- Provider Configuration

  - is the set of “Service Configurations” of a single provider, so will include zero to many Service Configurations.

Finally, it defines three supported ways of representing a Configuration:

- No representation (i.e. hard-coded configurations such as camera preset modes)

- Implementation-specific representation

- COM standardised representation (only for COM Compliant configuration type)

For COM compliant configurations the Configuration service objects will only hold references to the actual service specific COM objects. There will be no duplication. So, storing a new configuration (assuming that the service in question has created new objects), would only store in the COM archive links/references to those new objects.

It should be noted that the is no direct relationship between the contents of the Directory service and the Configuration service. For example, there can be a different set of providers in an instance of the Directory service to that managed by an instance of the Configuration service. Basically, the Directory service is used to hold the address and the supported operations of providers whereas the Configuration service is used to hold the configuration of providers, however there is no requirement for these two sets of providers to be the same (although that may make sense in some deployments).

## COM standardised representation

The COM standardised representation defines a simple mapping from the COM Objects used by the configuration service to XML. It uses the standard MO XML mapping defined in R[4].

The use of the standard representation is optional, however by defining and using the standard representation it allows the movement and sharing of service configuration a simple matter of importing the standard XML.

The use of the COM Standardised Representation is only supported by COM based services.

## Configuration service use cases

In the following sections, there are four expected uses of the Configuration service shown. This is not an exhaustive list of possible uses; however, it is the most common expected uses of the configuration service.

### Obtaining A Provider Configuration

- Find Configuration service in Directory service

- Get current configuration of providers from configuration service (with getCurrent)

- The configuration can then be retrieved from the Archive (using the COM Archive operations) or requested as a XML file (with exportXML).

  - Can choose to get it as a large XML file containing references and parameter definition values, small XML file containing just references, or a set of COM object references (in MAL format rather than XML directly) from the COM Archive.

### reconfiguring A service provider

- Find Configuration service in Directory service

- Get list of possible Provider Configurations from Configuration service provider including which one is currently active (list operation or/and getCurrent)

- Select one from list and call activate on Configuration service provider

  - The activate request results in a COM event being published announcing the configuration change request

  - Any affected providers should publish a matching event giving their success or failure result.

### Service start-up in A provider

- Find Configuration service in Directory service running on the same provider

- Get list of possible configurations from Configuration service provider

- Call getCurrent to retrieve the current configuration of the provider according to the Configuration service.

- Activate the “current” configuration

### storing A service Provider Configuration

- Find Configuration service in Directory service

- Call storeCurrent on the Configuration Service provider passing in the provider/service object identifiers i.e. let it know which provider/service we want to persist the configuration of

  - The store request results in a COM event being published announcing the configuration store request

  - Any affected providers should publish a matching event giving their success or failure result of their store attempt.

  - Configuration service provider creates in the COM archive a new set of Configuration Objects that link to the current configuration of the service/provider.

  - The actual ParameterDefinition objects are not duplicated as they are already in the archive. They are just linked to.

  - The new configuration is added to the list of available configurations for that service/provider.

# Specification: Common

## General

This section details the Common Services; the structures used by the services are detailed in section 4. The services and structures are defined in terms of the MO Message Abstraction Layer (MAL) which is defined in reference [2], so it is possible to deploy them over any supported protocol and message transport.

The services defined here are also specified in terms of the COM which is defined in reference [3].

To aid comprehension several tables are included for each service and operation definition. The table formats are the same as those used for the specification of the MO COM Services in reference [3]. The formats are fully described in reference [2] in section 2 and in reference [3] section 2, for COM usage.

All service specifications in this document are part of the Common Area. This has a short form number of '3'.

## Service: Directory

### General

The Directory service allows service providers to publish information about which services they provide and consumers to discover service provider address and capability information.

Service provider information is made available using the Directory service publishService operation and removed using the withdrawService operation.

The lookupService operation provides the ability for consumers to query the directory service based on a filter such as required service capability.

Finally, a provider may supply its set of service specification XML files when publishing its capabilities. This allows consumers that are able to process MO service XML files obtain the files for further processing. It is expected that this would be used to either ensure that no modifications have been made by a provider to a standard service or, in the case of a consumer that is able to dynamically interact with new service specifications, obtain the service specification to allow interaction with that new service.

Table 1-1:  Directory Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| Common | Directory | 3 | 1 | 1 |
| Interaction Pattern | Operation Identifier | Operation Number | Support in Replay | Capability Set |
| REQUEST | lookupProvider | 1 | Yes | 1 |
| REQUEST | publishProvider | 2 | No | 2 |
| SUBMIT | withdrawProvider | 3 | No |  |
| REQUEST | getServiceXML | 4 | No |  |

### High Level Requirements

- The directory service shall provide:

  - the capability for requesting service provider details based on a filter;

  - the capability for publishing new service provider details;

  - the capability for withdrawing service provider details;

  - the capability to request any supplied service XML for a service provider.

### Functional Requirements

- A service provider shall use the publishProvider operation to make available the set of services and the capabilities of those services that it offers.

- The publish operation shall take a list of one or more set of address information sets which defines one way to contact that service provider.

- It shall be possible for a provider to offer multiple service addresses to allows the provider to support multiple message transports and encodings.

- Each service address shall list the supported QoS levels and associated QoS properties available for that connection.

- A service consumer indicates its required QoS level and priority by using these values in the lookupProvider operation.

- For services that have operations based on the publish and subscribe interaction pattern there may be required a separate URI for the broker component. To support this the directory service shall hold two URIs for each service, the URI of the primary interface and also a secondary one which, if present, is used for publish and subscribe-based operations.

- If a broker component is shared between more than one provider, known as a shared broker, the broker shall be published as a directory service entry without a primary interface URI.

- Providers that wish to use the shared broker shall reference it by using its object instance identifier in the 'brokerProviderObjInstId' field in their directory service entry.

### COM usage

- A ServiceProvider object represents a service provider. The COM object body shall hold the service provider name.

- The ServiceProvider COM object related link shall not be used and therefore set to NULL.

- The ServiceProvider COM object source link shall not be used and therefore set to NULL.

- A ProviderCapabilities object represents the supported capabilities of a service provider. The COM object body shall hold the provider details of the service provider.

- The ProviderCapabilities COM object related link shall indicate which ServiceProvider COM object it links to.

- The ProviderCapabilities COM object source link shall not be used and therefore set to NULL.

- ServiceProvider and ProviderCapabilities objects shall be created by the publishService operation.

- The object instance identifier for the ServiceProvider and ProviderCapabilities objects shall be populated by the provider of the directory service.

- For the AddressDetails of a particular ProviderCapabilities object, if the brokerProviderObjInstId field contains a value and the brokerURI field is NULL, then the brokerURI value of the referenced provider shall be used.

Table 1-1:  Directory Service Object Types

| Object Name | Object Number | Object Body Type | Related points to | Source points to |
| --- | --- | --- | --- | --- |
| ServiceProvider | 1 | MAL::Identifier | Set to NULL | Set to NULL |
| ProviderCapabilities | 2 | ProviderDetails | 1 | Set to NULL |

### COM Object Relationships

The Figure below shows the COM object relationships for this service:

Figure 1-1:  Directory Service COM object relationships

### COM Archive Service usage

All directory objects should be stored in the COM archive by the provider of the Directory service.

### OPERATION: lookupProvider

#### General

The lookup operation allows a service consumer to query the directory service to return a list of service providers that match the requested criteria. If no match is found, then an empty list is returned.

| Operation Identifier | lookupProvider |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Signature |
| IN | REQUEST | filter : (ServiceFilter) |
| OUT | RESPONSE | matchingProviders : (List<ProviderSummary>) |

#### Structures

- The filter field shall include the service details of the query.

- If the serviceProviderName field is the wildcard '*' then all service provider names shall be matched.

- If the final identifier of the domain field of the filter is the wildcard '*', then all sub-domains shall be searched for matches.

- If the wildcard is used in any other part of the domain other than the final one then an INVALID error shall be returned.

- If the domain field only contains the wildcard '*' then all domains shall be matched.

- If the network field is the wildcard '*' then all networks shall be matched.

- If the sessionType field is NULL then all session types shall be matched.

- If the sessionName field is the wildcard '*' then all session names shall be matched.

- If the area field is the wildcard '0' then all areas names shall be matched.

- If the service field is the wildcard '0' then all services shall be matched.

- If the version field is the wildcard '0' then all area versions shall be matched.

- If the requiredCapabilities field is an empty list then all service capability sets shall be matched.

- The operation shall return a list of service providers that match the filter.

#### Errors

The operation may return the following error:

##### ERROR: INVALID

Invalid filter value.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

### OPERATION: publishProvider

#### General

The publishProvider operation adds a new or updates an existing entry in the list of service providers held in the directory service.

| Operation Identifier | publishProvider |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Signature |
| IN | REQUEST | newProviderDetails : (PublishDetails) |
| OUT | RESPONSE | providerObjId : (MAL::Long) capabilitiesObjId : (MAL::Long) |

#### Structures

- The newProviderDetails field shall hold the provider details of the service to be added or updated in the directory service.

- If any of the fields of the newProviderDetails domain/sessionType/SessionName/network fields are either empty or contain the wildcard '*' an INVALID error shall be returned.

- If the providerName field of the PublishDetails structure is empty or contains the wildcard '*' an INVALID error shall be returned.

- If the area/service/version fields of the PublishDetails structure contain '0' or the supportedCapabilities list is empty or contains '0' then an INVALID error shall be returned.

- For each contained ProviderAddressDetails structure if the supportedLevels list is empty or the priorityLevels field is '0' then an INVALID error shall be returned.

- If an error is being returned then no changes shall be made.

- If the providerName field of the PublishDetails structure matches an existing ServiceProvider COM object, the operation shall update the existing details of that provider.

- If the providerName field of the PublishDetails structure does not match an existing ServiceProvider COM object, then the operation shall create a new ServiceProvider COM object to represent the new service provider.

- A new ProviderCapabilities COM object shall be created to store the capabilities of the provider.

- The created objects should be stored in the COM archive by the service provider.

- The operation shall return the COM object instance identifiers of the ServiceProvider and ProviderCapabilities COM objects representing the provider.

#### Errors

The operation may return the following error:

##### ERROR: INVALID

Submitted values are invalid.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

### OPERATION: withdrawProvider

#### General

The withdrawProvider operation removes an existing entry from the list of service providers held in the directory service. If no match is found for the withdraw request, then nothing is changed.

| Operation Identifier | withdrawProvider |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Signature |
| IN | SUBMIT | providerObjId : (MAL::Long) |

#### Structures

- The providerObjId field shall hold the object instance identifier for the ServiceProvider COM object to remove from the directory service.

- If the supplied identifier is '0' an INVALID error shall be returned.

- If the supplied identifier does not match an existing ServiceProvider COM object then an UNKNOWN error shall be returned.

- If an error is being returned then no changes shall be made.

- The matched provider shall be removed from the directory service.

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

Provider to withdraw was not found.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: INVALID

Submitted values are invalid.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

### OPERATION: getServiceXML

#### General

The getServiceXML operation returns the list of XML files that were submitted by the service provider by the publishProvider operation.

If no files were supplied then this operation returns an empty list.

| Operation Identifier | getServiceXML |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Signature |
| IN | REQUEST | providerObjId : (MAL::Long) |
| OUT | RESPONSE | xmlFiles : (List<MAL::File>) |

#### Structures

- The providerObjId field shall hold the COM object instance indentifier for the ServiceProvider to obtain the service XML for.

- If the supplied instance identifier is '0' an INVALID error shall be returned.

- If the supplied identifier does not match an existing ServiceProvider COM object then an UNKNOWN error shall be returned.

- The list of XML files supplied during the publishProvider operation for the matched provider shall be returned.

- If no XML files were supplied by the provider then an empty list shall be returned.

#### Errors

The operation may return one of the following errors:

##### ERROR: INVALID

Submitted values are invalid.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

##### ERROR: UNKNOWN

Provider was not found.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

## Service: Login

### General

The Login service defines the primary mechanism for the submission of authentication details to a deployment specific security system. It supports operations to allow a user to login, logout, report available roles, and also handover the login to another user.

The service is closely tied to the Access Control aspect of the MAL where the returned authentication identifiers are used in the MAL message header to authenticate and authorise message via Access Control.

The login service supports the concept of roles, where users may log in with a specific role; the meaning of each role is mission-specific, however it is expected that a specific role allocates the user privileges to invoke operations on mission operation services.

The use of login roles is optional but if they are used then the role details are held in the COM archive and the COM archive operations are used to manage the role definitions. The responsibility for maintenance of the login roles is outside the scope of this specification as it is a deployment issue to define the possible roles and associate users to those roles.

The form in which the password is sent to the Login service provider must be agreed upon beforehand and is dependent on the security system deployed. For example, most security implementations do not recommend the use of plain text passwords but rather some encrypted version of the password. For this reason the contents of the messages sent between the login service consumer and provider during authentication handshaking are implementation-specific.

The authentication and authorisation concept of the MO services is covered in section 3.6 of the Reference Model (R2).

The Reference Model (R2) also provides sequence diagrams for security and login in sections 5.2 and 5.3.

Table 1-1:  Login Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| Common | Login | 3 | 2 | 1 |
| Interaction Pattern | Operation Identifier | Operation Number | Support in Replay | Capability Set |
| REQUEST | login | 1 | No | 1 |
| SUBMIT | logout | 2 | No |  |
| REQUEST | listRoles | 3 | No | 2 |
| REQUEST | handover | 4 | No | 3 |

### High Level Requirements

- The login service shall provide:

  - the capability for logging in;

  - the capability for logging out;

  - the capability for reporting the list of possible roles for a login profile;

  - the capability to hand over an existing login from one user to another.

### COM usage

- Instances of a user login shall be represented as LoginInstance COM object.

- Instances of a user role shall be represented as LoginRole COM object.

- LoginInstance objects shall be created by the login and handover operations.

- The object instance identifier for a LoginInstance object shall be populated by the provider of the Login service.

- The LoginInstance object shall use the related link to indicate which LoginRole (if any) the login uses.

- If a LoginInstance object was created during a login operation then the source link shall be set to NULL.

- If a LoginInstance object was created during a handover operation it shall use the source link to indicate which LoginInstance the login was handed over from.

Table 1-1:  Login Service Object Types

| Object Name | Object Number | Object Body Type | Related points to | Source points to |
| --- | --- | --- | --- | --- |
| LoginRole | 1 | MAL::Identifier | Set to NULL | Set to NULL |
| LoginInstance | 2 | Profile | 1 | 2 |

### COM Event Service usage

- When a user logs in a LoginEvent COM event shall be generated.

- When a user logs out a LogoutEvent COM event shall be generated.

- When the handover operation is successful a LogoutEvent COM event shall be generated for the previous login and a LoginEvent COM event shall be generated for the new login.

- The LoginEvent event shall use the related link to indicate which LoginInstance object is being logged in.

- The LogoutEvent event shall use the related link to indicate which LoginInstance object is being logged out.

- The LoginEvent event shall not use the COM object source link and shall set it to NULL.

- The LogoutEvent event shall use the source link to indicate which LoginEvent event it is logging out.

- The events shall be published using the COM event service.

Table 1-1:  Login Service Events

| Event Name | Object Number | Object Body Type | Related points to | Source points to |
| --- | --- | --- | --- | --- |
| LoginEvent | 3 | No body | 2 | Set to NULL |
| LogoutEvent | 4 | No body | 2 | 3 |

### COM Object Relationships

The Figure below shows the COM object and event relationships for this service:

Figure 1-1:  Login Service COM object and event relationships

### COM Archive Service usage

- LoginInstance objects shall be stored in the COM archive.

- When a login service event is published, the event object shall be stored in the COM archive by the Login service provider.

- LoginRole objects shall be stored in the COM archive.

- The COM archive service shall be used for maintaining the LoginRole objects.

### OPERATION: login

#### General

The login operation allows a user to log in to the system. A user can log in more than once by using a different role; however, a specific deployment may place limits on the number of users that may use a specific role, and in that case will fail the login operation.

| Operation Identifier | login |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Signature |
| IN | REQUEST | userDetails : (Profile) password : (MAL::String) |
| OUT | RESPONSE | authId : (MAL::Blob) objInstId : (MAL::Long) |

#### Structures

- The userDetails field shall contain the details of the new user and role combination.

- If the username field of the supplied Profile structure is either the wildcard '*' or empty an INVALID error shall be returned.

- If roles are required by the system and the role field of the supplied Profile structure is NULL then an INVALID error shall be returned.

- The role field of the supplied Profile structure may be NULL if roles are not used by the system.

- An UNKNOWN error shall be returned if the username, password and role combination are not correct for the system i.e. unknown user/role or incorrect password.

- A DUPLICATE error shall be returned if the username and role combination is currently in use.

- A TOO_MANY error shall be returned if the username or role are already used and exceed the permitted maximum usage value (deployment dependent).

- If the login is successful the provider should create a new LoginInstance COM object and store it in the COM archive.

- The related link of the new LoginInstance COM object shall be set to the requested LoginRole COM object.

- A LoginEvent COM event shall be generated at this point.

- The returned authId field shall be used as the authenticationId field in future MAL messages by the consumer MAL for authentication. The token is specific to the user and role in use.

- The returned objInstId field shall contain the LoginInstance COM object instance identifier that was created by the login operation.

#### Errors

The operation may return one of the following errors:

##### ERROR: DUPLICATE

Username/role combination currently in use.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DUPLICATE | Defined in COM | Not Used |

##### ERROR: INVALID

Submitted profile contains invalid values.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

##### ERROR: TOO_MANY

Role concurrent session limit count exceeded.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TOO_MANY | Defined in MAL | Not Used |

##### ERROR: UNKNOWN

Unknown username/role/password combination.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

### OPERATION: logout

#### General

The logout operation allows a user to log out from the system. No information is passed in the message as the MAL authentication Id is enough to identify the login.

| Operation Identifier | logout |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Signature |
| IN | SUBMIT | Empty |

#### Structures

- Upon reception of the message the operation shall remove the matched user from the set of logged in users in the login service provider.

- A LogoutEvent COM event shall be generated at this point.

- No errors shall be returned by this operation.

#### Errors

The operation does not return any errors.

### OPERATION: listRoles

#### General

The listRoles operation returns the list of available roles for a specific user. This operation is expected to be called before a user logs in so that the software can provide a list of possible roles.

| Operation Identifier | listRoles |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Signature |
| IN | REQUEST | username : (MAL::Identifier) password : (MAL::String) |
| OUT | RESPONSE | permittedRoles : (List<MAL::Long>) |

#### Structures

- The username field shall hold the details of the user.

- If the username field is either the wildcard '*', NULL or empty an INVALID error shall be returned.

- An UNKNOWN error shall be returned if the username and password combination are not correct for the system i.e. unknown user or incorrect password.

- The operation shall return a list of role object instance identifiers that are permitted for the user or NULL if roles are not used by the system.

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

Unknown username/password combination.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: INVALID

Submitted profile contains invalid values.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

### OPERATION: handover

#### General

The handover operation allows an existing login to be transferred to a new user. Two cases are expected here, the first is where the operation is used to change the user's current role, and the second is where an operations context is handed over to another user.

| Operation Identifier | handover |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Signature |
| IN | REQUEST | newUserDetails : (Profile) newUserPassword : (MAL::String) |
| OUT | RESPONSE | newAuthId : (MAL::Blob) newObjInstId : (MAL::Long) |

#### Structures

- The newUserDetails field shall contain the details of the new user and role combination.

- If the username field of the supplied Profile structure is either NULL, the wildcard '*', or empty an INVALID error shall be returned.

- If roles are required by the system and the role field of the supplied Profile structure is NULL then an INVALID error shall be returned.

- The role field of the supplied Profile structure may be NULL if roles are not used by the system.

- An UNKNOWN error shall be returned if the username, password and role combination are not correct for the system i.e. unknown user/role or incorrect password.

- A DUPLICATE error shall be returned if the username and role combination is currently in use.

- A TOO_MANY error shall be returned if the username or role are already used and exceed the permitted maximum usage value (deployment dependent).

- The DUPLICATE and TOO_MANY checks shall take into account the fact that current operator/role combination will be logged out after the handover operation completes.

- If the handover is successful the provider should create a new LoginInstance COM object and store it in the COM archive.

- The related link of the new LoginInstance COM object shall be set to the requested LoginRole COM object.

- The source link of the new LoginInstance COM object shall be set to the LoginInstance COM object that represents the previous login.

- The returned newAuthId field shall be used as the authenticationId field in future MAL messages by the consumer MAL for authentication. The token is specific to the new user and role in use.

- The returned newObjInstId field shall contain the new LoginInstance COM object instance identifier that was created by the operation.

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

Unknown username/role/password combination.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: INVALID

Submitted profile contains invalid values.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

##### ERROR: TOO_MANY

Role concurrent session limit count exceeded.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TOO_MANY | Defined in MAL | Not Used |

##### ERROR: DUPLICATE

Username/role combination currently in use.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DUPLICATE | Defined in COM | Not Used |

## Service: Configuration

### General

The Configuration service allows a service consumer to activate pre-defined configurations of a service provider.

The service uses a COM object to represent the different configurations allowed by a service provider; a service consumer selects one configuration to activate using the Configuration service activate operation.

The contents of a configuration for a service provider is deployment specific however the management of these configurations, and the selection of a configuration for current use, is the purpose of this service.

Implementations of this service may also use bespoke methods for configuration representation (such as hardcoded configuration) which is outside the scope of this specification, however, the status and management of these configurations can still be managed with this service.

Table 1-1:  Configuration Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| Common | Configuration | 3 | 5 | 1 |
| Interaction Pattern | Operation Identifier | Operation Number | Support in Replay | Capability Set |
| SUBMIT | activate | 1 | No | 1 |
| REQUEST | list | 2 | No | 2 |
| REQUEST | getCurrent | 3 | No |  |
| REQUEST | exportXML | 4 | No | 3 |
| SUBMIT | add | 5 | No | 4 |
| SUBMIT | remove | 6 | No |  |
| INVOKE | storeCurrent | 7 | No | 5 |
| REQUEST | importXML | 8 | No | 6 |

### High Level Requirements

- The configuration service shall provide:

  - the capability for activating a configuration;

  - the capability for listing available configurations;

  - the capability to manage the available configurations;

  - the capability to get and store the current configuration;

  - and the capability to import/export configurations from/to XML.

### COM usage

- A ProviderConfiguration COM object represents a single configuration of a service provider, multiple actual service providers may use the same provider configuration. The object body shall hold a name to identify the provider configuration.

- The ProviderConfiguration COM object related link shall link to the ConfigurationObjects COM object that contains the objects that form the provider configuration.

- The ProviderConfiguration COM object source link should be the object that caused it to be created, most likely a COM OperationActivity object or an operator login in the case of off-line editors being used.

- A ServiceConfiguration COM object represents a single configuration of a service in a provider, multiple provider configurations may reference the same service configuration. The object body shall hold the service key that identifies the service it is a configuration of.

- The ServiceConfiguration COM object related link shall link to the ConfigurationObjects COM object that contains the objects that form the service configuration.

- The ServiceConfiguration COM object source link should be the object that caused it to be created, most likely a COM OperationActivity object or an operator login in the case of off-line editors being used.

- A ConfigurationObjects COM object represents a set of links to a set of COM objects that form an actual configuration. The object body shall hold a configuration object details structure that links to the objects that form the configuration.

- The ConfigurationObjects COM object related link shall be set to NULL.

- The ConfigurationObjects COM object source link should be the object that caused it to be created, most likely a COM OperationActivity object or an operator login in the case of off-line editors being used.

- A ConfigurationFile COM object provides a mechanism for holding files that contain non-COM configuration information so that it can still be managed and referenced by the configuration service. The object body shall hold the configuration file.

- The ConfigurationFile COM object related link shall be set to NULL.

- The ConfigurationFile COM object source link should be the object that caused it to be created, most likely a COM OperationActivity object or an operator login in the case of off-line editors being used.

- A ProviderConfigurations COM object represents the use of a provider configuration by a specific service provider. The object body is not used and shall be NULL.

- The ProviderConfigurations COM object related link shall link to the ServiceProvider COM object that represents the service provider in the Directory Service.

- The ProviderConfigurations COM object source link shall link to the ProviderConfiguration COM object in use by the provider.

Table 1-1:  Configuration Service Object Types

| Object Name | Object Number | Object Body Type | Related points to | Source points to |
| --- | --- | --- | --- | --- |
| ServiceConfiguration | 1 | ServiceKey | 4 | The object that caused it to be created, most likely a COM OperationActivity object or an operator login in the case of off-line editors being used. |
| ProviderConfiguration | 2 | MAL::Identifier | 4 | The object that caused it to be created, most likely a COM OperationActivity object or an operator login in the case of off-line editors being used. |
| ConfigurationObjects | 4 | ConfigurationObjectDetails | Set to NULL | The object that caused it to be created, most likely a COM OperationActivity object or an operator login in the case of off-line editors being used. |
| ConfigurationFile | 5 | MAL::File | Set to NULL | The object that caused it to be created, most likely a COM OperationActivity object or an operator login in the case of off-line editors being used. |
| ProviderConfigurations | 6 | No body | Directory::1 | 2 |

### COM Event Service usage

- A ConfigurationSwitch COM event shall represent a request change in active configuration.

- The ConfigurationSwitch COM event body shall hold the configuration to be activated.

- The ConfigurationSwitch COM event related link shall point to the COM ServiceProvider object that is required to attempt the configuration switch.

- The ConfigurationSwitch COM event source link shall indicate the activate COM OperationActivity object that caused it to be created.

- A ConfigurationSwitched COM event shall be raised when a configuration is made active.

- The ConfigurationSwitched COM event body shall hold the result of the activation attempt.

- If the activation was successful then the body of the ConfigurationSwitched event shall be set to TRUE, otherwise FALSE for failure.

- The ConfigurationSwitched COM event related link shall point to the ConfigurationSwitch event that triggered the switch attempt.

- The ConfigurationSwitched COM event source link shall point to the previous active configuration or be NULL if no configuration was previously active.

- A ConfigurationStore COM event shall represent a request to store the current configuration.

- The ConfigurationStore COM event body is not used and shall be NULL.

- The ConfigurationStore COM event related link shall link to the ServiceProvider object that represents the provider that must store its configuration.

- The ConfigurationStore COM event source link shall indicate the storeCurrent COM OperationActivity object that caused it to be created.

- A ConfigurationStored COM event shall be raised when a configuration has been stored.

- The ConfigurationStored COM event body shall hold the Result of the store attempt.

- The ConfigurationStored COM event related link shall point to the ConfigurationStore event that triggered the store attempt.

- The ConfigurationStored COM event source link shall be NULL.

Table 1-1:  Configuration Service Events

| Event Name | Object Number | Object Body Type | Related points to | Source points to |
| --- | --- | --- | --- | --- |
| ConfigurationSwitch | 8 | COM::ObjectId | Directory::1 | The source link of the event is the object that triggered the activation, most likely the activate operation. |
| ConfigurationSwitched | 9 | MAL::Boolean | 8 | The previous active configuration or be NULL if no configuration was previously active. |
| ConfigurationStore | 10 | No body | Directory::1 | The source link of the event is the object that triggered the activation, most likely the storeCurrent operation. |
| ConfigurationStored | 11 | MAL::Boolean | 10 | Set to NULL |

### COM Object Relationships

The Figure below shows the COM object and event relationships for this service:

Figure 1-1:  Configuration Service COM object and event relationships

### COM Archive Service usage

- Configuration definition objects should be stored in the COM archive.

- The COM objects that hold the actual configuration definition details should be stored in the COM archive.

- When a configuration switch or store event is published, the event objects should be stored in the COM archive.

### OPERATION: activate

#### General

The activate operation instructs a service provider to make a specific configuration active.

| Operation Identifier | activate |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Signature |
| IN | SUBMIT | serviceProvider : (COM::ObjectKey) configObjId : (COM::ObjectId) |

#### Structures

- The serviceProvider field shall contain the object instance identifier of the service provider being (re)configured.

- If the service provider is not known an UNKNOWN error shall be returned.

- The configObjId field shall hold the COM object identifier that identifies the configuration to activate.

- The supplied object identifier shall reference either a ProviderConfiguration or ServiceConfiguration object.

- An UNKNOWN error shall be returned if the object instance identifier does not match an existing configuration.

- An INVALID error shall be returned if the object instance identifier is not of either of the supported types.

- If the object instance identifier does not reference a valid configuration for the service provider an INVALID error shall be returned.

- A ConfigurationSwitch COM Event shall be published if no errors are being returned containing the ObjectId of the service or provider configuration to use, i.e. the contents of the configObjId field of this operation.

- The service provider that implements the selected service shall, after the reception of the event, reconfigure itself and publish a ConfigurationSwitchResult COM event.

- If the operation fails the previous configuration shall remain active.

- In the case of a provider configuration, where multiple service configurations are being switched, the provider must switch all configurations successfully or roll back to the previous configuration. No partial reconfiguration is supported.

- If a provider level configuration is successful then the service provider that implements the selected service shall store in the COM archive a new ProviderConfigurations COM object that links its ServiceProvider object to the new activated ProviderConfiguration COM object.

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

Requested configuration is unknown.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: INVALID

Requested configuration is invalid.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

### OPERATION: list

#### General

The list operation returns list of known configurations for a certain configuration type in a specific domain.

| Operation Identifier | list |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Signature |
| IN | REQUEST | type : (ConfigurationType) domain : (List<MAL::Identifier>) service : (ServiceKey) |
| OUT | RESPONSE | objInstIds : (List<COM::ObjectId>) |

#### Structures

- The configurationType argument shall hold the type of configuration to be listed.

- The domain request argument shall contain the domain of the configuration objects to return.

- The domain field supports the wildcard value of '*' only in the last part of the domain, otherwise an INVALID error shall be returned.

- If the request configuration type is SERVICE, then an optional service filter may be supplied in the serviceKey field.

- For other types of configuration the serviceKey field shall be ignored and may be set to NULL in the request.

- The operation shall return the list of matched configuration objects.

- If no configurations matched then an empty list shall be returned.

#### Errors

The operation may return one of the following errors:

##### ERROR: UNKNOWN

Requested object is unknown.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

##### ERROR: INVALID

Requested configuration is not a valid configuration object type.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

### OPERATION: getCurrent

#### General

The getCurrent operation returns the currently selected configuration of a service provider, either of the complete provider or a specific service of that provider.

| Operation Identifier | getCurrent |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Signature |
| IN | REQUEST | serviceProvider : (List<COM::ObjectKey>) serviceKey : (ServiceKey) |
| OUT | RESPONSE | objInstId : (COM::ObjectId) |

#### Structures

- The serviceProvider field shall contain the object instance identifier of the service provider being queried.

- If the service provider is not known an UNKNOWN error shall be returned.

- If the serviceKey field is not NULL, then the operation shall return the configuration of the selected service, as specified in the field.

- For retrieval of the provider level configuration the serviceKey field shall be set to NULL in the request.

- An UNKNOWN error shall be returned if the combination of service provider and service filter fields don't match an existing configuration.

- No wildcards are supported, an INVALID error must be returned in this case.

#### Errors

The operation may return one of the following errors:

##### ERROR: INVALID

Requested configuration is not a valid configuration object type.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

##### ERROR: UNKNOWN

Requested object is unknown.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

### OPERATION: exportXML

#### General

The exportXML operation returns the actual Configuration information in the XML format from the configuration object stored in the Archive.

The returned XML is in the standardised format and one of two levels of detail, compact or complete, can be selected. Compact contains just the COM object instance identifiers with the respective domains and object types whereas complete augments the compact with the additional set of values inside the respective service objects.

| Operation Identifier | exportXML |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Signature |
| IN | REQUEST | confObjId : (COM::ObjectId) getComplete : (MAL::Boolean) |
| OUT | RESPONSE | xmlConfiguration : (MAL::File) |

#### Structures

- The confObjId argument shall contain the COM object instance identifier of the configuration object to return the XML representation of.

- The getComplete Boolean shall be set to True if the returned XML is to be in the complete standardised format, otherwise it will be in the compact standardised format.

- The returned File object shall contain the configuration XML.

- The Configuration object shall not be deleted from the COM Archive.

#### Errors

The operation may return one of the following errors:

##### ERROR: INVALID

Requested configuration is not a valid configuration object type.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

##### ERROR: UNKNOWN

Requested object is unknown.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

### OPERATION: add

#### General

The add operation makes a new Configuration available on the Configuration Service. The Configuration must already exist in the COM archive to be added to the Configuration Service.

| Operation Identifier | add |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Signature |
| IN | SUBMIT | serviceProvider : (COM::ObjectKey) configObjIds : (List<COM::ObjectKey>) |

#### Structures

- The first argument shall contain the object identifier of the service provider which the configurations are being added to.

- The second argument shall contain a list of provider configurations to add to the list of configurations available for the specific service provider.

- If either the service provider or the configuration object are unknown then an UNKNOWN error shall be returned.

#### Errors

The operation may return the following error:

##### ERROR: UNKNOWN

Supplied object is unknown in the COM archive.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

### OPERATION: remove

#### General

The remove operation, removes a provider configuration from the list of configurations available for that provider in the configuration service. The operation does not remove the configuration objects from the COM archive, merely removes the objects from the configuration service provider.

| Operation Identifier | remove |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Signature |
| IN | SUBMIT | serviceProvider : (COM::ObjectKey) configObjIds : (List<COM::ObjectId>) |

#### Structures

- The first argument shall contain the object identifier of the service provider which the configurations are being removed from.

- The second argument shall contain a list of provider configurations to remove from the list of configurations available for the specific service provider.

- If a provided object identifier does not match an existing configuration object then this operation shall fail with an UNKNOWN error.

- If an error is raised then no configurations shall be removed as a result of this operation call.

- Matched configuration objects shall not be removed from the COM archive only the list of configuration objects in the provider.

#### Errors

The operation may return the following error:

##### ERROR: UNKNOWN

- One of the supplied configuration object instance identifiers is unknown.

- A list of the indexes of the error values shall be contained in the extra information field.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

### OPERATION: storeCurrent

#### General

The storeCurrent generates a new Configuration object with the current Configuration of a specific Service or Provider configuration and stores it in the COM archive. Optionally the configuration can be added to the list of available configurations.

| Operation Identifier | storeCurrent |
| --- | --- |
| Interaction Pattern | INVOKE |
| Pattern Sequence | Message | Body Signature |
| IN | INVOKE | serviceProvider : (COM::ObjectKey) autoAdd : (MAL::Boolean) |
| OUT | ACK | Empty |
| OUT | RESPONSE | objInstId : (COM::ObjectId) |

#### Structures

- The serviceProvider field shall contain the object instance identifier of the service provider that must store its current configuration.

- If the service provider is not known an UNKNOWN error shall be returned.

- The operation shall publish a ConfigurationStore event containing the selected configuration to be stored.

- The service provider that implements the selected service shall, after the reception of the event, store the current Configuration in the COM Archive.

- Once the relevant service provider has finished storing its configuration it shall publish a ConfigurationStored event.

- If the autoAdd field is set to TRUE then, once the stored event has been published the configuration service provider shall add the new configuration to the list of available configurations for the selected service provider. In effect call the add operation.

- The response shall contain the object identifier of the new configuration object.

#### Errors

The operation may return the following error:

##### ERROR: INVALID

Not a valid Service or Provider object

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

### OPERATION: importXML

#### General

The importXML generates a new Configuration object from a XML File and stores the Configuration in the COM archive. Afterwards, the configuration can be optionally added to the list of available configurations.

The operation is only for importing XML configurations that use the standardised format defined by the Configuration service.

| Operation Identifier | importXML |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Signature |
| IN | REQUEST | xmlFile : (MAL::File) |
| OUT | RESPONSE | objInstIds : (COM::ObjectId) |

#### Structures

- The newly generated Configuration object should be checked for consistency. An error shall be raised if the configuration is not valid.

- For every object present within the XML file that does not exist in the COM Archive, the Configuration service shall create a new object with the same content and store the object in the COM Archive.

- If the object already exists in the COM Archive, nothing shall be created.

- The newly generated Configuration object shall always reference existing objects in the Archive.

- The return response shall contain the object identifier of the new configuration object.

#### Errors

The operation may return the following error:

##### ERROR: INVALID

The supplied XML was not valid.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | Defined in COM | Not Used |

# Data types

## Area data types: Common

### Composite: ServiceKey

| Name | ServiceKey |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 3 |
| Field | Type | Nullable | Comment |
| area | MAL::UShort | No | The area of this service taken from the numeric Area identifier of the service specification. |
| service | MAL::UShort | No | The service taken from the numeric Service identifier of the service specification. |
| version | MAL::UOctet | No | The version of this service taken from the Area Version of the area specification. |

## Service data types: Directory

### Composite: ProviderDetails

The ProviderDetails structure holds information about a provider of a service and its capabilities. The structure contains a list of AddressDetails structures which should be used when the individual services listed by the provider do not supply address information. A provider may support more than one transport technology and therefore can be reached using more than one address.

| Name | ProviderDetails |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 1 |
| Field | Type | Nullable | Comment |
| serviceCapabilities | List<ServiceCapability> | No | The service capabilities supported by this service provider |
| providerAddresses | List<AddressDetails> | No | List of address for all services of this service provider unless service specific addresses are supplied in the serviceCapabilities field. If all address information is supplied in the serviceCapabilities field this list should be zero length. |

### Composite: ServiceCapability

The ServiceCapability structure holds information about a service and the capabilities offered by a provider.

| Name | ServiceCapability |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 2 |
| Field | Type | Nullable | Comment |
| serviceKey | ServiceKey | No | The area, service, and version fields. |
| supportedCapabilities | List<MAL::UShort> | Yes | The set of capabilities set numbers that this service provider supports. If NULL then all capabilities supported. |
| serviceProperties | List<MAL::NamedValue> | No | Allows the passing of deployment specific service properties. |
| serviceAddresses | List<AddressDetails> | Yes | Optional set of address details for this specific service which shall be used instead of the provider ones when accessing this service. If all address information is supplied in the containing ProviderDetails structure field this list should be replaced with a NULL. |

### Composite: AddressDetails

The AddressDetails structure holds all information required by the Directory service about a service providers URI and attributes relating to QoS.

| Name | AddressDetails |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 4 |
| Field | Type | Nullable | Comment |
| supportedLevels | List<MAL::QoSLevel> | No | The set of possible QoS levels this service can provide. |
| QoSproperties | List<MAL::NamedValue> | No | Any QoS properties relevant to this address URIs and the specified transport. |
| priorityLevels | MAL::UInteger | No | The number of QoS priority levels that this provider supports. |
| serviceURI | MAL::URI | Yes | The Service URI that identifies the physical location of this service. NULL if represents a shared data provider (Broker). |
| brokerURI | MAL::URI | Yes | The broker URI that identifies the physical location of the publish and subscribe interface. NULL if service does not use publish and subscribe operations or if a shared broker is to be used. |
| brokerProviderObjInstId | MAL::Long | Yes | The object instance identifier of a ServiceProvider COM object that is the shared broker used by this provider. |

### Composite: ProviderSummary

The ProviderSummary structure holds information about a provider of a service and its capabilities.

| Name | ProviderSummary |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 5 |
| Field | Type | Nullable | Comment |
| providerKey | COM::ObjectKey | No | The COM object key of this service provider |
| providerName | MAL::Identifier | No | The name of this service provider. |
| providerDetails | ProviderDetails | No | The service capabilities supported by this provider |

### Composite: PublishDetails

The PublishDetails structure holds all the required information to publish new service provider details.

| Name | PublishDetails |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 6 |
| Field | Type | Nullable | Comment |
| providerName | MAL::Identifier | No | The unique service provider name; allows multiple service providers of the same service type to coexist in the directory service. |
| domain | List<MAL::Identifier> | No | The domain of the provider. |
| sessionType | MAL::SessionType | No | The type of session of the provider. |
| sourceSessionName | MAL::Identifier | Yes | If this is part of a replay session, this field holds the session name of the source session. NULL otherwise |
| network | MAL::Identifier | No | The network of the provider. |
| providerDetails | ProviderDetails | No | The new service provider details. |
| serviceXML | List<MAL::File> | Yes | The optional XML files to associate with this provider. |

### Composite: ServiceFilter

The ServiceFilter structure holds all information required by the Directory service for service lookup operation. The field filters are AND'd together.

| Name | ServiceFilter |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 7 |
| Field | Type | Nullable | Comment |
| serviceProviderName | MAL::Identifier | No | The required service provider. Can be the wildcard value of '*' in which case matches all values. |
| domain | List<MAL::Identifier> | No | The domain to query. Can be the wildcard value of '*' in which case matches all values. |
| network | MAL::Identifier | No | The network to match. Can be the wildcard value of '*' in which case matches all values. |
| sessionType | MAL::SessionType | Yes | The session type to match. Can be NULL in which case matches all values. |
| sessionName | MAL::Identifier | No | The session name to match. Can be the wildcard value of '*' in which case matches all values. |
| serviceKey | ServiceKey | No | The service to filter on, values can be '0' which matches all values. |
| requiredCapabilities | List<MAL::UInteger> | No | List of required capabilities. If zero length list then matches any. |

## Service data types: Login

### Composite: Profile

The Profile structure contains details of the user who is logging on to take a specified role.

| Name | Profile |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 1 |
| Field | Type | Nullable | Comment |
| username | MAL::Identifier | No | The name of the user. |
| role | MAL::Long | Yes | The optional object instance identifier of the role required by the user. |

## Service data types: Configuration

### ENUMERATION: ConfigurationType

The configuration type enumeration holds the possible types of a configuration.

| Name | ConfigurationType |
| --- | --- |
| Short Form Part | 4 |
| Enumeration Value | Numerical Value | Comment |
| PROVIDER | 1 | The configuration is a Provider configuration. |
| SERVICE | 2 | The configuration is a Service configuration. |

### Composite: ConfigurationObjectSet

The configuration object set holds a set of object identifiers for a single COM object type in a single domain.

| Name | ConfigurationObjectSet |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 1 |
| Field | Type | Nullable | Comment |
| objType | COM::ObjectType | No | The COM object type of the configuration objects. |
| domain | List<MAL::Identifier> | No | The domain of the configuration objects. |
| objInstIds | List<MAL::Long> | No | The set of COM object identifiers that form this configuration set. |

### Composite: ConfigurationObjectDetails

The configuration object details holds a zero to many ConfigurationObjectSet structures. It allows a configuration to reference COM objects from more than one domain or of more than one COM object type.

| Name | ConfigurationObjectDetails |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 2 |
| Field | Type | Nullable | Comment |
| configObjects | List<ConfigurationObjectSet> | No | The list of configuration objects. |

### Composite: ServiceProviderKey

The ServiceProviderKey structure holds information to uniquely identify a service Provider.

| Name | ServiceProviderKey |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 3 |
| Field | Type | Nullable | Comment |
| serviceKey | ServiceKey | Yes | The area, service, and version fields. If NULL then all the services will be matched. |
| domain | List<MAL::Identifier> | No | The domain of the provider. Only the objects whose domain matches the provided domain will be returned. The domain field supports the wildcard value of '*' only in the last part of the domain. |

# Error codes

No errors are defined in this specification.

# SERVICE SPECIFICATION XML

The following section defines the service in the XML notation as specified in reference [2].

The use of XML for service specification provides a machine-readable format rather than the text-based document format. The published specifications and XML schemas are held in an online SANA registry, located at:

[SANA Registry location to be supplied]

The normative XML for this specification, validated against the XML schemas, is located:

[SANA Registry location to be supplied]

Protocol IMPLEMENTATION CONFORMANCE Statement Proforma

(Normative)

[The required PICS Proforma annex will be supplied prior to final publication.]

Security, SANA, and Patent Considerations

(Informative)

SECURITY CONSIDERATIONS

The security considerations of this specification are the same as those of reference [2]. Specifically authentication and authorisation of a participating consumer or provider is provided by the MAL access control concept and is covered in sections 3.6, 5.2 and 5.3 of the Reference Model (R[1]).

Security of a communications link is delegated to the transport layer.

SANA CONSIDERATIONS

The recommendations of this document request SANA populate the registry specified in reference [2] with the schema and XML detailed in section 5 of this document.

As stated in reference [2], the registration rule for change to this registry requires an engineering review by a designated expert. The expert shall be assigned by the WG Chair, or in absence, Area Director.

PATENT CONSIDERATIONS

The recommendations of this document have no patent issues.

Definition of Acronyms

(Informative)

API	Application Program Interface

AMS	CCSDS Asynchronous Messaging System

CCS	Central Checkout System

CCSDS	Consultative Committee for Space Data Systems

COM	Common Object Model

MAL	Message Abstract Layer

M&C	Monitor and Control

MCS	Mission Control System

MO	Mission Operations

SDU	Service Data Units

SPP	CCSDS Space Packet Protocol

UML	Unified Modeling Language

XML	eXtensible Markup Language

Informative References

(Informative)

[D1] 	Mission Operations Services Concept. Issue 3. Report Concerning Space Data System Standards (Green Book), CCSDS 520.0-G-3. Washington, D.C.: CCSDS, December 2010.

NOTE	–	Normative references are contained in 1.9.