Draft Recommendation for
Space Data System Standards

Mission Operations Message Abstraction Layer—Space Packet Binding

Draft Recommended Standard

CCSDS 524.1-R-0

Red Book

November 2012

AUTHORITY

|  | Issue: | Red Book, Issue 0 |  |
| --- | --- | --- | --- |
|  | Date: | November 2012 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-3), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This document is published and maintained by:

CCSDS Secretariat

Space Communications and Navigation Office, 7L70

Space Operations Mission Directorate

NASA Headquarters

Washington, DC 20546-0001, USA

FOREWORD

The intended use for this document is to allow the implementation of a protocol layer that binds the Mission Operations (MO) service framework to the Space Packet Protocol. This document assumes that the reader is familiar with the MO concepts, especially the Message Abstraction Layer (MAL).

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur. This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in the Procedures Manual for the Consultative Committee for Space Data Systems. Current versions of CCSDS documents are maintained at the CCSDS Web site:

http: //www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt e.V. (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- CSIR Satellite Applications Centre (CSIR)/Republic of South Africa.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard.  Its ‘Red Book’ status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations.  As such, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

Recipients of this draft are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

# DOCUMENT CONTROL

| Document | Title and Issue | Date | Status |
| --- | --- | --- | --- |
| CCSDS 524.1-R-0 | Mission Operations Message Abstraction Layer—Space Packet Binding, Draft Recommended Standard, Issue 0 | November 2012 | Current draft |

# CONTENTS

Section	Page

1	Introduction	1-1

1.1	PURPOSE	1-1

1.2	SCOPE	1-1

1.3	APPLICABILITY	1-1

1.4	RATIONALE	1-1

1.5	Document structure	1-1

1.6	Definitions	1-2

1.7	NOMENCLATURE	1-3

1.8	Bit Numbering Convention	1-4

1.9	references	1-4

2	Overview	2-1

2.1	General	2-1

2.2	MO Service Framework above Space Packet Protocol	2-2

3	Protocol Layer	3-1

3.1	Overview	3-1

3.2	URI Format	3-2

3.3	QoS Properties	3-3

3.4	SupportedQoS Request	3-5

3.5	SupportedIP Request	3-5

3.6	Transmit Request	3-5

3.7	TransmitMultiple Request	3-6

3.8	Receive indication	3-6

3.9	ReceiveMultiple indication	3-7

4	Protocol Data Unit	4-1

4.1	Overview	4-1

4.2	Primary Header	4-1

4.3	Secondary Header	4-3

4.4	User Data Field	4-8

4.5	Encoding Patterns	4-12

ANNEX A Protocol Implementation Conformance Statement Proforma  (Normative)	A-1

ANNEX B Encoding Format of Parameter Types  (Normative)	B-1

ANNEX C SECURITY, SANA, AND PATENT CONSIDERATIONS  (Informative)	C-1

ANNEX D acronyms  (informative)	D-1

ANNEX E informative References  (Informative)	E-1

# CONTENTS (continued)

Figure	Page

1-1	Bit Numbering Convention	1-4

1-2	Octet Convention	1-4

2-1	Mission Operations Services Concept Document Set	2-1

2-2	Overview of the MO Service Framework	2-3

2-3	MO Service Framework above Space Packet Protocol	2-4

Table

3-1	MAL Transport Interface Primitives	3-1

3-2	Packet Interface Primitives	3-2

3-1	QoS Properties	3-3

4-1	Space Packet Type	4-2

4-2	Secondary Header Format	4-4

4-4	Telecommand SDU Types	4-6

4-5	Telemetry SDU Types	4-6

4-3	User Data Field Format	4-9

4-4	QoS Enumerated Value	4-10

4-4	Session Enumerated Value	4-10

B-1	Variable Signed Integer Bit Shifting	B-9

7-3	MAL Space Packet Binding Version Number initial values	C-3

7-3	MAL Binding URI Scheme Name initial values	C-3

# Introduction

## PURPOSE

This Recommended Standard defines a protocol that maps the Mission Operations (MO) Message Abstraction Layer (MAL) specified in reference [2] to the Space Packet Protocol specified in reference [1].

## SCOPE

The scope of this Recommended Standard is the specification of a MAL Transport Layer in terms of:

- the interface required by the MAL layer;

- the interface provided by the Space Packet Protocol layer;

- the Protocol Data Unit (PDU) that results from the mapping of the MAL message model to the Space Packet Protocol.

This Recommended Standard does not specify:

- individual implementations or products;

- the implementation of entities or interfaces within real systems.

The MAL space packet binding is intended to provide full interoperability of implemented services defined in terms of MAL.

## APPLICABILITY

This Recommended Standard specifies a protocol that enables different implementations of the MO service framework to interoperate through the Space Packet Protocol.

## RATIONALE

The goal of this Recommended Standard is to specify how to translate the MAL message model in an unambiguous way into a specific protocol tied to a specific PDU above the Space Packet Protocol.

## Document structure

This Recommended Standard is organized as follows:

- section 1 provides purpose, scope, applicability and rationale, and lists definitions, conventions, and references used throughout this Recommended Standard;

- section 2 presents an overview of the MAL space packet binding in relation with the MO service framework;

- section 3 specifies the protocol layer;

- section 4 specifies the protocol data unit.

## Definitions

### Open Systems Interconnection Terms

#### Overview

This Recommended Standard makes use of a number of terms defined in the Open Systems Interconnection (OSI) references [E2] and [E3]. The use of those terms in this Recommended Standard shall be understood in a generic sense, i.e., in the sense that those terms are generally applicable to any of a variety of technologies that provide for the exchange of information between real systems.

#### Definitions Adopted from the OSI Basic Reference Model

protocol: A set of rules and formats (semantic and syntactic) which determine the communication behavior of entities in the performance of functions at the level of this protocol layer (N).

protocol data unit: A unit of data specified in a protocol consisting of protocol control information and possibly user data.

Service Data Unit (SDU): An amount of information whose identity is preserved when transferred between the upper layer (N+1) peer entities and which is not interpreted by the supporting entities of this layer (N).

#### Definitions Adopted from OSI Service Definition Conventions

primitive: An abstract, atomic, implementation-independent representation of an interaction between a service user and its service provider.

request: A submit primitive issued by a requestor.

indication: A deliver primitive received by an acceptor.

### Message Abstraction Layer Terms

### service: A set of capabilities that a component provides to another component via an interface. A Service is defined in terms of the set of operations that can be invoked and performed through the Service Interface. Service specifications define the capabilities, behaviour and external interfaces, but do not define the implementation.

### binding: the access mechanism for a Service. Bindings are used to locate and access Service Interfaces. Services use bindings to describe the access mechanisms that consumers have to use to call the Service. The binding specifies unambiguously the protocol stack required to access a Service Interface. Bindings may be defined statically at compile time or they may use a variety of dynamic run-time mechanisms (DNS, ports, discovery).

### Terms Defined in This Recommended Standard

For the purposes of this Recommended Standard, the following definitions also apply. Many other terms that pertain to specific items are defined in the appropriate sections.

abstract interface: An interface defined as a set of interaction patterns. An abstract interface can be specified by a service or provided by a protocol layer.

technology mapping: The mapping from the MAL abstract interfaces, including the MAL data types specification, to a particular technology.

messaging technology: A technology enabling the sending and receiving of messages through a particular protocol.

message model: An abstract message format specified in terms of message header fields and a message body.

interaction pattern: A message exchange protocol.

## NOMENCLATURE

### Normative Text

The following conventions apply for the normative specifications in this Recommended Standard:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification;

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

NOTE	–	These conventions do not imply constraints on diction in text that is clearly informative in nature.

### Informative Text

In the normative sections of this document, informative text is set off from the normative specifications either in notes or under one of the following subsection headings:

- Overview;

- Background;

- Rationale;

- Discussion.

## Bit Numbering Convention

In this document, the following convention is used to identify each bit in an N-bit field. The first bit in the field to be transmitted (i.e., the most left justified when drawing a figure) is defined to be ‘Bit 0’; the bit following is defined to be ‘Bit 1’, and so on up to ‘Bit N–1’.When the field is used to express a binary value (such as a counter), the Most Significant Bit (MSB) shall be the first transmitted bit of the field, i.e., ‘Bit 0’.

Figure 1-1: Bit Numbering Convention

In accordance with modern data communications practice, spacecraft data fields are often grouped into eight-bit ‘words’ which conform to the above convention. Throughout this Recommended Standard, the following nomenclature is used to describe this grouping:

Figure 1-2: Octet Convention

By CCSDS convention, all ‘spare’ or ‘unused’ bits shall be permanently set to value ‘zero’.

## references

The following publications contain provisions which, through reference in this text, constitute provisions of this document. At the time of publication, the editions indicated were valid. All publications are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the publications indicated below. The CCSDS Secretariat maintains a register of currently valid CCSDS publications.

[1]	Space Packet Protocol.  Recommendation for Space Data System Standards, CCSDS 133.0-B-1.  Blue Book.  Issue 1.  Washington, D.C.: CCSDS, September 2003.

[2]	Mission Operations Message Abstraction Layer (pink sheets).  Recommendation for Space Data System Standards, CCSDS 521.0-B-1.  Blue Book.  Issue 1.  Washington, D.C.: CCSDS, October 2010.

[3]	IEEE Standard for Floating-Point Arithmetic.  2nd ed.  IEEE Std.  754-2008.  New York: IEEE, 2008.

[4]	F. Yergeau.  UTF-8, a Transformation Format of ISO 10646.  STD 63.  Reston, Virginia: ISOC, November 2003.

[5]	Time Code Formats.  Recommendation for Space Data System Standards, CCSDS 301.0-B-4.  Blue Book.  Issue 4.  Washington, D.C.: CCSDS, November 2010.

# Overview

## General

This Recommended Standard provides a technology mapping from the MAL transport interface and the MAL data types specification to the Space Packet Protocol messaging technology (reference [1]).

The MAL Blue Book (reference [2]) defines an abstract transport interface as a set of request and indication primitives. A technology mapping specifies how these primitives are provided according to the messaging technology.

In particular, a technology mapping translates the MAL message model into one or several specific PDUs in compliance with the protocol used by the messaging technology. Moreover, a technology mapping casts the MAL data types into a specific binary encoding format.

Full interoperability of services is achieved only once a binding has been created to a specific messaging technology. Because all service specifications are defined in terms of MAL using a formal service description language, the technology mapping can be used, without modification, to bind the service specifications to the messaging technology protocol.

The diagram shown in figure 2-1 presents the set of standards documentation in support of the Mission Operations Services Concept. This MO MAL Space Packet Binding book belongs to the technology mappings documentation.

Figure 2-1: Mission Operations Services Concept Document Set

This Recommended Standard defines a mapping from the abstract notation of MAL to an unambiguous wire-level protocol. More specifically, it specifies:

- how the specific technology shall be used;

- how any transmission errors or issues shall be communicated to higher layers;

- how all link-level issues shall be defined;

- the physical representation of the abstract MAL messages necessary to constitute the operation templates;

- the mapping of the message structure rules for that technology;

- the physical representation of the abstract MAL data types.

It does not specify:

- individual application services, implementations, or products;

- the implementation of entities or interfaces within real systems;

- the methods or technologies required to acquire data;

- the management activities required to schedule a service;

- the representation of any service-specific PDUs (this is derived from the encoding rules defined in this document).

## MO Service Framework above Space Packet Protocol

The CCSDS Spacecraft Monitoring & Control (SM&C) working group has developed a concept for a mission operations service framework, which follows the principles of service-oriented architectures. The framework defines two important aspects: the first is a protocol for interaction between two separate entities; the second is a framework of common services providing functionality common to most uses of the service framework. An overview of this framework is presented in figure 2-2.

Figure 2-2: Overview of the MO Service Framework

This Recommended Standard defines how the MAL layer is mapped to the specific transport layer messaging technology called Space Packet Protocol.

The layer diagram displayed in figure 2-3 presents the MAL space packet binding layer in the MO service framework stack. It also gives the name of the main interfaces used and implemented by each layer. The main primitives are shown for each interface:

- the primitives for every operation provided by an MO service;

- the primitives for every interaction pattern provided by MAL;

- the primitives for transmitting and receiving a single MAL message or multiple MAL messages;

- the primitives for transmitting and receiving a space packet.

Figure 2-3: MO Service Framework above Space Packet Protocol

# Protocol Layer

### Overview

The MAL specification (reference [2], ‘Transport Interface’ section) defines the interface to be provided by the space packet binding layer. The following primitives are defined:

- SUPPORTEDQOS request;

- SUPPORTEDQOS RESPONSE indication;

- SUPPORTEDIP request;

- SUPPORTEDIP RESPONSE indication;

- TRANSMIT request;

- TRANSMIT ACK indication;

- TRANSMIT ERROR indication;

- TRANSMITMULTIPLE request;

- TRANSMITMULTIPLE ACK indication;

- TRANSMITMULTIPLE ERROR indication;

- RECEIVE indication;

- RECEIVEMULTIPLE indication.

The parameters are listed in table 3-1.

Table 3-1: MAL Transport Interface Primitives

| Primitive | Parameters |
| --- | --- |
| SUPPORTEDQOS request | QoS Level |
| SUPPORTEDQOS RESPONSE indication | Boolean |
| SUPPORTEDIP request | Interaction Type |
| SUPPORTEDIP RESPONSE indication | Boolean |
| TRANSMIT request | MAL Message QoS Properties |
| TRANSMIT ACK indication | - |
| TRANSMIT ERROR indication | MAL Message Header Error Number Extra Information QoS Properties |
| TRANSMITMULTIPLE request | List of: MAL Message QoS Properties |
| TRANSMITMULTIPLE ACK indication | - |
| TRANSMITMULTIPLE ERROR indication | List of: MAL Message Header Error Number Extra Information QoS Properties |
| RECEIVE indication | MAL Message QoS Properties |
| RECEIVEMULTIPLE indication | List of: MAL Message QoS Properties |

The Space Packet Protocol binding layer uses the interface defined by the Space Packet Protocol specification (reference [1]). The following primitives are provided:

- packet request;

- packet indication.

The parameters are listed in table 3-2.

Table 3-2: Packet Interface Primitives

| Primitive | Parameters |
| --- | --- |
| Packet request | Space Packet Application Process Identifier (APID) APID Qualifier (optional) QoS Requirement (optional) |
| Packet indication | Space Packet APID APID Qualifier (optional) |

- URI Format

The SPP binding URI format shall comply with the following rules:

- the URI scheme name shall be “malspp”;

- the scheme name shall be followed by a colon separator ‘:’ and a rootless path, i.e. a path that does not begin with a slash ‘/’;

- the path shall begin with the APID, an integer represented in decimal;

- the APID shall be a positive integer, including zero, strictly less than 2047;

- the APID shall be followed by a slash separator ‘/’ and the endpoint identifier, an integer represented in decimal;

- the endpoint identifier shall be a positive integer, including zero, strictly less than 256;

- the endpoint identifier may be followed by a slash separator ‘/’ and the APID qualifier.

- The scheme name “malspp” shall be added to the SANA registry “MAL Binding URI Scheme Name” and shall refer to the MAL Space Packet Binding document “524x1b1”.

- The MAL header fields ‘URI From’, and ‘URI To’ shall be compliant with the SPP binding URI format.

- The MAL header fields ‘URI From’, and ‘URI To’ shall contain the same APID in order to ensure that the APID of a MAL message is unique.

- The MAL header fields ‘URI From’, and ‘URI To’ shall contain the same APID qualifier in order to ensure that the APID qualifier of a MAL message is unique.

- QoS Properties

The QoS properties listed in table 3-1 shall be interpreted by the space packet binding layer.

NOTE	–	Some QoS properties refer to the terms Parameter Type Code (PTC) and Parameter Format Code (PFC). These terms are defined in ANNEX B.

Table 3-1: QoS Properties

| Property name | Type | Description | Default Value |
| --- | --- | --- | --- |
| APPL_TIME_CODE | MAL::UOctet | PFC to be applied to the secondary header field ‘Timestamp’ | 2 |
| AUTHENTICATION_ID | MAL::Blob | Value to be assigned to the MAL header field ‘Authentication Id’ if the QoS property ‘MAL_AUTHENTICATION’ is FALSE | Empty Blob |
| COMPACT_MAL_HEADER | MAL::Boolean | Boolean indicating whether the MAL header is mapped to a compact format or not | FALSE |
| DOMAIN | List<MAL::Identifier> | Value to be assigned to the MAL header field ‘Domain’ if the QoS property ‘COMPACT_MAL_HEADER’ is TRUE | Empty list |
| DURATION_FORMAT CODE | MAL::UOctet | PFC to be applied to the relative time parameters (PTC = 10) that result from the mapping of MAL::Duration elements | 16 |
| FINE_TIME_FORMAT_CODE | MAL::UOctet | PFC to be applied to the absolute time parameters (PTC = 9) that result from the mapping of MAL::FineTime elements | 18 |
| MAL_AUTHENTICATION | MAL::Boolean | Boolean indicating whether the MAL header field ‘Authentication Id’ is transmitted or not | TRUE |
| NETWORK_ZONE | MAL::Identifier | Value to be assigned to the MAL header field ‘Network Zone’ if the QoS property ‘COMPACT_MAL_HEADER’ is TRUE | Empty identifier |
| PRIORITY | MAL::UInteger | Value to be assigned to the MAL header field ‘Priority’ if the QoS property ‘COMPACT_MAL_HEADER’ is TRUE | 0 |
| QOS_LEVEL | MAL::QoSLevel | Value to be assigned to the MAL header field ‘QoSlevel’ if the QoS property ‘COMPACT_MAL_HEADER’ is TRUE | ASSURED |
| SESSION | MAL::SessionType | Value to be assigned to the MAL header field ‘Session’ if the QoS property ‘COMPACT_MAL_HEADER’ is TRUE | LIVE |
| SESSION_NAME | MAL::Identifier | Value to be assigned to the MAL header field ‘Session Name’ if the QoS property ‘COMPACT_MAL_HEADER’ is TRUE | LIVE |
| TIME_FORMAT_CODE | MAL::UOctet | PFC to be applied to the absolute time parameters (PTC = 9) that result from the mapping of MAL::Time elements | 2 |

Every QoS property listed in table 3-1 shall be assigned according to one of the following policy:

- mission defined: the value of the QoS property is unique for a given mission;

- application process defined: the value of the QoS property is defined for a given APID and APID qualifier, i.e. the value is applied to every MAL message generated by the application process which APID and APID qualifier are specified.

- Every QoS property listed in table 3-1 shall not be assigned with the value NULL.

### SupportedQoS Request

The SUPPORTEDQOS request primitive shall be provided.

Support for the Quality of Service (QoS) levels defined by MAL shall depend on the capabilities of the underlying layer used to convey the space packets.

### SupportedIP Request

The SUPPORTEDIP request primitive shall be provided.

The SUPPORTEDIP request primitive shall return TRUE for the interaction patterns SEND, SUBMIT, REQUEST, INVOKE, and PROGRESS.

The SUPPORTEDIP request primitive shall return FALSE for the interaction pattern PUBLISH-SUBSCRIBE.

NOTE	–	The MAL specification (reference [2]) requires that implementations of the MAL layer support the Publish-Subscribe pattern but that they can delegate this pattern to a transport that supports the pattern natively. The space packet protocol does not support the Publish-Subscribe pattern natively therefore a MAL implementation has to support this pattern itself.

### Transmit Request

The TRANSMIT request primitive shall be provided in order to translate a MAL message into a space packet and send the packet by calling the primitive ‘packet request’.

If any of the MAL header fields is NULL, then the TRANSMIT ERROR primitive shall be called with the error number MAL::INTERNAL.

The MAL message header fields and body elements shall be mapped to the space packet according to the specification given in section 4 of this Recommendation.

If any of the fields ‘URI From’, or ‘URI To’ is not compliant with the SPP binding URI format, then the TRANSMIT ERROR primitive shall be called with the error number MAL::INTERNAL.

If the field ‘URI To’ does not contain the same APID as the field ‘URI From’, then the TRANSMIT ERROR primitive shall be called with the error number MAL::INTERNAL.

If the field ‘URI To’ does not contain the same APID qualifier as the field ‘URI From’, then the TRANSMIT ERROR primitive shall be called with the error number MAL::INTERNAL.

The QoS properties that are listed in table 3-1 shall not be passed in the TRANSMIT request, i.e., on a per message basis, otherwise the TRANSMIT ERROR primitive shall be called with the error number MAL::INTERNAL.

If the QoS property ‘COMPACT_MAL_HEADER’ is TRUE, then the MAL header fields ‘QoSlevel’, ‘Priority’, ‘Domain’, ‘Network Zone’, ‘Session’, and ‘Session Name’ shall be assigned with the values of the QoS properties ‘QOS’, ‘PRIORITY’, ‘DOMAIN’, ‘NETWORK_ZONE’, ‘SESSION’, and ‘SESSION_NAME’, respectively, otherwise the TRANSMIT ERROR primitive shall be called with the error number MAL::INTERNAL.

If the QoS property ‘MAL_AUTHENTICATION’ is FALSE, then the MAL header field ‘Authentication Id’ shall be assigned with the value of the QoS property ‘AUTHENTICATION_ID’, otherwise the TRANSMIT ERROR primitive shall be called with the error number MAL::INTERNAL.

The QoS properties from the TRANSMIT request shall be passed to the Packet request primitive.

If the number of octets in the packet data field is strictly greater than 65536 octets, then the TRANSMIT ERROR primitive shall be called with the error number MAL::INTERNAL.

If an error is returned by the space packet sending request, then the TRANSMIT ERROR primitive shall be called with the error number MAL::INTERNAL.

If the packet is successfully sent, then the TRANSMIT ACK primitive shall be called.

### TransmitMultiple Request

- The TRANSMITMULTIPLE request primitive shall be provided by calling the TRANSMIT request primitive for every MAL message.

### Receive indication

The RECEIVE indication primitive shall be provided in order to receive a space packet and translate the packet into a MAL message.

The RECEIVE indication primitive shall be called when a Packet indication is triggered by the Space Packet Protocol layer.

The MAL message header fields and body elements shall be generated from the space packet and the Packet indication parameter ‘APID qualifier’ according to the specifications given in sections 3.2 and 4 of this Recommendation.

If the QoS property ‘COMPACT_MAL_HEADER’ is TRUE, then the MAL header fields ‘QoSlevel’, ‘Priority’, ‘Domain’, ‘Network Zone’, ‘Session’, and ‘Session Name’ shall be assigned with the values of the QoS properties ‘QOS’, ‘PRIORITY’, ‘DOMAIN’, ‘NETWORK_ZONE’, ‘SESSION’, and ‘SESSION_NAME’, respectively.

If the QoS property ‘MAL_AUTHENTICATION’ is FALSE, then the MAL header field ‘Authentication Id’ shall be assigned with the value of the QoS property ‘AUTHENTICATION_ID’.

If the field ‘URI To’ is unknown, then the error MAL::DESTINATION_UNKNOWN shall be returned if the interaction pattern enables to return a MAL message.

### ReceiveMultiple indication

- The RECEIVEMULTIPLE indication primitive shall not be provided.

# Protocol Data Unit

## Overview

This section specifies the way the MAL message header is mapped to a space packet and how the MAL message body is encoded and transmitted into the packet.

A simple tabular notation is used to describe the format of the packet secondary header and user data field. This tabular notation is composed of three levels:

- the name of the fields;

- the encoding format of the fields;

- the condition or the number of times the fields are encoded in.

A field can be assigned either with a parameter (as defined in annex B) or with the result of an encoding pattern.

If a field is assigned with a parameter, then the encoding format is specified by a Parameter Type Code (PTC) and a Parameter Format Code (PFC) as defined in annex B.

## Primary Header

### Overview

This subsection specifies the values to be assigned to the space packet primary header fields.

### Version Number

The field ‘Version Number’ shall be assigned with the value ‘000’ as specified by [1] and declared in the SANA registry “Packet Version Number”.

NOTE	–	Only Version 1 CCSDS Packet is supported.

### Type

The field ‘Type’ shall be assigned according to the MAL header fields ‘Interaction Type’ and ‘Interaction Stage’ as defined by table 4-1.

NOTE	–	Telecommand type is '1'. Telemetry type is '0'.

Table 4-1: Space Packet Type

| Interaction Type | Interaction Stage | Type name | Type value |
| --- | --- | --- | --- |
| SEND | Send | Telecommand | 1 |
| SUBMIT | Submit SubmitAck SubmitError | Telecommand Telemetry Telemetry | 1 0 0 |
| REQUEST | Request RequestResponse RequestError | Telecommand Telemetry Telemetry | 1 0 0 |
| INVOKE | Invoke InvokeAck InvokeResponse InvokeAckError InvokeResponseError | Telecommand Telemetry Telemetry Telemetry Telemetry | 1 0 0 0 0 |
| PROGRESS | Progress ProgressAck ProgressUpdate ProgressResponse ProgressAckError ProgressUpdateError ProgressResponseError | Telecommand Telemetry Telemetry Telemetry Telemetry Telemetry Telemetry | 1 0 0 0 0 0 0 |
| PUBSUB | Register Deregister Publish Register Publish Deregister Register Ack Deregister Ack Publish Register Ack Publish Deregister Ack Publish Publish Error Notify | Telecommand Telecommand Telecommand Telecommand Telemetry Telemetry Telemetry Telemetry Telemetry Telemetry Telemetry | 1 1 1 1 0 0 0 0 0 0 0 |

If a message is not allowed to be transmitted because of the space packet type, then the error MAL::INTERNAL shall be raised.

### Secondary header flag

The field ‘Secondary Header Flag’ shall be assigned with the value ‘1’.

NOTE	–	The field ‘Secondary Header Flag’ indicates presence of packet secondary header.

### Application Process ID

The field ‘APID’ shall be assigned with the APID part of the MAL header field ‘URI To’.

### Sequence Flags

The field ‘Sequence Flags’ shall be assigned with the value ‘11’, unsegmented user data.

### Sequence Count

The field ‘Sequence Count’ shall be assigned with the sequential binary count of each space packet generated for every APID..

### Packet length

The field ‘Packet Length’ shall be assigned with the total number of octets in the Packet Data Field minus 1.

## Secondary Header

### Overview

This subsection specifies the format of the space packet secondary header and the values to be assigned to its fields.

The secondary header is defined for MAL purposes by selecting option ‘c’ of clause ‘4.1.3.2.1.5’ of [1]:

- the Time Code Field is called ‘Timestamp’;

- the Ancillary Data Field is comprised of the fields ‘Version Number’, ‘SDU Type’, ‘Area’, ‘Service’, ‘Operation’, ‘Source Identifier’, ‘Destination Identifier’, ‘Transaction Identifier’, ‘Area version’, ‘Is Error’ and ‘Spare’.

However, if the QoS property APPL_TIME_CODE is NULL, then the option ‘b’ of clause ‘4.1.3.2.1.5’ of [1] is selected as the field ‘Timestamp’ is left out. The QoS property APPL_TIME_CODE is either mission defined or application process defined, so the chosen option remains static for a specific Path ID throughout all Mission Phases as required by the clause ‘4.1.3.2.1.6’ of [1].

The format of the packet secondary header is shown in table 4-2.

Table 4-2:  Secondary Header Format

| Timestamp | Version Number | SDU Type | Area | Service | Operation | Area Version | Is Error | Spare | Source Identifier | Destination Identifier | Transaction Identifier |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Absolute time (PTC = 9) (variable, integral number of octets) | Unsigned integer (PTC = 3) (PFC = 0) (4 bits) | Enumerated (PTC = 2) (PFC = 4) (4 bits) | Unsigned integer (PTC = 3) (PFC = 4) (8 bits) | Unsigned integer (PTC = 3) (PFC = 4) (8 bits) | Unsigned integer (PTC = 3) (PFC = 4) (8 bits) | Unsigned integer (PTC = 3) (PFC = 0) (4 bits) | Boolean (PTC = 1) (1 bit) | (3 bits) | Unsigned integer (PTC = 3) (PFC = 4) (8 bits) | Unsigned integer (PTC = 3) (PFC = 4) (8 bits) | Signed integer (PTC = 4) (PFC = 16) (64 bits) |
| Optional (left out if the QoS property ‘APPL_TIME_CODE’ is NULL) |  |  |  |  |  |  |  |  |  |  | Optional (left out if the packet Type is ‘1’ and if the SDU type is ‘0’) |

Timestamp

The field ‘Timestamp’ shall be encoded as an absolute time parameter (PTC = 9) with a PFC equal to the value of the QoS property ‘APPL_TIME_CODE’.

If the CDS format is used, then the standard CCSDS epoch of 1958 January 1 shall be applicable (see reference [5]).

If the QoS property ‘APPL_TIME_CODE’ is NULL, then the field ‘Timestamp’ shall be left out.

The field ‘Timestamp’ shall be assigned with the value of the MAL header field ‘Timestamp’.

### NOTE	–	The choice between CUC and CDS formats and the resolution of the timestamp field can vary from mission to mission and even between different application processes. For some missions or application processes, this time field may not even be present. The presence or absence of the field and its encoding are explicitly defined by the QoS property APPL_TIME_CODE.

### Version Number

The field ‘Version Number’ shall be encoded as an unsigned integer (PTC = 3) with PFC = 0.

The field ‘Version Number’ shall identify the user data field as defined by this Recommendation.

The field ‘Version Number’ shall be assigned with the value ‘0000’.

The version number ‘0000’ shall be added to the SANA registry “MAL Space Packet Binding Version Number” and shall refer to the MAL Space Packet Binding document “524x1b1”.

### SDU Type

The field ‘SDU Type’ shall be encoded as an enumerated parameter (PTC = 2) with PFC = 4.

If the space packet type is telecommand, then the field ‘SDU Type’ shall be assigned according to the MAL header fields ‘Interaction Type’ and ‘Interaction Stage’ as specified by table 4-4.

Table 4-4: Telecommand SDU Types

| Interaction Type | Interaction Stage | SDU Type |
| --- | --- | --- |
| Send | Initial | 0 |
| Submit | Initial | 1 |
| Request | Initial | 2 |
| Invoke | Initial | 3 |
| Progress | Initial | 4 |
| Pub/Sub | Register | 5 |
| Pub/Sub | Deregister | 6 |
| Pub/Sub | Publish Register | 7 |
| Pub/Sub | Publish Deregister | 8 |

If the space packet type is telemetry, then the field ‘SDU Type’ shall be assigned according to the MAL header fields ‘Interaction Type’ and ‘Interaction Stage’ as specified by table 4-5.

Table 4-5: Telemetry SDU Types

| Interaction Type | Interaction Stage | SDU Type |
| --- | --- | --- |
| Submit | Ack | 0 |
| Request | Response | 1 |
| Invoke | Ack | 2 |
| Invoke | Response | 3 |
| Progress | Ack | 4 |
| Progress | Update | 5 |
| Progress | Response | 6 |
| Pub/Sub | Register Ack | 7 |
| Pub/Sub | Deregister Ack | 8 |
| Pub/Sub | Publish Register Ack | 9 |
| Pub/Sub | Publish Deregister Ack | 10 |
| Pub/Sub | Publish | 11 |
| Pub/Sub | Publish Error | 12 |
| Pub/Sub | Notify | 13 |

### Area

The field ‘Area’ shall be encoded as an unsigned integer parameter (PTC = 3) with PFC = 4.

The field ‘Area’ shall be assigned with the value of the MAL header field ‘Service Area’.

### Service

The field ‘Service’ shall be encoded as an unsigned integer parameter (PTC = 3) with PFC = 4.

The field ‘Service’ shall be assigned with the value of the MAL header field ‘Service’.

### Operation

The field ‘Operation’ shall be encoded as an unsigned integer parameter (PTC = 3) with PFC = 4.

The field ‘Operation’ shall be assigned with the value of the MAL header field ‘Operation’.

### Area Version

The field ‘Area Version’ shall be encoded as an unsigned integer (PTC = 3) with PFC= 0.

The field ‘Area Version’ shall be assigned with the value of the MAL header field ‘Area Version’.

### Is Error

The field ‘Is Error’ shall be encoded as a Boolean parameter (PTC = 1).

The field ‘Is Error’ shall be assigned with the value of the MAL header field ‘Is Error Message’.

### Spare

The field ‘Spare’ shall be used to reach an integral number of octets.

The field ‘Spare’ shall be assigned with 3 bits equal to 0.

### Source Identifier

The field ‘Source Identifier’ shall be encoded as an unsigned integer parameter (PTC = 3) with PFC = 4.

The field ‘Source Identifier’ shall be assigned with the ‘endpoint identifier’ part of the MAL header field ‘URI From’.

### Destination Identifier

The field ‘Destination Identifier’ shall be encoded as an unsigned integer parameter (PTC = 3) with PFC = 4.

The field ‘Destination Identifier’ shall be assigned with the ‘endpoint identifier’ part of the MAL header field ‘URI To’.

Transaction Identifier

The field ‘Transaction Identifier’ shall be encoded as a signed integer parameter (PTC = 4) with PFC = 16.

If the MAL header field ‘Interaction Type’ is equal to the value ‘SEND’, then the field ‘Transaction Identifier’ shall not be encoded in the secondary header.

The field ‘Transaction Identifier’ shall be assigned with the value of the MAL header field ‘Transaction Id’.

## User Data Field

### Overview

This subsection specifies the format of the space packet user data field and the values to be assigned to its fields.

The format of the user data field is shown in table 4-3.

Table 4-3:  User Data Field Format

| QoS | Session | Spare | Priority | Network Zone | Session Name | Domain Identifier | Authentication Identifier | Body |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Enumerated (PTC = 2) (PFC = 2) (2 bits) | Enumerated (PTC = 2) (PFC = 2) (2 bits) | (4 bits) | Variable unsigned integer (PTC = 11) (PFC = 2) (variable, integral number of octets) | Character-string (PTC = 8) (variable, integral number of octets) | Character-string (PTC = 8) (variable, integral number of octets) | Encoding pattern List (variable, integral number of octets) | Octet-string (PTC = 7) (PFC = 0) (variable, integral number of octets) | Encoding pattern Body (variable, integral number of octets) |
| Optional (not encoded if the QoS property ‘COMPACT_MAL_HEADER’ is TRUE) | Optional (not encoded if the QoS property ‘MAL_AUTHENTICATION’ is FALSE) |  |

### QoS

The field ‘QoS’ shall be encoded as an enumerated parameter (PTC = 2) with PFC = 2.

If the QoS property ‘COMPACT_MAL_HEADER’ is TRUE, then the field ‘QoS’ shall be left out.

If the QoS property ‘COMPACT_MAL_HEADER’ is FALSE, then the field ‘QoS’ shall be assigned according to the value of the MAL header field ‘QoSlevel’ as specified by the table.

Table 4-4: QoS Enumerated Value

| QoSlevel | Enumerated value |
| --- | --- |
| BESTEFFORT | 0 |
| ASSURED | 1 |
| QUEUED | 2 |
| TIMELY | 3 |

### Session

The field ‘Session’ shall be encoded as an enumerated parameter (PTC = 2) with PFC = 2.

If the QoS property ‘COMPACT_MAL_HEADER’ is TRUE, then the field ‘Session’ shall be left out.

If the QoS property ‘COMPACT_MAL_HEADER’ is FALSE, then the field ‘Session’ shall be assigned according to the value of the MAL header field ‘Session’ as specified by the table.

Table 4-4: Session Enumerated Value

| Session | Enumerated value |
| --- | --- |
| LIVE | 0 |
| SIMULATION | 1 |
| REPLAY | 2 |

Spare

If the QoS property ‘COMPACT_MAL_HEADER’ is TRUE, then the field ‘Spare’ shall be left out.

If the QoS property ‘COMPACT_MAL_HEADER’ is FALSE, then the field ‘Spare’ shall be assigned with 4 bits equal to 0.

### Priority

The field ‘Priority’ shall be encoded as a variable unsigned integer parameter (PTC = 11) with PFC = 2.

If the QoS property ‘COMPACT_MAL_HEADER’ is TRUE, then the field ‘Priority’ shall be left out.

If the QoS property ‘COMPACT_MAL_HEADER’ is FALSE, then the field ‘Priority’ shall be assigned with the value of the MAL header field ‘Priority’.

### Network Zone

The field ‘Network Zone’ shall be encoded as a character-string parameter (PTC = 8).

If the QoS property ‘COMPACT_MAL_HEADER’ is TRUE, then the field ‘Network Zone’ shall be left out.

If the QoS property ‘COMPACT_MAL_HEADER’ is FALSE, then the field ‘Network Zone’ shall be assigned with the value of the MAL header field ‘Network Zone’.

### Session name

The field ‘Session Name’ shall be encoded as a character-string parameter (PTC = 8).

If the QoS property ‘COMPACT_MAL_HEADER’ is TRUE, then the field ‘Session Name’ shall be left out.

If the QoS property ‘COMPACT_MAL_HEADER’ is FALSE, then the field ‘Session Name’ shall be assigned with the value of the MAL header field ‘Session Name’.

### Domain Identifier

The field ‘Domain Identifier’ shall be encoded according to the List encoding pattern (defined in section 4.5.12).

If the QoS property ‘COMPACT_MAL_HEADER’ is TRUE, then the field ‘Domain Identifier’ shall be left out.

If the QoS property ‘COMPACT_MAL_HEADER’ is FALSE, then the field ‘Domain Identifier’ shall be assigned with the value of the MAL header field ‘Domain’.

### Authentication identifier

The field ‘Authentication Identifier’ shall be encoded as an octet-string parameter (PTC = 7) with a variable length (PFC = 0).

If the QoS property ‘MAL_AUTHENTICATION’ is FALSE, then the field ‘Authentication Identifier’ shall be left out.

If the QoS property ‘MAL_AUTHENTICATION’ is TRUE, then the field ‘Authentication Identifier’ shall be assigned with the value of the MAL header field ‘Authentication Id’.

### Body

## The field ‘Body’ shall be assigned with the result of the Body encoding pattern (defined in section 4.5.2) applied to the MAL message body.

## Encoding Patterns

### Overview

An encoding pattern is a function that translates a MAL::Element into a sequence of encoded parameters. This translation is defined in a generic and modular way:

- ‘generic’ means that the encoding format is not specifically defined for every data structure and every usage context; it is generated by applying the generic patterns to the data structure to be encoded in a specific usage context;

- ‘modular’ means that the encoding patterns are defined by isolating every MAL data type pattern and specifying the encoding format for each of them.

An encoding pattern can delegate to another pattern the generation of a part of the encoding format: a pattern is a graph of patterns with potential cycles.

Two types of pattern are defined:

- conditional pattern: a pattern that selects a pattern among a list of patterns according to some conditions;

- field encoding pattern: a pattern that encodes a sequence of fields.

A conditional pattern is specified by a condition table with two columns:

- the first column contains the conditions to be checked in the order of the rows in the table;

- the second column contains the pattern to be applied if the condition is verified.

A field encoding pattern is specified with a tabular notation as defined in section 4.1.

The patterns are defined in the following subsections.

### Body

The Body pattern shall be applied to encode a MAL message body.

The Body pattern shall encode the following field:

Body element

Pattern Body Element

Repeated for every element in the body in the same order as the elements are declared in the operation definition

Each element of the body shall be encoded in the same order as they are declared in the operation definition.

If the body declared by the operation is empty, then the encoding result shall be empty.

Body Element

The Body Element pattern shall check the following condition table:

| Condition | Pattern |
| --- | --- |
| The MAL header fields ‘Interaction Type’ and ‘Interaction stage’ are respectively equal to: Pub/Sub Publish And the element is a list of updates. | Publish Update List |
| The MAL header fields ‘Interaction Type’ and ‘Interaction stage’ are respectively equal to: Pub/Sub Notify And the element is a list of updates. | Nullable Element |
| The MAL header field ‘Interaction Type’ is Pub/Sub | Element |
| The MAL header field ‘Is Error Message’ is TRUE | Element |
| No condition | Nullable Element |

### Nullable Element

The Nullable Element pattern shall encode the following fields:

| Null Tag | Element |
| --- | --- |
| Boolean (PTC = 1) | Pattern Element |
|  | If Null Tag is FALSE |

The field ‘Null Tag’ shall be TRUE if the element is NULL; it shall be FALSE if the element is not NULL.

NOTE	–	The NULL value could be encoded in a specific way depending on the element type, but it would break the modularity of the encoding format.

### Element

The Element pattern shall check the following condition table:

| Condition | Pattern |
| --- | --- |
| The declared type of the element is MAL::Attribute | Abstract Attribute |
| The declared type of the element is MAL::Element, MAL::Composite, or an abstract composite | Abstract |
| The declared type of the element is final | Final |

NOTE	–	Only the last message body element is allowed to be typed MAL::Element, MAL::Composite or an abstract composite type. So the pattern Abstract can only be applied to the last element of a message body.

### Abstract

The Abstract pattern shall encode the following fields:

| Area | Service | Area Version | Type | Element |
| --- | --- | --- | --- | --- |
| Unsigned integer (PTC = 3, PFC = 12) | Unsigned integer (PTC = 3, PFC = 12) | Unsigned integer (PTC = 3, PFC = 4) | Unsigned integer (PTC = 3, PFC = 13) | Pattern Final |

The field ‘Area’ shall be assigned with the area number of the element type.

If the element type is defined by a service, then the field ‘Service’ shall be assigned with the service number of the element type.

If the element type is not defined by a service, then the field ‘Service’ shall be assigned with ‘0’.

The field ‘Area Version’ shall be assigned with the area version of the element type.

The field ‘Type’ shall be assigned with the short form part of the element type.

### Abstract Attribute

The Abstract Attribute pattern shall encode the following fields:

| Attribute Tag | Attribute |
| --- | --- |
| Unsigned integer (PTC = 4, PFC = 4) | Pattern Attribute |

The field ‘Attribute Tag’ shall be assigned with the short form part of the attribute minus 1 in order that the tag starts from zero.

### Final

The Final pattern shall check the following condition table:

| Condition | Pattern |
| --- | --- |
| The type of the element is a MAL::Attribute | Attribute |
| The type of the element is a MAL::Enumeration | Enumeration |
| The type of the element is a MAL::List | List |
| The type of the element is a MAL::Composite | Composite |

### Enumeration

The Enumeration pattern shall be applied to encode a MAL::Enumeration.

The Enumeration pattern shall encode the following field:

Enumeration Value Index

The PTC and PFC depend on the enumeration size

If the enumeration size is smaller or equal to 256, then the field ‘Enumeration Value Index’ shall be an unsigned integer (PTC = 3) with a PFC equal to 4 (8 bits).

If the enumeration size is greater than 256 and smaller or equal to 65536, then the field ‘Enumeration Value Index’ shall be an unsigned variable integer (PTC = 11) with a PFC equal to 1.

If the enumeration size is greater than 65536, then the field ‘Enumeration Value Index’ shall be an unsigned variable integer (PTC = 11) with a PFC equal to 2.

The field ‘Enumeration Value Index’ shall be assigned with the index of the value in the enumeration; the index shall start at 0.

### Composite

The Composite pattern shall be applied to encode a MAL composite.

The Composite pattern shall encode the following field:

Body element

Pattern Body Element

Repeated for every field in the composite in the same order as the fields are declared

The fields shall be encoded in the same order as they are declared.

If the composite inherits from another composite structure, the Composite pattern shall be applied first to the inherited composite and then to the composite.

### Field

The Field pattern shall check the following condition table:

| Condition | Pattern |
| --- | --- |
| The value of the attribute ‘canBeNull’ in the field declaration is TRUE | Nullable Element |
| No condition | Element |

### List

The List pattern shall be applied to encode a MAL::List.

The List pattern shall encode the following fields:

| List Length | List Element |
| --- | --- |
| Unsigned variable integer (PTC = 11, PFC = 2) | Pattern Nullable Element |
|  | Repeated for every element in the list in the same order as the list |

### The field ‘List Length’ shall be assigned with the length of the list.

### The list elements shall be encoded in the same order as in the list.

### Publish Update List

The Publish Update List pattern shall be applied to encode an update list from a publish message.

NOTE	–	The Publish Update List pattern enables a MAL broker not to decode the updates when handling a publish message.

The Publish Update List pattern shall encode the following fields:

| Null Tag | List Length | Encoded Update Size | Update |
| --- | --- | --- | --- |
| Boolean (PTC = 1) | Unsigned variable integer (PTC = 11, PFC = 2) | Unsigned variable integer (PTC = 11, PFC = 2) | Pattern Nullable Element |
|  |  | Repeated for every update in the list in the same order as the list |

The field ‘Null Tag’ shall be TRUE if the list is NULL; it shall be FALSE if the list is not NULL.

The field ‘List Length’ shall be assigned with the length of the list.

### The field ‘Encoded Update Size’ shall be assigned with the number of octets used to encode the following field ‘Update’.

### The updates shall be encoded in the same order as in the list.

### Attribute

The Attribute pattern shall be applied to encode a MAL::Attribute.

The Attribute pattern shall check the following condition table:

| Condition | Pattern |
| --- | --- |
| The attribute type is MAL::Blob | Blob |
| The attribute type is MAL::Boolean | Boolean |
| The attribute type is MAL::Duration | Duration |
| The attribute type is MAL::Float | Float |
| The attribute type is MAL::Double | Double |
| The attribute type is MAL::Identifier | Identifier |
| The attribute type is MAL::Octet | Octet |
| The attribute type is MAL::UOctet | UOctet |
| The attribute type is MAL::Short | Short |
| The attribute type is MAL::UShort | UShort |
| The attribute type is MAL::Integer | Integer |
| The attribute type is MAL::UInteger | UInteger |
| The attribute type is MAL::Long | Long |
| The attribute type is MAL::ULong | ULong |
| The attribute type is MAL::String | String |
| The attribute type is MAL::Time | Time |
| The attribute type is MAL::FineTime | FineTime |
| The attribute type is MAL::URI | Uri |

### Blob

The Blob pattern shall be applied to encode a MAL::Blob.

The Blob pattern shall encode the following field:

Blob Value

Variable length octet-string (PTC = 7, PFC = 0)

The field ‘Blob Value’ shall be assigned with the MAL::Blob value.

### Boolean

The Boolean pattern shall be applied to encode a MAL::Boolean.

The Boolean pattern shall encode the following field:

Boolean Value

Boolean (PTC = 1)

The field ‘Boolean Value’ shall be assigned with the MAL::Boolean value.

### Duration

The Duration pattern shall be applied to encode a MAL::Duration.

The Duration pattern shall encode the following field:

Duration Value

Relative Time (PTC = 10)

The field ‘Duration Value’ shall be encoded with a PFC given by the QoS property DURATION_FORMAT CODE.

The field ‘Duration Value’ shall be assigned with the MAL::Duration value.

### Float

The Float pattern shall be applied to encode a MAL::Float.

The Float pattern shall encode the following field:

Float Value

Real (PTC = 5, PFC = 1) (32 bits)

### The field ‘Float Value’ shall be assigned with the MAL::Duration value.

### Double

The Double pattern shall be applied to encode a MAL::Double.

The Double pattern shall encode the following field:

Double Value

Real (PTC = 5, PFC = 2) (64 bits)

### The field ‘Double Value’ shall be assigned with the MAL::Double value.

### Identifier

The Identifier pattern shall be applied to encode a MAL::Identifier.

The Identifier pattern shall encode the following field:

Identifier Value

Character-string (PTC = 8)

### The field ‘Identifier Value’ shall be assigned with the MAL::Identifier value.

### Octet

The Octet pattern shall be applied to encode a MAL::Octet.

The Octet pattern shall encode the following field:

Octet Value

Signed integer (PTC = 4, PFC = 4) (8 bits)

The field ‘Octet Value’ shall be assigned with the MAL::Octet value.

### UOctet

The UOctet pattern shall be applied to encode a MAL::UOctet.

The UOctet pattern shall encode the following field:

UOctet Value

Unsigned integer (PTC = 3, PFC = 4) (8 bits)

The field ‘UOctet Value’ shall be assigned with the MAL::UOctet value.

### Short

The Short pattern shall be applied to encode a MAL::Short.

The Short pattern shall encode the following field:

Short Value

Signed variable integer (PTC = 12, PFC = 1)

The field ‘Short Value’ shall be assigned with the MAL::Short value.

### UShort

The UShort pattern shall be applied to encode a MAL::UShort.

The UShort pattern shall encode the following field:

UShort Value

Unsigned variable integer (PTC = 11, PFC = 1)

The field ‘UShort Value’ shall be assigned with the MAL::UShort value.

### Integer

The Integer pattern shall be applied to encode a MAL::Integer.

The Integer pattern shall encode the following field:

Integer Value

Signed variable integer (PTC = 12, PFC = 2)

The field ‘Integer Value’ shall be assigned with the MAL::Integer value.

### UInteger

The UInteger pattern shall be applied to encode a MAL::UInteger.

The UInteger pattern shall encode the following field:

UInteger Value

Unsigned variable integer (PTC = 11, PFC = 2)

The field ‘UInteger Value’ shall be assigned with the MAL::UInteger value..

### Long

The Long pattern shall be applied to encode a MAL::Long.

The Long pattern shall encode the following field:

Long Value

Signed variable integer (PTC = 12, PFC = 3)

The field ‘Long Value’ shall be assigned with the MAL::Long value.

### ULong

The ULong pattern shall be applied to encode a MAL::ULong.

The ULong pattern shall encode the following field:

ULong Value

Unsigned variable integer (PTC = 11, PFC = 3)

The field ‘ULong Value’ shall be assigned with the MAL::ULong value.

### String

The String pattern shall be applied to encode a MAL::String.

The String pattern shall encode the following field:

String Value

Character-string (PTC = 8)

The field ‘String Value’ shall be assigned with the MAL::String value.

### Time

The Time pattern shall be applied to encode a MAL::Time.

The Time pattern shall encode the following field:

Time Value

Absolute time (PTC = 9)

The field ‘Time Value’ shall be encoded with a PFC given by the QoS property TIME_FORMAT_CODE.

The field ‘Time Value’ shall be assigned with the MAL::Time value.

### FineTime

The FineTime pattern shall be applied to encode a MAL::FineTime.

The FineTime pattern shall encode the following field:

FineTime Value

Absolute time (PTC = 9)

The field ‘FineTime Value’ shall be encoded with a PFC given by the QoS property FINE_TIME_FORMAT_CODE.

The field ‘FineTime Value’ shall be assigned with the MAL::FineTime value.

### Uri

The Uri pattern shall be applied to encode a MAL::URI.

The Uri pattern shall encode the following field:

URI Value

Character-string (PTC = 8)

The field ‘URI Value’ shall be assigned with the MAL::URI value.

Protocol Implementation Conformance Statement Proforma

(Normative)

INTRODUCTION

Overview

This annex provides the Protocol Implementation Conformance Statement (PICS) Requirements List (PRL) for implementations of the MAL space packet binding standard. The PICS for an implementation is generated by completing the PRL in accordance with the instructions below.

An implementation’s completed PRL is called the PICS. The PICS states which protocol features have been implemented. The following entities can use the PICS:

–	the protocol implementer, as a checklist to reduce the risk of failure to conform to the standard through oversight;

–	the supplier and acquirer or potential acquirer of the implementation, as a detailed indication of the capabilities of the implementation, stated relative to the common basis for understanding provided by the standard PICS proforma;

–	the user or potential user of the implementation, as a basis for initially checking the possibility of interworking with another implementation (while interworking can never be guaranteed, failure to interwork can often be predicted from incompatible PICSes);

–	a protocol tester, as the basis for selecting appropriate tests against which to assess the claim for conformance of the implementation.

NOTATION

Status Column Symbols

The following are used in the PRL to indicate the status of features:

| Symbol | Meaning |
| --- | --- |
| M | Mandatory |
| O | Optional |

Support Column Symbols

The support of every item as claimed by the implementer is stated by entering the appropriate answer (Y, N, or N/A) in the support column.

| Symbol | Meaning |
| --- | --- |
| Y | Yes, supported by the implementation |
| N | No, not supported by the implementation |
| N/A | Not applicable |

GENERAL INFORMATION

IDENTIFICATION OF PICS

| Ref | Question | Response |
| --- | --- | --- |
| 1 | Date of Statement (DD/MM/YYYY) |  |
| 2 | CCSDS document number containing the PICS |  |
| 3 | Date of CCSDS document containing the PICS |  |

IDENTIFICATION OF IMPLEMENTATION UNDER TEST (IUT)

| Ref | Question | Response |
| --- | --- | --- |
| 1 | Implementation name |  |
| 2 | Implementation version |  |
| 3 | Machine name |  |
| 4 | Machine version |  |
| 5 | Operating System name |  |
| 6 | Operating System version |  |
| 7 | Special Configuration |  |
| 8 | Other Information |  |

USER IDENTIFICATION

| Supplier |  |
| --- | --- |
| Contact Point for Queries |  |
| Implementation name(s) and Versions |  |
| Other Information Necessary for full identification —e.g., name(s) and version(s) for machines and/or operating systems; System Name(s) |  |

INSTRUCTIONS FOR COMPLETING THE PRL

An implementer shows the extent of compliance to the protocol by completing the PRL; the resulting completed PRL is called a PICS.

MO MAL Space Packet Binding PICS

Message Abstraction Layer

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1-1 | Transaction Handling | [2] section 3.2 | M |  |
| 1-2 | State Transitions | [2] section 3.3 | M |  |
| 1-3 | Message Composition | [2] section 3.4 | M |  |
| 1-4 | MAL Service Interface | [2] section 3.5 | M |  |
| 1-5 | Access Control Interface | [2] section 3.6 | M |  |
| 1-6 | Transport Interface | [2] section 3.7 | M |  |
| 1-7 | MAL Data Type Specification | [2] section 4 | M |  |
| 1-8 | MAL Errors | [2] section 5 | M |  |

space packet binding Layer

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 2-1 | URI Format | 3.2 | M |  |
| 2-2 | QoS Properties | 3.3 | M |  |
| 2-3 | SupportedQoS Request | 3.4 | M |  |
| 2-4 | SupportedIP Request | 3.5 | M |  |
| 2-5 | Transmit Request | 3.6 | M |  |
| 2-6 | MultipleTransmit Request | 3.7 | M |  |
| 2-7 | Receive Indication | 3.8 | M |  |
| 2-8 | MultipleReceive Indication | 3.9 | M |  |

Protocol Data Unit

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 3-1 | Primary Header Encoding | 4.2 | M |  |
| 3-2 | Secondary Header Encoding | 4.3 | M |  |
| 3-3 | Field ‘Timestamp’ | 4.3.2 | O |  |
| 3-4 | User Data Field Encoding | 4.4 | M |  |
| 3-5 | Fields ‘QoS’, ‘Session’, ‘Spare’, ‘Priority’, ‘Network Zone’, ‘Session Name’, ‘Domain Identifier’ | 4.4.2, 4.4.3, 4.4.4, 4.4.5, 4.4.6, 4.4.7, 4.4.8 | O |  |
| 3-6 | Field ‘Authentication Identifier’ | 4.4.9 | O |  |
| 3-7 | Encoding Patterns | 4.5 | M |  |

Encoding Format of Parameter Types

(Normative)

INTRODUCTION

A parameter is the smallest data type that can be encoded in a packet. A parameter cannot be decomposed into smaller data types.

The parameter type defines the abstract class to which the parameter values belong. For a given parameter type there can be variations in the format and length of the values.

Each combination of a parameter type and encoding format has an associated parameter code, which identifies completely a simple type and how it is physically encoded in a packet.

The parameter code is used whenever an explicit definition of a parameter field is requested.

When contained in a packet, the parameter code consists of two consecutive parameter fields with type ‘Enumerated’ (as defined later in this section):

| PTC | PFC |
| --- | --- |
| Enumerated | Enumerated |

where:

- PTC = Parameter Type Code;

- PFC = Parameter Format Code.

The only parameter types are those defined in this annex. For each type of parameter, a list of standard parameter formats is defined.

Boolean Parameter (PTC = 1)

A Boolean parameter is a one-bit parameter, with two distinguished values only, involved in logical operations where:

- value 1 denotes ‘TRUE’;

- value 0 denotes ‘FALSE’.

The parameter format code for a Boolean parameter is PFC = 0.

Enumerated Parameter (PTC = 2)

An enumerated parameter is a bit-field of length PFC bits that must be mapped, using a relevant look up table, into some other form that carries the actual meaning. For example, an enumerated parameter with PFC = 3 could map the bit sequence ‘101’ to the character-string ‘INVALID’.

The enumerated values are discrete integer values only, involved in logical and comparative expressions (but not in numeric and relational expressions). The enumerated values are unordered.

The parameter format codes of an enumerated parameter is PFC = 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, 15, 16, 24, or 32; i.e., the code is equal to the length in bits of the parameter values.

Unsigned Integer Parameter (PTC = 3)

The values that an unsigned integer parameter can take are positive and can be involved in arithmetical, relational, and comparative expressions. An unsigned integer is encoded, with Bit 0 being the MSB and Bit N-1 the Least Significant Bit (LSB).

The most significant octet is encoded first.

The formats of an unsigned integer are:

| Format Code | Format Definition | Lowest Value | Highest Value |
| --- | --- | --- | --- |
| 0 ≤ PFC ≤ 12 | PFC + 4 bits, unsigned | 0 | 2^(PFC + 4) -1 (15 to 65535) |
| PFC = 13 | 3 octets, unsigned | 0 | 2^24 -1 (16277215) |
| PFC = 14 | 4 octets, unsigned | 0 | 2^32 -1 (~ 4,3 10^9) |
| PFC = 15 | 6 octets, unsigned | 0 | 2^48 -1 (~ 2,8 10^14) |
| PFC = 16 | 8 octets, unsigned | 0 | 2^64 -1 (~ 18,5 10^18) |

Signed Integer Parameter (PTC = 4)

The values that a signed integer parameter can take are positive or negative and can be involved in arithmetical, relational, and comparative expressions.

- If Bit 0 = 0, the value is positive following the unsigned integer convention.

- If Bit 0 = 1, the value is negative and the field is the ‘2's complement’ of the positive value.

The most significant octet is encoded first.

The formats of a signed integer are:

| Format Code | Format Definition | Lowest Value | Highest Value |
| --- | --- | --- | --- |
| 0 ≤ PFC ≤ 12 | PFC + 4 bits, signed | -2^(PFC + 3) (-8 to -32768) | 2^(PFC + 3) -1 (7 to 32767) |
| PFC = 13 | 3 octets, signed | -2^23 (-8388608) | 2^23 -1 (8388607) |
| PFC = 14 | 4 octets, signed | -2^31 (~ -2,15*10^9) | 2^31 -1 (~ 2,15*10^9) |
| PFC = 15 | 6 octets, signed | -2 ^47 (~ -1,4*10^14) | 2^47 -1 (~ 1,4*10^14) |
| PFC = 16 | 8 octets, signed | -2^63 (~ -9,2*10^18) | 2^63 -1 (~ 9,2*10^18) |

Real Parameter (PTC = 5)

A real parameter is either the single-precision format or the double-precision format defined in IEEE 754 Standard for Binary Floating-Point Arithmetic (reference [3]). The important features of their definitions are repeated here:

- Each format permits the representation of the numerical values of the form:

(-1)^S*2^E*(b0,b1,b2…bp-1)

where:

- b0,b1,b2…bp-1 means b0 / 2^0 + b1 / 2^1 + b2 / 2^2 + … + bp-1/ 2^(p-1);

- S =0 or 1;

- E = any integer between Emin and Emax, inclusive;

- bi = 0 or 1;

- p = number of significant bits (precision).

- Each format also permits the representation of two infinities, ‘∞’ and ‘-∞’, and special values which are not numbers.

- Real numbers in both formats are composed of three subfields:

- sign unsigned integer, contains the value S;

- exponent unsigned integer, contains the value E+127 on 8 bits (single precision) or E+1023 (double precision);

- fraction bit string, contains the value b0,b1,b2…bp-1 with p = 24 (single precision) or p = 53 (double precision).

The format codes of a real parameter are

- PFC = 1: 4 octets single-precision format (IEEE standard);

- PFC = 2: 8 octets double-precision format (IEEE standard).

The encoded value of a single-precision real parameter is constituted as follows:

| Sign | Exponent | Fraction |
| --- | --- | --- |
| 1 bit | 8 bits | 23 bits |

The value of a single-precision parameter is:

|  | Value |
| --- | --- |
| If exponent = 255 and fraction <> 0 | Not a Number |
| If exponent = 255 and fraction = 0 | (-1)^sign * ∞ |
| If 0 < exponent < 255 | (-1)^sign * 2^(exponent -127) * (1, fraction) |
| If exponent = 0 and fraction <> 0 | (-1)^sign * 2^(-126) * (0, fraction) |
| If exponent = 0 and fraction = 0 | 0 |

The encoded value of a double-precision real parameter is constituted as follows:

| Sign | Exponent | Fraction |
| --- | --- | --- |
| 1 bit | 11 bits | 52 bits |

The value of a double-precision parameter is:

|  | Value |
| --- | --- |
| If exponent = 2047 and fraction <> 0 | Not a Number |
| If exponent = 2047 and fraction = 0 | (-1)^sign * ∞ |
| If 0 < exponent < 2047 | (-1)^sign * 2^(exponent -1023) * (1, fraction) |
| If exponent = 0 and fraction <> 0 | (-1)^sign * 2^(-1022) * (0, fraction) |
| If exponent = 0 and fraction = 0 | 0 |

NOTE	–	In the cases where exponent = 0 and fraction <> 0, the values are called denormalized.

The range of possible values and precision for a real parameter are as follows:

- single precision:

1,12*10-38 ≤ | value | ≤ 3,40*1038 (precision 1,15*10-7)

- double precision:

2,22*10-308 ≤ | value | ≤ 1,79*10308 (precision 2,22*10-16)

Bit-String Parameter (PTC = 6)

The values that a bit-string parameter can take are variable-length or fixed-length sequences of bits, each with a value 1 or 0. The meaning and interpretation of a value is application-process specific.

The format codes of a bit-string parameter are

- PFC = 0: A variable-length bit string;

- PFC > 0: A fixed-length bit string with a number of bits equal to PFC.

A variable-length bit-string parameter is of the form:

| n | B1…Bn |
| --- | --- |
| Variable unsigned integer | n bits |

where:

- B1…Bn	are bits;

- n indicates the number of bits which follows.

A fixed-length bit-string parameter is of the form:

B1…Bn

n bits

where:

- B1…Bn	 are bits;

- n indicates the number of bits and is equal to PFC.

Octet-String Parameter (PTC = 7)

The values that an octet-string parameter can take are variable-length or fixed-length sequences of octets, each octet being an ordered sequence of eight bits. The meaning and interpretation of a value is application-process specific.

The format codes of an octet-string parameter are

- PFC = 0: A variable-length octet string;

- PFC > 0: A fixed-length octet string with a number of octets equal to PFC.

A variable-length octet-string parameter is of the form:

| n | O1 | O2 | … | On |
| --- | --- | --- | --- | --- |
| Variable unsigned integer | octet | octet |  | octet |

where:

- O1 … On	are octets;

- n indicates the number of octets which follows.

A fixed-length octet-string parameter is of the form:

| O1 | O2 | … | On |
| --- | --- | --- | --- |
| octet | octet |  | octet |

where:

- O1 … On	are octets;

- n indicates the number of octets and is equal to PFC.

Character-String Parameter (PTC = 8)

The values that a character-string parameter can take are variable-length sequences of visible characters (visible characters are defined in Unicode). A visible character is represented by its UTF-8 code (reference [4]). The meaning and interpretation of a value is application-process specific.

A variable-length character-string parameter is of the form:

| Size | Character |
| --- | --- |
| Variable unsigned integer (PTC = 11, PFC = 2) | UTF-8 |
|  | Repeated for every character in the string |

- The field ‘Size’ is assigned with the number of octets required to encode the characters of the string.

Absolute Time Parameter (PTC = 9)

General

The value of an Absolute Time parameter field is a number of seconds and fractions of second from a given agency epoch. It is a positive time offset.

The format codes of an Absolute Time parameter are

- PFC = 0: Explicit definition of time format (CUC or CDS), i.e., including the P-field;

- PFC = 1: 2 octets day CDS format without a µsec field (parameter field is 6 octets);

- PFC = 2: 2 octets day CDS format with a µsec field (parameter field is 8 octets);

- 3 ≤ PFC ≤ 18: CUC format with ((PFC + 1)÷4, rounded down) octets of coarse time and ((PFC + 1)modulo 4) octets of fine time. PFC values in this range do not include the P-field (the value of the implicit P-field can be derived from the PFC).

NOTE	–	The CUC and CDS time formats are defined in reference [5].

CDS Format

The CDS format with µsec (PFC = 2) is as follows:

| Day | msec of day | µsec of msec |
| --- | --- | --- |
| 2 octets | 4 octets | 2 octets |

The value of Day is an unsigned integer in the range 0 to 216-1.

CUC Format

The CUC format consists of 1 to 4 octets of coarse time (seconds) and 0 to 3 octets of fine time (sub-seconds). The coarse time code elements are a count of the number of seconds elapsed from the epoch. Four octets of coarse time results in a maximum ambiguity period of approximately 136 years. This allows a time code representation of time through the year 2094 for those which are referenced to the TAI epoch of 1958 January 1.

Zero to three octets of fine time code elements result in a resolution of, respectively: 1 second; 2-8 second (about 4 msec); 2-16 second (about 15 µsec); or 2-24 second (about 60 nsec).

The full CUC format (PFC = 18) is as follows:

| C1 | C2 | C3 | C4 | F1 | F2 | F3 |
| --- | --- | --- | --- | --- | --- | --- |
| 1 octet | 1 octet | 1 octet | 1 octet | 1 octet | 1 octet | 1 octet |

The time in seconds from the given agency epoch is given by:

t = C1*2563+ C2*2562+ C3*256 + C4+ F1*256-1+ F2*256-2+ F3*256-3.

where:

- C1 … C4	are octets of coarse time, i.e., the number of seconds elapsed from the epoch;

- F1 … F3	are octets of fine time, i.e., the number of 2-24 seconds.

Relative Time Parameter (PTC = 10)

The value of a Relative Time parameter field is a number of seconds and fractions of a second from the occurrence time of an event whose identification can be derived from other parameters in the packet (e.g., identifying a type of onboard event) or a number of seconds and fractions of a second between two absolute times. It can be a positive or negative time offset.

The format codes of a Relative Time parameter are

- PFC = 0: Explicit definition of CUC time format, i.e., including the P-field;

- 1 ≤ PFC ≤ 16: CUC format with ((PFC + 3)÷4, rounded down) octets of coarse time and ((PFC + 3)modulo 4) octets of fine time. PFC values in this range do not include the P-field (the value of the implicit P-field can be derived from the PFC).

The full CUC format (PFC = 16) is as follows:

| C1 | C2 | C3 | C4 | F1 | F2 | F3 |
| --- | --- | --- | --- | --- | --- | --- |
| 1 octet | 1 octet | 1 octet | 1 octet | 1 octet | 1 octet | 1 octet |

The positive time offset is given by:

t = C1*2563+ C2*2562+ C3*256 + C4+ F1*256-1+ F2*256-2+ F3*256-3

where Ci and Fi are in the range 0 to 127.

NOTE	–	A negative time offset is expressed as the ‘2's complement’ of the corresponding positive time offset.

Variable Unsigned Integer Parameter (PTC = 11)

The format codes of a variable unsigned integer parameter are

- PFC = 1: 2 octets unsigned integer;

- PFC = 2: 4 octets unsigned integer;

- PFC = 3: 8 octets unsigned integer.

The ‘2's complement’ representation of the integer is divided in groups of 7 bits. The least significant group is encoded first. It is encoded in an octet as shown below:

| MSB | Least significant group of 7 bits |
| --- | --- |
| 1 bit | 7 bits |

The MSB indicates whether there are further octets to come or not:

- MSB = ‘0’: there are no further octets to come;

- MSB = ‘1’: there are further octets to come.

The other groups of 7 bits are encoded in the same way, the least significant group being encoded first.

Variable Signed Integer Parameter (PTC = 12)

The format codes of a variable signed integer parameter are

- PFC = 1: 2 octets signed integer;

- PFC = 2: 4 octets signed integer;

- PFC = 3: 8 octets signed integer.

Signed integers are mapped to unsigned integers in order that numbers with a small absolute value, for example -1, can be encoded as a small unsigned variable integer parameter.

The mapping is done by moving the sign bit from the left-most position to the right-most position.

Using bit shift operators, the mapping is done according to the PFC as defined in table B-1. The variable ‘n’ represents the integer.

Table B-1:  Variable Signed Integer Bit Shifting

| PFC | Bit Shifting |
| --- | --- |
| 1 | (n << 1) ^ (n >> 15) |
| 2 | (n << 1) ^ (n >> 31) |
| 3 | (n << 1) ^ (n >> 63) |

SECURITY, SANA, AND PATENT CONSIDERATIONS

(Informative)

SECURITY CONSIDERATIONS

Overview

This annex subsection discusses various aspects of security with respect to the MAL space packet binding protocol.

SECURITY BACKGROUND

The following security aspects are typically separated:

- data and data origin authentication: corroboration of the source of information that is contained in a message;

- authorization: conveyance, to another entity, of official sanction to do or be something;

- confidentiality: keeping information secret from all but those who are authorized to see it;

- integrity: detecting that information has not been altered by unauthorized or unknown means.

The MAL space packet binding protocol is not responsible for ensuring all these security aspects; however, it has to fulfill the security criteria expected by the MAL layer from every transport binding. These criteria are:

- the Transport Layer is responsible for the transmission of the authentication identifier assigned by the MAL layer to every consumer;

- the Transport Layer has to provide authentication, confidentiality, and integrity of the transmitted messages.

SECURITY CONCERNS

Authentication of the consumers is done above the MAL layer through a specific service that enables a consumer to get an authentication identifier. The meaning of that authentication identifier is dependent on the security system used for the deployment. This identifier must allow the MAL access control implementation to perform a lookup for authorization purposes.

The authentication identifier is conveyed by the space packet binding in the parameter ‘Authentication Identifier’ of the space packet user data field; however, this parameter may be omitted as it is optional.

Authorization is done by the MAL access control that performs any required authorization checks and converts the consumer identifier into technology dependent security credentials.

It is assumed that message authentication and confidentiality are provided beneath the Space Packet Protocol layer and are transparent to the space packet binding and above. As a consequence, once a message rises above the Space Packet Protocol layer, the message has been authenticated and all encryption has been removed.

Integrity is ensured by the protocol that conveys the space packets.

POTENTIAL THREATS AND ATTACK SCENARIOS

Potential threats and attack scenarios depend on the layer that is beneath the Space Packet Protocol because this is the layer that defines the security algorithms ensuring authentication, confidentiality and integrity.

CONSEQUENCES OF NOT APPLYING SECURITY

The only security aspect that may not be applied is the transmission of the authentication identifier in the space packet user data field. If the authentication identifier is not transmitted by the space packet binding, then delivered messages may be rejected by the MAL access control.

SANA CONSIDERATIONS

Version Number

The recommendations of this document request SANA to create the registry defined as follows:

- the registry named “MAL Space Packet Binding Version Number” consists of a table of parameters:

  - Version Number: a string of text specifying the four bits to be assigned to the space packet secondary header field ‘Version Number’;

  - Reference: a string of text referencing the CCSDS document that specifies the version of the MAL Space Packet Binding;

- the initial registry should be filled with the values in table [MAL Space Packet Binding Version Number initial values].

- the registration rule for new values of this registry may require an engineering review, and the request must come from the official representative of a space agency, member of the CCSDS.

Table 7-3:  MAL Space Packet Binding Version Number initial values

| Version Number | Reference |
| --- | --- |
| 0000 | 524x1b1 |

URI Scheme name

The recommendations of this document request SANA to create the registry defined as follows:

- the registry named “MAL Binding URI Scheme Name” consists of a table of parameters:

  - Scheme Name: a string of text specifying the name of the URI scheme defined by the MAL binding;

  - Reference: a string of text referencing the CCSDS document that specifies the MAL binding;

- the initial registry should be filled with the values in table [MAL Binding URI Scheme Name initial values].

- the registration rule for new values of this registry may require an engineering review, and the request must come from the official representative of a space agency, member of the CCSDS.

Table 7-3:  MAL Binding URI Scheme Name initial values

| Scheme Name | Reference |
| --- | --- |
| malspp | 524x1b1 |

PATENT CONSIDERATIONS

No patents are known to apply to this Recommended Standard.

acronyms

(informative)

APID	Application Process Identifier

BNF	Backus-Naur Form

IP	Interaction Pattern

LSB	Least Significant Bit

MAL	Message Abstract/Abstraction Layer

MSB	Most Significant Bit (MSB)

PDU	Protocol Data Unit

PFC	Parameter Format Code

PTC	Parameter Type Code

QoS	Quality of Service

SANA	Space Assigned Numbers Authority

SDU	Service Data Unit

SM&C	CCSDS Spacecraft Monitoring and Control

SP	Space Packet

SPP	Space Packet Protocol

TC	Telecommand

TM	Telemetry

URI	Universal Resource Identifier

informative References

(Informative)

[E1]	Mission Operations Services Concept.  Report Concerning Space Data System Standards, CCSDS 520.0-G-3.  Green Book.  Issue 3.  Washington, D.C.: CCSDS, December 2010.

[E2]	Information Technology—Open Systems Interconnection—Basic Reference Model: The Basic Model.  International Standard, ISO/IEC 7498-1:1994.  2nd ed.  Geneva:  ISO, 1994.

[E3]	Information Technology—Open Systems Interconnection—Basic Reference Model—Conventions for the Definition of OSI Services.  International Standard, ISO/IEC 10731:1994.  Geneva:  ISO, 1994.