Draft Recommendation for
Space Data System Standards

Mission Operations—Space Packet Binding

Draft Recommended Standard

CCSDS 524.1-R-1

Red Book

December 2014

AUTHORITY

|  | Issue: | Red Book, Issue 1 |  |
| --- | --- | --- | --- |
|  | Date: | December 2014 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-3), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This document is published and maintained by:

CCSDS Secretariat

Space Communications and Navigation Office, 7L70

Space Operations Mission Directorate

NASA Headquarters

Washington, DC 20546-0001, USA

STATEMENT OF INTENT

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF INTENT:)

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

o	Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

o	Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

o	Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible.  It is the responsibility of each member to determine when such standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

The intended use for this document is to allow the implementation of a protocol layer that binds the Mission Operations (MO) service framework to the Space Packet Protocol. This document assumes that the reader is familiar with the MO concepts, especially the Message Abstraction Layer (MAL).

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. CCSDS shall not be held responsible for identifying any or all such patent rights.

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-3).  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- CSIR Satellite Applications Centre (CSIR)/Republic of South Africa.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard.  Its ‘Red Book’ status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations.  As such, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

Recipients of this draft are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

# DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS 524.1-R-1 | Mission Operations—Space Packet Binding, Draft Recommended Standard, Issue 1 | December 2014 | Current draft |

# CONTENTS

Section	Page

1	Introduction	1-1

1.1	PURPOSE	1-1

1.2	SCOPE	1-1

1.3	APPLICABILITY	1-1

1.4	RATIONALE	1-2

1.5	Document structure	1-2

1.6	Definitions—Message Abstraction Layer Terms	1-2

1.7	NOMENCLATURE	1-2

1.8	Bit Numbering Convention	1-3

1.9	references	1-4

2	Overview	2-1

2.1	General	2-1

2.2	MO Service Framework Over Space Packet Protocol	2-2

2.3	Typical Use	2-5

2.4	MAL message mapping	2-7

2.5	MAL Transport Interface Mapping	2-11

3	MAL Message Mapping	3-1

3.1	Overview	3-1

3.2	URI Format	3-5

3.3	MAL Header Mapping	3-6

3.4	Space Packet specific Fields	3-11

3.5	MAL Message Body Mapping	3-13

4	MAL Transport Interface Mapping	4-1

4.1	Overview	4-1

4.2	SupportedQoS Request	4-3

4.3	SupportedIP Request	4-3

4.4	Transmit Request	4-3

4.5	TransmitMultiple Request	4-6

4.6	Receive indication	4-6

4.7	ReceiveMultiple indication	4-7

5	MAL Data Encoding	5-8

5.1	Overview	5-8

5.2	Element	5-9

5.3	Enumeration	5-10

5.4	Composite	5-10

5.5	List	5-11

5.6	Nullable Element	5-11

5.7	Blob	5-11

5.8	Boolean	5-12

5.9	Duration	5-12

5.10	Float	5-12

5.11	Double	5-12

5.12	Identifier	5-12

5.13	Octet	5-12

5.14	UOctet	5-13

5.15	Short	5-13

5.16	UShort	5-13

5.17	Integer	5-13

5.18	UInteger	5-13

5.19	Long	5-13

5.20	ULong	5-14

5.21	String	5-14

5.22	Time	5-14

5.23	FineTime	5-14

5.24	Uri	5-15

5.25	Unsigned N-bit Integer	5-15

5.26	Signed N-bit Integer	5-15

5.27	Unsigned Varint	5-15

5.28	Signed Varint	5-17

ANNEX A	Protocol Implementation Conformance 
Statement Proforma  (Normative)	A-1

ANNEX B	Mapping Configuration Parameters  (Normative)	B-1

ANNEX C	SECURITY, SANA, AND PATENT CONSIDERATIONS  (Informative)	C-1

ANNEX D	acronyms  (informative)	D-1

ANNEX E	informative References  (Informative)	E-1

Figure

1-1	Bit Numbering Convention	1-3

1-2	Octet Convention	1-3

2-1	Mission Operations Services Concept Document Set	2-2

2-2	Overview of the MO Service Framework	2-3

# CONTENTS (continued)

Figure	Page

2-3	MO Service Framework above Space Packet Protocol	2-5

2-4	Typical Deployment of the MAL Space Packet Binding	2-6

2-5	MAL Message Mapping to Space Packet	2-9

Table

3-1	MAL Message Header Fields	3-1

3-2	Space Packet Primary Header Format	3-2

3-3	Space Packet Secondary Header Format	3-4

3-4	QoSlevel Field Encoding	3-7

3-5	Session Field Encoding	3-8

3-6	Interaction Type and Stage Mapping	3-9

4-1	MAL Transport Interface Primitives	4-2

4-2	Packet Interface Primitives	4-2

5-1	Unsigned Integer 7-bit Groups	5-13

5-2	Signed Integer Bit Shifting	5-14

B-2	Mapping Configuration Parameters	B-1

C-1	MAL Space Packet Binding Version Number Initial Values	C-3

C-2	MAL Binding URI Scheme Name Initial Values	C-3

# Introduction

## PURPOSE

This Recommended Standard defines the binding between the Mission Operations (MO) Message Abstraction Layer (MAL) specified in reference [2] and the Space Packet Protocol specified in reference [1]. This binding allows MO Services to use the Space Packet Protocol as messaging technology in all situations where this may be required.

## SCOPE

The scope of this Recommended Standard is the specification of the binding in terms of technology mapping to the Space Packet Protocol of:

- MAL message;

- MAL Transport Interface.

The MAL Blue Book (reference [2]) specifies the MAL protocol in an abstract way, i.e., without defining the concrete protocol data units. The MAL Space Packet Binding specifies:

- a complete and unambiguous mapping of the MAL message to the Space Packet;

- a complete and unambiguous mapping of the MAL transport interface to the Space Packet Protocol interface;

- a complete and unambiguous mapping of the MAL data types to a binary encoding format.

This Recommended Standard does not specify:

- individual implementations or products;

- the implementation of entities or interfaces within real systems.

MO services defined in terms of MAL using the Space Packet Protocol binding as defined in this Recommended Standard are fully interoperable.

## APPLICABILITY

This Recommended Standard specifies a technology mapping that enables different implementations of the MO service framework (see 2.2) to interoperate through the Space Packet Protocol.

## RATIONALE

The goal of this Recommended Standard is to specify how to translate the abstract MAL message model in an unambiguous way into a concrete message exchange protocol, namely the Space Packet Protocol.

This Recommended Standard also aims at defining a generic encoding format for the MAL data types that can be re-used by a MAL binding to a messaging technology that is not the Space Packet Protocol.

## Document structure

This Recommended Standard is organized as follows:

- section 1 provides purpose, scope, applicability, and rationale, and lists definitions, conventions, and references used throughout this Recommended Standard;

- section 2 presents an overview of the MAL Space Packet Binding in relation with the MO service framework;

- section 3 specifies the mapping of the MAL message to the Space Packet;

- section 4 specifies the mapping of the MAL transport interface to the Space Packet Protocol interface;

- section 5 specifies a generic encoding format for the MAL data types.

## Definitions—Message Abstraction Layer Terms

service: A set of capabilities that a component provides to another component via an interface.

NOTE	–	A service is defined in terms of the set of operations that can be invoked and performed through the service interface. Service specifications define the capabilities, behaviour and external interfaces, but do not define the implementation. Service interface binding and discovery are not addressed in this document.

## NOMENCLATURE

### Normative Text

The following conventions apply for the normative specifications in this Recommended Standard:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification;

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

NOTE	–	These conventions do not imply constraints on diction in text that is clearly informative in nature.

### Informative Text

In the normative sections of this document, informative text is set off from the normative specifications either in notes or under one of the following subsection headings:

- Overview;

- Background;

- Rationale;

- Discussion.

## Bit Numbering Convention

In this document, the following convention is used to identify each bit in an N-bit field. The first bit in the field to be transmitted (i.e., the most left justified when drawing a figure) is defined to be ‘Bit 0’; the bit following is defined to be ‘Bit 1’, and so on up to ‘Bit N–1’. When the field is used to express a binary value (such as a counter), the Most Significant Bit (MSB) shall be the first transmitted bit of the field, i.e., ‘Bit 0’.

Figure 1-1: Bit Numbering Convention

In accordance with modern data communications practice, spacecraft data fields are often grouped into eight-bit ‘words’ which conform to the above convention. Throughout this Recommended Standard, the following nomenclature is used to describe this grouping:

Figure 1-2: Octet Convention

By CCSDS convention, all ‘spare’ or ‘unused’ bits shall be permanently set to value ‘zero’.

## references

The following publications contain provisions which, through reference in this text, constitute provisions of this document. At the time of publication, the editions indicated were valid. All publications are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the publications indicated below. The CCSDS Secretariat maintains a register of currently valid CCSDS publications.

[1]	Space Packet Protocol. Issue 1. Recommendation for Space Data System Standards (Blue Book), CCSDS 133.0-B-1. Washington, D.C.: CCSDS, September 2003.

[2]	Mission Operations Message Abstraction Layer. Issue 2. Recommendation for Space Data System Standards (Blue Book), CCSDS 521.0-B-2. Washington, D.C.: CCSDS, March 2013.

[3]	IEEE Standard for Floating-Point Arithmetic. 2nd ed. IEEE Std. 754-2008. New York: IEEE, 2008.

[4]	F. Yergeau. UTF-8, a Transformation Format of ISO 10646. STD 63. Reston, Virginia: ISOC, November 2003.

[5]	Time Code Formats. Issue 4. Recommendation for Space Data System Standards (Blue Book), CCSDS 301.0-B-4. Washington, D.C.: CCSDS, November 2010.

[6]	Data Elements and Interchange Formats—Information Interchange—Representation of Dates and Times. 3rd ed. International Standard, ISO 8601:2004. Geneva: ISO, 2004.

# Overview

## General

This Recommended Standard allows MO services defined in terms of the MAL to interoperate across an end-to-end communication link using a normative binding of the MAL abstractions to the Space Packet Protocol for exchanging messages. This is of particular interest for MO services that are deployed across the space-ground link, for instance when the MO service provider is located onboard a spacecraft and the consumer on the ground. The messages that provider and consumer exchange to implement the MO services are encoded in Space Packets and carried via the Space Packet Protocol, which acts as a Message Layer mapping. This can run directly over a space Data Link Layer or over a true Transport Layer such as TCP, UDP, or BP.

To achieve this, this Recommended Standard provides a technology mapping of the MAL transport interface, the MAL abstract message, and the MAL data types specification (reference [2]) to the Space Packet Protocol (reference [1]). This technology mapping requires the specification of a concrete encoding format that is compliant with the Space Packet Protocol.

The MAL Blue Book (reference [2]) defines an abstract transport interface as a set of request and indication primitives. A technology mapping specifies how these primitives are provided according to the messaging technology.

In particular, a technology mapping translates the MAL message model into one or several specific PDUs in compliance with the protocol used by the messaging technology. Moreover, a technology mapping casts the MAL data types into a specific encoding format.

Full interoperability of services is achieved only once a binding has been created to a specific messaging technology. Because all MO service specifications are defined in terms of MAL using a formal service description language, the technology mapping can be used, without modification, to bind the service specifications to the messaging technology.

The diagram shown in figure 2-1 presents the set of standards documentation in support of the Mission Operations Services Concept. This MO MAL Space Packet Binding book belongs to the technology mappings documentation.

Figure 2-1: Mission Operations Services Concept Document Set

## MO Service Framework Over Space Packet Protocol

The CCSDS Spacecraft Monitoring & Control (SM&C) working group has developed a concept for an MO service framework, which follows the principles of service-oriented architectures. The framework defines two important aspects: the first is a protocol for interaction between two separate entities; the second is a framework of common services providing functionality common to most uses of the service framework. An overview of this framework is presented in figure 2-2.

Figure 2-2: Overview of the MO Service Framework

This Recommended Standard defines how the MAL layer is mapped to the specific transport layer messaging technology called Space Packet Protocol. More specifically, it specifies:

- how the specific technology shall be used;

- how any transmission errors or issues shall be communicated to higher layers;

- how all underlying Data Link or Network Layer issues shall be handled;

- the physical representation of the MAL messages necessary to constitute the operation templates;

- the mapping of the message structure rules for that technology;

- the encoding of the MAL data types.

It does not specify:

- individual application services, implementations, or products;

- the implementation of entities or interfaces within real systems;

- the methods or technologies required to acquire data;

- the management activities required to schedule a service;

- the representation of any service-specific PDUs (this is derived from the encoding rules defined in this document in section 5).

The MAL Blue Book (reference [2]) groups all the interfaces to the Transport Layer in a single place called the MAL transport interface (subsection 3.7 of reference [2]). Thanks to this, only the MAL transport interface needs to be mapped to the Space Packet Protocol, without the need to map the entire MAL Blue Book.

Figure 2-3 expands the previous figure (figure 2-2) by presenting the MAL Space Packet Binding layer in the MO service framework stack and highlighting the various interfaces and their main primitives.

Figure 2-3 shows that the mapping of the MAL transport interface to the Space Packet Protocol layer requires the insertion of a layer in between. This layer is called the MAL Space Packet Binding. It is responsible for the translation of the abstract MAL message to the concrete Space Packet.

The protocol stack represented in figure 2-3 is conceptual. It can be implemented in various ways. For example, an onboard implementation of the stack may, for performance reasons, merge the MAL layer and the MAL Space Packet Binding layer into a single layer called ‘MAL over Space Packet Protocol’.

The names of the main interfaces used and implemented by each layer are given by figure 2-3. The main primitives are shown for each interface:

- the primitives for every operation provided by an MO service;

- the primitives for every interaction pattern provided by MAL;

- the primitives for transmitting and receiving a single MAL message or multiple MAL messages;

- the primitives for transmitting and receiving a Space Packet.

Figure 2-3: MO Service Framework above Space Packet Protocol

## Typical Use

Possible uses of the MAL SPP binding may be between MO entities operating over a space link, for example:

- ground and onboard applications interacting through a space link;

- onboard components identified with distinct Application Process Identifiers and interacting with each other;

- applications deployed in separate spacecraft and communicating through the Internet protocol.

A typical deployment is illustrated in figure 2-4. In this example, the MO service framework is only used by the end nodes: the ground end node (e.g., in a control centre) and the onboard end node (e.g., in a spacecraft). The intermediary nodes are not represented in this figure so both end nodes are shown as though directly connected through the space-to-ground link. In real deployments the ground end node would use SLE services to connect to an Earth Space Link Terminal that would provide these space link services.

The MO stack is shown on both sides with horizontal arrows representing the interaction from the consumer to the provider at each level of the MO stack:

- at the application level, the consumer invokes an operation of the provider;

- at the MO services level, an interaction pattern is initiated;

- at the MAL level, an abstract MAL message is sent;

- at the MAL Space Packet Binding level, the abstract MAL message is mapped to the Space Packet Protocol;

- at the Space Packet Protocol level, a Space Packet is transmitted.

The Consumer/Provider application, MO services, and MAL layers are abstract, and they exchange MO Application Layer service data across APIs. The first concrete PDU is produced at the MAL Space Packet Binding level as the result of the mapping of the MAL message to the Space Packet Protocol.

The lower protocol layers between the Space Packet Protocol and the space link are not represented.

Figure 2-4:  Typical Deployment of the MAL Space Packet Binding

## MAL message mapping

### Mapping to the Space Packet Protocol

Each field of the MAL message needs to map to a field of the Space Packet, either in the primary header, the secondary header or in the user data field:

- the Space Packet primary header is specified by the Space Packet Protocol (reference [1]);

- the Space Packet secondary header and the user data field are defined and constrained by reference [1] and specified by this Recommended Standard.

This Recommended Standard uses the Space Packet primary header field ‘APID’ as an identifier of the sending or receiving application process that can be located either on-board, or on the ground. In order to stay compliant with existing systems, the APID of a TC packet identifies the destination application, whereas the APID of a TM packet identifies the source application.

The mapping to the primary header field ‘Packet Type’ is left as a configuration matter for the missions. The value assigned to the ‘Packet Type’ does not result from the mapping of any field of the MAL message.

Figure 2-5 illustrates the mapping of the MAL message to the Space Packet. All MAL message fields are mapped to the Space Packet fields. Most of the MAL message fields are mapped according to a one-to-one equivalence. In this case the original MAL header field name is kept and the background colour is blue. However, the following fields require a more complex mapping:

- in a TC packet, the MAL header field ‘URI From’ is mapped to the secondary header fields ‘Secondary APID’, ‘Secondary APID Qualifier’ and ‘Source Id’; the background colour is yellow;

- in a TC packet, the MAL header field ‘URI To’ is mapped to the primary header field ‘Application Process Identifier’, and the secondary header field ‘Destination Id’; the background colour is yellow;

- in a TM packet, the MAL header field ‘URI From’ is mapped to the primary header field ‘Application Process Identifier’, and the secondary header field ‘Source Id’; the background colour is yellow;

- in a TM packet, the MAL header field ‘URI To’ is mapped to the secondary header fields ‘Secondary APID’, ‘Secondary APID Qualifier’ and ‘Destination Id’; the background colour is yellow;

- the MAL header fields ‘Interaction Type’ and ‘Interaction Stage’ are mapped to the secondary field ‘SDU Type’; the background colour is orange;

The secondary header fields ‘Source Id’ and ‘Destination Id’ can be left out according to the secondary header fields ‘Source Id Flag’ and ‘Destination Id Flag’.

Some MAL header fields are optional. Their presence in the secondary header is specified by the QoS properties defined in annex C. The optional fields are mapped to two fields in the secondary header: a presence flag that indicates whether the value is encoded in the secondary header or not, and a field that gives the value in case it is encoded. The background colour is green.

The MAL header fields shall not be NULL, especially the field ‘Transaction Id’, even in MAL messages whose interaction type is SEND.

Space Packet fields whose values do not result from the mapping of a MAL message field have a white background.

The secondary header field ‘Segment Counter’ is left out according to the primary header ‘Sequence Flags’. The field ‘Segment Counter’ is included if the Space Packet user data is segmented.

Finally, the MAL message body field and its equivalent Space Packet user data field have a grey background. If the MAL message body is oversized, then it is segmented into several contiguous Space Packets.

The generated Space Packets resulting from the mapping of a MAL message need to be delivered to the right MAL recipient application which is identified by the MAL header field ‘URI To’. Space Packets whose packet type is TC are delivered according to the primary header field ‘APID’ and the parameter ‘APID Qualifier’ passed to the ‘Packet request’ primitive. TM packets are delivered according to the secondary header fields ‘Secondary APID’ and ‘Secondary APID Qualifier’.

Both MAL and SPP protocol layers rely on an error control mechanism (i.e. a CRC field) that is outside the scope of this Recommended Standard.

The reasons why the MAL header fields are reordered when mapped to the Space Packet are given in section 3.1.

Figure 2-5:  MAL Message Mapping to Space Packet

### Mapping Configuration Parameters

This Recommended Standard defines parameters that allow to configure and optimize the MAL message mapping and the format of the Space Packet. Those parameters are called ‘mapping configuration parameters’ or ‘configuration parameters’. They are defined in annex B.

The configuration parameters are either mission specific or application process specific. They are managed parameters, defined by some out-of-band agreement.

Each mapping configuration parameter is specified using a MAL data type in order to be taken into account by the interacting peers as part of the deployment configuration.

### Mapping Specification

The MAL Space Packet Binding defines a generic encoding format for every MAL data type (see section 5). Therefore the MAL message can be encoded in a generic way.

A simple tabular notation is used to specify the format of the mapping result, i.e., the Space Packet primary header, secondary header, and user data field. This tabular notation is composed of three levels:

- the name of each field;

- the encoding format of each field, as defined in section 5; the length of the format is put in brackets, either in bits or octets; the length can be variable; if the value to encode is directly given in binary format, then the encoding format is called ‘Binary value’;

- the condition, or the number of times the field is encoded in, or the static value to be assigned to the field.

The variable length of a field can be caused by an encoding format that is statically defined for a given mission and APID, e.g., the time code formats. A variable length can also result from an encoding format whose length is inherently variable, like:

- List

- String

- Varint

The List and String formats contain a length field as specified respectively in 5.5 and 5.21.

The Varint format allows to encode an integer using a number of octets that depends on the integer value. Each encoded octet begins with a continuation bit (Bit ‘0’) allowing to know whether there are more octets to decode or not. The advantage is that the number of octets required to encode small integer values is reduced. The drawback is that big integer values require more octets to be encoded. Depending on its value, a 4-octet integer can be encoded with 1, 2, 3, 4, or 5 octets. The signed and unsigned Varint formats are specified in 5.27 and 5.28.

### Complete Mapping

The MAL message mapping completeness is ensured by the following conditions:

- every MAL data type is mapped;

- every MAL message field is mapped;

- every mandatory Space Packet field is assigned.

Moreover, the translation from a MAL message to its binary form is reversible. No information is lost in the translation from a MAL message to its binary form.

## MAL Transport Interface Mapping

The mapping of the MAL transport interface requires specifying the expected behaviour for each of the MAL transport primitives. Three types of behaviour are defined:

- a MAL transport request initiating a Space Packet Protocol request by sending a Space Packet, and returning a reply;

- a Space Packet Protocol indication initiating a MAL transport indication when receiving a Space Packet;

- a MAL transport request returning a reply without calling the Space Packet Protocol layer.

The MAL transport mapping is complete as all the primitives are mapped.

Moreover, the behaviour of each primitive is fully specified.

# MAL Message Mapping

## Overview

This section specifies how the MAL message header, body and QoS properties are mapped to the Space Packet.

Table 3-1 is taken from reference [2] and provides the full list of fields in the MAL message header.

Table 3-1:  MAL Message Header Fields

| Field | Type | Value |
| --- | --- | --- |
| URI From | URI | Message Source URI |
| Authentication Id | Blob | Source Authentication Identifier |
| URI To | URI | Message Destination URI |
| Timestamp | Time | Message generation timestamp |
| QoSlevel | QoSLevel | The QoS level of the message |
| Priority | UInteger | The QoS priority of the message |
| Domain | List<Identifier> | Domain of the message |
| Network Zone | Identifier | Network zone of the message |
| Session | SessionType | Type of session of the message |
| Session Name | Identifier | Name of the session of the message |
| Interaction Type | InteractionType | Interaction Pattern Type |
| Interaction Stage | UOctet | Interaction Pattern Stage |
| Transaction Id | Long | Unique to consumer |
| Service Area | UShort | Service Area Identifier |
| Service | UShort | Service Identifier |
| Operation | UShort | Service Operation Identifier |
| Area version | UOctet | Area version |
| Is Error Message | Boolean | ‘True’ if this is an error message; else ‘False’ |

The MAL message header is mapped to the Space Packet primary and secondary headers.

The primary header is specified by the Space Packet Protocol (reference [1]). Table 3-2 expands the primary header specification with the encoding format of each field, as defined in section 5, and the static values to be assigned to the fields that are constant.

Table 3-2: Space Packet Primary Header Format

| Packet Version Number | Packet Type | Secondary Header Flag | Application Process Identifier | Sequence Flags | Packet Sequence Count | Packet Data Length |
| --- | --- | --- | --- | --- | --- | --- |
| Binary value (3 bits) | Binary value (1 bit) | Binary value (1 bit) | Unsigned 11-bit integer (11 bits) | Binary value (2 bits) | Unsigned 14-bit integer (14 bits) | Unsigned 16-bit integer (16 bits) |
| Always equal to ‘000’ |  | Always equal to ‘1’ |  |  |  |  |

The Space Packet secondary header is defined for MAL purposes by selecting option b) of subsection 4.1.3.2.1.5 of reference [1], the Ancillary Data Field being comprised of the fields ‘Version Number’, ‘SDU Type’, ‘Service Area’, ‘Service’, ‘Operation’, ‘Area version’, ‘Is Error Message’, ‘QoSlevel’, ‘Session’, ‘Secondary APID’, ‘Secondary APID Qualifier’,  ‘Transaction Id’, ‘Source Id Flag’, ‘Destination Id Flag’, ‘Priority Flag’, ‘Timestamp Flag’, ’Network Zone Flag’, ‘Session Name Flag’, ‘Domain Flag’, ‘Authentication Id Flag’, ‘Source Id’, ‘Destination Id’, ‘Segment Counter’, ‘Priority’, ‘Timestamp’, ‘Network Zone’, ‘Session Name’, ‘Domain’, and ‘Authentication Id’.

The ordering of the secondary header fields is justified as follows:

- the field ‘Version Number’ needs to come first in the Ancillary Data Field because it identifies the secondary header and the user data field as defined by this Recommended Standard;

- the fields ‘SDU Type’, ‘Service Area’, ‘Service’, ‘Operation’, ‘Area Version’, and ‘Is Error Message’ identify the interaction that occurs between the source and destination peers, i.e., the interaction type, the current stage of the interaction, the service that is used, its version, and the operation that is invoked; this information should come first after the secondary header field ‘Version Number’;

- the fields ‘Secondary APID’, ‘Secondary APID Qualifier’ identify the interacting peers; this information should come after the fields that identify the interaction (see above);

- the fields ‘QoSlevel’ and ‘Session’ are inserted between the field ‘Is Error Message’ and the field ‘Secondary APID’ in order to reach an octet boundary (1 + 2 + 2 + 11 = 16 bits);

- the field ‘Transaction Id’ refines the previous information about the interaction and the peers identification: it identifies the current interaction occurrence;

- a flag is added to the secondary header for the optional source and destination identifiers, and for every MAL header field that is optional;

- the fields ‘Source Id’ and ‘Destination Id’ allow to refine the identity of the interacting peers in case there are several consumers or providers of the same service per APID and APID Qualifier;

- the field ‘Segment Counter’ is used in case the MAL message is segmented in several Space Packets;

- the field ‘Priority’ could be used as soon as the MAL message is delivered;

- the fields ‘Network Zone’, ‘Session Name’, ‘Domain’, and ‘Authentication Id’ are relegated to the back of the secondary header in order to enable not to decode them in case the packet decoding is allowed to be interrupted; for example, in an on-board environment, only the fixed-length fields could be decoded (from ‘Version’ to ‘Timestamp’); the variable-length fields (from ‘Network Zone’ to ‘Authentication Id’) and the MAL message body would be ignored;

- the field ‘Authentication Id’ is used by the MAL Access Control component; it is not part of the security protocol that may be used to transmit the Space Packets.

The format of the packet secondary header is shown in table 3-3.

Optional fields are specified out of band, with a mapping configuration parameter as defined by annex B.

Variable length fields are delineated as follows:

- the format ‘Varint’ is delineated by continuation bits as specified in 5.27;

- the formats ‘Blob’, ‘Identifier’ and ‘List’ contain a length field as specified respectively in 5.7, 5.12, and 5.5.

The QoS properties defined by annex C allow to set the values of secondary header flags which cannot be deduced from the MAL header fields.

The mapping of the MAL message is composed of the following specifications:

- the URI format to be applied to the MAL header fields ‘URI From’ and ‘URI To’;

- the mapping of the MAL header to the Space Packet;

- the values to be assigned to the fields of the Space Packet that are not the result of the MAL message header and body mapping;

- the mapping of the MAL message body to the Space Packet.

Table 3-3:  Space Packet Secondary Header Format

| Version Number | SDU Type | Service Area | Service | Operation | Area Version | Is Error Message | QoSlevel | Session | Secondary APID | Secondary APID Qualifier | Transaction Id | Source Id Flag | Desti-nation Id Flag | Priority Flag | Time-stamp Flag |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary value (3 bits) | Unsigned 5-bit Integer (5 bits) | Unsigned 16-bit Integer (16 bits) | Unsigned 16-bit Integer (16 bits) | Unsigned 16-bit Integer (16 bits) | Unsigned 8-bit Integer (8 bits) | Binary value (1 bit) | Unsigned 2-bit Integer (2 bits) | Unsigned 2-bit Integer (2 bits) | Unsigned 11-bit Integer (11 bits) | Unsigned 16-bit Integer (16 bits) | Signed 64-bit Integer (64 bits) | Binary value (1 bit) | Binary value (1 bit) | Binary value (1 bit) | Binary value (1 bit) |

| Network Zone Flag | Session Name Flag | Domain Flag | Authen-tication Id Flag | Source Id | Destination Id | Segment Counter | Priority | Timestamp | Network Zone | Session Name | Domain | Authentication Id |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Binary value (1 bit) | Binary value (1 bit) | Binary value (1 bit) | Binary value (1 bit) | Unsigned 8-bit Integer (8 bits) | Unsigned 8-bit Integer (8 bits) | Unsigned 32-bit Integer (32 bits) | UInteger (see 5.18) (var., mult. of octet) | Time (see 5.22) (var., mult. of octet) | Identifier (see 5.12) (var., mult. of octet) | Identifier (see 5.12) (var., mult. of octet) | List<Identifier> (see 5.5) (var., mult. of octet) | Blob (see 5.7) (var., mult. of octet) |
|  |  |  |  | If ‘Source Id Flag’ is ‘1’ | If ‘Destination Id Flag’ is ‘1’ | If ‘Sequence Flags’ is either ‘00’, ’01, or ‘10’ | If ‘Priority Flag’ is ‘1’ | If ‘Timestamp Flag’ is ‘1’ | If ‘Network Flag’ is ‘1’ | If ‘Session Flag’ is ‘1’ | If ‘Domain Flag’ is ‘1’ | If ‘Authentication Id Flag’ is ‘1’ |

## URI Format

The format of the MAL header fields ‘URI From’ and ‘URI To’ shall comply with the following rules:

- the URI scheme name shall be ‘malspp’;

- the scheme name shall be followed by a colon separator ‘:’ and a rootless path, i.e., a path that does not begin with a slash ‘/’;

- the path shall begin with the APID qualifier, an integer represented in decimal;

- the APID qualifier shall be a positive integer, including zero, strictly less than 216;

- the APID qualifier shall be followed by a slash separator ‘/’ and the APID, an integer represented in decimal;

- the APID shall be a positive integer, including zero, strictly less than 2047; the APID shall be compliant with the APID values listed in the SANA registry called ‘Space Packet Protocol Application Process Identifier (APID)’;

NOTE	–	The APID value of 2047, indicating the Idle Packet, is not allowed because it cannot be used to map a MAL message.

- the APID may be followed by a slash separator ‘/’ and an integer represented in decimal which is called the ‘Source Id’ for the field ‘URI From’ and the ‘Destination Id’ for the field ‘URI To’;

- the source or destination identifier shall be a positive integer, including zero, strictly less than 256.

NOTES

- The range of the APID qualifier (16 bits) should be long enough for most use cases. According to reference [1], if Space Packets are transferred over a space-to-ground or space-to-space communications link with one of the Space Data Link Protocols (references [E2]-[E3]), the APID qualifier is assigned with the Master Channel Identifier (MCID) which is the concatenation of the Transfer Frame Version Number (TFVN, 2 bits) and the Spacecraft Identifier (SCID, 10 bits).

- The source or destination identifier is optional.

- An example of URI is ‘malspp:417/0/2’. This URI references the source or destination ‘2’ provided by the APID ‘0’ for the APID qualifier ‘417’.

The APID and APID qualifier shall uniquely identify a MAL application.

The source or destination identifier shall be unique for a given MAL application identified by its APID and APID qualifier.

NOTE	–	The APID and APID qualifier may designate several sources and destinations identified by their own source and destination identifiers.

The scheme name ‘malspp’ shall be added to the SANA registry ‘MAL Binding URI Scheme Name’ and shall refer to the MAL Space Packet Binding document ‘CCSDS 524.1-B-1’.

NOTE	–	This SANA registry is defined in C2.2.

## MAL Header Mapping

### Overview

The following subsections provide the mapping of each field of the MAL message header to the Space Packet.

The mapping configuration parameters are defined in annex B.

### URI From

If the MAL message is mapped to a TC packet, then the APID of the MAL header field ‘URI From’ shall be assigned to the secondary header field ‘Secondary APID’.

If the MAL message is mapped to a TC packet, then the APID qualifier of the MAL header field ‘URI From’ shall be assigned to the secondary header field ‘Secondary APID Qualifier’.

If the MAL message is mapped to a TM packet, then the APID of the MAL header field ‘URI From’ shall be assigned to the primary header field ‘Application Process Identifier’.

### If the MAL header field ‘URI From’ contains a Source Id, then this identifier shall be assigned to the secondary header field ‘Source Id’ and the secondary header field ‘Source Id Flag’ shall be set to the value ‘1’.

### If the MAL header field ‘URI From’ does not contain a Source Id, then the secondary header field ‘Source Id Flag’ shall be set to the value ‘0’ and the secondary header field ‘Source Id’ shall be left out.

### Authentication Id

If the QoS property AUTHENTICATION_ID_FLAG is TRUE, or not passed with the MAL message, then the MAL header field ‘Authentication Id’ shall be assigned to the secondary header field ‘Authentication Id’ and the ‘Authentication Id Flag’ shall be set to the value ‘1’.

If the QoS property AUTHENTICATION_ID_FLAG is FALSE, then the following rules shall be applied:

- the secondary header field ‘Authentication Id Flag’ shall be set to the value ‘0’ and the secondary header field ‘Authentication Id’ shall be left out;

- if the mapping configuration parameter AUTHENTICATION_ID is defined, then its value shall be assigned to the MAL header field ‘Authentication Id’;

- if the mapping configuration parameter AUTHENTICATION_ID is not defined, then an empty MAL::Blob shall be assigned to the MAL header field ‘Authentication Id’.

### URI To

If the MAL message is mapped to a TC packet, then the APID of the MAL header field ‘URI To’ shall be assigned to the primary header field ‘Application Process Identifier’.

If the MAL message is mapped to a TM packet, then the APID of the MAL header field ‘URI To’ shall be assigned to the secondary header field ‘Secondary APID’.

If the MAL message is mapped to a TM packet, then the APID qualifier of the MAL header field ‘URI To’ shall be assigned to the secondary header field ‘Secondary APID Qualifier’.

If the MAL header field ‘URI To’ contains a Destination Id, then this identifier shall be assigned to the secondary header field ‘Destination Id’ and the secondary header field ‘Destination Id Flag’ shall be set to the value ‘1’.

If the MAL header field ‘URI To’ does not contain a Destination Id, then the secondary header field ‘Destination Id Flag’ shall be set to the value ‘0’ and the secondary header field ‘Destination Id’ shall be left out.

### Timestamp

If the QoS property TIMESTAMP_FLAG is TRUE, or not passed with the MAL message, then the MAL header field ‘Timestamp’ shall be assigned to the secondary header field ‘Timestamp’ and the ‘Timestamp Flag’ shall be set to the value ‘1’.

If the QoS property TIMESTAMP_FLAG is FALSE, then the following rules shall be applied:

- the secondary header field ‘Timestamp Flag’ shall be set to the value ‘0’ and the secondary header field ‘Timestamp’ shall be left out;

- the value ‘0’ shall be assigned to the MAL header field ‘Timestamp’.

### QoSlevel

The value of the MAL header field ‘QoSlevel’ shall be assigned to the secondary header field ‘QoSlevel’ as specified by table 3-4.

Table 3-4: QoSlevel Field Encoding

| QoSlevel value | Encoded Value |
| --- | --- |
| BESTEFFORT | 0 |
| ASSURED | 1 |
| QUEUED | 2 |
| TIMELY | 3 |

### Priority

If the QoS property PRIORITY_FLAG is TRUE, or not passed with the MAL message, then the MAL header field ‘Priority’ shall be assigned to the secondary header field ‘Priority’ and the ‘Priority Flag’ shall be set to the value ‘1’.

If the QoS property PRIORITY_FLAG is FALSE, then the following rules shall be applied:

- the secondary header field ‘Priority Flag’ shall be set to the value ‘0’ and the secondary header field ‘Priority’ shall be left out;

- if the mapping configuration parameter PRIORITY is defined, then its value shall be assigned to the MAL header field ‘Priority’;

- if the mapping configuration parameter PRIORITY is not defined, then the value ‘0’ shall be assigned to the MAL header field ‘Priority’.

### Domain

If the QoS property DOMAIN_FLAG is TRUE, or not passed with the MAL message, then the MAL header field ‘Domain’ shall be assigned to the secondary header field ‘Domain’ and the ‘Domain Flag’ shall be set to the value ‘1’.

If the QoS property DOMAIN_FLAG is FALSE, then the following rules shall be applied:

- the secondary header field ‘Domain Flag’ shall be set to the value ‘0’ and the secondary header field ‘Domain’ shall be left out;

- if the mapping configuration parameter DOMAIN is defined, then its value shall be assigned to the MAL header field ‘Domain’;

- if the mapping configuration parameter DOMAIN is not defined, then an empty List<MAL::Identifier> shall be assigned to the MAL header field ‘Domain’.

### Network Zone

If the QoS property NETWORK_ZONE_FLAG is TRUE, or not passed with the MAL message, then the MAL header field ‘Network Zone’ shall be assigned to the secondary header field ‘Network Zone’ and the ‘Network Flag’ shall be set to the value ‘1’.

If the QoS property NETWORK_ZONE_FLAG is FALSE, then the following rules shall be applied:

- the secondary header field ‘Network Zone Flag’ shall be set to the value ‘0’ and the secondary header field ‘Network Zone’ shall be left out;

- if the mapping configuration parameter NETWORK_ZONE is defined, then its value shall be assigned to the MAL header field ‘Network Zone’;

- if the mapping configuration parameter NETWORK_ZONE is not defined, then an empty MAL::Identifier shall be assigned to the MAL header field ‘Network Zone’.

### Session

The value of the MAL header field ‘Session’ shall be assigned to the secondary header field ‘Session’ as specified by table 3-5.

Table 3-5: Session Field Encoding

| Session value | Encoded Value |
| --- | --- |
| LIVE | 0 |
| SIMULATION | 1 |
| REPLAY | 2 |

### Session Name

If the QoS property SESSION_NAME_FLAG is TRUE, or not passed with the MAL message, then the MAL header field ‘Session Name’ shall be assigned to the secondary header field ‘Session Name’ and the ‘Session Flag’ shall be set to the value ‘1’.

If the QoS property SESSION_NAME_FLAG is FALSE, then the following rules shall be applied:

- the secondary header field ‘Session Name Flag’ shall be set to the value ‘0’ and the secondary header field ‘Session Name’ shall be left out;

- if the mapping configuration parameter SESSION_NAME is defined, then its value shall be assigned to the MAL header field ‘Session Name’;

- if the mapping configuration parameter SESSION_NAME is not defined, then an empty MAL::Identifier shall be assigned to the MAL header field ‘Session Name’.

### Interaction Type and stage

- The MAL header fields ‘Interaction Type’ and ‘Interaction Stage’ shall be mapped to the secondary header field ‘SDU Type’ as defined by table 3-6, where the SDU type used to map an interaction stage raising an error shall be the same as the SDU type used by this interaction stage without an error.

Table 3-6: Interaction Type and Stage Mapping

| Interaction Type | Interaction Stage | SDU Type (decimal) |
| --- | --- | --- |
| SEND | SEND | 0 |
| SUBMIT | SUBMIT ACK ERROR | 1 2 2 |
| REQUEST | REQUEST RESPONSE ERROR | 3 4 4 |
| INVOKE | INVOKE ACK ACK_ERROR RESPONSE RESPONSE ERROR | 5 6 6 7 7 |
| PROGRESS | PROGRESS ACK ACK_ERROR UPDATE UPDATE_ERROR RESPONSE RESPONSE ERROR | 8 9 9 10 10 11 11 |
| PUBLISH-SUBSCRIBE | REGISTER REGISTER_ACK REGISTER_ERROR PUBLISH_REGISTER PUBLISH_REGISTER_ACK PUBLISH_REGISTER_ERROR PUBLISH PUBLISH_ERROR NOTIFY NOTIFY ERROR DEREGISTER DEREGISTER ACK PUBLISH_DEREGISTER PUBLISH_DEREGISTER_ACK | 12 13 13 14 15 15 16 16 17 17 18 19 20 21 |

### Transaction Id

The value of the MAL header field ‘Transaction Id’ shall be assigned to the secondary header field ‘Transaction Id’.

### Service Area

The value of the MAL header field ‘Service Area’ shall be assigned to the secondary header field ‘Service Area’.

### Service

The value of the MAL header field ‘Service’ shall be assigned to the secondary header field ‘Service’.

### Operation

The value of the MAL header field ‘Operation’ shall be assigned to the secondary header field ‘Operation’.

### Area Version

The value of the MAL header field ‘Area Version’ shall be assigned to the secondary header field ‘Area Version’.

### Is Error Message

If the MAL header field ‘Is Error Message’ is TRUE, then the secondary header field ‘Is Error Message’ shall be assigned with the value ‘1’, otherwise it shall be assigned with the value ‘0’.

## Space Packet specific Fields

### Overview

The following subsections specify the values to be assigned to the Space Packet fields that are not the result of the MAL header mapping.

NOTE	–	The Space Packet Protocol layer expects from the upper layer a fully formed Space Packet, as specified by subsection 3.3.3.2.2 of reference [1].

### Space Packet Primary Header

#### Overview

The following subsections provide the values to be assigned to the primary header fields that are not the result of the MAL header mapping. The Space Packet header is shown in table 3-2.

#### Packet Version Number

The field ‘Packet Version Number’ shall be assigned with the binary value ‘000’ as specified by reference [1] and declared in the SANA registry ‘Packet Version Number’.

NOTE	–	Only Version 1 CCSDS Packet is supported.

Packet Type

The field ‘Packet Type’ shall be assigned according to some out-of-band agreement done for a given mission.

#### Secondary Header Flag

The field ‘Secondary Header Flag’ shall be assigned with the binary value ‘1’.

NOTE	–	The field ‘Secondary Header Flag’ indicates presence of packet secondary header.

#### Sequence Flags

The field ‘Sequence Flags’ shall be assigned according to the size of the octet stream that results from the MAL message body encoding (see section 4.4).

#### Packet Sequence Count

The field ‘Packet Sequence Count’ shall be assigned with the sequential binary count of each Space Packet generated for every APID and APID qualifier.

#### Packet Data Length

The field ‘Packet Data Length’ shall be assigned with the total number of octets in the Packet Data Field minus 1.

### Space Packet Secondary Header

#### Overview

The following subsections provide the values to be assigned to the secondary header fields that are not the result of the MAL header mapping.

#### Version Number

The field ‘Version Number’ shall identify the secondary header and the user data field as defined by this Recommended Standard.

The field ‘Version Number’ shall be assigned with the binary value ‘000’.

The version number ‘000’ shall be added to the SANA registry ‘MAL Space Packet Binding Version Number’ and shall refer to the MAL Space Packet Binding document ‘CCSDS 524.1-B-1’.

NOTE	–	This SANA registry is defined in C2.1C-2.

Segment Counter

The field ‘Segment Counter’ shall enable to order a sequence of Space Packets resulting from the segmentation of a MAL message, as specified in sections 4.4 and 4.6.

## MAL Message Body Mapping

### Overview

The following subsections specify how the MAL message body is mapped to the Space Packet.

### Body mapping

The MAL message body shall be encoded as a Body (see 3.5.3.2) and assigned to the Space Packet user data field.

### Body Encoding

#### Overview

This subsection specifies how the MAL message body is encoded.

The encoding formats are defined in this subsection.  The encoding formats for data are in section 5.

NOTE	–	The body encoding format can be re-used by a MAL binding to a messaging technology that is not the Space Packet Protocol.

#### Body

Each element of the MAL message body shall be encoded as a Body Element in the same order as it is declared in the operation definition.

If the body declared by the operation is empty, then the encoding result shall be empty.

#### Body Element

If the MAL header fields ‘Interaction Type’ and ‘Interaction stage’ are respectively equal to PUBLISH-SUBSCRIBE and PUBLISH, and if the body element is typed ‘List< <<Update Value Type>> >’ (reference [2]), then the body element shall be encoded as follows:

| Area | Service | Area Version | Type | Body Element |
| --- | --- | --- | --- | --- |
| Unsigned 16-bit Integer (2 octets) | Unsigned 16-bit Integer (2 octets) | Unsigned 8-bit Integer (1 octet) | Signed 24-bit Integer (3 octets) | Publish Update List (variable, multiple of octet) |
| If <<Update Value Type>> is abstract |  |

The field ‘Area’ shall be assigned with the area number of the update list actual type encoded as an Unsigned 16-bit Integer.

If the update list actual type is defined by a service, then the field ‘Service’ shall be assigned with the service number of the update list actual type encoded as an Unsigned 16-bit Integer.

If the update list actual type is not defined by a service, then the field ‘Service’ shall be assigned with the value ‘0’ encoded as an Unsigned 16-bit Integer.

The field ‘Area Version’ shall be assigned with the area version of the update list actual type encoded as an Unsigned 8-bit Integer.

The field ‘Type’ shall be assigned with the short form part of the update list actual type encoded as a Signed 24-bit Integer.

If the MAL header fields ‘Interaction Type’ and ‘Interaction stage’ are respectively equal to PUBLISH-SUBSCRIBE and PUBLISH, and if the body element is typed ‘List<UpdateHeader>’, then the body element shall be encoded as an Element (see section 5).

If the MAL header fields ‘Interaction Type’ and ‘Interaction stage’ are respectively equal to PUBLISH-SUBSCRIBE and NOTIFY, and if the body element is typed ‘List< <<Update Value Type>> >’ (reference [2]), then the body element shall be encoded as an Element (see section 5).

If the MAL header fields ‘Interaction Type’ and ‘Interaction stage’ are respectively equal to PUBLISH-SUBSCRIBE and NOTIFY, and if the body element is typed either Identifier or ‘List<UpdateHeader>’, then the body element shall be encoded as an Element (see section 5).

If the MAL header field ‘Interaction Type’ is PUBLISH-SUBSCRIBE and if the ‘Interaction stage’ is neither PUBLISH or NOTIFY and if the MAL header field ‘Is Error Message’ is FALSE, then each body element shall be encoded as an Element (see section 5).

If the MAL header field ‘Is Error Message’ is TRUE, then the body elements shall be encoded as follows:

- the first body element (typed ‘UInteger’) shall be encoded as a UInteger (see 5.18);

- the second body element (typed ‘Element’) shall be encoded as a Nullable Element (see section 5).

If the MAL header field ‘Interaction Type’ is not PUBLISH-SUBSCRIBE and if the MAL header field ‘Is Error Message’ is FALSE, then each body element shall be encoded as a Nullable Element (see section 5).

#### Publish Update List

A Publish Update List shall be encoded as follows:

| List Length | Update |
| --- | --- |
| UInteger (variable, multiple of octet) | Publish Update (variable, multiple of octet) |
|  | Repeated for every update in the list |

The field ‘List Length’ shall be assigned with the length of the list encoded as a UInteger (see 5.18).

NOTE	–	The type List is required to be unbounded by MAL (reference [2]). Using a UInteger as length field limits the list length to 232 − 1 elements.

The updates shall be encoded in the same order as in the list.

#### Publish Update

The following fields shall be encoded:

| Presence Flag | Encoded Update Size | Update |
| --- | --- | --- |
| Boolean (see 5.8) (1 octet) | UInteger (variable, multiple of octet) | Element (see 5.2) (variable, multiple of octet) |
|  | If Presence Flag is TRUE |

The field ‘Presence Flag’ shall be FALSE if the element is NULL; it shall be TRUE if the element is not NULL.

The field ‘Encoded Update Size’ shall be assigned with the number of octets used to encode the following field ‘Update’.

The field ‘Encoded Update Size’ shall be encoded as a UInteger (see 5.18).

NOTES

- Using a UInteger as size field limits the size of the encoded update to 232 − 1 octets.

- The Publish Update encoding format enables a MAL broker not to decode the updates when handling a publish message.

# MAL Transport Interface Mapping

## Overview

The MAL specification (reference [2]) ‘Transport Interface’ section defines the interface to be provided by the Space Packet Binding layer. The following subsections specify the expected behaviour for each of the MAL transport interface request and indication primitives. If an indication is a response to a request then the behaviour of the indication is specified in the same subsection as the request.

The following primitives are defined in the MAL transport interface and need to be provided by the Space Packet Binding layer:

- SUPPORTEDQOS request;

- SUPPORTEDQOS RESPONSE indication;

- SUPPORTEDIP request;

- SUPPORTEDIP RESPONSE indication;

- TRANSMIT request;

- TRANSMIT ACK indication;

- TRANSMIT ERROR indication;

- TRANSMITMULTIPLE request;

- TRANSMITMULTIPLE ACK indication;

- TRANSMITMULTIPLE ERROR indication;

- RECEIVE indication;

- RECEIVEMULTIPLE indication.

The parameters are listed in table 4-1.

The following primitives defined by the Space Packet Protocol (reference [1]) are used by the mapping:

- ‘Packet request’;

- ‘Packet indication’.

The parameters are listed in table 4-2.

Table 4-1: MAL Transport Interface Primitives

| Primitive | Parameters |
| --- | --- |
| SUPPORTEDQOS request | QoS Level |
| SUPPORTEDQOS RESPONSE indication | Boolean |
| SUPPORTEDIP request | Interaction Type |
| SUPPORTEDIP RESPONSE indication | Boolean |
| TRANSMIT request | MAL Message QoS Properties |
| TRANSMIT ACK indication | - |
| TRANSMIT ERROR indication | MAL Message Header Error Number Extra Information QoS Properties |
| TRANSMITMULTIPLE request | List of: MAL Message QoS Properties |
| TRANSMITMULTIPLE ACK indication | - |
| TRANSMITMULTIPLE ERROR indication | List of: MAL Message Header Error Number Extra Information QoS Properties |
| RECEIVE indication | MAL Message QoS Properties |
| RECEIVEMULTIPLE indication | List of: MAL Message QoS Properties |

Table 4-2: Packet Interface Primitives

| Primitive | Parameters |
| --- | --- |
| Packet request | Space Packet Application Process Identifier (APID) APID Qualifier (optional) QoS Requirement (optional) |
| Packet indication | Space Packet APID APID Qualifier (optional) |

## SupportedQoS Request

The SUPPORTEDQOS request primitive shall be provided.

Support for the Quality of Service (QoS) levels defined by MAL shall depend on the capabilities of the underlying layer used to convey the Space Packets.

## SupportedIP Request

The SUPPORTEDIP request primitive shall be provided.

The SUPPORTEDIP request primitive shall return TRUE for the interaction patterns SEND, SUBMIT, REQUEST, INVOKE, and PROGRESS.

The SUPPORTEDIP request primitive shall return FALSE for the interaction pattern PUBLISH-SUBSCRIBE.

NOTE	–	The MAL specification (reference [2]) requires that implementations of the MAL layer support the Publish-Subscribe pattern but that they can delegate this pattern to a transport that supports the pattern natively. The Space Packet Protocol does not support the Publish-Subscribe pattern natively; therefore a MAL implementation has to support this pattern itself.

## Transmit Request

The TRANSMIT request primitive shall be provided in order to translate a MAL message into one or several Space Packets and send each packet by calling the primitive ‘Packet request’.

If any of the MAL header fields is NULL, then the TRANSMIT ERROR primitive shall be called with the error number MAL::INTERNAL.

NOTE	–	The MAL header field ‘Transaction Id’ shall not be NULL, especially in MAL messages whose interaction type is SEND.

The MAL message header fields and body elements shall be mapped to the Space Packet according to the specification given in section 3 of this Recommended Standard.

If either of the fields ‘URI From’ or ‘URI To’ is not compliant with the URI format defined in 3.2, then the TRANSMIT ERROR primitive shall be called with the error number MAL::INTERNAL.

If the MAL message is mapped to a TC packet, then the following rules shall be applied:

- the APID of the MAL header field ‘URI To’ shall be passed to the ‘Packet request’ primitive;

- the APID qualifier of the MAL header field ‘URI To’ shall be passed to the ‘Packet request’ primitive;

- the Space Packets that result from the mapping of the MAL message shall be delivered to the MAL application identified by the APID and APID qualifier of the MAL header field ‘URI To’; the APID and APID qualifier are passed as parameters of the ‘Packet request’ primitive.

If the MAL message is mapped to a TM packet, then the following rules shall be applied:

- the APID of the MAL header field ‘URI From’ shall be passed to the ‘Packet request’ primitive;

- the APID qualifier of the MAL header field ‘URI From’ shall be passed to the ‘Packet request’ primitive;

- the Space Packets that result from the mapping of the MAL message shall be delivered to the MAL application identified by the APID and APID qualifier of the MAL header field ‘URI To’; the APID and APID qualifier are passed in the secondary header fields ‘Secondary APID’ and ‘Secondary APID Qualifier’.

NOTE	–	The APID qualifier is not an optional parameter in the call to the ‘Packet request’ primitive.

The QoS properties from the TRANSMIT request shall be passed to the ‘Packet request’ primitive.

If the size of the octet stream that results from the MAL message body encoding (see 3.5.3.2) added to the size of the secondary header is less or equal than the value of the mapping configuration parameter PACKET_DATA_FIELD_SIZE_LIMIT, then the following rules shall be applied:

- the octet stream shall be sent in the user data field of one Space Packet;

- the field ‘Sequence Flags’ of the Space Packet shall be assigned with the binary value ‘11’, unsegmented user data.

If the size of the octet stream that results from the MAL message body encoding (see 3.5.3.2) added to the size of the secondary header is strictly greater than the value of the mapping configuration parameter PACKET_DATA_FIELD_SIZE_LIMIT, then the following rules shall be applied:

- the octet stream shall be split in several user data segments whose size added to the size of the secondary header is equal to PACKET_DATA_FIELD_SIZE_LIMIT or less for the last segment;

- the user data segments shall be sent in a sequence of Space Packets;

- the MAL message header shall be mapped to the primary and secondary headers of every Space Packet of the sequence;

- a segment counter starting from zero shall be incremented for each user data segment and assigned to the secondary header field ‘Segment Counter’;

- every message whose MAL header fields ‘Interaction type’, ‘Transaction Id’, ‘URI From’, ‘URI To’, ‘Session’, ‘Session Name’, ‘Domain’, ‘Network Zone’, ‘Service Area’, ‘Service’, and ‘Operation’ are the same shall use the same segment counter, without resetting the counter to zero after a MAL message has been segmented;

- the field ‘Sequence Flags’ in the first Space Packet of the sequence shall be assigned with the binary value ‘01’, first segment of user data;

- the field ‘Sequence Flags’ in the last Space Packet of the sequence shall be assigned with the binary value ‘10’, last segment of user data;

- the field ‘Sequence Flags’ in the other Space Packets of the sequence shall be assigned with the binary value ‘00’, continuation segment of user data.

NOTE	–	This Recommended Standard does not specify any packet retransmission protocol in case some packets are lost. Packet transmission reliability should be ensured by the protocol layer below the Space Packet Protocol.

If the size of the secondary header is not strictly less than the value of the mapping configuration parameter PACKET_DATA_FIELD_SIZE_LIMIT, then the TRANSMIT ERROR primitive shall be called with the error number MAL::INTERNAL.

If an error is returned by the Space Packet sending request, then the TRANSMIT ERROR primitive shall be called with the error number MAL::INTERNAL.

If the packet is successfully sent, then the TRANSMIT ACK primitive shall be called.

## TransmitMultiple Request

The TRANSMITMULTIPLE request primitive shall be provided by calling the TRANSMIT request primitive for every MAL message.

If the TRANSMIT ERROR indication is called for any of the MAL messages, the TRANSMIT ERROR indications should be collected and the TRANSMITMULTIPLE ERROR indication should be called with the content of the collected TRANSMIT ERROR indications. The individual TRANSMIT ERROR indications shall not be transmitted to MAL. Only the TRANSMITMULTIPLE ERROR indication shall be called.

## Receive indication

The RECEIVE indication primitive shall be provided in order to receive one or several Space Packets and translate the packets into a MAL message.

The RECEIVE indication primitive shall be called after the primitive ‘Packet indication’ has been triggered one or several times (in case of MAL message segmentation) by the Space Packet Protocol layer.

The primitive ‘Packet indication’ shall provide the parameter ‘APID qualifier’.

If the field ‘Sequence Flags’ of the delivered Space Packet is equal to the binary value ‘11’, unsegmented user data, then the MAL message header fields and body elements shall be generated according to the specifications given in section 3 of this Recommended Standard, by using the following input data:

- the Space Packet;

- the parameter ‘APID qualifier’ of the primitive ‘Packet indication’;

- the XML specification of the MO service (see section 6 of reference [2]) identified by the MAL header fields ‘Service Area’, ‘Service’, and ‘Area Version’.

If the field ‘Sequence Flags’ of the delivered Space Packet is not equal to the binary value ‘11’, unsegmented user data, then the following rules shall be applied:

- the MAL message header fields shall be generated according to the specifications given in section 3 of this Recommended Standard, by using the Space Packet and the parameter ‘APID qualifier’ of the primitive ‘Packet indication’;

- every Space Packet whose MAL header fields ‘Interaction Type’, ‘Transaction Id’, ‘URI From’, ‘URI To’, ‘Session’, ‘Session Name’, ‘Domain’, ‘Network’, ‘Service Area’, ‘Service’, and ‘Operation’ are the same shall be sequenced according to the secondary header field ‘Segment Counter’;

- a full Space Packet sequence shall be detected as follows:

  - the first Space Packet of the sequence shall have the field ‘Sequence Flags’ equal to the binary value ‘01’, first segment of user data;

  - the last Space Packet of the sequence shall have the field ‘Sequence Flags’ equal to the binary value ‘10’, last segment of user data;

  - the other Space Packets of the sequence shall have the field ‘Sequence Flags’ equal to the binary value ‘00’, continuation segment of user data;

  - starting from the second Space Packet of the sequence, every Space Packet shall have the secondary header field ‘Segment Counter’ assigned with the value 1 added to the ‘Segment Counter’ of the previous Space Packet in the sequence;

- if a full Space Packet sequence is detected, then a MAL message shall be generated according to the specifications given in section 3 of this Recommended Standard, by using the following input data:

- the MAL message header generated from the first Space Packet of the sequence;

- the user data segments of the Space Packet sequence;

- the parameter ‘APID qualifier’ of the primitive ‘Packet indication’ triggered by the first Space packet of the sequence;

- the XML specification of the MO service (see section 6 of reference [2]) identified by the MAL header fields ‘Service Area’, ‘Service’, and ‘Area Version’;

- if a Space Packet sequence is not full after a mission-defined timeout, then the Space Packets of the sequence may be discarded.

If the field ‘URI To’ is unknown, then the error MAL::DESTINATION_UNKNOWN shall be returned if the Interaction Pattern allows a MAL error message to be returned. The MAL header field ‘URI From’ of the returned error message shall be assigned with the ‘URI To’ field of the initial message, even if this URI is unknown.

## ReceiveMultiple indication

The RECEIVEMULTIPLE indication primitive shall not be provided.

# MAL Data Encoding

## Overview

This section specifies a complete and unambiguous mapping of the MAL data types to a binary encoding format.

Encoding is a function that translates a MAL::Element into a sequence of encoded fields. This translation is defined in a generic, modular, and ‘octet aligned’ way:

- ‘generic’ means that the encoding format is not specifically defined for every data structure and every usage context but can be used to encode every data structure and every usage context generically;

- ‘modular’ means that the encoding format is defined by isolating every MAL data type and declaration context and specifying the encoding format for each of them;

- ‘octet aligned’ means that every encoded field starts on an octet boundary and contains one or more octets.

The type of an element can designate either the declared type of the field the element is assigned to or the actual type of the element. In order to avoid any ambiguity the word ‘type’ is always qualified as follows:

- declared type: the type of the field the element is assigned to; if the field belongs to the MAL message header then the declared type is given by table 3-1; if the field belongs to the MAL message body then the declared type and more generally the declaration context is given by the XML specification of the service (see section 6 of reference [2]);

- actual type: the type of the element.

MAL only specifies non-abstract types that are final, i.e., that cannot be extended. As a consequence, if the declared type of an element is non-abstract then the actual type is the same as the declared type.

NOTE	–	This encoding format can be re-used by a MAL binding to a messaging technology that is not the Space Packet Protocol.

The following subsections specify the rules to be applied when encoding an element. These rules depend on the element declaration context (e.g., the declared type) and the element actual type.

## Element

If the element is not an element of a list, and if the declared type of the element is MAL::Attribute, then the following field shall be encoded:

Attribute Tag

Unsigned 8-bit Integer (1 octet)

The field ‘Attribute Tag’ shall be assigned with the short form part of the attribute minus 1 so that the tag starts from zero.

If the element is not an element of a list and if the declared type of the element is either MAL::Element, or MAL::Composite, or an abstract composite, or if the declared type of the element is either List<MAL::Attribute>, or List<MAL::Element>, or List<MAL::Composite>, or List<<abstract composite>>, then the following fields shall be encoded:

| Area | Service | Area Version | Type |
| --- | --- | --- | --- |
| Unsigned 16-bit Integer (2 octets) | Unsigned 16-bit Integer (2 octets) | Unsigned 8-bit Integer (1 octet) | Signed 24-bit Integer (3 octets) |

NOTE	–	As specified by MAL (reference [2]), only the last element of a message body can be declared either abstract or as a list of an abstract type. Therefore the encoding format specified above cannot be used more than once per message body.

The field ‘Area’ shall be assigned with the area number of the element actual type encoded as an Unsigned 16-bit Integer.

If the element actual type is defined by a service, then the field ‘Service’ shall be assigned with the service number of the element actual type encoded as an Unsigned 16-bit Integer.

If the element actual type is not defined by a service, then the field ‘Service’ shall be assigned with the value ‘0’ encoded as an Unsigned 16-bit Integer.

The field ‘Area Version’ shall be assigned with the area version of the element actual type encoded as an Unsigned 8-bit Integer.

The field ‘Type’ shall be assigned with the short form part of the element actual type encoded as a Signed 24-bit Integer.

NOTE	–	The short form part is required to be a signed 32-bit integer by MAL (reference [2]). Negative numbers identify the list types. Therefore using a signed 24-bit integer as type field prevents the mapping of data types whose short form part is strictly greater than 223−1.

The element shall be encoded as follows:

- if the actual type of the element is a MAL::Attribute, then the element shall be encoded as specified by its actual type;

- if the actual type of the element is a MAL::Enumeration, then the element shall be encoded as an Enumeration;

- if the actual type of the element is a MAL::List, then the element shall be encoded as a List;

- if the actual type of the element is a MAL::Composite, then the element shall be encoded as a Composite.

## Enumeration

The first element of an enumeration shall be encoded with the value 0.

The second and following elements of an enumeration shall be encoded with the previous element value plus one.

If the enumeration size is less than or equal to 256, then the value shall be encoded as an Unsigned 8-bit Integer.

If the enumeration size is greater than 256 and less than or equal to 216, then the value shall be encoded as a UShort (see 5.16).

If the enumeration size is greater than 216 and less than or equal to 232, then the value shall be encoded as a UInteger (see 5.18).

NOTE	–	As specified in reference [2], the MAL enumeration size is limited by the MAL::UInteger range.

## Composite

Each field of the Composite shall be encoded in the same order as it is declared in the Composite definition.

Each field of the Composite shall be encoded as follows:

- if the value of the attribute ‘canBeNull’ in the field declaration is TRUE, then the field shall be encoded as a Nullable Element;

- otherwise the field shall be encoded as an Element.

If the Composite inherits from another Composite, then the inherited Composite shall be encoded first.

## List

A List shall be encoded as follows:

| List Length | List Element |
| --- | --- |
| UInteger (variable, multiple of octet) | Nullable Element (variable, multiple of octet) |
|  | Repeated for every element in the list |

The field ‘List Length’ shall be assigned with the length of the list encoded as a UInteger (see 5.18).

NOTE	–	The type List is required to be unbounded by MAL (reference [2]). Using a UInteger as length field limits the list length to 232 − 1 elements.

The list elements shall be encoded in the same order as in the list.

## Nullable Element

A Nullable Element shall be encoded as follows:

| Presence Flag | Element |
| --- | --- |
| Boolean (1 octet) | Element (variable, multiple of octet) |
|  | If Presence Flag is TRUE |

The field ‘Presence Flag’ shall be FALSE if the element is NULL; it shall be TRUE if the element is not NULL.

## Blob

A MAL::Blob shall be encoded as follows:

| Blob Length | Blob Octet |
| --- | --- |
| UInteger (variable, multiple of octet) | Unsigned 8-bit Integer (1 octet) |
|  | Repeated for every octet in the Blob |

The field ‘Blob length’ shall be assigned with the length of the Blob encoded as a UInteger (see 5.18).

NOTE	–	The type Blob is required to be unbounded by MAL (reference [2]). Using a UInteger as size field limits the size to 232 − 1 octets.

The Blob octets shall be encoded in the same order as in the Blob.

## Boolean

A MAL::Boolean shall be encoded as an Unsigned 8-bit Integer.

If the Boolean value is TRUE then the integer ‘1’ shall be encoded otherwise the integer ‘0’ shall be encoded.

## Duration

A MAL::Duration shall be encoded according to the CUC Time Code Format (reference [5]) given by the mapping configuration parameter DURATION_CODE_FORMAT.

Negative values shall be encoded using the two’s complement representation of the MAL::Duration.

The Time Code Format P-Field shall not be encoded.

## Float

A MAL::Float value shall be encoded according to the binary interchange format of width 32 bits defined in reference [3].

## Double

A MAL::Double shall be encoded according to the binary interchange format of width 64 bits defined in reference [3].

## Identifier

A MAL::Identifier shall be encoded as a String.

## Octet

A MAL::Octet shall be encoded as a Signed 8-bit Integer.

## UOctet

A MAL::UOctet shall be encoded as an Unsigned 8-bit Integer.

## Short

If the mapping configuration parameter VARINT_SUPPORTED is TRUE, then a MAL::Short shall be encoded as a 2-octet Signed Varint (see 5.28).

If the mapping configuration parameter VARINT_SUPPORTED is FALSE, then a MAL::Short shall be encoded as a Signed 16-bit Integer (see 5.26).

## UShort

If the mapping configuration parameter VARINT_SUPPORTED is TRUE, then a MAL::UShort shall be encoded as a 2-octet Unsigned Varint (see 5.27).

If the mapping configuration parameter VARINT_SUPPORTED is FALSE, then a MAL::UShort shall be encoded as an Unsigned 16-bit Integer (see 5.25).

## Integer

If the mapping configuration parameter VARINT_SUPPORTED is TRUE, then a MAL::Integer shall be encoded as a 4-octet Signed Varint (see 5.28).

If the mapping configuration parameter VARINT_SUPPORTED is FALSE, then a MAL::Integer shall be encoded as a Signed 32-bit Integer (see 5.26).

## UInteger

If the mapping configuration parameter VARINT_SUPPORTED is TRUE, then a MAL::UInteger shall be encoded as a 4-octet Unsigned Varint (see 5.27).

If the mapping configuration parameter VARINT_SUPPORTED is FALSE, then a MAL::UInteger shall be encoded as an Unsigned 32-bit Integer (see 5.25).

## Long

If the mapping configuration parameter VARINT_SUPPORTED is TRUE, then a MAL::Long shall be encoded as a 8-octet Signed Varint (see 5.28).

If the mapping configuration parameter VARINT_SUPPORTED is FALSE, then a MAL::Long shall be encoded as a Signed 64-bit Integer (see 5.26).

## ULong

If the mapping configuration parameter VARINT_SUPPORTED is TRUE, then a MAL::ULong shall be encoded as a 8-octet Unsigned Varint (see 5.27).

If the mapping configuration parameter VARINT_SUPPORTED is FALSE, then a MAL::ULong shall be encoded as an Unsigned 64-bit Integer (see 5.25).

## String

A MAL::String shall be encoded as follows:

| String Length | Character |
| --- | --- |
| UInteger (variable, multiple of octet) | UTF-8 (variable, multiple of octet) |
|  | Repeated for every character in the String |

The field ‘String Length’ shall be assigned with the number of octets required to encode the characters of the string.

The field ‘String Length’ shall be encoded as a UInteger (see 5.18).

NOTE	–	The types Identifier, String, and URI are required to be unbounded by MAL (reference [2]). Using a UInteger as length field limits the encoded string length to 232 − 1 octets.

The field ‘Character’ shall be encoded according to the UTF-8 format (reference [4]).

The String characters shall be encoded in the same order as in the String.

## Time

A MAL::Time shall be encoded according to the CCSDS Time Code Format (reference [5]) specified by the mapping configuration parameters TIME_CODE_FORMAT and TIME_EPOCH.

The Time Code Format P-Field shall not be encoded.

## FineTime

A MAL::FineTime shall be encoded according to the CCSDS Time Code Format (reference [5]) specified by the mapping configuration parameters FINE_TIME_CODE_FORMAT and FINE_TIME_EPOCH.

The Time Code Format P-Field shall not be encoded.

## Uri

A MAL::URI shall be encoded as a String.

## Unsigned N-bit Integer

An unsigned N-bit integer shall be encoded on a given number of bits N.

The bit ‘Bit N−1’ shall designate the least significant bit of the unsigned integer.

Each bit of the unsigned integer shall be encoded from ‘Bit 0’ to ‘Bit N−1’.

## Signed N-bit Integer

A signed N-bit integer shall be encoded according to its 2’s complement representation on a given number of bits N.

The sign bit shall be assigned to ‘Bit 0’.

Each bit of the signed integer shall be encoded from ‘Bit 0’ to ‘Bit N−1’.

## Unsigned Varint

The length of the unsigned integer to encode shall be either 2, 4, or 8 octets.

The unsigned integer to encode shall be divided in groups of 7 bits as specified by table 5-1.

Table 5-1: Unsigned Integer 7-bit Groups

|  | Unsigned Integer Length (octets) |
| --- | --- |
|  | 2 | 4 | 8 |
| Group 1 | Begin | Bit N-7 | Bit N-7 | Bit N-7 |
|  | End | Bit N-1 | Bit N-1 | Bit N-1 |
| Group 2 | Begin | Bit N-14 | Bit N-14 | Bit N-14 |
|  | End | Bit N-8 | Bit N-8 | Bit N-8 |
| Group 3 | Begin | 5 zeros and Bit 0 | Bit N-21 | Bit N-21 |
|  | End | Bit N-15 | Bit N-15 | Bit N-15 |
| Group 4 | Begin | - | Bit N-28 | Bit N-28 |
|  | End | - | Bit N-22 | Bit N-22 |
| Group 5 | Begin | - | 3 zeros and Bit 0 | Bit N-35 |
|  | End | - | Bit N-29 | Bit N-29 |
| Group 6 | Begin | - | - | Bit N-42 |
|  | End | - | - | Bit N-36 |
| Group 7 | Begin | - | - | Bit N-49 |
|  | End | - | - | Bit N-43 |
| Group 8 | Begin | - | - | Bit N-56 |
|  | End | - | - | Bit N-50 |
| Group 9 | Begin | - | - | Bit N-63 |
|  | End | - | - | Bit N-57 |
| Group 10 | Begin | - | - | 6 zeros and Bit 0 |
|  | End | - | - | Bit 0 |

NOTE	–	The 7-bit groups are ordered from the least significant group to the most significant group. The bit ordering is not changed.

If the most significant 7-bit group contains only zeros, and if it is not the first group, then it should be discarded; this prescription shall be repeated until either the most significant 7-bit group does not contain any zero, or it is the first group.

The 7-bit groups shall be encoded from the least significant group to the most significant group.

Every 7-bit group shall be encoded in an octet as shown below:

| Continuation bit | 7-bit Group |
| --- | --- |
| Binary value (1 bit) | Binary value (7 bits) |

The field ‘Continuation bit’ shall be assigned with the value ‘1’ if there are further 7-bit groups to come, otherwise it shall be assigned with the value ‘0’.

## Signed Varint

The length of the signed integer to encode shall be either 2, 4, or 8 octets.

The signed integer shall be translated to an unsigned integer according to the bit shifting formula specified in table 5-2 where the following symbols are used:

- the variable ‘n’ is the 2’s complement representation of the signed integer;

- the operator ‘<<’ shifts the left-hand operand to the left by a number of positions given by the right-hand operand; a zero is shifted into the rightmost position;

- the operator ‘>>’ shifts the left-hand operand to the right by a number of positions given by the right-hand operand; the sign bit is shifted into the leftmost position.

- the operator ‘^’ performs a bitwise exclusive OR operation.

Table 5-2: Signed Integer Bit Shifting

| Signed Integer Length (octets) | Bit Shifting Formula |
| --- | --- |
| 2 | (n << 1) ^ (n >> 15) |
| 4 | (n << 1) ^ (n >> 31) |
| 8 | (n << 1) ^ (n >> 63) |

NOTE	–	The bit shifting translation, also called a ‘zig-zag translation’, is applied in order that small negative values (-1, -2 etc.) use the same number of octets as their opposite positive values. Otherwise these small negative values would use one more octet than the integer size (e.g. 5 octets for a 32-bit integer) and only the big negative values would benefit from the size reduction.

The resulting unsigned integer shall be encoded as an Unsigned Varint.

Protocol Implementation Conformance Statement Proforma

(Normative)

INTRODUCTION

Overview

This annex provides the Protocol Implementation Conformance Statement (PICS) Requirements List (PRL) for implementations of the MAL Space Packet Binding standard. The PICS for an implementation is generated by completing the PRL in accordance with the instructions below.

An implementation’s completed PRL is called the PICS. The PICS states which protocol features have been implemented. The following entities can use the PICS:

- the protocol implementer, as a checklist to reduce the risk of failure to conform to the standard through oversight;

- the supplier and acquirer or potential acquirer of the implementation, as a detailed indication of the capabilities of the implementation, stated relative to the common basis for understanding provided by the standard PICS proforma;

- the user or potential user of the implementation, as a basis for initially checking the possibility of interworking with another implementation (while interworking can never be guaranteed, failure to interwork can often be predicted from incompatible PICSes);

- a protocol tester, as the basis for selecting appropriate tests against which to assess the claim for conformance of the implementation.

NOTATION

Status Column Symbols

The following are used in the PRL to indicate the status of features:

| Symbol | Meaning |
| --- | --- |
| M | Mandatory |
| O | Optional |

Support Column Symbols

The support of every item as claimed by the implementer is stated by entering the appropriate answer (Y, N, or N/A) in the support column.

| Symbol | Meaning |
| --- | --- |
| Y | Yes, supported by the implementation |
| N | No, not supported by the implementation |
| N/A | Not applicable |

GENERAL INFORMATION

IDENTIFICATION OF PICS

| Ref | Question | Response |
| --- | --- | --- |
| 1 | Date of Statement (DD/MM/YYYY) |  |
| 2 | CCSDS document number containing the PICS |  |
| 3 | Date of CCSDS document containing the PICS |  |

IDENTIFICATION OF IMPLEMENTATION UNDER TEST (IUT)

| Ref | Question | Response |
| --- | --- | --- |
| 1 | Implementation name |  |
| 2 | Implementation version |  |
| 3 | Machine name |  |
| 4 | Machine version |  |
| 5 | Operating System name |  |
| 6 | Operating System version |  |
| 7 | Special Configuration |  |
| 8 | Other Information |  |

USER IDENTIFICATION

| Supplier |  |
| --- | --- |
| Contact Point for Queries |  |
| Implementation name(s) and Versions |  |
| Other Information Necessary for full identification —e.g., name(s) and version(s) for machines and/or operating systems; System Name(s) |  |

INSTRUCTIONS FOR COMPLETING THE PRL

An implementer shows the extent of compliance to the protocol by completing the PRL; the resulting completed PRL is called a PICS.

MO MAL Space Packet Binding PICS

Message Abstraction Layer

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1-1 | Transaction Handling | [2] subsection 3.2 | M |  |
| 1-2 | State Transitions | [2] subsection 3.3 | M |  |
| 1-3 | Message Composition | [2] subsection 3.4 | M |  |
| 1-4 | MAL Service Interface | [2] subsection 3.5 | M |  |
| 1-5 | Access Control Interface | [2] subsection 3.6 | M |  |
| 1-6 | Transport Interface | [2] subsection 3.7 | M |  |
| 1-7 | MAL Data Type Specification | [2] section 4 | M |  |
| 1-8 | MAL Errors | [2] section 5 | M |  |

MAL Message Mapping

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 2-1 | URI Format | 3.2 | M |  |
| 2-2 | MAL Header Mapping | 3.3 | M |  |
| 2-3 | Field ‘Timestamp’ | 3.3.5 | O |  |
| 2-4 | Fields ‘Priority’, ‘Domain’, ‘Network Zone’, ‘Session Name’ | 3.3.7 3.3.8 3.3.9 3.3.11 | O |  |
| 2-5 | Field ‘Authentication Id’ | 3.3.3 | O |  |
| 2-6 | Space Packet Specific Fields | 3.4 | M |  |
| 2-7 | MAL Message Body Mapping | 3.5 | M |  |

MAL Transport Interface Mapping

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 3-1 | SupportedQoS Request | 4.2 | M |  |
| 3-2 | SupportedIP Request | 4.3 | M |  |
| 3-3 | Transmit Request | 4.4 | M |  |
| 3-4 | TransmitMultiple Request | 4.5 | M |  |
| 3-5 | Receive Indication | 4.6 | M |  |
| 3-6 | ReceiveMultiple Indication | 4.7 | M |  |

MAL Data Encoding

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 4-1 | MAL Data Encoding | section 5 | M |  |

Mapping Configuration Parameters

(Normative)

This annex defines the parameters that are provided by the MAL Space Packet Binding protocol in order to configure and optimize the MAL message mapping and the format of the Space Packet.

Those parameters are either mission specific or application process specific, i.e. specific to the value of the Space packet primary header field ‘Application Process Identifier’ and the APID qualifier.

The mapping configuration parameters are managed parameters, defined by some out-of-band agreement.

Table B-1 lists the mapping configuration parameters.

Table B-1: Mapping Configuration Parameters

| Parameter Name | Type | Description |
| --- | --- | --- |
| AUTHENTICATION_ID | MAL:Blob | Value to be assigned to the MAL header field ‘Authentication Id’ if the QoS property AUTHENTICATION_ID_FLAG is FALSE |
| DOMAIN | List<MAL::Identifier> | Value to be assigned to the MAL header field ‘Domain’ if the QoS property DOMAIN_FLAG is FALSE |
| DURATION_CODE_FORMAT | MAL::Blob | P-Field of the CUC Time Code Format (reference [5]) to be applied to the MAL::Duration elements |
| DURATION_UNIT | MAL::String | Name of the time unit used by the Time Code Format for MAL::Duration, e.g. second, millisecond. |
| FINE_TIME_CODE_FORMAT | MAL::Blob | P-Field of the Time Code Format (reference [5]) to be applied to the MAL::FineTime elements |
| FINE_TIME_EPOCH | MAL::String | Epoch in ISO-8601 format (reference [6]) to be applied to the MAL::FineTime elements |
| FINE_TIME_EPOCH_TIMESCALE | MAL::String | Name of the time scale for the MAL::FineTime epoch, either “TAI” or “UTC”. |
| FINE_TIME_UNIT | MAL::String | Name of the time unit used by the Time Code Format for MAL::FineTime, e.g. second, millisecond. |
| NETWORK_ZONE | MAL::Identifier | Value to be assigned to the MAL header field ‘Network Zone’ if NETWORK_ZONE_FLAG is FALSE |
| PACKET_DATA_FIELD_SIZE_LIMIT | MAL::UShort | Packet Data Field size limit in octets, strictly less than 65536. A value of 0 denotes the maximum allowable size of 65536 octets. |
| PRIORITY | MAL::UInteger | Value to be assigned to the MAL header field ‘Priority’ if PRIORITY_FLAG is FALSE |
| TIME_CODE_FORMAT | MAL::Blob | P-Field of the Time Code Format (reference [5]) to be applied to the MAL::Time elements |
| TIME_EPOCH | MAL::String | Epoch in ISO-8601 format (reference [6]) to be applied to the MAL::Time elements |
| TIME_EPOCH_TIMESCALE | MAL::String | Name of the time scale for the MAL::Time epoch, either “TAI” or “UTC”. |
| TIME_UNIT | MAL::String | Name of the time unit used by the Time Code Format for MAL::Time, e.g. second, millisecond. |
| SESSION_NAME | MAL::Identifier | Value to be assigned to the MAL header field ‘Session Name’ if SESSION_NAME_FLAG is FALSE |
| VARINT_SUPPORTED | MAL::Boolean | Boolean indicating whether the ‘Varint’ encoding format is supported or not |

QoS Properties

(Normative)

This annex defines the QoS properties that are provided by the MAL Space Packet Binding protocol. QoS properties are set on a per message basis as specified by MAL (reference [2]).

Table C-1 lists the QoS properties.

Table C-1: QoS Properties

| QoS Property Name | Type | Description |
| --- | --- | --- |
| AUTHENTICATION_ID_FLAG | MAL::Boolean | Value to be assigned to the secondary header field ‘Authentication Id Flag’ |
| DOMAIN_FLAG | MAL::Boolean | Value to be assigned to the secondary header field ‘Domain Flag’ |
| NETWORK_ZONE_FLAG | MAL::Boolean | Value to be assigned to the secondary header field ‘Network Zone Flag’ |
| PRIORITY_FLAG | MAL::Boolean | Value to be assigned to the secondary header field ‘Priority Flag’ |
| SESSION_NAME_FLAG | MAL::Boolean | Value to be assigned to the secondary header field ‘Session Name Flag’ |
| TIMESTAMP_FLAG | MAL::Boolean | Value to be assigned to the secondary header field ‘Timestamp Flag’ |

SECURITY, SANA, AND PATENT CONSIDERATIONS

(Informative)

SECURITY CONSIDERATIONS

Overview

This annex subsection discusses various aspects of security with respect to the MAL Space Packet Binding protocol.

SECURITY BACKGROUND

The following security aspects are typically separated:

- data and data origin authentication: corroboration of the source of information that is contained in a message;

- authorization: conveyance, to another entity, of official sanction to do or be something;

- confidentiality: keeping information secret from all but those who are authorized to see it;

- integrity: detecting that information has not been altered by unauthorized or unknown means.

The MAL Space Packet Binding protocol is not responsible for ensuring all these security aspects; however, it has to fulfil the security criteria expected by the MAL layer from every transport binding. These criteria are:

- the Transport Layer is responsible for the transmission of the authentication identifier assigned by the MAL layer to every consumer;

- the Transport Layer has to provide authentication, confidentiality, and integrity of the transmitted messages.

SECURITY CONCERNS

Authentication of the consumers is done above the MAL layer through a specific service that enables a consumer to get an authentication identifier. The meaning of that authentication identifier is dependent on the security system used for the deployment. This identifier must allow the MAL access control implementation to perform a lookup for authorization purposes.

The authentication identifier is transmitted by the Space Packet binding in the parameter ‘Authentication Identifier’ of the Space Packet secondary header; however, this parameter may be omitted as it is optional.

Authorization is done by the MAL access control that performs any required authorization checks and converts the consumer identifier into technology dependent security credentials.

It is assumed that message authentication and confidentiality are provided beneath the Space Packet Protocol layer and are transparent to the Space Packet Binding and above. As a consequence, once a message rises above the Space Packet Protocol layer, the message has been authenticated and all encryption has been removed.

Integrity is ensured by the protocol that conveys the Space Packets.

POTENTIAL THREATS AND ATTACK SCENARIOS

Potential threats and attack scenarios depend on the layer that is beneath the Space Packet Protocol because this is the layer that defines the security algorithms ensuring authentication, confidentiality, and integrity.

CONSEQUENCES OF NOT APPLYING SECURITY

The only security aspect that may not be applied is the transmission of the authentication identifier in the Space Packet secondary header. If the authentication identifier is not transmitted by the Space Packet Binding, then delivered messages may be rejected by the MAL access control.

SANA CONSIDERATIONS

Version Number

The recommendations of this document request SANA to create the registry defined as follows:

- the registry named ‘MAL Space Packet Binding Version Number’ consists of a table of parameters:

- Version Number: a string of text specifying the three bits to be assigned to the packet secondary header field ‘Version Number’;

- Reference: a string of text referencing the CCSDS document that specifies the version of the MAL Space Packet Binding;

- the initial registry should be filled with the values in table C-1.

Table D-1:  MAL Space Packet Binding Version Number Initial Values

| Version Number | Reference |
| --- | --- |
| 000 | CCSDS 524.1-B-1 |

URI Scheme name

The recommendations of this document request SANA to create the registry defined as follows:

- the registry named ‘MAL Binding URI Scheme Name’ consists of a table of parameters:

- Scheme Name: a string of text specifying the name of the URI scheme defined by the MAL binding;

- Reference: a string of text referencing the CCSDS document that specifies the MAL binding;

- the initial registry should be filled with the values in table C-2.

Table C-2:  MAL Binding URI Scheme Name Initial Values

| Scheme Name | Reference |
| --- | --- |
| malspp | CCSDS 524.1-B-1 |

PATENT CONSIDERATIONS

No patents are known to apply to this Recommended Standard.

Encoding efficiency

(informative)

Bandwidth Overhead

This section lists the potential overhead costs caused by the encoding format.

Secondary header

The overhead caused by the secondary header depends on whether the optional fields are inserted or not in the header: ‘Source Id’, ‘Destination Id’, ‘Segment Counter’, ‘Priority’, ‘Timestamp’, ‘Network Zone’, ‘Session Name’, ‘Domain’, and ‘Authentication Id’.

The minimum overhead is 21 bytes. It is obtained with every optional MAL header fields not passed (presence flags set to FALSE) and without segmentation of the MAL message. The additional overheads are given by table D-1 in terms of:

- the name of a secondary header field;

- the encoding format of the field (as specified by section 5).

Table D-1: Secondary Header Additional Overheads

| Field Name | Encoding Format |
| --- | --- |
| Source Id | Unsigned 8-bit Integer |
| Destination Id | Unsigned 8-bit Integer |
| Segment Counter | Unsigned 32-bit Integer |
| Priority | UInteger |
| Timestamp | Time |
| Network Zone | Identifier |
| Session Name | Identifier |
| Domain | List<Identifier> |
| Authentication Id | Blob |

Presence Flag

An overhead of 1 octet is added for every field that can be null in a composite data structure.

polymorphism

Type information is only encoded where absolutely necessary, i.e. when polymorphism is employed. Otherwise, type information is directly taken from the service specification.

The last element of a MAL body may be abstract. In this case, a type information needs to be added depending on the last element type. If the last element is typed MAL::Element, MAL::Composite, or an abstract composite, then the overhead is 8 octets. If the last element is MAL::Attribute, then the overhead is 1 octet. This overhead is added at most once per MAL message body.

An overhead of 1 octet is also added for every field typed MAL::Attribute declared in a composite structure.

Effort reduction

Missions benefit from the generic nature of the encoding format. Mission-specific solutions of mapping MAL messages to Space Packets are avoided, thus allowing easier cross support, reuse of components for several missions and less personnel training. The effort required by the definition of a specific encoding format is reduced to zero. There is no dependency on the spacecraft database any more.

Besides, a mission has still the ability to define compact data structures dedicated to its needs. The effort is still lower than the one required by the definition of a specific packet format.

acronyms

(informative)

AOS	Advanced Orbiting System

APID	Application Process Identifier

BP	Bundle Protocol

CRC	Cyclic Redundancy Check

IP	Interaction Pattern

MAL	Message Abstract/Abstraction Layer

MSB	Most Significant Bit

PDU	Protocol Data Unit

QoS	Quality of Service

SANA	Space Assigned Numbers Authority

SDU	Service Data Unit

SLE	Space Link Extension

SM&C	CCSDS Spacecraft Monitoring and Control

SP	Space Packet

SPP	Space Packet Protocol

TC	Telecommand

TCP	Transmission Control Protocol

TM	Telemetry

URI	Universal Resource Identifier

UDP	User Datagram Protocol

informative References

(Informative)

[E1]	Mission Operations Services Concept. Issue 3. Report Concerning Space Data System Standards (Green Book), CCSDS 520.0-G-3. Washington, D.C.: CCSDS, December 2010.

[E2]	TM Space Data Link Protocol. Issue 1. Recommendation for Space Data System Standards (Blue Book), CCSDS 132.0-B-1. Washington, D.C.: CCSDS, September 2003.

[E3]	TC Space Data Link Protocol. Issue 2. Recommendation for Space Data System Standards (Blue Book), CCSDS 232.0-B-2. Washington, D.C.: CCSDS, September 2010.