Mission Operations Space Packet Transport Binding and Binary Encoding Prototype Test plan AND REPORT

DRAFT CCSDS Record

CCSDS 000.0-Y-0

Draft Yellow Book

April 2015

FOREWORD

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This document is therefore subject to CCSDS document management and change control procedures, which are defined in the Procedures Manual for the Consultative Committee for Space Data Systems.  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- British National Space Centre (BNSC)/United Kingdom.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt e.V. (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- Centro Tecnico Aeroespacial (CTA)/Brazil.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- MIKOMTEK: CSIR (CSIR)/Republic of South Africa.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

# DOCUMENT CONTROL

| Document | Title and Issue | Date | Status |
| --- | --- | --- | --- |
| CCSDS 000.0-Y-0 | MISSION OPERATIONS SPACE PACKET TRANSPORT BINDING AND BINARY ENCODING PROTOTYPE TEST PLAN AND REPORT, Draft CCSDS Record, Issue 0 | April 2015 | Current draft |

# CONTENTS

Section	Page

DOCUMENT CONTROL	iii

CONTENTS	iv

1	Introduction	1-1

1.1	Purpose	1-1

1.2	scope	1-1

1.3	structure of this report	1-1

1.4	References	1-1

2	OVERVIEW	2-1

2.1	TEST APPROACH	2.1-1

2.2	Testbed Configuration	2.2-3

2.3	TESTS OVERViEW	2.3-4

2.4	test Results SUMMARY	2.4-4

3	Test Scenarios	3-7

3.1	MAL Message Mapping test scenario	3.1-7

3.2	MAL Data Type encoding scenario	3.2-26

4	MALPrototype Service Specification	4-32

4.1	Service: IPTest	4.1-32

4.2	Service: DataTest	4.2-45

4.3	Service: ErrorTest	4.3-68

4.4	Service: IPTest2	4.4-76

5	MalPrototype Data types	5-80

5.1	Area data types: MALPrototype	5.1-80

5.2	Service data types: IPTest	5.2-80

6	Error codes	6-88

7	Compliance matrix	7-89

8	Mapping Configuration Parameters	8-98

8.1	APID Qualifier 247, APID 1	8.1-98

8.2	APID Qualifier 248, APID 2	8.2-99

8.3	APID Qualifier 347, APID 3	8.3-100

8.4	APID Qualifier 447, APID 5	8.4-101

8.5	APID Qualifier 547, APID 7	8.5-102

8.6	APID Qualifier 348, APID 4	8.6-103

8.7	APID Qualifier 647, APID 1	8.7-104

8.8	APID Qualifier 648, APID 2	8.8-105

8.9	APID Qualifier 647, APID 3	8.9-106

8.10	APID Qualifier 648, APID 4	8.10-107

8.11	APID Qualifier 123, APID 123	8.11-108

# Introduction

## Purpose

This document provides a report of the interoperability testing that occurred in support of the production of the CCSDS recommendation 524.1, MISSION OPERATIONS—SPACE PACKET TRANSPORT BINDING AND BINARY ENCODING.

## scope

This test report addresses primarily the formal prototype interoperations that occurred between the DLR developed prototype and the CNES developed prototype, against the formally released RED 1 version of the SPACE PACKET TRANSPORT BINDING AND BINARY ENCODING recommendation identified in 1.1.

## structure of this report

This test report is organized as follows:

- Section 1 provides purpose and scope, definitions and references used throughout the report;

- Section 2 gives an overview of the test report and a summary of the test results;

- Section 3 defines the test scenarios;

- Section 4 defines the test services;

- Section 5 defines the test data structures;

- Section 6 defines the errors raised by the test services;

- Section 7 gives the compliance matrix;

- Section 8 specifies the Mapping Configuration Parameters.

## References

The following documents are referenced in this document.  At the time of publication, the editions indicated were valid.  All documents are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the documents indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS documents.

[1]	Mission Operations—Space Packet Transport Binding and Binary Encoding.  Draft Recommendation for Space Data System Standards, CCSDS 524.1-R-1.  Red Book.  Issue 1.  Washington, D.C.: CCSDS, December 2014.

# OVERVIEW

This document provides a report of the prototype interoperations conducted in support of the development of the CCSDS recommendation for Mission Operations (MO) Space Packet Transport Binding and Binary Encoding.

The Deutsches Zentrum für Luft- und Raumfahrt (DLR), and the Centre National d’Etudes Spatiales (CNES) of France each developed prototype implementations of the draft CCSDS recommendation.

## TEST APPROACH

The tests check that two independent implementations of the MO Space Packet Transport Binding and Binary Encoding specification adhere to the standard as specified by the CCSDS recommendation.

Two distinct stacks are built by assembling the following components:

- Test Consumer

- Test Provider

- Service Java API

- Service Stubs and Skeletons

- MAL Java API

- MAL Java Implementation

- Transport Java API

- Binding Java Implementation

- SPP Java API

- SPP Java Implementation over TCP/IP

The figure below presents the two stacks in a particular test instance where the Test Consumer uses the Space Packet Binding implemented by CNES and the Test Provider uses the Space Packet Binding implemented by DLR.

Figure 2-1 MO SPP Binding prototype

The following component is separately produced by DLR and CNES:

- Binding Java Implementation

The following components are developed by DLR and CNES together:

- Test Consumer

- Test Provider

- MAL testbed extensions, e.g. space packet interception module, test services

- SPP Java API

- SPP Java Implementation overTCP/IP

The following components are reused from the MAL testbed:

- MAL testbed

- Some MAL test consumers and providers

- MAL Java API

- MAL Java Implementation

- Transport Java API

- Testbed Configuration

- The MAL testbed is a software component providing a framework for MO services and binding prototyping activities. Physical computers are not provided and no network connection is used as both stacks (consumer and provider) are co-located on the same machine. However the Test Consumer and the Test Provider modules are launched in distinct processes, which is enough to test every statement of the MAL Space Packet Transport Binding and Binary Encoding.

- The configuration of the testbed is defined by the following elements:

- Maven scripts for running the tests;

- Environment properties;

- Mapping Configuration Parameters.

- Maven scripts

- Maven is a build automation tool used primarily for Java projects.

- A Maven script specifies how the Consumer and Provider Processes are built and executed. Four profiles are defined to launch tests internally at CNES and at DLR, and to launch interoperability tests between CNES and DLR implementations of the Space Packet Binding:

- CNES Consumer to CNES Provider

- DLR Consumer to DLR Provider

- CNES Consumer to DLR Provider

- DLR Consumer to CNES Provider

- Environment properties

- The Consumer and Provider Processes expect some environment properties to be defined. Those properties are listed below:

- MAL Java API properties

- Class name of the transport in charge of MAL message interception; this is not the SPP Binding transport but a test transport which intercepts MAL messages and delegates the transport primitives to another transport (see Testbed properties below);

- Class name of the encoding module; this is the SPP Binding encoding module;

- Testbed properties

  - Name of the binding protocol (as defined by the MAL Java API): “malspp”;

- Class name of the transport to be used by the MAL message interceptor (to delegate the transport primitives); this is the SPP Binding transport;

- SPP over TCP properties

  - Class name of the Space Packet transport; this is the transport used by the SPP Binding to send and receive Space Packets;

- Connection role (client or server) and port.

- Mapping configuration parameters

- The expected mapping configuration parameters are specified in section 8. They need to be configured in a way that depends on the SPP Binding implementation, for example, an XML descriptor.

## TESTS OVERViEW

Two test scenarios are developed:

- MAL Message Mapping verifies sections 3 and 4 of the MO MAL Space Packet Transport Binding and Binary Encoding book

- MAL Data Encoding verifies section 5 of the MO MAL Space Packet Transport Binding and Binary Encoding book

## test Results SUMMARY

The parts of the test bed are built as a set of Maven (http://maven.apache.org/) components and hosted in a shared component repository (no code only binaries shared). This permits not only automated build and dependency management or the two application stacks but also the use of automated test tools.

Tests are a set of FitNesse (http://fitnesse.org/) pages, tests are defined using a special Wiki language, and test output is HTML web pages. The top level test application provides a set of methods for performing the various tests and these are invoked by the Wiki pages, the output of which is formatted into a HTML report.

Total of 12660 individual tests were defined.

There are two separate implementations of the MO SPP Binding, DLR and CNES, which permitted a total of 4 configurations to be tested:

- CNES to CNES using the MO SPP Binding

- DLR to DLR using the MO SPP Binding

- CNES to DLR using the MO SPP Binding

- DLR to CNES using the MO SPP Binding

Therefore a total of 4 configuration by 12660 tests were performed, 50640 tests executed in total.

### TEST RESULTS

#### Overview

Each of the sub-sections in section 3 outline the test and include the test result in the form of a table, an example of which is shown below:

| script | data type scenario |
| --- | --- |
| check | explicit duration type works | OK |
| check | explicit Fine Time type works | OK |
| check | explicit Identifier type works | OK |

Each row of the table represents a test of the test, the first row being the test name. If the test step is completed with success the row will be highlighted green, if it fails then it is highlighted red. A row without highlighting is a step that does not produce a result.

#### Result summary

| 11417 MAL Message Mapping tests |
| --- |
| CNES to CNES using the MO SPP Binding | All passed |
| DLR to DLR using the MO SPP Binding | All passed |
| CNES to DLR using the MO SPP Binding | All passed |
| DLR to CNES using the MO SPP Binding | All passed |

| 1243 MAL Data Encoding tests |
| --- |
| CNES to CNES using the MO SPP Binding | All passed |
| DLR to DLR using the MO SPP Binding | All passed |
| CNES to DLR using the MO SPP Binding | All passed |
| DLR to CNES using the MO SPP Binding | All passed |

| Total of 12660 individual tests |
| --- |
| CNES to CNES using the MO SPP Binding | All passed |
| DLR to DLR using the MO SPP Binding | All passed |
| CNES to DLR using the MO SPP Binding | All passed |
| DLR to CNES using the MO SPP Binding | All passed |

# Test Scenarios

## MAL Message Mapping test scenario

The MAL Message Mapping test scenario is split into several test cases, each testing a specific aspect of the mapping.

The cases are split according to the following:

- Test the MAL message mapping for every interaction pattern except Publish-Subscribe

- Test the MAL message mapping for Publish-Subscribe

- Test the MAL message body mapping

- Test the empty body special case

- Test the MAL message segmentation

- Test the MO SPP Binding specific QoS properties

- Test the assignement of the source and destination identifiers

- Test the mapping of the MAL Transport primitives

The test service provider is required to implement the MAL prototype IPTest service.

Each of the test cases details the required behaviour of the test service provider and also the test client.

Assertions specific to the MO SPP Binding are done at the transport level thanks to the MAL message and space packet interception mechanisms.

### All Except PubSub test case

This test case reuses the MAL test procedure that does the following actions:

- Call the operation <ip> provided by the IPTest service with the parameters passed to the test procedures: 'ip', 'qos', 'session' and 'transition list id'.

- Wait for the expected transitions to be done.

- Check the message headers

- Check the transitions

The TM/TC packet type modifies the meaning of the primary header APID. The primary header APID identifies the destination of a TC packet whereas it identifies the source of a TM packet. As a consquence, the following aspects are impacted:

- URIs From and To mapping

- Out-of-band parameters choice, as they depends on the primary header APID, e.g. the time code format used to encode the MAL message timestamp

Therefore the related statements are tested for every interaction pattern and stage in every TM/TC combination:

- Consumer sending TC packets to provider sending TC packets

- Consumer sending TC packets to provider sending TM packets

- Consumer sending TM packets to provider sending TC packets

- Consumer sending TM packets to provider sending TM packets

Several APID qualifiers and APIDs are used:

- 248/2: IPTest providers sending TC packets

- 348/4: IPTest providers sending TM packets

- 247/1: IPTest consumers sending TC packets and expecting to receive TC packets

- 347/3: IPTest consumers sending TC packets and expecting to receive TM packets

- 447/5: IPTest consumers sending TM packets and expecting to receive TC packets

- 547/7: IPTest consumers sending TM packets and expecting to receive TM packets

The error ‘unkown URI’ is also tested.

#### Final results

| script | mal spp pattern test |
| --- | --- |
| test mal spp pattern with consumer tc | true | and provider tc | true |
| test mal spp pattern with consumer tc | true | and provider tc | false |
| test mal spp pattern with consumer tc | false | and provider tc | true |
| test mal spp pattern with consumer tc | false | and provider tc | false |

#### Primary header check

These assertions are checked for every TM/TC combination, every interaction pattern and stage.

| scenario | primary header |
| --- | --- |
| check | packet version number is | 0 |
| check space packet type |
| check | secondary header flag is | 1 |
| ensure | packet data length is length of packet data field minus one |

#### Secondary header check

These assertions are checked for every TM/TC combination, every interaction pattern and stage.

| scenario | secondary header |
| --- | --- |
| check | version is | 0 |
| check | sdu type is | 0 |
| check | area is | 100 |
| check | service is | 1 |
| check | operation is | 100 |
| check | area version is | 1 |
| check | error flag is | 0 |
| ensure | check qos | Best Effort |
| ensure | check session | Live |
| ensure | check secondary apid |
| ensure | check secondary apid qualifier |
| ensure | check transaction id |
| check | source id flag is | 1 |
| check | destination id flag is | 1 |
| check | priority flag is | 1 |
| check | timestamp flag is | 1 |
| check | network zone flag is | 1 |
| check | session name flag is | 1 |
| check | domain flag is | 1 |
| check | authentication id flag is | 1 |
| ensure | read source id |
| ensure | read destination id |
| ensure | check uri from |
| ensure | check uri to |
| check | priority is | 1 |
| ensure | check timestamp |
| check | network zone is | NetworkZone |
| check | session name is | LIVE |
| ensure | check domain id |
| ensure | check authentication id |

#### Body element check

These assertions are checked for every TM/TC combination, every interaction pattern and stage.

| scenario | body element | type | encoded as nullable element |
| --- | --- | --- | --- |
| check | presence flag is | 1 |
| read element IPTestDefinition |

#### Body ending check

These assertions are checked for every TM/TC combination, every interaction pattern and stage.

| scenario | body ends here |
| --- | --- |
| check | buffer remaining size is | 0 |

#### Unknown URI check

These assertions are checked for every TM/TC combination, and every interaction pattern allowing to return an error.

| scenario | test interaction pattern | pattern | with unknown uri to |
| --- | --- | --- | --- |
| ensure | pattern initiation for | SUBMIT | with unknown uri to | malspp:123/123/0 |
| ensure | select last received message |
| ensure | received message mal header field is error message |
| check | received message body contains error | destination unknown |
| check | received message mal header field uri from is | malspp:123/123/0 |

### PubSub test case

This test case reuses the MAL prototype test procedure that checks the MAL message header in every stage of the Publish-Subscribe interaction.

However the Pub/Sub error tests could not be reused because the MAL prototype artificially produces error messages at the test transport level, so above the MAL/SPP layer, preventing from getting the SPP packets. A specific broker handler has been implemented in order to raise Register, Notify and Publish Register errors. This broker is deployed on the consumer side.

Specific providers and consumers have also been implemented.

A provider is launched on the consumer side in order to initiate a Publish Register with the error broker.

Several APIDs and APID qualifiers are used:

- 248/2: IPTest providers or brokers sending TC packets

- 348/4: IPTest providers or brokers sending TC packets

- 247/1: IPTest consumers, brokers and publishers sending TC packets and expecting to receive TC packets

- 347/3: IPTest consumers, brokers and publishers sending TC packets and expecting to receive TM packets

- 447/5: IPTest consumers, brokers and publishers sending TM packets and expecting to receive TC packets

- 547/7: IPTest consumers, brokers and publishers sending TM packets and expecting to receive TM packets

The consumer creates subscriptions from the following parameters:

- subscription identifier: 'sub1'

- authentication identifier: '0x00,0x01'

- priority: 1

- domain: 'Test,Domain'

- networkZone: '!-NetworkZone-!'

- entity expression: 'A,null,null,null'

- only on change: false

All the tests are executed once with a private broker and a second time with a shared one.

The shared broker is created one the consumer side because. In this way, it enables the test to intercept the messages going out of the provider's publisher.

Some headers are only checked with the shared broker (deployed on the consumer side):

- Publish

- Publish Register

- Publish Register ack

- Publish Register Error

- Publish Deregister

- Publish Deregister ack

The Publish Error is triggered by publishing an entity that has not been registered: 'B,null,null,null'.

The Register Error is triggered by registering to the error broker.

The Publish Register Error is triggered by registering to the error broker.

The Notify Error is triggered by requesting the error provider to publish updates.

The MAL assertions are still checked:

The provider assertions are described in the IPTest service specification (section 5.1).

The consumer assertions are described in annex B.

The MAL/SPP assertions are specified in this script. They check the MAL header mapping statements for the Pub/Sub interaction.

#### Final results

| script | mal spp pubsub test |
| --- | --- |
| test mal spp pubsub with consumer tc | true | and provider tc | true |
| test mal spp pubsub with consumer tc | true | and provider tc | false |
| test mal spp pubsub with consumer tc | false | and provider tc | true |
| test mal spp pubsub with consumer tc | false | and provider tc | false |

#### Primary header check

These assertions are checked for every TM/TC combination, and every Publish-Subscribe stage.

| scenario | primary header |
| --- | --- |
| check | packet version number is | 0 |
| check space packet type |
| check | secondary header flag is | 1 |
| ensure | packet data length is length of packet data field minus one |

#### Secondary header check

These assertions are checked for every TM/TC combination, every Publish-Subscribe stage.

| scenario | secondary header |
| --- | --- |
| check | version is | 0 |
| check | sdu type is | 15 |
| check | area is | 100 |
| check | service is | 1 |
| check | operation is | 105 |
| check | area version is | 1 |
| check | error flag is | 0 |
| ensure | check qos | Best Effort |
| ensure | check session | Live |
| ensure | check secondary apid |
| ensure | check secondary apid qualifier |
| ensure | check transaction id |
| check | source id flag is | 1 |
| check | destination id flag is | 1 |
| check | priority flag is | 1 |
| check | timestamp flag is | 1 |
| check | network zone flag is | 1 |
| check | session name flag is | 1 |
| check | domain flag is | 1 |
| check | authentication id flag is | 1 |
| ensure | read source id |
| ensure | read destination id |
| ensure | check uri from |
| ensure | check uri to |
| ensure | read segment counter if segmented |
| check | priority is | 1 |
| ensure | check timestamp |
| check | network zone is | NetworkZone |
| check | session name is | LIVE |
| ensure | check domain id |
| ensure | check authentication id |

#### Publish Register Body element check

These assertions are checked for every TM/TC combination.

| scenario | body element | type | encoded as element |
| --- | --- | --- | --- |
| read element EntityKeyList |

#### Register body element check

These assertions are checked for every TM/TC combination.

| scenario | body element | type | encoded as element |
| --- | --- | --- | --- |
| read element Subscription |

#### Publish body element check

These assertions are checked for every TM/TC combination.

| scenario | body element | type | encoded as element |
| --- | --- | --- | --- |
| read element Identifier |
| scenario | body element | type | encoded as element |
| read element UpdateHeaderList |
| scenario | body element | type | encoded as element |
| read element list of update value type |

#### Publish Error body element check

These assertions are checked for every TM/TC combination.

| scenario | body element encoded as UInteger |
| --- | --- |
| ensure | read UInteger |
| scenario | body element | type | encoded as nullable element |
| check | presence flag is | 1 |
| read element element |

#### Deregister body element check

These assertions are checked for every TM/TC combination.

| scenario | body element | type | encoded as element |
| --- | --- | --- | --- |
| read element IdentifierList |

#### Publish Deregister body element check

These assertions are checked for every TM/TC combination.

| scenario | body element encoded as empty |
| --- | --- |
| body ends here |

#### Register Error body element check

These assertions are checked for every TM/TC combination.

| scenario | body element encoded as UInteger |
| --- | --- |
| ensure | read UInteger |
| scenario | body element null encoded as nullable element |
| check | presence flag is | 0 |

#### Notify Error body element check

These assertions are checked for every TM/TC combination.

| scenario | body element encoded as UInteger |
| --- | --- |
| ensure | read UInteger |
| scenario | body element null encoded as nullable element |
| check | presence flag is | 0 |

#### Publish Register Error body element check

These assertions are checked for every TM/TC combination.

| scenario | body element encoded as UInteger |
| --- | --- |
| ensure | read UInteger |
| scenario | body element null encoded as nullable element |
| check | presence flag is | 0 |

#### Publish body element with an abstract update (service defined) check

These assertions are checked for every TM/TC combination.

| scenario | body element | type | encoded as element |
| --- | --- | --- | --- |
| read element UpdateHeaderList |
| scenario | body element concrete encoded for publish message |
| publish update list is for | concrete | update value type |
| scenario | body element abstract service-defined encoded for publish message |
| note | update value type is TestUpdate |
| check element short form area | 100 | and service | 1 | and type | -8 |
| publish update list is for | abstract service-defined | update value type |

#### Publish body element with an abstract update (non service defined) check

These assertions are checked for every TM/TC combination.

| scenario | body element | type | encoded as element |
| --- | --- | --- | --- |
| read element UpdateHeaderList |
| scenario | body element concrete encoded for publish message |
| publish update list is for | concrete | update value type |
| scenario | body element abstract non-service defined encoded for publish message |
| note | update value type is MAL::Integer |
| check element short form area | 1 | and service | 0 | and type | -11 |
| publish update list is for | abstract non-service defined | update value type |

#### Body ending check

These assertions are checked for every TM/TC combination, every Publish-Subscribe stage.

| scenario | body ends here |
| --- | --- |
| check | buffer remaining size is | 0 |

#### Unknown URI check

These assertions are checked for every TM/TC combination, and every stage allowing to return an error: Register, Publish Register, Deregister, Publish Deregister.

| check | received message body contains error | destination unknown |
| --- | --- | --- |
| check | received message mal header field uri from is | malspp:123/123/0 |

### MAL message body mapping

This test case reuses the data type MAL test scenario and checks the body element order.

| scenario | check body element order |
| --- | --- |
| check | explicit multi return works | OK |
| note | skip first packet setTestDataOffset |
| ensure | select sent packet at | 1 |
| check | presence flag is | 1 |
| ensure | check uoctet |
| check | presence flag is | 1 |
| ensure | check ushort |
| check | presence flag is | 1 |
| ensure | check uinteger |
| check | presence flag is | 1 |
| ensure | check ulong |
| ensure | reset spp interceptor |

### Empty body Test Case

| script | mal spp data type test |
| --- | --- |
| ensure | reset spp interceptor |
| ensure | test empty body |
| ensure | select sent packet at | 0 |
| ensure | mal message body is empty |
| ensure | reset spp interceptor |

### MAL message segmentation test case

All test services are extensions of other MAL/SPP services and/or MAL services.

Message segmentation is tested using three providers and three consumers:

- APID qualifier/APID 248/2: DataTest service provider - configured to maximum packet size

- APID qualifier/APID 247/1: DataTest service consumer

- APID qualifier/APID 648/2: DataTest service provider - configured to limited packet size

- APID qualifier/APID 647/1: DataTest service consumer

- APID qualifier/APID 648/4: IPTest service provider - configured to medium packet size

- APID qualifier/APID 647/3: IPTest service consumer

The testData operation of the DataTest service is used to check proper sending and reception of a Blob that encodes to a packet smaller than PACKET_DATA_FIELD_SIZE_LIMIT of 65536 bytes (the maximum).

The testBlobData operation of the DataTest service is used to check proper sending and reception of a Blob that encodes to three fully filled and one partially filled packet for the maximum possible value of PACKET_DATA_FIELD_SIZE_LIMIT.

In both cases the Blob is statically known to the provider and consumer side. The Blob content is specified by the test so the Test Consumer and Provider know what the expected Blob value is.

The testStringData operation of the DataTest service is used with endpoints configured for a limited packet data field size of 27 bytes. Three cases are tested:

- secondary header: 23 bytes; body: 2 bytes; one packet, no error expected.

- secondary header: 23 bytes + 4 bytes for counter (because of message segmentation); body: 6 bytes; INTERNAL error expected.

- secondary header: 24 bytes + 4 bytes for counter (because of message segmentation); body: 6 bytes; INTERNAL error expected.

Secondary header size is set by per-message QoS property flag Priority. All other flags (except Source and Destination id flag) are set to false.

Correct sequencing of Space Packets is ensured by scrambling outgoing packets in certain patterns.

Packets are either scrambled on the consumer side, on the provider side or on both sides. In order to enabling scrambling on the provider side the IPTest submitMulti operation is invoked with the scramble pattern. Scrambling is realized in the packet interceptor by collecting packets for an interval of one second starting with the first packet. These are scrambled according to a cyclic pattern given by the test. This pattern gives the indices of the packets that shall be sent out next. Indices referring to non-existent packets (because less packets were collected during the interval) are skipped. A negative index means to drop the packet. For test purposes it is assumed that a mission-defined timeout is longer than the one second collection interval.

The procedure to test for correct counter selection does not need to scramble packets. The progressNulti operation of the IPTest service is used to check correct selection of segment counters by invoking the pattern twice and triggering updates and responses using the sendMulti operation of the same service. By invoking the pattern twice on the same service the only difference is in the transaction id. It is checked that different counters are used, when transaction ids are different and that same counters are used when all fields of clause 4.4.9e are the same.

| script | mal spp segmentation test |
| --- | --- |
| test message segmentation with scrambling pattern | [] |
| test message segmentation with scrambling pattern | [1, 0] |
| test message segmentation with scrambling pattern | [9, 0, 4, 3, 6, 1, 2, 8, 7, 5] |
| set scrambling for remote reception to | [] | and for local reception to | [] |
| check segment counter selection |
| check dropped packet |
| note | mission-defined timeout is assumed to be less than 8 seconds |
| check timeout with | 8 | seconds delay and expect | 1 | updates |
| check timeout with | 2 | seconds delay and expect | 2 | updates |

### QoS properties test case

This test case uses the Request interaction pattern in order to test that the !-QoS-! properties set at the provider side are effective in the Response MAL message.

One test procedure has been defined for every flag:

- authenticationIdFlagTest

- domainFlagTest

- networkZoneFlagTest

- priorityFlagTest

- sessionNameFlagTest

- timestampFlagTest

The provider has to set to false the value of the QoS property specified by the procedure.

Two cases are tested depending on the provider packet type (TC or TM).

- If the provider sends TC packets, then the missing field is assigned according to the consumer APID and APID qualifier.

- If the provider sends TM packets, then the missing field is assigned according to the provider APID and APID qualifier.

In the first case, the default MAL/SPP values are assigned because the consumer (APID 247/1) does not specify the mapping configuration parameters (see section 8.1).

In the second case, the mapping configuration parameters of the provider (APID 348/4) are assigned.

#### Final results

| script | qos properties test |
| --- | --- |
| test qos properties with provider tc | true |
| test qos properties with provider tc | false |

#### Flags check

These assertions are checked for every QoS property assigned with TRUE/FALSE.

| scenario | test qos properties |
| --- | --- |
| check space packet type |
| check | version is | 0 |
| check | sdu type is | 4 |
| check | area is | 100 |
| check | service is | 1 |
| check | operation is | 102 |
| check | area version is | 1 |
| check | error flag is | 0 |
| ensure | check qos | Best Effort |
| ensure | check session | Live |
| ensure | check secondary apid |
| ensure | check secondary apid qualifier |
| ensure | check transaction id |
| check | source id flag is | 1 |
| check | destination id flag is | 1 |
| check | priority flag is | 1 |
| check | timestamp flag is | 1 |
| check | network zone flag is | 1 |
| check | session name flag is | 1 |
| check | domain flag is | 1 |
| check | authentication id flag is | 0 |
| ensure | read source id |
| ensure | read destination id |
| ensure | check uri from |
| ensure | check uri to |

### Source Destination Id test case

This test uses the Request interaction pattern in order to test that the source  and destination identifiers can be omitted in the MAL message header fields 'URI From' and 'URI To' and that the source and destination id flags are set to false in this case.

The consumer is configured in order not to append the optional identifier at the  end of its URI. A TC/TC Request interaction is initiated and the source/destination id flags are checked in the request and response MAL messages:

- the source id flag should be down in the request and up in the response.

- the destination id flag should be up in the request and down in the response.

#### Source id flag check

| secondary header sdu type | 3 | and source id flag | 0 | and destination id flag | 1 |
| --- | --- | --- | --- | --- | --- |

#### Destination id flag check

| secondary header sdu type | 4 | and source id flag | 1 | and destination id flag | 0 |
| --- | --- | --- | --- | --- | --- |

### Transmit Request test case

A template message is created and sent using the send operation of the IPTest service:

- APID qualifier/APID 648/4: IPTest service provider

- APID qualifier/APID 647/3: IPTest service consumer

The MAL message header fields of the template message are modified and correct behaviour of the transmit request is checked by directly invoking the transmit request on the transport API. The provider does not do anything. Errors on provider side are ignored, because they are not relevant to the test.

| script | transmit request test |
| --- | --- |
| check null mal header field |
| check uri from format |
| check uri to format |
| check space packet sending request error |
| check transmit multiple |
| check transmit multiple error |

### Transmit QoS Properties Test case

Several APIDs and APID qualifiers are used:

- 248/2: IPTest providers sending TC packets

- 348/4: IPTest providers sending TM packets

- 247/1: IPTest consumers sending TC packets and expecting to receive TC packets

- 347/3: IPTest consumers sending TC packets and expecting to receive TM packets

- 447/5: IPTest consumers sending TM packets and expecting to receive TC packets

- 547/7: IPTest consumers sending TM packets and expecting to receive TM packets

#### Final results

| script | mal spp pattern test |
| --- | --- |
| test transmit qos properties with consumer tc | true | and provider tc | true |
| test transmit qos properties with consumer tc | true | and provider tc | false |
| test transmit qos properties with consumer tc | false | and provider tc | true |
| test transmit qos properties with consumer tc | false | and provider tc | false |

#### QoS properties transmission check

These assertions are checked for every TM/TC combination.

| scenario | test transmit qos properties with consumer tc | consumerTc | and provider tc | providerTc |
| --- | --- | --- | --- | --- |
| ensure | reset spp interceptor |
| ensure | consumer packet is tc | true |
| ensure | provider packet is tc | true |
| ensure | initiate send pattern with qos | Best Effort | and session | Live |
| ensure | select sent packet at | 0 |
| ensure | check transmit qos properties |
| ensure | reset spp interceptor |

### MAL SPP transport

| script | mal spp transport test |
| --- | --- |
| ensure | supports qos level | Best Effort | is | True |
| ensure | supports qos level | Assured | is | True |
| ensure | supports qos level | Queued | is | True |
| ensure | supports qos level | Timely | is | True |
| ensure | supports interaction type | Send | is | True |
| ensure | supports interaction type | Submit | is | True |
| ensure | supports interaction type | Request | is | True |
| ensure | supports interaction type | Invoke | is | True |
| ensure | supports interaction type | Progress | is | True |
| ensure | supports interaction type | Pub/Sub | is | False |

## MAL Data Type encoding scenario

### Attribute test case

This test case checks the encoding format of every MAL attribute.

The local APID and APID qualifier are respectively equal to 1 and 247.

The remote APID and APID qualifier are respectively equal to 2 and 248.

The time encoding formats are specified according to the APID and APID qualifier, as follows:

- Time: 0001 1111 (CUC, CCSDS epoch, 4 bytes, 3 bytes)

- !-FineTime-!: 1010 1111 0000 1000 (CUC, agency epoch, 4 bytes, 3+2 bytes)

- Duration: 0001 1100 (CUC, no fractional time)

| scenario | check every attribute |
| --- | --- |
| ensure | reset spp interceptor |
| check | explicit duration type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check duration |
| ensure | reset spp interceptor |
| check | explicit Fine Time type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check fine time |
| ensure | reset spp interceptor |
| check | explicit Identifier type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check identifier |
| ensure | reset spp interceptor |
| check | explicit Time type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check time |
| ensure | reset spp interceptor |
| check | explicit URI type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check uri |
| ensure | reset spp interceptor |
| check | explicit Blob type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check blob |
| ensure | reset spp interceptor |
| check | explicit Boolean type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check boolean |
| ensure | reset spp interceptor |
| check | explicit Octet type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check octet |
| ensure | reset spp interceptor |
| check | explicit Double type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check double |
| ensure | reset spp interceptor |
| check | explicit Float type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check float |
| ensure | reset spp interceptor |
| check | explicit Integer type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check integer |
| ensure | reset spp interceptor |
| check | explicit Long type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check long |
| ensure | reset spp interceptor |
| check | explicit Short type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check short |
| ensure | reset spp interceptor |
| check | explicit String type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check string |
| ensure | reset spp interceptor |
| check | explicit UOctet type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check uoctet |
| ensure | reset spp interceptor |
| check | explicit UInteger type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check uinteger |
| ensure | reset spp interceptor |
| check | explicit ULong type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check ulong |
| ensure | reset spp interceptor |
| check | explicit UShort type works | OK |
| ensure | select sent packet at | 0 |
| check | presence flag is | 1 |
| ensure | check ushort |
| ensure | reset spp interceptor |

### Composite test case

This test case checks the encoding format of a MAL composite.

| script | mal spp data type test |
| --- | --- |
| check field order |
| check composite inheritance |

### Element test case

This test case checks the encoding format of a MAL element.

| script | mal spp data type test |
| --- | --- |
| check a composite with a field typed MAL::Attribute |
| check a composite sent as a MAL::Element |
| check a composite sent as a MAL::Composite |
| check a composite sent as an abstract composite |
| check a composite defined by a service and sent as a MAL::Element |
| check an attribute sent as a MAL::Element |
| check an attribute sent as a MAL::Attribute |
| check an attribute list sent as a MAL::Element list |
| check an attribute list sent as a MAL::Attribute list |
| check an attribute list sent as a MAL::Composite |
| check a composite list sent as a MAL::Element list |
| check a composite list sent as a MAL::Composite list |
| check a composite list sent as an abstract composite list |
| check a composite list sent as a MAL::Composite |
| check every attribute |
| check an enumerated sent as a MAL::Element |
| check a composite with a field typed as a list |

### Enumeration test case

This test case checks the encoding format of a MAL enumeration.

| script | mal spp data type test |
| --- | --- |
| check first element in an enumeration |
| check first and second elements in an enumeration |
| check an enumerated sent as a MAL::Element |

### List test case

This test case checks the encoding format of a MAL list.

| script | mal spp data type test |
| --- | --- |
| check list format and elements order |

### Nullable element test case

This test case checks the encoding format of a nullable MAL element.

| script | mal spp data type test |
| --- | --- |
| check presence flag |

### Time code format test case

This test case checks the time code formats and the MAL time types (Duration, Time and FineTime) .

| script | mal spp data type test |
| --- | --- |
| note | Using CUC time code format and other default settings |
| ensure | use default configuration | true |
| check every attribute affected by time code formats |
| note | Using CDS time code format and alternate units, epochs and time scales |
| ensure | use default configuration | false |
| check every attribute affected by time code formats |

### Varint supported test case

This test case checks the mapping configuration parameter ‘VARINT_SUPPORTED’.

| script | mal spp data type test |
| --- | --- |
| note | varintSupported is true |
| ensure | use default configuration | true |
| check every attribute affected by varintSupported |
| note | varintSupported is false |
| ensure | use default configuration | false |
| check every attribute affected by varintSupported |

# MALPrototype Service Specification

## Service: IPTest

### General

Table 1-1:  IPTest Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| MALPrototype | IPTest | 100 | 1 | 1 |
| Interaction Pattern | Operation Identifier | Operation Number | Support in Replay | Capability Set |
| SEND | send | 100 | No | 100 |
| SUBMIT | testSubmit | 101 | No |  |
| REQUEST | request | 102 | No |  |
| INVOKE | invoke | 103 | No |  |
| PROGRESS | progress | 104 | No |  |
| PUBLISH-SUBSCRIBE | monitor | 105 | No |  |
| REQUEST | getResult | 106 | No | 101 |
| SUBMIT | publishUpdates | 108 | No | 102 |
| SUBMIT | publishRegister | 110 | No |  |
| SUBMIT | publishDeregister | 111 | No |  |
| SUBMIT | testMultipleNotify | 112 | No |  |
| SEND | sendMulti | 113 | No | 103 |
| SUBMIT | submitMulti | 114 | No |  |
| REQUEST | requestMulti | 115 | No |  |
| INVOKE | invokeMulti | 116 | No |  |
| PROGRESS | progressMulti | 117 | No |  |
| PUBLISH-SUBSCRIBE | monitorMulti | 118 | No |  |
| REQUEST | testRequestEmptyBody | 120 | No | 104 |
| INVOKE | testInvokeEmptyBody | 121 | No |  |
| PROGRESS | testProgressEmptyBody | 122 | No |  |

### OPERATION: send

#### General

This operation cleans the assertions table and check that the header of the received message is the same as the one expected (see 4.1.1).

| Operation Identifier | send |
| --- | --- |
| Interaction Pattern | SEND |
| Pattern Sequence | Message | Body Type |
| IN | SEND | IPTestDefinition |

#### Structures

#### Errors

The operation cannot return any errors.

### OPERATION: testSubmit

#### General

This operation cleans the assertions table and checks that the header of the received message is the same as the one expected (see 4.1.1). Moreover it triggers the transitions specified by the IPTestDefinition (see 3.1.2).

| Operation Identifier | testSubmit |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | IPTestDefinition |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: TEST_ERROR

Fake error for testing.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TEST_ERROR | 70000 | Not Used |

### OPERATION: request

#### General

This operation cleans the assertions table and checks that the header of the received message is the same as the one expected (see 4.1.1). Moreover it triggers the transitions specified by the IPTestDefinition (see 3.1.2).

| Operation Identifier | request |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | IPTestDefinition |
| OUT | RESPONSE | MAL::String |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: TEST_ERROR

Fake error for testing.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TEST_ERROR | 70000 | Not Used |

### OPERATION: invoke

#### General

This operation cleans the assertions table and checks that the header of the received message is the same as the one expected (see 4.1.1). Moreover it triggers the transitions specified by the IPTestDefinition (see 4.1.2).

| Operation Identifier | invoke |
| --- | --- |
| Interaction Pattern | INVOKE |
| Pattern Sequence | Message | Body Type |
| IN | INVOKE | IPTestDefinition |
| OUT | ACK | MAL::String |
| OUT | RESPONSE | MAL::String |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: TEST_ERROR

Fake error for testing.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TEST_ERROR | 70000 | Not Used |

### OPERATION: progress

#### General

This operation cleans the assertions table and checks that the header of the received message is the same as the one expected (see 4.1.1). Moreover it triggers the transitions specified by the IPTestDefinition (see 4.1.2).

| Operation Identifier | progress |
| --- | --- |
| Interaction Pattern | PROGRESS |
| Pattern Sequence | Message | Body Type |
| IN | PROGRESS | IPTestDefinition |
| OUT | ACK | MAL::String |
| OUT | UPDATE | MAL::Integer |
| OUT | RESPONSE | MAL::String |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: TEST_ERROR

Fake error for testing.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TEST_ERROR | 70000 | Not Used |

### OPERATION: monitor

#### General

This operation initiates a Pub/Sub interaction. It is not implemented by the service provider but by a broker.

| Operation Identifier | monitor |
| --- | --- |
| Interaction Pattern | PUBLISH-SUBSCRIBE |
| Pattern Sequence | Message | Body Type |
| OUT | PUBLISH/NOTIFY | TestUpdate |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: UNKNOWN

One or more of the entities identified in the registration do not exist.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

### OPERATION: getResult

#### General

This operation returns an IPTestResult.

| Operation Identifier | getResult |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | IPTestResult |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: publishUpdates

#### General

This operation cleans the assertions table, publishes an update as specified by the parameter TestPublishUpdate and checks the header of the Publish message (see 4.1.3). Moreover if an error is expected by the TestPublishUpdate then the operation hangs until a Publish error is raised or a timer ends (see 4.1.10). The header of the Publish error message is checked (see 4.1.4).

| Operation Identifier | publishUpdates |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | TestPublishUpdate |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: publishRegister

#### General

This operation cleans the assertions table, registers a publisher as specified by the parameter TestPublishRegister and checks the header of the Publish Register message (see 4.1.5). Moreover if no error is expected by the TestPublishRegister, it checks the header of the Publish Register acknowledgement message (see 4.1.6). Otherwise it checks the header of the Publish Register error message (see 4.1.7).

| Operation Identifier | publishRegister |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | TestPublishRegister |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: publishDeregister

#### General

This operation cleans the assertions table, registers a publisher as specified by the parameter TestPublishDeregister and checks the header of the Publish Deregister message (see 4.1.5). Moreover if no error is expected by the TestPublishDeregister, it checks the header of the Publish Deregister acknowledgement message (see 4.1.8). Otherwise it checks the header of the Publish Deregister error message (see 4.1.9).

| Operation Identifier | publishDeregister |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | TestPublishDeregister |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testMultipleNotify

#### General

| Operation Identifier | testMultipleNotify |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | TestPublishUpdate |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: sendMulti

#### General

This operation cleans the assertions table and check that the header of the received message is the same as the one expected (see 4.1.1).

| Operation Identifier | sendMulti |
| --- | --- |
| Interaction Pattern | SEND |
| Pattern Sequence | Message | Body Type |
| IN | SEND | IPTestDefinition MAL::Element |

#### Structures

#### Errors

The operation cannot return any errors.

### OPERATION: submitMulti

#### General

This operation cleans the assertions table and checks that the header of the received message is the same as the one expected (see 4.1.1). Moreover it triggers the transitions specified by the IPTestDefinition (see 3.1.2).

| Operation Identifier | submitMulti |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | IPTestDefinition MAL::Element |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: TEST_ERROR

Fake error for testing.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TEST_ERROR | 70000 | Not Used |

### OPERATION: requestMulti

#### General

This operation cleans the assertions table and checks that the header of the received message is the same as the one expected (see 4.1.1). Moreover it triggers the transitions specified by the IPTestDefinition (see 3.1.2).

| Operation Identifier | requestMulti |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | IPTestDefinition MAL::Element |
| OUT | RESPONSE | MAL::String MAL::Element |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: TEST_ERROR

Fake error for testing.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TEST_ERROR | 70000 | Not Used |

### OPERATION: invokeMulti

#### General

This operation cleans the assertions table and checks that the header of the received message is the same as the one expected (see 4.1.1). Moreover it triggers the transitions specified by the IPTestDefinition (see 4.1.2).

| Operation Identifier | invokeMulti |
| --- | --- |
| Interaction Pattern | INVOKE |
| Pattern Sequence | Message | Body Type |
| IN | INVOKE | IPTestDefinition MAL::Element |
| OUT | ACK | MAL::String MAL::Element |
| OUT | RESPONSE | MAL::String MAL::Element |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: TEST_ERROR

Fake error for testing.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TEST_ERROR | 70000 | Not Used |

### OPERATION: progressMulti

#### General

This operation cleans the assertions table and checks that the header of the received message is the same as the one expected (see 4.1.1). Moreover it triggers the transitions specified by the IPTestDefinition (see 4.1.2).

| Operation Identifier | progressMulti |
| --- | --- |
| Interaction Pattern | PROGRESS |
| Pattern Sequence | Message | Body Type |
| IN | PROGRESS | IPTestDefinition MAL::Element |
| OUT | ACK | MAL::String MAL::Element |
| OUT | UPDATE | MAL::Integer MAL::Element |
| OUT | RESPONSE | MAL::String MAL::Element |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: TEST_ERROR

Fake error for testing.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| TEST_ERROR | 70000 | Not Used |

### OPERATION: monitorMulti

#### General

This operation initiates a Pub/Sub interaction. It is not implemented by the service provider but by a broker.

| Operation Identifier | monitorMulti |
| --- | --- |
| Interaction Pattern | PUBLISH-SUBSCRIBE |
| Pattern Sequence | Message | Body Type |
| OUT | PUBLISH/NOTIFY | TestUpdate MAL::Element |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: UNKNOWN

One or more of the entities identified in the registration do not exist.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

### OPERATION: testRequestEmptyBody

#### General

This operation checks that an empty body can be sent and received explicitly for a request pattern

| Operation Identifier | testRequestEmptyBody |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | IPTestDefinition |
| OUT | RESPONSE |  |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testInvokeEmptyBody

#### General

This operation checks that an empty body can be sent and received explicitly for a request pattern

| Operation Identifier | testInvokeEmptyBody |
| --- | --- |
| Interaction Pattern | INVOKE |
| Pattern Sequence | Message | Body Type |
| IN | INVOKE | IPTestDefinition |
| OUT | ACK |  |
| OUT | RESPONSE |  |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testProgressEmptyBody

#### General

This operation checks that an empty body can be sent and received explicitly for a request pattern

| Operation Identifier | testProgressEmptyBody |
| --- | --- |
| Interaction Pattern | PROGRESS |
| Pattern Sequence | Message | Body Type |
| IN | PROGRESS | IPTestDefinition |
| OUT | ACK |  |
| OUT | UPDATE |  |
| OUT | RESPONSE |  |

#### Structures

#### Errors

The operation does not return any errors.

## Service: DataTest

### General

Table 1-1:  DataTest Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| MALPrototype | DataTest | 100 | 2 | 1 |
| Interaction Pattern | Operation Identifier | Operation Number | Support in Replay | Capability Set |
| SUBMIT | setTestDataOffset | 99 | No | 100 |
| REQUEST | testData | 100 | No |  |
| REQUEST | testDataBlob | 101 | No |  |
| REQUEST | testDataBoolean | 102 | No |  |
| REQUEST | testDataDouble | 103 | No |  |
| REQUEST | testDataDuration | 104 | No |  |
| REQUEST | testDataFineTime | 105 | No |  |
| REQUEST | testDataFloat | 106 | No |  |
| REQUEST | testDataIdentifier | 107 | No |  |
| REQUEST | testDataInteger | 108 | No |  |
| REQUEST | testDataLong | 109 | No |  |
| REQUEST | testDataOctet | 110 | No |  |
| REQUEST | testDataShort | 111 | No |  |
| REQUEST | testDataString | 112 | No |  |
| REQUEST | testDataTime | 113 | No |  |
| REQUEST | testDataURI | 114 | No |  |
| REQUEST | testDataComposite | 115 | No |  |
| REQUEST | testDataEnumeration | 116 | No |  |
| REQUEST | testDataList | 117 | No |  |
| REQUEST | testDataUInteger | 118 | No |  |
| REQUEST | testDataULong | 119 | No |  |
| REQUEST | testDataUOctet | 120 | No |  |
| REQUEST | testDataUShort | 121 | No |  |
| REQUEST | testExplicitMultiReturn | 122 | No |  |
| REQUEST | testAbstractMultiReturn | 123 | No |  |
| REQUEST | testEmptyBody | 124 | No |  |
| REQUEST | testMalAttribute | 125 | No |  |
| REQUEST | testMalComposite | 126 | No |  |
| REQUEST | testAbstractComposite | 127 | No |  |
| REQUEST | testMalAttributeList | 128 | No |  |
| REQUEST | testMalElementList | 129 | No |  |
| REQUEST | testMalCompositeList | 130 | No |  |
| REQUEST | testAbstractCompositeList | 131 | No |  |

### OPERATION: setTestDataOffset

#### General

This operation sets the index into the test list for the testData operation. Passing non positive values resets it to the start of the list.

| Operation Identifier | setTestDataOffset |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | MAL::Integer |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testData

#### General

The 'testData' operation allows a consumer to check that a data is correctly decoded on the provider side. The provider needs to statically know the list of data that the consumer is going to send. The consumer selects the data in the same order as the list and calls the operation 'testData'. The provider keeps the index of the currently selected data from the static list. When the operation 'testData' is called, the provider checks that the received data is equal to the selected data from the list. If the equality test fails, then the error DATA_ERROR is raised otherwise the provider returns the sent data.

| Operation Identifier | testData |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataBlob

#### General

This operation checks that a basic Blob type can be sent and received explicitly

| Operation Identifier | testDataBlob |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Blob |
| OUT | RESPONSE | MAL::Blob |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataBoolean

#### General

This operation checks that a basic Boolean type can be sent and received explicitly

| Operation Identifier | testDataBoolean |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Boolean |
| OUT | RESPONSE | MAL::Boolean |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataDouble

#### General

This operation checks that a basic Double type can be sent and received explicitly

| Operation Identifier | testDataDouble |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Double |
| OUT | RESPONSE | MAL::Double |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataDuration

#### General

This operation checks that a basic Duration type can be sent and received explicitly

| Operation Identifier | testDataDuration |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Duration |
| OUT | RESPONSE | MAL::Duration |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataFineTime

#### General

This operation checks that a basic FineTime type can be sent and received explicitly

| Operation Identifier | testDataFineTime |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::FineTime |
| OUT | RESPONSE | MAL::FineTime |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataFloat

#### General

This operation checks that a basic Float type can be sent and received explicitly

| Operation Identifier | testDataFloat |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Float |
| OUT | RESPONSE | MAL::Float |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataIdentifier

#### General

This operation checks that a basic Identifier type can be sent and received explicitly

| Operation Identifier | testDataIdentifier |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Identifier |
| OUT | RESPONSE | MAL::Identifier |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataInteger

#### General

This operation checks that a basic Integer type can be sent and received explicitly

| Operation Identifier | testDataInteger |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Integer |
| OUT | RESPONSE | MAL::Integer |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataLong

#### General

This operation checks that a basic Long type can be sent and received explicitly

| Operation Identifier | testDataLong |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Long |
| OUT | RESPONSE | MAL::Long |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataOctet

#### General

This operation checks that a basic Octet type can be sent and received explicitly

| Operation Identifier | testDataOctet |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Octet |
| OUT | RESPONSE | MAL::Octet |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataShort

#### General

This operation checks that a basic Short type can be sent and received explicitly

| Operation Identifier | testDataShort |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Short |
| OUT | RESPONSE | MAL::Short |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataString

#### General

This operation checks that a basic String type can be sent and received explicitly

| Operation Identifier | testDataString |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::String |
| OUT | RESPONSE | MAL::String |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataTime

#### General

This operation checks that a basic Time type can be sent and received explicitly

| Operation Identifier | testDataTime |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Time |
| OUT | RESPONSE | MAL::Time |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataURI

#### General

This operation checks that a basic URI type can be sent and received explicitly

| Operation Identifier | testDataURI |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::URI |
| OUT | RESPONSE | MAL::URI |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataComposite

#### General

This operation checks that a composite type can be sent and received explicitly

| Operation Identifier | testDataComposite |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | Assertion |
| OUT | RESPONSE | Assertion |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataEnumeration

#### General

This operation checks that a enumeration type can be sent and received explicitly

| Operation Identifier | testDataEnumeration |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::SessionType |
| OUT | RESPONSE | MAL::SessionType |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataList

#### General

This operation checks that a list type can be sent and received explicitly

| Operation Identifier | testDataList |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | List<Assertion> |
| OUT | RESPONSE | List<Assertion> |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataUInteger

#### General

This operation checks that a basic UInteger type can be sent and received explicitly

| Operation Identifier | testDataUInteger |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::UInteger |
| OUT | RESPONSE | MAL::UInteger |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataULong

#### General

This operation checks that a basic ULong type can be sent and received explicitly

| Operation Identifier | testDataULong |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::ULong |
| OUT | RESPONSE | MAL::ULong |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataUOctet

#### General

This operation checks that a basic UOctet type can be sent and received explicitly

| Operation Identifier | testDataUOctet |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::UOctet |
| OUT | RESPONSE | MAL::UOctet |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testDataUShort

#### General

This operation checks that a basic UShort type can be sent and received explicitly

| Operation Identifier | testDataUShort |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::UShort |
| OUT | RESPONSE | MAL::UShort |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testExplicitMultiReturn

#### General

This operation checks that multiple types can be sent and received explicitly

| Operation Identifier | testExplicitMultiReturn |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::UOctet MAL::UShort MAL::UInteger MAL::ULong |
| OUT | RESPONSE | MAL::UOctet MAL::UShort MAL::UInteger MAL::ULong |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testAbstractMultiReturn

#### General

This operation checks that multiple types with a final abstract type can be sent and received explicitly

| Operation Identifier | testAbstractMultiReturn |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::UOctet MAL::UShort MAL::UInteger MAL::Element |
| OUT | RESPONSE | MAL::UOctet MAL::UShort MAL::UInteger MAL::Element |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testEmptyBody

#### General

This operation checks that an empty body can be sent and received explicitly

| Operation Identifier | testEmptyBody |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST |  |
| OUT | RESPONSE |  |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testMalAttribute

#### General

This operation checks that a MAL::Attribute can be sent and received explicitly

| Operation Identifier | testMalAttribute |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Attribute |
| OUT | RESPONSE | MAL::Attribute |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testMalComposite

#### General

This operation checks that a MAL::Composite can be sent and received explicitly

| Operation Identifier | testMalComposite |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Composite |
| OUT | RESPONSE | MAL::Composite |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testAbstractComposite

#### General

This operation checks that an abstract Composite can be sent and received explicitly

| Operation Identifier | testAbstractComposite |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | TestPublish |
| OUT | RESPONSE | TestPublish |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testMalAttributeList

#### General

This operation checks that a list of MAL::Attribute can be sent and received explicitly

| Operation Identifier | testMalAttributeList |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | List<MAL::Attribute> |
| OUT | RESPONSE | List<MAL::Attribute> |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testMalElementList

#### General

This operation checks that a list of MAL::Element can be sent and received explicitly

| Operation Identifier | testMalElementList |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | List<MAL::Element> |
| OUT | RESPONSE | List<MAL::Element> |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testMalCompositeList

#### General

This operation checks that a list of MAL::Composite can be sent and received explicitly

| Operation Identifier | testMalCompositeList |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | List<MAL::Composite> |
| OUT | RESPONSE | List<MAL::Composite> |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

### OPERATION: testAbstractCompositeList

#### General

This operation checks that a list of abstract composite can be sent and received explicitly

| Operation Identifier | testAbstractCompositeList |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | List<TestPublish> |
| OUT | RESPONSE | List<TestPublish> |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: DATA_ERROR

Data interoperability error

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DATA_ERROR | 70001 | Not Used |

## Service: ErrorTest

### General

Table 1-1:  ErrorTest Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| MALPrototype | ErrorTest | 100 | 3 | 1 |
| Interaction Pattern | Operation Identifier | Operation Number | Support in Replay | Capability Set |
| REQUEST | testDeliveryFailed | 100 | No | 100 |
| REQUEST | testDeliveryTimedout | 101 | No |  |
| REQUEST | testDeliveryDelayed | 102 | No |  |
| REQUEST | testDestinationUnknown | 103 | No |  |
| REQUEST | testDestinationTransient | 104 | No |  |
| REQUEST | testDestinationLost | 105 | No |  |
| REQUEST | testEncryptionFail | 106 | No |  |
| REQUEST | testUnsupportedArea | 107 | No |  |
| REQUEST | testUnsupportedOperation | 108 | No |  |
| REQUEST | testUnsupportedVersion | 109 | No |  |
| REQUEST | testBadEncoding | 110 | No |  |
| REQUEST | testUnknown | 111 | No |  |
| REQUEST | testAuthenticationFailure | 112 | No |  |
| REQUEST | testAuthorizationFailure | 113 | No |  |

### OPERATION: testDeliveryFailed

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Identifier | testDeliveryFailed |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testDeliveryTimedout

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Identifier | testDeliveryTimedout |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testDeliveryDelayed

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Identifier | testDeliveryDelayed |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testDestinationUnknown

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Identifier | testDestinationUnknown |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testDestinationTransient

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Identifier | testDestinationTransient |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testDestinationLost

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Identifier | testDestinationLost |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testEncryptionFail

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Identifier | testEncryptionFail |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testUnsupportedArea

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Identifier | testUnsupportedArea |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testUnsupportedOperation

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Identifier | testUnsupportedOperation |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testUnsupportedVersion

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Identifier | testUnsupportedVersion |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testBadEncoding

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Identifier | testBadEncoding |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testUnknown

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Identifier | testUnknown |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testAuthenticationFailure

#### General

This operation does nothing. Actually the error is raised by the MAL layer before the provider is invoked.

| Operation Identifier | testAuthenticationFailure |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testAuthorizationFailure

#### General

This operation does nothing. Actually the error is raised by the MAL layer before the provider is invoked.

| Operation Identifier | testAuthorizationFailure |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Body Type |
| IN | REQUEST | MAL::Element |
| OUT | RESPONSE | MAL::Element |

#### Structures

#### Errors

The operation does not return any errors.

## Service: IPTest2

### General

Table 1-1:  IPTest2 Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| MALPrototype | IPTest2 | 100 | 4 | 1 |
| Interaction Pattern | Operation Identifier | Operation Number | Support in Replay | Capability Set |
| PUBLISH-SUBSCRIBE | monitor | 105 | No | 100 |
| SUBMIT | publishUpdates | 108 | No | 102 |
| SUBMIT | publishRegister | 110 | No |  |
| SUBMIT | publishDeregister | 111 | No |  |
| SUBMIT | testMultipleNotify | 112 | No |  |

### OPERATION: monitor

#### General

This operation initiates a Pub/Sub interaction. It is not implemented by the service provider but by a broker.

| Operation Identifier | monitor |
| --- | --- |
| Interaction Pattern | PUBLISH-SUBSCRIBE |
| Pattern Sequence | Message | Body Type |
| OUT | PUBLISH/NOTIFY | TestUpdate |

#### Structures

#### Errors

The operation may return the following error:

##### ERROR: UNKNOWN

One or more of the entities identified in the registration do not exist.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

### OPERATION: publishUpdates

#### General

This operation cleans the assertions table, publishes an update as specified by the parameter TestPublishUpdate and checks the header of the Publish message (see 4.1.3). Moreover if an error is expected by the TestPublishUpdate then the operation hangs until a Publish error is raised or a timer ends (see 4.1.10). The header of the Publish error message is checked (see 4.1.4).

| Operation Identifier | publishUpdates |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | TestPublishUpdate |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: publishRegister

#### General

This operation cleans the assertions table, registers a publisher as specified by the parameter TestPublishRegister and checks the header of the Publish Register message (see 4.1.5). Moreover if no error is expected by the TestPublishRegister, it checks the header of the Publish Register acknowledgement message (see 4.1.6). Otherwise it checks the header of the Publish Register error message (see 4.1.7).

| Operation Identifier | publishRegister |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | TestPublishRegister |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: publishDeregister

#### General

This operation cleans the assertions table, registers a publisher as specified by the parameter TestPublishDeregister and checks the header of the Publish Deregister message (see 4.1.5). Moreover if no error is expected by the TestPublishDeregister, it checks the header of the Publish Deregister acknowledgement message (see 4.1.8). Otherwise it checks the header of the Publish Deregister error message (see 4.1.9).

| Operation Identifier | publishDeregister |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | TestPublishDeregister |

#### Structures

#### Errors

The operation does not return any errors.

### OPERATION: testMultipleNotify

#### General

| Operation Identifier | testMultipleNotify |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Body Type |
| IN | SUBMIT | TestPublishUpdate |

#### Structures

#### Errors

The operation does not return any errors.

# MalPrototype Data types

## Area data types: MALPrototype

### Composite: Assertion

| Name | Assertion |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 1 |
| Field | Type | Nullable | Comment |
| procedureName | MAL::String | Yes | Name of the test procedure that evaluated the assertion. |
| Info | MAL::String | Yes | Message explaining what the assertion checks. |
| Result | MAL::Boolean | Yes | Boolean indicating whether the assertion succeeded (true) or not (false). |

## Service data types: IPTest

### ENUMERATION: IPTestTransitionType

| Name | IPTestTransitionType |
| --- | --- |
| Short Form Part | 1 |
| Enumeration Value | Numerical Value | Comment |
| ACK | 1 |  |
| RESPONSE | 2 |  |
| ACK_ERROR | 3 |  |
| RESPONSE_ERROR | 4 |  |
| UPDATE | 5 |  |
| UPDATE_ERROR | 6 |  |

### Composite: IPTestDefinition

This abstract structure is inherited by all the IP test definition structures.

| Name | IPTestDefinition |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 2 |
| Field | Type | Nullable | Comment |
| procedureName | MAL::String | Yes | Name of the test procedure |
| consumerURI | MAL::URI | Yes | The consumer's URI |
| authenticationId | MAL::Blob | Yes | The authentication identifier used by the consumer |
| Qos | MAL::QoSLevel | Yes | The QoS level required by the consumer |
| Priority | MAL::UInteger | Yes | The priority level required by the consumer |
| Domain | List<MAL::Identifier> | Yes | The domain used by the consumer |
| networkZone | MAL::Identifier | Yes | The network zone used by the consumer |
| Session | MAL::SessionType | Yes | The type of the session used by the consumer |
| sessionName | MAL::Identifier | Yes | The identifier of the session used by the consumer |
| transitions | List<IPTestTransition> | Yes | The transitions that are requested by the consumer |
| timestamp | MAL::Time | Yes | The time the consumer initiated the interaction. |

### Composite: IPTestTransition

This structure is used to define an expected transition from an IP test. It asserts what transition is expected and what result is expected from the transition: successful or failure.

| Name | IPTestTransition |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 3 |
| Field | Type | Nullable | Comment |
| Type | IPTestTransitionType | Yes | The type of the transition to do |
| errorCode | MAL::UInteger | Yes | The code of the error expected to be raised when doing the transition (failed transition).-1 if no error is expected (successful transition). |

### Composite: BadHeaderReport

This data structure is an error report produced after having found a faulty header.

| Name | BadHeaderReport |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 4 |
| Field | Type | Nullable | Comment |
| expectedHeader | MessageHeader | Yes | The expected header |
| faultyHeader | MessageHeader | Yes | The header that is not compliant with the MAL rules |

### Composite: TestPublish

This abstract structure is a publish context.

| Name | TestPublish |
| --- | --- |
| Extends | MAL::Composite |
| Abstract |
| Field | Type | Nullable | Comment |
| Qos | MAL::QoSLevel | Yes | The QoS level to be used by the provider. |
| Priority | MAL::UInteger | Yes | The priority to be used by the provider. |
| domain | List<MAL::Identifier> | Yes | The domain to be used by the provider. |
| networkZone | MAL::Identifier | Yes | The network zone to be used by the provider. |
| Session | MAL::SessionType | Yes | The session type to be used by the provider. |
| sessionName | MAL::Identifier | Yes | The session name to be used by the provider. |
| testMultiType | MAL::Boolean | Yes | Whether to use the multi type version of the PubSub operation. |

### Composite: TestPublishRegister

This data structure specifies how the IPTest provider shall register.

| Name | TestPublishRegister |
| --- | --- |
| Extends | TestPublish |
| Short Form Part | 5 |
| Field | Type | Nullable | Comment |
| entityKeys | List<MAL::EntityKey> | Yes | The keys of the entities to be registered. |
| errorCode | MAL::UInteger | Yes | The code of the Publish Register error expected to be received.-1 if no Publish Register error is expected. |

### Composite: TestPublishDeregister

This data structure specifies how the IPTest provider shall register.

| Name | TestPublishDeregister |
| --- | --- |
| Extends | TestPublish |
| Short Form Part | 6 |
| Field | Type | Nullable | Comment |
| entityKeys | List<MAL::EntityKey> | Yes | The keys of the entities to be registered. |
| errorCode | MAL::UInteger | Yes | The code of the Publish Deregister error expected to be received.-1 if no Publish Deregister error is expected. |

### Composite: TestPublishUpdate

This data structure specifies how the IPTest provider shall publish an update.

| Name | TestPublishUpdate |
| --- | --- |
| Extends | TestPublish |
| Short Form Part | 7 |
| Field | Type | Nullable | Comment |
| updateHeaders | List<MAL::UpdateHeader> | Yes | The headers of the updates to be published by the provider |
| updates | List<TestUpdate> | Yes | The updates to be published by the provider |
| errorCode | MAL::UInteger | Yes | The code of the Publish error expected to be received.-1 if no Publish error is expected. |
| isException | MAL::Boolean | Yes | Indicates whether the error is returned as an Exception or a Publish Error message |
| failedEntityKeys | List<MAL::EntityKey> | Yes | The keys of the published entities that have not been registered. |

### Composite: TestUpdate

This data structure defines an Update published by the IPTest.

| Name | TestUpdate |
| --- | --- |
| Extends | Composite |
| Short Form Part | 8 |
| Field | Type | Nullable | Comment |
| Counter | MAL::Integer | Yes | A counter used to distinguish the test updates and to check the ordering. |

### Composite: InteractionKey

| Name | InteractionKey |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 9 |
| Field | Type | Nullable | Comment |
| URIfrom | MAL::URI | Yes | The consumer's URI |
| transactionId | MAL::Integer | Yes | The transaction identifier of the interaction |
| interactionType | MAL::InteractionType | Yes | The type of the interaction |
| Service | MAL::Identifier | Yes | The name of the called service |
| operation | MAL::Identifier | Yes | The name of the called operation |

### Composite: IPTestResult

| Name | IPTestResult |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 10 |
| Field | Type | Nullable | Comment |
| transactionId | MAL::Identifier | Yes | The transaction identifier assigned to the last interaction |
| assertions | List<Assertion> | Yes | The list of assertions checked by the provider. |

### Composite: MessageHeader

The MessageHeader structure is used to hold all fields that are passed for each message exchanged between a consumer and provider. See 4.1 for more information.

| Name | MessageHeader |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 11 |
| Field | Type | Nullable | Comment |
| URIfrom | MAL::URI | Yes | Message Source URI |
| authenticationId | MAL::Blob | Yes | Source Authentication Credentials |
| URIto | MAL::URI | Yes | Message Destination URI |
| timestamp | MAL::Time | Yes | Message generation timestamp |
| QoSlevel | MAL::QoSLevel | Yes | The QoS level of the message |
| priority | MAL::UInteger | Yes | The QoS priority of the message |
| domain | List<MAL::Identifier> | Yes | Domain of the message |
| networkZone | MAL::Identifier | Yes | Network zone of the message |
| session | MAL::SessionType | Yes | Type of session of the message |
| sessionName | MAL::Identifier | Yes | Name of the session of the message. Shall be ‘LIVE’ if session type is LIVE. |
| interactionType | MAL::InteractionType | Yes | Interaction Pattern Type |
| interactionStage | MAL::UOctet | Yes | Interaction Pattern Stage |
| transactionId | MAL::Identifier | Yes | Unique to consumer |
| area | MAL::Identifier | Yes | Service Area Identifier |
| service | MAL::Identifier | Yes | Service Identifier |
| operation | MAL::Identifier | Yes | Service Operation Identifier |
| version | MAL::UOctet | Yes | Service version |
| isError | MAL::Boolean | Yes | True if this is an error message else False. |

# Error codes

The following table lists the errors defined in this specification:

Table 1-1:  MALPrototype Error Codes

| Error | Error # | Comment |
| --- | --- | --- |
| TEST_ERROR | 70000 | Fake error for testing. |
| DATA_ERROR | 70001 | Data interoperability error |

# Compliance matrix

This section lists all the requirements specified in the MO MAL Space Packet Transport Binding and Binary Encoding book that are checked by the test scenarios. The table below gather the MO SPP Binding requirements and indicate the test procedure responsible for checking it.

| Statements | Test scenarios | Test cases | Test methods |
| --- | --- | --- | --- |
| 3.2.1x | MalMessageMapping | AllExceptPubSub, PubSub, UriTest | check uri from, check uri to, check uri from format, check uri to format |
| 3.3.2.x | MalMessageMapping | AllExceptPubSub, PubSub | check uri from |
| 3.2.2 | MalMessageMapping | AllExceptPubSub, PubSub | implicit check |
| 3.2.3 | MalMessageMapping | AllExceptPubSub, PubSub | implicit check |
| 3.3.2.5 | MalMessageMapping | SourceDestIdTest | source id flag is, check uri from |
| 3.3.3.1 | MalMessageMapping | AllExceptPubSub, PubSub | check authentication id |
| 3.3.3.2 | MalMessageMapping | QoSProperties | check authentication id is left out |
| 3.3.4.x | MalMessageMapping | AllExceptPubSub, PubSub | check uri to |
| 3.3.4.5 | MalMessageMapping | SourceDestIdTest | destination id flag is, check uri to |
| 3.3.5.1 | MalMessageMapping | AllExceptPubSub, PubSub | check timestamp |
| 3.3.5.2 | MalMessageMapping | QoSProperties | check timestamp is left out |
| 3.3.6 | MalMessageMapping | AllExceptPubSub, PubSub | check qos |
| 3.3.7.1 | MalMessageMapping | AllExceptPubSub, PubSub | priority is |
| 3.3.7.2 | MalMessageMapping | QoSProperties | check priority is left out |
| 3.3.8.1 | MalMessageMapping | AllExceptPubSub, PubSub | check domain id |
| 3.3.8.2 | MalMessageMapping | QoSProperties | check domain is left out |
| 3.3.9.1 | MalMessageMapping | AllExceptPubSub, PubSub | network zone is |
| 3.3.9.2 | MalMessageMapping | QoSProperties | check network zone is left out |
| 3.3.10 | MalMessageMapping | AllExceptPubSub, PubSub | check session |
| 3.3.11.1 | MalMessageMapping | AllExceptPubSub, PubSub | session name is |
| 3.3.11.2 | MalMessageMapping | QoSProperties | check session name is left out |
| 3.3.12 | MalMessageMapping | AllExceptPubSub, PubSub | sdu type is |
| 3.3.13 | MalMessageMapping | AllExceptPubSub, PubSub | check transaction id |
| 3.3.14 | MalMessageMapping | AllExceptPubSub, PubSub | area is |
| 3.3.15 | MalMessageMapping | AllExceptPubSub, PubSub | service is |
| 3.3.16 | MalMessageMapping | AllExceptPubSub, PubSub | operation is |
| 3.3.17 | MalMessageMapping | AllExceptPubSub, PubSub | area version is |
| 3.3.18 | MalMessageMapping | AllExceptPubSub, PubSub | error flag is |
| 3.4.2.2 | MalMessageMapping | AllExceptPubSub, PubSub | packet version number is |
| 3.4.2.3 | MalMessageMapping | AllExceptPubSub, PubSub | check space packet type |
| 3.4.2.4 | MalMessageMapping | AllExceptPubSub, PubSub | secondary header flag is |
| 3.4.2.5 | MalMessageMapping | MalMessageSegmentation | primary header sequence flags are |
| 3.4.2.6 | MalMessageMapping | MalMessageSegmentation | primary header sequence counter is initial counter plus |
| 3.4.2.7 | MalMessageMapping | AllExceptPubSub, PubSub | packet data length is length of packet data field minus one |
| 3.4.3.2.x | MalMessageMapping | AllExceptPubSub, PubSub | version is |
| 3.4.3.3 | MalMessageMapping | MalMessageSegmentation | secondary header segment counter is, test message segmentation with scrambling pattern |
| 3.5.3.2.1 | MalMessageMapping | MalMessageBodyMapping | check body element order |
| 3.5.3.2.2 | MalMessageMapping | EmptyBody | mal message body is empty |
| 3.5.3.3.1 | MalMessageMapping | PubSub | testPublishAndSessionAndSessionNameAndDomain, testPublishWithAndSessionAndSessionNameAndDomain |
| 3.5.3.3.3-7 | MalMessageMapping | PubSub | check element short form area and service and type |
| 3.5.3.3.4 | MalMessageMapping | PubSub | body element abstract service defined encoded for publish message |
| 3.5.3.3.5 | MalMessageMapping | PubSub | body element abstract non-service defined encoded for publish message |
| 3.5.3.3.8 | MalMessageMapping | PubSub | body element encoded as element |
| 3.5.3.3.9 | MalMessageMapping | PubSub | body element encoded as nullable element |
| 3.5.3.3.10 | MalMessageMapping | PubSub | body element encoded as element |
| 3.5.3.3.11 | MalMessageMapping | PubSub | body element encoded as element |
| 3.5.3.3.12a | MalMessageMapping | AllExceptPubSub, PubSub | body element encoded as uinteger |
| 3.5.3.3.12b | MalMessageMapping | AllExceptPubSub, PubSub | body element encoded as nullable element, body element null encoded as nullable element |
| 3.5.3.3.13 | MalMessageMapping | AllExceptPubSub | body element encoded as nullable element |
| 3.5.3.4 | MalMessageMapping | PubSub | publish update list is for update value type |
| 3.5.3.5 | MalMessageMapping | PubSub | read publish update for concrete/abstract service-defined/abstract non-service defined update value type with value |
| 4.2.x | MalMessageMapping | MalSppTransport | supports qos level |
| 4.3.x | MalMessageMapping | MalSppTransport | supports interaction type |
| 4.4.1 | MalMessageMapping | AllExceptPubSub, PubSub | select sent packet at |
| 4.4.2-3 | MalMessageMapping | TransmitRequest | send message with null mal header field and expect |
| 4.4.4 | See statements 3.x |
| 4.4.5 | MalMessageMapping | TransmitRequest | send message from uri to uri and expect |
| 4.4.6 | MalMessageMapping | AllExceptPubSub, PubSub | check uri from, check uri to |
| 4.4.7 | MalMessageMapping | AllExceptPubSub, PubSub | check uri from, check uri to |
| 4.4.8 | MalMessageMapping | TransmitQosProperties | check transmit qos properties |
| 4.4.9 | MalMessageMapping | MalMessageSegmentation | check small blob |
| 4.4.10a | MalMessageMapping | MalMessageSegmentation | packet data length is consistent with |
| 4.4.10b | MalMessageMapping | MalMessageSegmentation | number of sent packets is |
| 4.4.10c | MalMessageMapping | MalMessageSegmentation | mal message header mapping compares packet at index to first packet |
| 4.4.10d | MalMessageMapping | MalMessageSegmentation | secondary header segment counter is |
| 4.4.10e | MalMessageMapping | MalMessageSegmentation | check segment counter selection |
| 4.4.10f,g,h | MalMessageMapping | MalMessageSegmentation | primary header sequence flags are |
| 4.4.11 | MalMessageMapping | MalMessageSegmentation | check packet data field size limits |
| 4.4.12 | MalMessageMapping | TransmitRequest | check space packet sending request error |
| 4.4.13 | MalMessageMapping | AllExceptPubSub, PubSub | implicit check |
| 4.5.1 | MalMessageMapping | TransmitRequest | check transmit multiple |
| 4.5.2 | MalMessageMapping | TransmitRequest | check transmit multiple error |
| 4.6.1 | MalMessageMapping | AllExceptPubSub, PubSub | select received packet at |
| 4.6.2 | MalMessageMapping | AllExceptPubSub, PubSub, MalMessageSegmentation | select received packet at, small blob works, large blob works |
| 4.6.3 | MalMessageMapping | AllExceptPubSub, PubSub | check uri from, check uri to |
| 4.6.4x | MalMessageMapping | MalMessageSegmentation | small blob works |
| 4.6.5a | MalMessageMapping | MalMessageSegmentation | large blob works |
| 4.6.5b,c | MalMessageMapping | MalMessageSegmentation | test message segmentation with scrambling pattern, check dropped packet |
| 4.6.5d | MalMessageMapping | MalMessageSegmentation | large blob works, test message segmentation with scrambling pattern |
| 4.6.5e | MalMessageMapping | MalMessageSegmentation | check timeout with |
| 4.6.6 | MalMessageMapping | AllExceptPubSub, PubSub | test interaction pattern with unknown uri to, test stage with unknown uri to |
| 5.2.1-2 | MalDataEncoding | ElementTest | check a composite with a field typed MAL::Attribute, attribute tag is |
| 5.2.3,4,7,8 | MalDataEncoding | ElementTest | check a composite sent as a MAL::Element, check short form |
| 5.2.3,4,7,8 | MalDataEncoding | ElementTest | check a composite sent as a MAL::Composite |
| 5.2.3,4,7,8 | MalDataEncoding | ElementTest | check a composite sent as an abstract composite |
| 5.2.3,4,7,8 | MalDataEncoding | ElementTest | check an attribute sent as a MAL::Element, check short form |
| 5.2.3,4,7,8 | MalDataEncoding | ElementTest | check an attribute sent as a MAL::Attribute, check an attribute list sent as a MAL::Element list, check an attribute list sent as a MAL::Attribute list |
| 5.2.3,4,7,8 | MalDataEncoding | ElementTest | check an attribute list sent as a MAL::Composite |
| 5.2.3,4,7,8 | MalDataEncoding | ElementTest | check a composite list sent as a MAL::Element list |
| 5.2.3,4,7,8 | MalDataEncoding | ElementTest | check a composite list sent as a MAL::Composite list |
| 5.2.3,4,7,8 | MalDataEncoding | ElementTest | check a composite list sent as an abstract composite list |
| 5.2.3,4,7,8 | MalDataEncoding | ElementTest | check a composite list sent as a MAL::Composite |
| 5.2.5 | MalDataEncoding | ElementTest | check a composite defined by a service and sent as a MAL::Element |
| 5.2.6 | MalDataEncoding | ElementTest | check an attribute sent as a MAL::Element, check short form |
| 5.2.9a | MalDataEncoding | ElementTest | check every attribute |
| 5.2.9b | MalDataEncoding | ElementTest | check an enumerated sent as a MAL::Element |
| 5.2.9c | MalDataEncoding | ElementTest | check a composite with a field typed as a list |
| 5.2.9d | MalDataEncoding | ElementTest | check a composite sent as a MAL::Element |
| 5.3.1 | MalDataEncoding | EnumerationTest | check first element in an enumeration |
| 5.3.1 | MalDataEncoding | EnumerationTest | check second and third elements in an enumeration |
| 5.3.2 | MalDataEncoding | EnumerationTest | check an enumerated sent as a MAL::Element |
| 5.3.3 | MalDataEncoding | EnumerationTest | check a medium enumeration |
| 5.3.4 | MalDataEncoding | EnumerationTest | check a large enumeration |
| 5.4.1 | MalDataEncoding | CompositeTest | check field order |
| 5.4.2 | MalDataEncoding | CompositeTest | check presence flag |
| 5.4.3 | MalDataEncoding | CompositeTest | check composite inheritance |
| 5.5.1-4 | MalDataEncoding | ListTest | check list format and elements order |
| 5.6.1-2 | MalDataEncoding | NullableElementTest | check presence flag |
| 5.7-28 | MalDataEncoding | AttributeTest | check every attribute |
| 5.15-20 | MalDataEncoding | VarintSupportedTest | check every attribute affected by varintSupported |
| 5.15-20 | MalMessageMapping | AllExceptPubSub | priority is, check domain id, network zone is, session name is, check authentication id |
| 5.22-23 | MalDataEncoding | TimeCodeFormatTest | check every attribute affected by time code formats |
| 5.22-23 | MalMessageMapping | AllExceptPubSub | check timestamp |

Mapping Configuration Parameters

The Mapping Configuration Parameters are listed according to the APID qualifier and APID of transmitted Space Packets.

APID Qualifier 247, APID 1

| Mapping Configuration Parameter | Value |
| --- | --- |
| DURATION_CODE_FORMAT | 0001 1100 (CUC, no fractional time) |
| DURATION_UNIT | second |
| TIME_CODE_FORMAT | 0001 1111 (CUC, CCSDS epoch) |
| TIME_EPOCH | 1958-01-01T00:00:00.000 |
| TIME_EPOCH_TIMESCALE | TAI |
| TIME_UNIT | second |
| FINE_TIME_CODE_FORMAT | 1010 1111 0000 1000 (CUC, agency epoch, fractional=3+2) |
| FINE_TIME_EPOCH | 2013-01-01T00:00:00.000 |
| FINE_TIME_EPOCH_TIMESCALE | TAI |
| FINE_TIME_UNIT | second |
| PACKET_DATA_FIELD_SIZE_LIMIT | 0 (maximum size) |
| VARINT_SUPPORTED | True |
| AUTHENTICATION_ID | Null (default value is assigned: empty Blob) |
| DOMAIN | Null (default value is assigned: empty List) |
| NETWORK_ZONE | Null (default value is assigned: empty Identifier) |
| PRIORITY | Null (default value is assigned: 0) |
| SESSION_NAME | Null (default value is assigned: empty Identifier) |

## APID Qualifier 248, APID 2

| Mapping Configuration Parameter | Value |
| --- | --- |
| DURATION_CODE_FORMAT | 0001 1100 (CUC, no fractional time) |
| DURATION_UNIT | second |
| TIME_CODE_FORMAT | 0001 1111 (CUC, CCSDS epoch) |
| TIME_EPOCH | 1958-01-01T00:00:00.000 |
| TIME_EPOCH_TIMESCALE | TAI |
| TIME_UNIT | second |
| FINE_TIME_CODE_FORMAT | 1010 1111 0000 1000 (CUC, agency epoch, fractional=3+2) |
| FINE_TIME_EPOCH | 2013-01-01T00:00:00.000 |
| FINE_TIME_EPOCH_TIMESCALE | TAI |
| FINE_TIME_UNIT | second |
| PACKET_DATA_FIELD_SIZE_LIMIT | 0 (maximum size) |
| VARINT_SUPPORTED | True |
| AUTHENTICATION_ID | 0A0B0C |
| DOMAIN | malspp.test.domain |
| NETWORK_ZONE | malsppTestNw |
| PRIORITY | 4294967295 |
| SESSION_NAME | malsppTestSession |

## APID Qualifier 347, APID 3

| Mapping Configuration Parameter | Value |
| --- | --- |
| DURATION_CODE_FORMAT | 0001 1100 (CUC, no fractional time) |
| DURATION_UNIT | second |
| TIME_CODE_FORMAT | 0001 1111 (CUC, CCSDS epoch) |
| TIME_EPOCH | 1958-01-01T00:00:00.000 |
| TIME_EPOCH_TIMESCALE | TAI |
| TIME_UNIT | second |
| FINE_TIME_CODE_FORMAT | 1010 1111 0000 1000 (CUC, agency epoch, fractional=3+2) |
| FINE_TIME_EPOCH | 2013-01-01T00:00:00.000 |
| FINE_TIME_EPOCH_TIMESCALE | TAI |
| FINE_TIME_UNIT | second |
| PACKET_DATA_FIELD_SIZE_LIMIT | 0 (maximum size) |
| VARINT_SUPPORTED | True |
| AUTHENTICATION_ID | 0A0B0C |
| DOMAIN | malspp.test.domain |
| NETWORK_ZONE | malsppTestNw |
| PRIORITY | 4294967295 |
| SESSION_NAME | malsppTestSession |

## APID Qualifier 447, APID 5

| Mapping Configuration Parameter | Value |
| --- | --- |
| DURATION_CODE_FORMAT | 0001 1100 (CUC, no fractional time) |
| DURATION_UNIT | second |
| TIME_CODE_FORMAT | 0001 1111 (CUC, CCSDS epoch) |
| TIME_EPOCH | 1958-01-01T00:00:00.000 |
| TIME_EPOCH_TIMESCALE | TAI |
| TIME_UNIT | second |
| FINE_TIME_CODE_FORMAT | 1010 1111 0000 1000 (CUC, agency epoch, fractional=3+2) |
| FINE_TIME_EPOCH | 2013-01-01T00:00:00.000 |
| FINE_TIME_EPOCH_TIMESCALE | TAI |
| FINE_TIME_UNIT | second |
| PACKET_DATA_FIELD_SIZE_LIMIT | 0 (maximum size) |
| VARINT_SUPPORTED | True |
| AUTHENTICATION_ID | 0A0B0C |
| DOMAIN | malspp.test.domain |
| NETWORK_ZONE | malsppTestNw |
| PRIORITY | 4294967295 |
| SESSION_NAME | malsppTestSession |

## APID Qualifier 547, APID 7

| Mapping Configuration Parameter | Value |
| --- | --- |
| DURATION_CODE_FORMAT | 0001 1100 (CUC, no fractional time) |
| DURATION_UNIT | second |
| TIME_CODE_FORMAT | 0001 1111 (CUC, CCSDS epoch) |
| TIME_EPOCH | 1958-01-01T00:00:00.000 |
| TIME_EPOCH_TIMESCALE | TAI |
| TIME_UNIT | second |
| FINE_TIME_CODE_FORMAT | 1010 1111 0000 1000 (CUC, agency epoch, fractional=3+2) |
| FINE_TIME_EPOCH | 2013-01-01T00:00:00.000 |
| FINE_TIME_EPOCH_TIMESCALE | TAI |
| FINE_TIME_UNIT | second |
| PACKET_DATA_FIELD_SIZE_LIMIT | 0 (maximum size) |
| VARINT_SUPPORTED | True |
| AUTHENTICATION_ID | 0A0B0C |
| DOMAIN | malspp.test.domain |
| NETWORK_ZONE | malsppTestNw |
| PRIORITY | 4294967295 |
| SESSION_NAME | malsppTestSession |

## APID Qualifier 348, APID 4

Duration format is CUC with fractional time. Time format is CDS, agency epoch is 1958-01-01T00:00:00.000 and time scale is UTC. Fine time format is CDS, agency epoch is 2012-01-01T00:00:00.000 and time scale is UTC. Varint is not supported.

| Mapping Configuration Parameter | Value |
| --- | --- |
| DURATION_CODE_FORMAT | 0001 1111 (CUC, with fractional time) |
| DURATION_UNIT | second |
| TIME_CODE_FORMAT | 0100 1110 (CDS, agency epoch) |
| TIME_EPOCH | 1958-01-01T00:00:00.000 |
| TIME_EPOCH_TIMESCALE | UTC |
| TIME_UNIT | second |
| FINE_TIME_CODE_FORMAT | 0100 1110 (CDS, agency epoch) |
| FINE_TIME_EPOCH | 2012-01-01T00:00:00.000 |
| FINE_TIME_EPOCH_TIMESCALE | UTC |
| FINE_TIME_UNIT | second |
| PACKET_DATA_FIELD_SIZE_LIMIT | 0 (maximum size) |
| VARINT_SUPPORTED | False |
| AUTHENTICATION_ID | 0A0B0C |
| DOMAIN | malspp.test.domain |
| NETWORK_ZONE | malsppTestNw |
| PRIORITY | 4294967295 |
| SESSION_NAME | malsppTestSession |

## APID Qualifier 647, APID 1

Packet data field size limit is set to 27 octets (limited size).

| Mapping Configuration Parameter | Value |
| --- | --- |
| DURATION_CODE_FORMAT | 0001 1100 (CUC, no fractional time) |
| DURATION_UNIT | second |
| TIME_CODE_FORMAT | 0001 1111 (CUC, CCSDS epoch) |
| TIME_EPOCH | 1958-01-01T00:00:00.000 |
| TIME_EPOCH_TIMESCALE | TAI |
| TIME_UNIT | second |
| FINE_TIME_CODE_FORMAT | 1010 1111 0000 1000 (CUC, agency epoch, fractional=3+2) |
| FINE_TIME_EPOCH | 2013-01-01T00:00:00.000 |
| FINE_TIME_EPOCH_TIMESCALE | TAI |
| FINE_TIME_UNIT | second |
| PACKET_DATA_FIELD_SIZE_LIMIT | 27 |
| VARINT_SUPPORTED | True |
| AUTHENTICATION_ID | Null (default value is assigned: empty Blob) |
| DOMAIN | Null (default value is assigned: empty List) |
| NETWORK_ZONE | Null (default value is assigned: empty Identifier) |
| PRIORITY | Null (default value is assigned: 0) |
| SESSION_NAME | Null (default value is assigned: empty Identifier) |

## APID Qualifier 648, APID 2

Packet data field size limit is set to 27 octets (limited size).

| Mapping Configuration Parameter | Value |
| --- | --- |
| DURATION_CODE_FORMAT | 0001 1100 (CUC, no fractional time) |
| DURATION_UNIT | second |
| TIME_CODE_FORMAT | 0001 1111 (CUC, CCSDS epoch) |
| TIME_EPOCH | 1958-01-01T00:00:00.000 |
| TIME_EPOCH_TIMESCALE | TAI |
| TIME_UNIT | second |
| FINE_TIME_CODE_FORMAT | 1010 1111 0000 1000 (CUC, agency epoch, fractional=3+2) |
| FINE_TIME_EPOCH | 2013-01-01T00:00:00.000 |
| FINE_TIME_EPOCH_TIMESCALE | TAI |
| FINE_TIME_UNIT | second |
| PACKET_DATA_FIELD_SIZE_LIMIT | 27 |
| VARINT_SUPPORTED | True |
| AUTHENTICATION_ID | Null (default value is assigned: empty Blob) |
| DOMAIN | Null (default value is assigned: empty List) |
| NETWORK_ZONE | Null (default value is assigned: empty Identifier) |
| PRIORITY | Null (default value is assigned: 0) |
| SESSION_NAME | Null (default value is assigned: empty Identifier) |

## APID Qualifier 647, APID 3

Packet data field size limit is set to 200 octets (medium size).

| Mapping Configuration Parameter | Value |
| --- | --- |
| DURATION_CODE_FORMAT | 0001 1100 (CUC, no fractional time) |
| DURATION_UNIT | second |
| TIME_CODE_FORMAT | 0001 1111 (CUC, CCSDS epoch) |
| TIME_EPOCH | 1958-01-01T00:00:00.000 |
| TIME_EPOCH_TIMESCALE | TAI |
| TIME_UNIT | second |
| FINE_TIME_CODE_FORMAT | 1010 1111 0000 1000 (CUC, agency epoch, fractional=3+2) |
| FINE_TIME_EPOCH | 2013-01-01T00:00:00.000 |
| FINE_TIME_EPOCH_TIMESCALE | TAI |
| FINE_TIME_UNIT | second |
| PACKET_DATA_FIELD_SIZE_LIMIT | 200 |
| VARINT_SUPPORTED | True |
| AUTHENTICATION_ID | Null (default value is assigned: empty Blob) |
| DOMAIN | Null (default value is assigned: empty List) |
| NETWORK_ZONE | Null (default value is assigned: empty Identifier) |
| PRIORITY | Null (default value is assigned: 0) |
| SESSION_NAME | Null (default value is assigned: empty Identifier) |

## APID Qualifier 648, APID 4

Packet data field size limit is set to 200 octets (medium size).

| Mapping Configuration Parameter | Value |
| --- | --- |
| DURATION_CODE_FORMAT | 0001 1100 (CUC, no fractional time) |
| DURATION_UNIT | second |
| TIME_CODE_FORMAT | 0001 1111 (CUC, CCSDS epoch) |
| TIME_EPOCH | 1958-01-01T00:00:00.000 |
| TIME_EPOCH_TIMESCALE | TAI |
| TIME_UNIT | second |
| FINE_TIME_CODE_FORMAT | 1010 1111 0000 1000 (CUC, agency epoch, fractional=3+2) |
| FINE_TIME_EPOCH | 2013-01-01T00:00:00.000 |
| FINE_TIME_EPOCH_TIMESCALE | TAI |
| FINE_TIME_UNIT | second |
| PACKET_DATA_FIELD_SIZE_LIMIT | 200 |
| VARINT_SUPPORTED | True |
| AUTHENTICATION_ID | Null (default value is assigned: empty Blob) |
| DOMAIN | Null (default value is assigned: empty List) |
| NETWORK_ZONE | Null (default value is assigned: empty Identifier) |
| PRIORITY | Null (default value is assigned: 0) |
| SESSION_NAME | Null (default value is assigned: empty Identifier) |

APID Qualifier 123, APID 123

| Mapping Configuration Parameter | Value |
| --- | --- |
| DURATION_CODE_FORMAT | 0001 1100 (CUC, no fractional time) |
| DURATION_UNIT | second |
| TIME_CODE_FORMAT | 0001 1111 (CUC, CCSDS epoch) |
| TIME_EPOCH | 1958-01-01T00:00:00.000 |
| TIME_EPOCH_TIMESCALE | TAI |
| TIME_UNIT | second |
| FINE_TIME_CODE_FORMAT | 1010 1111 0000 1000 (CUC, agency epoch, fractional=3+2) |
| FINE_TIME_EPOCH | 2013-01-01T00:00:00.000 |
| FINE_TIME_EPOCH_TIMESCALE | TAI |
| FINE_TIME_UNIT | second |
| PACKET_DATA_FIELD_SIZE_LIMIT | 0 |
| VARINT_SUPPORTED | True |
| AUTHENTICATION_ID | 0A0B0C |
| DOMAIN | malspp.test.domain |
| NETWORK_ZONE | malsppTestNw |
| PRIORITY | 4294967295 |
| SESSION_NAME | malsppTestSession |