## Slide 1: Functional Resource Model Status
CSSA Workshop
Cyberspace
11 May 2021
John Pietras
Global Science and Technology, Inc.
With updates from the CSTSWG meeting on 11 May 2021

## Slide 2: Functional Resource Model Status - Outline
FRM Tier-1 – Status and Open Points
FRM Tier-2 – Status and Open Points
FRM Magenta Book

## Slide 3: FRM Tier-1 – Status and Open Points (1 of 2)
28 Tier-1 FRs
  Antenna;
  CCSDS 401 Space Link Carrier Transmission
  Ranging Transmission
  CCSDS 401 Space Link Carrier Reception
  Range and Doppler Extraction
  TC PLOP, Synchronization, and Channel Encoding
  Fixed Length Frame Synchronization, Channel Encoding, and Only-Idle-Data Generation
  Fixed Length Frame Synchronization and Channel Decoding
  TC Master Channel (MC) Multiplexing
  TC Virtual Channel (VC) Multiplexing
  AOS MC Multiplexing
  AOS VC Multiplexing
  Fixed Length Frame (FLF) USLP MC Multiplexing
  FLF USLP VC Multiplexing
  TM/AOS MC Demultiplexing
  TM/AOS VC Demultiplexing
  Frame Data Sink
  TDM Segment Generation
  Offline Frame Buffer
  TDM Recording Buffer
  SLE F-CLTU Transfer Service Provider
  Forward Frame CSTS Provider
  SLE RAF Transfer Service Provider
  SLE RCF Transfer Service Provider
  SLE ROCF Transfer Service Provider
  Tracking Data CSTS Provider
  Monitored Data CSTS Provider

## Slide 4: FRM Tier-1 – Status and Open Points (2 of 2)
All Tier-1 FR MIB (i.e., SANA FR Registry) definitions were reviewed and approved for registration in 2020
The CFDP Entity FR was removed from Tier-1 due to the lack of a commonly-agreed concept of operations and absence of specifications for the FRs that use or are used by the CFDP Entity
Are we still waiting for SANA to update the registry?
  11 May update: The registry has been updated, but there are new errors, as recorded in the minutes of the meeting
Subsequently, several FR MIB definitions have required updating
  Antenna
  CCSDS 401 Space Link Carrier Transmission
  CCSDS 401 Space Link Carrier Reception
  TC PLOP, Synchronization, and Channel Encoding
  TC Master Channel (MC) Multiplexing
  TM/AOS MC Demultiplexing
  TM/AOS VC Demultiplexing

## Slide 5: FRM Tier-1 – Status and Open Points: Antenna
SAPs for Physical Channel strata FRs have changed back and forth over the months to support D-DOR and Open Loop
  Went from RF to IF and back to RF
  Current SAP names:
    Transmit RF Carrier Signal
    Received RF Carrier Signal
  Only affected FRM Magenta Book definition
    No effect on SANA FR registry entry: SAPs are not currently published in SANA Registry
Issue triggered by Tier-2
  Antenna has a “Pointing Angles” ancillary interface, which is sufficient to provide antenna-related data for TD-CSTS
  Tier-2 Non-validated Radiometric Data Collection FR also requires weather data from the antenna
    Proposed resolution: change “Pointing Angles” to “Aperture Data”, which represents any and all ancillary data required of the aperture (antenna)
      The only purpose of this ancillary interface is to identify which aperture is providing ancillary data, so it does not have to be specific to any single data type

## Slide 6: FRM Tier-1 – Status and Open Points: CCSDS 401 Space Link Carrier Transmission/Reception
Antenna SAPs have changed back and forth over the months to support D-DOR and Open Loop
  Went from RF to IF and back to RF
  Current SAP names:
    Transmit RF Carrier Signal
    Received RF Carrier Signal
  Only affected FRM Magenta Book definition
    No effect on SANA FR registry entry: SAPs are not currently published in SANA Registry
CCSDS 401 Space Link Carrier Reception FR uses ccsds401CarrierRcptTransponderRatio to identify the CCSDS 401 Space Link Carrier Transmission FR instance with which it is coherently related
  Parameter added to FR MIB, definition updated in FRM MB
  Open point: need to confirm that this mechanism could be used in 3-way tracking by using TD-CSTS
Issue on the horizon
  CCSDS 401.0 is adding new modulation (n-psk)

## Slide 7: FRM Tier-1 – Status and Open Points: TC PLOP, Synchronization, and Channel Encoding
Removed redundant configuration parameter and removed systematic retransmission of CLTUs received from SLE F-CLTU service instance
Description of Systematic Retransmission has been updated in the FRM MB
  Now is consistent with parameters and semantic definitions in the FR MIB

## Slide 8: FRM Tier-1 – Status and Open Points: TC MC Multiplexing (1 of 2)
tcMcMuxMaxNumberOfFramesPerCltu now semantically constrained by tcPlopSyncInputDataFormat: frame: maxNumberOfCltuRepetitions parameter of the underlying TcPlopSyncAndChnlEncode FR instance
  Multiple repetitions of multi-frame CLTUs prohibited
Description of Systematic Retransmission has been updated in the FRM MB
Open Point: Maximum Frame Length and Maximum Number of Frames per CLTU constraints
  As currently defined: tcMcMuxMaxFrameLength X tcMcMuxMaxNumberOfFramesPerCltu must be LEQ the set of frames that can fit into tcPlopSyncMaxCltuLength
    For a given max CLTU size, the longest possible frame length will determine the number of frames per CLTU
  If the VCs of a physical channel can carry “long” frames and “short” frames, CLTUs with “short” frames will be smaller than their maximum allowed size
  Possible alternative constraint: create a tcMcMuxMaxFrameSetLength parameter to allow maximum population of all CLTUs, where tcMcMuxMaxFrameSetLength must be LEQ the set of frames that can fit into tcPlopSyncMaxCltuLength
  W. Hell does not see a real-world benefit in the alternative from his experience: does anyone else in the WG think it might be useful?

## Slide 9: FRM Tier-1 – Status and Open Points: TC MC Multiplexing (2 of 2)
Open Point: Maximum Frame Length and Maximum Number of Frames per CLTU constraints (concluded)
  H. Dreihahn comment on 11 May: Even though the Forward Frame service supports TC frames, it will be unlikely that the service will be used for TC frames. Instead, TC-using Missions will likely continue using F-CLTU service. DTN and CFDP will likely use USLP and not TC. In other words, the TC SDLP Transmission FR Set will most likely not be used, or rarely used at best. As such, it is not necessary to optimize the CLTU capacity of TC Channel Access Frame Sets, and the current constraint is sufficient
  With no further comment from the rest of the WG, the current position is to keep the current constrain and not add the tcMcMuxMaxFrameSetLength parameter

## Slide 10: FRM Tier-1 – Status and Open Points: TM/AOS MC and VC Demultiplexing FRs
Current FR MIB definitions allows only one MC per physical channel to carry MC-OCFs, or only one VC per VC to carry VC-OCFs
  Needs to be updated to allow multiple MCs to carry OCFs
  FRM MB definitions will need to be updated
Data types defining OCF services need to be tightened
  Current data types allow illegal AOS combinations
  USLP_MC_OCF service does not map cleanly into existing MC-OCF/VC-OCF paradigm
FRM MB definitions need to be corrected regarding performance of MC-OCF and VC-OCF decommutation

## Slide 11: FRM Tier-2 – Status and Open Points
13 Tier-2 FRs
  Delta-DOR Raw Data Collection
  Open Loop Data Collection
  VLF Synchronization and Channel Decoding
  Variable Frame Length (VLF) USLP MC Multiplexing
  VLF USLP VC Multiplexing
  VLF USLP MC Demultiplexing
  VLF USLP VC Demultiplexing
Removed from Tier-2
  Open Loop Data Store
  TGFT Host
Removed from FR Model
  SLE Forward Space Packet
Proposed SANA FR Candidate Registry abandoned
  All Approved and Candidate FRs will be listed in the same SANA FR Registry
  Approved FRs have populated Authorizing Entity attributes
  Approved FRs have blank Authorizing Entity attributes
    Do we want to make it something like “Unauthorized Candidate”?
  FRM MB descriptions has been updated
  FLF USLP MC Demultiplexing
  FLF USLP MC Demultiplexing
  Non-validated Radiometric Data Collection
  Non-validated Radiometric Data Store
  Validated Radiometric Data Store
  D-DOR Raw Data Store

## Slide 12: FRM Tier-2 – Status and Open Points: Delta-DOR Raw Data Collection
D-DOR Raw Data Collection is now in the Physical Channel stratum, with CCSD 401 Space Link Carrier Transmission and Reception
Definition spans reception of the RF signal through the recording of raw D-DOR measurements in Raw D-DOR data formatted file
Candidate FR MIB definition has been developed by W. Hell
  J. Pietras has not yet reviewed it
M. Gnat is preparing a strawman configuration profile for D-DOR service to be discussed with the D-DOR WG on 12 May
  J. Pietras provided M. Gnat with a HTML Word version of the FR MIB containing the Delta-DOR Raw Data Collection FR definition, with caveat that it is the first draft of the definition

## Slide 13: FRM Tier-2 – Status and Open Points: Open Loop Data Collection
Open Loop Data Collection is now in the Physical Channel stratum, with CCSD 401 Space Link Carrier Transmission and Reception
Definition spans reception of the RF signal through the recording of open loop measurements on Agency-specific media and format
Candidate FR MIB definition has been developed by W. Hell
  J. Pietras has not yet reviewed it

## Slide 14: FRM Tier-2 – Status and Open Points: VLF Synchronization and Channel Decoding
VLF Synchronization and Channel Decoding definition spans reception of the symbol stream, decoding, and outputting at one or both SAPs
  All Undelimited Received Transfer Frames SAP
    Intended for VLF USLP Reception FRs
      Could be used by TC SDLP Reception FRs, if and when they are defined for non-ESLT uses
    Frame delimitation, fill removal, and frame validation is performed by USLP or TC SDLP
  All Annotated Received Transfer Frames SAP
    Provides Frame delimitation, fill removal, and frame validation that is required by Return SLE transfer services
    Used only for non-truncated VLF USLP frames
Candidate FR MIB and corresponding FRM MB definitions have been developed by J. Pietras
  No one else has yet reviewed them

## Slide 15: FRM Tier-2 – Status and Open Points: VLF USLP MC Multiplexing
VLF USLP MC Multiplexing FR
  USLP All Frames Generation function (VLF aspects)
    Optional FECF
    TC Channel Access Frame Set creation and Repetition annotation
  USLP MC Multiplexing function (VLF aspects)
    Merges MC streams of frames into a single physical channel stream of frames
    Implements CSTS MC multiplexing scheme
Candidate FR MIB definition has been developed by W. Hell
  J. Pietras is in the process of reviewing the FR MIB definition and updating the FRM MB definition

## Slide 16: FRM Tier-2 – Status and Open Points: VLF USLP VC Multiplexing
VLF USLP VC Multiplexing FR
  USLP VC Multiplexing function (VLF aspects)
    Merges VC streams of frames into a single MC stream of frames
    Implements CSTS VC multiplexing scheme
Candidate FR MIB definition has been developed by W. Hell
  J. Pietras is in the process of reviewing the FR MIB definition and updating the FRM MB definition
Note: For uses other than ESLTs, this FR would also include injection of USLP_MC_OCFs, but it has been omitted from the current FR definition because for ESLTs that’s not possible
  For the same reason, MC-OCF and VC-OCF input are not included in TM and AOS Mux FRs

## Slide 17: FRM Tier-2 – Status and Open Points: FLF USLP MC Multiplexing
FLF USLP MC Multiplexing FR
  USLP All Frames Generation function (FLF aspects)
    Optional FECF
  USLP MC Multiplexing function (FLF aspects)
    Merges MC streams of frames into a single physical channel stream of frames
    Implements CSTS MC multiplexing scheme
    Does NOT generate OID Frames
      OID Frame generation is performed by FLF Sync, Channel Coding and OID Generation FR
Candidate FR MIB definition has been developed by W. Hell
  J. Pietras is in the process of reviewing the FR MIB definition and updating the FRM MB definition

## Slide 18: FRM Tier-2 – Status and Open Points: FLF USLP VC Multiplexing
VLF USLP VC Multiplexing FR
  USLP VC Multiplexing function (FLF aspects)
    Merges VC streams of frames into a single MC stream of frames
    Implements CSTS VC multiplexing scheme
Candidate FR MIB definition has been developed by W. Hell
  J. Pietras is in the process of reviewing the FR MIB definition and updating the FRM MB definition
Note: For uses other than ESLTs, this FR would also include injection of USLP_MC_OCFs, but it has been omitted from the current FR definition because for ESLTs that’s not possible
    For the same reason, MC-OCF and VC-OCF input are not included in TM and AOS Mux FRs

## Slide 19: FRM Tier-2 – Status and Open Points: VLF USLP MC Demultiplexing
VLF USLP MC Demultiplexing FR
  USLP All Frames Reception function (VLF aspects)
    Frame delimiting, fill removal, and frame validity check
  USLP MC Demultiplexing function (VLF aspects)
    Demuxes MCs from a single stream of physical channel frames
Candidate FR MIB definition has been developed by W. Hell
  J. Pietras is in the process of reviewing the FR MIB definition and updating the FRM MB definition
Work to be done
  Add table of truncated frame lengths for VCs in the MC
  Finish FRM MB definition

## Slide 20: FRM Tier-2 – Status and Open Points: VLF USLP VC Demultiplexing
VLF USLP VC Demultiplexing FR
  USLP Master Channel Reception function (VLF aspects)
    Decommutates USLP_MC_OCFs out of the MC
  USLP VC Demultiplexing function (VLF aspects)
    Demuxes VCs from a single MC
Candidate FR MIB definition has been developed by W. Hell
  J. Pietras is in the process of reviewing the FR MIB definition and updating the FRM MB definition
Open points: Unlike TM and AOS, the presence of OCF is signaled in each frame
  A CLCW extraction table of OCF-bearing VCs is not strictly necessary
  Perhaps a simple ocfsPresentOnMc Boolean parameter is sufficient

## Slide 21: FRM Tier-2 – Status and Open Points: FLF USLP MC Demultiplexing
FLF USLP MC Demultiplexing FR
  USLP MC Demultiplexing function (VLF aspects)
    Demuxes MCs from a single stream of physical channel frames
Candidate FR MIB definition has been developed by W. Hell
  J. Pietras is in the process of reviewing the FR MIB definition and updating the FRM MB definition
FR MIB appears to be okay at the moment, but the FRM MB definition needs to be completed

## Slide 22: FRM Tier-2 – Status and Open Points: FLF USLP VC Demultiplexing
FLF USLP VC Demultiplexing FR
  USLP Master Channel Reception function (FLF aspects)
    Decommutates USLP_MC_OCFs out of the MC
  USLP VC Demultiplexing function (FLF aspects)
    Demuxes VCs from a single MC
Candidate FR MIB definition has been developed by W. Hell
  J. Pietras is in the process of reviewing the FR MIB definition and updating the FRM MB definition
Open points: Unlike TM and AOS, the presence of OCF is signaled in each frame
  A CLCW extraction table of OCF-bearing VCs is not strictly necessary
  Perhaps a simple ocfsPresentOnMc Boolean parameter is sufficient

## Slide 23: FRM Tier-2 – Status and Open Points: Non-validated Radiometric Data Collection
Definition spans collection of radiometric and weather data into a Tracking Data Message (TDM)-formatted file
Candidate FR MIB definition has been developed by W. Hell
  J. Pietras reviewed first draft and provided review comments
  W. Hell updated the definition in response to the comments
  J. Pietras has not yet reviewed the updated definition

## Slide 24: FRM Tier-2 – Status and Open Points: Data Store FRs
Non-validated Radiometric Data Store, Validated Radiometric Data Store, and D-DOR Raw Data Store
Candidate FR MIB definitions have been developed by W. Hell
  J. Pietras reviewed first drafts and provided review comments
  W. Hell updated the definitions in response to the comments
  J. Pietras has not yet reviewed the updated definitions
Open Point: Qualified SCIDs may impact Data Store definitions

## Slide 25: FRM Magenta Book Status
SAP names
Need to systematically address how ancillary interfaces are identified in the book and MIB parameters
Need to analyze impact of Qualified SCIDs on Data Stores
Open point: how should partial FR Sets be addressed in the published version of the Magenta Book?
  “Upper” FRs in SDLP FR Sets are not included in Tiers 1 & 2
    Not needed now that CFDP Entity and SLE FSP are no longer in Tiers 1 & 2
  Possible options
    Identify them as future FRs and keep them in the diagrams (current approach in FRM MB)
      When the FRs are eventually developed, that may not even look like what we currently assume
    Ignore them completely
    Do not identify specific future FRs, but identify the functionality that will be covered by future versions of the FR Sets, e.g., USLP MAP Multiplexing
      Limit FR Set diagrams to the defined Tier-1 and Tier-2 FRs