## Slide 1
Initial Thoughts on Event Sequences

## Slide 2: Context
Input to this presentation is the Erik’s ‘Strawman of proposed event sequence structuring’ from 11 Oct 2017
Still not too clear about the goal of Event Sequences
  Provide a common understanding for mission and network provider what shall happen during a pass
  Support pass automation at the ground station?
  Mission specific ad-hoc actions (change bitrate) at defined intervals?
  X-support?
Output seems to be ‘mission sequence’ and (per carrier) a ‘provider sequence’ – differences?

## Slide 3: Sates and State Machines
Apparently the Event Sequences are representing sequences of states:

## Slide 4: Formalize State Machines
If we know states we can model state machines
What triggers state transitions?
One-way tracking
Two-way tracking
?
?

## Slide 5: Functional Resource Model
Can we use the Functional Resource Model (FRM) somehow in the context of Event Sequences?
The FRM is an abstraction of ground equipment, in principle it can provide
  Observable events (e.g. loss of lock, CLCW information)
  Directives to do something (e.g. start uplink)
  Parameters for monitoring
Can we use the FRM ‘Vocabulary’ in terms of
  Events -> Real Time Events / Predicted Events
  Directives -> Real Time / Time Tagged

## Slide 6: Try an Example

## Slide 7: Example
Un-Locked
Return Carrier Locked
FRM Event
Carrier Lock
Data Transport
FRM Event
Frame Sync
FRM Directive (time tagged or real time)
Change Symbolrate
[rate=high]
[rate=high]
#2
[rate=low]
[rate=low]
Un-Locked
Return Carrier Locked
Data Transport
[rate = low]
Data Transport
[rate = high]
Un-Locked
Return Carrier Locked
State sequence (Time Domain)
Carrier Lock
Frame Sync
Carrier Lock
Frame Sync
Directive Change Symbol Rate
State Machine

## Slide 8
All events and states occur in two flavors
  Predicted
  Realtime
At pass execution time they should ‘match’ with some margin. If FRM concepts are used we can use
  MD-CSTS for Real Time Event Detection
  SC-CSTS for Directive Invocation (or time tagged)
Can Event Sequences been seen as a layer on top of the FRM?
If we do *not* use the FRM vocabulary, how do MD-CSTS and SC-CSTS relate to Event Sequencing?