## Slide 1
Current PIF Status
Fall Meeting 2017
C. R. Haddow November 2017

## Slide 2: Decisions from San Antonio Meeting
  Replace OWLT by RTLT
  Add RTLT as an optional parameter to all PIF COMMS events
    But also keep separate RTLT event
  Add Azimuth and Elevation as optional parameters to all PIF COMMS events
    But also keep separate
      ElevationAscendingEvent
      ElevationDescendingEvent
      MaximumElevationEvent
    Events.
  Split KeyholeEvent into 2;
    KeyholeStartEvent
    KeyholeEndEvent

## Slide 3: Erik’s Comments 28th August
1 | ElevationAscendingEvent | Ascending angle of elevation with respect to aperture (ground or spacecraft), i.e. when the aperture passes through a specified angle when ascending. | Do we need to state the context/assumptions here? Presumably the event is trigged crossing some well recognized thresholds? If so do we need to state them, and/or do we assume that eventually we might think about some parameterization in the SMURF to request events for specific elevations (in degrees), or some specifically named (perhaps unique to the provider) mask/event type.
3 | MaximumElevationEvent | Maximum elevation with respect to aperture (ground or spacecraft) | What is the frame of reference for spacecraft in free space? Assume that if on another celestial body reference point is local horizon?
4 | OccultationStartEvent | Start of occultation with respect to aperture (ground or spacecraft) | Might need another parameter for "soft" occultations -- DSN currently distinguishes "hard" occultation, and also entering/exiting atmosphere (of another planet), umbra, and penumbra. This should be easy to accomdate by adding an additional parameter to indicate type of occultation.
6 | SunAlignmentAngleEvent | Sun alignment angle – see section 3.3.1.1 for definition of this. | Is this a "warning" or to be output for every event? If a warning, what is the threshold for emitting this event? That might be a value specific to the service provider?
7 | RangeEvent | Distance with respect to aperture (ground or spacecraft) | Not sure what this really means. Does this mean exceeding some range? Or is this is used to indicate apopapsis, periapsis, that kind of thing?
8 | RangeRateEvent | Rate at which the range is changing with respect to aperture (ground or spacecraft) | Not sure what this really means. Does this mean exceeding a doppler dynamic threshold? If so, assume that this provider specific?
9 | OwltEvent | One Way Light Time with respect to aperture (ground or spacecraft) | Overcome by events? RTLT is to be included for every event, correct? If so, then we have the value (just divide by 2).
14 | KeyholeEvent | Keyhole occurrence at aperture | Believe this is to be split into two events for start and end?
15 | CableWrapEvent | Cable wrap occurrence at aperture. | Believe this is to be split into two events for start and end?

## Slide 4: Marcin’s Comments on Erik’s Comments 13th Sept
1. I agree with Erik’s comment here, this event needs additional specification or naming (like ElevationAscendingEvent5Deg, ElevationAscendingEvent10Deg, etc…).
3. This one may be treated two way: either it has no meaning for free space spacecraft station, or this would define the closest distance within the visibility range (however the visibility be limited).
4. Comment from Erik is fine for me and additional (optional) parameter would be ok.
6. No special thoughts on that. Erik’s comment is valid.
7. I think this is straight forward – if some distance/range is reached (no difference from which direction coming) the event is being generated. The exact meaning will become apparent in context with other surrounding events (like Elevation ones).
8. This would be analogue to the above, just wrt range rate.
9. No special thoughts. Erik has a point in his comment though.
14. On the first shot, I’d agree with Erik (split it into start and stop event), but maybe I’m overseeing something. I have an impression we already discussed that, but not remember.
15. As above.

## Slide 5: Current PIF UML Model

## Slide 6: Service Management Abstract Event

## Slide 7: Abstract Parameter