## Slide 1: XFDU for TGFT
9 May 2017
John Pietras
Global Science and Technology, Inc.

## Slide 2: Outline
Concept for using XFDUs for TGFT
Simplification of XFDU Manifest for TGFT (component by component)
File naming conventions
Extending XFDU with TGFT-specific and TGFT-using-service-specific metadata
Example XFDU Manifest

## Slide 3: Concept for using XFDUs for TGFT (1 of 2)

## Slide 4
Concept for using XFDUs for TGFT (2 of 2)

## Slide 5: Simplification of XFDU Manifest for TGFT (Component by Component)
In the Tech Note, section 2 provides the rationale fro inclusion/exclusion of attributes and parameters, and section 3 provides the resulting composition rules
The standard CCSDS XFDU Manifest comprises five major components
  Package Header
  Information Package Map
  Data Object Section
  Metadata Section
  Behavior Section

## Slide 6: Top-Level XFDU Manifest Schema
Version of the XFDU specification.
For TGFT, value is “1.0”
Intended to contain
executable code
– not used for TGFT

## Slide 7
Package Header
For TGFT, default value is “PkgHdr”, but services
may redefine (e.g., for sequences of XFDUs)
For TGFT, at least one instance is
required, containing a required
extension element

## Slide 8: Information Package Map
For TGFT, this is required and is used
to identify the service to which the
XFDU belongs
One Content Unit
per payload
data file
For TGFT, only one
Data Object per
Content Unit
For TGFT, used to add per-payload-
data-file, TGFT-specific and TGFT-
using-service-specific metadata
Points to Data Object
for the payload data file
Points to the set of metadataObjects
associated with the payload data file
For this content unit
For TGFT, required for XFDU
Packages containing more than one
Payload data file

## Slide 9: Data Object Section
Pointed to by dataObjectID attribute of
informationPackageMap:contentUnit:dataObjectPointer
element
For TGFT, this is always “URL”
For TGFT, is the URL of the
payload data file within the
same zipped/tarred
XFDU Package
For TGFT, only
one byteStream
per dataObject

## Slide 10: Metadata Section
For TGFT, this is either absent
or “OTHER” (use defined by service)
For TGFT, this is either absent
or “OTHER” (use defined by service)
For TGFT, this is either absent or the
name of the service-specific classification
For TGFT, this is either absent or the
name of the service-specific category
Pointed to by anyMdID
attribute of content unit(s)
For TGFT, this is
always “URL”
For TGFT, is the URL of the
metadata file within the
same zipped/tarred
XFDU Package
-OR-
File at remote location

## Slide 11: File Naming and Packaging Conventions
XFDU Package
  Packaged as a zipped/tarred folder containing
    XFDU Manifest file
    One or more payload data files
    Zero or more metadata files
  XFDU Package name = <service-specific part>+<timestamp part>.zip|tar
    <service-specific part> constrained to the character set {[a-z], [0-9], -, _, .}
    <timestamp part> is a modified CCSDS ASCII Time Code B: <YYYY>-<DDD>T<hh>-<mm>-<ss>Z (dashes instead of colons in HHMMSS substring)
XFDU Manifest file naming convention is left to the service, except that the file extension type shall be “.xfdu”
Payload data file naming convention is left to the service
Embedded metadata file naming convention is left to the service
Remote metadata file naming conventions are left to the creators of those files

## Slide 12: Extending XFDU with TGFT-Specific and TGFT-Using-Service-Specific Metadata
Two TGFT XFDU extension schema types are defined
  TgftXfduExtensionType to add TGFT-standard metadata parameters that apply to the XFDU Package as a whole
  TgftContentUnitExtensionType to add metadata parameters that apply to individual payload data files
  Actual TGFT parameters of both schema types are still TBD: the following are examples

## Slide 13: Candidate TGFT XFDU Extension Metadata Parameters Identified at Rome Meeting (1 of 2)
Number of Files: Not covered by XFDU standard; could be added to TgftXfduExtensionType
File Name: Covered by XFDU standard
File version: Not covered by XFDU standard; could be added to TgftContentUnitExtensionType
Creation Date (of individual payload files): Not covered by XFDU standard; could be added to TgftContentUnitExtensionType
File Content Type (not sure what this means. XFDU has mime and unitType attributes that may service this purpose)
File size: Covered by XFDU standard
File encoding (binary, ASCII, etc.): Not covered by XFDU standard; could be added to TgftContentUnitExtensionType
Security Credentials (per each payload data file?): Not covered by XFDU standard; could be added to TgftContentUnitExtensionType

## Slide 14: Candidate TGFT XFDU Extension Metadata Parameters Identified at Rome Meeting (2 of 2)
Originator: Not covered by XFDU standard; could be added to TgftXfduExtensionType
Recipient: Not covered by XFDU standard; could be added to TgftXfduExtensionType
Valid dates (start/end times): Not covered by XFDU standard;
  Is this for the whole XFDU Package or for each individual payload data file?
Description/Reason: Presumably covered by the various text attributes
Checksum: Covered by XFDU standard
Category: Not covered by XFDU standard; what does this mean? (could be added to TgftContentUnitExtensionType)
Identifier: Multiple identifiers throughout the XFDU Manifest, but do they service the purpose intended by this?
Sequence Number: Covered by the order attribute of the Content Unit

## Slide 15: Example XFDU Manifest (XmlSpy Grid View)
SANA repository
TDM file embedded in XFDU Package
.tdm