Message Abstraction Layer Prototype Test plan AND REPORT

DRAFT CCSDS Record

CCSDS 000.0-Y-0

Draft Yellow Book

September 2009

FOREWORD

[Foreword text specific to this document goes here.  The text below is boilerplate.]

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This document is therefore subject to CCSDS document management and change control procedures, which are defined in the Procedures Manual for the Consultative Committee for Space Data Systems.  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- British National Space Centre (BNSC)/United Kingdom.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt e.V. (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- Centro Tecnico Aeroespacial (CTA)/Brazil.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- MIKOMTEK: CSIR (CSIR)/Republic of South Africa.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

# DOCUMENT CONTROL

| Document | Title and Issue | Date | Status |
| --- | --- | --- | --- |
| CCSDS 000.0-Y-0 | [Document Title], Draft CCSDS Record, Issue 0 | September 2009 | Current draft |

# CONTENTS

Section	Page

DOCUMENT CONTROL	iii

CONTENTS	iv

1	Introduction	1-1

1.1	Purpose	1-1

1.2	scope	1-1

1.3	structure of this report	1-1

1.4	definitions (terms,  nomenclature, conventions)	1-1

1.5	references	1-1

1.6	References	1-1

2	OVERVIEW	3

2.1	TEST APPROACH	3

2.2	TESTS OVERViEW	4

2.3	test Results SUMMARY	5

3	Test scenarios	6

3.1	IP test scenario	7

3.2	Data type test scenario	25

3.3	Error test scenario	26

3.4	Access control test scenario	32

3.5	Transport test scenario	33

4	MALPrototype Service Specification	38

4.1	IPTest Service	38

4.2	DataTest Service	49

4.3	ErrorTest Service	50

5	MALPrototype Data Types	58

5.1	Data Structures	58

5.2	IPTest Service Structures	58

6	Compliance matrix	64

6.1	Message Abstraction Layer	64

6.2	Data types	68

6.3	Errors	68

# Introduction

## Purpose

This test report provides a record of the interoperability testing that occurred in support of the production of the CCSDS recommendation 521.0, MISSION OPERATIONS—MESSAGE ABSTRACTION LAYER.

## scope

This test report addresses primarily the formal prototype interoperations that occurred between the ESA developed prototype and the CNES developed prototype, against the formally released Red-1.1 version of the draft Message Abstraction Layer recommendation identified in 1.1.

## structure of this report

This test report is organized as follows:

- Section 1 provides purpose and scope, definitions and references used throughout the report;

- Section 2 gives an overview of the test report and a summary of the test results;

- Section 3 defines the test scenarios;

- Section 4 defines the test services;

- Section 5 defines the test data structures;

- Section 6 gives the compliance matrix.

## definitions (terms,  nomenclature, conventions)

TBS.

## references

## References

The following documents are referenced in this document.  At the time of publication, the editions indicated were valid.  All documents are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the documents indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS documents.

[A list of documents referenced in this document goes here.  See CCSDS A20.0-Y-2, CCSDS Publications Manual (Yellow Book, Issue 2, June 2005) for reference list format.]

[Further references are TBS]

# OVERVIEW

This document provides a record of the prototype interoperations conducted in support of the development of the CCSDS recommendation for Mission Operations Message Abstraction Layer.

The European Space Agency (ESA), and the Centre National d’Etudes Spatiales (CNES) of France each developed prototype implementations of the draft CCSDS recommendation.

## TEST APPROACH

The tests check that two independent implementations of the MAL interoperate as specified by the CCSDS recommendation.

Two distinct stacks are built by assembling the following components:

- Test application

- Service specific API

- Service stubs and skeletons

- MAL API

- MAL implementation

- Security API

- Security implementation

- Transport API

- Transport adapter implementation

- Message transport

The figure below presents the two stacks:

Figure 2-1 Initial MAL prototype

The following components are separately produced by ESA and CNES:

- Service specific API

- Service stubs and skeletons

- MAL API

- MAL implementation

- Security API

- Security implementation

- Transport API

The other components are shared by ESA and CNES:

- Test application

- Transport adapter implementation

- Message transport

## TESTS OVERViEW

Five test scenarios are developed each verifying one aspect of the MAL book:

- Interaction Patterns

- Data types

- Standard errors

- Access control

- Transport

## test Results SUMMARY

### general discussion

TBS

### TEST RESULTS

TBS

# Test scenarios

A scenario is comprised of several test cases. Each test case launches several test procedures.

Scenarios, test cases and procedures are uniquely identified by a name. They also have a status that can be RUN, DONE or FAIL.

All the scenarios are coordinated at the consumer side:

- They are started by a consumer initiating an interaction

- The status of scenarios, test cases and procedures is determined on the consumer side.

Of course, assertions can be checked on both sides: consumer and provider.

A test procedure is in charge of checking a set of assertions. There are two possible results for an assertion: OK (the assertion succeeded) or ERROR (the assertion failed).

A test procedure is DONE if it completes and if all the assertions are OK. If it is not completed, its status is RUN. If it is completed and if at least one assertion is in ERROR then its status is FAIL.

A test case is DONE if all the test procedures complete with the status DONE. If at least one procedure is not completed, its status is RUN. If all the procedures have completed and if at least one of them is FAIL then the test case status is FAIL.

A scenario is DONE if all the test cases complete with the status DONE. If at least one test case is not completed, its status is RUN. If all the test cases have completed and if at least one of them is FAIL then the scenario status is FAIL.

Providers are implemented as specified in section 4.

Two processes are launched:

- The first one is called the “TestCoordinator” process. It launches the test procedures.

- The second one is called the “TestPeer” process.

The “TestPeer” process instantiates the following providers:

- One IPTest provider with a private broker

- Two IPTest providers using the same shared broker

- DataTest provider without broker

The parameters of the shared broker are listed below:

| Broker name | AuthenticationId | Provider max number |
| --- | --- | --- |
| SharedBroker | {0x01, 0x02} | 1 |

The parameters of the providers are listed below:

| Provider name | Service | AuthenticationId | Broker |
| --- | --- | --- | --- |
| IPTest-private | IPTest | {0x02, 0x03} | Private broker |
| IPTest-shared1 | IPTest | {0x02, 0x04} | Shared broker “SharedBroker” |
| IPTest-shared1 | IPTest | {0x02, 0x05} | Shared broker “SharedBroker” |
| DataTest | DataTest | {0x02, 0x06} | No broker |

It writes the URIs of providers and brokers into a properties file that is read by the TestCoordinator process.

The TestCoordinator process is launched after the TestPeer started in order that:

- The providers are ready to be called

- The URIs properties file is ready to be read by the TestCoordinator

A properties file enables to share the values of the following data:

- Providers authentication identifiers

- Shared broker authentication identifier

## IP test scenario

Two test cases are defined:

- The first one tests every interaction pattern except the Pub/Sub pattern.

- The second one is dedicated to the Pub/Sub pattern which is different as it does not involve the provider in the same way and it is more complex. Several aspects of the Pub/Sub pattern need to be tested. One test procedure is done for each of them.

Pub/Sub tests are to be done with a private and a shared broker.

Two constraints are required in order to check the IP state charts:

- no message loss

- FIFO message ordering is required

As a consequence, the Best Effort QoS can only be used if the specific transport layer ensures in the context of the test bed that messages are delivered exactly once and according to a FIFO ordering.

### Test case: all patterns except Pub/Sub

The consumer initiates the patterns by calling the following operations provided by the service IPTest:

- send

- submit

- request

- invoke

- progress

Those operations shall be called once for each QoS level and session type. It is not necessary to test each combination of QoS and session. One call for each QoS level and session type is enough.

The following parameters are used to make the calls:

| authenticationId | {0x00, 0x01} |
| --- | --- |
| qos | Best Effort, Assured, Queued, Timely |
| priority | 1 |
| domain | {“Test”, “Domain”} |
| networkZone | “TestNetwork” |
| session | Live, Simulation, Replay |
| session name | If the session type is Live, the name is “LIVE”. If the session type is Replay, the name is “R1”. If the session type is Simulation, the name is “S1”. |

Moreover it is necessary to go through all the transitions of the IP state charts. The following IPTestDefinitions have to be instantiated. The table only gives the IPTestTransitionType part of the IPTestTransition. The faulty transitions are underlined. In the faulty case, the field 'errorCode' of the IPTestTransition is set to the value INCORRECT_STATE otherwise it is set to “-1”. The field 'Transition list id' is used to identify the test procedure.

| IPTest operation | IPTestTransitionList | Transition list id |
| --- | --- | --- |
| submit | {ACK} | 1 |
|  | {ACK_ERROR} | 2 |
|  | {ACK, ACK_ERROR} | 3 |
|  | {ACK_ERROR, ACK_ERROR} | 4 |
| request | {RESPONSE} | 1 |
|  | {RESPONSE_ERROR} | 2 |
|  | {RESPONSE, RESPONSE} | 3 |
|  | {RESPONSE_ERROR, RESPONSE} | 4 |
| invoke | {ACK, RESPONSE} | 1 |
|  | {ACK, RESPONSE_ERROR} | 2 |
|  | {ACK_ERROR} | 3 |
|  | {ACK, RESPONSE, RESPONSE} | 4 |
|  | {ACK, RESPONSE_ERROR, RESPONSE} | 5 |
|  | {ACK_ERROR, ACK} | 6 |
|  | {RESPONSE, ACK, RESPONSE} | 7 |
| progress | {ACK, RESPONSE} | 1 |
|  | {ACK, RESPONSE_ERROR} | 2 |
|  | {ACK_ERROR} | 3 |
|  | {ACK, UPDATE, UPDATE, RESPONSE} | 4 |
|  | {ACK, UPDATE, UPDATE, UPDATE_ERROR} | 5 |
|  | {ACK, UPDATE, UPDATE, RESPONSE_ERROR} | 6 |
|  | {ACK, RESPONSE, RESPONSE} | 7 |
|  | {ACK, RESPONSE_ERROR, RESPONSE} | 8 |
|  | {ACK_ERROR, ACK} | 9 |
|  | {UPDATE, ACK, UPDATE, UPDATE, RESPONSE} | 10 |
|  | {UPDATE_ERROR, ACK, UPDATE, UPDATE, RESPONSE} | 11 |
|  | {RESPONSE, ACK, UPDATE, UPDATE, UPDATE_ERROR} | 12 |
|  | {ACK, UPDATE, UPDATE, UPDATE_ERROR, RESPONSE} | 13 |
|  | {ACK, UPDATE, UPDATE, RESPONSE_ERROR, RESPONSE} | 14 |

The consumer has to execute the following test procedure for every possible header values (QoS and session fields) and every possible transition. The name of the procedure is built from the parameters:

- ip: name of the tested IP

- qos: QoS level to be used

- session: session type to be used

- transition list id: identifier of the IPTestTransitionList that is expected by the consumer (see table above).

#### Test procedure: <ip>/<qos>/<session>/<transition list id>

The test procedure does the following actions:

- Call the operation <ip> provided by the IPTest service with the parameters passed to the test procedures: 'ip', 'qos', 'session' and 'transition list id'.

- Wait for the expected transitions to be done, except the faulty ones that are ignored.

- Call the operation 'getResult' provided by the IPTest service.

- Check the provider assertions from the IPTestResult returned by 'getResult'

- Check the message header

- Check the transitions

##### Check message header

When the consumer receives a MAL message it has to check that the header is the same as the expected header.

The expected header is deduced from the IPTestDefinition as follows:

| Field | Assigned with |
| --- | --- |
| URIfrom | The provider's URI |
| authenticationId | Authentication id of the provider (statically defined) |
| URIto | Field 'consumerURI' of the IPTestDefinition. |
| timestamp | Field 'timestamp' of the IPTestDefinition. |
| QoSlevel | Field 'qos' of the IPTestDefinition. |
| priority | Field 'priority' of the IPTestDefinition. |
| domain | Field 'domain' of the IPTestDefinition. |
| networkZone | Field 'networkZone' of the IPTestDefinition. |
| session | Field 'session' of the IPTestDefinition. |
| sessionName | Field 'sessionName' of the IPTestDefinition. |
| interactionType | Interaction type used by the operation, e.g. the operation “send” uses a SEND interaction type. |
| interactionStage | Expected interaction stage as specified by the IPTestDefinition |
| transactionId | Assigned with the transaction identifier returned by the provider in the structure IPTestResult. |
| area | The test area name “MALPrototype”. |
| service | The test service name “IPTest”. |
| operation | The operation name. |
| version | The test service version. |
| isError | Depends on the expected interaction stage as specified by the IPTestDefinition: True if a *_ERROR transition is expected False otherwise |

For each field, except 'timestamp', the following assertion is made:

| Assertion |
| --- |
| Info | Result |
| Check header field '<field name>' | True if the value of the received header field is equal to the expected value fields False otherwise. |

For 'timestamp' the assertion is:

| Assertion |
| --- |
| Info | Result |
| Check header field 'timestamp' | True if the value of the received header timestamp is greater than the expected header timestamp. False otherwise. |

##### Check the transitions

The following assertion has to be checked for each transition of the IPTestTransitionList:

| Assertion |
| --- |
| Info | Result |
| Check transition step #<transition index in the IPTestTransitionList> | True if the value of the received 'transition stage' is equal to the value of the expected stage (extracted from the IPTestTransitionList) False otherwise. |

### Test case: Pub/Sub interaction

This test checks that the message header is correct during the Pub/Sub interaction.

#### Test procedure: pubsub/<qos>/<session>

The test procedure is described below. It shall be executed once for each QoS level and session type. It is not necessary to test each combination of QoS and session. One execution for each QoS level and session type is enough.

The consumer creates subscriptions from the following parameters:

| subscription id | “sub1” |
| --- | --- |
| authenticationId | {0x00, 0x01} |
| qos | Best Effort, Assured, Queued, Timely |
| priority | 1 |
| domain | {“Test”, “Domain”} |
| networkZone | “TestNetwork” |
| session | Live, Simulation, Replay |
| session name | If the session type is Live, the name is “LIVE”. If the session type is Replay, the name is “R1”. If the session type is Simulation, the name is “S1”. |
| entity expression | {“A”, null, null, null} |
| only on change | false |

##### Check Publish Register and Publish Register acknowledgement

The consumer does the following actions:

- Calls the operation 'publishRegister' with the following parameter:

| TestPublishRegister |
| --- |
| qos | Assured |
| priority | 1 |
| domain | {“Test”, “Domain”} |
| networkZone | “TestNetwork” |
| session | Live |
| session name | “LIVE” |
| update key | {“A”, null, null, null} |
| errorCode | -1 |

- Call the operation 'getResult' provided by the IPTest service.

- Check the provider assertions from the IPTestResult returned by 'getResult'

##### Check Register

The consumer registers for the PubSub operation ‘monitor’.

The Register header is obtained through the test transport module (see section 3.5).

The expected header is built as follows:

| Field | Assigned with |
| --- | --- |
| URIfrom | The broker's URI |
| authenticationId | Parameter 'authenticationId' |
| URIto | The consumer's URI |
| timestamp | Current time before the subscription |
| QoSlevel | Parameter 'qos' |
| priority | Parameter 'priority' |
| domain | Parameter 'domain' |
| networkZone | Parameter 'networkZone' |
| session | Parameter 'session' |
| sessionName | Parameter 'sessionName' |
| interactionType | Pub/Sub |
| interactionStage | 1 |
| transactionId | Not assigned. |
| area | The test area name “MALPrototype”. |
| service | The test service name “IPTest”. |
| operation | The operation name. |
| version | The test service version. |
| isError | False |

For each field, except 'timestamp' and 'transactionId', the following assertion is made:

| Assertion |
| --- |
| Info | Result |
| Check header field '<field name>' | True if the value of the received header field is equal to the expected value fields False otherwise. |

For 'timestamp' the assertion is:

| Assertion |
| --- |
| Info | Result |
| Check header field 'timestamp' | True if the value of the received header timestamp is greater than the expected header timestamp. False otherwise. |

For 'transactionId' the assertion is:

| Assertion |
| --- |
| Info | Result |
| Check header field 'transactionId' | True if the value of 'transactionId' changes at each registration. False otherwise. |

##### Check Register acknowledgement

The expected header is built in the same way as before in section 3.1.2.1.1 except for the fields:

| Field | Assigned with |
| --- | --- |
| authenticationId | The authentication identifier of the broker (statically known) |
| interactionStage | 2 |
| transactionId | Field 'transactionId' of the Register message header. |

For each field, except 'timestamp', the following assertion is made:

| Assertion |
| --- |
| Info | Result |
| Check header field '<field name>' | True if the value of the received header field is equal to the expected value fields False otherwise. |

For 'timestamp' the assertion is:

| Assertion |
| --- |
| Info | Result |
| Check header field 'timestamp' | True if the value of the received header timestamp is greater than the expected header timestamp. False otherwise. |

##### Check Publish

The consumer does the following actions:

- Call the operation 'publishUpdates' provided by the IPTest service. The consumer triggers publications with the entity key {“A”, null, null, null}. Four publications are passed as parameters of the call: one for each update type: creation, update, modification and deletion.

- Call the operation 'getResult' provided by the IPTest service.

- Check the provider assertions from the IPTestResult returned by 'getResult'

##### Check Notify

The consumer checks the updates arrival (not implicit as the Notify reception is asynchronous):

| Assertion |
| --- |
| Info | Result |
| Check Notify messages arrival | True if the four updates have been received. False otherwise. |

The consumer checks the Notify header correctness. The expected header is built in the same way as before in section 3.1.2.1.2 except for the fields:

| Field | Assigned with |
| --- | --- |
| timestamp | Current time before the update publications |
| interactionStage | 6 |

The same assertions as in section 3.1.2.1.2 are done.

##### Check Deregister

The consumer deregisters from the subscription “sub1”.

The Deregister header is obtained through the test transport module (see section 3.5).

The expected header is built in the same way as before in section 3.1.2.1.2 except for the fields:

| Field | Assigned with |
| --- | --- |
| timestamp | Current time before the deregistration. |
| interactionStage | 7 |

The same assertions as in section 3.1.2.1.2 are done.

##### Check Deregister acknowledgement

The expected header is built in the same way as before in section 3.1.2.1.2 except for the fields:

| Field | Assigned with |
| --- | --- |
| timestamp | Current time before the deregistration |
| interactionStage | 8 |

The same assertions as in section 3.1.2.1.2 are done.

##### Check Publish Deregister and Publish Deregister acknowledgement

The consumer does the following actions:

- Calls the operation 'publishDeregister' with the following parameter:

| TestPublishDeregister |
| --- |
| qos | Assured |
| priority | 1 |
| domain | {“Test”, “Domain”} |
| networkZone | “TestNetwork” |
| session | Live |
| session name | “LIVE” |
| errorCode | -1 |

- Call the operation 'getResult' provided by the IPTest service.

- Check the provider assertions from the IPTestResult returned by 'getResult'

#### Test procedure: subscription checking

The consumer calls the operation 'addPublishedEntities' with the entity key “A” and “B”.

The consumer creates the subscription “sub1” defined in test procedure 4.1.2.1 with the QoS level Assured and the session LIVE.

The consumer keeps the transaction identifier of the registration.

The consumer redefines the subscription “sub1” (i.e. the consumer registers again) with two identical entity requests:

- same expression “A”

- same 'only on change' parameter set to the value 'true'.

The consumer triggers two publications in this order:

- key = “A”, type = Update

- key = “A”, type = Modification

The consumer checks:

| Assertion |
| --- |
| Info | Result |
| Check update uniqueness | True if each update arrives only once despite the two entity requests own the same expression. False otherwise. |
| Check 'only on change' | True if the update which type is Update is not received ('only on change' is true). False otherwise. |
| Check the 'transactionId' invariance | True if 'transactionId' is the same as before the subscription redefinition. |

#### Test procedure: publish error

The consumer does the following actions:

- call the operation 'publishRegister' with the entity key {“A”, null, null, null}

- call the operation ‘publishUpdates’ with the following parameter:

| TestPublishUpdate |
| --- |
| qos | Assured |
| priority | 1 |
| domain | {“Test”, “Domain”} |
| networkZone | “TestNetwork” |
| session | Live |
| session name | “LIVE” |
| update key | {“B”, null, null, null} |
| errorCode | UNKNOWN |

This TestPublishUpdate checks that the error UNKNOWN is raised because the entity key {“B”, null, null, null} has not been registered by the provider.

- Call the operation 'getResult' provided by the IPTest service.

- Check the provider assertions from the IPTestResult returned by 'getResult'

#### Test procedure: subscription identifier uniqueness

This test procedure verifies that the URI of the consumer and the subscription identifier form the unique identifier of the subscription.

Two IPTest consumers are created. Two subscriptions with the same identifier “sub1” are created with both consumers as defined below:

| Consumer URI | URI #1 | URI #2 |
| --- | --- | --- |
| subscription id | “sub1” | “sub1” |
| authenticationId | {0x00, 0x01} | {0x00, 0x01} |
| qos | Assured | Assured |
| priority | 1 | 1 |
| domain | {“Test”, “Domain1”} | {“Test”, “Domain1”} |
| networkZone | “TestNetwork” | “TestNetwork” |
| session | Live | Live |
| session name | “LIVE” | “LIVE” |
| entity expression | “A” | “A” |
| only on change | false | false |

The consumer triggers one publication with the key “A” and the update type “Modification”.

The consumer checks:

| Assertion |
| --- |
| Info | Result |
| Check subscription identifier uniqueness | True if the update is received once by both consumers. False otherwise. |

#### Test procedure: subscription entity requests

This test checks that the entity requests are correctly interpreted by the broker, in particular the expression used to define the expected entities.

A list of entity keys is defined:

- A

- A.B

- A.B.C

- A.B.C.D

- B

- Q.B.C

The consumer calls the operation 'addPublishedEntities' with the entity keys list presented above.

A list of entity request expressions is defined:

- A

- A.[null]

- A.*

- A.B.[null]

- A.B.*

- [null].B.[null]

- *.B.*

- *

The consumer does the following actions:

- Creation of one subscription for each expression and registration.

The QoS level is Assured.

- Trigger the publication of one TestUpdate for each entity key.

Use the same header values as in section 3.1.1.

Check that:

| Assertion |
| --- |
| Info | Result |
| Check entity request expression <expression> | True if the expected keys are received and only them (see table below). False otherwise. |

The expected keys depending on the expression used are listed below:

| Expression | Expected keys |
| --- | --- |
| A | A |
| A.[null] | A.B |
| A.* | A, A.B, A.B.C, A.B.C.D |
| A.B.[null] | A.B.C |
| A.B.* | A.B, A.B.C, A.B.C.D |
| [null].B.[null] | A.B.C, Q.B.C |
| *.B.* | A.B, A.B.C, A.B.C.D, B, Q.B.C |
| * | A, A.B, A.B.C, A.B.C.D, B, Q.B.C |

#### Test procedure: registration error

The consumer registers to a private broker in order to receive the updates published by an unknown entity called “C”. The test procedure checks:

| Assertion |
| --- |
| Info | Result |
| Check registration error | True if an error is raised. False otherwise. |

#### Test procedure: notify error

The consumer creates the subscription “sub1” defined in test procedure 3.1.2.1 with the QoS level Assured and the session LIVE. Then the consumer deletes the provider and checks:

| Assertion |
| --- |
| Info | Result |
| Check notify error | True if a Notify error is raised. False otherwise. |

#### Test procedure: publish register error

The consumer does the following actions:

- Calls the operation 'publishRegister' of the provider instance “IPTest-shared1” with the same parameter as in 3.1.2.1.1

- Calls the operation 'publishRegister' of the provider instance “IPTest-shared2” with the same parameter as in 3.1.2.1.1 except the field ‘errorCode’ assigned with TOO_MANY error code.

- Call the operation 'getResult' provided by “IPTest-shared1” and “IPTest-shared2” and check the returned assertions.

#### Test procedure: publish register redefinition

The consumer does the following actions:

- call the operation 'publishRegister' with the entity key {“A”, null, null, null}

- call the operation 'publishRegister' with the entity key {“B”, null, null, null}

- call the operation ‘publishUpdates’ with the following parameter:

| TestPublishUpdate |
| --- |
| qos | Assured |
| priority | 1 |
| domain | {“Test”, “Domain”} |
| networkZone | “TestNetwork” |
| session | Live |
| session name | “LIVE” |
| update key | {“B”, null, null, null} |
| errorCode | -1 |

This TestPublishUpdate checks that no error is raised.

- Call the operation 'getResult' provided by the IPTest service.

- Check the provider assertions from the IPTestResult returned by 'getResult'

## Data type test scenario

A list of MAL data structure instances is statically defined according to the following constraints:

- All the data types shall be instantiated at least once.

- Enumerations shall be instantiated once for each enumerated value.

- Abstract types need to be extended by a concrete type for the test

- The value Null shall belong to the list

- The value Null shall be inserted into a Composite structure

This data list is statically known by the DataTest service provider and consumer.

The consumer takes the data from the list one by one, in the same order, and calls the operation 'testData'. It checks that no error is raised by the provider, especially DATA_ERROR and BAD_ENCODING.

## Error test scenario

The following tests use the ErrorTest service.

### Test case: transport errors

These tests use a specific transport module called “Error transport module” that raises errors depending on the operation called.

This transport module implements the Transport SPI as shown by the following figure:

Both primitives 'Transmit' and 'TransmitMultiple' return the following errors depending on the service and operation names:

| Service | Operation | Error to raise |
| --- | --- | --- |
| ErrorTest | testDeliveryFailed | DELIVERY_FAILED |
| ErrorTest | testDeliveryTimedout | DELIVERY_TIMEDOUT |
| ErrorTest | testDeliveryDelayed | DELIVERY_DELAYED |
| ErrorTest | testDestinationUnknown | DESTINATION_UNKNOWN |
| ErrorTest | testDestinationTransient | DESTINATION_TRANSIENT |
| ErrorTest | testDestinationLost | DESTINATION_LOST |
| ErrorTest | testEncryptionFail | ENCRYPTION_FAIL |
| ErrorTest | testUnsupportedArea | UNSUPPORTED_AREA |
| ErrorTest | testUnsupportedOperation | UNSUPPORTED_OPERATION |
| ErrorTest | testUnsupportedVersion | UNSUPPORTED_VERSION |
| ErrorTest | testBadEncoding | BAD_ENCODING |
| ErrorTest | testUnknown | UNKNOWN |
| IPTest | monitor | ENCRYPTION_FAIL (used in section 3.5.4.2) |

#### Test procedure: Delivery failed

The ErrorTest consumer calls the operation testDeliveryFailed and checks that the error DELIVERY_FAILED is returned.

| Assertion |
| --- |
| Info | Result |
| Check DELIVERY_FAILED error | True if a DELIVERY_FAILED error is raised. False otherwise. |

#### Test procedure:Delivery timedout

The ErrorTest consumer calls the operation testDeliveryTimedout and checks that the error DELIVERY_TIMEDOUT is returned.

| Assertion |
| --- |
| Info | Result |
| Check DELIVERY_TIMEDOUT error | True if a DELIVERY_TIMEDOUT error is raised. False otherwise. |

#### Test procedure:Delivery delayed

The ErrorTest consumer calls the operation testDeliveryDelayed and checks that the error DELIVERY_DELAYED is returned.

| Assertion |
| --- |
| Info | Result |
| Check DELIVERY_DELAYED error | True if a DELIVERY_DELAYED error is raised. False otherwise. |

#### Test procedure:Destination unknown

The ErrorTest consumer calls the operation testDestinationUnknown and checks that the error DESTINATION_UNKNOWN is returned.

| Assertion |
| --- |
| Info | Result |
| Check DESTINATION_UNKNOWN error | True if a DESTINATION_UNKNOWN error is raised. False otherwise. |

#### Test procedure: Destination transient

The ErrorTest consumer calls the operation testDestinationTransient and checks that the error DESTINATION_TRANSIENT is returned.

| Assertion |
| --- |
| Info | Result |
| Check DESTINATION_TRANSIENT error | True if a DESTINATION_TRANSIENT error is raised. False otherwise. |

#### Test procedure: Destination lost

The ErrorTest consumer calls the operation testDestinationLost and checks that the error DESTINATION_LOST is returned.

| Assertion |
| --- |
| Info | Result |
| Check DESTINATION_LOST error | True if a DESTINATION_LOST error is raised. False otherwise. |

#### Test procedure: Encryption fail

The ErrorTest consumer calls the operation testEncryptionFail and checks that the error ENCRYPTION_FAIL is returned.

| Assertion |
| --- |
| Info | Result |
| Check ENCRYPTION_FAIL error | True if a ENCRYPTION_FAIL error is raised. False otherwise. |

#### Test procedure: Unsupported area

The ErrorTest consumer calls the operation testUnsupportedArea and checks that the error UNSUPPORTED_AREA is returned.

| Assertion |
| --- |
| Info | Result |
| Check UNSUPPORTED_AREA error | True if a UNSUPPORTED_AREA error is raised. False otherwise. |

#### Test procedure: Unsupported operation

The ErrorTest consumer calls the operation testUnsupportedOperation and checks that the error UNSUPPORTED_OPERATION is returned.

| Assertion |
| --- |
| Info | Result |
| Check UNSUPPORTED_OPERATION error | True if a UNSUPPORTED_OPERATION error is raised. False otherwise. |

#### Test procedure: Unsupported version

The ErrorTest consumer calls the operation testUnsupportedVersion and checks that the error UNSUPPORTED_VERSION is returned.

| Assertion |
| --- |
| Info | Result |
| Check UNSUPPORTED_VERSION error | True if a UNSUPPORTED_VERSION error is raised. False otherwise. |

#### Test procedure: Bad encoding

The ErrorTest consumer calls the operation testBadEncoding and checks that the error BAD_ENCODING is returned.

| Assertion |
| --- |
| Info | Result |
| Check BAD_ENCODING error | True if a BAD_ENCODING error is raised. False otherwise. |

#### Test procedure: Unknown

The ErrorTest consumer calls the operation testUnknown and checks that the error UNKNOWN is returned.

| Assertion |
| --- |
| Info | Result |
| Check UNKNOWN error | True if a UNKNOWN error is raised. False otherwise. |

### Test case: security errors

A test security module is to be implemented in order to raise errors depending on the operation called:

| Service | Operation | Error to raise |
| --- | --- | --- |
| ErrorTest | testAuthenticationFailure | AUTHENTICATION_FAIL |
| ErrorTest | testAuthorizationFailure | AUTHORIZATION_FAIL |

#### Test procedure: authentication failure

The ErrorTest consumer calls the operation testAuthenticationFail and checks that the error AUTHENTICATION_FAIL is returned.

| Assertion |
| --- |
| Info | Result |
| Check AUTHENTICATION_FAIL error | True if a AUTHENTICATION_FAIL error is raised. False otherwise. |

#### Test procedure: authorization failure

The ErrorTest consumer calls the operation testAuthorizationFail and checks that the error AUTHORIZATION_FAIL is returned.

| Assertion |
| --- |
| Info | Result |
| Check AUTHORIZATION_FAIL error | True if a AUTHORIZATION_FAIL error is raised. False otherwise. |

## Access control test scenario

The Access Control interface has to be implemented by a test security module in charge of checking that the primitive CHECK is called by the MAL. The message passed with the CHECK request is returned to the MAL without being modified through the CHECK Response indication.

The consumer process has to create a MAL instance that uses the test security module.

### Test case: CHECK interaction

#### Test procedure: CHECK interaction

The consumer has to do the following actions:

- create an IPTest consumer

- initiate a Request interaction by calling the operation “request”

- wait for the end of the interaction

- check that the MAL has interacted twice with the Access Control. The following assertion is checked:

| Assertion |
| --- |
| Info | Result |
| Check the CHECK interaction for a message coming from the application and for a message coming from the transport | True if the Access Control primitive “CHECK Request” has been called twice: once for a message which interaction stage is “1” (Request coming from the application) and a second time for a message which interaction stage is “2” (Request response coming from the transport). False otherwise. |

## Transport test scenario

The Transport interface is implemented by a test transport module in charge of:

- Checking that the Transport primitives are called by the MAL

- Keeping the last message that has been transmitted to the transport by the MAL (this feature is used by the test procedures 3.1.2.1 and 3.1.2.9)

- Forwarding the primitive Request to the actual transport layer

- Listening to the Indications triggered by the actual transport and transmitting them to the MAL

This test transport module is an intermediate layer between the MAL and the actual transport used for the test as shown by the following figure:

### Test case: supported QoS interaction

#### Test procedure: supported QoS interaction

An IPTest consumer is created for each available QoS level: BEST_EFFORT, ASSURED, QUEUED and TIMELY. It is important that the MAL instance was not used before as the MAL only calls the SUPPORTEDIP once when first interacting with a specific transport.

The test checks the following assertion:

| Assertion |
| --- |
| Info | Result |
| Check the SUPPORTEDQOS interaction. | True if: the primitive 'SUPPORTEDQOS Request' has been called once by the MAL for each QoS level and the value of the QoSLevel parameter is equal to the QoSLevel used when creating the consumer and the primitive 'SUPPORTEDQOS Indication' has been called once by the actual transport for each QoS level. False otherwise. |

### Test case: supported IP interaction

#### Test procedure: supported IP interaction

A single instance of MAL and an IPTest consumer are created. It is important that the MAL instance was not used before as the MAL only calls the SUPPORTEDIP once when first interacting with a specific transport.

The test checks the following assertion:

| Assertion |
| --- |
| Info | Result |
| Check the SUPPORTEDIP interaction. | True if: the primitive 'SUPPORTEDIP Request' has been called once by the MAL for each InteractionType. and the primitive 'SUPPORTEDQIP Indication' has been called once by the actual transport for each InteractionType. False otherwise. |

### Test case: transmit interaction

#### Test procedure: transmit interaction

An IPTest consumer is created and a Send interaction is initiated by calling the operation “send”.

The test checks the following assertion:

| Assertion |
| --- |
| Info | Result |
| Check the TRANSMIT interaction. | True if: the primitive 'TRANSMIT Request' has been called once by the MAL with a message which interaction stage is “1” (Send coming from the application) and the primitive 'TRANSMIT Indication' has been called once by the actual transport. False otherwise. |

### Test case: transmit multiple interaction

#### Test procedure: transmit multiple interaction

This is a single process test: 'TestCoordinator'. This test doesn't check the MAL interoperability so it is not necessary to have two processes with two MAL implementations.

An IPTest provider and a private broker are created. Two IPTest consumers are created and registered to the private broker through the operation 'monitor. An update is published by calling the operation 'publishUpdates'.

The test checks the following assertion:

| Assertion |
| --- |
| Info | Result |
| Check the TRANSMITMULTIPLE interaction. | True if: the primitive 'TRANSMITMULTIPLE Request' has been called once with two messages which interaction stage is “3” (Publish coming from the application) and the primitive 'TRANSMITMULTIPLE Indication' has been called once by the actual transport. False otherwise. |

#### Test procedure: transmit multiple error

The same test as above (see 3.5.4.1) is launched on top of the “Error transport module” (see section 3.3.1).

The test checks the following assertion:

| Assertion |
| --- |
| Info | Result |
| Check the TRANSMITMULTIPLE Error indication. | True if the error ENCRYPTION_FAIL is caught by the publisher. False otherwise. |

### Test case: receive interaction

#### Test procedure: receive interaction

An IPTest consumer is created and a Request interaction is initiated by calling the operation “request”.

The test checks the following assertion:

| Assertion |
| --- |
| Info | Result |
| Check the RECEIVE interaction. | True if the primitive 'TRANSMIT Request' has been called once by the MAL with a message which interaction stage is “2” (Request response coming from the actual transport) False otherwise. |

### Test case: receive multiple interaction

#### Test procedure: receive multiple interaction

As it is not possible to make the assumption that a transport module uses this interaction, the test transport module has to be enhanced with an operation enabling to trigger a RECEIVEMULTIPLE Indication.

An IPTest consumer is created. It is registered to the IPTest provider private broker running in the “TestPeer” process. One update is published by calling the operation “publishUpdate”. The Notify message is received by the consumer. Then the test procedure copies this message twice, making two Notify messages and directly injects them into the test transport module in order to trigger a RECEIVEMULTIPLE Indication.

The test checks the following assertion:

| Assertion |
| --- |
| Info | Result |
| Check the RECEIVEMULTIPLE interaction. | True if the two Notify messages are received by the consumer. False otherwise. |

# MALPrototype Service Specification

## IPTest Service

This service aims at testing each Interaction Pattern (IP). It provides one operation for Send, Submit, Request, Invoke and Progress. The input parameter is an IPTestDefinition that contains:

- The parameters used by the consumer in order to initiate the interaction. These parameters enable the provider to check whether the received message header is correct or not.

- A list of interaction transitions expected by the consumer.

An operation 'getResult' is provided in order to enable the consumer to get:

- the interaction transaction identifier

- and the assertions evaluated on the provider side during an interaction.

Finally four operations 'monitor', 'addPublishedEntities', 'publishUpdates' and 'publishError' are provided in order to test the Pub/Sub interaction.

### Check message header

When the provider receives a MAL message (initiating an interaction) it has to check that the header is the same as the expected header.

The expected header is deduced from the IPTestDefinition as follows:

| Field | Assigned with |
| --- | --- |
| URIfrom | Field 'consumerURI' of the IPTestDefinition. |
| authenticationId | Field 'authenticationId' of the IPTestDefinition. |
| URIto | The provider's URI. |
| timestamp | Field 'timestamp' of the IPTestDefinition. |
| QoSlevel | Field 'qos' of the IPTestDefinition. |
| Priority | Field 'priority' of the IPTestDefinition. |
| Domain | Field 'domain' of the IPTestDefinition. |
| networkZone | Field 'networkZone' of the IPTestDefinition. |
| Session | Field 'session' of the IPTestDefinition. |
| sessionName | Field 'sessionName' of the IPTestDefinition. |
| interactionType | Interaction type used by the operation, e.g. the operation “send” uses a SEND interaction type. |
| interactionStage | 1 |
| transactionId | Not assigned |
| Area | The test area name “MALPrototype”. |
| Service | The test service name “IPTest”. |
| Operation | The operation name. |
| version | The test service version. |
| isError | False |

The provider creates an InteractionKey and checks that it is unique by adding it into a hash table. The InteractionKey table is never cleaned during the life time of the provider.

For each field, except 'timestamp' and 'transactionId', the following assertion is made:

| Assertion |
| --- |
| Info | Result |
| Check header field '<field name>' | True if the value of the received header field is equal to the expected value fields False otherwise. |

For 'timestamp' and 'transactionId', the assertions are:

| Assertion |
| --- |
| Info | Result |
| Check header field 'timestamp' | True if the value of the received header timestamp is greater than the expected header timestamp. False otherwise. |
| Check header field 'transactionId' | True if the InteractionKey is unique. False otherwise. |

### Check transitions

The provider has to trigger the transitions that are expected by the consumer. Those transitions are specified by the attribute 'transitions' of the operation parameter IPTestDefinition.

For each IPTestTransition, the provider calls the primitive that triggers the transition, catches potential errors and evaluate the following assertion:

| Assertion |
| --- |
| Info | Result |
| Check transition <transition type> | True if: No error is raised and no error is expected. An error is raised and its code is equal to the expected error code. False otherwise. |

### Check Publish header

The Publish header is obtained through the test transport module (see section 3.5).

The expected header is built from the parameter TestPublish as follows:

| Field | Assigned with |
| --- | --- |
| URIfrom | The provider's URI |
| authenticationId | Field 'authenticationId' of the TestPublish |
| URIto | The broker's URI |
| Timestamp | Current time before the publication |
| QoSlevel | Field 'qos' of the TestPublish |
| Priority | Field 'priority' of the TestPublish |
| Domain | Field 'domain' of the TestPublish |
| networkZone | Field 'networkZone' of the TestPublish |
| Session | Field 'session' of the TestPublish |
| sessionName | Field 'sessionName' of the TestPublish |
| interactionType | Pub/Sub |
| interactionStage | 5 |
| transactionId | Not assigned. |
| Area | The test area name “MALPrototype”. |
| Service | The test service name “IPTest”. |
| Operation | The operation name. |
| version | The test service version. |
| isError | False |

For each field, except 'timestamp' and 'transactionId', the following assertion is made:

| Assertion |
| --- |
| Info | Result |
| Check header field '<field name>' | True if the value of the received header field is equal to the expected value fields False otherwise. |

For 'timestamp' the assertion is:

| Assertion |
| --- |
| Info | Result |
| Check header field 'timestamp' | True if the value of the received header timestamp is greater than the expected header timestamp. False otherwise. |

The field 'transactionId' is not used by the Publish request so it is not checked

### Check Publish Error header

The Publish Error header is returned by the MAL API.

The expected header is built from the parameter TestPublishUpdate in the same way as in section 4.1.3 except for the field:

| Field | Assigned with |
| --- | --- |
| URIfrom | The provider's URI |
| AuthenticationId | The broker authentication identifier (statically known from the test configuration data). |
| URIto | The broker's URI |
| isError | True |

The same assertions as in section 4.1.3 are made.

### Check Publish Register header

The Publish Register header is obtained through the test transport module (see section 3.5).

The expected header is built from the parameter TestPublishRegister in the same way as in section 4.1.3 except for the fields:

| Field | Assigned with |
| --- | --- |
| interactionStage | 3 |
| transactionId | Not assigned. |

For each field, except 'timestamp' and 'transactionId', the following assertion is made:

| Assertion |
| --- |
| Info | Result |
| Check header field '<field name>' | True if the value of the received header field is equal to the expected value fields False otherwise. |

For 'timestamp' the assertion is:

| Assertion |
| --- |
| Info | Result |
| Check header field 'timestamp' | True if the value of the received header timestamp is greater than the expected header timestamp. False otherwise. |

For 'transactionId' the assertion is:

| Assertion |
| --- |
| Info | Result |
| Check header field 'transactionId' | True if the value of 'transactionId' changes at each registration. False otherwise. |

### Check Publish Register acknowledgement header

The Publish Register acknowledgement header is returned by the MAL API (this implies to start an asynchronous invocation of the Publish Register interaction).

The expected header is built from the parameter TestPublishRegister in the same way as in section 4.1.3 except for the fields:

| Field | Assigned with |
| --- | --- |
| URIfrom | The provider's URI |
| URIto | The broker's URI |
| AuthenticationId | The broker authentication identifier (statically known from the test configuration data). |
| interactionStage | 4 |
| transactionId | Field 'transactionId' of the Publish Register message header. |

For each field, except 'timestamp', the following assertion is made:

| Assertion |
| --- |
| Info | Result |
| Check header field '<field name>' | True if the value of the received header field is equal to the expected value fields False otherwise. |

For 'timestamp' the assertion is:

| Assertion |
| --- |
| Info | Result |
| Check header field 'timestamp' | True if the value of the received header timestamp is greater than the expected header timestamp. False otherwise. |

### Check Publish Register error header

The Publish Register Error header is returned by the MAL API (this implies to start an asynchronous invocation of the Publish Register interaction).

The expected header is built from the parameter TestPublishRegister in the same way as in section 4.1.6 except for the field:

| Field | Assigned with |
| --- | --- |
| isError | True |

The same assertions as in section 4.1.6 are made.

### Check Publish Deregister header

The Publish Register header is obtained through the test transport module (see section 3.5).

The expected header is built from the parameter TestPublish in the same way as in section 4.1.3 except for the fields:

| Field | Assigned with |
| --- | --- |
| interactionStage | 9 |
| transactionId | Not assigned. |

The same assertions as in section 4.1.5 are made.

### Check Publish Deregister acknowledgement header

The Publish Deregister acknowledgement header is returned by the MAL API (this implies to start an asynchronous invocation of the Publish Register interaction).

The expected header is built from the parameter TestPublishRegister in the same way as in section 4.1.6 except for the fields:

| Field | Assigned with |
| --- | --- |
| interactionStage | 10 |

The same assertions as in section 4.1.6 are made.

### General

The service interface is described below:

| Area Identifier | Service Identifier | Area Number | Service Number | Service Version |
| --- | --- | --- | --- | --- |
| MALPrototype | IPTest | <test area nb> | 0 | 1 |
| Interaction Pattern | Operation Name | Operation Number | Support in replay | Capability Set |
| SEND | send | 100 | No | 100 |
| SUBMIT | submit | 101 | No |  |
| REQUEST | request | 102 | No |  |
| INVOKE | invoke | 103 | No |  |
| PROGRESS | progress | 104 | No |  |
| PUBSUB | monitor | 105 | No |  |
| REQUEST | getResult | 106 | No | 101 |
| SEND | addPublishedEntity | 107 | No | 102 |
| SEND | publishUpdates | 108 | No | 103 |
| SEND | publishError | 109 | No |  |
| SEND | publishRegister | 110 | No |  |
| SEND | publishDeregister | 111 | No |  |

### OPERATION: send

#### General

This operation cleans the assertions table and check that the header of the received message is the same as the one expected (see 4.1.1).

| Operation Name | Send |
| --- | --- |
| Interaction Pattern | SEND |
| IP Sequence | Message | Field Type |
| IN | Send | IPTestDefinition |

### OPERATION: submit

#### General

This operation cleans the assertions table and checks that the header of the received message is the same as the one expected (see 4.1.1). Moreover it triggers the transitions specified by the IPTestDefinition (see 3.1.2).

| Operation Name | Submit |
| --- | --- |
| Interaction Pattern | SUBMIT |
| IP Sequence | Message | Field Type |
| IN | Submit | IPTestDefinition |

#### Errors

The following error can be raised by this operation:

| Error | Error # | Comments |
| --- | --- | --- |
| TEST_ERROR | 70000 | Fake error for testing. |

### OPERATION: request

#### General

This operation cleans the assertions table and checks that the header of the received message is the same as the one expected (see 4.1.1). Moreover it triggers the transitions specified by the IPTestDefinition (see 3.1.2).

| Operation Name | Request |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | IPTestDefinition |
| OUT | Response | MAL::String |

#### Errors

The following error can be raised by this operation:

| Error | Error # | Comments |
| --- | --- | --- |
| TEST_ERROR | 70000 | Fake error for testing. |

### OPERATION: invoke

#### General

This operation cleans the assertions table and checks that the header of the received message is the same as the one expected (see 4.1.1). Moreover it triggers the transitions specified by the IPTestDefinition (see 4.1.2).

| Operation Name | Invoke |
| --- | --- |
| Interaction Pattern | INVOKE |
| IP Sequence | Message | Field Type |
| IN | Request | IPTestDefinition |
| OUT | Acknowledgement | MAL::String |
| OUT | Response | MAL::String |

#### Errors

The following error can be raised by this operation:

| Error | Error # | Comments |
| --- | --- | --- |
| TEST_ERROR | 70000 | Fake error for testing. |

### OPERATION: progress

#### General

This operation cleans the assertions table and checks that the header of the received message is the same as the one expected (see 4.1.1). Moreover it triggers the transitions specified by the IPTestDefinition (see 4.1.2).

| Operation Name | Progress |
| --- | --- |
| Interaction Pattern | PROGRESS |
| IP Sequence | Message | Field Type |
| IN | Request | IPTestDefinition |
| OUT | Acknowledgement | MAL::String |
| OUT | Update | MAL::Integer |
| OUT | Response | MAL::String |

#### Errors

The following error can be raised by this operation:

| Error | Error # | Comments |
| --- | --- | --- |
| TEST_ERROR | <TEST ERROR CODE> | Fake error for testing. |

### OPERATION: getResult

#### General

This operation returns an IPTestResult.

| Operation Name | getResult |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | IPTestResult |

### OPERATION: monitor

#### General

This operation initiates a Pub/Sub interaction. It is not implemented by the service provider but by a broker.

| Operation Name | Monitor |
| --- | --- |
| Interaction Pattern | PUBLISH-SUBSCRIBE |
| IP Sequence | Message | Field Type |
| OUT | Publish/Notify | TestUpdate |

#### Errors

The following error can be raised by this operation:

| Error | Error # | Comments |
| --- | --- | --- |
| UNKNOWN |  | One or more of the entities identified in the registration do not exist. |

### OPERATION: publishRegister

#### General

This operation cleans the assertions table, registers a publisher as specified by the parameter TestPublishRegister and checks the header of the Publish Register message (see 4.1.5).

Moreover if no error is expected by the TestPublishRegister, it checks the header of the Publish Register acknowledgement message (see 4.1.6).

Otherwise it checks the header of the Publish Register error message (see 4.1.7).

| Operation Name | publishRegister |
| --- | --- |
| Interaction Pattern | SEND |
| IP Sequence | Message | Field Type |
| IN | Send | TestPublishRegister |

### OPERATION: publishDeregister

#### General

This operation cleans the assertions table, registers a publisher as specified by the parameter TestPublishDeregister and checks the header of the Publish Deregister message (see 4.1.5).

Moreover if no error is expected by the TestPublishDeregister, it checks the header of the Publish Deregister acknowledgement message (see 4.1.8).

Otherwise it checks the header of the Publish Deregister error message (see 4.1.9).

| Operation Name | publishRegister |
| --- | --- |
| Interaction Pattern | SEND |
| IP Sequence | Message | Field Type |
| IN | Send | TestPublishDeregister |

### OPERATION: publishUpdates

#### General

This operation cleans the assertions table, publishes an update as specified by the parameter TestPublishUpdate and checks the header of the Publish message (see 4.1.3).

Moreover if an error is expected by the TestPublishUpdate then the operation hangs until the error is raised or a timer ends.

The following assertion is checked:

| Assertion |
| --- |
| Info | Result |
| Check the Publish error message arrival | True if the Publish error message arrived. False otherwise. |

The header of the Publish error message is checked (see 4.1.4).

| Operation Name | publishUpdates |
| --- | --- |
| Interaction Pattern | SEND |
| IP Sequence | Message | Field Type |
| IN | Send | TestPublishUpdate |

### OPERATION: publishError

#### General

This operation cleans the assertions table, publishes an update as specified by the parameter TestErrorPublication and checks the header of the Publish message (see 3.1.3).

| Operation Name | publishError |
| --- | --- |
| Interaction Pattern | SEND |
| IP Sequence | Message | Field Type |
| IN | Send | TestErrorPublication |

## DataTest Service

This service aims at testing the data structures.

It provides an operation 'testData' that enables to transmit any Element to the provider and check that it is well interpreted by the provider.

| Area Identifier | Service Identifier | Area Number | Service Number | Service Version |
| --- | --- | --- | --- | --- |
| MALPrototype | DataTest | <test area nb> | 0 | 1 |
| Interaction Pattern | Operation Name | Operation Number | Support in replay | Capability Set |
| REQUEST | testData | 100 | No | 100 |

### OPERATION: testData

#### General

The 'testData' operation allows a consumer to check that a data is correctly decoded on the provider side. The provider needs to statically know the list of data that the consumer is going to send. The consumer selects the data in the same order as the list and calls the operation 'testData'. The provider keeps the index of the currently selected data from the static list. When the operation 'testData' is called, the provider checks that the received data is equal to the selected data from the list. If the equality test fails, then the error DATA_ERROR is raised otherwise the provider returns Null.

| Operation Name | testData |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

#### Errors

The following error can be raised by this operation:

| Error | Error # | Comments |
| --- | --- | --- |
| DATA_ERROR | <DATA ERROR CODE> | Data interoperability error |

## ErrorTest Service

This service aims at testing the MAL errors. It doesn't need to be implemented as it is only used on the consumer side to make the transport layer raise errors (see section 3.3.1).

### General

| Area Identifier | Service Identifier | Area Number | Service Number | Service Version |
| --- | --- | --- | --- | --- |
| MALPrototype | ErrorTest | <test area nb> | 0 | 1 |
| Interaction Pattern | Operation Name | Operation Number | Support in replay | Capability Set |
| REQUEST | testDeliveryFailed | 100 | No | 100 |
| REQUEST | testDeliveryTimedout | 101 | No |  |
| REQUEST | testDeliveryDelayed | 102 | No |  |
| REQUEST | testDestinationUnknown | 103 | No |  |
| REQUEST | testDestinationTransient | 104 | No |  |
| REQUEST | testDestinationLost | 105 | No |  |
| REQUEST | testEncryptionFail | 106 | No |  |
| REQUEST | testUnsupportedArea | 107 | No |  |
| REQUEST | testUnsupportedOperation | 108 | No |  |
| REQUEST | testUnsupportedVersion | 109 | No | 100 |
| REQUEST | testBadEncoding | 110 | No |  |
| REQUEST | testUnknown | 111 | No |  |
| REQUEST | testAuthenticationFailure | 112 | No |  |
| REQUEST | testAuthorizationFailure | 113 | No |  |

### OPERATION: testDeliveryFailed

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Name | testDeliveryFailed |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

### OPERATION: testDeliveryTimedout

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Name | testDeliveryTimedout |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

### OPERATION: testDeliveryDelayed

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Name | testDeliveryDelayed |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

### OPERATION: testDestinationUnknown

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Name | testDestinationUnknown |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

### OPERATION: testDestinationTransient

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Name | testDestinationTransient |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

### OPERATION: testDestinationLost

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Name | testDestinationLost |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

### OPERATION: testEncryptionFail

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Name | testEncryptionFail |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

### OPERATION: testUnsupportedArea

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Name | testUnsupportedArea |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

### OPERATION: testUnsupportedOperation

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Name | testUnsupportedOperation |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

### OPERATION: testUnsupportedVersion

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Name | testUnsupportedVersion |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

### OPERATION: testBadEncoding

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Name | testBadEncoding |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

### OPERATION: testUnknown

#### General

This operation does nothing. Actually the error is raised by the transport layer before the provider is invoked.

| Operation Name | testUnknown |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

### OPERATION: testAuthenticationFailure

#### General

This operation does nothing. Actually the error is raised by the MAL layer before the provider is invoked.

| Operation Name | testAuthenticationFailure |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

### OPERATION: testAuthorizationFailure

#### General

This operation does nothing. Actually the error is raised by the MAL layer before the provider is invoked.

| Operation Name | testAuthorizationFailure |
| --- | --- |
| Interaction Pattern | REQUEST |
| IP Sequence | Message | Field Type |
| IN | Request | MAL::Element |
| OUT | Response | MAL::Element |

# MALPrototype Data Types

This section defines the data types used by the test services (see section 4).

## Data Structures

### Assertion

| Structure Name | Assertion |
| --- | --- |
| Extends | MAL::Composite |
| Short form | test_asrt |
| Field | Type | Comment |
| procedureName | MAL::String | Name of the test procedure that evaluated the assertion. |
| Info | MAL::String | Message explaining what the assertion checks. |
| Result | MAL::Boolean | Boolean indicating whether the assertion succeeded (true) or not (false). |

### AssertionList

| List Name | AssertionList |
| --- | --- |
| Short form | test_asrt_lst |
| List of | Assertion |

## IPTest Service Structures

### IPTestDefinition

This abstract structure is inherited by all the IP test definition structures.

| Structure Name | IPTestDefinition |
| --- | --- |
| Extends | MAL::Composite |
| Short form | test_ip_def |
| Field | Type | Comment |
| procedureName | MAL::String | Name of the test procedure |
| consumerURI | MAL::URI | The consumer's URI |
| authenticationId | MAL:Blob | The authentication identifier used by the consumer |
| Qos | MAL::QoSLevel | The QoS level required by the consumer |
| Priority | MAL::Integer | The priority level required by the consumer |
| Domain | MAL::DomainIdentifier | The domain used by the consumer |
| networkZone | MAL::Identifier | The network zone used by the consumer |
| Session | MAL::SessionType | The type of the session used by the consumer |
| sessionName | MAL::Identifier | The identifier of the session used by the consumer |
| transitions | IPTestTransitionList | The transitions that are requested by the consumer |
| timestamp | MAL::Date | The time the consumer initiated the interaction. |

### IPTestTransitionType

This enumeration is used to require an expected transition from an IP test.

| Enumeration Name | IPTestTransitionType |
| --- | --- |
| Short form | test_ip_trt |
| Enumeration Value | Short form | Comment |
| ACK | 1 | Return an acknowledgement. |
| RESPONSE | 2 | Return a response. |
| ACK_ERROR | 3 | Return an error as an acknowledgement. The error is a TEST_ERROR. |
| RESPONSE_ERROR | 4 | Return an error as a response. The error is a TEST_ERROR. |
| UPDATE | 5 | Return a progress update. |
| UPDATE_ERROR | 6 | Return an error as an update. The error is a TEST_ERROR. |

### IPTestTransition

This structure is used to define an expected transition from an IP test. It asserts what transition is expected and what result is expected from the transition: successful or failure.

| Structure Name | IPTestTransition |
| --- | --- |
| Extends | MAL::Composite |
| Short form | test_ip_tr |
| Field | Type | Comment |
| Type | IPTestTransitionType | The type of the transition to do |
| errorCode | MAL::Integer | The code of the error expected to be raised when doing the transition (failed transition). -1 if no error is expected (successful transition). |

### IPTestTransitionList

| List Name | IPTestTransitionTypeList |
| --- | --- |
| Short form | test_ip_trl |
| List of | IPTestTransition |

### BadHeaderReport

This data structure is an error report produced after having found a faulty header.

| Structure Name | BadHeaderReport |
| --- | --- |
| Extends | MAL::Composite |
| Short form | test_ip_bhr |
| Field | Type | Comment |
| expectedHeader | MAL::MessageHeader | The expected header |
| faultyHeader | MAL::MessageHeader | The header that is not compliant with the MAL rules |

### BadHeaderReportList

This data structure is a list of BadHeaderReport.

| List Name | BadHeaderReportList |
| --- | --- |
| Short form | test_ip_bhrl |
| List of | BadHeaderReport |

### TestPublish

This abstract structure is a publish context.

| Structure Name | TestPublish |
| --- | --- |
| Extends | MAL::Composite |
| Abstract |
| Field | Type | Comment |
| Qos | MAL::QoSLevel | The QoS level to be used by the provider. |
| Priority | MAL::Integer | The priority to be used by the provider. |
| domain | MAL::DomainIdentifier | The domain to be used by the provider. |
| networkZone | MAL::Identifier | The network zone to be used by the provider. |
| Session | MAL::SessionType | The session type to be used by the provider. |
| sessionName | MAL::Identifier | The session name to be used by the provider. |

### TestPublishRegister

This data structure specifies how the IPTest provider shall register.

| Structure Name | TestPublishRegister |
| --- | --- |
| Extends | TestPublish |
| Short form | test_ip_tpr |
| Field | Type | Comment |
| entityKeys | MAL::EntityKeyList | The keys of the entities to be registered. |
| errorCode | MAL::Integer | The code of the Publish Register error expected to be received. -1 if no Publish Register error is expected. |

### TestPublishDeregister

This data structure specifies how the IPTest provider shall register.

| Structure Name | TestPublishDeregister |
| --- | --- |
| Extends | TestPublish |
| Short form | test_ip_tpdr |
| Field | Type | Comment |
| entityKeys | MAL::EntityKeyList | The keys of the entities to be registered. |
| errorCode | MAL::Integer | The code of the Publish Deregister error expected to be received. -1 if no Publish Deregister error is expected. |

### TestPublishUpdate

This data structure specifies how the IPTest provider shall publish an update.

| Structure Name | TestPublishUpdate |
| --- | --- |
| Extends | TestPublish |
| Short form | test_ip_tup |
| Field | Type | Comment |
| updates | MAL::UpdateList | The updates to be published by the provider |
| errorCode | MAL::Integer | The code of the Publish error expected to be received. -1 if no Publish error is expected. |

### TestUpdate

This data structure defines an Update published by the IPTest.

| Structure Name | TestUpdate |
| --- | --- |
| Extends | MAL::Update |
| Short form | test_ip_tu |
| Field | Type | Comment |
| Counter | MAL::Integer | A counter used to distinguish the test updates and to check the ordering. |

### TestErrorPublication

This data structure specifies how the IPTest provider shall publish an error.

| Structure Name | TestErrorPublication |
| --- | --- |
| Extends | TestPublish |
| Short form | test_ip_tep |
| Field | Type | Comment |
| Error | MAL::StandardError | The error to be published by the provider |

### InteractionKey

| Structure Name | InteractionKey |
| --- | --- |
| Extends | MAL::Composite |
| Short form | test_ip_itrk |
| Field | Type | Comment |
| URIfrom | MAL::URI | The consumer's URI |
| transactionId | MAL::Integer | The transaction identifier of the interaction |
| interactionType | MAL::InteractionType | The type of the interaction |
| Service | MAL::Identifier | The name of the called service |
| operation | MAL::Identifier | The name of the called operation |

### IPTestResult

| Structure Name | IPTestResult |
| --- | --- |
| Extends | MAL::Composite |
| Short form | test_ip_tstr |
| Field | Type | Comment |
| transactionId | MAL::Integer | The transaction identifier assigned to the last interaction |
| assertions | AssertionList | The list of assertions checked by the provider. |

# Compliance matrix

This section lists all the requirements specified in the MAL book that are checked by the test scenarios. Some requirements are implicitly tested by the API itself which restricts what a MAL client can do.

The tables below gather the MAL requirements and indicate either the test procedure responsible for checking it or how the Java MAL API implicitly verifies it.

## Message Abstraction Layer

### IP and service interface

The next sections list the MAL requirements and the test procedures in charge of verifying them.

#### Transaction handling (MAL book 3.2)

Test procedures

3.1.1.1 Test procedure: <ip>/<qos>/<session>/<transition list id> Assertion defined on the provider side: 4.1.1 Check message header (field 'transaction id')

3.1.2.1 Test procedure: pubsub/<qos>/<session> Assertion defined in 3.1.2.1.2 Check Register ('transactionId' checking)

#### Error handling (MAL book 3.5.x.4)

Submit (x=2), Request x=3), Invoke (x=4), Progress (x=5):

Test procedure

3.1.1.1 Test procedure: <ip>/<qos>/<session>/<transition list id> 3.1.1.1.1 Check message header (field 'isError')

Send:

Java MAL API: no error can be returned by a provider during a Send interaction.

#### PubSub error handling (MAL book 3.5.6.7)

Test procedures

3.1.2.6 Test procedure: registration error

3.1.2.7 Test procedure: notify error

3.1.2.8 Test procedure: publish register error

3.1.2.3 Test procedure: publish error

#### Operation template and primitives (MAL book 3.5.x.5, 3.5.x.6)

Java MAL API: the consumer and provider interfaces enable to send the Requests and receive the Indications defined for each IP.

#### Requests and Indications (MAL book 3.5.x.8)

Send (x=1), Submit (x=2), Request (x=3), Invoke (x=4), Progress (x=5)

Interaction initiation requests/indications:

Test procedure

3.1.1.1 Test procedure: <ip>/<qos>/<session>/<transition list id> Assertions defined on the provider side: 4.1.1 Check message header

Ack, Response, Update and errors requests/indications:

Test procedure

3.1.2.1 Test procedure: pubsub/<qos>/<session> Check message header

#### Pub/Sub Requests and Indications (MAL book 4.4.6.11)

All requests/indications except errors:

Test procedure

3.1.2.1 Test procedure: pubsub/<qos>/<session>

Error requests/indications:

Test procedures

3.1.2.6 Test procedure: registration error

3.1.2.7 Test procedure: notify error

3.1.2.8 Test procedure: publish register error

3.1.2.3 Test procedure: publish error

#### Pub/Sub overview: unique subscription identifier (MAL book 3.5.6.3 d)

Test procedure

3.1.2.4 Test procedure: subscription identifier uniqueness

#### Pub/Sub description (MAL book 3.5.6.2)

Test procedure

3.1.2.2 Test procedure: subscription checking

#### Pub/Sub entity key matching (MAL book 4.4.6.3)

Test procedure

3.1.2.5 Test procedure: subscription entity requests

#### State Charts (MAL book 3.5.x.7)

Send (x=1), Submit (x=2), Request (x=3), Invoke (x=4), Progress (x=5)

Test procedure

3.1.1.1 Test procedure: <ip>/<qos>/<session>/<transition list id> 3.1.1.1.2 Check the transitions

#### Pub/Sub, state charts, consumer side (MAL book 4.4.6.8.1)

Test procedures

3.1.2.1 Test procedure: pubsub/<qos>/<session>

3.1.2.3 Test procedure: publish error

3.1.2.6 Test procedure: registration error

3.1.2.7 Test procedure: deregistration error

#### Pub/Sub, state charts, provider side (MAL book 4.4.6.8.2)

Test procedures

3.1.2.1 Test procedure: pubsub/<qos>/<session> 3.1.2.1.1 Check Publish Register and Publish Register acknowledgement 3.1.2.1.3 Check Publish 3.1.2.1.8 Check Publish Deregister and Publish Deregister acknowledgement

3.1.2.3 Test procedure: publish error

3.1.2.8 Test procedure: publish register error

### Access control interface

| Requirement | Test procedure |
| --- | --- |
| Check interaction (4.5.2) | Check Check response | 3.4.1.1 Test procedure: CHECK interaction |
|  | Check error | 3.3.2.1 Test procedure: authentication failure |

### Transport interface

| Requirement | Test procedure |
| --- | --- |
| SupportedQoS interaction (4.6.2) | 3.5.1.1 Test procedure: supported QoS interaction |
| SupportedIP interaction (4.6.3) | 3.5.2.1 Test procedure: supported IP interaction |
| Transmit interaction (4.6.4) | Request and indication | 3.5.3.1 Test procedure: transmit interaction |
|  | Error indication | 3.3.1.7 Test procedure: Encryption fail An error is raised by the transport layer during a transmit interaction. |
| Transmit multiple interaction (4.6.5) | Request and indication | 3.5.4.1 Test procedure: transmit multiple interaction |
|  | Error indication | 3.5.4.2 Test procedure: transmit multiple error |
| Receive interaction (4.6.6) | Indication | 3.5.5.1 Test procedure: receive interaction |
| Receive multiple interaction (4.6.7) | Indication | 3.5.6.1 Test procedure: receive multiple interaction |

## Data types

All the data types are checked in section 3.2.

## Errors

| Requirement (5.2) | Test procedure |
| --- | --- |
| DELIVERY_FAILED | 3.3.1.1 Test procedure: Delivery failed |
| DELIVERY_TIMEDOUT | 3.3.1.2 Test procedure:Delivery timedout |
| DELIVERY_DELAYED | 3.3.1.3 Test procedure:Delivery delayed |
| DESTINATION_UNKNWON | 3.3.1.4 Test procedure:Destination unknown |
| DESTINATION_TRANSIENT | 3.3.1.5 Test procedure: Destination transient |
| DESTINATION_LOST | 3.3.1.6 Test procedure: Destination lost |
| AUTHENTICATION_FAIL | 3.3.2.1 Test procedure: authentication failure |
| AUTHORIZATION_FAIL | 3.3.2.2 Test procedure: authorization failure |
| ENCRYPTION_FAIL | 3.3.1.7 Test procedure: Encryption fail |
| UNSUPPORTED_AREA | 3.3.1.8 Test procedure: Unsupported area |
| UNSUPPORTED_OPERATION | 3.3.1.9 Test procedure: Unsupported operation |
| UNSUPPORTED_VERSION | 3.3.1.10 Test procedure: Unsupported version |
| BAD_ENCODING | 3.3.1.11 Test procedure: Bad encoding |
| UNKNOWN | 3.3.1.12 Test procedure: Unknown |
| INCORRECT_STATE | 3.1.1.1 Test procedure: <ip>/<qos>/<session>/<transition list id> Check faulty transitions on the provider side (see 4.1.2) |

[ANNEX TITLE]

[Annexes contain ancillary information.  See CCSDS A20.0-Y-2, CCSDS Publications Manual (Yellow Book, Issue 2, June 2005) for discussion of the kinds of material contained in annexes.]