## Slide 1: Space Communications Cross Support – Architecture Definition Document (SCCS-ARD) Update – 4 January 2021
SES SAWG
4 January 2021
John Pietras
Global Science and Technology, Inc.

## Slide 2: Candidate topics
Consolidating protocol requirements into section 6
Cleaning up the representation of transfer services
Issue: No ABA Space User Node requirements in section 4

## Slide 3: Consolidating protocol requirements into section 6 (1 of 13)
Proposal tentatively approved at 7 December 2020 telecon
  Replace references to specific protocols in sections 4 and 5 with their abstract “layer” names, with a reference to the appropriate subsection of section 6 (Communications View)
    E.g., replace “ABA ESLTs shall implement one or both AOS or TM frame decoding functions (references [X], [Y], [Z])” with “ABA ESLTs shall implement frame synchronization and decoding functions, as specified in 6.?”, where 6.? lists the current protocol requirements for ABA ESLTs
  Put all information regarding optional/required/recommended protocols in section 6
  Proposal: adopt an extended set of PICS Proforma notations in the tables
    M: mandatory
    O: optional
    O<n>: optional, but support of at least one of the group of options labeled by the same numeral <n> is required
    R<n>: the recommended option of a group of options labeled by the same numeral <n> (if and as appropriate)
    C<n>: conditional as defined in corresponding expression below the table
J Pietras agreed to flesh out examples for presentation at the January SAWG telecon
Summary observations
  Section 4 (Services) requirements refer to “services” and their underlying protocols (e.g., RAF, FCLTU, FF-CSTS), whereas Section 5 (Physical) requirements refer to production functionality (e.g., frame synchronization and decoding functions)
    Attempts to address all aspects in a single table proved unwieldy

## Slide 4: Consolidating protocol requirements into section 6 (2 of 13)
Summary observations
  Section 4 (Services) requirements refer to “services” and their underlying protocols (e.g., RAF, FCLTU, FF-CSTS), whereas Section 5 (Physical) requirements refer to production functionality (e.g., frame synchronization and decoding functions)
    Attempts to address all aspects in a single table proved unwieldy
  Modified approach: two sets of tables in section 6
    Mappings of services to protocols (used for cross references from section 4)
    Mappings of production functionality to protocols (used for cross references from section 5)
  I was able to work examples of the services-to-protocols tables, but the production-functionality-to-protocols table(s) are still To Be Supplied
  To accommodate future additions in the services-to-protocols tables, Table 6-4 (Required and Optional ABA ESLT Terrestrial Side Protocols) and been broken into 3 tables
    6-4: Required and Optional ABA ESLT Terrestrial Side Protocols for Space Communication
    6-5: Required and Optional ABA ESLT Terrestrial Side Protocols for Radiometric Data
    6-6: Required and Optional ABA ESLT Terrestrial Side Protocols for Service Management

## Slide 5: Consolidating protocol requirements into section 6 (3 of 13)
Table 6-4 from M-1 issue of SCCS-ARD

## Slide 6: Consolidating protocol requirements into section 6 (4 of 13)
New table 6-4

## Slide 7: Consolidating protocol requirements into section 6 (5 of 13)
New table 6-5

## Slide 8: Consolidating protocol requirements into section 6 (6 of 13)
New table 6-6 (part 1)

## Slide 9: Consolidating protocol requirements into section 6 (7 of 13)
New table 6-6 (part 2)

## Slide 10: Consolidating protocol requirements into section 6 (8 of 13)
Table 6-5 from M-1 issue of SCCS-ARD

## Slide 11: Consolidating protocol requirements into section 6 (9 of 13)
New Table 6-7 (part 1)

## Slide 12: Consolidating protocol requirements into section 6 (10 of 13)
New Table 6-7 (part 2, conditions and options)

## Slide 13: Consolidating protocol requirements into section 6 (11 of 13)
Resulting simplifications in section 4 (1st example)
  Explicit identification of combinations in section 4 (“old style”)

## Slide 14: Consolidating protocol requirements into section 6 (12 of 13)
Resulting simplifications in section 4 (1st example)
  References to section 6 tables (“new style”)

## Slide 15: Consolidating protocol requirements into section 6 (13 of 13)
  Explicit identification of combinations in section 4 (“old style”)
Resulting simplifications in section 4 (1st example)
  References to section 6 tables (“new style”)

## Slide 16: Cleaning up the representation of transfer services
Problem: some of the protocol diagrams misrepresent protocol functionality that is not specific to SLE transfer services and CSTSes by making them part of those services’ “Processing”
  E.g., the VC and MC Mux functions of the ESLT are included in the FF-CSTS Processing functional element even though those protocol functions are used by other (non transfer service) services: CFDP, DTN, and IP over CCSDS
Proposed change: Confine the SLE/CSTS Processing functional elements to represent only the service provision and service-specific production functions associated with that service (if any)
  Protocol functionality that is shared with other services is represented explicitly
Some examples follow – more changes if this approach is adopted

## Slide 17: Figure 6-1: ESLT Fwd / Ret Service Provider Protocol Stack Building Blocks – original
SLE F-CLTU
Processing
RF & Mod
TCP
SLE RAF
Processing
TCP
Frame Sync & De-Code
CSTS F-Frame
Processing
(Frame Muxing)
TCP
Code & Sync
SLE RCF
Processing
(Frame De-Muxing)
TCP
a) SLE F-CLTU
b) SLE RAFs
c) CSTS F-Frame
(multiplex)
d) SLE RCFs
(de-multiplex)
SLE F-CLTU
CSTS F-Frame
SLE RAF
SLE RCF
Frame Sync & De-Code
IP
RF & Mod
IP
RF & De-Mod
IP
RF & De-Mod
IP
Issue:
erroneously
attributes
VC & MC
muxing to
FF-CSTS
Issue:
erroneously
attributes
all VC & MC
demuxing to
SLE RCF.
Each RCF
instance
performs
MC/VC Demux
only for its
(single) service
user

## Slide 18: Figure 6-8: Service User / Provider ABA CSTS Forward-File Building Block - original
CSTS F-Frame
Delivery Service
(Frame Muxing)
RF & Mod
IP
TCP
Code & Sync
Encapsulation
TC/AOS Link Framing
CSTS Forward-
File Processing
CFDP
a) ABA CSTS Forward-File Service Provider
Using CFDP File Delivery over SPP and CSTS F-Frame
CSTS F-Frame
User CSTS Forward-
File Application
IP
TCP
CSTS Transfer File
b) ABA User CSTS Forward-File
(Requires CSTS Transfer-File in Service Provider)
CSTS Transfer File
Issue: Forward File service has nothing to do with FF-CSTS. The only reason FF-CSTS is in this diagram is that frame muxing is (erroneously) attributed to being “owned” by FF-CSTS

## Slide 19: Figure 6-1: ESLT Fwd / Ret Service Provider Protocol Stack Building Blocks – revised
SLE F-CLTU
Processing
RF & Mod
TCP
SLE RAF
Processing
TCP
Frame Sync & De-Code
FF-CSTS Processing
TCP
Code & Sync
TCP
a) SLE F-CLTU
b) SLE RAFs
c) FF-CSTS
d) SLE RCFs
(de-multiplex)
SLE F-CLTU
CSTS F-Frame
SLE RAF
SLE RCF
Frame Sync & De-Code
IP
RF & Mod
IP
RF & De-Mod
IP
RF & De-Mod
IP
VC & MC MUX
SLE and CSTS “Processing” is defined as provision and service-specific production (if any)
SLE RCF
Processing
VC & MC Mux
function is
separated from
CSTS F-Frame
production
Each RCF
instance
performs
MC/VC Demux
only for its
(single) service
user
Callouts are only for this explanation: not to be included in ARD

## Slide 20: Figure 6-8: Service User / Provider ABA CSTS Forward-File Building Block - revised
RF & Mod
IP
TCP
Code & Sync
Encapsulation
TC/AOS Link Framing
CSTS Forward-
File Processing
CFDP
a) ABA CSTS Forward-File Service Provider
Using CFDP File Delivery over EPP
User CSTS Forward-
File Application
IP
TCP
Terrestrial Generic File Transfer
b) ABA User CSTS Forward-File
(Requires Terrestrial Generic File Transfer
Provider)
VC & MC MUX
Terrestrial Generic File Transfer
FF-CSTS-specific entities disappear from the Forward File service profile

## Slide 21: Figure 6-9: Service Provider ABA CSTS Return-File Building Block (original)
SLE RCF
Delivery Service
(Frame De-Muxing)
RF & De-Mod
IP
TCP
Frame Sync & De-Code
Encapsulation
TM/AOS Link Framing
CFDP
ABA CSTS Return-File Service Provider
Using CFDP File Delivery over SPP and SLE RCF
SLE RCF
CSTS Transfer File
CSTS Return-
File Processing
Offline Radiometric
Processing
D-DOR Correlation
Processing
TDM File
TDM File

## Slide 22: Figure 6-9: Service Provider ABA CSTS Return-File Building Block (revised)
RF & De-Mod
IP
TCP
Frame Sync & De-Code
Encapsulation
TM/AOS Link Framing
CFDP
ABA CSTS Return-File Service Provider
Using CFDP File Delivery over EPP
MC & VC Demux
CSTS Transfer File
CSTS Return-
File Processing
Offline Radiometric
Processing
D-DOR Correlation
Processing
TDM File
TDM File
MC/VC Demux
(independent of
RCF service
Instances)

## Slide 23: Figure 6-2: ESLT Radiometric Service Provider Protocol Stack Building Blocks - original
CSTS F-Frame
Processing
(Frame Muxing)
TCP
Code & Sync
SLE RCF
Processing
(Frame De-Muxing)
TCP
TD-CSTS Ranging & Radiometric Data
CSTS F-Frame
SLE RCF
Frame Sync & De-Code
IP
IP
TCP
TD-CSTS
IP
Ranging Sequence Recovery
Ranging Sequence Generation
RF & Mod
RF & De-Mod
Ranging Data
Doppler Data
Ranging
Signal
TD-CSTS
Processing
(Real-time Radiometric Data)

## Slide 24: Figure 6-2: ESLT Radiometric Service Provider Protocol Stack Building Blocks - revised
CSTS F-Frame
Processing
TCP
Code & Sync
SLE RCF
Processing
TCP
TD-CSTS Ranging & Radiometric Data
CSTS F-Frame
SLE RCF
Frame Sync & De-Code
IP
IP
TCP
TD-CSTS
IP
Ranging Sequence Recovery
Ranging Sequence Generation
RF & Mod
RF & De-Mod
Ranging Data
Doppler Data
Ranging
Signal
TD-CSTS
Processing
(Real-time Radiometric Data)
VC & MC MUX
In the case of TD-CSTS, the TD-CSTS Processing functional element performs both service provision and TD-specific production: no change to TD-CSTS oval

## Slide 25: Issue: No ABA Space User Node requirements in Section 4 (1 of 2)
M-1 section 4 outline
  4.2.2 ABA Service User Service Requirements
    4.2.2.1 Current ABA Service User Service Requirements
      All requirements are for ABA Earth User Node only
    4.2.2.2 Future ABA Service User Requirements
      All requirements are for ABA Earth User Node only
  4.2.3 ABA Service Provider Requirements
    4.2.3.1 Current ABA Service Provider Requirements
      All requirements are for ABA ESLTs only (which is okay)
    4.2.3.2 Future ABA Service Provider Requirements
      All requirements are for ABA ESLTs only (which is okay)
  4.3.2 Future SSI Service User Requirements
    Includes requirements on both EUNs and SUNs
  4.3.3 Future SSI Service Provider Requirements
    4.3.3.1 Future SSI Earth Based Service Provider Requirements
    4.3.3.2 SSI Earth Management/Routing Node Service Provider Requirements
    4.3.3.3 SSI Space Based Service Provider Requirements
    4.3.3.4 Future SSI Last Hop Service Provider Requirements

## Slide 26: Issue: No ABA Space User Node requirements in Section 4 (2 of 2)
Do ABA SUNs “see” “services”?
  If so, do we document them in separate subsections under 4.2.2 (ABA Service User Service Requirements) or combine them as is done in 4.3.2 (Future SSI Service User Requirements)?