## Slide 1: Physical Layer Security
11/9/2017
IGNACIO AGUILAR SANCHEZ, ESA
CHARLES SHEEHE, NASA

## Slide 2: Outline
Introduction
Threats
Options
Recommendations for follow-on development

## Slide 3: Introduction
SecWG0517:2; Action Item
  Review of threats to the link communications from CCSDS 350.1-G-2
  Generate a threats list that can be remediated by physical layer security
  Generate a concept paper for possible project for the fall 2017 meeting.
Scope
  Today a short presentation introducing the threats from the threat book that could be mitigated by Physical Layer Security.

## Slide 4: Threats (1/3)
INTERCEPTION OF DATA (resulting in loss of confidentiality, traffic analysis to determine which entities are communicating with each other without actually being able to read the communicated information. )
Possible Mission Impact: Interception of data may result in the loss of data confidentiality and data privacy if the data is not encrypted. In addition to those entities authorized for the data, non-authorized entities may also gain access. The interception of data could also result in masquerade or replay attacks.
Traffic analysis (generic)
Determine usage & idle periods, signaling formats, the information can be used to assist in the denial of the spectrum, reduction in throughput or manipulating format and sharing algorithms to be more advantageous to them.
  Quantum Computers (loss of confidentiality & authentication)
Quantum computers excel at processing numbers very quickly. They can operate exponentially faster than traditional computers. Researchers are making tremendous progress towards developing a computer that works quickly enough to make decrypting a private key a reality. Expected availability about 2024.

## Slide 5: Threats (2/3)
JAMMING (resulting in denial of service and loss of availability and data integrity);
Possible Mission Impact: Spacecraft commanding as well as the ability to receive science or engineering data from the spacecraft could be blocked. In addition, authorized access to system resources can be blocked, possibly delaying time-critical operations on both the ground and in space.
Data Corruption
  Possible Mission Impact: Corruption might be a result of software failures or bugs, hardware failures, use of unauthorized software, or active attempts to change/modify data to deny its use. A corrupted spacecraft command could result in catastrophic loss if either no action occurred (e.g., command is discarded) or the wrong action was taken onboard a spacecraft. For example, if a navigation maneuver burn command were corrupted, the spacecraft might end up in an unusable orbit, miss an encounter with a comet/planet/asteroid, or be destroyed.

## Slide 6: Threats (3/3)
REPLAY
Possible Mission Impact: If the recorded data were a command set from the ground to the spacecraft and they are re-transmitted to their originally intended destination, they might be acted upon, potentially for a second time. If the replayed commands are not rejected, they could result in a duplicate spacecraft operation such as a maneuver burn or a spacecraft reorientation with the result that a spacecraft is in an unintended orientation (e.g., tumbling, antenna pointed in the wrong direction, solar arrays pointed away from the sun).
DATA MODIFICATION (In time)
  Possible Mission Impact: Corruption might be a result of software failures or bugs, hardware failures, use of unauthorized software, or active attempts to change/modify data to deny its use. A corrupted spacecraft command could result in catastrophic loss if either no action occurred (e.g., command is discarded) or the wrong action was taken onboard a spacecraft. For example, if a navigation maneuver burn command were corrupted, the spacecraft might end up in an unusable orbit, miss an encounter with a comet/planet/asteroid, or be destroyed.

## Slide 7: Physical layer security options
Cryptographic spreading or hopping of the signal (Active).
  Data Interception
  Jamming
  Replay
Cryptographic information manipulation (Active).
  Data Interception
  Jamming
  Replay
Radio Frequency Fingerprinting (Passive).
  Data Interception (Authentication)
  Replay (Authentication)