Draft Recommendation for
Space Data System Standards

Security Credentials

PROPOSED Draft Recommended Standard

CCSDS 000.0-W-0

White Book

October 2017

AUTHORITY

|  | Issue: | White Book, Issue 0 |  |
| --- | --- | --- | --- |
|  | Date: | October 2017 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY):

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies. The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This document is published and maintained by:

CCSDS Secretariat

Space Communications and Navigation Office, 7L70

Space Operations Mission Directorate

NASA Headquarters

Washington, DC 20546-0001, USA

FOREWORD

The goal of this specification is to develop a profile to facilitate the use of Internet X.509 Public Key Infrastructure Certificate (X.509) certificates within Space applications for those communities wishing to make use of X.509 technology. In order to relieve some of the obstacles to using X.509 certificates, this document defines a profile to promote certificate management systems for space interoperability. Some communities will need to supplement, this profile in order to meet the requirements of specialized application domains or environments with additional authorization, assurance, or operational requirements.

The specification allows for Simple Protected Authentication Procedure in conformance with ISO/IEC 9594-8 standard for those communities that have performed an evaluation of its use.

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. CCSDS shall not be held responsible for identifying any or all such patent rights.

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur. This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4). Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- South African National Space Agency (SANSA)/Republic of South Africa.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- Swiss Space Office (SSO)/Switzerland.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard. It’s ‘White Book’ status indicates that its contents are not stable, and several iterations resulting in substantial technical changes are likely to occur before it is considered to be sufficiently mature to be released for review by the CCSDS Agencies.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

Recipients of this draft are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

DOCUMENT CONTROL

| Document | Title and Issue | Date | Status |
| --- | --- | --- | --- |
| CCSDS 000.0-W-0 | Security Credentials, Proposed Draft Recommended Standard, Issue 0 | November 2017 | Current draft |

CONTENTS

1.0	INTRODUCTION	1

1.1	SECURITY CREDENTIALS	1

1.2	PURPOSE	1

1.3	SCOPE	1

1.4	APPLICABILITY	1

1.5	RATIONALE	1

1.6	REFERENCES	2

2.0	OVERVIEW	3

2.1	X.509 CERTIFICATES	3

2.2	SIMPLE PROTECTED AUTHENTICATION	4

3.0	CREDENTIAL SPECIFICATION	5

3.1	X.509 Certificates Syntax	5

3.1.1	CCSDS shall implement X.509 V3 certificates	5

3.1.2	The CCSDS X.509 V3 certificates shall use generalized time.	5

3.1.3	The CCSDS X.509 V3 certificates shall utilize the CCSDS Calendar Segmented Time Code (CCS), CCSDS 301.0-B-4 TIME CODE FORMATS.	5

3.1.4	THE CCSDS X.509 V3 OUTPUT FILE FORMAT SHALL BE PERSONAL INFORMATION EXCHANGE SYNTAX (PKCS) #12.	5

3.2	SIMPLE PROTECTED AUTHENTICATION PROCEDURE	5

3.2.1	CCSDS SHALL IMPLEMENT PROTECTED SIMPLE AUTHENTICATION.	5

3.2.2	CCSDS Implementation of Protected Simple Authentication Shall Utilize THE CCSDS CALENDAR SEGMENTED TIME CODE (CCS), CCSDS Time Code Formats.	5

ANNEX A.—IMPLEMENTATION CONFORMANCE STATEMENT (ICS) PROFORMA (NORMATIVE)	6

ANNEX B.—SECURITY, SANA, AND PATENT CONSIDERATIONS (INFORMATIVE)	11

ANNEX C.—GLOSSARY OF TERMS (INFORMATIVE)	13

LIST OF TABLES

Table A-1.1 Security Credentials Structure	8

LIST OF FIGURES

# INTRODUCTION

## SECURITY CREDENTIALS

Credentials contracts trust between entities. They are as simple as challenge word and response word. CCSDS must utilize a trust mechanism as a prerequisite to securely communicate between entities. CCSDS utilizes two methods that will be specified in this document, X.509 certificates and simple protected authentication. The X.509 certificates properties are specified by the Internet Engineering Task Force (IETF) and its specific CCSDS profile is stated in this document. The Simple Protected Authentication process outlined in the, Information technology Open Systems Interconnection (ISO) 9594-8, as stated in this document will not require a protocol development and testing because it is currently in use at various location throughout CCSDS.

## PURPOSE

This CCSDS Recommendation provides the basis for the Credentials that facilitate network layer security for missions utilizing the Internet Protocol Security (IPsec) and Simple Protected Authentication.

## SCOPE

This recommendation specifies the manner in which the Credentials will be utilized to ensure the security for CCSDS missions.

## APPLICABILITY

This recommendation applies to any CCSDS mission using the IPsec or Simple Protected Authentication requiring end-to-end confidentiality, authentication, or integrity from the sender to the receiver regardless of the number of intermediate hops between them.

## RATIONALE

Many CCSDS missions require security services to protect commanding (command authentication, command confidentiality, command integrity) and payload data (confidentiality, integrity). This document specifies a CCSDS “credential profiles” for trusted communication between CCSDS entities.

The following publications contain articles which, through reference in this text, constitute provisions of this document. At the time of publication, the editions indicated were valid. All publications are subject to revision, and users of this Recommended Standard are encouraged to investigate the possibility of applying the most recent editions of the publications indicated below. The CCSDS Secretariat maintains a register of currently valid CCSDS publications.

## REFERENCES

[1]	RFC 5280 Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile, May 2008 https://www.ietf.org/rfc/rfc5280.txt

[2]	RFC 5818 Updates to the Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile, January 2013 https://www.ietf.org/rfc/rfc6818.txt

[3]	ISO/IEC 9594-8 Information technology—Open Systems Interconnection—The Directory—Part 8: Public-key and attribute certificate frameworks

[4]	Information Technology—Abstract Syntax Notation One (ASN.1): Specification of Basic Notation. 4th ed. International Standard, ISO/IEC 8824-1:2008. Geneva: ISO, 2008.

[5]	Information Technology—ASN.1 Encoding Rules: Specification of Basic Encoding Rules (BER), Canonical Encoding Rules (CER) and Distinguished Encoding Rules (DER). 4th ed. International Standard, ISO/IEC 8825-1:2008. Geneva: ISO, 2008.

[6]	Information Security Glossary of Terms. Green Book. Issue 1. November 2012.CCSDS 350.8-G-1 https://public.ccsds.org/Pubs/350x8g1.pdf

[7]	Time Code Formats. Issue 4. Recommendation for Space Data System Standards (Blue Book), CCSDS 301.0-B-4. Washington, D.C.: CCSDS, November 2010.

[8]	Internet Security Glossary https://www.ietf.org/rfc/rfc2828.txt

[9]	PKCS #12: Personal Information Exchange Syntax v1.1 https://tools.ietf.org/html/rfc7292

[Only references required for the implementation of the specification are listed in the References subsection. See CCSDS A20.0-Y-4, CCSDS Publications Manual (Yellow Book, Issue 4, April 2014) for additional information on this subsection.]

# OVERVIEW

Credentials are contracts of trust between entities. They can be as simple as challenge word and response word. CCSDS must utilize a trust mechanism in order to securely communicate between entities. Credentials attest to the identity or other attributes of an individual or entity called the subject of the credentials. Some examples of  paper credentials include passports, birth certificates, driver’s licenses, and employee identity cards. The authenticity of credentials is established in a variety of ways: traditionally perhaps by a signature or a seal, special papers and inks, high quality engraving, and today by more complex mechanisms difficult to copy or forge.

A certificate authority (CA) is a trusted entity that issues electronic documents that verify a digital entity’s identity. The electronic documents, which are called digital certificates, are an essential part of secure communications and play an important part in the public key infrastructure (PKI): Framework established to issue, maintain, and revoke public key certificates accommodating a variety of security technologies, including the use of software.

A Digital Certificate is an electronic documents attesting to the attributes, addressing the who were, what, when (time period effective for), and the systems public key. The Digital Certificate is signed by the CA to validate/bind its information.

CCSDS utilizes two methods to validate interactions for security and they are specified in this document, X.509 certificates and simple protected authentication

## X.509 CERTIFICATES

The X.509 certificates properties are specified by the Internet Engineering Task Force (IETF) and its specific CCSDS profile is stated in this document.

Certificate Authority (CA): Trusted entity authorized to create, sign, and issue public key certificates. By digitally signing each certificate issued, the user’s identity is certified, and the association of the certified identity with a public key is validated. CCSDS 350.8-G-1, ISO/IEC 9594-8

CAs are responsible for all aspects of the a certificates issued to users and devices, including control over the enrollment process, the certificate manufacturing process, publication of certificates, revocation of certificates, and re-keying, the entire certificate lifecycle.

A Subscriber is the entity (the user to whom, or device or software to which, a certificate is issued) whose Distinguished Name (DN) appears as the subject in a certificate, and who asserts that it uses the key and certificate in accordance with the CA’s policy. The term “Subscriber” as used refers only to those who request certificates for uses other than signing and issuing certificates or certificate status information.

Subscribers include but are not limited to the following categories of entities that may wish to conduct official Department business:

Personnel:

Non-Human Assets: These components must be under the cognizance of humans, who accept the certificate and are responsible for the correct protection and use of the associated private key.

A digital certificate binds a user or service’s identity to a public key, through signing of the certificate with the CA’s key. Certificates issued are structured to meet these objectives based on standards established by the Public-Key Infrastructure.

The Internet Protocol, known as IP Security (IPsec), can be used to protect an IP layer path between a pair of end-systems or hosts. IPsec is first outlined in the Internet Engineering Task Force (IETF), Request For Comment (RFC) 2828, 1825, 1826, and 1827.

## SIMPLE PROTECTED AUTHENTICATION

The Simple Protected Authentication process, Information technology—Open Systems Interconnection ISO 9594-8, is stated in this document.

Simple authentication is intended to provide peer entity authorization based upon the distinguished name of a user, a bilaterally agreed  password, and a bilateral understanding of the means of using and handling this password within a single domain. The utilization of simple authentication is primarily intended for within a domain use only, i.e., for peer entity authentication between one Directory User Agent (DUA) and one Directory System Agent (DSA) or between one DSA and another DSA.

This process is the basic protected logon activity.  The user name and password are entered and the computer adds data to protect the information that is sent to the server, which verifies the information and either accepts the connection or not.

This process is in use between ESA and NASA, latest recorded interaction was on the (XXX) project on (date).

# CREDENTIAL SPECIFICATION

CCSDS shall use current version of the X.509 certificate specifications.

## X.509 Certificates Syntax

### CCSDS shall implement X.509 V3 certificates

Note: Reference # 1

### The CCSDS X.509 V3 certificates shall use generalized time.

Note: Reference # 1

### The CCSDS X.509 V3 certificates shall utilize the CCSDS Calendar Segmented Time Code (CCS), CCSDS 301.0-B-4 TIME CODE FORMATS.

Note: Reference # 7

### THE CCSDS X.509 V3 OUTPUT FILE FORMAT SHALL BE PERSONAL INFORMATION EXCHANGE SYNTAX (PKCS) #12.

Note: Reference # 9

## SIMPLE PROTECTED AUTHENTICATION PROCEDURE

CCSDS has implementations of the Protected Simple Authentication and will not be tested.

### CCSDS SHALL IMPLEMENT PROTECTED SIMPLE AUTHENTICATION.

Note: Reference # 2

### CCSDS Implementation of Protected Simple Authentication Shall Utilize THE CCSDS CALENDAR SEGMENTED TIME CODE (CCS), CCSDS Time Code Formats.

Note: Reference # 7

# ANNEX A.—IMPLEMENTATION CONFORMANCE STATEMENT (ICS) PROFORMA
(NORMATIVE)

INTRODUCTION

OVERVIEW

This annex provides the Implementation Conformance Statement (ICS) Requirements List (RL) for an implementation of [Specification]. The ICS for an implementation is generated by completing the RL in accordance with the instructions below. An implementation claiming conformance must satisfy the mandatory requirements referenced in the RL.

ABBREVIATIONS AND CONVENTIONS

CRL distribution point: A directory entry or other distribution source for Certificate Revocation Lists (CRL); a CRL distributed through a CRL distribution point may contain revocation entries for only a subset of the full set of certificates issued by one CA or may contain revocation entries for multiple CAs, it is a managed parameter within the X.509 credential.

CONFORMANCE

The Conformance Requirements List consists of information in tabular form. The status of features is indicated using the abbreviations and conventions described below.

Item Column

The item column contains sequential numbers for items in the table.

Feature Column

The feature column contains a brief descriptive name for a feature. It implicitly means “Is this feature supported by the implementation?”

Status Column

The status column uses the following notations:

- M		mandatory;

- O		optional;

- C		conditional;

- X		prohibited;

- I		out of scope;

- N/A		not applicable.

Support Column Symbols

The support column is to be used by the implementer to state whether a feature is supported by entering Y, N, or N/A, indicating:

Y	Yes, supported by the implementation.

N	No, not supported by the implementation.

N/A	Not applicable.

The support column should also be used, when appropriate, to enter values supported for a given capability.

Section three Structure

| Security Credential Structure |  |  |
| --- | --- | --- |
| Item # | Feature | Status | Support |
| 1 | ASN1 | M |  |
| 2 | DER | M |  |
| 3 | X.509.V3 | M |  |
| 4 | tbsCertificate | M |  |
| 5 | Version | M |  |
| 6 | Serial number | M |  |
| 7 | algorithm identification | M |  |
| 8 | Issuer Signature | M |  |
| 9 | Validity from | M |  |
| 10 | Validity to | M |  |
| 11 | Subject | M |  |
| 12 | Subject algorithm identification | M |  |
| 13 | Subject public Key | M |  |
| 14 | Issuer Unique ID | O |  |
| 15 | Subject Unique ID Public Key Info | O |  |
| 16 | Universal Time Coordinated Time Certificate | M |  |
| 17 | Generalized Time | M |  |
| 18 | object identifiers (OID) | O |  |
| 19 | Policy Mapping | O |  |
| 20 | Subject Alternative Name | O |  |
| 21 | Certificate Revocation Lists distribution points | O |  |
| 22 | signatureAlgorithim | M |  |
| 23 | signatureValue | M |  |

Table A-1.1 Security Credentials Structure

INSTRUCTIONS FOR COMPLETING THE RL

An implementer shows the extent of compliance to the Recommended Standard by completing the RL; that is, the state of compliance with all mandatory requirements and the options supported are shown. The resulting completed RL is called an ICS. The implementer shall complete the RL by entering appropriate responses in the support or values supported column, using the notation described in A1.3. If a conditional requirement is inapplicable, N/A should be used. If a mandatory requirement is not satisfied, exception information must be supplied by entering a reference Xi, where i is a unique identifier, to an accompanying rationale for the noncompliance.

ICS PROFORMA FOR [SPECIFICATION]

GENERAL INFORMATION

Identification of ICS

| Date of Statement (DD/MM/YYYY) |  |
| --- | --- |
| ICS serial number |  |
| System Conformance statement cross-reference |  |

Identification of Implementation Under Test

| Implementation Name |  |
| --- | --- |
| Implementation Version |  |
| Special Configuration |  |
| Other Information |  |

Identification of Supplier

| Supplier |  |
| --- | --- |
| Contact Point for Queries |  |
| Implementation Name(s) and Versions |  |
| Other information necessary for full identification, e.g., name(s) and version(s) for machines and/or operating systems; System Name(s) |  |

Identification of Specification

| [CCSDS Document Number] |
| --- |
| Have any exceptions been required? NOTE – A YES answer means that the implementation does not conform to the Recommended Standard. Non-supported mandatory capabilities are to be identified in the ICS, with an explanation of why the implementation is non-conforming. | Yes [ ] No [ ] |

REQUIREMENTS LIST

[See CCSDS A20.1-Y-1, CCSDS Implementation Conformance Statements (Yellow Book, Issue 1, April 2014).]

# ANNEX B.—SECURITY, SANA, AND PATENT CONSIDERATIONS
(INFORMATIVE)

b1	Security Considerations

CCSDS utilization of X.509 and Simple Protected Authentication Procedure codifies the processes with which access to and communication with entities will be secured. Access to CCSDS networks rely on the use of credentials to validate the identities of users, applications, and devices. CCSDS Organizations employ technologies to convey identity and to attest to the claims and trust are associated with those identities.

There is a risk to CCSDS systems utilizing the credentials if an attacker gains control of the external credential management system they can issue weak, invalid or false credentials. If a compromised credential management processes results, then a need to re-issue valid credentials will result.

A CCSDS credential management program would result in higher levels of assurance of the credentials while ensuring interoperability, ease they deployments of systems that are pre-tested to integrate with credential management system. The system would provide a unified administration, compliance, and auditing. A credential management system allows the Future-proof your trust models and policies.

CCSDS Credentials will employ cryptographic algorithms specified in the CCSDS Cryptographic Algorithms, CCSDS 352.0-B-1 used by CCSDS-conformant missions to provide confidentiality and authentication.

b1.1	security concerns with respect to the CCSDS document

A credential management system must be built to decrease the risks of an attacker gaining control of your credential management systems. This book only specifies the utilization of the credentials and not its issuance or revoking of the credentials. There are no known exploits of the processes.

B1.1.1	Data Privacy

Data may be exposed when sent between entities who have not been authenticated and subsequent key agreements made to prevent exposure of the information.

B1.1.2	Data Integrity

Data may not be valid if the keys used to protect the information are corrupted or wrong. The data will need to be replaced.

B1.1.3	Authentication of Communicating Entities

Authentication is necessary to ensure that the exchange of information is between intended entities. This document specifies the protocols used for CCSDS compliant systems.

B1.1.4	Control of Access to Resources

This document deals with exchange protocols and not internal system resources.

B1.1.5	Availability of Resources

This document deals with exchange protocols and not internal system resources.

B1.1.6	Auditing of Resource Usage

This document deals with exchange protocols and not internal system processes.

b1.2	Potential threats and attack scenarios

If properly implemented there is no known threat vector.

b1.3	Consequences of not applying security to the technology

If authentication is not implemented, an attacker could inject false or unauthorized commands into a communications path to the spacecraft’s command chain, and potentially take over control of the spacecraft. This could result in the loss of a mission.

b2	SANA Considerations

This document does not require any action from SANA. A review of the SANA terms, several additions could be made for clarification reasons i.e. Credentials.

b3	Patent Considerations

Algorithms and processes referenced in this document are in the public domain, and there are no known patents that apply to the recommendations in this document.

# ANNEX C.—GLOSSARY OF TERMS
(INFORMATIVE)

| Certificate Authority (CA) | Certificate authority or certification authority (CA) is an entity that issues digital certificates. A digital certificate certifies the ownership of a public key by the named subject of the certificate. This allows others (relying parties) to rely upon signatures or on assertions made about the private key that corresponds to the certified public key. |
| --- | --- |
| Certificate Revocation Lists (CRL) | This specification profiles the format and semantics of certificates and certificate revocation lists (CRLs) for the Internet PKI. |
| Directory Access Protocol (DAP) | Common management information protocol ISO/IEC 9596-1 |
| Directory Information Base (DIB) | The DIB is made up of information about objects. It is composed of (Directory) entries, each of which consists of a collection of information on one object. |
| Directory System Agent (DSA) | Is an application process which is part of the Directory and whose role is to provide access to the DIB to DUAs, LDAP clients and/or other DSAs. |
| Directory User Agent (DUA) | Each user is represented in accessing the Directory by a Directory User Agent (DUA) or an LDAP client, each of which is considered to be an application-process. |
| Distinguished Name (DN) | An identifier that uniquely represents an object in the X.500 Directory Information Tree. A DN is a set of attribute values that identify the path leading from the base of the DIT to the object that is named. |
| Domain Name | The style of identifier--a sequence of case-insensitive ASCII labels separated by dots ("bbn.com.")--defined for subtrees in the Internet Domain Name System and used in other Internet. |

| HyperText Transfer Protocol (HTTP) | HTTP is the underlying protocol used by the World Wide Web and this protocol defines how messages are formatted and transmitted, and what actions Web servers and browsers should take in response to various commands. |
| --- | --- |
| HyperText Transfer Protocol, over SSL or Secure (HTTPS) | (HTTPS) HTTP uses of Secure Socket Layer (SSL) or Transport Layer Security (TLS) as a sublayer under regular HTTP application layering. HTTPS encrypts and decrypts user page requests as well as the pages that are returned by the Web server. |
| Information technology Open Systems Interconnection (ISO) | ISO (the International Organization for Standardization) is a worldwide federation of national standards bodies (ISO member bodies). The work of preparing International Standards is normally carried out through ISO technical committees. ISO creates documents that provide requirements, specifications, guidelines or characteristics that can be used consistently to ensure that materials, products, processes and services are fit for their purpose |
| Internet Engineering Task Force (IETF) | The goal of the IETF is to make the Internet work better. The mission of the IETF is to make the Internet work better by producing high quality, relevant technical documents that influence the way people design, use, and manage the Internet. |
| Internet Protocol security (IPsec) | The name of the IETF working group that is specifying a security architecture and protocols to provide security services for Internet Protocol traffic. |
| Internet X.509 Public Key Infrastructure Certificate (X.509) | X.509 is a standard that defines the format of public key certificates. X.509 certificates are used in many Internet protocols, including TLS/SSL, which is the basis for HTTPS, the secure protocol for browsing the web. X.509 certificate contains a public key and an identity (a hostname, or an organization, or an individual), and is either signed by a certificate authority or self-signed. X.509 specifies certificate revocation lists as a means to distribute information about certificates that are no longer valid, and a certification path validation algorithm, which allows for certificates to be signed by intermediate CA certificates, which are in turn signed by other certificates, eventually reaching a trust anchor. |
| Lightweight Directory Access Protocol (LDAP) | LDAP provides access to distributed directory services that act in accordance with X.500 data and service models. These protocol elements are based on those described in the X.500 Directory Access Protocol (DAP). |
| Personal Information Exchange Syntax (PKCS) | syntax for personal identity information, including private keys, certificates, miscellaneous secrets, and extensions. |
| Request For Comment (RFC) | Requests for Comments (RFC) document series contain technical and organizational notes about the Internet. |
| Secure Sockets Layer (SSL) Secure Sockets Layer (SSL) protocol, can be applied to a web application, and the requirements necessary to create a secure link between a server and a client machine. | Secure Sockets Layer (SSL) protocol, can be applied to a web application, and the requirements necessary to create a secure link between a server and a client machine. |
| Transport Layer Security (TLS) | Transport Layer Security (TLS) protocol, can be applied to a web application, and the requirements necessary to create a secure link between a server and a client machine. |

# Comments

Reference

Why don’t we limit ourselves here to the IpSec Adaptation Profile of CCSDS?

Would like to but it has not been accepted yet.

Is it possible to have procedures one does not want to test in the normative part of a BB?

I agree The Area director wanted this. This is currently in use on SLE.  “In the WG meetings we agreed to have both options since the Cross Support guys have already used the simple authentication procedure.”