AMS Interoperability Test Plan

V.0.1 (Proposed Draft)

Green Book, Part II

1.	Introduction	3

1.1.	Overview	3

1.2.	Definitions & Conventions	3

1.3.	Testing Requirements	3

2.	Nominal Testing Procedures	4

2.1.	Base Registrar Configuration	4

2.2.	Basic Node Registration	5

2.3.	Message Exchange	5

2.4.	Cross-Domain Communication	7

2.5.	Resynchronization	9

3.	Robustness Verification	10

3.1.	Basic Configuration Robustness	10

3.2.	Extended Robustness Validation	11

4.	Remote AMS Test Procedures	13

4.1.	Basic RAMS Verification	13

4.2.	Advanced RAMS Verification	14

5.	Transport Service Testing Requirements	16

5.1.	UDP	16

5.2.	POSIX or VxWorks Message Queues (Pxmq or Vxmq)	16

# Introduction

Overview

This document provides interoperability testing procedures for the Asynchronous Messaging Service (AMS).

## Definitions & Conventions

All scenarios are designed for the testing of two distinct implementations, ALPHA (abbreviated A) and BETA (abbreviated B).  Abbreviations indicating the implementation will be appended to all entity names, such as RegistrarA for a registration server from implementation ALPHA, or NodeB for a node in implementation BETA.

If multiple entities of the same type are used in a single implementation, a number shall be appended to its mnemonic, such as NodeA1 and NodeA2.  Names are used for reference purposes only and do not necessarily reflect internal node identifiers.  Mappings of node or registrar names may be swapped as necessary to facilitate alternate test scenarios with similar initial states.

The following configuration mnemonics will be used.  Their values are not currently defined, but must be common in the MIB shared among all tested implementations.

- Subject1 … SubjectN

- Default_Role = ROLE_A

- Default_Unit =  UNIT_A

- ROLE_A … ROLE_N

- UNIT_A … UNIT_N

All testing procedures, with the exception of RAMS procedures, assume that all entities are members of a single continuum.

## Testing Requirements

These procedures, unless otherwise noted, require that all implementations are operating across a common transport service and MIB configuration state.  The  chapter describes any TS specific configuration suggestions.

Verification requirements, as stated, may assume the availability of debug information on internal status of nodes or other entities as appropriate.  Direct monitoring of message traffic across the selected transport service(s) may also be used for validation purposes.  These are suggested verification techniques only and, in the absence of direct verification, success may be inferred from related actions as appropriate.   A test result of undetermined (U) should be recorded if no verification was possible for a given step.

For all message exchanges the following defaults should be used if not otherwise specified.  The default subject is Subject1, role is Default_Role, and unit is Default_Unit.  Message content is not specified, however it is suggested that a known test value (ie: a test pattern, counter, or timestamp) be used and verified when appropriate.

Results tables should be marked as follows, with an explanation attached for any unsuccessful test performed:

- P for successful test.

- F for a failed test

- -  for a test that has not been performed.

- U for a test whose results are undetermined.

- I for partial success or incomplete test.

# Nominal Testing Procedures

This section describes testing procedures for core AMS functionality under normal operations.  The basic series may be used for testing a single implementation for compliance, or for the interoperability testing of any combination of implementations.  A table provided at the end of each section illustrates sample test scenarios for testing between implementations.

## Base Registrar Configuration

Validate the ability for the RS to communicate and register with the CS.

- Start Configuration Server

- Start RegistrarA

  - Confirm registration

  - Confirm heartbeats

- Start RegistrarB

  - Confirm registration

  - Confirm heartbeats

- Verify Mutual Awareness of Registrars

  - Confirm RegistrarA is aware of RegistrarB

  - Confirm RegistrarB is aware of RegistrarA

The following testing combinations should be performed.  Italicized cases are optional, to be used if there is a failure in any previous test combination.

| Test# | CS | RegistrarA | RegistrarB | Results |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 | 2 | 3 |
| 2.1a | ALPHA | BETA | ALPHA |  |  |  |
| 2.1b | BETA | ALPHA | BETA |  |  |  |
| 2.1c | ALPHA | ALPHA | ALPHA |  |  |  |
| 2.1d | BETA | BETA | BETA |  |  |  |

## Basic Node Registration

Validate the ability for a node to register and unregister itself.

- Initial Configuration should include one CS and at least one active RS.

  - This may correspond to the final state of the previous section, case 1, with any additional registrars ignored for this scenario and/or these procedures mirrored within each active cell (registrar).

- Verify that a node can register

  - Confirm ability to locate registrar by querying the CS

  - Verify registration success

  - Verify Heartbeat exchange between RS and node.

- Verify that the node can cancel its registration (unregister)

  - Confirm processing by the registrar

  - Confirm configuration propagation to other nodes.

- Verify that the node can Re-Register

The following testing combinations should be performed.

| Test# | CS | Registrar | NodeA | Results |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 | 2 | 3 |
| 2.2a | ALPHA | ALPHA | BETA |  |  |  |
| 2.2b | BETA | BETA | ALPHA |  |  |  |

## Message Exchange

Validate the ability for two nodes in the same cell to register and communicate.  This section will test subscriptions, publish, receive, invite, send, and announce.

- One CS, one RS, and one node are active.

  - This may correspond to the final state of case 2.

- Register a second node, NodeB.

  - Confirm successful registration

  - Verify that NodeB is told of NodeA’s existence and empty subscription list.

  - Verify that NodeA is told of NodeB’s registration.

- Publish a message on Subject1 from NodeA

  - Verify that NodeB does not receive this message; no subscriptions are in place at this time.

- Subscribe to Subject1 from NodeB

  - Verify that NodeA receives subscription notification.

- Publish a message on Subject1 from NodeA

  - Verify that NodeB receives the message

  - Repeat using Subject2 and verify NodeB does not receive the message; this is not the subject that has been subscribed to.

- From NodeB, subscribe to ALL_Subjects

  - Verify subscription receipt by NodeA

- Publish a message from NodeA on Subject2

  - Verify NodeB receives this message (subscribed to all)

- Send a message on Subject1 from NodeA addressed to a domain that includes NodeB

  - Verify that NodeB does not receive this message; no invitations are in place at this time.

- From NodeB, cancel subscription on ALL_SUBJECTS

  - Verify propagation to NodeA.  If necessary, attempt to publish a message from NodeB on Subject2 and verify message is not received.

- From NodeB, invite a domain that includes NodeA to send Subject2

  - Verify NodeA receives invitation

- Publish a message from NodeA on Subject2.

  - Verify that NodeB does not receive this message.  An invitation does not apply to published messages.

- Send a message from NodeA to NodeB on Subject2

  - Verify that NodeB receives the message

- From NodeA, query NodeB on Subject2

  - Verify NodeB receives query.

- From NodeB, attempt to reply to NodeA with Subject2

  - Verify failure, NodeA has not issued an invitation on this subject.

- Verify query/reply exchange

  - From NodeB, invite messages on Subject2 in a domain that includes NodeA

  - Repeat steps 12 & 13, verifying success now that appropriate subscriptions are in place on both ends.

- From NodeA, issue an announcement on Subject2

  - Verify that the message is received by NodeB

  - Repeat from NodeB and verify the message is not received.  NodeA has no invitations in place on this topic.

  - Repeat announcement from NodeA, addressing the message to a domain that does not include NodeB.  Verify message is not received.

- Cancel NodeA registration (unregister)

  - Verify registrar processes and forwards request.

  - Verify unregisteration notification by NodeB

- Re-register NodeA

  - Verify registration success

  - Verify correct state of subscriptions, for example:

    - Publish a message on Subject1from NodeA and verify its receipt by NodeB.

    - Attempt to send a message from NodeB to NodeA on Subject2 and verify failure.  Invitations expire upon cancellation of a nodes registration.

    - Attempt to send a message from NodeA to NodeB on Subject2 and verify success.

The following testing combinations should be performed:

| Test# | CS | Registrar | NodeA | NodeB |
| --- | --- | --- | --- | --- |
| 2.3a | ANY | ALPHA | ALPHA | BETA |
| 2.3b | ANY | BETA | BETA | ALPHA |

| Test# | Results |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 |
| 2.3a |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 2.3b |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

## Cross-Domain Communication

This scenario validates message exchange and configuration between cells and associated message filtering by domain.

- Initial state consists of a CS and two cells

  - The first cell consists of RegistrarA, NodeA1, NodeA2 in UNIT_A

  - The second cell consist of RegistrarB, NodeB1, NodeB2 in UNIT_B

  - Nodes A1 and B1 perform ROLE_A

  - Nodes A2 and B2 perform ROLE_B

  - At the start of this test both Registrars, NodeA1, and NodeB1 are active.

- Register the remaining nodes, NodeA2, and NodeB2 to their respective cells.

  - Verify successful registration to their respective cells

  - Verify receipt of registration notification in neighboring cells.

- NodeA1 Subscribes to Subject1 in UNIT_A and ROLE_B

  - Publish a message on Subject1 from NodeA2

    - Verify receipt by NodeA1

  - Publish a message on Subject1 from NodeB1 and from NodeB2.

    - Verify neither message is received.

- NodeA1 Subscribes to Subject2 on UNIT_B and ROLE_A

  - Publish a message on Subject2 from NodeB1

    - Verify receipt by NodeA1

  - Publish a message on Subject2 from NodeA2 and from NodeB2.

    - Verify neither message is received.

- NodeA1 Subscribes to Subject3 on UNIT_B and ALL_ROLES

  - Publish a message on Subject3 from NodeA2 and verify it is not received.

  - Publish a message on Subject3 from NodeB1 and NodeB2 and verify receipt of each.

- NodeA1 Subscribes to Subject4 on ALL_UNITS and ALL_ROLES

  - Publish a message on Subject4 from every other node in the continuum and verify receipt.

- Cancel Subscription to Subject4 from NodeA1 on ALL_UNITS and ALL_ROLES.

  - Verify propagation to all other nodes.  If necessary, attempt to publish a message on this subject to verify.

- From NodeA1, invite messages on Subject5 from ALL_UNITS and ALL_ROLES

  - Verify that all others nodes may privately send messages on Subject5 to NodeA1

  - Verify NodeA1 can receive an announcement on this subject from all other nodes.

- From NodeA1, invite messages on Subject6 from UNIT_B and ALL_ROLES

  - Verify that only NodeB1 and NodeB2 can send messages on Subject6 to NodeA1 in this configuration.

  - Repeat verification for transmission and receipt of announcements.

- From NodeA1, invite messages on Subject7 from UNIT_B and ROLE_A

  - Verify that only NodeB1 can send a private message to NodeA1 on this subject.

  - Repeat verification for transmission and receipt of announcements.

- From NodeA1, invite messages on Subject8 from UNIT_A and ROLE_B

  - Verify that only NodeA2 can send a private message to NodeA1 on this subject.

  - Repeat verification for transmission and receipt of announcements.

- From NodeA1, Cancel Invitation on Subject5

  - Verify propagation to all nodes.

- Cancel Registration of NodeB1

  - Verify propagation of configuration change to all other nodes.

  - Re-register NodeB1 and verify that it is made aware of all active subscriptions and invitations.

- Cancel Registration of NodeA1

  - Verify propagation of configuration change to all other nodes.

  - Confirm that all invitations and subscriptions are cancelled upon shutdown of NodeA1.

The following testing combinations are recommended.  Compatible scenarios may be executed from the same configuration by swapping entity mnemonics accordingly.

| Test# | CS | RegistrarA | NodeA1 | NodeA2 | RegistrarB | NodeB1 | NodeB2 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2.4a | ANY | ALPHA | ALPHA | BETA | BETA | BETA | ALPHA |
| 2.4b | ANY | BETA | BETA | ALPHA | ALPHA | ALPHA | BETA |

| Test# | Results |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 2.4a |  |  |  |  |  |  |  |  |  |  |  |  |
| 2.4b |  |  |  |  |  |  |  |  |  |  |  |  |

Resynchronization

Resynchronization may be performed periodically to ensure a consistent configuration within a cell.  Full verification of this capability may require the availability of debugging capabilities in the system, or transport service, to artificially create a non-synchronized scenario.  These procedures should be repeated for the Registrar of each available implementation.

- Initial state includes:

  - A non-zero resynchronization value for a given cell

  - A minimum of one CS, RS, and two nodes (one of each implementation type).

  - A second cell (RegistrarB and at least one associated node) is recommended to verify propagation between cells.

  - Establish some set of invitations and subscriptions spanning all combinations of active nodes.

- Verify resynchronization period.  A cell_status should be received by all active nodes in the message space at the expiration of this period.

- Verify that all subscriptions, invitations, and registration databases remain valid following the resynchronization.

- If possible, cause the nodes to become out of sync.  This may be done by issuing an invitation, subscription, or registration change and blocking receipt by one or more entities.

  - Wait for the conclusion of the next resynchronization period and validate that all entities are now synchronized.

| Test# | CS | RegistrarA | NodeA | NodeB | Results |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | 1 | 2 | 3 |
| 2.5a | ALPHA | BETA | ALPHA | BETA |  |  |  |
| 2.5b | BETA | ALPHA | BETA | ALPHA |  |  |  |

# Robustness Verification

## Basic Configuration Robustness

This scenario confirms the robustness of a configuration server in its management of its registration server.

- Initial configuration consists of a CS and a Registrar

- Delete (kill) the registrar.

  - Wait N3*N6 period and verify imputed death of registrar

  - Verify Registrar is restarted successfully by the CS (or other implementation-specific mechanism).

- Suspend the registrar for a period of N3 such that it misses one heartbeat.

  - Verify Registrar continues normal operation and the CS does not prematurely impute its death.

- Suspend the registrar for a period of N3*N6 seconds

  - Verify that its death is imputed by the registrar

  - Verify that a new instance of the registrar is successfully activated.

  - Verify that upon resumption, the existing registrar is appropriately terminated.

    - Termination should be imputed by failure of CS to respond to heartbeats.

- Activate and register one node for each available implementation.

  - Verify registration and initiation of heartbeat exchange.

- Terminate the registrar

  - Verify imputed termination and restart by the server

  - Verify ability of each node to successfully impute death of the registrar, locate its successor, reconnect and resume activities (heartbeats).

  - Verify ability for nodes to subscribe and publish messages.

- Terminate the Configuration Server.

  - Verify imputed loss by the registrar.

  - Verify that node communication is not impeded

    - Message exchange and heartbeats continue as previously.

    - Verify that additional subscriptions or invitations cannot be exchanged successfully.

- Restart the Configuration Server

  - Verify ability for registrars to reconnect.

- Terminate a node.  This is a test of the servers, any node may be terminated.

  - Verify its registrar imputes the nodes death and propagates the news to all other nodes in the message space.

  - Restart the node.

    - Verify successful registration

    - Verify communication with existing nodes.

The following testing combinations should be performed.

| Test# | CS | Registrar | Nodes | Results |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 3.1a | ALPHA | BETA | ALL |  |  |  |  |  |  |  |  |
| 3.1b | BETA | ALPHA | ALL |  |  |  |  |  |  |  |  |
| 3.1c | ALPHA | ALPHA | ALL |  |  |  |  |  |  |  |  |
| 3.1d | BETA | BETA | ALL |  |  |  |  |  |  |  |  |

## Extended Robustness Validation

This scenario confirms configuration robustness between cells.

- Initial configuration consists of a CS, two RS each with two registered nodes (four total) and some set of established subscriptions and invitations.  This may correspond to the final state of basic case 3.

- Terminate the Configuration Server

  - Verify imputed loss by the registrars

  - Verify that node communication is not impeded

    - Message exchange and heartbeats continue as previously.

    - Confirm that additional subscriptions or invitations can not be propagated.

- Restart the Configuration Server

  - Verify ability for registrars to reconnect.

- Terminate  RegistrarA

  - Verify imputed termination.

  - If applicable, confirm ability for nodes to continue AAMS message exchange, then restart by the registrar.

  - Verify ability of each client node to successfully impute death of the registrar, locate its successor, reconnect and resume activities (heartbeats).

  - Verify ability for nodes to subscribe and publish messages.

- Suspend a node of RegistrarA

  - Verify RegistrarA imputes the nodes death and the news propagates to all applicable entities, including RegistrarB and its registered nodes.

  - Resume execution of the node.

    - Verify it receives notification or imputes its own demise.

    - Reconnect or re-register and verify success

    - Verify communication with existing nodes.

- Repeat step 3 for RegistrarB

- Repeat step 4 for RegistrarB

The following testing combinations should be performed.

| Test# | CS | RegistrarA | NodeAx | RegistrarB | NodeBx | Results |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 |
| 3.2a | ALPHA | ALPHA | ALL | BETA | ALL |  |  |  |  |  |  |
| 3.2b | BETA | ALPHA | ALL | BETA | ALL |  |  |  |  |  |  |

# Remote AMS Test Procedures

# This section describes testing procedures for the Remote AMS (RAMS) protocol, including both Mesh and Tree configurations.  These test procedures assume the existence of up to three discrete continuums.  For brevity, they will be referred to as C1, C2, and C3.  ALL_CONTINUA indicates all continuum are addressed.

The following procedures are intended to exercise all RAMS components, in both the Tree and Mesh configurations.  As indicated, certain steps may not apply to all test configurations.

## Basic RAMS Verification

- The initial state consists of two continuums, C1 and C2 in an active state on the RAMS network, each containing one relevant cell.

  - RegistrarA, NodeA1, and NodeA2 are members of C1

  - RegistrarB, NodeB1, and NodeB2 are members of C2.

  - All entities belong to UNIT_A and ROLE_A.

  - All entities are active at the start of this test.

- Verify each continuum is aware of its neighbor.

- NodeA1 Subscribes to Subject1 in C1

  - Verify subscription is not transmitted outside of C1.

  - Publish a message on Subject1 from NodeA2

    - Verify receipt only by NodeA1

  - Publish a message on Subject1 from NodeB1

    - Verify message is not received

- NodeA1 Subscribes to Subject2 in C2

  - Publish a message on Subject2 from NodeB1

    - Verify receipt by NodeA1

  - Publish a message on Subject2 from NodeA2

    - Verify message is not received.

- NodeA1 Subscribes to Subject3 on ALL_CONTINUA

  - Publish a message on Subject3 from NodeB1and verify receipt.

- Cancel Subscription to Subject2 from NodeA1 on C2.

  - Verify propagation to all other nodes and continuum.  If necessary, attempt to publish a message on this subject to verify.

- From NodeA1, invite messages on Subject4 from ALL_CONTINUA

  - Verify that NodeB1 can send messages on Subject4 to NodeA1.

  - Verify NodeA1 can receive an announcement on this subject from NodeB1.

  - Optionally, repeat a + b for messages transmitted by NodeA2 and verify their receipt only by NodeA1.

  - Optionally, repeat for an invitation in the reverse direction, followed by a query and reply exchange.

- From NodeA1, invite messages on Subject5 from C2

  - Verify that only NodeB1 can send a private message to NodeA1 on this subject.

  - Repeat verification for transmission and receipt of announcements.

- From NodeA1, Cancel Invitation on Subject5

  - Verify propagation to all nodes and continua.

The following are suggested testing configurations that should be performed, if available.

| Test# | C1 | C2 | Configuration | Results |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 4.1a | ALPHA | BETA | TREE |  |  |  |  |  |  |  |  |
| 4.1b | BETA | ALPHA | MESH |  |  |  |  |  |  |  |  |

Advanced RAMS Verification

This section adds a third continuum for verification of messages requiring multiple hops (Tree configuration only), the ability to add or remove a continuum, and general message filtering with more than two continuum.

This procedure assumes the conclusion of the previous section as its initial configuration, or an environment with the same subscriptions already in place.

- Continua C1 and C2 are operating as described above.

  - C3 is active, but its RAMS Gateway is offline.

  - RegistrarC and NodeC are members of C3.

  - Some subscriptiosn and/or invitations should be in place between C1 and C2, both addressed to a specific domain (not including C3), and one that includes ALL_CONTINUA.

- C3 joins the RAMS Network. If operating under a Tree configuration, C3 becomes a child of C2.

  - Verify C1 and C2 receive appropriate petitions indicating the arrival of C3

  - Verify C3 receives appropriate petitions from C1 and C2, including notification of all pre-existing subscriptions.

- NodeC publishes a message on Subject1

  - Verify the message is not received.

  - Repeat for Subject3 and verify receipt by NodeA1, currently subscribing to this subject on ALL_CONTINUA.

- NodeC attempts to send a private message to NodeA1

  - Verify ability to send messages on Subject4, invited from all continuum.

  - Verify inability to send messages on Subject5.

- NodeA1 Subscribes to Subject6 in C3

  - Publish a message on Subject6 from NodeC

    - Verify receipt by NodeA1

  - Publish a message on Subject6 from NodeB1

    - Verify message is not received.

- From NodeA1, invite messages on Subject7 from C3

  - Verify that NodeC can send a private message to NodeA1 on this subject.

  - Verify that NodeB1 cannot send a private message to NodeA1 on this subject.

  - Optionally, repeat a+b for transmission and receipt of announcements.

- NodeB1 Subscribes to Subject8 in C3

  - Publish a message on Subject8 from NodeC

    - Verify receipt by NodeB1

  - Publish a message on Subject8 from NodeA1

    - Verify message is not received.

- From NodeC, invite messages on Subject9 from ALL_CONTINUA

  - Verify that node A1 can successfully send a private message to NodeC on this subject.

  - Verify that node B1 can successfully send a private message to NodeC on this subject.

- Remove C3 from the RAMS network

  - Verify petition propagations to C1 and C2.

  - Verify cancellation of all active invitations and subscriptions for C3.

- Add a C3 gateway back into the RAMS network.

  - Verify propagation of all expected petitions and declarations.

- Terminate the C1 gateway (ie: Ctrl+C) to simulate an unexpected failure.  A new instance of the C1 gateway should then attempt to join the RAMS Network, preferably with all other members of C1 continuing to run without interruption.

  - Verify its ability to rejoin and communicate with all other continua successfully, with only the expected configuration messages exchanged.

The following are suggested testing configurations that should be performed, if available.  DELTA may be a third implementation, or a second instance of an existing one.

| Test# | C1 | C2 | C3 | Configuration | Results |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 4.2a | ALPHA | BETA | DELTA | TREE |  |  |  |  |  |  |  |  |  |  |
| 4.2b | DELTA | ALPHA | BETA | MESH |  |  |  |  |  |  |  |  |  |  |

# Transport Service Testing Requirements

The following sections describe any transport specific procedures that may be recommended to ensure a common configuration and basic connectivity.

## UDP

UDP is the preferred transport service for interoperability testing at this time.  The following conventions will be followed for this TS:

- MAMS messages will be carried via UDP.

- Each node will have only one input port for AAMS messages, and it will be a UDP port.  (Each node will have two UDP input ports -- one for MAMS and one for AAMS)

- All AAMS messages will be null-terminated character strings consisting of printable text.

To test UDP connectivity prior to AMS testing, we may be able to use the ‘netcat’ utility:

machine1> nc -u machine2 6001 -p 6002

machine2> nc -u machine1 6002 -p 6001

Then type a line in on each machine - it should be received at the partner machine.

## POSIX or VxWorks Message Queues (Pxmq or Vxmq)

Connectivity testing for onboard message queue transport services is implementation specific and may require non-standard procedures to establish communication that are outside the scope of this document.   This may include system-specific procedures for allocating and assigning message queues.

# Comments

TBD

This test verifies that NodeA’s subscription does not apply to invitations.

This item has recently changed.  Previous (future?) behavior was for the CS to issue a ‘you_are_dead’ directive.