Asynchronous Message Service (AMS) — interoperability test plan and report

CCSDS Record

CCSDS 720.4-Y-0

Yellow Book

July 2011

FOREWORD

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This CCSDS Record is therefore subject to CCSDS document management and change control procedures, which are defined in the Procedures Manual for the Consultative Committee for Space Data Systems.  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- British National Space Centre (BNSC)/United Kingdom.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- Deutsches Zentrum für Luft- und Raumfahrt e.V. (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- Centro Tecnico Aeroespacial (CTA)/Brazil.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- MIKOMTEK: CSIR (CSIR)/Republic of South Africa.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Organization (NSPO)/Taiwan.

- Naval Center for Space Technology (NCST)/USA.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

# DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS 735.1-Y-1 | CCSDS Asynchronous Message Service (AMS)—Interoperability Test Plan and Report, CCSDS Record, Issue 1 | July 2011 | Current issue |

CONTENTS

DOCUMENT CONTROL	4

1.	Introduction	6

1.1.	Purpose	6

1.2.	Scope	6

1.3.	Applicability	6

1.4.	Rationale	6

1.5.	Document Structure	7

1.6.	References	7

2.	Test Plan Overview & Configuration	7

2.1.	Overview	7

2.2.	Definitions & Conventions	8

2.3.	Testing Requirements	8

3.	Nominal Testing Procedures	9

3.1.	Base Registrar Configuration	9

3.2.	Basic Module Registration	10

3.3.	Message Exchange	10

3.4.	Cross-Domain Communication	12

3.5.	Resynchronization	14

3.6.	Security & Data Integrity Verification	15

4.	Robustness Verification	17

4.1.	Registrar Failover	17

4.2.	Robustness Validation	18

5.	Remote AMS Test Procedures	20

5.1.	Basic RAMS Verification	20

5.2.	Advanced RAMS Verification	21

6.	Transport Service Testing Requirements	23

6.1.	UDP	23

6.2.	Buffered UDP (BUDP)	23

7.	Spring 2011 Interoperability Test Results	24

7.1.	Summary & Conclusion	24

7.2.	Results	24

7.2.1.	Nominal Testing Procedures	24

7.2.2.	Robustness Verification	25

7.2.3.	Remote AMS Test Sequence	26

8.	Supporting conventions for AMS interoperability testing	27

8.1.	Operations structure	27

8.2.	Transport services	28

8.3.	Marshaling and unmarshaling	28

8.4.	Encryption and decryption	30

8.5.	Digital Signatures	31

8.6.	Access Control	31

8.7.	Sample representation of the interoperability testing MIB	32

# Introduction

## Purpose

This document provides interoperability testing procedures for the Asynchronous Messaging Service (AMS) and the results of those tests.  This test plan was first developed following the Fall 2008 meetings and subsequently revised for the second round of interoperability testing conducted in Spring 2011.  Results are provided in section 7.

## Scope

The scope of this document is the testing of the Asynchronous Messaging Service (AMS), including AAMS, MAMS, and RAMS protocols.

## Applicability

This Recommended Standard specifies protocols and associated services that enable communication among modules of mission data systems, specifically:

- between modules of a ground data system;

- between modules of a flight data system;

- between modules of different ground data systems;

- between modules of the flight data systems of different spacecraft;

- between modules of flight data systems and modules of ground data systems, over interplanetary distances.

This document applies to the interoperability testing required to advance AMS from Red Book to Blue Book status.  It may also be used as a reference to confirm conformance with future implementations.

## Rationale

The CCSDS Procedures Manual states that for a Recommendation to become a Blue Book, the standard must be tested in an operational manner. The following requirements for an implementation exercise were excerpted from reference [1]:

“At least two independent and interoperable prototypes or implementations must have been developed and demonstrated in an operationally relevant environment, either real or simulated.”

This document outlines the AMS Working Group’s approach to meeting this requirement.

## Document Structure

Configuration parameters and conventions for the interoperability testing are outlined in chapter 2 with additional details provided in the Appendix.

The following chapters describe general classes of tests.  Within each class there are test topics defining distinct sequences of test procedures.  Procedures correspond to individual columns in the associated results tables and may have individual test cases defining additional steps required to confirm a successful test.

Test results are provided in chapter 7.

## References

The following documents are referenced in this document. At the time of publication, the editions indicated were valid. All documents are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the documents indicated below. The CCSDS Secretariat maintains a register of currently valid CCSDS documents.

[1]	Procedures Manual for the Consultative Committee for Space Data Systems. CCSDS A00.0-Y-9. Yellow Book. Issue 9. Washington, D.C.: CCSDS, November 2003

[2]	Asynchronous Messaging Service.  Recommendation for Space Data System Standards, CCSDS 735x1b0.  Blue Book.  Issue 1.  Washington, DC.: CCSDS, July 2011

# Test Plan Overview & Configuration

## Overview

An implementation of the Asynchronous Message Service includes a Registration Server (RS), Configuration Server (CS), and two or more application modules in a given continuum.  These entities communicate using a common transport service(s).  The AAMS sub-protocol defines user data messages, while the MAMS protocol is used for configuration and status messages.  A RAMS gateway utilizes the Remote AMS protocol for communication across continua.

The interoperability testing described in this document is designed to exercise all aspects of the described protocols defining the Asynchronous Message Service between two independently developed implementations.

## Definitions & Conventions

All scenarios are designed for the testing of two distinct implementations, ALPHA and BETA.  Tables listed at the end of each section define the mapping of implementation to entity name for each case.  In general, the first implementation used in any case is abbreviated as ‘A’, such as RegistrarA, while the second implementation is abbreviated as ‘B’, such as NodeB.

Wherever multiple entities of the same type are used in a single implementation, a number shall be appended to the mnemonic for that entity type; for example, NodeA1 and NodeA2 refer to two distinct application modules operating within a given unit A.  Entity names are used for reference purposes only and do not necessarily reflect internal identifiers.  Mappings of module or registrar names may be swapped as necessary to facilitate alternate test scenarios with similar initial states.

The following configuration mnemonics will be used.  All mnemonics are defined in terms of appropriate values in the agreed upon MIB prior to each test sequence where applicable.

- Subject1 … Subject9

- ROLE_2, … ROLE_5

- UNIT_0, UNIT_1, UNIT_2

A default role of ROLE_2 and unit of UNIT_1 shall be used in all test sequences if not otherwise stated.

A marshaling scheme will be defined and used for Subject1, Subject2, and Subject3.  No marshaling will be used for any other subject.  The test procedures implicitly tests message exchange with and without marshaling through the usage of the full range of subject ids.

All entities will support at least two transport services, as specified in the test handbook.  Subject1 will use the primary transport service (UDP) and Subject2 will specify the quality of service for the secondary transport service (BUDP).  Supplementary transport services are thus implicitly tested through the usage of the range of subject ids throughout the test sequences.

All testing procedures, with the exception of RAMS procedures, assume that all entities are members of a single continuum, Continuum11 abbreviated as C1.  The RAMS procedures additionally use Continuum13, abbreviated C2 and Continuum17, abbreviated as C3.

## Testing Requirements

These procedures, unless otherwise noted, require that all implementations are operating across a common primary transport service and MIB configuration state.  A Supplementary Transport Service (STS) is available for usage when indicated.  The Transport Service Testing Requirements chapter describes any TS specific configuration options.

Verification requirements, as stated, may assume the availability of debug information on internal status of modules or other entities as appropriate.  Direct monitoring of message traffic across the selected transport service(s) may also be used for validation purposes.  These are suggested verification techniques only and, in the absence of direct verification, success may be inferred from related actions as appropriate.   A test result of undetermined (U) should be recorded if no verification was possible for a given step.

For all message exchanges the following defaults should be used if not otherwise specified.  The default subject is Subject1, role is Default_Role, and unit is Default_Unit.  Message content is not specified, however it is suggested that a known test value (ie: a test pattern, counter, or timestamp) be used and verified when appropriate.

Results tables should be marked as follows, with an explanation attached for any test that is not completed successfully:

- P for successful test.

- F for a failed test

- -  for a test that has not been performed.

- U for a test whose results are undetermined.

- I for partial success or incomplete test.

# Nominal Testing Procedures

This section describes testing procedures for core AMS functionality under normal operations.  The basic series may be used for testing a single implementation for compliance, or for the interoperability testing of any combination of implementations.  A table provided at the end of each section illustrates sample test scenarios for testing between implementations.

## Base Registrar Configuration

Validate the ability for the RS to communicate and register with the CS.

- Start Configuration Server

- Start RegistrarA

  - Confirm registration

  - Confirm heartbeats

- Start RegistrarB

  - Confirm registration

  - Confirm heartbeats

- Verify Mutual Awareness of Registrars

  - Confirm RegistrarA is aware of RegistrarB

  - Confirm RegistrarB is aware of RegistrarA

The following testing combinations will be performed, except that italicized cases are optional, to be used if there is a failure in any previous test combination.

| Test# | CS | RegistrarA | RegistrarB | Results |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 | 2 | 3 |
| 3.1a | ALPHA | BETA | ALPHA |  |  |  |
| 3.1b | BETA | ALPHA | BETA |  |  |  |
| 3.1c | ALPHA | ALPHA | ALPHA |  |  |  |
| 3.1d | BETA | BETA | BETA |  |  |  |

## Basic Module Registration

Validate the ability for a module to register and unregister itself.

- Initial Configuration should include one CS and at least one active RS.

  - This may correspond to the final state of the previous section, case 1, with any additional registrars ignored for this scenario and/or these procedures mirrored within each active cell (registrar).

- Verify that a module can register

  - Confirm ability to locate registrar by querying the CS

  - Verify registration success

  - Verify Heartbeat exchange between RS and module.

- Verify that the module can cancel its registration (unregister)

  - Confirm processing by the registrar

  - Confirm configuration propagation to other modules.

- Verify that the module can Re-Register

The following testing combinations will be performed.

| Test# | CS | Registrar | NodeA | Results |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 | 2 | 3 |
| 3.2a | ALPHA | ALPHA | BETA |  |  |  |
| 3.2b | BETA | BETA | ALPHA |  |  |  |

## Message Exchange

Validate the ability for two modules in the same cell to register and communicate.  This section will test subscriptions, publish, receive, invite, send, and announce.

- One CS, one RS, and one module are active.

  - This may correspond to the final state of case 2.

- Register a second module, NodeB.

  - Confirm successful registration

  - Verify that NodeB is told of NodeA’s existence and empty subscription list.

  - Verify that NodeA is told of NodeB’s registration.

- Publish a message on Subject1 from NodeA

  - Verify that NodeB does not receive this message; no subscriptions are in place at this time.

- Subscribe to Subject1 from NodeB

  - Verify that NodeA receives subscription notification.

- Publish a message on Subject1 from NodeA

  - Verify that NodeB receives the message

  - Repeat using Subject2 and verify NodeB does not receive the message; this is not the subject that has been subscribed to.

- From NodeB, subscribe to ALL_Subjects

  - Verify subscription receipt by NodeA

- Publish a message from NodeA on Subject2

  - Verify NodeB receives this message (subscribed to all)

- Send a message on Subject1 from NodeA addressed to a domain that includes NodeB

  - Verify that NodeB does not receive this message; no invitations are in place at this time.

- From NodeB, cancel subscription on ALL_SUBJECTS

  - Verify propagation to NodeA.  Attempt to publish a message from NodeB on Subject2 and verify the message is not received.

- From NodeB, invite a domain that includes NodeA to send Subject2

  - Verify NodeA receives invitation

- Publish a message from NodeA on Subject2.

  - Verify that NodeB does not receive this message.  An invitation does not apply to published messages.

- Send a message from NodeA to NodeB on Subject2

  - Verify that NodeB receives the message

- From NodeA, query NodeB on Subject2

  - Verify NodeB receives query.

- From NodeB, attempt to reply to NodeA with Subject3

  - Verify failure, NodeA has not issued an invitation on this subject.

- Verify query/reply exchange

  - From NodeA, invite messages on Subject3 in a domain that includes NodeB

  - Repeat steps 12 & 13, verifying success now that appropriate subscriptions are in place on both ends.

- From NodeA, issue an announcement on Subject3

  - Verify that the message is received by NodeA

  - Repeat from NodeA and verify the message is not received.  NodeB has no invitations in place on this topic.

  - Repeat announcement from NodeB, addressing the message to a domain that does not include NodeA.  Verify message is not received.

- Cancel NodeA registration (unregister)

  - Verify registrar processes and forwards request.

  - Verify unregisteration notification by NodeB

- Re-register NodeA

  - Verify registration success

  - Verify correct state of subscriptions as follows:

    - Publish a message on Subject1from NodeA and verify its receipt by NodeB.

    - Attempt to send a message from NodeB to NodeA on Subject2 and verify failure.  Invitations expire upon cancellation of a modules registration.

    - Attempt to send a message from NodeA to NodeB on Subject2 and verify success.

The following testing combinations will be performed:

| Test# | CS | Registrar | NodeA | NodeB |
| --- | --- | --- | --- | --- |
| 3.3a | ANY | ALPHA | ALPHA | BETA |
| 3.3b | ANY | BETA | BETA | ALPHA |
| Test# | Results |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 |
| 3.3a |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 3.3b |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

## Cross-Domain Communication

This scenario validates message exchange and configuration between cells and associated message filtering by domain.

- Initial state consists of a CS and two cells

  - The first cell consists of RegistrarA, NodeA1, NodeA2 in UNIT_1

  - The second cell consist of RegistrarB, NodeB1, NodeB2 in UNIT_2

  - Nodes A1 and B1 perform ROLE_2

  - Nodes A2 and B2 perform ROLE_3

  - At the start of this test both Registrars, NodeA1, and NodeB1 are active.

- Register the remaining modules, NodeA2, and NodeB2 to their respective cells.

  - Verify successful registration to their respective cells

  - Verify receipt of registration notification in neighboring cells.

- NodeA1 Subscribes to Subject1 in UNIT_1 and ROLE_3

  - Publish a message on Subject1 from NodeA2

    - Verify receipt by NodeA1

  - Publish a message on Subject1 from NodeB1 and from NodeB2.

    - Verify neither message is received.

- NodeA1 Subscribes to Subject2 on UNIT_2 and ROLE_2

  - Publish a message on Subject2 from NodeB1

    - Verify receipt by NodeA1

  - Publish a message on Subject2 from NodeA2 and from NodeB2.

    - Verify neither message is received.

- NodeA1 Subscribes to Subject3 on UNIT_2 and ALL_ROLES

  - Publish a message on Subject3 from NodeA2 and verify it is not received.

  - Publish a message on Subject3 from NodeB1 and NodeB2 and verify receipt of each.

- NodeA1 Subscribes to Subject4 on ALL_UNITS and ALL_ROLES

  - Publish a message on Subject4 from every other module in the continuum and verify receipt.

- Cancel Subscription to Subject4 from NodeA1 on ALL_UNITS and ALL_ROLES.

  - Verify propagation to all other modules.  This includes attempting to publish a message on this subject from each of the remaining modules and confirming that NodeA1 does not receive it.

- From NodeA1, invite messages on Subject5 from ALL_UNITS and ALL_ROLES

  - Verify that all others modules may privately send messages on Subject5 to NodeA1

  - Verify NodeA1 can receive an announcement on this subject from all other modules.

- From NodeA1, invite messages on Subject6 from UNIT_2 and ALL_ROLES

  - Verify that only NodeB1 and NodeB2 can send messages on Subject6 to NodeA1 in this configuration.

  - Repeat verification for transmission and receipt of announcements.

- From NodeA1, invite messages on Subject7 from UNIT_2 and ROLE_2

  - Verify that only NodeB1 can send a private message to NodeA1 on this subject.

  - Repeat verification for transmission and receipt of announcements.

- From NodeA1, invite messages on Subject8 from UNIT_1 and ROLE_3

  - Verify that only NodeA2 can send a private message to NodeA1 on this subject.

  - Repeat verification for transmission and receipt of announcements.

- From NodeA1, Cancel Invitation on Subject5

  - Verify propagation to all modules.

- Cancel Registration of NodeB1

  - Verify propagation of configuration change to all other modules.

  - Re-register NodeB1 and verify that it is made aware of all active subscriptions and invitations.

- Cancel Registration of NodeA1

  - Verify propagation of configuration change to all other modules.

  - Confirm that all invitations and subscriptions are cancelled upon shutdown of NodeA1.

The following testing combinations will be performed.  Compatible scenarios may be executed from the same configuration by swapping entity mnemonics accordingly.

| Test# | CS | RegistrarA | NodeA1 | NodeA2 | RegistrarB | NodeB1 | NodeB2 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3.4a | ANY | ALPHA | ALPHA | BETA | BETA | BETA | ALPHA |
| 3.4b | ANY | BETA | BETA | ALPHA | ALPHA | ALPHA | BETA |
| Test# | Results |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 |
| 3.4a |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 3.4b |  |  |  |  |  |  |  |  |  |  |  |  |  |

Resynchronization

Resynchronization may be performed periodically to ensure a consistent configuration within a cell.  Full verification of this capability may require the availability of debugging capabilities in the system, or transport service, to artificially create a non-synchronized scenario.  These procedures will be repeated for a Registrar of each implementation.

- Initial state includes:

  - A non-zero resynchronization value for a given cell

  - A minimum of one CS, RS, and three modules (including a minimum of one of each implementation type).

  - A second cell (RegistrarB and at least one associated module) is recommended to verify propagation between cells.

  - Establish some set of invitations and subscriptions.

- Verify resynchronization period.

  - Confirm that all modules receive a cell_status message at the expiration of this period.

- Verify that all subscriptions, invitations, and registration databases remain valid following the resynchronization.

- Artificially cause the modules to become out of sync.  This may be done by killing the third module (NodeC) in a method that prevents it from transmitting an ‘I_am_quitting’ message, or using some other implementation-specific method to cause knowledge of subscriptions and invitations to be lost.

  - Transmit a message from each remaining module to the now defunct NodeC and verify no adverse affects.

  - Wait for the conclusion of the next resynchronization period and validate that all entities are now synchronized.

| Test# | CS | RegistrarA | NodeA | NodeB | Results |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | 1 | 2 | 3 |
| 3.5a | ALPHA | BETA | ALPHA | BETA |  |  |  |
| 3.5b | BETA | ALPHA | BETA | ALPHA |  |  |  |

## Security & Data Integrity Verification

- Initial State includes:

  - One CS, two Registrars, and six modules.  Modules shall be spawned in step 1.  Modules A1, A2, and A3 belonging to RegistrarA, and Modules B1, B2, and B3 belonging to RegistrarB.

  - Modules A3 and B3 will lack digital signatures, and B3 will additionally lack checksums.  All other entities defined shall have unique encryption keys used in digital signatures and for encryption of all message traffic.

  - The following entries will be limited by the encryption key specified in the MIB:

    - Subject10 is limited to receivers of type ROLE_4

    - Subject12 is limited to senders of type ROLE_5

    - ROLE_4 is only authorized for NodeA1

    - ROLE_5 is only authorized for NodeB1

  - NodeA1 is part of ROLE_4, NodeB1 is part of ROLE_5,.  All other modules may belong to ROLE_2.

- Register all specified modules.

  - Verify successful registration of all modules.

- Register two additional modules (one per registrar and implementation) using the restricted ROLE_4.

  - Verify registration failure due to lack of authorization to assume the given role.

- All modules issue a subscription request for Subject1

  - Verify all subscriptions are accepted and acknowledged.

- Some module (with checksums enabled) subscribes to Subject2, with a checksum error deliberately inserted in the MDPU message.

  - Confirm message is discarded by all other modules

- One module per unit, with checksums enabled, publishes a message on Subject1, with a checksum error deliberately injected in the AAMS message.

  - Confirm message is discarded by all modules

- NodeB3 publishes a message on Subject1 (with no checksum inserted)

  - Verify receipt and acceptance by all subscribing modules.

- Create a new registrar, RegistrarC and cause it to register itself with a checksum error deliberately injected into the MAMS message.

  - Verify registration failure.

- Repeat previous step with a valid checksum and an invalid (or missing) digital signature.

  - Verify registration failure.

- NodeA1 subscribes to Subject10.

  - Verify all modules accept subscription.

- NodeB1 subscribes to Subject10

  - Verify all other modules reject the subscription as unauthorized.

- Each active module publishes a message on Subject10.

  - Verify NodeA1 and no others receive it.

- NodeA1 subscribes to Subject12.

  - Verify success

- NodeB1 subscribes to Subject12.

  - Verify success

- Each active module publishes a message on Subject12.

  - Verify that message is accepted only from NodeB, currently fulfilling ROLE_5.

| Test# | CS | RegistrarA | RegistrarB | NodeA1, NodeB1, NodeA3 | NodeA2, NodeB2, NodeB3 |
| --- | --- | --- | --- | --- | --- |
| 3.6a | ALPHA | ALPHA | BETA | ALPHA | BETA |
| 3.6b | BETA | BETA | ALPHA | BETA | ALPHA |

| Test# | Results |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 |
| 3.7a |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 3.7b |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

# Robustness Verification

## Registrar Failover

This scenario confirms the robustness of a configuration server in its management of its registration server.

- Initial configuration consists of a CS and a Registrar

- Delete (kill) the registrar.

  - Wait N3*N6 period and verify imputed death of registrar

  - Verify Registrar is restarted successfully.

- Suspend the registrar for a period of N3 such that it misses one heartbeat.

  - Verify Registrar continues normal operation and the CS does not prematurely impute its death.

- Suspend the registrar for a period of N3*N6 seconds

  - Verify that its death is imputed by the configuration server

  - Verify that a new instance of the registrar is successfully activated.

  - Verify that upon resumption, the existing registrar is appropriately terminated.

    - Confirm that termination is imputed by a failure of the CS to respond to heartbeats.

- Activate and register one module for each available implementation.

  - Verify registration and initiation of heartbeat exchange.

- Terminate the registrar

  - Verify imputed termination and restart by the server

  - Verify ability of each module to successfully impute death of the registrar, locate its successor, reconnect and resume activities (heartbeats).

  - Verify ability for modules to subscribe and publish messages.

- Terminate the Configuration Server.

  - Verify imputed loss by the registrar.

  - Verify that module communication is not impeded

- Restart the Configuration Server

  - Verify ability for registrar to reconnect.

- Terminate a module.  This is a test of the servers; any module may be terminated.

  - Verify its registrar imputes the modules death and propagates the news to all other modules in the message space.

  - Restart the module.

    - Verify successful registration

    - Verify communication with existing modules.

The following testing combinations will be performed.

| Test# | CS | Registrar | Modules | Results |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 4.1a | ALPHA | BETA | ALL |  |  |  |  |  |  |  |  |
| 4.1b | BETA | ALPHA | ALL |  |  |  |  |  |  |  |  |
| 4.1c | ALPHA | ALPHA | ALL |  |  |  |  |  |  |  |  |
| 4.1d | BETA | BETA | ALL |  |  |  |  |  |  |  |  |

## Robustness Validation

This scenario confirms configuration robustness between cells and configuration server failover mechanisms.

- Initial configuration consists of a CS (at the primary network location), two RS each with two registered modules (four total) and some set of established subscriptions and invitations.  This may correspond to the final state of basic case 3.

- Terminate primary Configuration Server

  - Verify imputed loss by the registrars after period N6.

  - Verify that module communication is not impeded

    - Message exchange and heartbeats continue as previously.

    - Confirm that additional subscriptions or invitations can be propagated.

  - Spawn a new module and confirm its inability to register.

- Spawn a Configuration Server at a secondary network location

  - Verify registrars connect to secondary configuration server

  - Verify ability to register a new module.  This will be done for each implementation.

  - Verify ability to assert subscriptions and invitations.  This will be done by each of the original four modules.

- Respawn the primary Configuration Server

  - Verify secondary CS is automatically terminated upon receipt of an ‘I_am_running’ message from the primary CS.

  - Verify all registrars detect the termination and revert to the primary CS

  - Verify ability to register a new module.  This will be done for one module of each implementation.

  - Verify ability to assert subscriptions and invitations.  This will be done by each of the original four modules.

- Terminate  RegistrarA

  - Verify imputed termination.

  - Verify ability for modules to continue AAMS message exchange.

  - Verify inability to register new modules in RegistrarA’s cell.

  - Verify ability of each client module to successfully impute death of the registrar.

- Respawn RegistrarA at a new network location

  - Verify ability of each client module to successfully locate the new registrar, reconnect and resume activities (heartbeats).

  - Verify ability for modules to subscribe and publish messages.

- Suspend a module of RegistrarA

  - Verify RegistrarA imputes the module’s death and the news propagates to all applicable entities, including RegistrarB and its registered modules.

  - Resume execution of the module.

    - Verify it receives notification or imputes its own demise.

    - Reconnect or re-register and verify success

    - Verify communication with existing modules.

- Repeat step 3 for RegistrarB

- Repeat step 4 for RegistrarB

The following testing combinations will be performed.

| Test# | CS1 | CS1 (backup) | RegistrarA | NodeAx | RegistrarB | NodeBx | Results |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 4.2a | ALPHA | BETA | ALPHA | ALL | BETA | ALL |  |  |  |  |  |  |  |  |
| 4.2b | BETA | ALPHA | ALPHA | ALL | BETA | ALL |  |  |  |  |  |  |  |  |

# Remote AMS Test Procedures

This section describes testing procedures for the Remote AMS (RAMS) protocol, including both Mesh and Tree configurations.  These test procedures assume the existence of three discrete continua, Continuum11, Continuum13, and Continuum17.  For brevity, they will be referred to as C1, C2, and C3.  ALL_CONTINUA indicates all continua are addressed.

All entities in these test sequences are assumed to have encryption keys defined and in use.

The following procedures are intended to exercise all RAMS components, in both the Tree and Mesh configurations.  As indicated, certain steps may not apply to all test configurations.

## Basic RAMS Verification

- The initial state consists of two continuums, C1 and C2 in an active state on the RAMS network, each containing one relevant cell.

  - RegistrarA, NodeA1, and NodeA2 are members of C1

  - RegistrarB, NodeB1, and NodeB2 are members of C2.

  - All entities belong to UNIT_1 and ROLE_2.

  - All entities are active at the start of this test.

- Verify each continuum is aware of its neighbor.

- NodeA1 Subscribes to Subject1 in C1

  - Verify subscription is not transmitted outside of C1.

  - Publish a message on Subject1 from NodeA2

    - Verify receipt only by NodeA1

  - Publish a message on Subject1 from NodeB1

    - Verify message is not received

- NodeA1 Subscribes to Subject2 in C2

  - Publish a message on Subject2 from NodeB1

    - Verify receipt by NodeA1

  - Publish a message on Subject2 from NodeA2

    - Verify message is not received.

- NodeA1 Subscribes to Subject3 on ALL_CONTINUA

  - Publish a message on Subject3 from NodeB1and verify receipt.

- Cancel Subscription to Subject2 from NodeA1 on C2.

  - Verify propagation to all other modules and continua.  Attempt to publish a message on this subject to verify.

- From NodeA1, invite messages on Subject4 from ALL_CONTINUA

  - Verify that NodeB1 can send messages on Subject4 to NodeA1.

  - Verify NodeA1 can receive an announcement on this subject from NodeB1.

- From NodeA1, invite messages on Subject5 from C2

  - Verify that only NodeB1 can send a private message to NodeA1 on this subject.

  - Repeat verification for transmission and receipt of announcements.

- From NodeA1, Cancel Invitation on Subject5

  - Verify NodeB1 cannot privately transmit messages to NodeA1.

The following testing configurations will be performed.

| Test# | C1 | C2 | Configuration | Results |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 5.1a | ALPHA | BETA | TREE |  |  |  |  |  |  |  |  |
| 5.1b | BETA | ALPHA | MESH |  |  |  |  |  |  |  |  |

## Advanced RAMS Verification

This section adds a third continuum for verification of messages requiring multiple hops (Tree configuration only), the ability to add or remove a continuum, and general message filtering with more than two continuum.

This procedure assumes the conclusion of the previous section as its initial configuration, or an environment with the same subscriptions already in place.

- Continua C1 and C2 are operating as described above.

  - C3 is active, but its RAMS Gateway is offline.

  - RegistrarC and NodeC are members of C3.

  - Subscriptions and/or invitations are in place between C1 and C2, both addressed to a specific domain (not including C3), and one that includes ALL_CONTINUA.

- C3 joins the RAMS Network. If operating under a Tree configuration, C3 becomes a child of C2.

  - Verify C1 and C2 receive appropriate petitions indicating the arrival of C3

  - Verify C3 receives appropriate petitions from C1 and C2, including notification of all pre-existing subscriptions.

- NodeC publishes a message on Subject1

  - Verify the message is not received.

  - Repeat for Subject3 and verify receipt by NodeA1, currently subscribing to this subject on ALL_CONTINUA.

- NodeC attempts to send a private message to NodeA1

  - Verify ability to send messages on Subject4, invited from all continuum.

  - Verify inability to send messages on Subject5.

- NodeA1 Subscribes to Subject6 in C3

  - Publish a message on Subject6 from NodeC

    - Verify receipt by NodeA1

  - Publish a message on Subject6 from NodeB1

    - Verify message is not received.

- From NodeA1, invite messages on Subject7 from C3

  - Verify that NodeC can send a private message to NodeA1 on this subject.

  - Verify that NodeB1 cannot send a private message to NodeA1 on this subject.

  - Optionally, repeat a+b for transmission and receipt of announcements.

- NodeB1 Subscribes to Subject8 in C3

  - Publish a message on Subject8 from NodeC

    - Verify receipt by NodeB1

  - Publish a message on Subject8 from NodeA1

    - Verify message is not received.

- From NodeC, invite messages on Subject9 from ALL_CONTINUA

  - Verify that NodeA1 can successfully send a private message to NodeC on this subject.

  - Verify that NodeB1 can successfully send a private message to NodeC on this subject.

- Remove C3 from the RAMS network.  This is a clean shutdown with appropriate petition cancellations being generated prior to shutdown of the RAMS gateway.

  - Verify petition propagations to C1 and C2.

  - Verify cancellation of all active invitations and subscriptions for C3.

- Add a C3 gateway back into the RAMS network.

  - Verify propagation of all expected petitions and declarations.

- Terminate the C1 gateway (ie: Ctrl+C) to simulate an unexpected failure.  A new instance of the C1 gateway will then attempt to join the RAMS Network.

  - Verify all pre-existing members of C1 continue to run without interruption.

  - Verify C1’s ability to rejoin and communicate with all other continua successfully, with only the expected configuration messages exchanged.

The following test configurations will be performed.

| Test# | C1 | C2 | C3 | Configuration | Results |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 5.2a | ALPHA | BETA | ALPHA | TREE |  |  |  |  |  |  |  |  |  |  |
| 5.2b | BETA | ALPHA | BETA | MESH |  |  |  |  |  |  |  |  |  |  |

# Transport Service Testing Requirements

The following sections describe any transport specific procedures that may be recommended to ensure a common configuration and ensure basic connectivity.

## UDP

UDP is the preferred transport service for interoperability testing at this time.  The following conventions will be followed for this TS:

- MAMS messages will be carried via UDP.

- Each module will have only one input port for AAMS messages, and it will be a UDP port.  (Each module will have two UDP input ports -- one for MAMS and one for AAMS.)

- All AAMS messages will be null-terminated character strings consisting of printable text.

To test UDP connectivity prior to AMS testing, the ‘netcat’ utility may be used:

machine1> nc -u machine2 6001 -p 6002

machine2> nc -u machine1 6002 -p 6001

Then type a line in on each machine - it should be received at the partner machine.

## Buffered UDP (BUDP)

Buffered UDP uses the buffering option to ensure that message delivery occurs in transmission order. All other parameters are the same as for the UDP transport service.

# Spring 2011 Interoperability Test Results

## Summary & Conclusion

Formal interoperability testing for the Asynchronous Messaging Service (AMS) was conducted at the Johns Hopkins University Applied Physics Laboratory in Laurel, MD from March 22-24, 2011, with David Edell (APL) serving as test director. Scott Burleigh from the Jet Propulsion Laboratory (JPL), Pat Donahue from Marshall (MSFC), and Tim Ray from Goddard (GSFC) were in attendance.  Testing was concluded via teleconference on May 12, 2011.

Interoperability testing was performed between the GSFC and MSFC implementations.  All test procedures, as described in the preceding chapters, were completed successfully. The tests performed have demonstrated interoperability between two independently developed implementations across all aspects of the AMS protocol.

## Results

### Nominal Testing Procedures

#### Base Registrar Configuration

| Test# | CS | RegistrarA | RegistrarB | Results |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 | 2 | 3 |
| 3.1a | MSFC | GSFC | MSFC | P | P | P |
| 3.1b | GSFC | MSFC | GSFC | P | P | P |

#### Basic Module Registration

| Test# | CS | Registrar | NodeA | Results |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 | 2 | 3 |
| 3.2a | MSFC | MSFC | GSFC | P | P | P |
| 3.2b | GSFC | GSFC | MSFC | P | P | P |

#### Message Exchange

| Test# | CS | Registrar | NodeA | NodeB |
| --- | --- | --- | --- | --- |
| 3.3a | ANY | MSFC | MSFC | GSFC |
| 3.3b | ANY | GSFC | GSFC | MSFC |

| Test# | Results |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 |
| 3.3a | P | P | P | P | P | P | P | P | P | P | P | P | P | P | P | P | P |
| 3.3b | P | P | P | P | P | P | P | P | P | P | P | P | P | P | P | P | P |

#### Cross-Domain Communication

| Test# | CS | RegistrarA | NodeA1 | NodeA2 | RegistrarB | NodeB1 | NodeB2 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3.4a | ANY | MSFC | MSFC | GSFC | GSFC | GSFC | MSFC |
| 3.4b | ANY | GSFC | GSFC | MSFC | MSFC | MSFC | GSFC |

| Test# | Results |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 |
| 3.3a | P | P | P | P | P | P | P | P | P | P | P | P | P | P | P | P | P |
| 3.3b | P | P | P | P | P | P | P | P | P | P | P | P | P | P | P | P | P |

#### Resynchronization

| Test# | CS | RegistrarA | NodeA | NodeB | Results |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | 1 | 2 | 3 |
| 3.5a | MSFC | GSFC | MSFC | GSFC | P | P | P |
| 3.5b | GSFC | MSFC | GSFC | MSFC | P | P | P |

#### Security & Data Integrity Verification

| Test# | CS | RegistrarA | RegistrarB | NodeA1, NodeB1, NodeA3 | NodeA2, NodeB2, NodeB3 |
| --- | --- | --- | --- | --- | --- |
| 3.6a | MSFC | MSFC | GSFC | MSFC | GSFC |
| 3.6b | GSFC | GSFC | MSFC | GSFC | MSFC |

| Test# | Results |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 |
| 3.7a | P | P | P | P | P | P | P | P | P | P | P | P | P | P |
| 3.7b | P | P | P | P | P | P | P | P | P | P | P | P | P | P |

### Robustness Verification

#### Registrar Failover

| Test# | CS | Registrar | Modules | Results |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 4.1a | MSFC | GSFC | ALL | P | P | P | P | P | P | P | P |
| 4.1b | GSFC | MSFC | ALL | P | P | P | P | P | P | P | P |

#### Robustness Validation

Section 4.2 was completed via teleconference on May 12 following updates to the Marshall implementation related to the handling of configuration server failover.

| Test# | CS1 | CS1 (backup) | RegistrarA | NodeAx | RegistrarB | NodeBx | Results |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 4.2a | MSFC | GSFC | MSFC | ALL | GSFC | ALL | P | P | P | P | P | P | P | P |
| 4.2b | GSFC | MSFC | MSFC | ALL | GSFC | ALL | P | P | P | P | P | P | P | P |

### Remote AMS Test Sequence

#### Basic RAMS Verification

| Test# | C1 | C2 | Configuration | Results |
| --- | --- | --- | --- | --- |
|  |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| 5.1a | MSFC | GSFC | TREE | P | P | P | P | P | P | P | P |
| 5.1b | GSFC | MSFC | MESH | P | P | P | P | P | P | P | P |

#### Advanced RAMS Verification

Section 5.2b (mesh configuration) was completed via teleconference on May 12 following updates to the Marshall implementation

| Test# | C1 | C2 | C3 | Configuration | Results |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| 5.2a | MSFC | GSFC | MSFC | TREE | P | P | P | P | P | P | P | P | P | P |
| 5.2b | GSFC | MSFC | GSFC | MESH | P | P | P | P | P | P | P | P | P | P |

# Supporting conventions for AMS interoperability testing

## Operations structure

Testing will occur within and between these AMS continua:

- “gsfc” (11)

- “msfc” (17)

For the purposes of this interoperability testing, a single venture numbered 23 is defined for application “amstest” and authority “ccsds”.  Within this venture, four units are defined (in addition to the root unit 0):

- “thermal” (1)

- “power” (2)

- “power.battery” (3)

- “power.panel” (4)

The application roles defined for application “amstest” are:

- “sensor” (2)

- “actuator” (3)

- “logger” (4)

- “monitor” (5)

Twelve message subjects are defined for this application:

- “text” (1)  The content of any AAMS message on this subject will be a NULL-terminated array of ASCII characters.

- “count” (2)  The content of any AAMS message on this subject will be a single unsigned integer.

- “range” (3)  The content of any AAMS message on this subject will be a pair of unsigned integers.

- “string” (4)  The content of any AAMS message on this subject will be a NULL-terminated array of ASCII characters; the subject differs from “text” only in that the content of a “string” message is never marshaled.

- “text5” (5)  Same as “text” except neither marshaled nor encrypted; defined only for cross-domain communication tests.

- “text6” (6)  Same as “text” except neither marshaled nor encrypted; defined only for cross-domain communication tests.

- “text7” (7)  Same as “text” except neither marshaled nor encrypted; defined only for cross-domain communication tests.

- “text8” (8)  Same as “text” except neither marshaled nor encrypted; defined only for cross-domain communication tests.

- “text10” (10)  Same as “text” except neither marshaled nor encrypted; defined only for access control tests.

- “text11” (11)  Same as “text” except neither marshaled nor encrypted; defined only for access control tests.

- “text12” (12)  Same as “text” except neither marshaled nor encrypted; defined only for access control tests.

- “text13” (13)  Same as “text” except neither marshaled nor encrypted; defined only for access control tests.

(Note that AAMS messages within this venture may be on subjects other than these, but those subjects are not defined.)

## Transport services

What really matters in terms of testing compliance to the spec is having and exercising two transport services that differ in name.  We go slightly beyond that: we define a second transport service with a different name and assert that it differs from UDP in service mode (delivery sequence and/or diligence).

So our transport services are:

- “udp”: sequence is delivery in arrival order, diligence is best-effort.

- "budp" ("buffered UDP"): sequence is delivery in transmission order, diligence is best-effort.

Since in interoperability testing over a LAN it's virtually impossible for IP packets to arrive out of transmission order anyway, “budp” is in practice just an alias for “udp”, but in the MIB it will be characterized by a different service mode.

Selection of transport service is normally based on the service mode specified at subscription or invitation time.  So to test correct transport service selection we need some variation in subscription service modes: subscriptions to subject “count” will specify the service mode satisfied by transport service “budp” while all other subscriptions will specify the service mode satisfied by “udp”.

## Marshaling and unmarshaling

AAMS messages on selected subjects will be marshaled from native representation to machine-independent representation on transmission and then unmarshaled back to native representation on reception.

All messages on subjects ‘text’, ‘count’, and ‘range’ will be marshaled.  All other messages will not be marshaled.

The general rules for the marshaling convention are as follows:

- Two types of containers are defined: mailbag and envelope.

- Every container of either type consists of a header plus contents.  The same header structure is used for both containers.

- The contents of a mailbag must be envelope(s) and/or other mailbag(s).

- The contents of an envelope are not specified by the generic message structure.

- The outermost container for any message must be a mailbag.

A <label> consists of printable ASCII characters.  Any character that can take more than one column to print is not allowed (e.g. tab and newline characters).

If the desired name for the <label> is less than 11 characters, we fill in the remaining slots with dots (‘.’).   E.g. if the desired label is “AMS”, then the transmitted <label> would be “AMS........”.  When referring to the label, we can ignore the trailing dots and simply say that the label is “AMS”.

The <label> of the outermost mailbag is “Outermost”.

The <length> specifies the number of octets in the <contents> that follow the header.

The <length> is in ASCII-decimal format, with leading zeros.  E.g. “00000012” = twelve.

We define three types of envelopes:

- Any envelope with label “text…….” will always have a NULL-terminated array of ASCII characters in its contents, and its length will be the length of that array (including the terminating NULL).

- Any envelope with label “count….” will always have the ASCII representation of an unsigned integer (10 ASCII numeric digits, with leading zeroes as needed) in its contents, and its length will be 10.

- Any envelope with label “range….” will always have the ASCII representation of two unsigned integers (two successive arrays of 10 ASCII numeric digits each, with leading zeroes in each as needed) in its contents, and its length will be 20.

No value in excess of (2^31) – 1 shall ever be marshaled into a “count” or into either numeric field of a “range”.

Examples:

- Suppose we’re sending the text “Hello, world” in an AAMS message on subject 1.  The marshaled application data for that message will be “Outermost..M00000032text…….E00000013Hello, world\0”.

- Similarly, a count of 97 would be sent in an AAMS message on subject 2 whose marshaled application data would be “Outermost..M00000030count….E000000100000000097”.

- And a range of 71 to 77 would be sent in an AAMS message on subject 3 whose marshaled application data would be “Outermost..M00000040range….E0000002000000000710000000077”.

The marshaled application data is encrypted if there’s an applicable key in the MIB.

The result, whether encrypted or not, is used as the application data for a newly generated AAMS message.

## Encryption and decryption

Encryption and decryption of MAMS digital signatures and (as applicable) AAMS message contents will be performed by simply XOR’ing message text with key text.

The text of every encryption key will be an array of ASCII characters without a terminating NULL character.  (For example, if the text of a given key is “abcd” the length of that key is 4 bytes, not 5.)

Given an array of N bytes of plain (unencrypted) ASCII text and an ASCII text key of M bytes, the result of encrypting the plain text will be an array of N bytes of cipher (encrypted) text.  Encryption will be performed as follows:

Let m = 0, n = 0.

While n < N:

Cipher text character n = plain text character n XOR key text character m.

Add 1 to n.

Add 1 to m.

If m is equal to M

m = 0.

Decrypting an array of N bytes of cipher text is accomplished in exactly the same way.

The encryption key to be used for generating the signature of a module (formerly “node”) shall be the module’s role-name (e.g. “actuator”), except that only modules registered in the roles “actuator”, “logger”, and “monitor” will have signatures on their MAMS messages.

The encryption key to be used for generating a registrar’s signature shall be the application-name characterizing the message space that contains the cell served by the registrar.  For our testing there is only one application (named “amstest”), so all registrars will use the same key.

The encryption key to be used for generating a configuration server’s signature shall be the name of the continuum served by the configuration server (e.g. “msfc”), except that only the configuration servers for continua “msfc” and “jpl” will have signatures on their MAMS messages.

Messages on the subjects “count”, “range” and “string” shall be encrypted.  In each case, the encryption key to be used shall be the subject’s name.  Messages on other subjects will not be encrypted .

## Digital Signatures

The digital signature for a MAMS message is formed by concatenating a randomly selected “nonce” with the result of encrypting the concatenation of that nonce with a “well-known string”.  The well-known string has to be something that is agreed-to by everybody, but it doesn’t have to be a constant or even a string of constant length:

- If the sender of the MAMS message is a module, the applicable well-known string is the module’s NULL-terminated role name.

- If the sender of the MAMS message is a registrar, the applicable well-known string is the NULL-terminated name of the application for the message space of which the registrar’s cell is one part.

- If the sender of the MAMS message is a configuration server, the applicable well-known string is the NULL-terminated name of the continuum served by that configuration server.

## Access Control

For each message subject, transmission and/or reception of messages on that subject can be restricted to a subset of the registered modules in the venture.

The way we manage which modules can send which messages and which modules can receive which messages is by providing (conceptual) lists of “authorized receiver roles” and/or “authorized sender roles” for any message subject that we want to be access-controlled.

So the way a module becomes eligible to send a transmission-restricted message subject is by registering in one of that subject’s authorized sender roles.  (Likewise reception, etc.)

But that’s not especially secure in itself.  What makes it a security feature is that there can be a “public key” associated with a given role in a registrar’s MIB.  When a new module tries to register in one of the roles that are authorized to send (or receive) messages on some access-controlled subject, and the registrar has got a public key for that role, the module must provide a digital signature encrypted in the corresponding private key when it sends its node_registration message.  So a random bad person can’t get access to those restricted subjects, because he won’t know the private key that enables registration in an authorized role.

- Messages on subject 10 can only be received by modules that have registered in role 4, “logger”.

That means that the MIB exposed to every module should say that messages on subject 10 can only be sent to “logger”.  Since there are public and private keys for MAMS digital signatures associated with role “logger” (both are “logger”), only a module that registers as a “logger” and has that secret private key in its MIB will be able to receive messages on subject 10.  In our testing, only one module will have that secret key in its MIB, enabling it to register as a “logger” and to receive messages on subject 10.

- Similarly, messages on subject 11 can only be received by modules that have registered in role 3, “actuator”.  Only one module will have the secret key for registering as a “actuator”.

- Messages on subject 12 can only be sent by modules that have registered in role 5, “monitor”.  That means that the MIB exposed to every module should say that messages on subject 12 can only be sent by “monitor” modules.  Since there are public and private keys for MAMS digital signatures associated with role “monitor” (both are “monitor”), only a module that registers as a “monitor” and has that secret private key in its MIB will be able to send messages on subject 12.  In our testing, only one module will have that secret private key in its MIB, enabling it to register as a “monitor” and to send messages on subject 12.

- Similarly, messages on subject 13 can only be sent by modules that have registered in role 2, “sensor”.  Only one module will have the secret key for registering as a “sensor”.

## Sample representation of the interoperability testing MIB

<?xml version="1.0" standalone="yes"?>

<ams_mib_load>

<ams_mib_init continuum_nbr="13" ptsname="dgr" pubkey="jpl" privkey="jpl"/>

<ams_mib_add>

<continuum nbr="17" name="msfc" desc="Pat Donahue at Marshall"/>

<csendpoint epspec="loretta:2357"/>

<application name="amstest" pubkey="amstest" privkey="amstest"/>

<venture nbr="23" appname="amstest" authname="ccsds" net_config="tree" gweid="udp@loretta.jpl.net:2113">

<role nbr="2" name="sensor"/>

<role nbr="3" name="actuator" pubkey="actuator" privkey="actuator"/>

<role nbr="4" name="logger" pubkey="logger" privkey="logger"/>

<role nbr="5" name="monitor" pubkey="monitor" privkey="monitor"/>

<subject nbr="1" name="text" desc="ASCII text" marshal="text" unmarshal="text"/>

<subject nbr="2" name="count" desc="one integer" marshal="count" unmarshal="count" symkey="count"/>

<subject nbr="3" name="range" desc="two integers" marshal="range" unmarshal="range" symkey="range"/>

<subject nbr="4" name="string" desc="unmarshaled text" symkey="string"/>

<subject nbr="10" name="text10" desc="more text">

<receiver name=”logger”/>

</subject>

<subject nbr="11" name="text11" desc="more text">

<receiver name=”actuator”/>

</subject>

<subject nbr="12" name="text12" desc="more text">

<receiver name=”monitor”/>

</subject>

<subject nbr="13" name="text13" desc="more text">

<receiver name=”sensor”/>

</subject>

<unit nbr="1" name="thermal"/>

<unit nbr="2" name="power"/>

<unit nbr="3" name="power.battery"/>

<unit nbr="4" name="power.panel"/>

<msgspace nbr="17" gweid="udp@198.119.225.228:8361"/>

</venture>

</ams_mib_add>

</ams_mib_load>

Note that the term “module” supersedes the term “node” as used in early versions of the AMS specification.  Some language in this test plan uses the superseded term “node” in place of “module” to reflect accurately the manner in which the tests were conducted; the two terms are equivalent.

Insert reference to AMS CCSDS document number here?

Fix section formatting, add references to other AMS documents as appropriate.

We should reference the standard here.  But: What is the official document name/publication-date to reference?

TODO.  Perhaps list all elements to be tested explicitly (with corresponding test sequences), and those tested implicitly (ie:marshalling).

Move this and following section into a new chapter for “Test Setup” or similar.

Scott proposes globally renaming these to be Role2- and Unit0-

Should we reference Tim’s document or include it as an appendex?  Should we list details (ie:Subject1=text, 2=count,etc)?

VERIFY: Didn’t we omit the dedicated section in favor of having certain TS associated with specific subjects?  Update this to indicate such.

Move this into test configuration section OR as an Appendix

Based on example from other Yellow books (502x1y1).  “AMS Specification” in this sentence should be replaced with the formal document number.

Maybe, but I’m doubtful.  I think this formal resolution needs to come from the Area Director in a separate email.