## Slide 1: Next Generation Uplink Action Item Responses
Drilling Down one level to Understand
Implications on Next Generation Uplink

## Slide 2: NGU End State
Torwards what end state is the NGU WG working towards?
  Interoperability at a maximum data rate per application profile
  Impact on the Ranging Channel must be factored in
  Determine where and when new solutions must be provided in the standards

## Slide 3: NGU WG Agenda
Focusing on identifying requirements and work assignments associated with the 3 NGU application profiles
  File Upload
  Human support profile
  Emergency comm unmanned
We will go though the Action Item Responses next

## Slide 4: Current Deep Space Constrained Comm Scenarios
EDL
  One-way comm only; no uplink
  Effectively only signaling events
  Use Semaphores or Beacon Tones
Automated Safeing will have communications on omni antenna
  Stable pointing for long contacts but pointing is possibly off axis
  Low rates for both TLM/CMD should be possible
Solar Conjunction
  Scintillation causes significantly increased Gaussian noise.
  Examine Statistics of Scintillation with JPL’s Dave Morabito
Launch and Initial Deployments
  Uplink Large Power Margins but tumbling could cause short visibility
  Visibility constraints due to geometry, pointing, ant. coverage
  Nominal 2Kb/sec Uplink Rate possible
Commanding in the Blind
  Hardware Commands and/or short reconfiguration commands

## Slide 5: Current Deep Space Emer Comm Scenario
Emergency Uplink Data Rate
  7.8125 bps
Subcarrier
  16 KHz sinewave
  MI = 0.92 Rad (NASA Mars Orbiters)
  Doppler compensated due to narrow BW of tracking loop on S/C
TC Frame Size
  Most S/C allow this to be variable and usually not a fixed size
Uses BCH Code
Commanding is bursty, using an asynchronous data link
Operational Considerations
  Human intervention by Project required to obtain additional antenna coverage for DFE uplink
  New NASA MAROS (Mars Relay Operations Service) to provide Mars Landed Assets with FWD Link commands for any overflight
  Today’s spacecraft do not have any Real-time critical commanding requirements; Typically they limit how many cmds/sec to send
  Command time tags typically have to be accurate to around 1 sec

## Slide 6: Current Near Earth Emer Comm Scenario
Emergency Uplink Data Rate
  NEN (GN): 1000 to 2000 bps SN (TDRSS) 125 bps to 2000 bps
Subcarrier
  NEN: 16 KHz sinewave SN: PN spread, no subcarrier
  NEN: MI = ~ 1.4 Rad SN: na
  NEN: sweep for acquisition SN: Doppler compensated due to PN spreading
TC Frame Size
  Most S/C allow this to be variable and usually not a fixed size
Uses BCH Code
Commanding is bursty, using an asynchronous data link
Operational Considerations
  Human intervention by Project required to obtain additional antenna coverage
  Today’s spacecraft do not have any Real-time critical commanding requirements; Typically they limit how many cmds/sec to send
  Time of release of commands typically have to be accurate to around 1 sec

## Slide 7: Howie Weiss – NGU Security Issues
General: It appears that either AOS or TC will be used as a link protocol for all 3 of these profiles. Since that's the case, then either the link layer security protocol that we're working on will suffice (since its being worked on assuming use with TC, TM, and AOS) or upper layer security could be used (e.g., IPSec or application layer such as TLS or just plain old file encryption).
File Upload Profile: For files its best to provide writer-to-reader security which translates into application layer security. This could mean SSL/TLS or simple file encryption where both ends have prior knowledge of the crypto key. Failing this, we could use IPSec as a value-added service assuming that IP is used somewhere in the xmission protocol stack. Failing that, the link layer security protocol could be used with AOS.
Human Support: Again, more of the above. For specific human support such as HIPPA health data, application layer security is the *right* answer to provide the writer-to-reader confidentiality I discussed earlier. Otherwise, IPSec and/or link layer security would work assuming IP or AOS or TC.
Emergency Comm: Once again more of the above. No difference here other than probably application layer security is not required under any circumstances. There is also debate over whether any security is required for emergency comms. The one side of the argument is that all hell has broken loose so get the security the heck out of my way and let me make repairs. The other side of the argument is that we must protect the emergency comms because otherwise the 'bad guys' might find a way through to the spacecraft command system that was not intended for use under nominal circumstances. The DoD satellite folks never allow a by-pass. They'd rather loose the bird than to have an open hole. They have, in the past, simulated onboard crypto failures and modified ground systems with the same failure mode to recover satellites whose comm systems failed because of bad crypto.

## Slide 8: RF&Mod WG Responses (1-4)
File Upload (1 Mb/s uplink)
  Without Ranging use existing CCSDS spec
    For Lunar Comm 2, 7 GHz/ Mars Comm 7, 34 GHz
      CCSDS 401 (2.2.8) allows TC up to 1.024 Mbps
        Can be easily extended to 2.048 Mbps
      CCSDS 401 (2.2.7) allows TC up to 256 Kbps
      CCSDS 401 (2.2.4) allows TC up to 8 Kbps
      If radiometrics required other than Ranging
        CCSDS 401 (2.2.8) Doppler and Delta DOR

## Slide 9: RF&Mod WG Responses (2-4)
File Upload (1 Mb/s uplink)
  If Ranging must be simultaneous with commanding > 256Kb/sec
    Requires new command and Ranging Scheme
    Requires new task for RF&MOD and Ranging WGs

## Slide 10: RF&Mod WG Responses (3-4)
Human Support (25 Mb/s uplink)
  Without simultaneous Command + Ranging
    For Lunar Comm use 22 GHz TC, 2 GHz Ranging
    Modulation is TBD until frequency allocation is secured in 2011
  If simultaneous command + ranging required
    RF&MOD and Ranging WGs would conduct study
      Very preliminary consideration of UQPSK modulation with marker in TC Packets transmitted via TM - TBC

## Slide 11: RF&Mod WG Responses (4-4)
Emergency Comm Unmanned (100 – 1000 b/s uplink)
  Current technology makes it possible to have the spacecraft acquire the U/L without Ground sweep via on-board FFT compatible with CCSDS 401 (2.2.4) up to 8 Kbps.
  * Define # distinct channels to be made available for multiple TC access
    X-band 7/8 GHz
    Ka-band 34/32 GHz
    Ka-band 40/38 GHz
  34 GHz frequency not recommend for Emergency Mars Commanding
    Used with HGA not suitable for low rate comm.

## Slide 12: Using Block Code for NGU
Rationale for using BLOCK code in Physical layer for uplink is to obtain greater coding gain to support higher uplink data rates.

## Slide 13: Rational for Change - NGU
Technology has significantly changed since CCSDS adopted TC. More sophisticated coding can be decoded easily within a small FPGA. The point is more sophisticated decoding can be accomplished on-board within a small FPGA, among the possible are LDPC
The BCH code provides little or no coding gain and can not correct for even a burst of two errors. Future higher rate uplinks may require significant coding gain to overcome weak signals. CCSDS wants more coding gain for higher rate uplinks but higher rates will reflect in lower bit SNRs
TC is variable length frames, Block codes are fixed length. Using a block code that is synchronous to the start of a frame will create significant overhead and since block codes are required to have sync patterns at a periodic interval the timing of TC uplinks is constrained to the periodic repeat of the codeblock

## Slide 14: Order of Uplink CMD processing in Security Era*
1. Carrier detect
2. Subcarrier detect (if applicable)
3. Symbol detect
4. Bit synchronize
5. Code block sync
6. Derandomize
7. Frame Sync
8. Authenticate
9. Block Decode
10. Decrypt (Note: With GCM 8&9 done together)
11. COP-1

## Slide 15: Consequences of New Block Code on Uplink processing
There would be no need to change the Command decoder (eliminating the BCH code however could be accommodated if the CRC for the frame was utilized) and the COP-1 process would not be effected.
No need to change the cmd decoder, because the security function on-board happens after block decoding. There is no reason to do BCH FEC because its already done by the block code. The CRC will detect data loss caused by block decoder finding an uncorrectable error.