## Slide 1: Deterministic Communication with SpaceWire
Martin Suess CCSDS Spring Meeting 2015 23/03/2015

## Slide 2: Overview
Introduction
SpaceWire-D Protocol Main Requirements
Scheduling of SpaceWire Traffic
SpaceWire-D Protocol Stack
SpaceWire-D Prototyping
Conclusion

## Slide 3: Introduction
SpaceWire is a widely used on-board data link standard for payload communication.
The SpaceWire standard ECSS-E-ST-50-12C defines the point to point links as well as networks.
The communication over the bi-directional SpaceWire links and the network is asynchronous, i.e. no synchronization between data sources.
If communication channels share the same hardware resources the access is arbitrated.
As result the message latency through the network is not fixed.
The mean latency and the jitter around the mean is a function of many parameters: link speed, network traffic, network topology, segment or packet size.
The maximum (worse case) latency has always an upper bound but this bound depends on many parameters.
This makes it difficult to manage the latency in a system.

## Slide 4: SpaceWire-D Main Protocol Requirements
Provide deterministic data delivery
Using Remote Memory Access Protocol (RMAP) ECSS-E-ST-50-52C as the basic communication mechanism.
Operates on existing SpaceWire networks with current routing switches.
Compatible with existing SpaceWire RMAP target devices.
SpaceWire-D protocol initiator part can be implemented in software.
Other SpaceWire packets can be sent without disrupting deterministic traffic
Allows SpaceWire to be used for
Time critical avionics applications (e.g. AOCS)
Concurrently with regular payload data handling
Basic service shall be very simple to implement

## Slide 5: Determinism with a Single Initiator
Inst. 1
Inst. 2
Inst. 3
SpaceWire Router
Inst. 4
Inst. 5
Mass
Memory
Data-Handling
Processor
SpaceWire Router
Initiating
Node
Read Command
Read Reply
Read Command
Read Reply
Target
Nodes

## Slide 6: Multiple Initiators
Inst. 1
Inst. 2
Inst. 3
SpaceWire Router
Inst. 4
Inst. 5
Mass
Memory
Data-Handling
Processor
SpaceWire Router
Read Command
Read Command

## Slide 7: Determinism through Scheduling
Inst. 1
Inst. 2
Inst. 3
Mass
Memory
Data-Handling
Processor
SpaceWire Router
0
1
2
3
4
...
Y
N
N
Y
N
...
0
1
2
3
4
...
N
Y
Y
N
N
...
Each initiator has a schedule table
Specifies in which time-slots an initiator is allowed to initiate an RMAP command

## Slide 8: Time-Slot 0
Inst. 1
Inst. 2
Inst. 3
Mass
Memory
Data-Handling
Processor
SpaceWire Router
Write Reply
Write Command
0
Y
1
N
2
N
3
Y
4
N
...
...
0
N
1
Y
2
Y
3
N
4
N
...
...

## Slide 9: Time-Slot 1
Inst. 1
Inst. 2
Inst. 3
Mass
Memory
Data-Handling
Processor
SpaceWire Router
Read Reply
Read Command
0
Y
1
N
2
N
3
Y
4
N
...
...
0
N
1
Y
2
Y
3
N
4
N
...
...

## Slide 10: Concurrent Data Transfer
Inst. 1
Inst. 2
Inst. 3
Mass
Memory
Data-Handling
Processor
SpaceWire Router
Write Reply
Write Command
0
Y
1
N
2
Y
3
Y
4
N
...
...
0
N
1
Y
2
Y
3
N
4
N
...
...
Read Reply
Read Command
Doubles the effective network bandwidth

## Slide 11: Schedule
Schedule arranged to avoid conflicting use of network resources
In a single slot can have
  Parallel Initiators with non conflicting Targets or groups of Targets
  Single Initiator that can send commands to any Target
The synchronization of the schedule between the SpaceWire-D initiators is achieved using SpaceWire Time-Codes.

## Slide 12: SpaceWire-D Transaction
Transaction
  SpaceWire RMAP transaction:
    Send an RMAP command
    Receive an RMAP reply
Transaction Group
  A group of transactions that can fit into a single slot
  The basic entity which is scheduled on the network

## Slide 13: SpaceWire-D Virtual Bus
A “virtual bus” or “bus” comprises
  An initiator
  A group of targets it is allowed to talk to
  One or more slots for executing transactions between initiator and target
Over a bus an initiator can
  Read or write to memory
  In a target node
Two or more buses scheduled in the same slot
  Must not use the same resources (links)

## Slide 14: SpaceWire-D Services
Static Bus
  Deterministic.
  Transaction group sent one specific slot per schedule round.
Dynamic Bus
  Not fully deterministic.
  Transaction group sent in one of several slots assigned to the virtual bus.

## Slide 15: SpaceWire-D Services
Asynchronous Bus
  Not deterministic.
  Individual transactions with priority grouped into transaction group and sent in one of several assigned slots.
Packet Bus
  Not deterministic.
  Sends and receives SpaceWire packets using RMAP.
  Packet segmented if necessary to fit into slot.
  One or more or part of a packet sent in one of several assigned slots.

## Slide 16: SpaceWire-D Services
SpaceWire- D provides 4 different services with different properties and applications
  Static Bus Service
  Dynamic Bus Service
  Asynchronous Bus Service
  Packet Bus Service

## Slide 17: SpaceWire-D Services
Static Bus
  Fully deterministic
  One slot assigned to it
  Group of transactions executed in specific time slot
  Can be a fixed or varying group of transactions

## Slide 18: SpaceWire-D Services
Dynamic Bus
  Not fully deterministic
  One or more slots assigned to it
  Group of transactions executed in one of several time slots
  Two buffers
    Current Transaction Group
    Next Transaction Group

## Slide 19: SpaceWire-D Services
Asynchronous Bus
  One or several slots are assigned to it
  Accepts individual transactions with priority
  Sorts out transaction group to be sent in next time-slot assigned to the bus
  Not deterministic
  Provides a means of reading and writing to memory in target devices without upsetting deterministic traffic
  Each bus has its own transaction queue

## Slide 20: SpaceWire-D Services
Packet Bus
  One or more slots assigned to it
  Accepts requests to send packet or receive packet
  Requests converted into RMAP transactions executed which are collected in a transaction group
  Not deterministic
  Provides a means of sending and receiving packets from target devices without upsetting deterministic traffic

## Slide 21: SpaceWire-D Protocol Stack
Dynamic Bus
Initiator
Static Bus
Target
Packet Bus
Target
Dynamic Bus
Target
Async Bus
Target
SpaceWire
SpaceWire-D
User Application
SpaceWire
RMAP
Initiator
Static Bus
Initiator
User
Application
SpaceWire
RMAP
Target
User Application
Packet Bus
Initiator
Initiator
Target
Network
Async Bus
Initiator
RMAP

## Slide 22: SpaceWire-D FDIR
Fault Detection, Isolation and Recovery (FDIR) requirements have been considered from the beginning and addressed in SpaceWire-D.
Initiator can monitor the completion of all transactions within the time slot.
If an error is detected the network manager is informed to perform isolation and recovery.
For faster failure isolation a schedule conscious bus guarding function can be integrated in the SpaceWire routing switches.
  This function is not yet available in current routing switches.

## Slide 23: SpaceWire-D Prototype
AT6981 Castor system-on-chip
  Used for both RMAP initiators and targets
  8-port SpaceWire router
  Dedicated RMAP engines
  LEON2-FT processor
Software built using the RTEMS real-time operating system
  Board support package ports the OS to the AT6981 board
Link Analyser Mk2 used to monitor traffic
USB Brick Mk2 used as time-code master

## Slide 24: SpaceWire Prototype
Castor-PXI
Castor-PCIe
Castor-PXI
Brick
Mk2
Link
Analyser Mk2

## Slide 25: SpaceWire-D Protocol Definition
The SpaceWire-D protocol has been defined by the University of Dundee under ESA contract.
Protocol requirements have been have been established with active involvement of two major European System Integrators (TAS-F, Airbus Defense & Space)
The SpaceWire-D protocol specification has been regularly reviewed by
  ESA
  TAS-F
  Airbus D&S
  SpaceWire Working Group
The prototype implementation is performed by UoD
The protocol definition is very advanced
  SpaceWire-D Standard Draft D v0.15 (July 2014)

## Slide 26: Conclusion
SpaceWire-D addresses the need of deterministic data delivery over SpaceWire.
Based on currently existing SpaceWire devices
  Routers
  RMAP Target devices
  RMAP Initiators
Additional software to handle the protocol only required on Initiators.
Further error resilience can be gained by introducing the bus guarding function in the routers.
SpaceWire-D is planned for standardization in ECSS in 2016-2017